SHOWHPGL	A viewing program for HP-GL and HP-GL/2 plotting programs.

Version 1.9


Introduction

This program is designed to preview HP-GL and HP-GL/2 plotting programs
on the console screen of an IBM PC or compatible computer.  It
impliments 47 of 97 HP-GL or HP-GL/2 instruction.  Of the 97
instruction, 22 either have no meaning for this type of program or
are otherwise unrelated to drawing.  Four instructions are included to
provide backward compatibility with the HP9872 plotter.  These instructions
are interpreted as NOP's.

It is written in Microsoft C, version 6.0.  It requires MS-DOS
version 3.0 or above to run.  This program is meant to be used as a
preview tools for HP-GL files.  It is as accurate as it could be made
with the limited information and resources available at the time it
was written.  Known bugs or deficiencies are listed after the
instruction set summary.

Version 1.9 adds solid fills to RR and RA (relative and absolute filled
rectangles), and fixes a bug which allowed drawing outside the hard clip
border when using IW (windowing).

Revision History

Version 1.9	17 August, 1992

- Added solid fill types to RA and RR.
- Added transparent data (TD) instruction.
- Fixed bug allowing drawing outside P1/P2 border using IW.


Version 1.8 	8 August, 1992

- The LB command would not draw labels with more non-printing characters
  than printing characters.  This caused labels which used embedded
  backspaces for positioning to not be drawn.  Fixed.

- The LB command would not terminate properly at the end-of-file without
  a label terminator present.  Fixed.

- Relative text size on the CRT increased as paper size enlarged.
  'Should have decreased.  Fixed.

- IW clipping window incorrectly placed when P1/P2 (the corner
  hard clip limits) were not lower-left and upper-right, respectively.
  This resulted in no visible lines being drawn.  Fixed.  It also failed
  to restore the correct clipping when turned off if scaling was on. 
  Fixed.

- DR drew characters in the wrong direction when P1/P2 were exchanged.
  Fixed.

- HP-GL/2 defaults to SI (absolute character sizes) at initialization
  (IN) or when issuing the DF (default) instruction, as does the
  DraftPro plotter.  However, the HP7475 and HP7470 plotters specify
  SR (relative character sizes for these cases.  Two switches were
  added (-70 and -75) to select relative character scaling as the
  default condition.

- XT and YT (tick drawing commands: not HP-GL/2 instructions) were able
  to draw ticks outside the P1/P2 hard clip border.  Fixed.  Also,
  tick length was not rescaling when P1/P2 changed unless TL was 
  executed after P1/P2 changed.  Fixed

- Type 1 scaling (isotropic, with no left and bottom parameters
  specified) did not result in symmetric spacing on the axis which
  was lengthened to achieve isotropic scaling.  Fixed.

- A single pixel line would terminate the program with an integer
  divide overflow. Fixed.

- Filled rectangles didn't work properly if scaling was on.  Fixed.

- Operation of IR not clearly specified for the case of P1/P2 being
  exchanged.  IR as implimented is based on hard clip borders and
  assumes, for reference, P1 is the lower left corner and P2 is the
  upper left corner.


Version 1.6	25 July, 1992

- Fixed bug in graphix.lib preventing labeling from having more non-
  printing characters than printing chars and still be drawn.

- Relative character sizes increased as larger paper sizes were selected.
  They should have decreased due to the necessary reduction in size to
  fit the drawing to the screen.

- DR set the wrong character direction when P1/P2 (the hard clip corner
  points) were exchanged.

- IW set the wrong window coordinates when P1/P2 were exchanged.  The
  result was no drawing on the screen.


Version 1.5	30 December, 1991

- Added debugging flag.  Error messages regarding the source file are now
  suppressed.  The -db flag turns them on.  Error messages are printed to 
  stdout and may be redirected to a file.

- Added four instructions for HP9872 plotter backward compatibility.

- re-wrote the graphics adapter identification code to make maintaining
  the code easier.

- Added PE (polyline encoded) instruction.


Version 1.0	3 September, 1991

- Original release.

The P1/P2 Exchange Problem

There is an issue of semantics which arises for the case of P1/P2
being exchanged.  On a plotter, entering the P1 and P2 points is a
physical process whereby the operator mechanically places the cursor
at the desired corner points.  When one places P1 in the upper left
corner and P2 in the lower left corner of the page, the logical
coordinate system and the physical coordinate system of the plotter
become reflected and inverted.  The plotter defines P1 as the lower
left corner of the page and P2 as the upper right corner of the page. 
Thus, if you move the pen to the physical location P1 or P2
coordinates (using the control panel), the plotter moves the pen to
the upper right or lower left corner, respectively.  However, if you
told the plotter to move to the coordinates of P1 or P2, it would
move to a point opposite of the respective location.  For example, if
one sets P1 = (10250, 7479) and P2 = (250, 279), issuing "PU250,279;"
would move the plotter to the upper right corner of the page, even
though the physical P2 location is in the lower left corner of the
page.

The plotter is being forced to perform a translation from physical 
coordinates into logical coordinates.  By choosing P1 = (10250, 7479) 
and P2 = (250, 279), we have inverted and reflected the logical 
coordinate system.  Thus, moving the pen to the logical
coordinates of P1 (we are not commanding the plotter to move to the 
physical location of P1) moves the pen to the lower left corner of 
the page.  Our choice of coordinate values for P1 and P2 has placed 
larger numerical values in the lower left corner of the page and 
smaller values in the upper right corner.

What does this mean? If you examine the display for program
SHOW_TST.DPF, two of the four frames show P2 in the lower left corner
of the frame.  These frames have P1 and P2 exchanged.  If you examine
the program, the coordinate values given for point P2 are the values
of the P1 coordinate.  The labels are intended to show where the
physical location of P2 would be if you could display it.  However,
the P2 logical coordinate is always in the upper right corner, and
the P1 logical coordinate is always in the lower left corner.  Thus,
wer are forced to appear to mislabel the graph in order to show the
physical P1 and P2 coordinate locations.



Usage

SHOWHPGL -[video][paper][plotter][debug]  [filename]

where 

	filename	optional filename for HP-GL source file.  If a 
			filename is not supplied, standard input is 
			assumed.

	video		option to force usage of a particular video 
			mode.  Values are: c, e, v, for CGA, EGA, or 
			VGA.
			  'c' will force CGA 640 x 200 monochrome mode,
			  'e' will force EGA 640 x 350 16 color mode,
			  'v' will force VGA 640 x 480 16 color mode.

			Default mode is autodetect and select 
			highest resolutions standard mode available.  
			No SVGA modes are supported.

	paper		One of the following standard paper sizes:
			A, B, C, D, E, or A4, A3, A2, A1, A0 .  
			Default size is A. Case is important!!
			A0 is a paper size option: a0 is unknown.

	plotter		Default emulation is HPGL/2.
			'dp'  will select DraftPro emulation.
			'70'  will select HP7470 emulation.
			'75'  will select HP7475 emulation.  

			The HP 7470/7475 have the plotter units coordinate
			origin in the lower left corner.  The DraftPro
			uses the center of the page as the origin.  Note also
			that the 7470 and 7475 emulations do NOT limit the 
			number of pens available to 2 and 6, respectively.  Pen
			colors are limited to those available on the graphics 
			mode you are running (i.e., CGA, EGA, or VGA).

	debug		Default is to silently pass errors.  -db will
			turn on error output to stdout.


The user may also set the environment variable HP-GL to a default set 
of switches, i.e.,

set hpgl=dpA3

specifies default options of DraftPro mode and A3 size paper.

If command line switches are present, the environment settings are
ignored.  Multiple paper size selections will cause the program to
abort.  Multiple video mode selections will default to the highest
resolution autodetected mode.

The switch character is defined as '-'.   It is hard coded into the 
program.  Directory path names may include either or both '\' and '/'
directory separators.  This program has been tested under MS-DOS 3.20
and MS-DOS 5.0 .

All video graphics functions draw using the video BIOS.  No direct 
screen I/O is used.  Additional BIOS supported graphics modes may be 
supported by defining the appropriate structures in graphix.h and the 
macros in graph.h and making appropriate changes to the mode lists in 
autogrph.c and showhpgl.c .

When the debugging flag is turned on, this program generates diagnostic
output text strings when illegal or unsupported instructions are
encountered.  THESE STRINGS APPEAR IN THE GRAPHICS DISPLAY AND MAY
INTERFERE WITH THE DRAWING IF SUFFICIENT ERRORS OCCUR.  If you expect
large numbers of errors and wish to retain a listing of the output,
redirect any generated output to a file.

Note that this program DOES NOT restore the video mode which was 
in use prior to calling this program.  Although the EGA and VGA 
display systems are capable of better than 80 columns and 25 rows on 
the screen, they do not appear as supported IBM BIOS video modes.  
Determination of nonstandard video mode parameters was beyond the 
scope of this program.  If you want to restore a recognized video mode 
at the end of program execution, add the following code to showhpgl.c just 
before the end of main ():

	twait (infile, 50);
	graphics_off ();

This will introduce a 50 second delay before restoring the video mode.  
Shorter delays can be had by changing the value 50 to a more reasonable
number.  If the initial video mode was not a BIOS standard video mode, 
graphics_off () may not be able to restore it properly.


Compilation

The entire package is compiled as follows:

cl showhpgl.c hpgl1.c hpgl2.c getargs.c autogrph.c graphix.lib

Note that this package is compiled with the default optimizations.  Failure 
use at least the default optimizations when compiling showhpgl.c may
result in a _TEXT segment which exceeds 64K and linking will fail. 
graphix.lib is compiled in the small memory model.

Because graphix.lib internally uses Microsoft interrupt calling 
functions, showhpgl must be compiled using the Microsoft compiler.  The object
module mscio.obj, which is in graphix.lib, contains all Microsoft, and PC
in general, specific functions.  This module must be replace in order to
use this package with other compilers and platforms.  Contact the author for
the required information.


Distribution Package

The distribution package includes the following:

showhpgl.doc		this document
showhpgl.exe		the executable program file
showhpgl.c		main program
hpgl1.c			additional functions
hpgl2.c			additional functions
hpgl.h			header file for showhpgl.c, hpgl1.c hpgl2.c
getargs.c		command line options and arguments
autogr.c		video graphix adapter detection
labels.c		labeling font for showhpgl (part of graphix.lib)
graphix.lib		graphics functions library
graphix.h		header file for main program (showhpgl.c)
graph.h			header file for additional modules (hpgl1.c, 
			hpgl2.c)
license.doc		license agreement

	HP-GL test programs

aa_artst.dpf		AA, AR, CI, IP, SC, CT, PR: test general performance
			    of arc and circle drawing with fixed and adaptive
			    segment lengths
attest.dpf		AT: 3-point arc, absolute
actest.dpf		AC: anchor corner test
cptest.dpf		CP: character plot 
ct_citst.dpf		CI, CT: circles with fixed and adaptive segment
			    lengths
di_drtst.dpf		DI, DR: absolute and relative label directions.
dv_sltst.dpf		SL, DV: test slant with DV command.
dvtest.dpf		DV: variable text path (fails this test)
ea_ertst.dpf		EA, ER: edge rectangle absolute and relative
estest.dpf		ES: extra inter-character spacing
ewtest.dpf		EW: outline wedge
ip_irtst.dpf		IP, IR: test & display usage of IP and IR
iwtest.dpf		IW: soft-clip window
labels.dpf		LB, LO, SL, SR, DV: labels and label origins, char. 
			    slant, char. size (relative), direction vertical.
lttest.dpf		LT: line type: note that types 6-9 are identical as 
			    types 7-9 are unsupported.
pa_prtst.dpf		PA, PR: test absolute and relative line drawing
petest.dpf		PE: polyline encoded
ra_rrtst.dpf		RA, RR: filled rectangle, absolute (no solid fills)
rttest.dpf		RT: 3-point arc, relative
sc_test.dpf		SC, DR, DI, LB: test all scaling types, DI, DR, and LB
			    instructions in normal and P1/P2 exchanged 
			    coordinate systems.
smtest.dpf		SM: symbol mode
tl_lotst.dpf		LB,LO,TL,XT,YT: test labels, label origins, x-,
				& y-ticks
fwdaltbx.dpf		drawing to demonstrate the -dp drawing option.  
				Use -C or larger for paper size.

Note: many of these program are dependent on using A-size paper to correctly
display the intended test functions.  Different results may occur from using
other paper sizes unless another paper size is specifically noted.

Some of these test programs are taken from "The HP-GL/2 Reference Guide" 
and, as such are copyright 1990 by Hewlett-Packard.  This book provides
illustrations of what the output of some of these programs should look 
like accompanying the description of the instruction.

The file labels.c is included for those who wish to modify the font used
for labeling.  This font is incorporated into graphix.lib.  To modify the
font, make the required changes to labels.c, compile it to a ".obj" file,
and update the library using "LIB -+labels;" (Microsoft library manager).
You may then re-link the remaining files to create a new program which
uses the new fonts.


Licensing

Please refer to the license agreement in license.doc.  Use of this 
software and the enclosed source code is limited to the terms of the
license.

Bug Reports:

Please report any bugs to 

becker@lennon.src.honeywell.com   (Robert Becker).  

If you prefer, mail them to me at

Robert Becker
15836 Quebec Circle
Eden Prairie, MN   55346


Instructions Status

The following is a list of instructions and the level of implimentation
in showhpgl.exe of HP-GL/2 instructions.  Note that not all instructions 
are HP-GL/2 instructions.  Those with notations in the source column 
indicate where this instruction was found.  Status indicates the level of 
implimentation of the instruction.  There are four levels of implimentation:

Full:		instruction is fully functional as per HP-GL/2
Partial:	instruction implimentation is incomplete
NOP:		no action or action not meaningful for this application
N/A:		not available: instruction was not implimented.

There are 38 Full, 8 partial, 26 NOP, and 29 N/A instructions.  Of the N/A
instructions, 11 are related to character set or font selection.  Of the
NOP instructions, 12 are related to output or digitizing a point and 4 are
for backward compatibility with earlier products.  All output instruction
that have no meaning in this application and are implimented as NOP
instructions.  No dual context mode instructions (HP-GL & PCL) have been
inplimented.

Command	Description			Status	source		Comments

AA	arc absolute			Full
AC	anchor corner			Full
AD	alternate font definition	N/A
AF	advance full page		NOP			compatibility w/HP9872
AH	advance half-page		NOP			compatibility w/HP9872
AR	arc relative			Full
AT	3 point arc absolute		Full
BP	begin plot			Partial			waits TWAIT seconds before clearing plot from screen
CA	designate alternate char. set	N/A	7470
CF	char. fill mode			N/A
CI	circle				Full
CP	character plot			Full
CS	designate std. character set	N/A
CR	color range			N/A
CT	chord tolerance			Full
DC	digitizer clear			NOP
DF	default				Full
DI	absolute label direction	Full
DL	download character		N/A
DP	digitize point			NOP
DR	relative label direction	Full
DS	designate char. set into slot	N/A	DraftPro
DT	Define label terminator		Full
DV	Define variable text path	Partial			No line feed reversal
EA	edge rectangle absolute		Full
EC	enable cutter			NOP
EP	edge polygon			N/A
ER	edge rectangle relative		Full
ES	extra space			Full
ESC	escape code instructions	Partial			No PCL mode switch commands
EW	edge wedge			Full
FI	primary font selection by ID	N/A
FN	secondary font selection by ID	N/A
FP	fill polygon			N/A
FR	frame advance			N/A
FT	fill type			Partial			Only hatched and cross-hatched fills
GM	graphics memory			NOP	DraftPro
IM	input mask			NOP	7470
IN	initialize			Full			Since there is no 'front panel', IN1 is same as IN
IP	input P1 & P2			Full
IR	input relative P1 & P2		Full
IW	input window			Full
LA	line attributes			NOP			No wide lines available
LB	label				Full
LO	label origin			Full
LT	line type			Partial			No adaptive line patterns: types 0-6, only.
MC	merge control			N/A
MG	message to panel		NOP
MT	media type			NOP
NP	number of pens			NOP
NR	not ready			Full
OA	output pen position & status	NOP	7470
OC	output commanded positon & sts	NOP	7470
OD	output digitized point & sts	NOP
OE	output error			NOP
OH	output hard-clip limits		NOP
OI	output identification		NOP
OO	output options			NOP	7470
OP	output P1 & P2			NOP
OS	output status			NOP
OW	output window			NOP	7470
PA	plot absolute			Full
PC	assign pen colors		N/A
PD	pen down			Full
PE	polyline encoded		Full
PG	page advance			Modified		Waits 6 seconds before clearing screen
PM	polygon mode			N/A
PR	plot relative			Full
PS	plot size			Full
PU	pen up				Full
PW	pen width			N/A
QL	quality level			NOP
RA	fill rectangle absolute		Partial			no user defined fills
RF	raster fill definition		N/A
RO	rotate coordinate system	N/A
RP	replot				N/A
RR	fill rectangle relative		Partial			no user defined fills
RT	relative arc 3-point		Full
SA	select alternate font		N/A
SB	scalable or bitmap font		N/A
SC	scale plot			Full
SD	standard font definition	N/A
SI	absolute char. size		Full
SL	char. slant			Full
SM	symbol mode			Full
SP	select pen			Full
SR	relative char. size		Full
SS	select standard char. set	N/A
ST	sort vectors			NOP
SV	screened vectors		N/A
TL	tick length			Full	7470
TD	transparent data		Partial			fn. char. set limited.
TR	transparency mode		N/A
UC	user defined character		N/A
UL	user defined line pattern	N/A
VA	adaptive pen velocity		NOP			compatibility w/HP9872
VN	normal pen velocity		NOP			compatibility w/HP9872
VS	velocity select			NOP
WG	fill wedge			Partial			Outline of wedge, only (no filling available)
WU	pen width unit selection	N/A
XT	x-tick				Full	7470
YT	y-tick				Full	7470

Notes:

	BP instruction is checked for syntax.  BP will wait PG_DELAY seconds
	before clearing the screen if the screen was plotted on.  If the
	screen was not plotted on, the plotter is initialized.  In either
	case, the plotter is initialized.

	PG instruction generates a wait of PG_DELAY seconds before clearing 
	the screen.

	PG_DELAY is defined in hpgl.h as 6 seconds.

	HP-GL and HP-GL/2 distinguish between <cr> and <lf> for 
	positioning on labels.  The C-language, being based in UNIX, 
	assumes the <lf> is the newline character and <cr> has no 
	meaning.  This assumption is also present in this program and 
	some test case labeling and character plotting tests will fail 
	because of this.  The test program dvtest.dpf fails because of 
	this.  The display should look something like:

          D A                  ABC
          E B                  DEF
          F C                     GHI
        G
        H
        I

	Several of the HP-GL/2 specifications are incomplete.  For 
	example, when one is drawing a wedge with symbol mode on, 
	placement of the symbol is unspecified.  Similarly, when TD 
	(transparent data) mode is on, the font used to display the 
	control characters is not specified.  Error handling is not 
	always specified.  For example, when CT is used to specify 
	deviation distance on circles and arcs, this reference does 
	not specify what action to take if a distance tolerance is
	not specified for subsequent circles and arcs.  The DraftPro
	manual specifies that the default shall be 5 degrees in this 
	case.  The Addison-Wesley book does not specify what action
	to take.

	For hatch and cross-hatch fills, it is not clearly specified 
	for the case of user-unit defined hatch x-spacing if the scale 
	in the y-direction should affect the spacing of the hatch. In this 
	implimentation, it was decided that the hatch spacing displayed on
	the screen should be invariant with the rotation angle.

	Additional questions arise in the case of the IR instruction.  One 
	would think that, for the case of P1 and P2 being opposite of their
	normal locations (lower left, and upper right, respectively), that 
	the IR instruction would work off of these coordinates.  However, 
	there are indications of the HP-GL/2 reference guide that IR works 
	off of the default P1 and P2 locations.  That being the case, then
	an IR of two arguments (IR x,y;) following an IP which exchanges 
	the P1 and P2 corners will take the x- and y-values as percentage 
	values based on the corners of convention for P1 and P2.  For 
	example, if one assumes IP10250,7479,250,279; and later executes an
	IR 10,10;, for A-size paper, the IR corner plotter coordinates will 
	be (1030, 765), which, because P2 tracks P1 changes for only one 
	coordinate pair arguments to IR or IP, will force P2 to assume the 
	value of (-8970, -6534).  This is unlikely to be the assumed 
	result.  Further, executing an IR of four arguments 
	(IR x1, y2, xy, y2;) following an IP which exchanges P1 and P2 
	corners will have the effect of reverting the coordinate system to 
	the normal locations for the P1 and P2 corners

	To use IR to exchange the P1 and P2 corners, the first coordinate 
	pair (x1, y2) must be greater than 50% (IR works in percent of the 
	hardclip limits), and the second pair (x2, y2) should be less than 
	50%.

	HP-GL, HP-GL/2, HP, Hewlett-Packard, and DraftPro are registered
	trademarks of the Hewlett-Packard company.

	PC, CGA, EGA, VGA are or may be registered trademarks of the IBM
	company.

	UNIX is a trademark of AT&T.

Reference:

	"The HP-GL/2 Reference Guide", Addison-Wesley Publishing Company.