ADI7221
                              Version 1.0b
                         University of Rochester
                          Psychology Department
                              March, 1992

Sections in this document:

   DISCLAIMER
   TRADEMARKS
   INTRODUCTION
   AUTHENTICITY
   COPYING
   COMPILING
   SYSTEM REQUIREMENTS
   USAGE
   AUTOCAD SETUP
   LINE TYPES
   ERROR AND WARNING MESSAGES
   BUGS

----------------------------------DISCLAIMER---------------------------------

   This software is distributed free of charge.  As such, it comes with 
   ABSOLUTELY NO WARRANTY.  The user of the software assumes ALL RISKS 
   associated with its use.

   Please read the COPYING section of this document to determine your rights
   to copy and/or modify this software.

----------------------------------TRADEMARKS---------------------------------

   IBM is a registered trademark of International Business Machines.

   AutoCAD and ADI are registered trademarks of Autodesk, Inc.

   Hewlett-Packard and HP are registered trademarks of Hewlett-Packard Corp.

   Microsoft and MS-DOS are registered trademarks of Microsoft Corporation.

---------------------------------INTRODUCTION--------------------------------

   The AutoCAD system provides very limited support for different types of
   printers and plotters. Instead of providing support for a wide variety of
   devices, AutoCAD (versions 2 and above) includes the ability to produce
   device independant plot files.  The files are written in the AutoCAD
   Device Independant (ADI) format.

   The ADI7221 program is an AutoCAD ADI file converter that takes an ASCII
   format ADI file and converts it to HP's 7221 plotter language.  The con-
   version produces an output file that can then be sent to the plotter for
   plotting.  Due to the way buffer control and program mode are handled, the
   file must be sent by the SEND7221 program, or some other program that
   understands HP 7221 device control.

   Since an ADI format file contains all of the information needed to plot
   any AutoCAD drawing, the ADI7221 program is quite simple to use, and
   actually has no options at all.  All of the setup work that needs to be
   done actually takes place in AutoCAD.  For that reason, a large portion of
   this document actually concerns itself with the procedures used to
   configure AutoCAD to produce a file that can be converted correctly by the
   ADI7221 program.  Please the read the AutoCAD Setup section of this
   docment for more information on this topic.

---------------------------------AUTHENTICITY--------------------------------
   To ensure that your copy of ADI7221 is virus free, it is recommened that          
   you obtain a copy of the VALIDATE program.  This program is free, and is
   part of the McAffee Associates virus protection package (the rest of the
   package is shareware).  McAffee associates can be contacted at
   (408) 988-3832.

   The Size reported for ADI7221.EXE and the Hex numbers associated with
   "Check Method 1" and "Check Method 2" should match the output from the
   following run of VALIDATE version 0.3:

              File Name:  ADI7221.EXE
                   Size:  15,613
                   Date:  3-16-1992
    File Authentication:
         Check Method 1 - 58FE
         Check Method 2 - 0DA1

-----------------------------------COPYING-----------------------------------

   You may copy and redistribute this software and its source code in its
   unaltered state, provided that each copy is labeled with the original 
   copyright and disclaimer of warranty notices.  Recipients of distributed
   copies of this software must also be given the rights outlined here.  No
   fee may be charged for copies beyond nominal copying and media costs.
   
   You may modify your copy of the source code, and may distribute the
   modified versions under the following conditions:  

      All modified files must be clearly labeled as modified versions, such
      labels must include the authors name, the date, and the nature of all
      changes.

      Any program that contains the source code from this software, in whole
      or in part, must be licensed free of charge, under the same conditions
      as those outlined in this document.  The one exception being that you
      can provide a warranty for your program if you choose.

      A reasonable attempt must be made to notify the orignal author of this 
      software prior to distribution of modified versions.  Such notification
      should include the nature of all changes made to the software.
      
   The original author can be contacted at any of the following address:

        Dave Lutz
        Psychology/Meliora Hall
        Univeristy of Rochester
        Rochester, NY 14627

   Electronic mail may be sent to one of the following addresses:

        Internet: lutz@psych.rochester.edu
                or
                  lutz@prodigal.psych.rochester.edu
        BITNET:   lutz@uordbv

   Bug reports can also be sent to any of the addresses listed above.

----------------------------------COMPILING----------------------------------

  The source code for the ADI 7221 program has been included so that you may
  compile it yourself if you wish.  The code is written in C, and was tested
  using MicroSoft C 5.1.  A Makefile for that compiler has been included in
  the distribution.  If you do not have MSC 5.1, you may have to create your
  own Makefile.

  The source code for ADI7221.EXE is meant to be portable among different PC
  compilers, and probably among different CPU types.  However, the source for
  SEND7221.EXE contains code that may be compiler dependant, and is 
  definitely CPU dependant. (sorry folks, serial I/O on a PC is a royal pain)
  For more information on the non-portable code in SEND7221, read
  SEND7221.DOC.

  The following discussion assumes that the files in the distribution were
  installed as follows:

        /ADI          - .DOC files and precompiled .EXE files
        /ADI/ADI7221  - source for ADI7221.EXE
        /ADI/SEND7221 - source for SEND7221.EXE

  It is critical that you DO NOT COMBINE the source code for ADI7221 and
  SEND7221 in the same directory.  The two programs have modules/files by
  the same names that have different contents.

  Before you begin compilation, CD to /ADI/ADI7221.  Next, look at the
  definitions in MAKEFILE.MSC and modify them for your local site.

  Assuming you have MSC 5.1, you should type "make makefile.msc".  The code
  should compile with no errors, except that you will get the normal "Warning
  target does not exist" message for each module as it is compiled.

  As it is currently defined, the makefile will first produce an executable
  called ADI7221.EXE in the ADI7221 directory.  This executable is then
  packed via MicroSoft's EXEPACK command, producing the final ADI7221.EXE
  in /ADI.

  Once the final exeutable is in place, you can delete all of the .OBJ files
  and the intermediate ADI7221.EXE file from /ADI/ADI7221.

-----------------------------SYSTEM REQUIREMENTS-----------------------------

  ADI7221 should run correctly on any IBM compatible PC that has at least
  80k of free memory.

  There is no limit to the size of the input or output files (except for
  available disk space), and the memory requirements of the program do not
  change with the size of the input and output files.

------------------------------------USAGE------------------------------------

   The command line for the ADI7221 program is quite simple, and consists
   of the following:

        ADI7221 infile.plt outfile.hpp

   There are no command line options.  The program expects infile.plt to be
   an ascii format, AutoCAD ADI file produced via the AutoCAD "plot"
   function.  ADI7221 produces outfile.hpp, overwriting that file if it
   already exists.  The output file contains the HP 7221 plotter codes that
   are to be sent to the plotter.

   In order for ADI7221 to work correctly, AutoCAD must have been set up with
   the correct information for producing the ADI plot file.  For information
   on configuring AutoCAD, consult the AutoCAD Setup section of this
   document.

   The file produced by ADI7221 must be sent to the plotter via the SEND7221
   program (or one similar to it).  The MS-DOS print command will not work
   correctly, due to the way buffer control is handled on the HP 7221
   plotter.  The SEND7221 program is described in the file SEND7221.DOC.

   Since the ADI7221 and SEND7221 programs will usually be run in sequence,
   a batch file, PLOT7221, has been included in the distribution.  The
   command line for this batch file consists of the following:

        PLOT7221 plotname

   The plotname parameter should not include a file extension.  PLOT7221
   looks for a file named plotname.PLT, and attempts to convert it to a
   file named plotname.HPP via the ADI7221 program.  If the ADI7221 program
   completes successfully, SEND7221 is then called to send plotname.HPP to
   the plotter.

   Command line options for the SEND7221 program can be included on the
   PLOT7221 command line.  These options must follow the plotname
   parameter.  Again, SEND7221 and its options are described in SEND7221.DOC.

--------------------------------AUTOCAD SETUP--------------------------------

   As mentioned earlier, there are no command line options for the ADI7221
   program.  The reason for this is that all of your options are set by the
   way you configure AutoCAD.  This section describes the AutoCAD configur-
   ation procedure, and defines settings that are critical for the successful
   use of ADI7221.

   The description that follows is based on AutoCAD release 10.  If you are
   using a different version of AutoCAD, the specific details of the pro-
   cedure may differ slightly.  However, the important thing to get from this
   section is the values used to reply to various configuration questions.  I
   suspect that the configuration questions will be very similar between
   versions.

   There are actually two steps in the confiuration process.  First, you
   define most of the permanent physical characteristics of the plotter,
   then you define pen numbers, line types, and speed settings for each
   of the colors you can use within an AutoCAD drawing.  The first step is
   completed through the configuration menus in AutoCAD, the second step
   is completed when you plot your first drawing.

   To begin the configuration process, start AutoCAD in the usual manner.
   You should be able to select "Configure AutoCAD" from the main AutoCAD
   menu.  Next, select "Configure Plotter" from the resulting menu.

   The currently active plotter type is then displayed on the screen, and
   you are asked if you want to change it.  If the current plotter is not
   "ADI plotter", answer Y and go on to select "ADI PLOTTER" from the
   resulting menu.

   The remaining questions are simple one liners (for the most part), so
   I'll just list the questions and answers.

   Output Format:  ASCII File

   Does the plotter have multiple pens?  Y
   How many?  4 or 10 depending on the model

   Does the plotter support multiple dashed-line styles? Y
   How many?  9

   Is the plotter variable speed?  Y
   Code for highest speed:  36

   Specify units in millimeters? N

   Maximum horizontal (X) plot size in inches: 15.2
   Plotter steps per inch in the horizontal (X) direction: 200

   Maximum vertical (Y) plot size in inches: 10.0
   Plotter steps per inch in the horizontal (Y) direction: 200

   Would you like to calibrate your plotter? N

   Size units (Inches or Millimeters)? I

   Plot origin in Inches: 0.0,0.0

   Enter size or Width,Height (inches): MAX

   Rotate 2D plots 90 degrees clockwise? N

   Pen Width: 0.010

   Adjust area fill boundries for pen width? N

   Remove Hidden lines? N

   Specify Scale by entering:
        plotted inches = Drawing Units or Fit? F

   At this point, you should return to the configuration menu.  Request an
   exit to the Main Menu.  When asked if you want to keep configuration
   changes, answer yes.

   To complete the configuration process, you must begin plotting a drawing.
   After supplying the name of the drawing you want to plot, you will be
   asked to specify the part of the drawing that you want to plot.  After
   that, you will be presented with a list of the settings defined in the
   configuration procedure, and will be asked if you want to change anything.
   You should respond yes.

   After responding yes to the above question, a list of the current pen
   settings for each color will be displayed.  Again, you will be asked if
   you want to change any of the above settings.  You should probably
   respond yes, because the default settings don't take advantage of the
   multiple pen/line-type/speed settings that are available.

   If you respond yes, you will receive a set of prompts for each color that
   has been defined to AutoCAD.  You will first be asked for the pen number
   for that color, then the linetype, then the speed.

   For a list of available line types, see the Line Types section of this
   document.  Typically, you will want to use line type 0 (solid line) for
   all of the colors.

   The speed settings can be anything from 1 to 36.  I set these all to the
   maximum, but it might be better for the plotter to set them somewhat
   lower.

   For most users, there will be several entries that have a color number but
   no color name.  Don't bother assigning values to these entries because
   they will never be used.

   Once you have set the definitions for all of the colors, you can use the
   X command to finish this section.  If you want to double check your work,
   use S to show the current settings.

   You can hit return in response to all of the remaining questions, since
   the only thing we really needed to change was the color/pen settings.  The
   settings that you defined will remain in effect for future plots until
   you change them.

---------------------------------LINE TYPES----------------------------------
             
   As mentioned in the AutoCAD Setup section, it is possible to assign a
   particular line type to any of the color definitions.  The line type
   assigned will be used for all lines drawn in that color.  This is of
   limited value, but might be useful for identifying a color when a pen
   for that color is not actually available.  For example, you might assign
   the color yellow to use the green pen, but to draw all lines in dashed
   mode.  I don't actually recommend this.

   For information on assigning line types, see the AutoCAD Setup section
   of this document.
             
   Currently supported line types are:

         (0)  ----------------------------------- (solid)
         (1)  -- -- -- -- -- -- -- -- -- -- -- -- (dashed)
         (2)  - - - - - - - - - - - - - - - - - - (hidden)
         (3)  ---- - ---- - ---- - ---- - ---- -  (center)
         (4)  ----- - - ----- - - ----- - - ----- (phantom)
         (5)  ................................... (dot)
         (6)  -- . -- . -- . -- . -- . -- . -- .  (dashdot)
         (7)  -- -- . -- -- . -- -- . -- -- . --  (border)
         (8)  -- .. -- .. -- .. -- .. -- .. -- .. (divide)

   Please note that, although the above line types are the same as those
   defined in Release 10 of AutoCAD, they are not used to produce lines
   drawn in a particular type in a drawing.  AutoCAD produces its line
   types by raising and lowering the pen appropriately.

   If the program wass compiled with VARIABLE_DASHES defined, patterns in
   the lines will be varied so that an integral number of patterns will be
   included in each line segment.  If VARIABLE_DASHES was not defined, fixed
   length patterns will be used without regard for the completeness of each
   pattern. (ie short line segments may not include a complete pattern)

   In the precompiled distribution, VARIABLE_DASHES was not defined.



--------------------------ERROR AND WARNING MESSAGES-------------------------

Warning: input file not a version 1 ADI file.

  This warning is produced when a file appears to be an ADI file, but is not
  labeled as a version 1 file.  ADI7221 will attempt to continue processing,
  but may terminate later if other errors are encountered.
  
  AutoCAD versions 2 through 10 all produce version 1 ADI files.  If you are
  using a version of AutoCAD within that range, this may indicate a bug in
  the ADI7221 program.  If you are using a version of AutoCAD higher than
  release 10, check the manuals to see if you can specify which version of
  ADI it should use when creating ADI files.

Warning: PEN_CHANGE encountered but not supported.

  This warning message will only appear if ADI7221 has been compiled with
  WARN_PENCHANGE defined.  The precompiled distribution was not compiled with
  this option defined.

  ADI7221 does not support manual pen changes, because it is not a direct
  feed to the plotter.  A manual pen change requires that output stop while
  an operator manually changes pens.

  Don't confuse the manual PEN_CHANGE command with an automatic pen select.
  ADI7221 will handle automatic pen selections correctly, formulating a
  request for the plotter to automatically select a new pen from the
  specified bay.

  ADI7221 will continue processing after this warning, but the currently
  selected pen will remain in effect.

Fatal error: can't allocate input buffer

  There was not enough available memory to allocate the input buffer.  You
  either have an extrememly low amount of memory, or you have too many things
  open in a multitasking or task switching environment.
  
  Try closing some applications.

Fatal error: can't allocate output buffer

  This is virtually the same as the input buffer allocation message.

Fatal error: can't open input file for reading

  The input file either could not be found, or an I/O error occured when an
  attempt was made to open the file.  
  
  Check the file name for correct spelling.  If the name is correct, try
  running the MS-DOS CHKDSK command to see if there is a problem with the
  disk.

Fatal error: can't open output file for writing

  One of three things can cause this error:  the output file couldn't be
  created due to lack of disk space, the output file exists and has its
  read-only bit set, or an I/O error occured when an attempt was made to
  open/create the file.

  If the output file already exists, run the MS-DOS ATTRIB command to see if
  the read-only bit is set.  If the file doesn't exist, check the amount of
  free space on the disk, or try running the MS-DOS CHKDSK command to see if
  there is a problem with the disk.

Fatal error: can't close input file

  This generally indicates a problem with the disk.

  Try running the MS-DOS CHKDSK command to identify the problem.

Fatal error: can't close output file

  This generally indicates a problem with the disk.

  Try running the MS-DOS CHKDSK command to identify the problem.

Fatal error: I/O error on input

  This generally indicates a problem with the disk.

  Try running the MS-DOS CHKDSK command to identify the problem.

Fatal error: I/O error on output

  This can be caused by either running out of space on the output disk, or
  encountering a real media error.

  Check the available free space on the output disk.  7221 format files
  typically use about 1/2 the space of the ADI input file.  If there seems
  to be enough space for the output file, try running the MS-DOS CHKDSK
  command to see if there is a problem with the disk.

Fatal error: input file not a valid ADI file

  Upon examining the input file, ADI7221 does not recognize it as an ADI
  file.

  Recreate the input file via the plot function in AutoCAD.  Make sure that
  AutoCAD has been configured to produce an ascii format ADI file.

Fatal error: Multiple BEGIN_PLOT commands found

  The input file was probably altered after it was created by AutoCAD.  The
  most likely cause would be appending one ADI file to another, which is a
  definite no no.

  Recreate the input file via the plot function in AutoCAD.

Fatal error: invalid MOVE command

  The ending location for the move was so far out of bounds that it exceeded
  the 7221 parameter limits.

  Check the configuration in AutoCAD.  Make sure that the size of the
  plotting area is the same as that specified in the AutoCAD Setup section of
  this manual.

Fatal error: invalid DRAW command

  The ending location for the draw was so far out of bounds that it exceeded
  the 7221 parameter limits.

  Check the configuration in AutoCAD.  Make sure that the size of the
  plotting area is the same as that specified in the AutoCAD Setup section of
  this manual.

Fatal error: invalid NEW_PEN command

  The requested pen number was so far out of bounds that it exceeded the 7221
  parameter limits.

  Check the configuration in AutoCAD.  Make sure that the number of pens
  defined is equal to the number of pens on the plotter (typically 4 or 10).

Fatal error: invalid SET_SPEED command

  The requested speed was out of the range defined in ADI7221.

  Check the configuration in AutoCAD.  Make sure that the highest speed
  setting is within the limits specified in the AutoCAD Setup section of
  this manual.

Fatal error: invalid LINE_TYPE command

  The requested line type was out of the range defined in ADI7221.

  Check the configuration in AutoCAD.  Make sure that the number of line
  types is within the limits specified in the AutoCAD Setup section of
  this manual.

Fatal error: input file contains ABORT_PLOT command

  The plot function in AutoCAD was interrupted during the creation of the
  input file.

  Recreate the input file via the AutoCAD plot function.

Fatal error: unknown command encountered

  ADI7221 encountered a command that it cannot decode.  The input file either
  is not an ADI file at all, or is not a version 1 ADI file.

  Try recreating the input file via the AutoCAD plot function.  AutoCAD
  versions 2 through 10 all produce version 1 ADI files.  If you are using
  a version of AutoCAD within that range, this may indicate a bug in the
  ADI7221 program.  If you are using a version of AutoCAD higher than release
  10, check the manuals to see if you can specify which version of ADI it
  should use when creating ADI files.

Fatal error: no END_PLOT encountered

  ADI7221 has come to the end of the ADI file, but has not encountered an
  END_PLOT command.  This may indicate that AutoCAD was interrupted while
  creating the ADI file.

  Recreate the input file via the AutoCAD plot function.

------------------------------------BUGS-------------------------------------

   Disk I/O errors are not all identified by type.  An error message caused
   by running out of space is the same as one caused by a true media error.

   AutoCAD must be configured for the correct number of pens.  ADI7221 does
   not check to ensure that a pen select request is within the range of
   available pens.  This is due to the differing number of pens available
   on 7221 series plotters.

   Due to the device independant nature of AutoCAD ADI files, none of the
   advanced features of the 7221 plotter are used.  This tends to result in
   large plot files, both for ADI format and for 7221 format.  This is
   espcially true for drawings containing text, since the text is actually
   drawn like a graphic figure.

   Error and Warning messages should probably have been given numbers so
   they would be easier to find in this manual.  There are only about 20
   possible errors, so it shouldn't be too big of a deal.