INSTALLATION MANUAL


This manual is intended for use with 
PINSTALL, the installation program supplied 
with the PADS-PCB and PADS-Logic Evaluation 
Packages.

The PINSTALL program is used to copy the 
PADS-PCB and PADS-Logic software and the 
parts library, from floppy diskettes onto 
the computer, and to configure the software 
for your hardware.

The installation process will take 
approximately three minutes to complete 
because of the large parts library shipped 
with the software.

Hardware Requirements

The computer that will be used for the 
PADS-PCB and PADS-Logic Evaluation must 
conform to the following:

o  	80286, 80386SX, 80386, 80486, or PS/2 
computer.
o  	DOS Version 3.30 or higher.
o  	EGA, VGA, or equivalent graphics 
adapter with 16 color capability. The 
programs support many high-resolution EGA 
and VGA adaptors.
o  	A 2 button or 3 button  serial or bus 
mouse that is compatible with Microsoft, 
Mouse Systems, or Logitech mice, with an 
installed driver.
o 	Serial port for a mouse (except for a bus 
mouse).
o	A 20 Megabyte hard drive with a minimum 
of 5 Megabytes of disk space available.
o	640 KBytes DOS memory.



Mouse Hardware

PADS does not provide a driver for your 
mouse. Either the mouse driver for your 
mouse must be loaded at startup time by  
inclusion in your CONFIG. SYS file, or it 
should be a program started in the 
AUTOEXEC.BAT file. Should you have 
questions, consult the manual shipped with 
your mouse for instructions how to do this.

Directories Created by the Evaluation Programs

The software may be loaded on any drive on 
your hard disk. When you load the software, 
the following directories will be created 
on the specified disk drive:

Directory Path	Files	Disk 
Size (MB)
<drive:>\PADSDEMO	PCB & Logic programs 
	2.9
<drive:>\PADSDEMO\LOGFIL	Schematic files	0.3
<drive:>\PADSDEMO\FILES	PCB  files	0.7
<drive:>\PADSDEMO\LIB	Library files	2.5
<drive:> \PADSDEMO\CAM	Output file 
directory	0
            
Installing PADS Evaluation Software

This installation procedure can be used to 
install PADS-PCB, PADS-Logic , or both 
programs. 

1) 	Place either the  disk labeled PADS-
Logic Evaluation or PADS-PCB Evaluation  
Software in drive A:.  In response to 
the prompt:
C>
	Type:  
A:PINSTALL <CR>
Note: <CR> will  be used to indicate the 
Enter key.
2)	The installation program's screen is 
displayed. In the center is  a pop-up 
menu with the following options:
	o	SHAREWARE INSTALLATION
	o 	HARDWARE SETUP
3) 	Select SHAREWARE INSTALLATION by moving 
the highlight bar to this choice with 
the arrow keys, and selecting with 
function key F1 or <CR>
4) 	The program to be installed is listed 
next, either SHAREWARE PCB or SHAREWARE 
LOGIC. You may select either. If you are 
installing both Evaluation programs,  
you should install SHAREWARE Logic 
first.
5) 	If you are installing SHAREWARE LOGIC, 
move the highlight bar to SHAREWARE 
LOGIC and again select with F1.
6) 	You are asked to specify the destination 
hard disk drive on which to load the 
software. Type the appropriate drive 
name:  C or D or E etc.  depending on 
the drive you wish to load the software 
onto. You are next asked to define the 
source floppy disk drive from which the 
software is being loaded. Type the drive 
name of your floppy disk:
A or B
7) 	Your selected source and destination 
drive are listed and you are asked to 
confirm.  If the choices  displayed are 
correct, respond with Y  .  If incorrect, 
respond with   N    and repeat steps 5 
through 7.
8) 	You are prompted if it is OK to load the 
software. Check that you have sufficient 
disk space, and that it is Ok to create 
the directories listed. If it is OK, 
respond  by typing  Y   to initiate the 
loading process. 
	Make sure the floppy disk is installed 
correctly,  and type   Y   again. As the 
software is being copied to the hard 
disk, a series of messages will be 
displayed
9) 	Next you are asked if you wish to load 
the library. Respond Y  if you plan to 
load the library. Respond N if the 
library has already been loaded.
10) Replace the PADS-Logic disk with  the 
PADS Library disk, and type Y again to 
transfer the contents of the disk into 
the library on the hard disk. The 
library will then be read.
11) When the library transfer is complete, 
the  message:
Software Installation has been Completed. It is 
Necessary To Run A Hardware Setup.
	appears. Respond by selecting F1 to 
return to the main menu.
12) If you do not wish to install PADS-PCB, 
go to the next section, Configuring Your 
Hardware. If you wish to install PADS-
PCB, select SHAREWARE INSTALLATION 
again, and select SHAREWARE PCB from the 
next menu. Install the floppy disk 
labelled PADS-PCB Evaluation package.
13) If you have installed PADS-Logic 
already, follow steps 6 through 8 above  
to install PADS-PCB.
14) If you did not install PADS-Logic, you 
must also install the library after  
installing PADS-PCB, following steps 9 
and 11.

Configuring Your Hardware

The software installation is now complete, 
and you will next configure the shareware 
program for your hardware.  If you have 
installed PADS-Logic and PADS-PCB, this 
procedure must be done twice, once for each 
program.

1) 	Move the highlight bar to HARDWARE SETUP 
and select it with F1.
2) 	You must select the program you wish to 
configure.  Move the highlight bar over 
either SHAREWARE PCB or SHAREWARE LOGIC, 
and select F1.
3) 	You will be asked to confirm the drive 
where  the PADS evaluation software and 
your DOS operating system are installed. 
If the displayed drives are correct, 
respond Y. If they are not correct, 
respond N  and correct the drives by 
answering the questions.
4) 	You then select the appropriate graphics 
driver from the list displayed. 
Selection is made by moving the 
highlight bar over the appropriate 
graphics name and selecting with F1. If 
you do not see your graphics card, 
select either 1. IBM EGA or 2. IBM VGA.
5) 	The next configuration option is for 
your Matrix Printer. Use the up and down 
arrow keys and the F1 key to select the 
printer you are using. If you do not 
have a printer, select any option.  An 
unlisted matrix printer can be used if 
it is compatible with one of the 
printers listed below. To the right of 
the printer name are entries that define 
the page width and page length. These 
are  in .001" units, and  may be edited 
by moving the cursor with the right 
arrow and typing a new value.
6) 	You next define the type of laser 
printer you have, if any. Move the 
highlight bar to the appropriate choice 
from the list, and select with F1. If 
you do not have a laser printer, select 
F1 to move to the next screen.
	To the right of the printer name are 
entries that define the page width and 
page length. These are  in .001" units, 
and  may be edited by moving the cursor 
with the right arrow and typing a new 
value. 
	Printer carriage widths are either 13.2" 
carriage or 8.0" in width.  Type in 
either 8000 or 13200, if the current 
value is not correct. When creating a 
check plot with the matrix printer, you 
will want the printer to ignore the page 
boundaries.  This is done  if the "page 
length" is set to zero.  Use the 
right/left arrows to position the cursor 
to the "page length" column and edit, as 
appropriate.  
7) 	You will next configure the software to 
support your pen plotter .The models 
supported are listed . If you do not 
have a pen plotter or your plotter is 
not compatible with any listed, choose 
any model. Move the highlight bar to the 
appropriate choice and select with F1. 
To the right of the plotter name are a 
number of parameters you may edit by 
moving the cursor with the right arrow. 
They are used as follows:
	o Pens is the number of pens your 
plotter has.
	o X and Y Size define the paper size you 
are using.
	o Pen Width is the width in mils of the 
pen.  This is used to calculate fill 
patterns.
	o Rotation identifies if you want the 
drawings rotated on the paper.
	Note: these last two settings may be 
overwritten from within the program, so 
if in doubt, use the default settings.
8) 	The next screen defines the photoplotter 
type, number of apertures, and output 
format for photoplotting . Both vector 
and laser plotters are supported. We 
recommend that you check with your 
photoplotting vendor on the following 
parameters. The meaning of the 
parameters is as follows:
	o APERTURES defines the number of 
apertures in the plotter.
	o XSIZE and YSIZE define the plotter 
table size.
	o UNITS defines the output format,  
Metric (1) or Inch (0).
	o PREC defines the precision of the 
plotter output. The value is the number 
of digits to the right of the decimal in 
the output.
	o DIGIT is  number of digits in the 
output coordinates, including leading or 
trailing zeros.  The decimal point is 
assumed and does not count as a digit.
	o ZERO defines the suppression rules for 
zeroes. 0 = No suppression; 1 = Suppress 
leading zeros; 2 = Suppress trailing 
zeros
	o COORD defines the coordinate system, 0 
= Absolute, 1 = Incremental
	o REPEAT defines if a repeated 
coordinate value for x or y should be 
suppressed (1) or not suppressed (0) in 
the Gerber file output. Suppression 
reduces the size of the output file, but 
not all plotters are compatible with 
this.
9) 	The Device Status screen defines which 
output devices are on-line, and the 
communication port that they are 
attached to. For each printer or 
plotter, you must define it as on-line 
or off-line, and then define the port.  
The port options are PRN, COM1, and 
COM2.
10) The next two messages may appear, 
depending on the system configuration. 
The software will automatically modify 
the AUTOEXEC.BAT file, if necessary. 
Before doing so, a message:
OKAY TO MODIFY AUTOEXEC.BAT  (YES/NO)
	will ask if you want  to change your 
AUTOEXEC.BAT file to include PADSDEMO in 
the search path, and to set up the 
serial port for the plotters. These 
modifications  do not delete any 
commands from your existing AUTOEXEC. 
They add those entries required for 
PADS-PCB and PADS-Logic.  If you respond 
Y, the system automatically modifies the 
AUTOEXEC.BAT  file.  You do not need to 
do anything further.  
	Note: AUTOEXEC cannot be updated when 
SHARE is loaded. Either remove SHARE 
before starting the installation, or 
manually edit the AUTOEXEC file. 
	This message may be followed by the 
message: 
YOUR CONFIG.SYS FILE NEEDS TO BE
MODIFIED TO ALLOW 40 FILES (YES/NO)
	If you respond Y, the program will 
modify your CONFIG.SYS file. 
11) The installation is complete. If you 
are installing both PADS-PCB and PADS-
Logic, you will have to repeat this 
process for the second program.
12) To exit from the installation program, 
return to the main menu and select the 
Esc key, followed by  a Y to  confirm.
	Remove the PADS Logic Evaluation disk 
from the floppy disk drive and store it 
in a safe place. Reboot the computer 
after confirming that CONFIG.SYS has the 
FILES=40 statement, and \PADSDEMO has 
been added to the PATH statement in your 
AUTOEXEC.BAT file. 




Possible Problems 


You may encounter problems trying to load 
or run the Evaluation programs. Frequent 
problems, and possible solutions, are 
listed below. If these do not work, call 
the PADS Software Inc. hotline, at (508) 
486-3328 for assistance. 

Mouse Not Functioning

The PADS SHELL appears  when you type:
PADSGO<CR>
 but the cursor does not move when the mouse is 
moved, and you cannot select a program. 

Solution:  
Probably the mouse driver is not installed 
correctly.  Check that the Mouse Driver for the 
mouse you are using is Installed in your CONFIG.SYS 
or AUTOEXEC.BAT files. The mouse should have a test 
program. Test the mouse with this program.
     
Graphic Problems
	
The PADS Shell appears, but a  blank screen appears 
when you enter either PADS-PCB  or PADS-Logic. 

Solution:
During the hardware installation, you have selected 
an incorrect graphics driver.  Type Alt-X to exit 
the program, and rerun PINSTALL again, skipping the 
Software Installation and selecting the Hardware 
Setup. If the graphics card is not listed or you do 
not know what kind of card you have,  choose either 
option 1 , IBM EGA, or option 2, IBM VGA.

Pen Plotter Does Not Work

When the pen plot option is selected, there is no 
output.

Solution:
1. Rerun the Hardware Setup in PINSTALL, to verify 
that the  port the pen plotter is set to, COM1 or 
COM2, is correct. Also, insure that the pen plotter 
is set to On-Line.
2. Insure the statement 
MODE COM2:9600, N, 8, 1, P
(or COM1) is in the AUTOEXEC.BAT file.

Insure there is a COM1 or COM2 recognized by the 
system. To check, type the following:
Mode COM2:9600,n,8,1,P<CR>
If there is a COM port, the system should echo back 
the MODE command; If there is not, the message:
Invalid parameter, COM
will appear. If  it does, either there is physically 
no card installed, or quite possibly the switch 
settings are incorrect on the card.


(end of manual)
PADS  Shareware Installation Manual

	PADS Shareware Installation Manual

1

	1

PADS  Shareware Installation Manual

	PADS Shareware Installation Manual

1

	1