Quickroute 1.3
--------------

The Professional Solution to PCB/Circuit Design
------------------------------------------------


All software is copyright (c) Dr Ian R Frost 1988,1992
POWERware, 14 Ley Lane, Marple Bridge, Stockport,
SK6 5DD, United Kingdom.





1 Introduction
--------------

Welcome to Quickroute (QR). This powerful package combines a sophisticated
environment with pull down menus, icons, windows and Microsoft(R) mouse
support, with a powerful full-featured PCB or circuit design system which
includes 'rats nest' auto-routing on up to 8 board layers simultaneously. 

Quickroute is a SHAREWARE product which means that you are free to
distribute this software by copying the files on the disk intact to another
disk and you are free to try out the software. However, if you wish to 
use Quickroute to design PCB's or other graphic designs you MUST register 
with POWERware by sending a cheque drawn on a USA bank for $60 to POWERware,
14 Ley Lane, Marple Bridge, Stockport, SK6 5DD, United Kingdom. In return you
will receive a full, good quality A4 manual, the latest version of Quickroute
Professional, a Hewlett Packard plotter driver (HPGL), a 24 pin EPSON style
printer driver, a Laser printer driver and ICONEDIT, a utility for editing
the bit-image symbol type. 

PCB designs made with Quickroute can be identified by the decisions it
takes when routing tracks, by the pad outer/inner radii ratio, and in the
way DIL and surface mount pin outs are drawn. Be warned, this product has
taken a great deal of time and effort to develop and POWERware takes the
requirement for registration seriously! 

Ensure the continued support of shareware by professional programmers by
registering your use of a product now!


2 Overview
----------


Quickroute includes an immense range of features some of which are:

* Powerful pull-down menu support with ultra-fast icon selection for
frequently used commands.

* Simple but FAST multi-layer auto-routing with rats nest input.

* FAST redraw in any scale from X0.0001 to X10000!

* High quality output to EPSON and IBM generic printers in various qualities
and virtually any scale.

* Powerful symbol manipulation including the ability to grab portions of a
PCB, rotate symbols, edit, etc. Two symbol libraries included (PCB and circuit
diagram).

* Choose from 96 pad sizes/styles, 24 track widths, filled or outlined
circles, ellipses and boxes, various text styles/sizes, arcs, custom
designed 40X40 bit images, any number of library symbols, and range of
instantly available DIL pin outs.

* Use up to 8 layers + 2 silk screen layers. Automatic solder mask
generation.

* Choose objects pictorially from windows!

* Use with virtually any IBM PC/XT/AT/386/486 machine with at least 512K
memory and either a CGA/EGA/VGA or Hercules graphics card. Support for a
Microsoft (R) compatible mouse included.



3 Tutorial
----------

This tutorial covers the basic operation of Quickroute. The full manual is
available when you register with POWERware (see section 1). You will need
this as most of the features are only briefly discussed, and others are not
mentioned at all. If you are going to spend your time developing a design
then it makes sense to register so that you get the most out of this
product.



3.1 Introduction
----------------

In order to run Quickroute you will need and IBM PC/XT/AT or 100% compatible
with at least 512K, a 720K disk drive, and either a CGA/EGA/VGA or Hercules
monochrome graphics card. A Microsoft(R) compatible mouse is also highly
recommended. This should be installed with a suitable driver (see the
manual that came with your mouse). 



3.2 Starting Quickroute
-----------------------

If your system has a hard disk drive then you can install Quickroute onto
the drive by inserting the Quickroute disk into drive A and typing INSTALL
at the MS-DOS prompt. Follow the instructions displayed on the screen
carefully. If you don't have a hard disk then simply insert the disk into
drive A and type QR.

Once started a sign on banner will be displayed on your screen followed by
a reminder to register your use of Quickroute. The screen will then clear to
show the main workbench. 

The menu line at the top of the screen is accessed by either, pointing the
mouse at the first letter of the menu you wish to pull down and pressing the
right mouse button, or by pressing the first letter of the menu. The menu
will then appear. To select a function again either point the mouse at the
required function and press the right button or press the first letter of
the menu option. You can also use the arrowed cursor keys to move the
highlighted bar up/down the menu. Press return to select the function.

The icons to the right of the screen are accessed by either pointing the
mouse at the icon and pressing the LEFT mouse button or by using the
function keys F1 and F2 to highlight an icon and pressing the space bar.

The status line at the bottom of the screen tells you how much memory you
have got left (the bar), the side you are editing, the object type you are
using and the cursor position. A variety of prompts will also be displayed
here.


3.3 Loading and Editing a PCB
-----------------------------

To get a feel for editing PCB's try loading the demonstration PCB into
Quickroute. To do this pull down the Files menu, and select 'Load Pcb'. Enter
the name 'DEMO.PCB' in the status line and hit return. The PCB will then be
loaded and drawn on the screen in the position it was saved at. To speed up
the screen redraw time, pull down the 'Options' menu and select 'Turbo'.
Alternatively just hit the 't' key. The redraw time will then be considerably
reduced because all objects will be drawn as outlines. To draw a grid again
pull down the 'Options' menu and select 'Grid' or press the 'g' key. Grid and
turbo can be toggled on/off as required.

The scale the demonstration PCB will be loaded in is X1.0. To change the
scale move the cursor to the centre of the screen and press one of the
numeric keys (1-8). The PCB will then be redrawn in a different scale.
Alternatively pull down the 'Options' menu and select zoom. A second menu
will open and the scale can be entered. To enter a custom zoom, say X1.635
simply pull down the 'Edit' menu and select 'Custom zoom'. Enter the required
scale in the status line.

When PCB's are scaled up, the screen becomes a window onto the total design
area. You can move the window around either by moving the mouse pointer to
one of the arrow boxes at the bottom left of the screen and pressing the
LEFT mouse button or by moving the cursor to the edge of the screen using
the normal cursor keys. Alternatively move the cursor to a given area of
the design and press 'p' for pan. The PCB will then be redrawn with the
selected area moved to the centre of the screen.


3.4 Adding Objects onto a PCB
-----------------------------

To place an object onto the design move the cursor to the position where
you wish the object to be placed and press the LEFT mouse button. The
current object type (see the status line) will then be placed. There are six
main object types; pads, tracks, integrated circuits, symbols, icons and
primitives. These are selected by clicking on the appropriate icon to the
right of the screen. Assuming that the top left hand icon is icon 1, and the
bottom left icon is icon 12 then icons allow the placement of respectively,
pads, tracks, integrated circuit pin outs (DIL), symbols, and icons. The icon
containing the question mark is used to change the pad/track/symbol/etc
type or size. The other icons allow the user to add text, circles, arcs,
ellipses and rectangles. Follow the instructions that appear in the status
line to use these.

Once an object type has been selected you can place any number onto the
PCB up to the memory limit.

Example
-------

1. Select the symbol object type by moving the cursor to icon number 4 and
pressing the LEFT mouse button.

2. Change the current symbol type by moving the mouse cursor to icon
number 6 and pressing the LEFT mouse button. You should then see a window
open at the centre of the screen with a page of symbols from the current
library.

3. Move the cursor to one of the symbols shown and press the LEFT button.
The arrows at the bottom left of the window allow you to move backwards and
forwards through the current symbol library a page at a time.

4. Move the cursor to any position on the PCB and press the LEFT mouse
button. The symbol will then be drawn.



3.5  Deleting Objects
---------------------

To delete an object move the mouse cursor to icon 7 ( an eraser symbol) and
press the LEFT mouse button. Then point to the object you wish to delete
(eg. the centre of a pad, the start of a track, the first pin on an ic pin out,
etc) and press the LEFT mouse button. A cross will appear on the object
selected for deletion. You will then be asked to either accept, quit or
continue. Press 'a' or point to the accept box and press the LEFT button to
delete the object. A more powerful block delete facility is described in
section 7.


3.6  Symbol Libraries
---------------------

Quickroute allows you to incorporate any number of symbols from any
number of libraries (up to the limits of computer memory) into your designs.
Symbols can be edited, rotated, added to, deleted, etc, using the commands
available under the 'Symbol' menu. Two sample libraries are provided,
CONFIG.COM, the default PCB symbol starter set, and CIRCUIT.COM, the circuit
diagram symbol set. Try loading in the circuit diagram symbols by pulling
down the 'Symbol' menu and selecting 'Load'. Enter 'CIRCUIT.COM' at the
status line and press return.


3.7  Block Commands
-------------------

Quickroute allows you to select rectangular blocks of your design and
either copy them to other regions of the design, move them to other areas,
delete them, rotate them through a variety of angles, or reflect the blocks
about the x or y axis. To do this pull down the 'Edit' menu and select 'Block'.
Then move the cursor to a given area of the PCB and press return/LEFT
mouse button. Next move the cursor to another region of the PCB so that the
'rubber banded' rectangle contains the region of interest. Press the LEFT
mouse button. Then select Move/Copy/Delete/Rotate/Reflect by pressing the
appropriate key (see the status line). Follow any further instructions in
the status line to complete the operation.


3.8  Autorouting
----------------

The autorouter will automatically attempt to find an unobstructed route
between any two given points. Start and finish positions can be entered
either singly or as a set of rat lines. All routes placed by Quickroute will
contain node angles which are multiples of 45 degrees, will have fewer than
10 nodes, and fit into a rectangle with opposite corners defined by the
start and finish positions. The router is simple but fast. 

To use the router, pull down the 'Edit' menu and select either 'Auto-route'
or 'Rats-nest'. You will then be asked to enter one or more start and finish
positions on the PCB. Press the 'Q' key or RIGHT mouse button to start
routing. Note that all sides currently displayed will be used by the auto-
router. 


3.9  Printing and Plotting Designs
----------------------------------

The shareware version of Quickroute allows you to print PCB's on either an
IBM or EPSON style 9 pin dot-matrix printer. The printer should be an EPSON
FX compatible, 8" carriage, machine or the equivalent IBM printer. 
Registering as a user of this product will entitle you to receive the full
driver pack which includes a Hewlett Packard Graphics Language (HPGL)
driver for pen plotters. Other drivers may also be included (eg. 24 pin dot-
matrix and LaserJet printer support) depending on demand, ie. the number of
people who register!
To print a PCB design, pull down the 'Files' menu and select 'Print PCB'.
Follow the instructions that appear in the status line. Make sure that you
answer 'no' when asked if you wish to change the printer/plotter options, or
you may get unpredictable results.

The default printer/plotter output port is LPT1, this can be changed by
pulling down the 'Files' menu and selecting 'Output'.



3.9  And finally ..
-------------------

This brief manual can only hope to give a taste of the abilities of
Quickroute. Remember that if you wish to use Quickroute to produce PCB's or
any other output you must register by sending a cheque for $60 to
POWERware, 14 Ley Lane, Marple Bridge, Stockport, SK6 5DD, United Kingdom. 

In return you will receive the latest version of Quickroute
Professional, a full manual, a full driver pack, and a list of any product
options or updates that are available. 



Dr I R Frost, 1992
------------------