S P L O T  -  The Pen Plotter Simulator V2.4
                --------------------------------------------
                   Copyright (C) 1989-92 by Alexandr NOVY
                             All rights reserved.

                                 April 1992


        This file  contains technical  information about  pen plotter
        types supported by the  SPLOT program. It also  contains list
        of  supported  plotter  instructions  for each listed plotter
        type.


          1. General Information:

          The  SPLOT  program  is   available  in  various   versions
        according to the type  of simulated  plotter. This means that
        each SPLOT.EXE  module is  designated for  a certain  plotter
        type.   This  principle  gives  the  maximum  reliability  of
        simulation of the given plotter type. At present versions for
        the following plotter types are at your disposal:

           Plotter type                          | Plotter syntax
         ------------------------------------------------------------
           ROLAND DXY 1100/1200/1300             | DXY-GL / RD-GL I
           HP 7470A                              | HP-GL
           HP 7475A                              | HP-GL
           HP 7440A ColorPro                     | HP-GL
           HP 7550A                              | HP-GL
           HP 7570A/7575A/7576A DraftPro DXL/EXL | HP-GL
           HP 7595A/7596A DraftMaster I/II       | HP-GL

          An UNREGISTERED COPY  of the program  is available only  in
        the version for the HP 7475A plotter. The versions for  other
        plotter types can  be received only  on the basis  of regular
        registration.  See  the  file  LICENCE.DOC  for  registration
        information.




          2. Description of Supported Plotters:

        -------------------------
        HP 7470A Graphics Plotter
        -------------------------

        Syntax: HP-GL

        Number of pens: 2

        Paper formats: ISO A4 (210 x 297 mm)
                       ANSI A (8.5 x 11 in.)

        Plotter unit: 0.025 mm

        Maximal number of digits in decimal fraction to be read: 4

        Number of character sets: 5 (0-4)
                                  (all supported by SPLOT)

        Alphabetical list of plotter instructions supported by
        the HP7470A version of SPLOT:

         AA  - The Arc Absolute Instruction
         AR  - The Arc Relative Instruction
         CA  - The Designate Alternate Character Set Instruction
         CI  - The Circle Instruction
         CP  - The Character Plot Instruction
         CS  - The Designate Standard Character Set Instruction
         DF  - The Default Instruction
         DI  - The Absolute Direction Instruction
         DR  - The Relative Direction Instruction
         DT  - The Define Terminator Instruction
         IN  - The Initialize Instruction
         IP  - The Input P1 and P2 Instruction
         IW  - The Input Window Instruction
         LB  - The Label Instruction
         LT  - The Line Type Instruction
         PA  - The Plot Absolute Instruction
         PD  - The Pen Down Instruction
         PR  - The Plot Relative Instruction
         PU  - The Pen Up Instruction
         SA  - The Select Alternate Character Set Instruction
         SC  - The Scale Instruction
         SI  - The Absolute Character Size Instruction
         SL  - The Character Slant Instruction
         SM  - The Symbol Mode Instruction
         SP  - The Select Pen Instruction
         SR  - The Relative Character Size Instruction
         SS  - The Select Standard Character Set Instruction
         TL  - The Tick Length Instruction
         UC  - The User Defined Character Instruction
         VS  - The Velocity Select Instruction (for information only)
         XT  - The X-Tick Instruction
         YT  - The Y-Tick Instruction

        The following instructions are  NOT supported by the  HP7470A
        version of  SPLOT (they  are checked  for syntax  only and no
        action is performed):

         - All escape code sequences.
         - All output instructions:
            OA, OC, OD, OE, OF, OI, OO, OP, OS and OW.
         - Digitizing instructions DP and DC.
         - The Input Mask Instruction IM.



        -------------------------
        HP 7475A Graphics Plotter
        -------------------------

        Syntax: HP-GL

        Number of pens: 6

        Paper formats: ISO A4 (210 x 297 mm)
                       ISO A3 (297 x 420 mm)
                       ANSI A (8.5 x 11 in.)
                       ANSI B (11  x 17 in.)

        Plotter unit: 0.02488 mm (0.025 mm in SPLOT)

        Maximal number of digits in decimal fraction to be read: 4

        Number of character sets: 19 (0-4,6-9,30-39)
                                  (all supported by SPLOT)

        Alphabetical list of plotter instructions supported by
        the HP7475A version of SPLOT:

         AA  - The Arc Absolute Instruction
         AR  - The Arc Relative Instruction
         CA  - The Designate Alternate Character Set Instruction
         CI  - The Circle Instruction
         CP  - The Character Plot Instruction
         CS  - The Designate Standard Character Set Instruction
         DF  - The Default Instruction
         DI  - The Absolute Direction Instruction
         DR  - The Relative Direction Instruction
         DT  - The Define Terminator Instruction
         EA  - The Edge Rectangle Absolute Instruction
         ER  - The Edge Rectangle Relative Instruction
         EW  - The Edge Wedge Instruction
         FT  - The Fill Type Instruction (Note, that for HP7475A
               plotter fill angle may be specified in  45 degree
               increments only.)
         IN  - The Initialize Instruction
         IP  - The Input P1 and P2 Instruction
         IW  - The Input Window Instruction
         LB  - The Label Instruction
         LT  - The Line Type Instruction
         PA  - The Plot Absolute Instruction
         PD  - The Pen Down Instruction
         PR  - The Plot Relative Instruction
         PT  - The Pen Thickness Instruction
         PU  - The Pen Up Instruction
         RA  - The Shade Rectangle Absolute Instruction
         RO  - The Rotate Coordinate Instruction
         RR  - The Shade Rectangle Relative Instruction
         SA  - The Select Alternate Character Set Instruction
         SC  - The Scale Instruction
         SI  - The Absolute Character Size Instruction
         SL  - The Character Slant Instruction
         SM  - The Symbol Mode Instruction
         SP  - The Select Pen Instruction
         SR  - The Relative Character Size Instruction
         SS  - The Select Standard Character Set Instruction
         TL  - The Tick Length Instruction
         UC  - The User Defined Character Instruction
         VS  - The Velocity Select Instruction (for information only)
         WG  - The Shade Wedge Instruction
         XT  - The X-Tick Instruction
         YT  - The Y-Tick Instruction

        The following instructions are  NOT supported by the  HP7475A
        version of  SPLOT (they  are checked  for syntax  only and no
        action is performed):

         - All escape code sequences.
         - All output instructions:
            OA, OC, OD, OE, OF, OH, OI, OO, OP, OS and OW.
         - Digitizing instructions DP and DC.
         - The Input Mask Instruction IM.
         - The Page Size Instruction PS - in the SPLOT paper size
               may be changed only via program control panel.



        ----------------------------------
        HP 7440A ColorPro Graphics Plotter
        ----------------------------------
        Including HP 17440 Graphics Enhancement Cartridge

        Syntax: HP-GL

        Number of pens: 8

        Paper formats: ISO A4 (210 x 297 mm)
                       ANSI A (8.5 x 11 in.)

        Plotter unit: 0.025 mm

        Maximal number of digits in decimal fraction to be read: 4

        Number of character sets:
         5 without HP 17440 (0-4)
         19 with   HP 17440 (0-4,6-9,30-39)
         (all supported by SPLOT)

        Alphabetical list of plotter instructions supported by
        the HP7440A ColorPro version of SPLOT:

         AA  - The Arc Absolute Instruction (HP 17440)
         AR  - The Arc Relative Instruction (HP 17440)
         CA  - The Designate Alternate Character Set Instruction
         CI  - The Circle Instruction (HP 17440)
         CP  - The Character Plot Instruction
         CS  - The Designate Standard Character Set Instruction
         DF  - The Default Instruction
         DI  - The Absolute Direction Instruction
         DR  - The Relative Direction Instruction
         DT  - The Define Terminator Instruction
         EA  - The Edge Rectangle Absolute Instruction (HP 17440)
         EP  - The Edge Polygon Instruction (HP 17440)
         ER  - The Edge Rectangle Relative Instruction (HP 17440)
         EW  - The Edge Wedge Instruction (HP 17440)
         FP  - The Fill Polygon Instruction (HP 17440)
         FT  - The Fill Type Instruction (HP 17440)
         IN  - The Initialize Instruction
         IP  - The Input P1 and P2 Instruction
         IW  - The Input Window Instruction
         LB  - The Label Instruction
         LT  - The Line Type Instruction
         PA  - The Plot Absolute Instruction
         PD  - The Pen Down Instruction
         PM  - The Polygon Mode Instruction (HP 17440)
         PR  - The Plot Relative Instruction
         PT  - The Pen Thickness Instruction (HP 17440)
         PU  - The Pen Up Instruction
         RA  - The Shade Rectangle Absolute Instruction (HP 17440)
         RO  - The Rotate Coordinate Instruction
         RR  - The Shade Rectangle Relative Instruction (HP 17440)
         SA  - The Select Alternate Character Set Instruction
         SC  - The Scale Instruction
         SI  - The Absolute Character Size Instruction
         SL  - The Character Slant Instruction
         SM  - The Symbol Mode Instruction
         SP  - The Select Pen Instruction
         SR  - The Relative Character Size Instruction
         SS  - The Select Standard Character Set Instruction
         TL  - The Tick Length Instruction
         UC  - The User Defined Character Instruction
         VS  - The Velocity Select Instruction (for information only)
         WG  - The Shade Wedge Instruction (HP 17440)
         XT  - The X-Tick Instruction
         YT  - The Y-Tick Instruction

        The following instructions are  NOT supported by the  HP7440A
        ColorPro version of SPLOT  (they are checked for  syntax only
        and no action is performed):

         - All escape code sequences.
         - All output instructions:
            OA, OC, OD, OE, OF, OH, OI, OO, OP, OS and OW.
         - Digitizing instructions DP and DC.
         - The Input Mask Instruction IM.



        -------------------------
        HP 7550A Graphics Plotter
        -------------------------

        Syntax: HP-GL

        Number of pens: 8

        Paper formats: ISO A4 (210 x 297 mm)
                       ISO A3 (297 x 420 mm)
                       ANSI A (8.5 x 11 in.)
                       ANSI B (11  x 17 in.)

        Plotter unit: 0.025 mm

        Maximal number of digits in decimal fraction to be read: 8

        Number of character sets: 40 (0-9,30-39,10-19,40-49)
                                  (20 supported by SPLOT (0-9,30-39))

        Alphabetical list of plotter instructions supported by
        the HP7550A version of SPLOT:

         AA  - The Arc Absolute Instruction
         AR  - The Arc Relative Instruction
         CA  - The Designate Alternate Character Set Instruction
         CI  - The Circle Instruction
         CP  - The Character Plot Instruction
         CS  - The Designate Standard Character Set Instruction
         CT  - The Chord Tolerance Instruction
         DF  - The Default Instruction
         DI  - The Absolute Direction Instruction
         DR  - The Relative Direction Instruction
         DT  - The Define Terminator Instruction
         EA  - The Edge Rectangle Absolute Instruction
         EP  - The Edge Polygon Instruction
         ER  - The Edge Rectangle Relative Instruction
         ES  - The Extra Space Instruction
         EW  - The Edge Wedge Instruction
         FP  - The Fill Polygon Instruction
         FT  - The Fill Type Instruction
         IN  - The Initialize Instruction
         IP  - The Input P1 and P2 Instruction
         IW  - The Input Window Instruction
         LB  - The Label Instruction
         LO  - The Label Origin Instruction
         LT  - The Line Type Instruction
         PA  - The Plot Absolute Instruction
         PD  - The Pen Down Instruction
         PM  - The Polygon Mode Instruction
         PR  - The Plot Relative Instruction
         PT  - The Pen Thickness Instruction
         PU  - The Pen Up Instruction
         RA  - The Shade Rectangle Absolute Instruction
         RO  - The Rotate Coordinate Instruction
         RR  - The Shade Rectangle Relative Instruction
         SA  - The Select Alternate Character Set Instruction
         SC  - The Scale Instruction
         SI  - The Absolute Character Size Instruction
         SL  - The Character Slant Instruction
         SM  - The Symbol Mode Instruction
         SP  - The Select Pen Instruction
         SR  - The Relative Character Size Instruction
         SS  - The Select Standard Character Set Instruction
         TL  - The Tick Length Instruction
         UC  - The User Defined Character Instruction
         VS  - The Velocity Select Instruction (for information only)
         WG  - The Shade Wedge Instruction
         XT  - The X-Tick Instruction
         YT  - The Y-Tick Instruction

        The following instructions are  NOT supported by the  HP7550A
        version of  SPLOT (they  are checked  for syntax  only and no
        action is performed):

         - All escape code sequences.
         - All output instructions:
            OA, OC, OD, OE, OF, OG, OH, OI, OK, OL, OO, OP, OS, OT
            and OW.
         - Digitizing instructions DP and DC.
         - The Input Mask Instruction IM.
         - And this:
           AF or AH - The Advance Page Instruction *
           AP  - The Automatic Pen Operations Instruction
           AS  - The Acceleration Select Instruction
           BF  - The Buffer Plot Instruction
           BL  - The Buffer Label Instruction *
           CC  - The Character Chord Angle Instruction *
           CM  - The Character Selection Mode Instruction *
           CV  - The Curved Line Generator Instruction
           DL  - The Define Downloadable Character Instruction *
           DS  - The Designate Character Set into Slot Instruction *
           FS  - The Force Select Instruction
           GC  - The Group Count Instruction
           GM  - The Graphics Memory Instruction *
           GP  - The Group Pen Instruction *
           IV  - The Invoke Character Slot Instruction *
           KY  - The Define Key Instruction
           NR  - The Not-Ready Instruction
           PB  - The Print Buffered Label Instruction *
           PG  - The Page Feed Instruction *
           RP  - The Replot Instruction
           SG  - The Select Pen Group Instruction *
           UF  - The User-Defined Fill Type Instruction *
           WD  - The Write to Display Instruction

                 * - may be supported in next versions



        ----------------------------
        HP DraftPro Graphics Plotter
        ----------------------------
        HP 7570A DraftPro
        HP 7575A DraftPro DXL
        HP 7576A DraftPro EXL

        Syntax: HP-GL

        Number of pens: 8

        Paper formats: ISO A4 (DXL/EXL only)
                       ISO A3 (DXL/EXL only)
                       ISO A2
                       ISO A1
                       ISO A0 (EXL only)
                       ANSI A (DXL/EXL only)
                       ANSI B (DXL/EXL only)
                       ANSI C
                       ANSI D
                       ANSI E (EXL only)
                       ARCH A (DXL/EXL only)
                       ARCH B (DXL/EXL only)
                       ARCH C
                       ARCH D
                       ARCH E (EXL only)
                       Supports EXPAND mode for each format.

        Note - origin of plotter coordinates is situated to the
               center of the plotting area (paper).

        Plotter unit: 0.025 mm

        Maximal number of digits in decimal fraction to be read: 4

        Number of character sets: 21 (0-9,30-39,99)
                                  (all supported by SPLOT)

        Alphabetical list of plotter instructions supported by
        the HP DraftPro version of SPLOT:

         AA  - The Arc Absolute Instruction
         AR  - The Arc Relative Instruction
         CA  - The Designate Alternate Character Set Instruction
         CI  - The Circle Instruction
         CP  - The Character Plot Instruction
         CS  - The Designate Standard Character Set Instruction
         CT  - The Chord Tolerance Instruction
         DF  - The Default Instruction
         DI  - The Absolute Direction Instruction
         DR  - The Relative Direction Instruction
         DT  - The Define Terminator Instruction
         DV  - The Direction Vertical Instruction
         EA  - The Edge Rectangle Absolute Instruction
         EP  - The Edge Polygon Instruction
         ER  - The Edge Rectangle Relative Instruction
         ES  - The Extra Space Instruction
         EW  - The Edge Wedge Instruction
         FP  - The Fill Polygon Instruction
         FT  - The Fill Type Instruction
         IN  - The Initialize Instruction
         IP  - The Input P1 and P2 Instruction
         IW  - The Input Window Instruction
         LB  - The Label Instruction
         LO  - The Label Origin Instruction
         LT  - The Line Type Instruction
         PA  - The Plot Absolute Instruction
         PD  - The Pen Down Instruction
         PM  - The Polygon Mode Instruction
         PR  - The Plot Relative Instruction
         PT  - The Pen Thickness Instruction
         PU  - The Pen Up Instruction
         RA  - The Shade Rectangle Absolute Instruction
         RO  - The Rotate Coordinate Instruction
         RR  - The Shade Rectangle Relative Instruction
         SA  - The Select Alternate Character Set Instruction
         SC  - The Scale Instruction
         SG  - The Select Pen Group Instruction
         SI  - The Absolute Character Size Instruction
         SL  - The Character Slant Instruction
         SM  - The Symbol Mode Instruction
         SP  - The Select Pen Instruction
         SR  - The Relative Character Size Instruction
         SS  - The Select Standard Character Set Instruction
         TL  - The Tick Length Instruction
         UC  - The User Defined Character Instruction
         VS  - The Velocity Select Instruction (for information only)
         WG  - The Shade Wedge Instruction
         XT  - The X-Tick Instruction
         YT  - The Y-Tick Instruction

        The  following  instructions  are  NOT  supported  by  the HP
        DraftPro version of SPLOT  (they are checked for  syntax only
        and no action is performed):

         - All escape code sequences.
         - All output instructions:
            OA, OC, OD, OE, OF, OH, OI, OO, OP, OS and OW.
         - Digitizing instructions DP and DC.
         - The Input Mask Instruction IM.
         - And this:
           AP  - The Automatic Pen Operations Instruction
           CM  - The Character Selection Mode Instruction *
           DS  - The Designate Character Set into Slot Instruction *
           GM  - The Graphics Memory Instruction *
           IV  - The Invoke Character Slot Instruction *
           NR  - The Not-Ready Instruction
           PE  - The Encoded Polyline Instruction *

                 * - may be supported in next versions



        -------------------------------
        HP DraftMaster Graphics Plotter
        -------------------------------
        HP 7595A DraftMaster I
        HP 7596A DraftMaster II

        Syntax: HP-GL

        Number of pens: 8

        Paper formats: ISO A4,A3,A2,A1,A0
                       ANSI A,B,C,D,E
                       ARCH A,B,C,D,E
                       Supports EXPAND mode for each format.

        Note - origin of plotter coordinates is situated to the
               center of the plotting area (paper).

        Plotter unit: 0.025 mm

        Maximal number of digits in decimal fraction to be read: 8

        Number of character sets: 64 (0-9,30-39,99,10-19,40-49,
                                      20-29,50-59,60,70,80)
                                 (21 supported by SPLOT (0-9,30-39,99))

        Alphabetical list of plotter instructions supported by
        the HP DraftMaster version of SPLOT:

         AA  - The Arc Absolute Instruction
         AR  - The Arc Relative Instruction
         BF  - The Buffer Plot Instruction (NOP)
         CA  - The Designate Alternate Character Set Instruction
         CI  - The Circle Instruction
         CP  - The Character Plot Instruction
         CS  - The Designate Standard Character Set Instruction
         CT  - The Chord Tolerance Instruction
         DF  - The Default Instruction
         DI  - The Absolute Direction Instruction
         DR  - The Relative Direction Instruction
         DT  - The Define Terminator Instruction
         DV  - The Direction Vertical Instruction
         EA  - The Edge Rectangle Absolute Instruction
         EP  - The Edge Polygon Instruction
         ER  - The Edge Rectangle Relative Instruction
         ES  - The Extra Space Instruction
         EW  - The Edge Wedge Instruction
         FP  - The Fill Polygon Instruction
         FT  - The Fill Type Instruction
         IN  - The Initialize Instruction
         IP  - The Input P1 and P2 Instruction
         IW  - The Input Window Instruction
         LB  - The Label Instruction
         LO  - The Label Origin Instruction
         LT  - The Line Type Instruction
         PA  - The Plot Absolute Instruction
         PD  - The Pen Down Instruction
         PM  - The Polygon Mode Instruction
         PR  - The Plot Relative Instruction
         PT  - The Pen Thickness Instruction
         PU  - The Pen Up Instruction
         RA  - The Shade Rectangle Absolute Instruction
         RO  - The Rotate Coordinate Instruction
         RR  - The Shade Rectangle Relative Instruction
         SA  - The Select Alternate Character Set Instruction
         SC  - The Scale Instruction
         SI  - The Absolute Character Size Instruction
         SL  - The Character Slant Instruction
         SM  - The Symbol Mode Instruction
         SP  - The Select Pen Instruction
         SR  - The Relative Character Size Instruction
         SS  - The Select Standard Character Set Instruction
         TL  - The Tick Length Instruction
         UC  - The User Defined Character Instruction
         VA  - The Adaptive Velocity Instruction (NOP)
         VN  - The Normal Velocity Instruction (NOP)
         VS  - The Velocity Select Instruction (for information only)
         WG  - The Shade Wedge Instruction
         XT  - The X-Tick Instruction
         YT  - The Y-Tick Instruction

        The  following  instructions  are  NOT  supported  by  the HP
        DraftMaster version  of SPLOT  (they are  checked for  syntax
        only and no action is performed):

         - All escape code sequences.
         - All output instructions:
            OA, OC, OD, OE, OF, OG, OH, OI, OK, OL, OO, OP, OS, OT
            and OW.
         - Digitizing instructions DP and DC.
         - The Input Mask Instruction IM.
         - The Page Size Instruction PS - in the SPLOT paper size
               may be changed only via program control panel.
         - And this:
           AF or AH - The Advance Page Instruction *
           AP  - The Automatic Pen Operations Instruction
           AS  - The Acceleration Select Instruction
           BL  - The Buffer Label Instruction *
           CC  - The Character Chord Angle Instruction *
           CM  - The Character Selection Mode Instruction *
           CV  - The Curved Line Generator Instruction
           DL  - The Define Downloadable Character Instruction *
           DS  - The Designate Character Set into Slot Instruction *
           EC  - The Enable Cut Line Instruction
           FR  - The Frame Advance Instruction
           FS  - The Force Select Instruction
           GC  - The Group Count Instruction
           GM  - The Graphics Memory Instruction *
           GP  - The Group Pen Instruction *
           IV  - The Invoke Character Slot Instruction *
           KY  - The Define Key Instruction
           NR  - The Not-Ready Instruction
           PB  - The Print Buffered Label Instruction *
           PG  - The Page Feed Instruction *
           SG  - The Select Pen Group Instruction *
           UF  - The User-Defined Fill Type Instruction *
           WD  - The Write to Display Instruction

                 * - may be supported in next versions



        -------------------------
        ROLAND DXY 1100/1200/1300
        -------------------------

        Syntax: RD-GL I (corresponds with the HP-GL syntax)
                DXY-GL

        Number of pens: 8

        Paper formats: ISO A4 (210 x 297 mm)
                       ISO A3 (297 x 420 mm)
                       ANSI A (8.5 x 11 in.)
                       ANSI B (11  x 17 in.)
                       Supports EXPAND mode for each format.

        Plotter unit: 0.025 mm in RD-GL mode
                      0.1 or 0.025 mm in DXY-GL mode

        Maximal number of digits in decimal fraction to be read: 4

        Number of character sets: 19 (0-4,6-9,30-39)
                                  (all supported by SPLOT)

        Alphabetical list of plotter instructions supported by
        the ROLAND version of SPLOT in RD-GL mode:

         AA  - The Arc Absolute Instruction
         AR  - The Arc Relative Instruction
         CA  - The Designate Alternate Character Set Instruction
         CI  - The Circle Instruction
         CP  - The Character Plot Instruction
         CS  - The Designate Standard Character Set Instruction
         DF  - The Default Instruction
         DI  - The Absolute Direction Instruction
         DR  - The Relative Direction Instruction
         DT  - The Define Terminator Instruction
         EA  - The Edge Rectangle Absolute Instruction
         ER  - The Edge Rectangle Relative Instruction
         EW  - The Edge Wedge Instruction
         FT  - The Fill Type Instruction (Note, that for ROLAND
               plotter fill angle may be specified in 45 degree
               increments only.)
         IN  - The Initialize Instruction
         IP  - The Input P1 and P2 Instruction
         IW  - The Input Window Instruction
         LB  - The Label Instruction
         LT  - The Line Type Instruction
         PA  - The Plot Absolute Instruction
         PD  - The Pen Down Instruction
         PR  - The Plot Relative Instruction
         PT  - The Pen Thickness Instruction
         PU  - The Pen Up Instruction
         RA  - The Shade Rectangle Absolute Instruction
         RO  - The Rotate Coordinate Instruction
         RR  - The Shade Rectangle Relative Instruction
         SA  - The Select Alternate Character Set Instruction
         SC  - The Scale Instruction
         SI  - The Absolute Character Size Instruction
         SL  - The Character Slant Instruction
         SM  - The Symbol Mode Instruction
         SP  - The Select Pen Instruction
         SR  - The Relative Character Size Instruction
         SS  - The Select Standard Character Set Instruction
         TL  - The Tick Length Instruction
         UC  - The User Defined Character Instruction
         VS  - The Velocity Select Instruction (for information only)
         WG  - The Shade Wedge Instruction
         XT  - The X-Tick Instruction
         YT  - The Y-Tick Instruction

        The following  instructions are  NOT supported  by the ROLAND
        version of SPLOT in RD-GL  mode (they are checked for  syntax
        only and no action is performed):

         - All escape code sequences.
         - All output instructions:
            OA, OC, OD, OE, OF, OH, OI, OO, OP, OS and OW.
         - Digitizing instructions DP and DC.
         - The Input Mask Instruction IM.
         - The Page Size Instruction PS - in the SPLOT paper size
               may be changed only via program control panel.

        Alphabetical list of plotter instructions supported by
        the ROLAND version of SPLOT in DXY-GL mode:

         A  - The Circle Center Instruction
         B  - The Line Scale Instruction
         C  - The Circle Instruction
         D  - The Draw Instruction
         E  - The Relative Circle Instruction
         G  - The A + Circle Instruction
         H  - The Home Instruction
         I  - The Relative Draw Instruction
         J  - The Pen Change Instruction
         K  - The A + % Instruction
         L  - The Line Type Instruction
         M  - The Move Instruction
         N  - The Mark Instruction
         P  - The Print Instruction
         Q  - The Alpha Rotate Instruction
         R  - The Relative Move Instruction
         S  - The Alpha Scale Instruction
         T  - The Hatching Instruction
         X  - The Axis Instruction
         ^  - The Up Instruction

        The following  instructions are  NOT supported  by the ROLAND
        version of SPLOT in DXY-GL mode (they are checked for  syntax
        only and no action is performed):

         Y  - The Curve Instruction *
         _  - The Relative Curve Instruction *

              * - may be supported in next versions


        End of list.