Electrical and Electronic Formulas version 2.02
Copyright (C) 1990 - 1992 Miller

Introduction:

      This program contains a collection of basic electrical and electronic
      formulas, which can be found in any electrical engineering handbook.
      The software was developed, in an effort, to alleviate the necessity
      of looking up individual formulas each time they are needed. This
      software includes the most commonly used electrical formulas.

      The software was complied to include the use of a math coprocessor,
      if one is present. The coprocessor will be emulated if one is not
      found in your system.

Differences:

      This release contains all the features of version 1.00, plus a new 
      on-screen calculator. Some additional minor maintenance changes
      were also put into effect in this version.
 
File Index:

      EEF    .EXE : 76816 Bytes, Electrical and Electronic Formula program
      EEF    .DOC : 13373 Bytes, file containing general program information
      EEFELEC.DBF : 21280 Bytes, file containing the world wide voltage chart
      EEFHELP.DBF : 12880 Bytes, file containing general help information

System Requirements:

      The program minimum requirements are as follows...
      
      Any XT compatible computer
      DOS version 3.0 or later
      256K memory
      A color monitor
      A floppy or hard disk drive
      
Installation:

      The program, including support files, is compact enough that it will
      run satisfactorily on a floppy disk. If a hard disk is available it
      should be used, this will allow faster access to the data files as
      they are needed. Type each of the following lines into the computer,
      at the DOS prompt, to install on a hard disk system.

      MD FORMULA                  <ENTER>    Make a directory
        
      COPY A:EEF*.* C:\FORMULA /V <ENTER>    Copy files to new directory

      CD\FORMULA                  <ENTER>    Change to new directory

      EEF                         <ENTER>    Execute the program

      A batch file can be created to allow easier loading of the program.
      This file should be located in the root directory of the hard drive.
      Type each of the following lines into the computer, at the DOS
      prompt, to create a batch file.
        
      COPY CON C:\EEF.BAT <ENTER>

      CD\FORMULA          <ENTER>

      EEF.EXE %1 %2 %3    <ENTER>

      ^Z                  <ENTER>

      To execute the program, change to the root or formula directory, and
      type EEF, followed by any of the command options available. 
      If the DOS path is set to include the root and formula directories,
      changing to a particular directory will become unnecessary. Refer to
      your DOS manual for instructions on using the path command.

Command Line Options:

      When loading the program, you have several options available. By
      including /Fxx and /Bxx, on the command line, the colors you want to
      use will be set automatically. If you include /NB the sounds,
      generated when an error is made, will be suppressed. The color codes
      can be copied from the color select screen, they are displayed in the
      box marked "Current Choice". The /FXX option sets the foreground
      color, while /Bxx sets the background color. Following are several
      examples  of valid command line entries...

      EEF/F11           Set foreground light blue                                     
                                                                                
      EEF/F11/B01       Set foreground light blue / background blue                   
                                                                                
      EEF/F11/B01/NB    Set foreground light blue / background blue
                                       / suppress sound  

GENERAL INFORMATION:                                                            
                                                                                
      Select the proper subject from the main menu. Once the new menu is
      displayed you will have to select an appropriate topic. The computer
      will then display this screen. The first few lines, starting at the
      top of the monitor will give a brief description of the area you have
      accessed. If a prompt will require more than a one character
      response, then a window will be displayed. The window has a wrap
      feature, which works as follows; as the window becomes filled,
      characters on the left will be dropped, as new characters are added
      on the right side of the window. The BACKSPACE key can be used to
      eliminate characters, from the right side of the window, one at a
      time. When you are sure that you have entered the data properly,
      press the ENTER key, this will allow the computer to read and store 
      the data. When all the necessary data has been entered the computer
      will solve for the unknown value, or perform a conversion, and
      display the result. The escape (ESC) key is always enabled, and can
      be used in any area, to exit and return to the most recent menu. Use
      this method to exit the program, and return to DOS, from the main
      menu.                                          
                                                                              
ELECTRONIC:                                                                     
                                                                                
      This section of the program will calculate various electronic related  
      formulas as listed below...                                                     
                                                                                
             Ohms law (DC)                 Coupled inductance                 
             Ohms law (AC)                 Impedance                          
             Resistance total              Resonance                          
             Capacitance total             Admittance                         
             Inductance total              Susceptance                        
             Mutual inductance             Conductance                        

      Most sections will calculate several different derivatives of a
      formula, for instance, the resonance area has the capability of
      solving not only for resonance, but also capacitance, or inductance
      in a resonant circuit. In the areas where this is possible, you will
      be given several choices then, by user selection, the formula for the
      specified quantity will be performed. The formula used to arrive at
      the result is displayed on the screen at the end of any calculation.
      The standard print screen function can be used to obtain a hard copy,
      the screen is also time and date stamped, as a further aid to the
      user.
                                                                       
ELECTRICAL:                                                                     
                                                                                
      This section of the program will calculate various electrical related  
      formulas as listed below...
                                                     
             Efficiency                    Required fuse, wire size           
             Power factor                  Wire resistance                    
             Amperes from horsepower       Voltage drop                       
             Amperes from kilowatts        Conduit fill                       
             Amperes from kva              Kvar sizing                        
             Kilowatts and KVA             Supply systems                     
                                                                                
      The left column represents formulas that can be used for calculating   
      both single and three phase circuits. The other formulas are not
      phase dependant and can be used for any circuit configuration.
      Efficiency and Power Factor are calculated and displayed on the    
      screen as a percent. Also, when entering data at an Efficiency or
      Power Factor prompt, the data must be input as a percent. The supply
      system area calculates the current draw, by a load, on any
      conventional power system. This is convenient for 60hz to 50hz
      conversions. The formula used to arrive at the result is displayed on
      the screen at the end of most calculations. The standard print screen
      function can be used to obtain a hard copy, the screen is time
      stamped, as a further aid to the user.
  
NUMBER SYSTEMS:                                                                 
                                                                                
      This section of the program will evaluate, and change a quantity in
      one number system to an equivalent value in another system. The
      number systems used in this section are as follows...

                             Decimal (base 10)                                
                             Hex     (base 16)                                
                             Octal   (base 08)                                
                             Binary  (base 02)                                
                                                                               
      The current lower and upper conversion limit is:

                             Decimal:+/-1048575
                             Binary :1111 1111 1111 1111 1111
                             Octal  :3777777
                             Hex    :FFFFF

      If a value outside these limits is entered, or calculated, an error
      message will be displayed indicting an overflow has occurred.
                                                                        
WORLD WIDE VOLTAGE DATABASE:                                                    
                                                                                
      This section of the program provides a current list of the worlds      
      electric power supplied to consumers. The list covers a wide range of
      countries, and includes frequency, system (wye/delta), single phase
      voltage, and three phase voltage, when available. All voltages listed
      are alternating current (AC). A wye or star system will have a high
      voltage that is 1.732 times the low voltage, for example 120/208. A
      delta system will have a high voltage that is 2 times the low
      voltage. If a single voltage is listed under the single phase
      column, then it can be assumed that the consumer has only the one
      voltage available, and that it is a two wire service, (one phase wire
      and one neutral). Two voltages listed under the same column would
      indicate that the consumer has a three wire service, and both are
      available, (two phase wires and one neutral). A three phase service,
      when available, will normally be furnished with four wires, (three
      phase wires and one neutral). The higher voltage listed can be either
      single or three phase, but the lower voltage will always be single
      phase.

Calculator:

      An on-screen calculator is available most everywhere, while the
      program is running. To access this feature just press the F(1) key.
      A short list of special functions will be displayed, along with the
      calculator itself. The capabilities include the normal four basic
      functions, plus squaring, square root, reciprocal, and exponential 
      math. The current result in the display can also be exported back to
      the main program.

Disclaimer:

      The author accepts no responsibility for the application of this
      software, the result obtained, any errors or omissions contained
      herein. This material is subject to change without notice.

Comments:

      The author welcomes comments good or bad, input from users is very
      important to future releases of this software. Please feel free to
      contact me on Compuserve (73407,546), or at the address below.

Registration:
        
      This program is copyrighted, and is offered as shareware software. If
      you find this software useful, and plan to retain and use it, then
      please register the program, by doing so you will be assured of being
      informed of any updates. Please send the form below, along with 
      $20.00, to the address shown.
 
      Name:___________________________________________________________

      Address:________________________________________________________

      City, State:____________________________________________________

      Zip Code:_______________________________________________________

      Country:________________________________________________________

      Version You Are Using:__________________________________________

      Gregory J. Miller
      2303 Bennington Place
      Maryland Heights, Mo. 63043