PCTRACE

                                     Version 5.0

                                     Users Manual

                                    June 21, 1992











                                          by







                                  Douglas E. Ehlers
                             Ehlers Technical Consultants
                                   4520 S. 58th St.
                                 Lincoln, NE   68516
                           (402) 435-8440  Voice (evenings)
                     (701) 642-3846 BBS 9600,N,8,1 V.32, V.42bis








                                                                          2

                                  Table of Contents

          Notice of Copyright............................................3
          Introduction...................................................4
          Installation...................................................4
          System Requirements............................................5
          Software Setup.................................................5
          Old file Upgrades..............................................6
          User support Methods...........................................6
               Voice.....................................................6
               BBS.......................................................7
          Input/Output Menu..............................................8
          Board Definition Menu..........................................9
               Chip Placement...........................................10
          Interactive Router............................................14
               Mouse use................................................18
          Autorouter....................................................18
          Board Statistics..............................................19
          Printer Menu..................................................21
          Export Menu...................................................21
          Exiting the program...........................................22
          Tutorial......................................................24
          RPRINT Subprogram.............................................26
          DEFGEN Subprogram.............................................28
          PC-Trace Keyboard control summaries...........................32
          Schematic CAD.................................................33
               Drawing Symbols..........................................36
               Entering Components/Symbols..............................40
               Making Connections.......................................43
               Additional Drawing Commands..............................44
               SCAD active keys.........................................49
          Conclusions...................................................50
          Appendix A - .NLT file format.................................51

















                                                          PC-Trace Users Manual








                                                                          3

                                 Notice of Copyright



               This program is protected by a copyright held by the author

          and filed with the United States Government.  Copying of this

          software is forbidden and a criminal offense.  Anyone caught

          distributing this software without the author's consent will be

          prosecuted to the fullest extent of the law.



          Note:     This program was originally marketed under the name

                    PCROUTE but for copyright reasons has been renamed to

                    PCTRACE.  SCAD is short for Schematic CAD and is a

                    schematic capture program that is part of the PCTRACE

                    system.

























                                                          PC-Trace Users Manual








                                                                          4

                                     Introduction

               PCTRACE is a computer aided design program for printed
          circuit boards.  It contains programs that can take the designer
          from a schematic, to a board layout, to computer control of the
          machines needed to make high quality circuit boards.  The program
          should be quite adequate for most purposes.  This program is not
          meant for IBM's use to design the next PS/2 motherboard.  It is
          intended for the late-night engineer to build home projects.  It
          contains a full featured autorouter that averages a 93%
          completion rate on low density boards and 70% on higher density
          boards.  It also supports  most popular printers for its output.
               PCTRACE is the general name given to all the programs that
          make up this system.  For example, PCTRACE includes SCAD, RPRINT,
          and PCTRACE itself.
          Key features include:
                1.  Autorouting
                2.  Graphic interactive routing
                3.  Board layout functions
                4.  Flexible pinouts for devices
                5.  2X and 1X output for use in making PC boards
                6.  Disk functions built into the software
                7.  Sophisticated component and connection entry systems
                8.  General statistics
                9.  Up to 300 components and 1800 connections
               10.  Mouse support in the interactive router
               11.  Variable pad and trace sizes
               12.  Single and double sided boards
               13.  Manual placement of traces
               14.  CGA, EGA, and VGA graphics support to display the
                    board. CGA:80x25 EGA:80x43 VGA:80x60
               15.  Gerber, DXF, and Autocad Script file output
               16.  Actual size silkscreen creation
               17.  Error handling for critical errors
               18.  Schematic Capture for a complete cad system.
               19.  The authors continued support



                                     Installation

          Contents of PC-Trace directory:
          PCTRACE   .EXE - The board layout/main program
          SCAD      .EXE - Schematic CAD
          RPRINT    .EXE - The PC-Trace printer output program
          SPRINT    .EXE - The SCAD printer output program
          CONVCDT   .EXE - Converts 4.0 and older files to 5.0
          CONVDEF   .EXE - Converts 4.0 and older files to 5.0


                                                          PC-Trace Users Manual








                                                                          5


          *         .DEF - PC-Trace part layout files
          *         .DIA - SCAD symbols



          System Requirements:
          To run this program requires:
               1. CGA, EGA, or VGA graphics
               2. 640k of memory with 520k free
               3. 1 floppy disk drive
               4. Hard Disk Drive or Large capacity floppy
               5. One of the following printers:
                    a. IBM PC or compatible printer
                    b. EPSON LQ-2500 or compatible printer
                    c. HP Laserjet II or compatible
                    d. Adobe Postscript Compatible printer
                    e. HP Deskjet or Deskjet +
                    f. Epson MX-80 or compatible
                    g. IBM Proprinter 24pin must be in AGM mode
                    h. HP and Roland Plotters
               6. Mouse is required for SCAD and usable in PC-Trace
          A fast processor and math coprocessor are also beneficial.

          Software Setup:

               For PCTRACE to run reliably, a line must appear in the
          config.sys files that says FILES=20.  If any other major
          commercial software applications are in use this command probably
          exists, but it should be checked.
               To install the software insert disk 1 in either drive A: or
          B:.  Change to the drive that the floppy disk is in.  To do this
          type A: or B: from the dos prompt.  To start the installation
          process, type INSTALL from the DOS prompt.  The installation
          program will run and prompt for the drive that the install disk
          is in.  Enter the letter and verify that it is correct.  The next
          prompt is for the destination drive.  This should be the letter
          of a hard-disk or alternate floppy disk that has at least 1mb of
          free space.  Verify that the destination of the program is
          correct.  The installation program will notify the user that it
          is ready to start the installation process and that Disk 1 should
          be placed in the disk drive.  This should already be the case. 
          Press SPACE to begin.  After a few moments, a prompt will appear
          for the user to insert disk 2.  If PCTRACE was shipped on a
          single floppy (3.5 inch) disk 2 is the same as disk 1.  If the
          program came on two floppies (5.25 inch) insert the second disk. 
          Press space to finish the installation.
               To execute the programs the user must change into the
          PCTRACE5 directory using the command CD \PCTRACE5.  The programs

                                                          PC-Trace Users Manual








                                                                          6

          will not run properly if run from some other directory than
          PCTRACE.  To run the programs type PCTRACE, SCAD, or RPRINT from
          the DOS prompt.  Install will also create two subdirectories
          called DEFILES and DIAGRAMS to store the definition files for
          PCTRACE and symbol files for SCAD.
               Two programs are included to help with the update process. 
          CONVDEF.EXE is used to modify the old .DEF files that the user
          might already have created.  To use this program, copy it into
          the subdirectory that holds the old .DEF files.  Type CONVDEF,
          the program will run and update the file format of all the old
          files.  CONVDEF can now be deleted from the hard-disk anywhere
          that it appears.
               The second program is used to update the .CDT files.  This
          program requires that the .CDT file be in the same directory as
          CONVCDT.EXE.  To convert the file, type:

               CONVCDT file1.CDT file2.CDT file3.CDT.

               The program will update the file from the 3.0 and 4.0 format
          to the 5.0 format.  The old file will be saved in a .BAK file.
               One major consideration when moving a 4.0 file to the 5.0
          system is the advanced silkscreening.  The parts are referenced
          to a most upper left corner for placement, this includes
          silkscreen parts.  If a part exists on an old board and is
          converted to the 5.0 program, that part should be left unchanged
          as far as silkscreen.  If the silkscreen is drawn around that
          part, it will offset the location of the pads and the existing
          traces will not meet the pads in the correct place.  This will be
          immediately visible as the affected parts will appear to have too
          many pads.  If the user desires the silkscreen on the old board
          with the 5.0 software, they should be prepared to move components
          around in the interactive router to get the pads in the popper
          places.  Traces that were overwritten by the incorrectly placed
          pad may have to be repaired as well.


                                 User Support Methods
          Phone Calls:
                    All registered users are free to call anytime to notify
               the author of bugs, perceived bugs, program usage questions,
               suggestions of additions, and anything else that the end
               user feels the need to discuss with the author.  The BBS is
               also a good way to receive support for the registered user.
                    Un-registered users are also welcome to call during the
               evening when having problems getting the demonstration
               version of PCTRACE running.  The support will be more
               limited.  A better, and preferred method by the author, is
               for these users to use the BBS.


                                                          PC-Trace Users Manual








                                                                          7

          BBS Support:
                    Perhaps the best reason to register the demo version is
               to get the support of the registered user section on the
               BBS.  The complete PCTRACE system is posted in this area for
               downloading.  Upon registration all users receive a password
               on this system that allows them to download the most current
               bug fixes any time they like.  The user name and password
               appear on the first page of the manual.  Part and symbol
               libraries will also be posted and hopefully uploaded by
               users of the system.  Other programs deemed useful by the
               author will be posted for all users as well as the demo
               version of the software.
                    To access the BBS, call the number listed on the
               opening screen of the software with a modem control package
               such as PROCOMM or QMODEM.  
                    Support is provided courtesy of the author.  Please
               feel free to log in to the BBS anytime.  Voice calls should
               be at a decent hour and evenings are best.  Please exhaust
               all possibilities before making the call and be sure to try
               and understand the problem before making the call to better
               explain it to the author.  If it is possible, please try and
               isolate the problem to the point that it can be repeated by
               executing a certain sequence of events.  By doing this, it
               becomes much easier to find and fix the errors in
               programming.

























                                                          PC-Trace Users Manual








                                                                          8

                                   PC-Trace Manual

                                  Input/Output Menu
          1. Load Data:
                    This function is used to retrieve from a disk necessary
               information to design a printed  circuit board.  Select this
               function  from the menu  and when  prompted, enter  the file
               name.  No extension  is used, the program will add  the .CDT
               extension.   The  path should  not be  used on  the filename
               itself.  There is a function that will be discussed later to
               set  the  path name.    After entering  the  filename, press
               Return.   The program will ask if  this is the correct name,
               enter Y  or  N to  answer.   If the  file is  not found  the
               program will reprompt for file name.  The ESC key is used to
               jump  back to  the main  menu instead  of entering  the file
               name.

          2. Save Data:
                    This function  will save a complete  description of the
               design layout,  component list,  and connection list.   When
               prompted, enter the filename.  Again do not specify the file
               extension  or path name.   PCTRACE will  ask, after entering
               the  file name, if everything is correct.   If so, enter a Y
               or N.   If  the file exists  the program  will ask if  it is
               alright to overwrite the file.  N will prompt for a new file
               name.  ESC will bypass the prompt back to the I/O menu.

          3. Erase Data:
                    This  routine  clears the  memory of  the program.   It
               erases the boards, component list, and connection list.  The
               program will ask for confirmation before erasing the data in
               memory.   Answer  Y or  N.   The  program will  respond with
               "Erasing..."  and after a few  seconds drop back  to the I/O
               menu.

          4. Import Data:
                    This load  routine works the  same as the  primary load
               command in this menu.  The difference is that it  is made to
               load a netlist  generated by SCAD.  Creation of this file is
               covered in the SCAD manual.  Once this file has been loaded,
               assuming that it is  a complete design, all that  remains is
               to  place the  parts,  make any  minor  design changes,  and
               autoroute the board.  This is a best case scenario and  more
               work is usually required.

          5. Disk Directory:
                    This function displays a listing of the all the circuit
               data files on the current drive and path.  Use the space bar
               to  view twenty file  names at a  time.  When  no more files

                                                          PC-Trace Users Manual








                                                                          9

               exist, the space bar returns to the I/O menu.

          6. Change drive/path:
                    This  function changes the  current path.   The ESC key
               will back  out of  the function  without changing the  path.
               The function  will display  the current  drive and  path and
               then prompt for a new one.  Just enter the new one and press
               Return.

                                Define/Edit Board Menu

          1. Component Edit/Entry:
               This function is  used to enter components into  the system.
          Selecting this function  will place the user in the entry/editing
          environment.    If  no  components have  been  entered  only  two
          possible commands  will  be shown,  if  there are  components  in
          memory  the programs  shows options to  delete, copy  and perform
          other functions. 

          New Component Entry:
               Typing  an  "A" will  allow entry  of  new components.   The
          program  will display the component number being entered and then
          prompt for the  name.  The name  may be up to  15 characters long
          and serves  only to remind  the designer  of what the  device is.
          ESC can  be used at this point to return you to the entry/editing
          environment.
               The  next  question is  for the  designation.   This  is the
          unique name  that is given to  the component and will  be used in
          the  future to refer to it.   Typical names include IC1, R1, IC2,
          and A1.  There are two reserved designations.  The first reserved
          designation starts with "V" and then a number, so V1 would not be
          accepted  but VI1 would be.   The second  reserved designation is
          "GRNDP".  If this is specified  as a source or destination pad in
          the  autorouter,  a  connection  to  the  ground  plane  will  be
          attempted if  one is defined.   ESC may be used to  back up while
          entering the designation name to reenter the component name.
               Third, the program will prompt for the definition file name.
          This is the name of a file that tells the program how the pins on
          the device being entered are situated.  The program first shows a
          list of  possible definition file names  at the lower right.   At
          the end of  the list the program will prompt for  a name.  Do not
          enter a file extension, the program will add it for you.   If the
          name of  the  file entered  exists,  it will  read  the file  and
          display the chip definition to see if it is correct.  If the user
          answers "yes" the program will continue to the next question.  If
          the  user  answers  "no",  the  program  will  reprompt  for  the
          definition  name after displaying the possible files.  ESC may be
          used  to  back up  and reenter  the  component designation.   New
          definition  files can be created with the subprogram DEFGEN.  See

                                                          PC-Trace Users Manual








                                                                         10

          that section of the manual for information on its usage.
               The  fourth prompt asks for the pad  size for the device.  A
          small window will  pop up and prompt for a  pad size between 0.05
          inches  and  0.15 inches.    All pads  are  circular.   Enter the
          corresponding number to the pad size.
               The  next question  the program  will ask  if everything  is
          correct.   Answering  "no" will  restart  this process  with  re-
          prompting  for the  name.   Answering  "yes"  will get  the  next
          prompt.
               The next prompt is to keep this device.  Answering "no" will
          skip the next prompt and ask if you wish to enter another device.
          Answering "yes" displays the next prompt.
               This prompt asks if the user wishes to place the device now.
          Entering  "no" will allow  the delay  of this  until later.   All
          devices must be placed somewhere on the board before they  can be
          connected.  Placing a chip goes as follows:

          Placing Chips:
                    When the  graphic screen  comes up a  representation of
               the current  circuit board with all  other placed components
               and ground planes are shown.  The chip being entered will be
               shown in the upper left corner of the board.  The arrow keys
               will  move this chip around on the  board. By using a shift-
               arrow  combination the chip can  be moved faster.   Move the
               chip to its final place  and press return.  Chips cannot  be
               overlapped.   The chip is now placed  in this location.  ESC
               will  exit  without  placing  the  chip.    Confirmation  of
               abandoning the placement  is asked.  Yes will go to the next
               prompt, no will return to the place before hitting ESC.

               The last prompt is to enter another chip or  not.  Answering
          "yes" will put the user back at the name prompt  to enter another
          chip.    No  will   put  the  user  back  in   the  entry/editing
          environment.

          Editing Component Definitions:
               Selecting  E  from  the  entry/editing   environment  allows
          editing of any part of each definition.  Simply select the letter
          of the item to change.  For example, to  change the name, press A
          after pressing  E and enter the  new name.  Either  enter the new
          name, or press  ESC to leave  it unchanged.   When done  editing,
          press the key that corresponds to exiting the edit.
               If editing the placement of chips, the  chip definition file
          must  be present  in the DEFILES  subdirectory for  the placechip
          function to work.   The  only time this  is a  problem is if  the
          board being edited is not your own, such that the chip definition
          files have different names from your own.



                                                          PC-Trace Users Manual








                                                                         11

          Deleting Component Definitions:
               This function allows removal of a  component.  The component
          that  will be  deleted  is the  one  currently displayed  on  the
          screen.   Press  D  and confirmation  will  be asked  for  before
          deleting  the component.   Answer  accordingly.   All connections
          that contained the deleted function will also be deleted.

          Copying Components:
               This function  will allow  copies of  a  chip definition  to
          speed  the entry  of chips.    It will  copy everything  from the
          displayed  definition   to  a  new  definition   except  for  the
          designation  from  which it  will take  the  alpha part  and then
          increment the numerical part to the next available part.  It also
          does not put the chip in the same location.  The program will ask
          if the user wishes to place the chip now or later.

          Searching for a Component:
               Sometimes finding the component  that needs to be edited  or
          deleted  can  take some  time on  a large  board.   This function
          allows a search  for components by  designation.  When  prompted,
          enter the designation.  PCTRACE will change the case to upper. If
          it exists,  the program will display that device's number.  If it
          doesn't exist, nothing happens.

          Incrementing and Decrementing the displayed Component:
               Using  + and  -  will change  the  displayed component.    +
          increments  and - decrements.  The display is circular in nature,
          therefore hitting  + at  the last component  will move it  to the
          first and hitting - at the first will move it to the last.

          Exiting the Entry/Editing Environment:
               Use the N key to end these functions and return to the board
          definition menu.

          2. Connection Edit/ Entry:
               This  system  allows  for  entry  and  editing  of  all  the
          connections  that need to be  made between the  components in the
          system.    The  functions  are  very  similar  to  the  component
          functions.

          New Connection Entry:
               Typing  an "A"  will allow  entry of  new connections.   The
          program will display the connection number being entered and then
          prompt  for the  name of the  source designation.   The name must
          exist in memory as a component.  ESC can be used at this point to
          return to the entry/editing  environment.  If a ground  plane has
          been defined, the  reserved designation  "GRNDP" can  be used  to
          connect to it.  The associated pin is ignored and defaults to 1.
               The  next question is for the source chip pin number.  Enter

                                                          PC-Trace Users Manual








                                                                         12

          the number of the pin that the  trace is to connect to.  ESC will
          back up to the previous prompt. 
               The  program will now prompt for the name of the destination
          designation.    The name  must exist  in  memory as  a component.
          "GRNDP" can be used as a destination as well.  ESC can be used at
          this point to return to the previous prompt.
               The  next question if  for the destination  chip pin number.
          Enter the number of the pin that the other end of the trace is to
          connect to.  ESC will back up to the previous prompt.
               The program will now ask if this is a priority route or not.
          By  answering "yes", this trace  will be routed  before all other
          non-priority  routes no matter how long it  may be and what other
          routes it may block.  This might be used for making sure a memory
          access  bus is all done in copper  instead of using jumpers for a
          vital connection.
               Next, the program will want to know the desired trace width.
          Traces  from 0.01  to  0.07 are  supported.   Select  the  number
          corresponding  to the  size required.   The following  table will
          show what size trace will  go between two pads of some  size that
          are spaced on 0.1 inch centers.
                                  Pad Size (inches)
          Trace width    0.05      0.06      0.07
               0.01 Yes       Yes       No
               0.02 Yes       No        No
               0.03 Yes       No        No
               0.04 No        No        No
               0.05 No        No        No
               0.06 No        No        No
               0.07 No        No        No

          These tolerances  can be overridden using  the interactive router
          which will be discussed later.
               The next question the  program will ask is if  everything is
          correct.  Answering "no" will restart this process by reprompting
          for the source designation.  Answering yes will bring up the next
          prompt.
               The  next  prompt  is  if  the  user  wishes  to  keep  this
          connection.   Answering "no" will skip the next prompt and ask if
          you  wish to enter another connection.  Answering "yes" brings up
          the next prompt.
               The  last  prompt asks  if  another connection  needs  to be
          entered.   Answering "yes", will put  start back up at the source
          designation prompt to enter another connection.  "No" returns the
          program back to the entry/editing environment.

          Editing Connection Definitions:
               Selecting  E from the  entry/editing environment  will gives
          the  user  the ability  to change  any  part of  each connection.
          Simply select  the letter of the item to change.  For example, to

                                                          PC-Trace Users Manual








                                                                         13

          change the source designation, press A after pressing E and enter
          the  new designation.  Either enter the new designation, or press
          ESC to leave it unchanged.  Press N to exit the edit mode.

          Deleting Connection Definitions:
               This  function   allows  removal  of  a   connection.    The
          connection that will be deleted is the one currently displayed on
          the screen.  Pressing D will confirm before actually deleting the
          connection.  Answer accordingly.

          Searching for a Connection:
               Finding  the connection to edit or delete can take some time
          on a large board.  This  function allows a search for connections
          by  designation.   When prompted,  enter the  designation sought.
          PCTRACE will change the case to upper for you.  PCTRACE then will
          search from  the current connection to the end.  It looks at both
          the source and destination designations for a match.  If it finds
          the  search string  the  program will  display that  connection's
          information.  If it doesn't exist, nothing changes.

          Incrementing and Decrementing the displayed Connection:
               Using  +  and -  will change  the  displayed connection.   +
          increments  and - decrements.  The display is circular in nature,
          therefore typing +  at the last connection moves it  to the first
          connection and pressing - at  the first will move it to  the last
          connection.

          Exiting the Entry/Editing Environment:
               Use the N key to end these functions and return to the board
          definition menu.

          3. Ground Plane:
               This function is used to set up a ground plane.  The program
               will display a picture of the board.  It will prompt for the
               width of  the ground  plane on  all four  sides on  both the
               component side and  solder side  of the board.   Each  digit
               entered corresponds to .05 actual  inches.  The ground plane
               may  be changed at any time.   ESC will also back out of the
               first prompt only (top-solder side).

               ***  Please note that  this function erases any work done in
                    the interactive router (discussed later).



          4. Define Board Size:
               This  function is the first  function used.   It defines the
               dimensions  of the board.  The  maximum board size supported
               by  PCTRACE is  8" X  10".  When  prompted for  numbers, the

                                                          PC-Trace Users Manual








                                                                         14

               numbers  are  entered  as  multiples  of  5.    Each  number
               represents 0.05" of  actual size.  So an entry  of 100 would
               correspond  to 5".   Board sizes can be  changed at any time
               during  the design process by calling the routine again.  If
               the board is made  smaller, the chips that were  outside the
               new border  will have to be  replaced.  ESC will  back up to
               the  previous prompt, or jump out of the routine leaving the
               board size unchanged.

          5. Spider Web:
               This function  is useful for checking to see if a chip would
               be more logically placed somewhere else.  By using the + and
               -  keys,   various  chips  and  their   connections  can  be
               displayed.   As each  chip is selected,  it, as  well as all
               traces connected to it are highlighted in red.  Once  a chip
               is highlighted, selecting M will allow movement of the chip.
               After pressing M, the arrow keys become active and the chip,
               as  well as all its connections will be rubber banded around
               the  board.   Pressing  RETURN will  place  the chip  at the
               current location, or press ESC to not place the chip and put
               it back  at its original  location.  The  ESC or E  key will
               exit from this function.
               *** Please note, if  chips are moved, the  work done by  the
               interactive router is erased.


                                  Interactive Router

               This   board  editing   system   allows   the  designer   to
          interactively design a board.  It can be very useful  for finding
          possible routes that  the autorouter  was unable to  find.   Upon
          entry  to this  section, the  program generates  the  borders and
          places  the  pads  of all  the  chips.    If  a large  number  of
          components has  been placed  on the  board, it  could take a  few
          moments.  It will also  ask the user to place all the  chips that
          have not  been placed  yet.   If you intend  to route  the entire
          board this way,  place your chips  and then leave  them.   Moving
          them  around  after  placing the  chip  will  distort the  board.
          PCTRACE  has  no way  of  connecting  traces up  to  a chips  new
          location.   The  screen  will  show  all  the  chips  with  their
          designations centered  amid each  component pin unless  DEFGEN is
          used to  lock the location  of the designation.   This system has
          many  keys that  are  active  while  in  this  environment.    An
          explanation of each follows.

          S - switch sides:
               This function changes the side of the board displayed.  When
               S is pressed, the  other side of the board  becomes visible.
               The program supports only 2 sides, solder and component.

                                                          PC-Trace Users Manual








                                                                         15

          K - Silkscreen toggle:
               Pressing this key toggles the silkscreen  display on and off
               while in the  interactive router.   It defaults  to ON  upon
               entry to the interactive router.

          C - move a component:
               Pressing this key will give the  user the option of moving a
               component within the interactive  router.  After pressing C,
               the bottom  of the screen  will show  a brief  listing of  a
               component.  The  name and  designation are listed.   +  will
               move to the next component, and - to the previous  one.  ESC
               will exit the component movement function.  Pressing  M will
               erase the  displayed component  and redraw the  screen.   At
               this point, move the cursor to the upper  left corner of the
               area where the component will be placed and press G to place
               it.    It  is  important  to  understand   that  the  cursor
               represents  the  absolute  upper  left corner  of  the  part
               including any silkscreen extensions.

          G - grab location:
               The key  is only active at  certain times.  The  F1, F2, F4,
               F5, F6, F7, and F10  function all use this key.  The  key is
               normally used to mark a location on the board or  a piece of
               a trace.

          B - Turn on background:
               This  key is used to  turn on and  off the background layer.
               If  editing  the  solder  side,  a  lightened  view  of  the
               component side  can be turned  on.   On a color  monitor, it
               will appear dotted and  red.  Black and white  monitors will
               show dotted graphics only.  Pressing B again turns this mode
               off.

          E or ESC - end:
               Pressing E or ESC will exit from the interactive router.

          Cursor Keys:
               The  cursor keys move the  solid block around  on the board.
               Each time an  arrow key is pressed,  the cursor will  move 1
               space.   Relative coordinates are displayed at the bottom of
               the  screen.  Using Shift-Arrow  moves the cursor 10 spaces.
               If  the edge of the screen  is encountered, but not the edge
               of the board, the screen will shift the board over.

          Function Keys:
               The function  keys numbered  F1-F10 do  the majority  of the
          work in PCTRACE.   They allow placement of vias,  running traces,
          deleting traces, resizing traces, and deleting vias.


                                                          PC-Trace Users Manual








                                                                         16

          F1 - Set Source:
               By  pressing  F1,  the bottom  of  the  screen  will say  to
               position  the cursor on the  pad that will  be designated as
               the source and then press  G to grab it.  The  bottom status
               line will display exactly what chip and pin number have been
               selected.

          F2 - Set Destination:
               This function works exactly  as the F1 function but  selects
               the destination pin.

          F3 - Run Trace:
               Once a source and destination have been defined, pressing F3
               will  attempt  to connect  the two  pins  with a  trace 0.01
               inches  wide.   If  it is  successful,  the screen  will  be
               redrawn  and the trace will  appear.  If  it cannot complete
               the route, a  message will be displayed at the bottom of the
               screen.   At this point try  placing a via and  routing from
               the source  to  it on  one  side and  from  the via  to  the
               destination on the other.

          F4 - Delete Trace:
               This  function  will delete  any part  of  any trace  on the
               board. Pressing F4 enters the  delete selection mode.  After
               pressing F4 the screen will  say to use G to grab  the parts
               to  be deleted.  As the user  presses G on valid traces, the
               pieces will  be highlighted.  Changing screens by moving the
               cursor off  the screen  will not  lose the  already selected
               traces.  Once all  the pieces to delete have  been selected,
               press F4  again  and  the  program will  prompt  to  confirm
               deleting of the  selected traces.   Answer Y  to finish  the
               delete operation.

          F5 - Add Via:
               This function  key will  add a  via at  the location  of the
               cursor when G  is pressed.  It  will be V and  then the next
               available number.   Use these for multilevel  routes or just
               extra  pads needed.  A  via cannot be  placed adjacent to an
               existing pad.  One can be placed diagonally from  a pad .  A
               via  also may not be  placed in the middle of  a trace.  All
               vias are deleted by the autorouter when it is invoked.

          F6 - Del Via:
               This  function deletes the via at the cursor location when G
               is pressed if a via exists there.





                                                          PC-Trace Users Manual








                                                                         17

          F7 - Resize trace:
               This function will resize  a trace to any valid  trace size.
               Select F7  and use G to  select the traces to  resize.  Once
               the traces to  resize have  been selected press  F7 and  the
               program will ask for  confirmation of the resize.   Answer Y
               to resize.   The program  will prompt for  the trace  resize
               value.  1 corresponds to 0.01  up to 7  which corresponds to
               0.07 inches.  Be careful not to overlap other traces or pads
               with this function.

          F8 - Check Route:
               This  function will check to see if  a selected pair of pads
               can be connected.  It will report back whether the route can
               be completed, the route  exists already, or if no  route can
               be found.  This is useful for doing multi-layer routes using
               vias.   Checking for  an available  route before  laying the
               actual trace will save a number of deletes if later the path
               is blocked.

          F9 - Manual Route:
               This  function allows  the  user to  manually route  traces.
               Place the  cursor on the starting pad or trace and press F9.
               A prompt will appear  at the bottom of the screen asking for
               the trace width.   Enter the number that corresponds  to the
               desired size and press  return.  Now use the  cursor control
               keys to  route the trace.  Every  time the cursor moves, the
               trace  is lengthened.   When  done, either  stop in  an open
               space and press F9  or stop on a trace or  pad and press F9,
               the  correct  connecting piece  will  be added  to  make the
               connection.  Please note that moving over an  existing trace
               will cause  PCTRACE to cut  that trace in  favor of  the new
               path.   This  works well  for putting  short jumpers  on the
               board.   This is very  useful for routing  traces that would
               normally  block other routes  if they  were not  placed this
               way.   With  the interactive  router any  size trace  can be
               placed anywhere.  It is possible to over-ride the autorouter
               and  run a 0.01  inch trace between  two 0.07 pads.   If the
               board-making process used is accurate to 0.01 many low power
               traces can be completed this way.  The manual router is also
               used  in  many  advanced  "tricks"  for  making  specialized
               boards.

          F10 - Write Text:
               Pressing  F10  allows additional  text  to be  added  to the
               silkscreen layer.   After pressing F10, the program will ask
               the user to move the cursor to the starting position for the
               text  and  press G.   After  pressing  G, the  software will
               prompt  for  the text  string.   It  will  accept  up to  20
               characters.   When done  entering text, press  return.   The

                                                          PC-Trace Users Manual








                                                                         18

               next prompt is for  double sized text.  Answer "yes" and the
               text  will  appear double  sized.   The  board will  then be
               redrawn with the text added in.   The only thing to be aware
               of is that normal silkscreen text takes precedence over user
               added text.

          Using a mouse in the interactive router:
               The mouse allows  a faster  method to do  all the  functions
          mentioned  previously except  for the  manual router.   The mouse
          must  be installed  before  running the  PCTRACE  program.   When
          entering the interactive program  four arrows will appear  in the
          lower right corner of  the screen.  By  using the mouse,  putting
          the cursor on one of these  arrows, and pressing the left button,
          the screen will  be moved by  half in that  direction.  The  same
          thing was accomplished by  moving the cursor off the  board using
          the arrow keys.
               Pressing  the  right button  will pop  up  a menu  along the
          bottom of the screen.  The  menu corresponds to function keys F1-
          F8, and F10.  The exit command at the far right, exits the  menu.
          By placing the cursor anywhere on  the command desired, execution
          of that  command is  done by  pressing the left  button.   If the
          command selected is F1, F2,  F4, F5, F6, F7, or F10,  the program
          will be using the "Grab" method.  The left button  works the same
          as the G  key in these cases.   Use it to highlight  sections and
          locations on the board to  work with.  When using the  delete and
          resizing  functions (F4 and F7)  the user must  press and release
          the left button for each piece of trace.

                                     Autorouting
               Selecting this from the menu will enable the user to connect
          all  or most of the connections  desired.  The program will first
          draw borders, place  pads, and set  up the ground  planes.  If  a
          component has not been placed,  the program will ask the  user to
          place it.   The program requires all chips to be placed before it
          can  route.    There are  four  routing  strategies  that can  be
          employed.  Select each strategy by  pressing Y or N as the cursor
          moves to each option.  If Y is selected for single or  double via
          routing a prompt will also appear for the maximum number of tries
          for each.   Just enter a  number.  Bigger numbers  are better for
          bigger boards, smaller numbers for small boards.
               The  PCTRACE  system  is  totally  re-entrant.    The  first
          question  asked  is  if the  user  wishes  to  clear all  traces.
          Answering  "yes" clears anything  currently on  the board.   "No"
          would keep the screen as it was.   ESC can  be pressed during any
          routing  strategy to exit that  routine and the  autorouter.  The
          program will then show  the list of all unconnected  routes still
          existing.   If the router  has not completed  one run-through the
          connection list,  traces may have  been completed by  the earlier
          route and still be  reported as unconnected.  A  design check can

                                                          PC-Trace Users Manual








                                                                         19

          be done  to see which routes in the connection list have not been
          connected,  either by hand or  by the autorouter,  by running the
          autorouter and not erasing  the current traces.  This  is because
          the autorouter  will not  reroute a connection  that has  already
          been completed.   Just select  the double or  single sided  route
          system.   It  will report  any routes  that are incomplete.   Any
          route  that was completed before  will be marked  as complete and
          not reported.   The program will  report whatever routes  weren't
          done and the ones it couldn't complete.

          Single Sided Route:
               This  function will attempt to  place all the  routes on the
               solder  side  of  the board.    It  is  the least  efficient
               strategy  but  is great  for  small projects  where  ease of
               making the board itself is a priority.  This function cannot
               be used in conjunction with the next three strategies.

          Double Sided Route:
               This function will do its routing on two sides of the board.
               It has a higher completion percentage  than the single sided
               strategy.

          Single Via Route:
               This  function requires  that the  double sided  strategy be
               selected first.    This function  is used  after the  double
               sided strategy  to try  to complete any  uncompleted routes.
               It places  a via  and tries  to do the  single route  with a
               trace on  each side of  the board.  A  number such as  50 is
               good for the maximum number of tries prompt.

          Double Via Route:
               This  function also  requires that  double sided  routing be
               selected to work.  It  uses two vias to attempt  to complete
               the route.   A good  maximum number  of tries is  30 or  so.
               This function can take a great deal of time so be patient.

                                   Board Statistics

          This function displays 5 statistics.

          Equivalent Integrated Circuit Count:
               This function is the total number of pins divided by 16.

          Board Density: This is  the amount of space total  that each chip
                         has  to occupy.   It  is calculated by  taking the
                         area of  the board and dividing  by the Equivalent
                         IC count.



                                                          PC-Trace Users Manual








                                                                         20

          Total Trace Length: The function  gives the  total length  of all
                              the  traces on  the board.   The  smaller the
                              number, the better the design.

          Board size:    The board dimensions in inches.

          File name:     This is the file name currently in memory.











































                                                          PC-Trace Users Manual








                                                                         21

                                     Printer Menu

          1. Print Components:     This  function will  generate a  list of
                                   all the components.  It can be sorted by
                                   name or designation.  

          2. Print Connections:    This  function will  generate a  list of
                                   all the  connections in memory.   It can
                                   be sorted  by the source  or destination
                                   designation.


                                     Export Menu

               The  export menu allows for files to be created that various
          other  cad software and board producers use.  After selecting the
          Export menu from the main menu, four export choices will be seen.

          1. Write Autocad Script file:
                    This function will  write a  file that can  in turn  be
               read into and edited with Autocad.  The process is one  way,
               no  way is provided to read autocad files back into PCTRACE.
               Call this function from the Export menu and give a name when
               prompted.  Specify no path or file extension.  The extension
               .SCR will  be added to the  file.  Once the  program is done
               writing the file, Autocad  may be started.  Use  the command
               "SCRIPT" from the "Command:"  prompt.  Autocad will ask  for
               the script file name.  Specify  the same name (with path  if
               needed)  as the one created in PCTRACE and Autocad will read
               in the  file.  Autocad  will display  three layers:  solder,
               component,  and silkscreen.  Each may be edited and saved as
               Autocad  drawing files.   Doing  this greatly  increases the
               number  of printers that can  be used for  output as Autocad
               supports a large number of printers.

          2. Write a DXF file:
                    The  DXF  file   is  used  by  many   cad  packages  to
               incorporate data into their  systems.  Autocad is  one prime
               example.   The  DXF file  includes all  three layers  in its
               output (Solder,  Component,  and Silkscreen).   The  command
               will prompt for  a file name.   Enter  the filename with  no
               extension.  The  extension .DXF  will be added.   After  the
               filename has  been  entered, the  DXF  file output  will  be
               created.   Autocad will  load  this file  using the  command
               "DXFIN"  from  the Autocad  "Command:" prompt.   Wordperfect
               will also read a DXF file and convert it to its own graphics
               format (WPG files).  



                                                          PC-Trace Users Manual








                                                                         22

          3. Write a Gerber file:
                    A Gerber file is the standard file type that is used by
               professional  board manufacturers.    The PC-Trace  software
               will  generate this file format and is accurate to 3 decimal
               places.  Upon selection of this option, the user is prompted
               to enter aperture names to be used.  The aperture is used to
               describe an entity on the board.   If the photo plotter that
               the board maker is using requires that  a pad 0.05 inches in
               diameter  be specified  as  D23,  then  the  0.05  inch  pad
               aperture name must be changed to reflect this.  The software
               will ask if the aperture  list is OK.  If it is, press Y for
               yes and the program will continue.   If N for no is pressed,
               each aperture must be re-entered as the cursor goes down the
               column.    ESC  will  bypass a  selection  without  erasing.
               Retyping will change the selection and return will erase the
               selection  which  would make  it  necessary  to re-edit  the
               aperture list.  Once  the list is determined to  be correct,
               the program prompts for the board  side to be plotted to the
               file.   Press  the number  that corresponds  to the  desired
               selection.   Last of all the  program will ask for an output
               filename.   Enter  the  filename with  no  extension.   Upon
               pressing  the  return key,  the  program  will generate  the
               Gerber file.   Two files  will be created.   The first  file
               will  be the filename plus the extension .GER for the actual
               Gerber  file.   The  second file  is  the filename  plus the
               extension  .AP for the aperture  list.  Both  of these files
               should  be sent  to  the  manufacturer.    A  file  must  be
               generated  for  each  board  side  that  is  desired  to  be
               manufactured.  Only one aperture file need be sent.

          4. Write a CNC Drill file:
                    A  CNC  drill  file  contains  the  information  for  a
               Computer Numerically  Controlled  drill press  to drill  the
               holes  for the pins of  the components to  be placed though.
               The  software will  prompt for the  drill bit  (tool number)
               size that should be used for each different  sized pad.  The
               entry system works the  same as that of the  Gerber aperture
               definition screen.  The  user will next be prompted  for the
               output  file  name.    It  should  be  entered   without  an
               extension.  After pressing return at the end of the filename
               the  computer will  create the  filename with  the extension
               .NC.  The file contains the X,Y coordinates of all the pads.


                                 Exiting the Program

               Selecting 8 from the  main menu will exit from  PCTRACE back
          to DOS.   If there is data in memory the  program will ask if you
          wish to  save it.  Answering  "Yes" will prompt for  a file name.

                                                          PC-Trace Users Manual








                                                                         23

          Enter  the file name as was done in the save data function in the
          Input/Output menu.   ESC  will abort  the save,  but it  will not
          return the user to the program.  Answering "No" to the save query
          will cause the program to go immediately to DOS.














































                                                          PC-Trace Users Manual








                                                                         24

                                    Brief Tutorial

               The  following is  intended as  a method  of getting  up and
          running with the program.  It will give a general idea of how the
          program works.
          1.   Begin by  running PCTRACE.   This  information can  be found
               back in the section on setting up PCTRACE for your machine.
          2.   Once  at the main menu,  press 3 for  define/edit board, and
               then select 4 for define board dimensions.  For our purposes
               we will use a board size of 80 x 80, which translates into a
               4 inch square board.
          3.   Select function 1  to enter  new components.   You will  see
               that no data has been  entered yet.  Press A to  enter data.
               We  will put  three chips  on the  board and  two resistors.
               Answer  each prompt  below with  the following  data.   When
               asked  to place each chip  answer Y and  place the chip with
               the  cursor keys.   After  you have  entered the  last item,
               answer N to the "Enter another component?" prompt.

          Name: 8051 uP                 Designation: IC1
          Definition file: DIP40V6      Placement: Left side
          Pad Size: 0.05

          Name: 74ls373                 Designation: IC2
          Definition file: DIP20V3      Placement: Upper right
          Pad Size: 0.05


          Name: 2716                    Designation:  IC3
          Definition file: DIP24V6      Placement: Lower right
          Pad Size: 0.05

          Name: 100k resistor           Designation:  R1
          Definition file: 2PAD50V      Placement: Upper middle
          Pad Size: 0.06

          Name: 10k resistor            Designation:  R2
          Definition file: 2PAD50V      Placement: Lower middle
          Pad Size: 0.07

          N exits to the board definition menu.
          4.   Next,  enter the list of connection between chips.  Select 2
               from  the menu to enter the connection entry section.  Enter
               the following connections.  All traces should be 0.02 inches
               wide.    Answer N  to each  prompt  of "Is  this  a priority
               connection?".   When  the last  connection has  been entered
               answer N to the "Enter another connection prompt?".

          Source Device  Pin  Destination Device  Pin

                                                          PC-Trace Users Manual








                                                                         25

               IC1  2         IC3       2
               IC1  3         IC2       16
               IC3  22        IC2       6
               R1   1         IC2       4
               R2   1         IC1       8
               R2   2         IC3       6
               R1   2         IC1       31
               IC2  8         IC3       17
               IC1  21        IC1       15
               IC2  8         IC3       8
               IC2  9         IC3       9
               IC2  10        IC3       10
               IC1  14        IC2       9

          N returns to the menu.
          5.   Ok, let's autoroute the board.  Go back to the main menu and
               select  4  to autoroute  the board.    When prompted  to use
               single sided routing or not, answer  Y.  Now hit the ESC key
               and  watch  the machine  route.   When  it is  done  is will
               display the  list of uncompleted connections  to the printer
               or  screen.   Select whichever  you  wish.   We will  now be
               dropped back to the main  menu.  We can take a look  at what
               we have done by  selecting number 5 from  the menu.   Cursor
               around  and see a representation of the board on the screen.
               Hit ESC when done.

               Now let's re-route the  board using double sided techniques.
               This time  say N to single  sided and Y to  double sided and
               then hit ESC.  The machine will route double sided and again
               give  a list of incomplete connections if any exist.  Select
               printer or screen for this  list.  Let's take a look  at the
               board again.  This time we may also want to use the S key to
               change sides of the board that we are viewing.  When you are
               done hit ESC.
          6.   From the main  menu, hit  6 for statistics.   Displayed  are
               five statistics that tell you how good your  design is.  Hit
               space when you are done with this.
          7.   Last of all we'll print out our design.  Follow instructions
               in the section on the RPRINT Subprogram to do this.











                                                          PC-Trace Users Manual








                                                                         26

                                RPRINT.EXE Subprogram

               Execute  this program by typing RPRINT  from the dos prompt.
          Upon  entry into  this program the  user will  be prompted  for a
          printer type.  Enter the corresponding number.  The second prompt
          is for  the board name.   Type the  name with no  extension.  The
          main control  panel will  now explode  onto the  screen.   A math
          coprocessor is particularly useful in this program.
          1. File name:  Selecting 1  will allow changing of the file to be
                         printed.  Enter the filename with no extension.
          2. Board side: This selects  the board side to  print.  Selecting
                         this  number will  toggle  between three  possible
                         sides   to   print    (Solder,   Component,    and
                         Silkscreen).  Single sided  boards are done on the
                         solder side.
          3. Mirroring:  This  selection toggles between  mirroring and not
                         mirroring the board.
          4. Negative:   This  function  will  allow  the  user  to  select
                         between printing  a negative or a  positive of the
                         actual board.
          5. Actual size:     Laser printers and 24 pin dot matrix printers
                              can output the images at actual size.  If the
                              selected  printer  lacks  the  resolution  to
                              achieve acceptable results, this  menu choice
                              will  not exist.   Selection  of  this choice
                              allows  toggling  between  actual   size  and
                              double sized printing.

          6. Pin1 square:     Toggling this  to the on position  will print
                              the  number one  pin of  all components  as a
                              square.  This  is useful for identifying  the
                              number one pin when placing the components on
                              the finished circuit board.
          7. Output file:     After selecting this menu choice, the user is
                              prompted for an output  file name.  Enter the
                              filename without an  extension.  The printout
                              of the file will now be sent to the file that
                              was designated.   The file will  be given the
                              extension  .PRT.    Be  careful  if  printing
                              multiple  files not  to overwrite  a previous
                              printing.
          8. Print Board:     This  selection starts  the  printing of  the
                              board.
          9. Exit program:    This  selection exits the RPRINT program back
                              to DOS.
          Plotter Notes:
               In using RPRINT with plotters, no provision is made to print
          to a serial port.   With DOS 3.3 and later, the MODE  command can
          be used  to redirect  printer output  to  the serial  port.   Two

                                                          PC-Trace Users Manual








                                                                         27

          commands are needed.
          MODE ComX:9600,N,8,1,p (press return) X is the com number
          MODE LPT1:=ComX: (press return)
          MODE LPT1: (press return) will return to normal operation














































                                                          PC-Trace Users Manual








                                                                         28

                                        DEFGEN
                                      Subprogram


               The  program needs  to  know the  exact  pin layout  of  any
          component  placed on the board.  This function allows creation of
          these definitions.   The largest difference  between this version
          and previous versions  of PCTRACE is  that surface mount  support
          can be acheived more easily.   When a device is defined, all pins
          of the surface mount  part must be terminated at  a through-holed
          pad.   That is  the same as  before.  With  version 5.0, pads and
          traces can  be defined within  the definition  file allowing  the
          user to draw small traces with flat pads to serve as locations to
          mount  a surface mount  part.  A  silkscreen outline  can also be
          drawn with the manual router in "SILKSCREEN" mode.
               The program  is  started by  typing  "DEFGEN" from  the  dos
          prompt in the PCTRACE subdirectory.


          ***Note:  Most chip  dimensions are available in  data books such
                    as RCA cross reference manuals.  Radio Shack  also puts
                    device dimensions on the back of their packages.

               When running DEFGEN to create  new chip layout patterns many
          keys are active.  A summary of each key follows:

          S - switch sides:
               This function changes the side of the board displayed.  When
               S is entered from the keyboard,  the other side of the board
               will  be displayed.    The program  supports  only 2  sides,
               solder and component.

          K - Silkscreen toggle:
               Pressing  this key  toggles  the drawing  on the  silkscreen
               layer as opposed to the solder  or component layers.  When K
               is pressed a green "SILKSCREEN" appears at the bottom of the
               screen.   The only commands that are available at this point
               are  the F9, manual router,  which is used  to draw the part
               outline, F10  which allows placing  text in addition  to the
               component designation, F1  which is Load, F2 which  is Save,
               and F3 which is erase.

          G - grab location:
               The key is only active at certain times.  The F4, F5, F7 and
               F10 functions all use this key.

          B - Turn on background:
               This key is  used to turn  on and off the  background layer.
               If the user is editing the solder side, this key will show a

                                                          PC-Trace Users Manual








                                                                         29

               lightened view of the  component side.  On a  color monitor,
               it will appear  dotted and  red.  Black  and white  monitors
               will show dotted graphics only.  Pressing B again turns this
               mode off.

          E or ESC - end:
               Pressing E  or ESC will exit  from the DEFGEN program.   The
               exit is immediate and should be used carefully.


          Cursor Keys:
               The  cursor keys move the  solid block around  on the board.
               Each time the  arrow key is pressed, the cursor  will move 1
               space.  Relative  coordinates are displayed at the bottom of
               the screen.   Using Shift-Arrow moves the  cursor 10 spaces.
               If the cursor comes to  the edge of the screen, but  not the
               edge of the board, the screen will shift the board over.

          Function Keys:
               The function keys  numbered F1-F10  do the  majority of  the
               work in  DEFGEN.   They allow the  user to  place vias,  run
               traces,  delete traces,  resize traces,  add pads,  and draw
               component outlines.

          F1 - Load Definition:
               By pressing F1, the bottom of the screen will prompt  for an
               input definition  file name.   Enter  the  filename with  no
               extension.  If the file is found it will be displayed on the
               screen  for editing.  Please  feel free to  use the provided
               definition files in creating others.

          F2 - Save Definition:
               This  function  will prompt  for  a  save filename  for  the
               definition.  Enter the save filename with no extension.  The
               program  will notify the user if the file already exists and
               check to make sure that  it is alright to rewrite the  file.
               Once the file has been written with this command, DEFGEN can
               be exited and the definition used in PCTRACE.

          F3 - Erase:
               This  command has  four options.   Option  1 will  erase the
               component layer of  everything except the pads.   The second
               option deletes everything but the pads off the solder layer.
               The third  layer will  remove everything off  the silkscreen
               layer  except for  the  placement of  the designation  text.
               Option 4 deletes  everything, including the pads.   Option 5
               exits without deleting anything.



                                                          PC-Trace Users Manual








                                                                         30

          F4 - Delete Trace:
               This  function will delete any part of any trace that exists
               in the  definition. Pressing F4 enters  the delete selection
               mode.   After pressing  F4 the screen  will say to  use G to
               grab  the parts  to be deleted.   As  G is  pressed on valid
               traces, the pieces will be highlighted.  The user can change
               screens by moving the cursor  off the screen without  losing
               the  already selected traces.  Once all the traces to delete
               have been  selected, press  F4 again  and  the program  will
               prompt  to make sure you wish to delete the selected traces.
               Answer Y to finish the delete operation.

          F5 - Add New Pad:
               This  function key will  add a  pad at  the location  of the
               cursor  when G  is pressed.   All  components must  have pad
               definitions.   The router is unable to route to a trace that
               cannot be specified by an attached pad.  The pads are placed
               in  sequence so  be  sure  to  place  them  in  the  package
               numbering order.

          F6 - Delete Last Pad:
               This function deletes  the last placed pad from  the screen.
               It requires that the definition be regenerated so the screen
               will be redrawn.

          F7 - Resize trace:
               This function will resize  a trace to any valid  trace size.
               Select F7  and then  use G to  select the traces  to resize.
               Once  you have selected the  traces to resize,  press F7 and
               you will be asked  if you really wish to resize  the traces,
               answer Y  if you do.   Next the program will  prompt for the
               trace  size. 1 corresponds to 0.01 up to 7 which corresponds
               to 0.07 inches.  Be  careful not to overlap other  traces or
               pads with this function.

          F8 - Coordinates for Designation:
               This  function   will  anchor  the  location   of  the  part
               designation.  Normally the designation moves to the centroid
               of the area  defined by  the pads.   For most  applications,
               like  DIPs,  this  is  acceptable.    Some  parts,  such  as
               transistors, benefit from having the designation text placed
               above  or below the pads.  Selecting this option will prompt
               for a location for the center of the designation text.  Move
               to  that location and press G.   The next prompt asks if the
               user  desires double sized text.   If "yes"  is entered, the
               designation will be drawn 0.1  inches high on the silkscreen
               layer.  "No" will draw text 0.05 inches high.



                                                          PC-Trace Users Manual








                                                                         31

          F9 - Manual Route:
               This  function allows  the  user to  manually route  traces.
               Place  the cursor on the  starting pad, trace,  or open area
               and press  F9.  Now use the cursor control keys to route the
               trace.     Every  time  the   cursor  moves,  the  trace  is
               lengthened.  When done, press F9.   If the end is on another
               trace, pressing F9 will add the proper connecting point.  If
               the green  SILKSCREEN indicator  is  on, the  trace will  be
               routed in green.  This should be used to draw the outline of
               the part.  This outline will be displayed in the interactive
               router and when printing the silkscreen.

          F10 - Write Text:
               Pressing  F10 allows the addition  of text to the silkscreen
               layer.  After  pressing F10, you  will be asked to  move the
               cursor  to the starting position  for the text  and press G.
               After pressing  G, the  software  will prompt  for the  text
               string.   It will  accept up  to 20  characters.   When done
               entering  text, press return.  The next prompt is for double
               sized  text.  Answer "yes"  and the text  will appear double
               sized.  The  board will then be redrawn  with the text added
               in.

          Using a mouse in the DEFGEN program:
               The  mouse  allows  usage  of all  the  functions  mentioned
          previously except for the  manual router.  The mouse  driver must
          be installed  before running the  DEFGEN program.   When entering
          the interactive  program, four  arrows will  appear in  the lower
          right corner  of the  screen.   By using  the mouse,  putting the
          cursor on one of  these arrows, and pressing the left  button the
          screen will be moved by  half in that direction.  The  same thing
          was accomplished by  moving the  cursor off the  board using  the
          arrow keys.
               Pressing the right mouse button will pop up a menu along the
          bottom of the screen.  The  menu corresponds to function keys F1-
          F8, and F10.  The exit command  at the far right, exits the menu.
          By  placing the  cursor  anywhere on  the  command desired,  that
          command  can be  executed by  pressing the left  button.   If the
          command selected  is F4,  F5, F7, F8,  or F10, the  "Grab" method
          will be in use.  The left button  works the same as the G key  in
          these cases.  Use  it to highlight sections and locations  on the
          board to work with.  When using the delete and resizing functions
          (F4 and F7) the user  must press and release the left  button for
          each piece of trace.






                                                          PC-Trace Users Manual








                                                                         32

                                  Keyboard Summaries
                                     for PCTRACE

          Chip Placement Screen:
          ESC       - Option to Abandon Placement
          RET       - Place chip at current location
          Cursor Keys    - Moves chip one space for each depression
          Shift Cursor Key - Moves chip 10 spaces for each depression

          Spider Web System:
          M*        - Set system to move highlighted chip
          Cursor keys    - Move chip one space on board
          RET       - Place chip at current location
          ESC       - Abandon placement
          +,-*      - Increment and Decrement through chips
          E*        - Exit Web System

          * -  Denotes that  this selection is  displayed on screen  at all
               times.

          Interactive Router:
          S         - Display other side of board
          G         - Grab a piece of trace at cursor
          E,ESC          - Exit interactive router
          B         - Turns on and off background
          C         - Allows movement of devices
          K         - Turns silkscreen layer on and off
          F1        - Select source pad
          F2        - Select destination pad
          F3        - Attempt to connect source and destination
          F4        - Delete traces
          F5        - Place via at cursor location
          F6        - Delete via at cursor location
          F7        - Resize selected trace
          F8        - See if route is possible between source              
                      and destination pads
          F9        - Enters and exits the manual router
          F10       - Puts user text on the silkscreen layer












                                                          PC-Trace Users Manual








                                                                         33








                                         SCAD






                                  Schematic Capture

                                     Version 1.0

                                     Users Manual

                                    June 21, 1992








                                          by






                                  Douglas E. Ehlers

                               Copyright (C) 1991,1992














               
               

                                     Introduction

               Schematic   CAD  is   a  program   for  drawing   electrical
          schematics.  While this drawing is being made, the software keeps
          track of all components and connections between them.  It is then
          possible to create an  export file (.NLT) that PC-Trace  can load
          and create  a board from.   This allows  the designer a  complete
          cycle  for production of a circuit board.  From conceptual design
          to computer controlled manufacture of the board,  this system has
          it all.

          Menu Usage:
               The menu  system in  SCAD requires  the use of  a mouse  for
          complete use of the  system.  Some functions can  be accomplished
          with  the use  of the  keyboard only.   Using  a mouse,  move the
          cursor  to the area  of the desired menu  selection.  By pressing
          the left  mouse button, a pull  down menu will appear.   Move the
          mouse down the menu  until the desired choice is  highlighted and
          release the button.  The menu  choice will be executed.   Another
          way to make menu choices is to open  the menu by pressing the ALT
          key and the  highlighted menu area key.   For example ALT-F  will
          open the Files  Menu.  The cursor  keys can be  used to move  the
          highlight bar up and down the menu.  Pressing return will  select
          the  menu  choice.   Once the  menu  appears, pressing  the first
          letter of the desired  choice will move the highlight bar to that
          choice.
               Some menus have  small arrows  that point to  the right.  By
          moving the  mouse across that arrow a  submenu will appear.  That
          menu  responds the  same way  as  the rest  of the  menus.   Many
          functions  use this  concept including  Print, Draw,  Delete, and
          Move.

          File Menu:
          New Diagram:
                    The New Diagram function from the FILES menu will clear
               the drawing space that SCAD uses to store files.  A dialogue
               box is used to confirm this selection.

          Load Diagram:
                    The Load Diagram  file will load  a schematic that  was
               saved  previously.   The  program will  prompt for  the file
               name.  Enter  the name  without the extension  (.SCH).   The
               program  will add the extension.  If the program cannot find
               the file it will report it and give the  user another chance
               to enter the filename or to exit back to the drawing area.

          Save Diagram:
                    The  Save Diagram  function  saves whatever  is in  the
               memory of the system at a given point.  When  prompted for a
               save name, enter the name with no extension.  SCAD  will add
               the extension (.SCH).  If the program can't find the entered
               file name, it will save the information from the given mode.
               If  the program finds that the save filename exists, it will
               prompt to see  if the old file  should be overwritten, or  a
               new file name should be specified.

                                                          PC-Trace Users Manual








                                                                         35





          Export DXF:
                    The Export  DXF function  is used  for creating  a file
               format that can  be read  by many popular  CAD programs  and
               word-processing packages.  The DXF format used is compatible
               back to Autocad Version 2.6.  The program will  prompt for a
               save  name.   Give the  file  name with  no extension.   The
               program will add it  (.DXF) automatically.  If  the filename
               already  exists on the disk,  the program will  prompt as to
               whether  or not to overwrite  the file.   Answering yes will
               overwrite the old filename, and answering no will cause SCAD
               to prompt for a new file name.

          Export PC-Trace:
                    The function is used  to create a netlist that  PCTRACE
               can  load.   It  contains  a  list  of  all  components  and
               connections  that have  been  entered while  using the  SCAD
               software.  All that will be required on the PCTRACE side  is
               to place  the  components and  start  the autorouter.    The
               program prompts for the export filename.  Enter the filename
               with no  extension, the  program will add  it automatically.
               If the program finds that  the entered filename exists,  the
               program will allow the option of overwriting the file or re-
               entering a new filename.

          Print Total/Window:
                    Print has  two options,  one, the option  called Total,
               that will  find the extents  of the drawing and  scale it to
               fit  on a page.   The second, or  Window, essentially prints
               what  is currently  being viewed  on the  screen.   Once the
               program is told to  print, it will create a print file, save
               the  current drawing  and chain  to the  sprint.exe program.
               The  first prompt in this  program is for  the printer type.
               The  user should  select  their printer  or  one that  their
               printer emulates.  The  sprint menu can print to  a file and
               that is toggled  with option 1.   When prompted for  a print
               filename,  enter the filename with no extension.  The second
               option will  allow printing  in portrait or  landscape mode.
               Option 3  actually prints  the drawing,  and option  4 exits
               sprint.exe and returns to SCAD.

          Show Drawing Info:
                    This  function  will  show  basic  drawing  information
               including the  current SNAP value, the  current window size,
               the  amount  of  free   memory,  and  the  currently  loaded
               filename.

          Exit:
                    The exit  function exits whichever mode  the program is
               currently running  in.  This function can  also be activated
               by  pressing ALT-X.  If  the user is  currently operating in

                                                          PC-Trace Users Manual








                                                                         36

               the Component  Drawing area, it  will exit the  drawing pad.
               If the user is editing the  main drawing, it will allow exit
               of the program.  No option is given to the user  to save the
               file once exiting the program is answered with an OKAY.


          Drawing Symbols:
               When Draw Component is selected from the Components menu,  a
          box appears  in the center  of the screen.   This is  the drawing
          area  for creation of  components.  A  component in this  case is
          defined to  be the  schematic symbol  for any part  that will  be
          placed in  the drawing.   A  small library  of common symbols  is
          included with the system for the user.  Invariably, a symbol will
          be  needed that  is not included.   That  is the  purpose of this
          editor.
               Once  the box appears in the middle of the screen, the Files
          menu  and the  Entities  menu  come  into  play.    Only  certain
          functions may  be used in each.   The unusable functions  will be
          grayed out and the  user will be unable to  use them.  The  Load,
          Save, New, and Exit functions in the Files menu work as described
          previously, except  that they only  apply to  the current  symbol
          being drawn.   For example, if an AND gate is drawn in this area,
          saving  it will only save the representation  of the AND gate and
          not the overall drawing.
               The  save routine itself is different at this point as well.
          It includes a  short routine that  asks the user  to outline  the
          symbol with a bounding  box before the save takes  place.  Select
          the  upper left  and lower  right of  the drawing  to save.   The
          entire drawing will  be shifted to call the upper  left corner of
          the bounding box the origin for later use.
               The  following  overview  tells  how  the  various  Entities
          commands work and what they do.  Their usage here is  essentially
          the same as their usage in the main drawing area.

          Draw-Line:
                    This function  is used to draw lines within the drawing
               window.   At the bottom of the  screen, SCAD will prompt the
               user  as  to  what   the  program  expects.     The  current
               coordinates  are shown  at  the bottom  right.   Select  the
               location of the  starting point  of the line  and click  the
               left  or right button.  Clicking the left button will anchor
               the  start  of  the  line at  the  current  mouse  location.
               Clicking the right button will anchor the start point at the
               current  point, plus it will  draw a connection  dot at this
               point.   The dot  will not  appear until  the start and  end
               points  of the line have been specified.  After clicking the
               left  or right button, the  program will prompt  for the end
               point.  Click either the right or left button.   The buttons
               have the same effect  as when picking the start  point.  ESC
               will exit or back up while  drawing lines.  To draw  another
               line, select this function again.


                                                          PC-Trace Users Manual




                                                          

                                                                         37

          Draw-Arc:
                    This function is used to draw  an arc of some size.  It
               can be used to draw 1/4 arcs from any start point to any end
               point and  at any  diameter.   The first  prompt is  for the
               center  point of the  arc.  Move the  mouse to this location
               and click  a button.  The second prompt is for the radius of
               the  arc.  Move the  pointer to the  location that shows the
               desired radius.   A floating line reminds the user as to the
               current length.  The next point is for the start of the arc.
               Pick  this point as before.  The  last prompt is for the arc
               ending point.   Click on this point.  The  arc will be drawn
               from the start point, counter-clockwise, to the end point at
               the  given radius.   ESC  will back  up at  any time  to the
               previous  prompt or will exit the function.  To draw another
               arc, pick this function again.

          Draw-Circle:
                    This function draws a circle  at some center point  and
               some radius.  When prompted, pick the center point and click
               a mouse button.  The second  prompt is for the radius of the
               circle.  Click on this point and the circle will be drawn on
               the screen.  ESC will back up to the previous prompt or exit
               the function.   To draw  another circle, pick  this function
               again.

          Draw-Text:
                    This  function is used place  text on the  screen.  The
               first prompt is for the starting location of the text.  This
               point is located at the top, left corner of the text string.
               Select  this  point  by  moving the  mouse  to  the  desired
               location and click  a button.  The second prompt  is for the
               scale of the text.  This number is the size of  the text.  A
               value of  0.25 will  create a string  with characters  every
               0.25  units.   The  third  prompt is  for  horizontal versus
               vertical text.  Answering yes  will draw the text horizontal
               and no will  draw the  string vertically.   The letters  are
               always upright, they are not rotated for vertical text.  The
               last prompt is for the text string itself.  This string will
               be displayed on  the drawing  itself.    When entering  text
               pressing  return  at the  end of  the  string will  draw the
               normal  text.  If the up-arrow cursor key is pressed instead
               of return, the text will be drawn with a line over it.  This
               is useful for digital systems when a signal is active low.

          Delete-Line:
                    This function is used to delete lines from the  current
               drawing area.  A  line will be highlighted  in red and  made
               dotted.   If this line  is to  be deleted press  Y for  yes.
               Another line will be  highlighted.  Pressing Y for  yes will
               delete that line  as well.   Other options for  keys are  to
               press N for no.  Saying no will move to the next line, or if
               no  other lines exist, will  exit the function.   Pressing B
               for back will back up to  the previous line.  This was added
               in  the  case  of   many  lines  on  the  screen   and  user
               inadvertently bypassed  the desired line.  ESC  will exit at
               any  time, leaving the current  line shown on  the screen in

                                                          PC-Trace Users Manual






                                                                         38

               the correct color.

          Delete-Circle/arc:
                    This function  is used to delete  circles/arcs from the
               current  drawing area.  A  circle/arc will be highlighted in
               red and made  dotted.  If this  circle/arc is to  be deleted
               press  Y for yes.   Another circle/arc  will be highlighted.
               Pressing Y  for yes  will  delete that  circle/arc as  well.
               Other options  for keys are  to press N  for no.   Saying no
               will  move   to  the  next   circle/arc,  or  if   no  other
               circles/arcs exist, will exit the function.   Pressing B for
               back  will back  up to  the previous  circle/arc.   This was
               added in the case of many circles/arcs on the screen and the
               user  inadvertently bypassed  the  desired circle/arc.   ESC
               will exit at any time,  leaving the current circle/arc shown
               on the screen in the correct color.

          Delete-Text:
                    This function is  used to delete text  from the current
               drawing area.  A text string will be highlighted  in red and
               made dotted.  If this text is to be deleted press Y for yes.
               Another text string will be highlighted.  Pressing Y for yes
               will  delete that text as well.   Other options for keys are
               to  press N for  no.  Saying  no will move  to the next text
               string,  or if no other text exists, will exit the function.
               Pressing B for back will back up to the previous text.  This
               was added in the case of many text strings on the screen and
               the user inadvertently bypassed the  desired text.  ESC will
               exit  at any  time, leaving  the current  text shown  on the
               screen in the correct color.

          Regenerate:
                    Selecting this function will redraw the current screen.
               SCAD sometimes creates a little  garbage on the screen  when
               adding and deleting lines.  This function will clean it up.

          Set Snap:
                    The Snap function  is used  to set  absolute units  and
               endpoints for drawing operations.  If the Snap  function has
               already been turned  on, selecting it again will  prompt the
               user  that it will now be turned  off.  If the Snap function
               is  currently off, a text entry dialogue box will appear and
               the snap  value will  be given.   Common values  are 0.1  or
               0.25.   Any value between 0  and 1 can be  entered and used.
               All subsequent usage of drawing commands will move endpoints
               of lines, arcs, circles and text to the grid points shown.

          Scale:
                    The  scale menu selection is used to change the size of
               the current symbol  uniformly across its  entire area.   The
               value  that  is  entered  when the  dialogue  box  opens  is
               multiplied by  the  dimensions of  all the  entities in  the
               symbol.   For example, if the  symbol was 1 unit  long and a
               scale factor of  0.5 was  entered, the final  length of  the

                                                          PC-Trace Users Manual




          

                                                                         39

               symbol  would be 0.5 units.  Pressing  ESC will exit with no
               changes.

          Shift Space:
                    The shift  space routine  will move the  entire drawing
               some  offset specified  by  entering a  starting and  ending
               point of a  line.  If a line  from 1,1 to 2,2 is  drawn, the
               entire drawing will be shifted 1 unit right and 1 unit down.
               To draw the line, when prompted, click on the starting point
               and ending point.   After the second click the  drawing will
               be shifted.  ESC will exit backwards or out of this routine.



          Extend/Trim:
                    This  function  allows a  line  to be  extended/trimmed
               to/by another line, or a circle to be extended/trimmed to/by
               a line, or  a line  to be extended/trimmed  to/by a  circle.
               This   function  is  useful   for  designing  symbols  whose
               intersection of  points aren't on convenient  dimensions.  A
               good example of this is the  OR gate.  The function works by
               first prompting  to see if the  object that will  be used to
               extend or trim with is a line  or a circle/arc.  Press L for
               line or  C for circle.   The software will now  use the same
               procedure as  is  used for  deleting objects  to select  the
               extend/trim edge.  Once it is selected it will be colored in
               Magenta.  The second  prompt is for the object  to extend or
               trim.   This  is the  object that  will have  its dimensions
               modified.  If  the trim object was a line,  the program will
               give the option of a line or a circle/arc to modify.  If the
               trim object was a  circle/arc the program will automatically
               select  the second object  to be a  line.  The  program will
               highlight each object in succession until the user picks the
               desired  object to modify.  The next  prompt is for the user
               to select a point, with the mouse, near the end point of the
               object to modify.  One more prompt exists if a circle is one
               of the affected  entities.  This  prompt is to pick  a point
               near  the projected intersection.  At the end of the prompts
               the entity will be modified as per the user instructions.  A
               regeneration may be required as well to clean up the screen.


               The tools that have been described above  should be adequate
          for drawing most objects.   Sometimes some creative usage  of the
          Snap function and Extend/Trim is required.

          Placing Components/Symbols:
               This function is used  to place symbols on the  main drawing
          area.   This area is separate  from the previous area  and has no
          limits in size  for practical use.   The only limiting  factor is
          the amount of available memory.
               When a set  of graphic symbols  are put  together to make  a
          meaningful  electrical symbol,  they  are grouped  as an  object.
          They can only be edited by choosing from the Components menu  the

                                                          PC-Trace Users Manual








                                                                         40

          Place Component command.  The Move, Delete, and other commands in
          the Entities section only affect the objects that have been drawn
          not using this menu selection.
               When Place Components is selected with the mouse or keyboard
          a  window  will appear  in  the  center of  the  screen.   If  no
          components  have been entered, only two choices will appear: N to
          exit or A to enter new symbols.  ESC will also exit the function.

          A-Enter new Components:
               This  function will clear the window and prompt for the name
          of the symbol that will be placed.  This name will not  appear on
          the  symbol itself and is used only  to tell the designer exactly
          what the part is.
               The  second prompt  if for  the part  designation.   This is
          later placed on  the name of the  part and is used  by PCTRACE to
          specify  autorouter connections.   This  designation need  not be
          unique  as it must be  in PCTRACE.   The reason for  this is that
          some parts, such as AND gates  like the 74LS08 have more than one
          part in them.   This allows  the user  to connect multiple  parts
          under  one  name.    No  automatic   provision  is  provided  for
          specifying  which part of the overall part is being connected to,
          other than the pin number.  The program will notify the user if a
          duplicate  designation  is  specified  to  verify  that  this  is
          desired.
               The  next prompt is a  filename for the  actual parts layout
          information.   This is the same  file as that used  by PCTRACE to
          specify  pad locations.  The  program will pop  up a small window
          with lists of names that  are available for use.  Enter  the name
          of the part without the extension and the program will display it
          on the screen  in a  small window.   Information  about the  part
          appears on the bottom  of the screen.   If it is correct  press Y
          for yes or click in the Yes box.   If it is not correct, click on
          the No  box or press N,  the program will reprompt  for the name.
          This entry is not significant  for drawing the schematic  itself,
          but is needed for export to PCTRACE.
               The next prompt  is for the Pad  size.  Enter 1  for 0.05, 2
          for 0.06, 3 for 0.07 and so forth.
               The last text prompt is for the name of the schematic symbol
          that will  be drawn on the  main drawing area.   The program will
          open a window showing a  list of valid diagram files.   Enter the
          diagram file with no extension and it will be drawn  to check for
          user approval.   Answering Y  will move to the  main drawing area
          for placement, and N  will go back  and reprompt for the  diagram
          file name.
               Once the diagram file has been selected the text window will
          disappear and two  crosshairs will be shown on the  screen.  This
          is  the size  of the  part that  has been  selected and  is being
          placed.  Moving the mouse to the desired location and  pressing a
          mouse  button will  anchor the  location of the  part.   The next

                                                          PC-Trace Users Manual








                                                                         41

          prompt  appears at  the bottom  of the  screen and  asks  for the
          location  of  the text.    The text  that  will be  drawn  is the
          designation  name  entered  earlier.   Remember  that  the  point
          selected is  the upper left corner of  the first character in the
          string.  The next prompt is for the  text scale and is the actual
          size, in units,  of the characters that will be  drawn.  The last
          prompt is for horizontal text.  Answering Y for yes will draw the
          text  in  a horizontal  line  and N  for  no will  draw  the text
          vertically.
               At this point the user is prompted as to whether or not they
          want to enter another component.  Click on the appropriate space.
          Answering Y will start the process again, and N will put the user
          on the last  entered component and give other options  as well as
          display the current data.  At any point in the previous component
          entry routine, ESC will back the user up.

          From a Display of Component Data:
               Once a  component has  been entered various  editing options
          can be used on it.  Those options are discussed below:
          E - Edit Component:
               This will allow the user to change things such as the  name,
          designation, pad  size, actual part layout  filename, location of
          the  diagram, orientation of the diagram, and the location of the
          text that is associated with this component.  The letters that do
          each of these are discussed below:

          A-Name:   This  will prompt for a new name, enter the new name or
                    press ESC to leave it unchanged.

          B-Designation: This will prompt for a new designation name, enter
                         the name or ESC to exit.

          C-Definition:  This will  prompt for  a new component  pad layout
                         definition.  Enter the new file or ESC to exit.

          D-Pad Size:    This will  open a window with  three different pad
                         sizes.  Enter the desired value.

          E-Move Comp:   This  will  allow the  user  to  move the  current
                         symbol  to a  new location.   The  crosshairs will
                         appear and mouse will move them.  Click the button
                         on the  location for the  new location.   ESC will
                         exit.

          F-Rotate: This function will rotate all  elements associated with
                    this  component.  The device can be rotated 90, 180, or
                    270 degrees  counter-clockwise.   It  may require  some
                    movement of text to make everything look right.


                                                          PC-Trace Users Manual








                                                                         42

          G-Move Text:   This function allows the  user to first select the
                         text,  using  the previously  mentioned  method or
                         moving forward, backward,  and selecting.   A  box
                         appears  that is the  outline of the  text.  Using
                         the mouse,  move the text to  the desired location
                         and click a  mouse button.  The  new text location
                         will now be at this point.

          H-Exit Edit:   Selecting H, will exit the edit function.

          A-Enter new Components:
               This function  allows entry of  more components  and is  the
          same routine that was discussed at the beginning of this section.

          Delete:
               This function will allow deletion  of the component that  is
          currently on screen.  The entire component can be deleted or just
          the text.  Enter the  number that is desired.  An entry of 3 will
          exit  with  no  deletions taking  place.    If  the component  is
          deleted, all associated connections will be deleted as well.

          Search:
               This will allow the user to search from the current location
          to the end  of the list of components.   Only the Designation can
          be searched on.  Follow the prompts to do either.

          + - Next:
               Pressing  the + key will  display the next  component on the
          screen.   If at  the  end of  the list,  the  first component  is
          displayed.

          - - Previous:
               Pressing  the - key will  display the next  component on the
          screen.  If that the beginning of the list, the last component is
          displayed.



          Text Entry:
               This  function allows text entry  that can be  placed on the
          main drawing area.  This text will be linked in  to the component
          that is currently displayed.  This text entry should only be used
          for text that is associated  with the component.  It can  only be
          modified  from this component.  More general text entry should be
          done from the  Entities menu  while running in  the main  drawing
          area.



                                                          PC-Trace Users Manual





                                                                         43

          N to End Component Entry and Editing:
               N or ESC will move the user  back to main drawing area.  All
          work will be held in memory.

          Connection Entry:
               Only one choice  exists from the Nconnections menu  and that
          is to make  connections between existing  components.  The  input
          routine was created to  minimize the amount of time  spent typing
          and  maximize  the  ease  with which  connections  are  drawn and
          recorded.  When the selection is executed it automatically starts
          entry of a new connection.
               The  first prompt  is  to pick  a  point inside  the  source
          component.  The  crosshair will  show on the  screen under  mouse
          control.  Place the crosshair in the "bounding box" of the source
          component  and click a button.  When prompted for the destination
          component  do the same  thing.   This will  tell the  program the
          source and destination components.
               The  next step is to tell the program the source pin number.
          Enter it at  the bottom of the  screen when prompted.  The second
          step is  to use the  mouse to specify  the starting point  of the
          number just entered.  The third step is to enter the scale of the
          pin number.  The destination pin number is done  exactly the same
          was as the source pin.
               The  source  and destination  pin  number  that are  entered
          during this process will  be normal text.  The source number will
          become  part of  the  source component  object  and will  not  be
          editable from  the main drawing area.  It will be necessary to go
          into the Place Components section to edit or move the  text.  One
          reason for this is to move  the pin numbers or change the letters
          to  have an  overline.   The  same is  true  for the  destination
          number, it will be attached to the destination component.
               After  both the source and destination  have been entered, a
          dialogue   box  appears  to   show  the  user   that  source  and
          destinations that  have  been  chosen.   If  the  information  is
          incorrect click  on the No box  or press N,  the connection entry
          will be  restarted at the beginning.  If yes is selected the line
          draw  routine will started and  the user can  draw the connection
          with as many  straight lines as desired.  The  e key for endpoint
          and  right mouse  buttons are  active for  finding endpoints  and
          making  connection dots.  The lines drawn will be attached to the
          current connection object.  Deleting this object will  remove the
          lines that are associated  with this connection.  The  only other
          difference between  connections and components is  that the lines
          drawn in  a connection can  be edited in  the main  drawing area.
          After the last  line has been entered, pressing  ESC will end the
          line drawing routine.   After pressing  ESC, the program  prompts
          asks  if the  user  wants to  enter  another connection  or  not.
          Answer  yes   to  restart  this  procedure   and  create  another
          connection.    No will  put the  user  at the  connection editing
          facilities.


                                                          PC-Trace Users Manual








                                                                         44

          Connection List Menus:
               Several  options are available from  this point.   A list of
          commands is shown as the last line in the window.      The   edit
          command  allows the  user to  change  the source  and destination
          names and pin numbers.  Changing this information will not change
          the  graphic  data  that was  entered.    To  change the  graphic
          representation of the number that are on the drawing will require
          finding the component that they are associated with.
               A)enter  new  will  allow  entry of  other  connections  are
          described above.
               Delete will delete the listed connection  and the lines that
          are associated with it.
               Search  will prompt for  a designation name  and search from
          the current location to the end of all connections for a matching
          source or destination designation.
               '+' and  '-'  move to  next  or previous  connection  entry.
          These keys  loop from start to  end or end to  start depending on
          the key.
               Line will allow the user to draw  lines in addition to those
          that were drawn during the initial connection entry.  These lines
          are drawn the same as during connection entry.  ESC will exit the
          line drawing routine.
               N for end or ESC will exit  this menu and return the user to
          the main drawing area.

          Drawing Entities:

          Draw-Line:
                    This function is  used to  draw lines  within the  main
               drawing area.  At the bottom of the screen, SCAD will prompt
               the  user as  to  what the  program  expects.   The  current
               coordinates  are  shown at  the  bottom right.    Select the
               location of the  starting point  of the line  and click  the
               left  or right button.  Clicking the left button will anchor
               the  start  of  the  line  at  the  current  mouse location.
               Clicking the right button will anchor the start point at the
               current  point, plus it will  draw a connection  dot at this
               point.   The  dot will  not appear until  the start  and end
               points  of the line have been specified.  After clicking the
               left  or right button, the  program will prompt  for the end
               point.  Click either the right or  left button.  The buttons
               have  the  same effect  as  when  picking the  start  point.
               Another option for selecting the  desired point is to  press
               'E' while  the program is asking for the start or end point.
               Pressing  'E' at  this time  will draw  a small  box  on the
               screen.  Placing this box at or near the endpoint of another
               line will select  the exact  endpoint of that  line or  arc.
               The  mouse buttons have the  same effect.   This function is
               active much of time when in the main drawing area and should

                                                          PC-Trace Users Manual








                                                                         45

               be tested whenever it is  needed.  ESC will exit or  back up
               while drawing lines.   To draw another line, select  a start
               and  end point  again.   This  function  will continue  this
               sequence until ESC is pressed to exit it.

          Draw-Arc:
                    This function  is used to draw an arc of some size.  It
               can  be used to draw any length  arc from any start point to
               any end point and at any  diameter.  The first prompt is for
               the  center  point  of the  arc.   Move  the  mouse  to this
               location and click a button.   The second prompt is  for the
               radius of the arc.   Move the pointer  to the location  that
               shows  the desired radius.  A floating line reminds the user
               as  to the current length.  The  next point is for the start
               of the arc.  Pick this point  as before.  The last prompt is
               for  the arc ending  point.  Click  on this point.   The arc
               will  be drawn  from the  angle of  the start point,  at the
               selected radius,  counter-clockwise, to the end  angle.  ESC
               will back up at any time to the previous prompt or will exit
               the  function.   To  draw  another arc,  pick  this function
               again.

          Draw-Circle:
                    This function draws  a circle at some  center point and
               some radius.  When prompted, pick the center point and click
               a mouse button.  The second prompt is for the  radius of the
               circle.  Click on this point and the circle will be drawn on
               the screen.  ESC will back up to the previous prompt or exit
               the function.   To draw another  circle, pick this  function
               again.

          Draw-Text:
                    This  function is used place  text on the  screen.  The
               first prompt is for the  scale of the text.  This  number is
               the size  of the text.  A value of 0.25 will create a string
               with  characters every 0.25 units.  The second prompt is for
               horizontal versus  vertical text.   Answering yes  will draw
               the text horizontal and no will  draw the string vertically.
               The letters  are always upright,  they are  not rotated  for
               vertical  text.   The third  prompt is  for the  text string
               itself.   This  string  will be  displayed  on  the  drawing
               itself.  The last prompt is for the starting location of the
               text.   This point is located at the top, left corner of the
               text string.  Select this  point by moving the mouse  to the
               desired  location and  click a  button.  When  entering text
               pressing  return  at the  end of  the  string will  draw the
               normal  text.  If the up-arrow cursor key is pressed instead
               of return, the text will be drawn with a line over it.  This
               is useful for digital systems when a signal is active low.

                                                          PC-Trace Users Manual








                                                                         46

          Move-Line:
                    The move line  is used  to change the  placement of  an
               existing line.   When this  selection is  made, the  program
               will highlight  lines in succession until  the user responds
               with a Y for yes.   At this point the user will be  asked to
               select, with the  mouse, a base point of movement.  Click on
               that point. E is active to  select the endpoint of the line,
               or  any other, for movement.   After the  basepoint has been
               selected and  the mouse button clicked, the entire line will
               move with the  movement of the mouse.   Position the line at
               the desired location and click a button to permanently place
               the line.  E is active to select an endpoint.  ESC will back
               up or exit the function.

          Move-Circle/Arc:
                    The  move circle/arc  function  is used  to change  the
               placement of an existing circle/arc.  When this selection is
               made,  the  program  will  highlight  circles  and  arcs  in
               succession until the  user responds with  a Y  for yes.   At
               this point the user will be asked to select, with the mouse,
               a base point of movement.   Click on that point. E is active
               to  select  the  endpoint of  the  arc,  or  any other,  for
               movement.   After the  basepoint has  been selected and  the
               mouse button  clicked, the entire circle/arc  will move with
               the movement of the  mouse.  Position the circle/arc  at the
               desired position and click a button to permanently place the
               circle/arc.   E  is active  to select an  endpoint.   ESC is
               active to back up or exit the function.

          Move-Text:
                    The  move text function is used to change the placement
               of  an existing text string.   When this  selection is made,
               the program will highlight  text strings in succession until
               the user responds with a Y for yes.  At  this point the user
               will be  asked to select,  with the  mouse, a base  point of
               movement.   After  the basepoint  has been selected  and the
               mouse button clicked, a box  representing the text will move
               with  the movement of the  mouse.  Position  the text box at
               the desired position and click a button to permanently place
               the text.  E is active to select an endpoint.  ESC is active
               to back up or exit the function.

          Delete-Line:
                    This  function is  used to delete  lines from  the main
               drawing area.  A  line will be highlighted  in red and  made
               dotted.   If this line  is to  be deleted press  Y for  yes.
               Another line will be  highlighted.  Pressing Y for  yes will
               delete that line  as well.   Other options for  keys are  to
               press N for no.  Saying no will move to the next line, or if

                                                          PC-Trace Users Manual








                                                                         47

               no  other lines exist, will  exit the function.   Pressing B
               for back will back up to the previous line.   This was added
               in  the  case  of   many  lines  on  the  screen   and  user
               inadvertently bypassed the  desired line.  ESC will  exit at
               any  time, leaving the current  line shown on  the screen in
               the correct color.

          Delete-Circle/arc:
                    This function  is used to delete  circles/arcs from the
               current drawing area.   A circle/arc will  be highlighted in
               red and  made dotted.  If  this circle/arc is  to be deleted
               press Y  for yes.   Another circle/arc will  be highlighted.
               Pressing  Y for  yes will  delete  that circle/arc  as well.
               Other options for  keys are to  press N for  no.  Saying  no
               will  move   to  the  next   circle/arc,  or  if   no  other
               circles/arcs exist, will exit the function.   Pressing B for
               back  will back  up to  the previous  circle/arc.   This was
               added in the case of many circles/arcs on the screen and the
               user inadvertently  bypassed  the desired  circle/arc.   ESC
               will exit at any time, leaving  the current circle/arc shown
               on the screen in the correct color.

          Delete-Text:
                    This function is  used to delete text  from the current
               drawing area.  A text string will be  highlighted in red and
               made dotted.  If this text is to be deleted press Y for yes.
               Another text string will be highlighted.  Pressing Y for yes
               will delete that text as well.   Other options for keys  are
               to press N  for no.   Saying no will  move to the next  text
               string,  or if no other text exists, will exit the function.
               Pressing B for back will back up to the previous text.  This
               was added in the case of many text strings on the screen and
               the user inadvertently bypassed the  desired text.  ESC will
               exit  at any  time, leaving  the current  text shown  on the
               screen in the correct color.

          Regenerate:
                    Selecting this function will redraw the current screen.
               SCAD  sometimes creates a little garbage  on the screen when
               adding and deleting lines.  This function will clean it up.


          Set Snap:
                    The  Snap function  is used to  set absolute  units and
               endpoints for  drawing operations.  If the Snap function has
               already been turned  on, selecting it again  will prompt the
               user  that it will now be turned  off.  If the Snap function
               is  currently off, a text entry dialogue box will appear and
               the  snap value  will be  given.  Common  values are  0.1 or

                                                          PC-Trace Users Manual








                                                                         48

               0.25.   Any value between 0  and 1 can be  entered and used.
               All subsequent usage of drawing commands will move endpoints
               of lines, arcs, circles and text to the grid points shown.

          Zoom In:
                    This function requires the  use of the mouse to  pick a
               bounding box for an area  to zoom in on.  Click the mouse on
               one corner of the area to zoom in on and  click the mouse on
               the opposite corner.  SCAD will show the boxed  in region on
               screen  as  the full  screen  while  maintaining the  aspect
               ratio.

          Zoom Out:
                    The Zoom out  function prompts for  a zoom out  factor.
               Enter a value.   A value of 2, for  example, will double the
               area  being viewed.  A  value of three  will triple the area
               and so forth.

          Zoom Total:
                    The Zoom Total will zoom out so that all of the drawing
               is shown on  the screen.   This function  finds the  overall
               size   of  the   drawing  and   adjusts  the   viewing  area
               accordingly.

          Shift Space:
                    The shift  space routine  will move the  entire drawing
               some  offset specified  by  entering a  starting and  ending
               point of a  line.  If a line  from 1,1 to 2,2 is  drawn, the
               entire drawing will be shifted 1 unit right and 1 unit down.
               To draw the line, when prompted, click on the starting point
               and ending point.   After the second click the  drawing will
               be shifted.  ESC will exit backwards or out of this routine.

          Extend/Trim:
                    This  function allows  a  line to  be  extended/trimmed
               to/by another line, or a circle to be extended/trimmed to/by
               a line, or  a line  to be extended/trimmed  to/by a  circle.
               This  function  is   useful  for  designing  symbols   whose
               intersection of  points aren't on convenient  dimensions.  A
               good example  of this is the OR gate.  The function works by
               first prompting to  see if the object  that will be used  to
               extend or trim with is a line or a circle/arc.   Press L for
               line or  C for circle.   The software will now  use the same
               procedure as  is used  for  deleting objects  to select  the
               extend/trim edge.  Once it is selected it will be colored in
               Magenta.  The  second prompt is for the object  to extend or
               trim.   This  is the  object that  will have  its dimensions
               modified.  If  the trim  object was line,  the program  will
               give the option of a line or a circle/arc to modify.  If the

                                                          PC-Trace Users Manual








                                                                         49

               trim object was a  circle/arc the program will automatically
               select the  second object to  be a  line.  The  program will
               highlight each object in succession until the user picks the
               desired object  to modify.  The next  prompt is for the user
               to select a point, with the mouse, near the end point of the
               object to modify.  One more prompt exists if a circle is one
               of the  affected entities.  This  prompt is to pick  a point
               near  the projected intersection.  At the end of the prompts
               the entity will be modified as per the user instructions.  A
               regeneration may be required as well to clean up the screen.


                                  Keyboard Summaries
                                       for SCAD



          When Entering Text on the schematic:

          RETURN         - enters the text normally
          Cursor Up Arrow - overlines the text

          When drawing points, lines, arcs, and text:

          E         - gives user box to find endpoints
          R. Mouse Button - puts connection dot on point of line
























                                                          PC-Trace Users Manual








                                                                         50

                                     Conclusion:

               The PCTRACE circuit design system was written by Doug Ehlers

          for use  by himself.   This  was  done without  ever having  used

          another design package.   The  decisions made were  chosen to  be

          intuitive  to   the  author.    The  program  is  under  constant

          refinement,  so the user should try and maintain contact with the

          author through  one of the previously  mentioned support methods.

          As always the author is interested in user input on the software.

          The program has evolved as it  has through the input and  support

          of its users.  In the words of a famous gentleman (almost) "Thank

          you for your support."





























                                                          PC-Trace Users Manual

































                                      Appendix A

                                   .NLT File Format








          The  file created by the export function  of SCAD and read by the
          import  function of  PC-TRACE  can be  used  as a  mechanism  for
          importing  netlists from other CAD software.  It is currently not
          feasible  for the author to  offer this support.   If conversions
          are written by users, they are encouraged to  let the author know
          so that they  can be shared by  other users.  The ->  signifies a
          line in the file.  The following is the file format:

          ->Number of Components in list

          Each component looks like:

          ->Name of component           15 characters
          ->Component Designation        5 characters
          ->Definition file name        12 characters
          ->Pincount  & Padsize          2 Integers with 2 spaces between

          Pincount is an integer signifying the number of pins in the file.
          The  Padsize is a 3 bit  number in the 5th, 6th,  and 7th bits of
          the number.  0  is 0.05, 1 (=32) is  0.06, and 2 (=64) is  a 0.07
          inch diameter pad.   The  lower five  bits of  Padsize should  be
          zero.   The bit 0 signifies  if the component has  been placed on
          the board yet.


          ->Number of Connections in list

          Each Connection looks like:

          ->Source Designation          5 characters
          ->Source Pin Number           Integer
          ->Destination Designation     5 characters
          ->Destination Pin Number      Integer