ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                º                                      º
                º               R8 Tuner               º
                º           Drake R8 to IBM            º
                º       Tuner Interface Program        º
                º                                      º
                º                                      º
                º                                      º
                º                                      º
                º             Version 2.0              º
                º Copyright (c) 1992 by Mike Musielski º
                ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼






Requirements:


        -IBM 286 compatible computer or higher running DOS
         3.3 or higher.

        -COM1, 2, 3 or 4 available. This version makes
         provision for adjusting the port to be used. Cable length is to
         your preference and should be dependant on the amount of RF
         coming off you computer.

        -DRAKE R8 Receiver obviously.





Files Included in this package:

                   * R8_TUNER.EXE
                   * R8INIT.IN1
                     MEMLOADR.EXE
                   * QSL.LOG
                     R8_BBC.DAT
                     R8_SPAIN.DAT
                     R8_SRI.DAT
                     R8_RFI.DAT
                     R8_NEDR.DAT
                     R8_SWED.DAT

*Both the above files must be in the same directory. The others needn't but it is
recommended.



Disclaimer:
        R8_Tuner is provided AS IS. The author specifically disclaims
        any and all warrantees, expressed or implied, including fitness
        for a particular purpose. Use this product at you own risk.
        This software is copyrighted by the author and all rights are
        reserved. The Drake R8 is manufactured by the R.L. Drake Company
        of Miamisburg. Ohio. The author of this software is not affiliated
        with the R.L. Drake Company and does not claim to be representing
        the interests of that company.

Registration:
        This product is intended as shareware (user supported
        software). This concept means you can evaluate the
        program on your own machine and determine if you want
        to purchase it. It is not free software and it is not
        in the public domain.  You may distribute
        it freely. But we ask that you also distribute this readme
        file with it when you do. If you find that it meets your
        needs and would like to purchase this software and be placed
        on our mailing list a donation to the project of $35.00 sent
        to the author whose address is discretely provided below is
        requested.

        It is our intention to upgrade this product in the future
        with a mouse driven interface, complete simple to use
        Database manipulation, Multi-event timer and automated file
        inport-export capabilities. This will be available only to registered users.

        If you have any questions regarding this product or suggestions
        about the future product, please contact the author at:

                       Compuserve -71600,614
                       U.S. Mail  -Mike Musielski
                       16 Academy Rd.
                       Madison, N.J.
                             07940






                            R8_TUNER  Ver2.0









File Descriptions:
R8_TUNER.EXE  -This is the main program. This is a standalone,
               full screen, menu driven, front-end driver for the
               Drake R8 communications receiver. Once initiated
               the program is designed to take-over as the radio's
               front panel for all operations except analog inputs
               such as volume control, notch adjustment and passband
               offset tuning. The program can be suspended revoking
               front panel control back to the radio for such
               operations as timer (to be implimented in a future
               version), scan operation (also to be implemented
               later) and minor adjustments to tweek in a DX signal.

R8INIT.IN1    -must be present in the same directory as R8_TUNER.EXE,
               if it is not, the program will automatically select COM1.
               Use ALT-C to change to the desired COM port.
               If it is necessary to scroll past COM4 and return to
               COM1, COM2 or COM3 the correct procedure is to scroll
               to the desired COM port then press ALT-S to suspend
               the program and then reset the COM port by pressing
               the SPACEBAR to resume the program.

QSL.LOG       -This file is a straight ascii text file created
               by the R8_TUNER.EXE program. The file is created
               (if not already present in the same directory) or
               appended whenever ALT-D is selected in the
               R8_TUNER.EXE program. The formating of the text
               appears below.
ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º                     R8 listing format for QSL.LOG                         º
ÇÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÂÄÄÂÄÄÄÄÄÄÄÄÄÄÂÄÂÄÂÄÂÄÂÄÄÄÂÄÂÄÂÄÂÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄº
º         ³        ³M ³          ³ ³ ³ ³ ³   ³ ³ ³ ³ ³                      º
º         ³        ³E ³          ³ ³ ³ ³ ³   ³ ³ ³N³ ³                      º
º         ³        ³M ³   F      ³ ³ ³ ³ ³   ³M³ ³O³S³                      º
º         ³        ³  ³   R      ³V³A³ ³A³   ³O³ ³T³Y³                      º
º         ³        ³C ³   E      ³F³N³R³G³   ³D³N³C³N³                      º
º  DATE   ³  TIME  ³H ³   Q      ³O³T³F³C³BW ³E³B³H³C³ PRGM NOTES           º
ÈÍÍÍÍÍÍÍÍÍØÍÍÍÍÍÍÍÍØÍÍØÍÍÍÍÍÍÍÍÍÍØÍØÍØÍØÍØÍÍÍØÍØÍØÍØÍØÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
12-23-1991³16:44:48³14³ 15.26000*³B³2³P³O³6.0³A³O³O³F³bbcnews program
12-23-1991³17:12:41³28³ 11.62000*³A³1³A³S³4.0³C³F³F³O³SRI to n. euro-dateline
12-23-1991³18:33:30³99³ 17.08000*³B³2³O³F³2.3³L³O³O³F³
ÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÁÄÄÁÄÄÄÄÄÄÄÄÄÄÁÄÁÄÁÄÁÄÁÄÄÄÁÄÁÄÁÄÁÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
  Whenever Alt-D is pressed you will be prompted for a note to add to the
  end of the current radios settings in the output log. After adding your
  note, pressing ENTER will add, or create and add, the complete radio setup
  and your note to the file QSL.LOG. TIP: Rename this file with a unique
  name after each days sessions and build a database. More on this later.







MEMLOADR.EXE  -Is a stand alone program. When initiated, you are prompted
               for a filename to load. This file is a straight ASCII text
               file formatted exactly like the output file from R8_TUNER.
               It will be search for a + sign immediately following the
               second memory channel number. Any listings with this
               charecter in this exact position will be loaded into the
               radio's memory. The program first scans the input file
               for this designator. Loads all such marked listings into
               a buffer and counts them. If it finds exactly 100 it will
               load the radio's memory channels sequentially. If there are
               less than 100 listings marked, the program will provide you
               with the number marked, prompting for which radio channel
               to start the sequentially load from. If you inadvertantly
               give it a number which when added to the marked listing
               count totals more than 100 the program will abort.
               (The radio's first memory channel is 00 not 1.)


               The listings marked R8_XXX.DAT are files which can
               be used with MEMLOADR.EXE. They contain a basic radio
               setup and all of the frequencies listed in the World
               Radio and TV Handbook for 1992 for the various
               stations. SRI is Swiss Radio International,
               NEDR is Radio Nederland, RFI is Radio France International,
               the BBC is of course the BBC and the rest are self
               explanitory. A simple text editor such as QEDIT,
               MULTIEDIT or even EDLIN can be used to modify these
               files directly. Be sure to overtype and not insert.
               It is VERY import that the data's positioning on the
               line remain as is.
               There should be no space before the start of the
               first date number. One space between date and time,
               time and memory channel, vfo and ant, ant and rf,
               rf and agc, agc and bw, bw and mode, mode and nb,
               nb and notch, notch and sync, sync and notes as
               illustrated in the above example. This sounds
               more difficult than it is. Actually use the
               overtype mode and Replace the choices with the
               new ones or in the case of making a selection
               place a + immediately following the second number
               of the memory channel. Make sure nothing moves on
               that line when you do and save the file as a pure
               text file. Once saved, from the dos prompt type
               MEMLOADR and press ENTER the program will ask
               for a filename and enter it just as you would
               from the dos prompt, path and all. Just make
               sure you do not overrun the highlighted box.















THE FOLLOWING CHOICES ARE AVAILABLE FOR EACH FIELD
ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
MEM CH:   At this time and for the purposes of memory channel loading
          this field has no meaning but must be a 2 place number.
          (I.E. 01 and not just  1). A plus sign immediately following
          the second memory channel number is used as a selector symbol
          by the program memloadr.exe to stuff it to the radio.

FREQ.:    This can be changed but not its postion on the line. There
          should always be two spaces between the last memory channel
          number and the first number of the frequency. (One if a plus
          sign is present and the frequency is above 10 MHz.)
          If the frequency is less than 10 MHz a third space or a zero
          can be used. It is important that the number be carried out
          to five decimal places followed by either two spaces or an
          asterisc and a space.

VFO:    A or B.

ANT:    1 or 2.

RF:     O(off), P(preamp) or A(attn).

AGC:    O(off), S(slow) or F(fast).

BW :    6.0, 4.0, 2.3, 1.8 or 0.5 (The decimal point is required)

MODE:   A(am), F(fm), C(cw), R(rtty), L(lsb) or U(usb).

NB:     O(off), N(narrow) or W(wide).

Notch:  F(off) or O(on) (sorry but with two positions... well it was late)

Synch:  F(off) or O(on).

Notes:  This field is just for your notes.
(When finished press a return and start on a new line. There
can be no blank lines in the file.)










ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º                     R8TUNER.EXE OPERATION MANUAL                            º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

         To START:  -the program type R8_TUNER and hit carriage return.
         To END:    -exit program press ALT-X.

        When the program starts, it looks for the file R8INIT.IN1. Not
        finding this file in the current directory will cause the screen
        to loadup with garble. To correct this hold down the ALT key while
        pressing the letter C (ALT-C). Then press ALT-X to exit the program.
        Which will create the file. Then restart the program. Pressing ALT-C
        will scroll through the four available COM ports. Stop when the
        correct port for your installation is displayed in the lower left
        portion of the base screen.

        Assuming you are now on the base screen with the correct COM port
        displayed in the lower left portion, pressing any highlighted key
        will open that menu. All the radio's functions can be controlled
        in this manner except certain scan functions. The menus can
        all be exited by pressing the escape key. The time and date displayed are    
        whichever your computor is set for (Local or GMT).


FUNCTIONS:
        F   -Opens the frequency window and prompts for the frequency
             desired. Enter only numbers in memgahertz. No period.
             (I.E. 9.500 should be entered: 09500 or 0950000)
             The number can be corrected by using the arrow keys or
             the backspace key and reentering the number. Pressing
             ENTER or RETURN stuffs the selected frequency to the radio.

        R   -Opens the power menu. Select either O for on or F for OFF.
             In all two selection menus the above will hold true.

        M   -Opens the mode menu. Selections can be made by by pressing
             just the highlighted letter (changing the radio immediately).
             Or using the arrow keys (which waits for you to press RETURN
             or ENTER before executing the command)
            -Pressing ESC exits from this menu returning you to the base
             screen with updated information.

        W   -Opens the Bandwidth menu. Selections can be made the same way
             as in the mode menu. Press ESC to exit.

        G   -Opens the AGC menu. Selections can be made the same way as in
             the mode menu. Press ESC to exit.

        P   -Opens the RF menu. Selections can be made the same way as in
             the mode menu. Press ESC to exit.

        B   -Opens the Noise Blanker menu. Selections can be made the same
             as in the mode menu.

                                --cont--



        V   -Opens the VFO menu. Selections can be made the same
             as in the mode menu.

        A   -Opens the Antenna menu. Selections can be made the same
             as in the mode menu.

        S   -Whenever this is pressed the frequency step size will be
             immediately changed.
             (I.E. if the Frequency displayed on the radio is 15.07000
                   pressing this will change the display to 15.0700
                   pressing again will change the display to 15.070)

        N   -Opens the Notch menu. Selections can be made the same
             as in the mode menu.

        Y   -Pressing this will immediately turn on the Synchro feature
             on the radio.

ALT FUNCTIONS:
        F1     -Help file.

        ALT-C  -Changes the com port selected. Displays the current
                choice in the lower left portion of the screen. Pressing
                ALT-S to suspend the program operation and then pressing
                the SPACEBAR to resume the program's control will usually
                re-establish the link using the newly selected COM port.
                If this doesn't work use ALT-X to exit the program and
                re-enter the program normally.

        ALT-M  -Puts you into memory mode allowing for scrolling
                through all the current memory channels. The use of
                U or the up arrow key increments the memory channel
                on the radio. The use of D or the down arrow will
                decrement the memory channel on the radio. Pressing
                the letter G while in this mode will prompt for which
                channel to GO to directly upon the pressing of the
                Enter or Return key.

        ALT-D  -Opens a prompt window asking for any notes
                pertaining to the current radio setup or program
                being listened to before saving the record to the
                file QSL.LOG. If QSL.LOG does not exist it will be
                created in the current directory.

        ALT-L  -Will open a prompt window asking for the channel you
                would like to load the current radio setup into.

        ALT-S  -Will suspend the program allowing you to manually
                tweek the radio. After you are finished pressing the
                spacebar will resume the program and refresh the
                screen with the current radio information.

        ALT-X  -Exits the program and closes all open files and ports.









ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
º                     MEMLOADR.EXE Program Manual                             º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

Discription:
        This is a stand alone program designed to allow the radio's
        memory channels to be automatically loaded from an input file
        provided by the user. It will prompt for the path and filename.
        Unpredictable results may occur if the maximum length is exceeded.
        If the file requested is not present, the program will terminate
        normally with the message:
                       Cannot open the file
                     PROGRAM ABORTED NORMALLY

        If the file is present but more than 500 lines the program will
        terminate normally with the message:
         PROGRAM TERMINATED DUE TO MEM_CH.DTA HAVING MORE THAN 500 LINES

        If the file has less than 500 lines the file will be loaded and
        checked. If a + sign is present next to the memory channel number
        the line will be prepared for loading into the radio. A counter
        will keep track of the number of selections. If the number is the
        maximum the receiver can handle, (100 selections), the program will
        automatically load the radio beginning with channel number 00 and
        continue until all 100 channels have been loaded. While the
        loading is in progress you will be reminded by a flashing White
        on Red window reading:
                THE MEMORY CHANNELS ARE BEING LOADED
              Please wait until the radio stops updating
                  then PRESS ANY KEY TO CONTINUE

Example of correct input format:
12-23-1991 17:12:41 28+ 11.62000* A 1 A S 4.0 C F F O
(notes field is not read and is optional

        On the conclusion of reading the input file you will be prompted
        for where to start loading the memory channels on the radio.
        (Provided 100 channels were not selected). Enter the channel
        number. This will be the first channel loaded and the program
        will sequentially load the selected programs.

       If you inadvertantly provide a channel number which when added
       with the number of programs waiting to be loaded exceeds the
       100 channel maximum the program will abort normally with a
       window reading:
                              DATA OVERRUN
                        UNABLE TO LOAD CHANNELS





       TIPS:
        Use a ASCII text editor such as QEDIT or MULTIEDIT to edit
        the QSL.LOG file to keep just those programs likely to be
        loaded into memory and save the file under unique names.
        Such as all the frequencys and radio setups you use for
        the BBC could be save in a file named BBC.LOG then when you
        wanted to load the memorys with BBC frequencys just edit
        the file with an ASCII text editor of choice adding a + sign
        next to the memory channel number. Go to the end of the
        file and look at the line count for the file. Make sure this
        isn't larger than 500 lines. A separate file of channels and
        setups can be kept individually for all the frequencys and their
        associated radio setups in uniquely named files.
        When wanting these in memory just rename it to preserve the
        original files add the + signs for the active channels and
        load it. The program will prompt you for where to start the
        sequential load.

        Also rename qsl.log at the end of a day's sessions so each is
        a unique name. I.E.:
                 r8122391.log for the qsl.log for dec. 23, 1991