4/6/1989         3Com Corporation

Notes on use of DISK01.sys.
    
This version of disk01.sys is for use with 3+Open on 3Com 3S/400,
3S/401, 3S/402, and 386Upgrade. It is not to be used on generic PC
systems. This is an update to the 3+Open for 3S/400, version 1.0.

It allows the use of SWAP/MOVE options as selected in config.os2.
This is necessary if you are using SQL server products.  No other
functional changes have been made to this version of the driver.
There is no benefit to updating, unless support for SWAP/MOVE is
required.


Please note that the SWAP/MOVE option is NOT RECOMMENDED by 3COM when
running  OS/2 1.0  except when using SQL products. Specifically, it
is recommended that systems runnning 3+Open Name, 3+Open Mail, and
3+Open ICM should be run with SWAP/MOVE DISABLED. See the release
notes included in the 3+Open Products for more information on system
requirements.

Use:
     To install this driver, replace the existing copy of disk01.sys
on c:\ with this new version. It is recommended that the old version
be renamed and kept.