Alternate Multiplex Interrupt Specification Sample Programs
Public Domain 1992 Ralf Brown
Version 0.83
LastEdit: 5/2/92

------------------------------------------------------------------------

AMITSRS
	list currently-installed TSRs using the alternate multiplex interrupt

Usage:	AMITSRS
		list manufacturer, name, and description of each TSR

	AMITSRS <anything>
		verbose listing; adds a second line with TSR version
		and private entry point (if any)

------------------------------------------------------------------------

FASTMOUS
	convert slow (on some systems) mouse hardware reset call into
	mouse software reset call.

Usage:	FASTMOUS
		install FASTMOUS

	FASTMOUS R
		remove FASTMOUS from memory

Resident Size: 128 bytes

------------------------------------------------------------------------

NOLPT
	turn a parallel port into a bit bucket by making it appear to
	always be ready for output and ignoring any output calls.

Usage:	NOLPT n
		install NOLPT on LPTn

	NOLPT nU
		remove (uninstall) NOLPT from LPTn

Resident Size: 192/240 bytes (high/low)

------------------------------------------------------------------------

NOTE
	popup one-line note taker

Usage:	NOTE -Ifile
		install NOTE, using <file> as the notepad

	NOTE -R
		remove NOTE from memory

Note:	NOTE keeps the notepad file open as long as it remains
	resident, in order to reduce the size of the resident code and
	data.  The file is open in write-only deny-none mode, which
	allows other programs using the correct sharing modes (such as
	LIST.COM and 4DOS) to access the notepad.  Unfortunately,
	COMMAND.COM does *NOT* use any sharing modes, even in version
	5.0--two major releases after sharing modes were introduced.
	Thus you will get a sharing violation if you attempt to TYPE
	or COPY the notepad using COMMAND.COM while NOTE is loaded.

Resident Size: 1856 bytes

------------------------------------------------------------------------

POPUP
	request that a specified TSR pop itself up if it supports that
	operation

Usage:	POPUP <tsrname>

	POPUP <manufacturer> <tsrname>

Note:	both <manufacturer> and <tsrname> may be abbreviated; if more
	than one TSR matches, the matching TSRs will be listed.

------------------------------------------------------------------------

REMOVE
	remove one or more TSRs from memory

Usage:	REMOVE <tsrname>

	REMOVE <manufacturer> <tsrname>

Note:	both <manufacturer> and <tsrname> may be abbreviated; if more
	than one TSR matches, you will be prompted whether to remove
	all matching TSRs.

------------------------------------------------------------------------

SWITCHAR
	provide switch-character support which was removed from MSDOS 5.0

Usage:	SWITCHAR I
		install

	SWITCHAR R
		remove from memory

	SWITCHAR D
		disable switchar calls

	SWITCHAR E
		enable switchar calls

	SWITCHAR <x>
		set switch character to <x>

Resident Size: 224/288 bytes (high/low)

------------------------------------------------------------------------

VGABLANK
	VGA-specific screen blanker

Usage:	VGABLANK n
		install, setting blanking interval to <n> minutes
		or if already installed, change blanking time

	VGABLANK R
		remove from memory

Resident Size: 208 bytes

------------------------------------------------------------------------

	Ralf Brown
	School of Computer Science
	Carnegie Mellon University
	Pittsburgh, PA 15213-3890

	Ralf Brown 1:129/26.1
	ralf+@cs.cmu.edu