E P A S M

                               Microprocessor assembler
                                 for the Intel 8749H




























                                    Joseph L. Hora
                                   January 12, 1992
                                     Version  1.3





                      EPASM  Assembler     October 11, 1990




                                  Table of Contents

          I.  Introduction  . . . . . . . . . . . . . . . . . . . . . .   2

          II.  Loading EPASM on your system . . . . . . . . . . . . . .   4

          III.  Creating an assembly language program . . . . . . . . .   6

          IV.  EPASM assembler directives . . . . . . . . . . . . . . .   8
               Description of assembler directives  . . . . . . . . . .   8

          ; . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .   8
                    ORG . . . . . . . . . . . . . . . . . . . . . . . .   8
                    "label"   . . . . . . . . . . . . . . . . . . . . .   8
                    CONST   . . . . . . . . . . . . . . . . . . . . . .   9
                    INCLUDE   . . . . . . . . . . . . . . . . . . . .    10

          V.  MCS-48 command notes  . . . . . . . . . . . . . . . . .    12

          VI. Assembling your program . . . . . . . . . . . . . . . .    15
               command line options . . . . . . . . . . . . . . . . .    15
               Running EPASM  . . . . . . . . . . . . . . . . . . . .    16

          VII.  Error messages  . . . . . . . . . . . . . . . . . . .    18
               VII.1  Command, file, and DOS errors . . . . . . . . .    18
               VII.2  EPASM assembly errors . . . . . . . . . . . . .    19

          VIII.  Using the EPROM programming device . . . . . . . . .    22

          INVOICE . . . . . . . . . . . . . . . . . . . . . . . . . .    24





















                                          1





                      EPASM  Assembler     October 11, 1990





          I.  Introduction


          The EPASM program is a one-pass assembler that was written for
          the Intel 8749H EPROM as described in the Intel Microcontroller
          Handbook, using the MCS-48 instruction set.  This assembler can
          also be used for other chips using this instruction set (8748H
          EPROM, 8048AH/8049AH/8050AH ROM, and 8035AHL/8039AHL/8040AHL CPU)
          as far as their memory structures are similar to the 8749H EPROM. 
          This manual is not intended to be a reference for the MCS-48
          instruction set or the above mentioned devices.  Please refer to
          the Intel Microcontroller handbook for a complete description.

          The input to the EPASM program is a file containing "source code"
          which is the EPROM program.  This contains the MCS-48 command
          mnemonics, labels, assembler directives, and comments.  EPASM
          converts it into the machine code of the processor, the actual
          command numbers that will direct the processor to carry out the
          steps the programmer has specified.  This machine code is saved
          to a file which then must be transferred to the processor using a
          EPROM "burner" or programming device.

          The output of EPASM is an object code module file.  In this file
          are the encoded commands that were specified by the assembler
          language program.   This program was written to construct an
          ASCII file suitable for the PROMPRO 7 EPROM Programming Unit,
          made by Logical Devices, Inc.   The files have also been used to
          program EPROMs using the B&C Microsystems 1409 Universal (E)EPROM
          programmer.  However, the file can also be passed to many other
          EPROM programming devices that support the same format.  The file
          could also be converted by a program of your own to the proper
          format for your device.

          This program is distributed as shareware.  It may be freely
          distributed to others, as long as it is in the form of the
          archived .ZIP file which contains all the separate files
          necessary for EPASM, and the files are not modified in any way. 
          If you find this program useful, register your use of the program
          by sending $15 to


          Joseph Hora
          46-1063 Emepela Way, Unit D
          Kaneohe, HI  96744-3975


          When registering, you will receive the latest version of EPASM
          (without the annoying registration screen), a printed copy of the
          manual, and the source code for EPASM (written in Turbo Pascal

                                          2





                      EPASM  Assembler     October 11, 1990

          5.0).  You will also be notified when updates of the program
          occur in the future.  Questions and technical support can be
          obtained by mail at the above address, or by phone at (808) 956-
          9848 weekdays 8am-5pm HST.

          Your registration entitles you to use this software on a single
          computer and to make as many copies of this software as you wish
          for backup purposes.


          Note:  MCS-48 and the various chip names mentioned above and
          throughout this manual are registered trademarks of the Intel
          Corporation.  The EPASM program and associated files are
          copyright 1990-92 by Joseph Hora.








































                                          3





                      EPASM  Assembler     October 11, 1990




          II.  Loading EPASM on your system


          Before doing anything else with your distribution disk, make a
          backup copy first. 

          The approved EPASM release is archived using the PKZIP file
          archiving utilities, and is named "EPASM.ZIP" .  This includes
          the following files:

          EPASM.EXE  - the assembler program
          EPASM.DOC  - this document
          INSTR.SET  - the MCS-48 instruction set 
          SAMPLE.ASM - a sample assembly language program
          INVOICE.DOC - the registration form for EPASM

          To install the assembler, these files must be extracted and
          placed in a directory of your choice.  The following are
          instructions for various system options.


          Single floppy drive systems:

          First, make a backup of the distribution disk.  Place the
          original EPASM (source) disk in drive A: and type 

          diskcopy a: a:

          Wait until the computer is done reading the disk and asks you for
          the target disk.  Remove the original disk and place a blank disk
          in drive A:, then type <RETURN>.  

          If you have PKUNZIP and EPASM.ZIP on the same 360K or larger
          floppy disk with nothing else, there will be enough room to store
          all the original plus extracted files.  At the DOS prompt, type 

          pkunzip epasm

          and the files will be extracted to the default directory.



          Dual Floppy users:

          First, make a backup of the distribution disk.  Place the
          original EPASM (source) disk in drive A: and a blank formatted
          disk (target) in drive B: and type 

          diskcopy a: b:


                                          4





                      EPASM  Assembler     October 11, 1990

          Wait until the computer is done reading the disk and writing to
          the target disk.   

          You can make an EPASM disk by doing the following:  First, make
          sure you have PKUNZIP and EPASM on one disk, and place it in the
          A: drive.  Place a blank formatted disk in the B: drive and type
          "B:" to change default to that drive. Then type

          a:pkunzip a:epasm

          and the files will be extracted and written to the disk in the B:
          drive.


          Hard disk users:

          See the above instructions to backup your copy of EPASM before
          you install the program on your hard drive.

          Place the disk with the files EPASM.ZIP and PKUNZIP in the A:
          drive.  Make a subdirectory on your hard drive to place your
          EPASM files into, for example, type

          C:\>mkdir epasm 

          (Type the commands above that are after the >).  Change directory
          to that subdirectory

          C:\>cd epasm
          C:\EPASM>

          Then type 

          C:\EPASM>a:pkunzip a:epasm

          and the files will be extracted and written to the directory you
          are currently in on the hard drive.

















                                          5





                      EPASM  Assembler     October 11, 1990




          III.  Creating an assembly language program


          You must create the source code for EPASM in a text editor
          program.  This can be any program that allows you to save the
          file in "ASCII" or "DOS" format.  This means just text, with no
          page breaks, printer commands, formatting codes or commands
          specific to the word processing program.  For example, in
          WordPerfect, you can use the Ctrl-F5,1,1 command to save the
          document as a DOS text file.  

          EPASM will create various output files, based on the text file
          containing commands it is given and the command line options (see
          Chapter VI.)  These output files can be viewed using the "TYPE"
          command from the DOS command prompt.  The files can also be read
          into the word processing program and viewed in the same way the
          source code can.  This is most useful when the user is trying to
          track down errors in the source code.

          There are two element types in the program, assembler directives
          and MCS-48 commands.  Assembler directives are commands that are
          processed during the assembly by the EPASM assembler.  The second
          type are commands that are converted directly into machine code
          for the EPROM processor.  These two types are discussed in the
          following chapters.

          Below is a short excerpt from a sample program written for this
          assembler:



          ; 
          ; 
          ;       IDLE routine:  remain here until interrupted 
          ;
          IDLE    mov       R3,#80        ;select expander 0, disable chop
                  mov       a,#8F         ;address   "     " 
                  outl      P2,a          ;   "      "     " 
                  movd      P7,a          ;output slave idle state 
                  call      riff          ;reset interrupt-in-progress
                  jmp       IDLE          ;jump to IDLE 
          ; 
          ;   End of IDLE routine 
          ; 


          This short excerpt illustrates a number of characteristics of the
          source code.  First, the simplest command is the semicolon
          character ";", the comment command.  This simply instructs the
          assembler to ignore all the characters following that one on the

                                          6





                      EPASM  Assembler     October 11, 1990

          current line.  It can be used at the beginning of the line to
          designate the entire line as a comment, or it can be at the end
          of a valid command.  In the above example, it is used to space
          out the routine with blank lines, hold the title of the routine,
          and annotate each command line with a comment.  This is usually a
          good practice, since even a small assembly language program is
          difficult to follow without a few comments explaining the code,
          even for the person who wrote the program!  

          Note that there is a mix of uppercase and lower case characters
          in this example.  EPASM treats upper and lower case letters to be
          equal.  Therefore, the commands "mov" and "MOV" are treated in
          exactly the same way.

          The next assembler directive used is in the first non-comment
          line, the text "IDLE".  This is being used as a "label", or a
          marker designating that line or address in the program.  This
          allows the programmer to reference commands in the program
          without knowing the actual address of the command in the program
          memory.  Notice at the end of the routine there is a "jmp IDLE"
          command, which will cause the EPROM to loop back to the beginning
          of the routine when it runs the program.  The EPASM program
          determines the address of "IDLE" as it assembles the program.

          On the same line as the "IDLE" label is the MCS-48 command for
          the processor.  Note that these words are all separated by a
          number of spaces.  Any combinations of spaces and tabs may be
          used to separate the words of each line.  The spacing can be
          chosen arbitrarily to make the program easy to read.  In the
          above example, the first column is reserved for labels.  This
          makes the labels easy to see and therefore easier to follow the
          flow of the program.  The next two columns hold the command
          arguments, and the third column holds a comment for that line. 
          This is a fairly standard format for assembly language programs. 
          Another equally valid format would be to have the commands be in
          one column, as in the following:


          ; 
          ; 
          ;       IDLE routine:  remain here until interrupted 
          ;
          IDLE    mov R3,#80         ;select expander 0, disable chop
                  mov a,#8F          ;address   "     " 
                  outl P2,a          ;   "      "     " 
                  movd P7,a          ;output slave idle state 
                  call riff          ;reset interrupt-in-progress
                  jmp IDLE           ;jump to IDLE 
          ; 
          ;   End of IDLE routine 
          ; 



                                          7





                      EPASM  Assembler     October 11, 1990




          IV.  EPASM assembler directives


          This chapter describes the valid assembler directives for the
          EPASM program.  An assembler directive is a command that does not
          directly generate machine code in the output file, but affects
          the way EPASM compiles the program.   The following are the
          recognized assembler directives, and a description of each:

          ;        ORG       "label"       CONST     INCLUDE



          Description of assembler directives:



          ; 
               the comment character.  Directs EPASM to ignore all other   
               characters following this one on the same line.
           

          ORG  

               specifies the location  of the start of the program in the  
               processor's program memory.  The default location if this   
               directive is not used is zero.  The correct syntax is 

                ORG addr

               where "addr" is the desired starting address, in
               hexadecimal.


          "label"  

               any word more that three characters long and less than nine
               characters which is intended to mark a location in memory. 
               I have enclosed the word "label" in quotes, since there is
               no actual command that you invoke by typing "label", you
               simply use a word that is not a command and the assembler
               will interpret it as a label.  The label cannot be the same
               as another of the assembler directives (such as ORG or
               CONST), or be the same as one of the MCS-48 commands (such
               as MOV or JMP).  Note that since no upper and lower case
               distinctions are made, the label "IDLE" is treated the same
               as the label "idle".  

               When the label appears as the first element of a line, that
               equates the label with the memory position of that line. 

                                          8





                      EPASM  Assembler     October 11, 1990

               When the label appears in any other line after a valid MCS-
               48 command, that means that label is being referenced.  When
               the EPROM program is assembled, the address corresponding to
               the line where the label appears will be placed in that
               command.  The label can be defined only once, but referenced
               many times.  Below is a program excerpt where labels are
               used.  The routine checks the test pins of the 8749H
               processor and takes actions based on their state.  Notice
               the use of labels: the first label is "Main" which is
               referenced in a number of instructions.  Other labels allow
               control of the program flow based on the conditions
               encountered.


          Example IV.1

          Main     JT0 Stat1           ;If T0 set, goto Stat1 
                   JT1 Stat2           ;If not T0 and T1, go here  
                   Mov R1,#20          ;Neither T0 or T1, BankA<<<<
                   Jmp StatEnd         ;Exit Stat section 
          Stat1    JNT1 Stat3          ; 
                   Mov R1,#00          ;If T1 also set, then WAIT
                   Jmp Main 
          Stat3    Mov R1,#40          ;T0 and not T1, so Bank B<<<< 
                   Jmp StatEnd         ; 
          Stat2    Mov R1,#60          ;not T0 and T1, so Bank C<<<< 
          StatEnd  Mov A,R1            ;Get current base address 
                   XRL A,R2            ;Compare to last base address
                   JZ  TakDat          ;If same, go inc. counters 
                   MOV A,R1            ;Different bank this time
                   MOV R2,A            ;set "old" base address here 
                   IN  A,P1            ;set old port reading equal 
                   MOV R3,A            ;     to current one 
                   IN  A,P2            ;same for port 2 
                   MOV R4,A 
                   JMP Main            ;End of Main Program loop 


               The processor running this program would repeat the loop, 
               testing T1 and T2.  If the current base address as the last
               time, the program jumps to the line designated by the
               "StatEnd".



          CONST  

               This assembler directive is useful for equating hex
               constants with words.  It is exactly like defining a label
               that references a constant, not a memory location.  The
               syntax of the directive is
           
               CONST  name   value

                                          9





                      EPASM  Assembler     October 11, 1990

               For example, the program in example IV.1 above considers the
               memory as being divided up into 3 "banks": A, B, and C, at
               locations 20, 40, and 60 (hex).  Instead of the statements
               above which explicitly specify these memory locations, one
               could define constants to make this more readable.  If the
               following lines are included in the program file:

               ;
               ;        Constants     
               CONST    BankA    20        ;Bank A: 32-63 decimal
               CONST    BankB    40        ;Bank B: 64-95 decimal
               CONST    BankC    60        ;Bank C: 96-127 decimal
               ;        

                Then example IV.1 could be written as follows:


           Example IV.2

          Main     JT0 Stat1           ;If T0 set, goto Stat1 
                   JT1 Stat2           ;If not T0 and T1, go here  
                   Mov R1,#BankA       ;Neither T0 or T1, so Bank A<<<<
                   Jmp StatEnd         ;Exit Stat section 
          Stat1    JNT1 Stat3          ; 
                   Mov R1,#00          ;If T1 also set, then WAIT
                   Jmp Main 
          Stat3    Mov R1,#BankB       ;T0 and not T1, so Bank B<<<< 
                   Jmp StatEnd         ; 
          Stat2    Mov R1,#BankC       ;not T0 and T1, so Bank C<<<< 
          StatEnd  Mov A,R1            ;Get current base address 
                   XRL A,R2            ;Compare to last base address
                   JZ  TakDat          ;If same, go increment counters 
                   MOV A,R1            ;Different bank this time, reset
                   MOV R2,A            ;set "old" base address here 
                   IN  A,P1            ;set old port reading equal 
                   MOV R3,A            ;     to current one 
                   IN  A,P2            ;same for port 2 
                   MOV R4,A 
                   JMP Main            ;End of Main Program loop 


               The main reason for having the CONST directive is for
               program clarity.  It is much easier to understand what you
               are doing if you write data to "BankC" instead of "80".  



          INCLUDE  

               This directive causes EPASM to stop reading from the current
               file being assembled, open the file specified and assemble
               commands from that file into the program until the end of
               that file is reached, then return to the original program

                                          10





                      EPASM  Assembler     October 11, 1990

               and continue assembling.   It is effectively the same as
               having those commands in the INCLUDE file in your program. 
               The command syntax is


               INCLUDE [path]filename


               The file must be in the current directory, or the full path
               specified, or else EPASM will not be able to find the file
               and an error will be generated.  This command is useful if
               you have a number of standard definitions or routines that
               you use in many programs.  Then you can have a single file
               containing them and all the other programs you write can
               INCLUDE this file, so you don't have to have multiple copies
               of the routines in every file.  Also, when editing the
               standard routines, you can then recompile the routines and
               the changes will be effective in all programs that use that
               file.

               The only limitation on the include file is that you cannot
               "nest" the include files.  That is, you cannot have an
               "INCLUDE" file that has another "INCLUDE" command for yet
               another file.

               Also, when there is an error in the program after the
               include file, the line number reported will be the actual
               line number of the program file plus the number of lines in
               the include file.  If the error is in the include file
               itself, the line number reported will be the line number of
               the error in the include file plus the number of lines ahead
               of it in the main program.  To be certain of the line
               numbers, the best way is to look at the .WRK file created by
               EPASM (see chapter VI).  This file will show all lines from
               the main program and the include file together, in the order
               assembled.


















                                          11





                      EPASM  Assembler     October 11, 1990




          V.  MCS-48 command notes


          The MCS-48 commands are stored in the file INSTR.SET.  This
          should, for the purposes of EPASM, be the reference for the
          correct syntax of the commands, since they will be expected to be
          exactly as they are spelled in this file.  Note that all the
          commands in the file INSTR.SET must be in upper case, since any
          file assembled will be converted to upper case before being
          compared to these commands.  The commands in the program to be
          assembled can be in either upper or lower case, as discussed
          above.

          The file INSTR.SET is an ASCII file, with each line being the
          definition for one command.  Comments can also be included, if
          they are preceded by a semicolon.  Below are a few sample lines.

          ;
          ;
          JF0  $    B6   2
          JF1  $    76   2
          JMP  !    04   2
          MOV  A,#  23   2    ;this command moves in the immediate word
          MOV  A,PSW C7  1
          MOV  A,R0 F8   1
          MOV  A,@R0 F0  1
          MOV  A,@R1 F1  1
          MOV  A,T  42   1


          The format of the line is first the command word(s), then an
          address or data indicator, if any, then the hex machine code for
          the command, then the number of machine cycles for that command. 
          The data or address indicators are the "#" and the "$"
          characters, respectively, and they show that the command includes
          a byte of data or an address.   For example, the command to move
          immediate data to the accumulator is given by the line

          MOV A,#  23  2

          Since it contains the "#" character, it indicates that a second
          byte is required; namely, the data to be moved into the
          accumulator.  So the correct usage of this command would be

          MOV A,#1C        ;Move the value 28 (1C hexadecimal) to acc.

          Similarly, the "$" character indicates that an address is needed
          in the command.  So in the command

          JF1  $    76   2

                                          12





                      EPASM  Assembler     October 11, 1990

          the program will jump to the address given if flag 1 is set.  The
          correct usage of this command is

          JF1  DONE          ;if flag set, jump to DONE

          where DONE is a label that is defined elsewhere in the program. 
          Note that when the address is given by an eight-bit value, the
          location of DONE must be on the same memory page as the JF1
          command, or else the jump will not be performed properly.

          The "!" character is used for the JMP and the CALL commands,
          which have a 11-bit address (in order to cover the entire 2K
          address space).  The upper three bits of the address are encoded
          into the first byte of the command.  This differs from the
          address byte in commands using the "$" character, which is just
          the second byte and therefore is limited to eight bits.  EPASM
          treats these two commands specially and encodes the address
          automatically.

          Other commands have no data or address information, and are
          completely specified in the INSTR.SET file.  For example,

          MOV  A,@R1 F1  1

          specifies the command to move data memory contents into the
          accumulator (register R1 has been previously loaded with the
          desired address).  The correct usage of this command is

          MOV A,@R1           ;Move register-addressed data into acc.

          almost precisely as it appears in INSTR.SET.

          Because the INSTR.SET file is in ASCII format and read into the
          EPASM program every time it is executed, the INSTR.SET file can
          be edited to change the syntax of the commands, if desired.  This
          is not usually recommended, since it is good to keep the command
          names similar to the MCS-48 commands for clarity.  However, if
          you wish to program for a different EPROM with a different
          command set, one could simply change the file INSTR.SET to
          contain the commands in the alternate instruction set.  The only
          restriction is that the CALL and JMP commands cannot be changed,
          since they are handled in a special way.  Also, new commands with
          the "!" character cannot be added, since it requires changes in
          the EPASM program.  Of course, if you have registered your copy
          of EPASM and have the source code, you can alter the assembler
          program for different devices.  

          Another feature of EPASM is the ability to do simple arithmetic
          within the statement with hexadecimal numbers.  The allowed
          operations are addition and subtraction.  For example, say that
          you wanted to move the value 8C into the accumulator.  The
          command would be


                                          13





                      EPASM  Assembler     October 11, 1990

          MOV A,#8C      ; fill accumulator with value

          Now say that you wanted to move a number that was 7 larger than
          8C.  The correct command would be

          MOV A,#8C+07    ;fill accumulator with 7 greater than 8C

          This expression is evaluated during the assembly, and the correct
          constant value (147, or 93 hexadecimal) is placed in that memory
          location.  So the command is equivalent to 

          MOV A,#93        ;fill accumulator with 93 hex

          Since the expression is evaluated before the .OBJ output file is
          written, the statement will not add to the object code file
          length, or slow the program down.  This feature is useful when
          you don't feel like doing the math operaation, or when you want
          to show the relationship between constants.




































                                          14





                      EPASM  Assembler     October 11, 1990




          VI. Assembling your program


          Once the program has been written and saved to disk as an ASCII
          or "DOS" format text file, it is ready to be assembled by EPASM. 
          The following is the command syntax for the assembler:

          epasm progname [-w -e -b -l -h] [filename]


          The "progname" above should be the file name of the ASCII file
          which contains the assembly language program you wish to
          assemble.  It can be just the file name, or the full path if the
          file is not in the default directory.  The extension ".ASM" is
          assumed if none is used.  Be sure not to use the extension .TMP,
          because EPASM uses this for a temporary file, and later erases
          it.  If you have another file with the same root name as your
          program and this extension, it will be erased.

          The command line options are:

              -w  : create a "work" file, showing the program memory
                    address, the assembled commands, and the original
                    command from the input file source code.  This is
                    extremely useful when debugging the program, to see
                    where the error is occurring and what the EPASM program
                    is trying to do with the commands it is given.  The
                    default file name is the original name, with the
                    extension ".WRK".

              -e  : create an error listing file.  This is a file
                    containing all the error messages generated when
                    running EPASM.  These messages are also printed to the
                    screen, but may come too fast to see them all.  The
                    default file name is the original file name with the
                    extension ".ERR".  

              -b  : in addition to the ASCII object module created whenever
                    EPASM successfully assembles a file, a binary file
                    containing the machine code can also be created using
                    this option.  The binary file is a non-printable file
                    which is 2K bytes in length and contains no format
                    characters, checksums, etc, just the machine code in
                    binary format.  This file may be useful when a EPROM
                    programming device may require a different format than
                    the default .OBJ module normally created by EPASM. 
                    This binary file can be read easily into a conversion
                    program that the user would write to output the proper
                    format.  The default name for this file is the original
                    name and the extension ".BIN".

                                          15





                      EPASM  Assembler     October 11, 1990

              -l  : this option creates a label listing output file that 
                    may also be useful for debugging purposes.  This file
                    contains a list of the program addresses and the
                    machine code to be placed in that address.  Labels are
                    indicated by a carat (^) followed by an ASCII character
                    for identification.  At the end of the program will be
                    a listing of all the labels used and the characters
                    used to identify them in the listing above it.  This
                    output was mainly used during the development of EPASM,
                    but it can also be useful as a debugging tool.  The
                    default name for this file is the original file name
                    plus the extension ".LAB".

              -h :  This option creates a "Hex" output file, which is an 
                    ASCII file with the assembled commands listed in
                    hexadecimal form, 16 bytes per line (32 characters). 
                    This is basically the .OBJ format without the header
                    information and the checksum.  See chapter VIII.


          Note that when using command line switches, either upper case or
          lower case can be used, so that "-E" is the same as "-e".  Also,
          the DOS switch character can be used (e.g., "/E").  


          Running EPASM

          When EPASM is run without any arguments, the program simply lists
          the command format and gives a short reminder of the command line
          options.  To do this, just type

          C> EPASM

          (Note: in this example and those below, the "C>" represents the
          DOS prompt and should not be typed.)  The EPASM program must be
          in the default directory, or a directory that is accessible via
          the current DOS PATH defined.  The file INSTR.SET must be in the
          default directory or the same directory as EPASM, otherwise the
          error "Instruction set not found" will be generated.  To assemble
          a program, type EPASM plus the file name to assemble.  For
          example, if you wish to assemble the file SAMPLE.ASM which is
          included with this documentation, type

          C> EPASM SAMPLE

          The extension ".ASM" is assumed, and need not be entered.  If you
          wish to assemble a file called SAMPLE.TST, just type 

          C> EPASM SAMPLE.TST

          If you use command line switches, separate them with spaces from
          the rest of the command and from each other.  For example, if you
          want to create a "work" file and an error listing (if there are

                                          16





                      EPASM  Assembler     October 11, 1990

          any errors in the program), type 

          C> EPASM SAMPLE -E -W

          If there are errors, the files SAMPLE.ERR and SAMPLE.WRK will be
          created.  If there are no errors, the files SAMPLE.WRK and
          SAMPLE.OBJ will be created.  If you wish to specify different
          file names for the output files, the names can be included after
          the switch.  For example, if we want to assemble the file
          SAMPLE.ASM, but want the work file name to be WORK.SMP, and
          create in addition to SAMPLE.OBJ a binary output file, we would
          type 

          C> EPASM SAMPLE -W WORK.SMP -B


          While the EPASM program is running, it will notify you of errors
          it encounters by printing a message to the screen.  If errors are
          encountered, no .OBJ, .HEX or .BIN output files are generated. 
          If no errors are encountered, an .OBJ file will be created, along
          with a .BIN or .HEX file if the proper command line switch is
          used.  An .ERR file will not be created, even if one is specified
          using the command line switch.

          If you wish to stop the assembly at any time, just press any key. 
          The program will suspend the assembly and ask if you wish to
          abort.  Type "Y" if you want to stop.  This feature means that
          you can't "type ahead" the next DOS commands after EPASM, but the
          ability to terminate the assembly is very useful, mostly when
          EPASM finds errors and you do not want the assembler to bother
          with the rest of the file until you have gone back and corrected
          the errors.

          The file SAMPLE.ASM is included with this release to mainly
          illustrate the proper syntax and structure of an .ASM program,
          not to show good or useful programming technique.  


















                                          17





                      EPASM  Assembler     October 11, 1990




          VII.  Error messages


          The first section below summarizes some of the errors that may
          occur in the command used to start EPASM from DOS, and errors in
          finding the proper files necessary to run EPASM.  The second
          section describes the error messages given by EPASM when it finds
          errors in the program it is assembling.  Tips are given as to
          what to do to correct the errors.



          VII.1  Command, file, and DOS errors


          Bad command or file name

               Make sure that you typed EPASM correctly, and that the
               EPASM.EXE program is in the current directory, or accessible
               via the PATH you have currently defined.


          Instruction set file INSTR.SET not found 

               The file INSTR.SET is not in the default directory or cannot
               be found in the directories defined in the current DOS PATH. 
               Make sure you have copied it from the distribution disk to
               the proper directory.


          Error in command line parameter 

               You used an invalid combinations of switches and file names
               in the command line when you ran EPASM.  See chapter VI for
               instructions on using the command line switches and file
               names.


          File not found 
          Path not found

               The file name you specified is not correct, or it is not in
               the directory you specified, or that directory does not
               exist.  Check the file names used in the command line, and
               in the INCLUDE files used, if any.


          Disk is write-protected

               If your files are on a floppy drive, make sure the write

                                          18





                      EPASM  Assembler     October 11, 1990

               protect tab is not on (for a 5 1/4" disk) or in the proper
               position (covering the hole in the 3.5" disk).


          Drive not ready

               Make sure the disk is in the drive specified, and the disk
               is locked in for reading.



          VII.2  EPASM assembly errors


          The following are error messages generated by EPASM when it finds
          errors in the program it is assembling.  The error message will
          be printed out, followed by some of the offending text, and a
          line number.  Often if a line has an error in it, two different
          error messages will be created, as EPASM tries to interpret the
          code in different ways.  When the problem is solved, both
          messages will go away.

          The error detection in EPASM can only detect certain errors.  It
          cannot, of course, diagnose logical errors that will cause your
          program to not work as you expect after you have "burned" the
          program into your EPROM.



          Invalid constant character 

               The text encountered is being interpreted as a hexadecimal
               constant, and there was an error in converting the number. 
               You may be trying to define a label that is two or fewer
               characters in length (a label must be three to eight
               characters long), or you mistyped the constant (you entered
               8L when you intended 8C).


          Hex constant overflow  

               The assembler is expecting a hexadecimal constant in that
               location, but the number there is over two digits in length
               (constant limits are 00 to FF hexadecimal).


          Invalid jump command 

               The jump command entered is not a valid MCS-48 jump command.





                                          19





                      EPASM  Assembler     October 11, 1990

          Syntax error 

               The command used on the line is not a valid MCS-48 command. 
               Most likely you have misspelled the command, or the
               assembler is attempting to evaluate a label as a command. 
               Make sure there are spaces or tabs separating the elements
               in a line.


          Call instruction cannot be located at [address]

               The CALL instruction cannot be located at addresses 2046-
               2047 or at 4094-4095.  You must change your program so that
               these statements do not fall on these addresses.


          Conditional jump at [address] cannot reach destination

               The conditional jump commands (e.g., JC, JF0, etc.) can only
               jump to addresses on the same 256-byte memory page, since
               the address used in the command is only 8 bits.  The program
               is trying to jump to a label (address) on another page.  You
               must change the program so that either the conditional jump
               and the destination are on the same page, or rewrite the
               code so that you jump across the page boundary (the CALL and
               JMP commands are not restricted to one page, they can jump
               directly to any location within the 2K program memory).
              


          Unresolved label 

               You have referenced a label somewhere, but never defined its
               location (you define a label by putting it as the first
               element in some line).  Either you forgot to define it, or
               misspelled it, either here or where it was defined.


          Warning: cannot nest INCLUDE files 

               Your INCLUDE file contains another INCLUDE file.  This is
               not allowed: call the second INCLUDE file from the main
               program.  The second INCLUDE file will be ignored, and the
               assembly will continue.


          Warning: error opening INCLUDE file 

               The INCLUDE file you specified could not be found.  The
               INCLUDE file must be in the default directory, or must be
               specified by the full path name. The assembly will continue,
               but without the information in the INCLUDE file.  Check the
               location of the file.

                                          20





                      EPASM  Assembler     October 11, 1990


          Work file error 

               There was an error opening or deleting the work file
               specified (or the default work file name, if none explicitly
               chosen).  EPASM first creates a work file with the extension
               .TMP, then at the end, erases this and makes a work file
               with the extension .WRK, or whatever you have specified.  Be
               sure not to have any other files in the directory with the
               extension .TMP, or they may be erased!












































                                          21





                      EPASM  Assembler     October 11, 1990




          VIII.  Using the EPROM programming device


          The procedure that you use to program or "burn" the EPROM will
          vary greatly, depending on the device being used.  In most cases
          you will be able to send the programming device a file of
          commands, which will direct the device to program the EPROM. 
          This file is one of the output files from the EPASM program which
          contains your assembled code, either the default .OBJ file (which
          is the most common case), or the hex or binary files containing
          the same program in different format.

          Some programming devices (such as the PROMPRO-7)  require that
          you communicate with it using a terminal emulator program.  In
          this case, the emulator program has to have an "upload" command
          to send a file to the device.  

          Other devices come with their own software drivers, such as the
          B&C Microsystems 1409 Universal programmer.  With this device,
          the file can be read in and sent directly using commands from the
          driver program.

          There are three output file options in the EPASM program.  The
          default .OBJ files are in Intel hex format.  Each line of the
          file has the following information (all numbers in hexadecimal):


                            INTEL  hex  format

          # of ASCII
          Characters     Description

             1         the colon character (:)
             2         number of data bytes N in record (00 for end record)
             4         the starting address of where the data bytes are to  
                        be located
             2         00=program data in line, 01=end of file record
            N*2        the program data to be loaded into the EPROM
             2         checksum (two's compliment of the sum of the bytes 
                        after the colon character, modulo 256)



          EPASM always sets N above equal to 10H (16 decimal).  

          Another format option is the binary file, which contains the
          program to be loaded into the EPROM with no formatting
          information, just the bytes starting at address 0 and going to
          the end of the program memory, for a total of 2048 8-bit bytes of
          data.  The locations from the end of the assembled program to the

                                          22





                      EPASM  Assembler     October 11, 1990

          end of the program memory space will be filled with zeros.

          A final format is the ASCII hex file, which contains the ASCII
          representation of the hex data to be loaded into the EPROM.  This
          is just the same as the Intel file, except only the program data
          is in the file, there is no header information or end record. 
          The data for program starting at address 0 going to the end of
          the program are included in the file.  Sixteen program memory
          values are written per line (32 ASCII hex digits).













































                                          23





                      EPASM  Assembler     October 11, 1990






                                       INVOICE




          Remit to:

          Joseph Hora
          46-1063 Emepela Way, Unit D
          Kaneohe, HI  96744-3975

          Questions and technical support number:
          (808) 956-9848
          internet: hora@galileo.ifa.hawaii.edu


                        From:

                        ________________________________________________

                        ________________________________________________

                        ________________________________________________

                        ________________________________________________




          Enclosed is $15.00 ( Check ___   Money Order ___  P. Order  ___)
          for registration of EPASM.  Please send me the latest version of
          the EPASM program and example files, a printed version of the
          manual, and the source code for the EPASM program (in Turbo
          Pascal 5.0), and put me on the mailing list for future updates
          and extensions to the EPASM program.














                                          24