Function documentation of Creative Sound Library Module

1. Introduction

    Author          :  T S Lee
    Version         :  1.00
    Last Updated    :  29 Sep 1989


    This version uses a more reliable detection scheme, and the
    codes are further optimized.

    Please replace all older versions with it.

    The  library  functions provided is for Microsoft  C  version
    5.00 and above. All the memory models, SMALL, COMPACT, MEDIUM
    and  LARGE  are  available. These functions  are  grouped  in
    library files named in following conversion:

          SBCx.LIB

    where  "x"  is the first character of the  respective  memory
    model.

    The default segment and group name defined in Microsoft C for
    each memory model is used to ensure compatibility. Any global
    variable  memtioned in following section must be declared  in
    the default data segment '_DATA'.


    The  FM feature of the Sound Blaster Card (SBC)  an  optional
    item in some OEM versions. So we suggest that if you want  to
    play  FM  music on the Sound Blaster Card, separate  FM  chip
    detection is required.


2. Function Documentation

Function    :  unint _ct_card_here()
Description :  Check   for  the  availibities  of   the   various
               music/sound  features  provided by  Creative.

               The  check is based on the I/O address  stored  in
               the global variable ct_io_addx which is defined in
               the application program.

Entry       :  none
Return      :  Music/Sound feature available

               High byte is alway zero now
               Low byte right most 3 bits indicate as follow

                    bit 0 : on for C/MS music available
                    bit 1 : on for FM music available
                    bit 2 : on for Creative voice available

               The type of Creative Music/Sound Card available on
               the  system  can  be determined  with  the  return
               value.

               Game  Blaster Card returns 1. Sound  Blaster  Card
               without  optional FM music returns 5, with the  FM
               music it returns 7.


Note        -  The I/O address used for the music/sound card must
               be   stored   in  ct_io_addx  before   the   call.
               (Application can set this variable to the  factory
               defualt value, 220 Hex).

            -  A  zero return value may due to wrong I/O  address
               used.



Function    :  unint sbc_version()
Description :  Return the version number of the DSP on the SBC.
Entry       :  none
Exit        :  version number, high byte major version 
                               low byte minor version




Function    :  void sbc_scan_int
Description :  Scan  for  the interrupt number selected  for  the 
               voice   card  and  update  the   global   variable 
               ct_int_num.
Entry       :  ct_io_addx must be set with the correct I/O.
Exit        :  The  global variable, ct_int_num, is updated  with
               one  of the following 2, 3, 5 or 7. If it is  zero 
               on return, the card DMA fails.



Function    :  void sbc_dac_spk(unint on_off_flag)
Description :  Turn   on/off  the  DAC  speaker  based   on   the 
               on_off_flag
Entry       :  If  the on_off_flag is non-zero, the DAC speak  is 
               turned on. A zero will turn it off.
Exit        :  none