Box Plot For Windows 3.0

                           By Rick Carlson
			  For Sparta Sound Co.
			 COMPUSERVE 71041,3015
		
			 SHAREWARE VERSION 1.0

		
	Box Plot is a Microsoft Windows based program that shows
	the frequency response and maximum Sound pressure level
	of a given Loudspeaker/Box Combination.
	
	This Version of Box Plot requires Microsoft Windows 3.0
	or later to run. A math coprocessor is not required but
	really helps speed things up if you want do alot of
	iterations on the box parameters.
	(Turn off Auto Plot on slow machines).

	If Terms like Qes, Fs, Vas are unfamiliar to you, then
	this program will be difficult for you to use. It is intended
	for the audio hobbyist or professional interested in building
	there own speaker enclosures, or modifying their present
	system.

	If you are interested in building your own speakers, I would
	suggest that you subscribe to Speaker Builder Magazine. It
	is a good source of information on this subject.
	(Unsolicited advertisement)

============================================================================
History:

      Box  Plot  is based on a program called Boxresponse,  which
    was published in Speaker Builder magazine a while back.   Box
    Plot   adds  graphical  output,   MS  Windows  compatability,
    printing, file storage, and a couple of other new features to
    the original BASIC version of Boxresponse.


Operation:

      This  Program  was  designed  to  allow 'almost'  real time
    update of the response plot as box parameters are  changed.
    This  is usefull when trying to shoehorn a speaker into a non
    optimum box.  Many different combinations of  box  parameters
    can  be  tried  in  a  short period of time.  If Auto Plot is
    turned on,  then  clicking  on  the  OK  button  of  the  BOX
    Parameters dialog box will replot the response curves.

Speaker Parameters:

      Speaker parameters are entered into  a  dialog  box.   When
    done,  click  on  the  OK button to save the parameters.  The
    Parameter names are the Thiele Small Parameters specified  on
    most good spec sheets.

Box Parameters:

      Box Parameters are entered in a dialog box.   When  the  OK
    button  is clicked the Box Parameters dialog box stays on the
    screen.  To close the dialog box click on the Close button or
    use the system drop down menu (upper left of dialog  box)  to
    close  the box.  The reason the dialog box stays on screen is
    to make it easier to edit parameters and see  the  effect  on
    frequency response.

    There are 6 types of boxes that can be modeled with Box Plot.
	Closed Box:
		Simple sealed Enclosure.
	Closed Box with first order equalizer:
		Sealed box with first order filter. The first order
		filter usually provides subsonic attenuation.
	Closed Box with second order filter:
		The second order filter is usually an active filter
		placed before the power amp. This filter can be used
		to extend the low end, or modify the response of an
		existing system.
	Vented Box:
		Box with tuned port.
	Vented Box with first order eq:
		First order Eq is more usefull here than is a sealed box.
	Vented Box with second order eq:	
		Same as sealed box.	

Comments:
      The comments field is a text string,  255 chars  long  that
    can be used to annotate the graph.

Vent Design:
      This  box  will  show  the vent length based on the present
    box/ speaker combination.

Auto Plot:
      When the Auto Plot menu item is checked,  anytime a speaker
    or  box parameter is changed,  the graph will be regenerated.
    This keeps the graph up to date with the  latest  parameters.
    This  also  may  be  annoying on slower machines so it can be
    turned off.

File:
	New:
		This will reset all parameters to some predefined settings.
		The settings are based on nothing at all, just some numbers
		that wont do real wierd things. (The speaker parameters are
		from a well known manufacturer.)
	
	Save:
	Save as:
		This will save the speaker, box, and comments in the specified
		file. (Registered Versions)

	Open:
		Read a file on the disk. The default file extension is .SPK
		but has no real significance.

	Print:
		This will print the response curves as shown on the screen
		along with the speaker and box parameters. (Registered versions)


	In the Unregistered shareware version, files cannot be saved
	and the response curves cannot be printed. Please register
	to recieve the complete version, as well as updates and
	bug fixes, as they become available.

	To register Please send $25.00 to
		Rick Carlson
		62 Fox Trail Rd
		Sparta, NJ. 07871

	Compuserve 71041,3015

	I will send out a disk with the complete version, and some
	more on line documentation.
	If you have suggestions, comments, bug reports or just feel
	like writing please do so.
	Let me know what other kinds of programs would be usefull to
	the audiophile.