ADDING HS/LINK TO WWIV 4.20
        TESTED WITH WWIV 4.0 AND HS/LINK V1.0áE3 (HSLK10E3.ZIP)

     Please refer to the WWIV documentation for detailed information on
     installation of external protocols.  This information was tested with
     HS/Link betas HSLK10E3 posted on 1/9/92 and WWIV version 4.2.

     The following installation steps should work for most folks:
     RBBS-PC uses a template file called PROTO.DEF for passing parameters
     to external protocols.  This template file can either call a BATCH
     file or pass parameters directly to the protocol engine.  Using either
     method ( BATCH or the direct passing of parameters directly to the
     engine will work.

     Place a copy of HSLINK.EXE into your main C:\WWIV directory, or
     into some other directory listed in your dos PATH setting.

     Run INIT.EXE and select 7 (external protocols)
     Press I to insert a new protocol.

     The definition of the HS/Link should look like this:

  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
  ³     Description          : HS/Link                                    ³
  ³                                                                       ³
  ³     Xfer OK code         : 0                                          ³
  ³                                                                       ³
  ³     Require MNP/LAPM     : N                                          ³
  ³                                                                       ³
  ³     Receive command line:                                             ³
  ³     hslink -p%2 -u%3                                                  ³
  ³                                                                       ³
  ³     Send command line:                                                ³
  ³     hslink -p%2 -nu %3                                                ³
  ³                                                                       ³
  ³     Receive batch command line:                                       ³
  ³     hslink -p%2 -u%3                                                  ³
  ³                                                                       ³
  ³     Send batch command line:                                          ³
  ³     hslink -p%2 -nu @%3                                               ³
  ³                                                                       ³
  ³     Bi-directional transfer command line (not implemented yet):       ³
  ³     hslink -p%2 @%3 -u%5                                              ³
  ³                                                                       ³
  ³     <ESC> when done.                                                  ³
  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

     The bi-directional capability of WWIV is not currently implemented.
     You may want to explain to your users that bidirectional transfers
     should not be attempted with this version of WWIV.

     Note for systems running locked COM ports:
     We have found that if you use a locked DTE of 9600 or above, you
     will need to have a NS16550AN UART installed.  Also, for rock solid
     performance you should add the -HS (Handshake Slow) switch to all
     of the above command lines.

     This should get you set up in under 10 minutes.

     You can edit the command lines to include options on the HSLINK
     command line, but most folks won't need to change anything.  If
     your system can't keep up with the COM port while accessing the
     disk drive, you may want to add -HS to both lines.  If you want to
     experiment, there are a number of optional parameters you can read
     about in HSLINK.DOC and HSLINK.NEW.

     I hope these instructions help, but remember, I can't take
     responsibility for any damages resulting from these instructions.
     If you get stuck, it always helps to read the DOC files that come
     with RemoteAccess and with HS/Link.  If all else fails, call up the
     Tool Shop and ask for help on the Support Conference.  Either I
     will help you, or somebody else will know the answer and give you a
     hand.

     Good luck!

     Samuel H. Smith
     Sysop of The Tool Shop

        Phone number         Modem type                Access
       --------------    ---------------------   -------------------
       (818) 891-3772    US Robotics HST 9600    Contributors only
       (818) 891-1344    Hayes-V series 9600     Contributors only
       (818) 891-6780    US Robotics 2400        Free to all