SLPACK
              Searchlight Message Base Pack/Optimize Utility
                       Version 2.15, November, 1991
                 (c) Copyright 1991 Searchlight Software


INTRODUCTION
------------
SLPACK is a message base packing and optimization utility for Searchlight 
2.15 message subboards. SLPACK operates on subboard header (HDR) and/or 
message (MSG) files, and performs three main tasks:

(1) Optimization -- Records in the data files are physically sorted into
    sequential order, improving access times.

(2) Packing -- Unused records are purged from the data files and the files
    are physically shrunk to release unused disk space back to DOS.

(3) Renumbering -- Messages can optionally be renumbered in sequential order
    starting with 1, when packing the subboard header files.

SLPACK is a command-line driven program; it can operate on one, several, or 
all subboards at once. Command line options are shown below.


SYNTAX
------
The command line syntax for running SLPACK is as follows:

  SLPACK [Options...] [Subboards...]

"Options" can be one or more of the option switches described below, and 
"Subboards" can be one or more valid subboard names. Subboard names are 
required unless the /A (All) switch is used. If no options or subboard names 
are specified, then SLPACK displays a brief summary of its options:

  /M       Pack message (MSG) files only
  /H       Pack header (HDR) files only
  /R       Renumber messages on subboard
  /N       Skip confirmation prompt
  /A       Pack all subboards
  /S       Scan subboards before packing
  /Fn[,m]  Free records for header [,message] files
  /Pn      Pack only if 1st message >= n

Note: Before running SLPACK, please see the CAUTION section below.


OPTIONS
-------
Option /M -- Pack Message Files Only

If the /M switch is given, SLPACK will pack only the message (*.MSG) files 
associated with the given subboards. Otherwise, both the header and message 
files are packed.

The message file is usually larger than the header file; therefore, packing 
the message file only provides a good deal of optimization in a shorter 
amount of time than if both files are packed. However, packing the header 
file is required if you want to renumber messages.

Example: SLPACK /M GENERAL SLBBS-R


Option /H -- Pack Header Files Only

This option causes just the header files of the specified subboards to be 
packed and optimized. Message files are not affected.

Example: SLPACK /H GENERAL SLBBS-R


Option /R -- Renumber Messages

The renumber option causes messages to be renumbered sequentially, with the 
first message number equal to 1 and the last number equal to the number of 
messages on the subboard.

Renumbering can only occur if the header file is packed; no renumbering will 
take place if the /M option is also selected.

The renumber option also causes the high message pointers contained in the 
subboard's member files to be updated.

Example: SLPACK /R GENERAL SLBBS-R


Option /N -- Skip Confirmation Prompt

When /N is NOT specified, SLPACK displays a warning message before it begins 
to run, and requires that you type "Y" and "Enter" to continue. If the /N 
switch is specified, this confirmation prompt is skipped.

Use /N when you run SLPACK in an unattended environment (such as in a batch 
file or as part of an event).

Example: SLPACK /R /N SLBBS-R


Option /A -- Pack All Subboards

The /A switch causes SLPACK to operate on all subboards in your system, 
instead of just the subboards specified on the command line. When /A is 
used, no subboard names need be specified.

Example: SLPACK /R /N /A


Option /S -- Scan Subboards Before Packing

When the /S switch is enabled, SLPACK does a repair scan (equivalent to the 
F3 utility functions in the SETUP program) before packing each file. 

This option is recommended, especially when running SLPACK in an unattended 
mode (such as when SLPACK is part of an event). Packing a subboard involves 
rearranging every record in the file; files which contain even one bad 
pointer or corrupt record can result in the entire subboard becoming corrupt 
and even in SLPACK aborting. Using the /S switch assures that each subboard
file is checked for consistency before it is packed.

If you are reasonably sure that a subboard is not corrupted, you can omit 
the /S switch, which will speed up SLPACK.

Note that the /S switch is not a substitute for making a backup; it is 
always recommended that a backup of the files to be packed be made before 
running SLPACK.


Option /Fn[,m] -- Specify Free Record Counts

The /F command, which is followed by one or two numeric parameters, 
specifies the number of free records to be appended to the end of the header 
and message files after packing is complete.

By default, SLPACK removes all free records from these files when it packs 
them; if /F is specified, then SLPACK appends the requested number of free 
records to the end of the files. Preallocated free records help reduce file 
fragmentation and increase speed when saving new messages to the file.

Note that free record parameters have no effect unless the respective file 
is actually packed.

Example: SLPACK /F30,100 SLBBS-R     (30 free header & 100 free message recs)
         SLPACK /F40 /H SLBBS-R      (40 free header records)
         SLPACK /F0,200 /M SLBBS-R   (200 free message records)


Option /Pn -- Check 1st Message Before Packing

If the /P option is used, followed by a numeric parameter, then SLPACK only 
packs subboards where the first message on the subboard is greater than or 
equal to the parameter given. For example, if /P100 is specified on the 
command line, then only subboards where the first message on the sub is 
equal to or greater than 100 are packed.

Used in conjunction with the /R option, /P allows you to monitor subboards 
which have high turnover volumes and renumber these subs only when the 
oldest message number reaches a certain level. For example, suppose you have 
a subboard which can contain a maximum of 1000 messages, has auto-purge 
enabled, and you prefer that the highest message number does not exceed 
1500. To accomplish this automatically, you could execute the following 
command on a regular basis:

  SLPACK /R /P500 SLBBS-R

The value of "500" is chosen for the /P parameter because 500 plus the 
subboard maximum messages (1000) equals the message number preference of 
1500. It should be noted that if messages are deleted from the subboard 
(other than the earliest messages) or if purge protection is enabled for any 
message, then the high message number may exceed 1500 before the lowest 
message number exceeds 500 and the renumber operation takes place.


MESSAGES
--------
SLPACK will display the following progress messages as it runs:

Packing Subboard: NAME
Packing/Renumbering Subboard: NAME

  The "Packing" or "Packing/Renumbering" message tells you which subboard is 
  currently being packed or renumbered.  

Performing Safety Scan...

  If the /S switch is used, this message appears while SLPACK is performing
  the initial repair scan of the file before packing it.

Header File: Reading, Sorting, Done.
 Rebuilding Indexes:
 Rebuilding Threads:
Rebuilding Free List:

  These messages follow the progress of the header file repacking, if that
  option has been selected. 

Expanding to nnn Free Records...

  If the /F option is used, this message appears to report that the file
  is being expanded.

Updating Member Records...

  This message appears during a renumber (/R) function while the member
  file is being updated.

Msg File: Reading, Sorting, Done.
Rebuilding Free List:
Expanding to nnn Free Records...

  These messages follow the progress of the message file packing process.
  The "Expanding" message appears only if a free record count for the 
  message file has been specified with /F.

Skipped (1st message number = nnn)

  This message indicates that a particular subboard is not being packed, 
  because the /P parameter has been used and the first message on the 
  subboard is less than the target value.

Insufficient Memory Available (nnn bytes needed)

  Not enough memory is available to pack this subboard. See memory 
  requirements, below.

Cannot Open Subboard:

  Indicates that the subboard cannot be opened. Check the subboard name and
  its data files path.


CAUTIONS
--------
SLPACK rewrites and rearranges the entire message and header files of the 
subboards it packs. Because of the way in which it operates, SLPACK is 
extremely sensitive to power failures, corrupt files, bad disk sectors, and 
other such problems which may occur during its operation. In order to 
prevent data loss, we stronly urge you to follow these precautions: 

(1) BACK-UP ALL SUBBOARD FILES BEFORE PACKING THEM. If an error occurs 
    during SLPACK's operation, it should be assumed that the subboard which
    was open at the time of the error is corrupted, and needs to be restored 
    from the backup copy.  

(2) Do not disturb SLPACK once it begins to run. Any attempt to abort
    SLPACK will result in a corrupted subboard. The same is true if SLPACK
    should be interrupted by a system failure such as a reboot, power
    failure, bad disk sector, etc.

(3) In multinode systems, no other nodes should be active while SLPACK is 
    running. Either shut your other nodes down manually or, if SLPACK runs 
    as an event, make sure the other nodes are idle while it runs.

(4) SLPACK will fail if it tries to pack a subboard which contains corrupted
    data files and the /S command line switch is not specified. Should 
    this occur, try to repair the subboard via the SETUP program repair 
    functions. If this fails, then restore the subboard from a backup file, 
    and pack it again, specifying the /S switch on the SLPACK command line.


EXIT CODES
----------
SLPACK will return one of three exit codes (errorlevels) when it completes:

Errorlevel 0 -- Indicates that no errors occured and all requested 
  operations were carried out successfully.

Errorlevel 1 -- Indicates that SLPACK has done nothing, for one of the 
  following reasons:

   A. No command line parameters were specified.
   B. SLPACK could not open the CONFIG.SL2 file. Be sure that CONFIG.SL2
      is either in the current directory, or pointed to by SET SLBBS=.
   C. You answered "N" to the confirmation prompt.

Errorlevel 2 -- Indicates that one or more operations failed, because of 
  the following reasons:

  A. Can't open subboard: a subboard name given on the command line was
     incorrect, or the subboard files could not be located and opened.
  B. Not enough RAM for requested operation. See RAM note below.

Note that Errorlevel 2 errors do not cause SLPACK to terminate immediately. 
It will continue to run and process as many subboards as possible.


RAM REQUIREMENTS
----------------
SLPACK requires a significant amount of memory to pack large message bases. 
If insufficient memory is available to pack a particular subboard, SLPACK 
will skip that subboard and display an error message. It will also exit with 
an error level of 2.

Here is how you can compute the memory required to pack a particular 
subboard:

  (1) Take the DOS file size of the header (*.HDR) file, subtract 8332,
      and divide by 256. If you are using the renumber (/R) option, multiply
      this result by 6. Otherwise, multiply it by 2.

  (2) Take the DOS file size of the message (*.MSG) file, subtract 140,
      and divide by 128.

  (3) Take THE LARGER OF the two numbers above and add 67,000. This is the
      approximate amount of free DOS memory that needs to be available 
      before you can run SLPACK on this subboard.


------