VFOSSIL.DOC

                        Using a Fossil Driver with VBBS

                          Roland De Graaf 1/22/1992
                              Revised 1/29/1992

         The fossil driver can open up a whole new world to VBBS.

         The "standard" serial driver which comes with VBBS is
         not able to allow IRQ sharing between COM ports.
         This is not so much a limitation in the serial driver, as it
         is a limitation of the underlying operating environement.

         A FOSSIL driver, on the other hand, can handle 2 or more
         serial ports using the same IRQ line. In fact, a FOSSIL
         can be used to control up to 8 ports. It can be "programmed"
         to use almost any serial board in existance.
         
         For the purposes of this document, we shall refer to the
         X00 and BNU fossil drivers. If you're new to fossil drivers,
         they are a "standard" way for programs to communicate with
         serial ports, and you only need one installed on your system
         in order to make use of it.

         X00 is one type of fossil driver that loads thru CONFIG.SYS.
         BNU is a another type of fossil driver that loads thru AUTOEXEC.BAT.
         Both programs do roughyl the same thing, and yu have your choice of
         which one you wish to use.
         
         ** Number of simultaneous open ports **
         ***************************************
         
         The "basic" CONFIG.SYS install line for X00 looks like:

         DEVICE=X00.SYS

         The "basic" AUTOEXEC.BAT install line for BNU is:

         BNU

         By default, a fossil will assume you wish to have only
         ONE COM port open at any given moment.
         
         This doesnt specify WHICH port (COM1, COM2, COM3, etc),
         but specifies the maximum number of simultaneous open
         ports.
         
         Each Port you request is like a "data channel," corresponding
         to your VBBS data channels.

         It is possible to request that the fossil make more ports
         available to you. 
         
         For more detailed information on the driver, consult 
         the fossil documentation.


         * VBBS Set Up *
         ***************

         Set up your VBBS Data Channels as you normally would.
         
         ***********************************************************
         
         VBBS - 2 user system example
         ----------------------------
         Ch 1 to be on COM1
         Ch 2 to be on COM2
         ------------------
         X00:
         DEVICE=X00.SYS 0=COM1 1=COM2
         BNU:
         BNU /P=2
         ---------------------------------------
         VCONFIG: Set Channel 1 to COM1
                  Set Channel 2 to COM2
         ***********************************************************
         
         VBBS - 2 user system example
         ----------------------------
         Ch 1 to be on COM2
         Ch 2 to be on COM3
         ------------------
         X00:
         DEVICE=X00.SYS 0=COM2 1=COM3
         BNU:
         BNU /P=2
         ---------------------------------------
         VCONFIG: Set Channel 1 to COM2
                  Set Channel 2 to COM3
         ***********************************************************
         
         VBBS - 4 user system example
         ----------------------------
         Ch 1 to be on COM1
         Ch 2 to be on COM2
         Ch 3 to be on COM3
         Ch 4 to be on COM4
         ------------------
         X00:
         DEVICE=X00.SYS 0=COM1 1=COM2 2=COM3 3=COM4
         BNU:
         BNU /P=4
         ---------------------------------------
         VCONFIG: Set Channel 1 to COM1
                  Set Channel 2 to COM2
                  Set Channel 3 to COM3
                  Set Channel 4 to COM4
         ***********************************************************