April 20, 1992

                        ROUTENAV Ver. 1.0
                       VFR FLIGHT PLANNER

     ******************
     *  INTRODUCTION  *     
     ******************
     Routenav is a very flexible graphics-based VFR flight planning
     program for private pilots and computer pilots. Listed below
     are only a few of the many features:

     NOTE:     When this manual refers to a navaid, it is
               referring to an airport, VOR, NDB, or any
               combination of these.  A waypoint is a navaid that
               has been selected as part of your route.

     *    Flight Plans:

          You may create manual flight plans (select every waypoint
          along the route), or automatic flight plans (select
          starting and ending airports (and an optional waypoint to
          overfly), and the computer will select the waypoints
          along the way).  The flight planning process is very
          flexible in that the computer displays all of the navaids
          along the route and, in automatic mode, selects the
          waypoints.  If you want to change the route, a navaid may
          be selected or deselected while viewing the route. 
          Specific information about a navaid (latitude, longitude,
          frequencies, runways, and distances from/to the
          previous/next waypoint,etc.) can also be displayed by
          selecting the navaid.  Once you are satisfied with the
          route, you then enter wind and altitude information for
          the route.  The program uses that information to
          calculate magnetic heading, distance, time, fuel,
          groundspeed, and descent information for the route.  You
          may then save the route to be recalled later, print it,
          and/or save it to disk as an ASCII file.

     *    PREVIOUS ROUTES:

          Previously saved routes may be easily recalled, viewed,
          or deleted.  When a route is recalled, the actual route
          is displayed along with the other navaids along the
          route.  You may edit the route by selecting or
          deselecting routes as previously described.


    *    NAVAID SELECTION:

          Finding the navaid you want is very easy.  If you know
          the name, or id of the navaid, you may enter it directly
          and the computer will search the database for it. 
          Selection may also be made by entering the two letter
          postal code for the state.  In this case, you would
          select the navaid from a list of all navaids from that
          state.  Selecting the navaid from a list of the entire
          database is another option for selection.

     *    NAVAID DATABASE:

          ROUTENAV allows new navaids to be added, and existing to
          be edited or deleted.  The navaid to be edited or deleted
          can be selected by name, id, state, or from the entire
          database.  The size of the database (number of navaids)
          is limited only by the amount of disk space available.

     *    AIRCRAFT DATABASE:

          Aircraft information used during flight planning may be
          added, edited, or deleted in the same manner as the
          navaids.  Again, with this database, the size (number of
          aircraft) is limited only by disk space.

     *    WEIGHT AND BALANCE:

          Weight and Balance may be calculated for any aircraft in
          the database.

     *    CONVERSIONS:

          A calculator is provided to convert fuel or distance. 
          Fuel may be converted between US Gallons, Imperial
          Gallons, and Liters.  Distance conversions may be done
          between Nautical Miles, Statute Miles, and Kilometers. 
          This calculator is provided only as a convenience,
          however.  ROUTENAV does not require you to manually
          convert anything, for it will automatically convert fuel
          and distance during the flight plan calculations
          utilizing the method of measurement you selected from the
          SETUP screen.


    *    FLIGHT SIMULATOR (tm) SELECTION

          ROUTENAV can be used just as easily for computer pilots
          as for private pilots.  When "Flight Simulator (tm) Only"
          is selected from the SETUP screen,  when ROUTENAV
          searches the navaid database, it will select only navaids
          that have a scenery defined.  By doing this, you do not
          have to sift through ALL of the navaids to find the ones
          available in Flight Simulator.


     ******************
     *  REQUIREMENTS  *
     ******************

     CPU:      IBM 286 or better
     Monitor:  EGA or VGA Monitor
               with graphics card.
     Hard 
     Drive:    At least 2 MB of disk space.
     Mouse:    A mouse is not required,
               but is recommended.
     Memory:   The program will make use of
               extended memory if it is available.
               If the program runs out of conventional
               or extended memory, it will use
               disk space to store data (this is why a
               Hard Drive is required).

     ******************
     *  INSTALLATION  *
     ******************

     To install ROUTENAV, simply go to the directory you want to
     use as the ROUTENAV directory and UNZIP the ROUTENAV.ZIP file. 
     For example, if ROUTENAV.ZIP is on drive A: and you wanted
     ROUTENAV in C:\ROUTENAV, you would go to the C:\ROUTENAV
     directory and type PKUNZIP A:ROUTENAV (assuming PKUNZIP.EXE is
     in the path).  The ROUTENAV files will then be uncompressed in
     the C:\ROUTENAV directory.  Type ROUTENAV to run the program. 
     The first thing you should do when you run the program is
     select SETUP from the main screen to enter your preferences. 
     

     ***************
     *  OPERATION  *
     ***************

     MAIN SCREEN:

     To move the cursor around the main screen, move the mouse or
     press the arrow keys.  Pressing SHIFT and the arrow keys
     allows you to move in smaller increments.  To select a menu,
     move the cursor to the menu block, and press the left mouse
     button or the ENTER key.  To exit the program, move the cursor
     to the EXIT button, and press ENTER or the left mouse button.

     SETUP:

     When the SETUP menu is selected, the SETUP screen is
     displayed.  Press the TAB key to move among the entry items
     (fields).  The fields may also be selected by moving the mouse
     cursor to the entry item, and pressing  the left mouse button. 
     Enter your name, the path for the main ROUTENAV files, and the
     path for the database files.  If a drive letter is not
     entered, the current drive is assumed.  Various Distance and
     Fuel measurements may also be selected from this screen.  If
     "FLIGHT SIMULATOR (tm) ONLY" is enabled, then only Flight
     Simulator Navaids will be selected for flight planning.

     AIRCRAFT DATABASE:

     The aircraft database menu allows you to add, edit, or delete
     aircraft.  
     ADD:      To add an aircraft to the database, first select
               the AIRCRAFT button, then select ADD AIRCRAFT.  You
               will be presented with the Aircraft Input screen. 
               Pressing the TAB key will scroll you through the
               various entry fields.

               To enter the Cruise IAS for the aircraft, select
               the CRUISE IAS button by clicking on it with the
               mouse, or moving the cursor (using the arrow keys)
               to the button and pressing HOME.  The Cruise IAS
               input screen will be shown.  Enter the IAS at
               different altitudes for the Aircraft.  For example,
               if the IAS up to 5,000 ft. is 115 Kts., the IAS at
               5,000 ft. is 120 Kts., and the IAS at 10,000 ft. is
               135 Kts., then you would enter 1000 for the
               altitude and 115 for the IAS, 5000 and 120, and
               10000 and 135.  ROUTENAV will make the cruise ias
               115 KTS/MPH from 1000 to 5000 ft., 120 KTS/MPH from
               5,000 to 9,000 ft., and 135 KTS/MPH from 10,000 ft.
               and above.  Select CONTINUE when you are finished.

         AIRCRAFT ENTRY FIELDS:

          N Number:      The N Number of the aircraft
          Description:   A description (make and model) of the
                         aircraft (20 characters maximum)
          Climb Rate:    The takeoff climb rate in FPM
          Descent Rate:  The rate of descent in FPM
          KTS/MPH:       The speed measurement you wish to use
          Takeoff IAS:   The takeoff IAS in KTS or MPH (whichever
                         you selected above)
          Descent IAS:   The descent IAS (when landing) for the
                         aircraft
          Cruise IAS:    The IAS at various altitudes
          Fuel Capacity: The amount of useable fuel (using the
                         fuel measure you selected from the SETUP
                         screen)
          Startup Fuel:  The amount of fuel burned during startup
                         of the aircraft
          Takeoff Fuel:  The amount of fuel burned during takeoff
          Cruise Fuel:   The amount of fuel burned (per hour)
                         during normal cruise flight
          Empty Weight:  The empty weight of the aircraft
          Max Weight:    The maximum fully loaded weight for the
                         aircraft
          Aircraft
          Moment:        The moment of the aircraft
          Forward Limit: The forward center of gravity (CG) limit
                         (INCH/MM) for the aircraft
          Aft Limit:     The aft CG limit for the aircraft
          INCH/MM:       Selects whether the Weight and Balance
                         Arms are in inches or millimeters
          Row 1 Arm:     The distance aft of the DATUM (INCH/MM)
                         for the first row of seats
          Row 2 Arm:     The distance aft of the DATUM (INCH/MM)
                         for the second row of seats
          Row 3 Arm:     The distance aft of the DATUM (INCH/MM)
                         for the third row of seats
          Row 4 Arm:     The distance aft of the DATUM (INCH/MM)
                         for the fourth row of seats
          Forward Arm:   The distance aft of the DATUM (INCH/MM)
                         for the forward baggage compartment
          Aft Arm:       The distance aft of the DATUM (INCH/MM)
                         for the aft baggage compartment
          Fuel Arm:      The distance aft of the DATUM (INCH/MM)
                         for the fuel


         Required Aircraft Inputs:

          Weight and Balance: Empty Weight, Maximum Takeoff
                              Weight, Aircraft Moment, Row 1 Arm,
                              and Fuel Arm.

          Flight Planning:    N Number and/or Description, all
                              airspeeds, all FPM rates, and Fuel
                              inputs (for fuel calculations).

     Edit:     To edit an aircraft record, select EDIT from the
               aircraft menu.  What happens next depends upon how
               many aircraft records already exist.  If there are
               no aircraft to edit, a message will be displayed
               informing you of this.  If there is only one
               aircraft in the database, you will be asked if you
               want to edit it.  If so, then you enter the
               Aircraft Edit screen to begin editing.  If you
               click the mouse button (or move the cursor and
               press home) on "NO", then you will exit back out to
               the Aircraft Database selection menu.  If the
               Aircraft Database contains more than one aircraft,
               you will be shown a list containing the N-Number
               and description of each aircraft and may then
               select one to edit by clicking on it, or select
               "CANCEL" to exit.

               When in the Aircraft Edit screen, you may change
               any or all information for the aircraft as you
               would when entering a new aircraft.

               NOTE:     A mouse may be used to select the entry
                         fields by moving the mouse cursor to the
                         entry field and pressing the left mouse
                         button.  THIS WORKS ON THE MAIN ENTRY
                         SCREEN ONLY!  IF YOU SELECT "CRUISE IAS"
                         AND USE THE MOUSE TO SELECT THE FIELDS,
                         THE PROGRAM WILL CRASH.  THIS WILL BE
                         FIXED IN A LATER VERSION.

     Delete:   To delete an aircraft, you simply select "DELETE"
               from the Aircraft Database select menu.  Options
               for selecting the aircraft are the same as for
               editing.  Once you select an aircraft to delete,
               you will be asked to confirm the deletion.  If you
               select "YES", the aircraft will be deleted (if
               "NO", then you will exit back to the Aircraft
               Database select menu).



    NAVAID DATABASE:

     Add:      To add a navaid to the Navaid Database, you first
               select the NAVAID button.  The Navaid Database
               select menu will then be shown.  Select ADD to add
               a navaid to the database.  NOTE:  The program does
               not check to see if a duplicate navaid exists, so a
               suggestion would be to select EDIT, then DATABASE
               to see a list of all navaids in the database.  You
               can then search the list for the navaid you want to
               add.  Select CANCEL from the selection list to
               return to the NAVAID DATABASE select menu.

               If you DO add a duplicate navaid, then every time
               you search for the navaid for flight planning or
               editing, you will have to select the one you wish
               to use.

               Once you decide you want to add a navaid to the
               database,  select ADD from the Navaid Database
               select menu to enter the Navaid ADD screen.
               You can select the various entry fields on the
               screen by pressing the TAB key.

               NAVAID ENTRY FIELDS:

               * ID:          A three letter/number combination to
                              identify the navaid.
               * Name:        The name of the navaid
                              (30 characters max).
               * State:       The two letter state postal
                              identifier.
               Elevation:     The elevation (in ft. MSL) of the
                              navaid.
               Mag. Var.:     The magnetic variation of the
                              navaid.  If you do not enter a
                              magnetic variation, 0E is assumed. 
                              If you are using Flight Simulator
                              (tm), and are not sure of the
                              magnetic variation, then you should
                              use the offset number shown on each
                              chart (the North and East
                              coordinates are canted clockwise or
                              counterclockwise to compensate for
                              orthagonal coordinate grid overlaid
                              on Lambert conformal conic
                              projection).  If the number is
                              positive, then the direction is
                              West.  If it is negative then the
                              direction is East.  For example, the
                              offset for the default scenery for
                              NY is +13.  This indicates 13W.
Type:The type of navaid.  The program
                              uses the following codes for the
                              navaids:  * = VOR and Airport or
                                            NDB and Airport
                                        V = VOR Only
                                        N = NDB Only
                                        A = Airport Only
               Description:   The description of the navaid
                              (VOR/Airprt, NDB/Airprt, VOR, NDB,
                              Airport).  You may enter any
                              description you wish (10 characters
                              max).
               Scenery:       If you intend to use this navaid for
                              Flight Simulator (tm), you must
                              enter the scenery description (Disk
                              number, file name, etc.).  When the
                              program is configured for Flight
                              Simulator Only, it will look for
                              this field when searching the
                              database to determine whether the
                              navaid is a FS navaid or not.
               * Latitude:    The Latitude in degrees and minutes
                              for the navaid.
               * Longitude:   The Longitude in degrees and minutes
                              for the navaid.
                              NOTE: If you know the North and East
                              coordinates, then you should use a
                              program such as COORDS.EXE to
                              convert North and East to Latitude
                              and Longitude.
               Comments:      Here you may add any comments you
                              wish about the navaid.
               Frequencies:   Select the FREQUENCIES button to
                              enter the frequencies for the
                              navaid.  A suggested ILS frequency
                              sequence is Runway Number/Runway
                              Direction/Frequency
                              (ex. 24/243/109.2).
               Runways:       Select RUNWAYS to enter the runway
                              numbers for the navaid.  A suggested
                              sequence is Runway Number/Runway
                              Length (Ex. 10L-28R/9500 X 150).
                              NOTE: The Navaid Database does not
                              contain frequencies (except VOR's)
                              and runway numbers for most NON
                              Flight Simulator (tm) airports.
               OK:            Select OK to save the navaid
                              information and exit.
               EXIT:          Selecting EXIT will abort the
                              procedure and exit without saving.

              NOTE:     A mouse may be used to select the entry
                         fields by moving the mouse cursor to the
                         entry field and pressing the left mouse
                         button.  THIS WORKS ON THE MAIN ENTRY
                         SCREEN ONLY!  IF YOU SELECT "FREQUENCIES"
                         OR "RUNWAYS" AND USE THE MOUSE TO SELECT
                         THE FIELDS, THE PROGRAM WILL CRASH.  THIS
                         BUG WILL BE FIXED IN A LATER VERSION.

     CONVERSION:

     The conversion section allows you to convert fuel and
     distance.  As previously stated, this utility is NOT needed
     for flight planning.  The flight planning part of the program
     will accept and calculate distance and fuel in any of the
     following three forms:
          Distance: Nautical Miles, Statute Miles, or Kilometers
          Fuel:     U.S. Gallons, Imperial Gallons, or Liters.

     To convert Distance or Fuel from one form of measurement to
     another, first select CONVERSION from the main screen.  You
     will be presented with the CONVERSION utility screen.

          Converting Distances:
               To select the measure of distance you want to
               enter, select the NAME of the distance measure. 
               For example to convert from Statute Miles, you
               would move the cursor to STATUTE MILES.  STATUTE
               MILES will change to white letters to show which
               distance measure is selected.  Selecting the
               numbered buttons will enter the number into the
               distance you selected.  When you are finished
               entering the number, select CALCULATE to calculate
               the other distances.  If you make a mistake while
               entering the number, select CLR to clear the entry
               and try again.
          Converting Fuel:
               To convert fuel, you must first select the FUEL
               button.  Distance selections will be replaced with
               Fuel selections.  The conversion process is the
               same for Distance.
          Exiting:
               To exit the Conversion screen,  select the small
               bar in the upper left corner of the screen.  At
               this point, if you select EXIT, you will exit the
               Conversion utility.  You may resume conversions by
               clicking the mouse outside the EXIT box.


    WEIGHT AND BALANCE:

     As with the Edit Aircraft Database Screen, the program checks
     for Aircraft in the database before you begin.  If none are
     found, you will be informed and return to the Main Screen.  If
     one is found, you will be asked if you want to use that
     aircraft for the weight and balance calculations.  If more
     than one exist, you are presented with a list from which to
     choose the aircraft you wish to use.

     To perform Weight and Balance calculations on an aircraft,
     first enter the Weight and Balance Forward and Aft limits,
     weight, arm, and moment information for the aircraft using the
     Aircraft Database screen.  If this information does not exist
     for the aircraft, you will be informed, and return to the Main
     Screen.

     Once you select the aircraft, the Weight And Balance screen
     will be displayed.  At this point, you enter the weight
     information for the various rows of seats in the aircraft. 
     First, choose whether the weight information will be in pounds
     or kilograms.  If your aircraft has less than four rows of
     seats, simply leave the excess rows at zero.  When you enter
     the fuel, it should be in the fuel measure you selected from
     the SETUP Screen.  Once all of the weight data is entered,
     select CALC to calculate the center of gravity.  If the center
     of gravity is within limits, a white dot will be displayed
     inside the borders of the weight and balance graph.  If the
     dot appears to the left or right of the borders (in the red),
     the Center of Gravity is outside of the range for the
     aircraft.  If the dot appears above the graph, the weight is
     over the limits for the aircraft.

     Select EXIT to return to the Main Screen.

    FLIGHT PLANNING:

     The flight planner is the heart of ROUTENAV.  As you will see,
     it is extremely versatile and informative.

     The first step to creating a flight plan is to select the
     aircraft you will be flying.  When you select NAVIGATE from
     the Main Screen, you will be asked to choose the aircraft.  If
     no aircraft exist (or the program cannot find any) then either
     there are no aircraft entered in the Aircraft Database, or the
     directory defined on the SETUP screen is not where the
     "AIRCRAFT.DAT" file is located.  If only one aircraft is
     defined, you will be asked if this is the aircraft you will be
     flying.  If more than one is found, you will be given a list
     of the aircraft from which to choose.

     Next, you are asked what type of flight plan you would like to
     generate.  The selections are explained below.

     AUTOMATIC:
          Automatic Flight Planning allows you to select the
          starting airport, ending airport, and an optional
          waypoint (Airport, VOR, or NDB) to fly over.  Once you
          have selected these two (or three), then the computer
          will find ALL of the navaids along your route.  It will
          also select waypoints from these navaids for you to fly
          over.

          When you select AUTOMATIC ROUTE, the next option is
          whether you want the computer to select all possible
          navaids for the route, or only VORs.

     MANUAL:
          In MANUAL flight planning, you select the starting
          airport and all other waypoints for your route.  ROUTENAV
          will then evaluates your route and select ALL of the
          navaids along the route.  The only waypoints that will be
          selected for your route are the ones you selected.

     Once you have selected AUTOMATIC or MANUAL flight planning,
     you will be asked to select the waypoints for your route. 
     There are four ways to select the waypoints:

     NAME:     If you know the EXACT name of the navaid (Case does
               not matter), you may select NAME, enter the name
               (and state if you know it), and the computer will
               search the database for the name.  If you enter the
               "NAME, STATE", the computer will search for NAME in
               STATE.  If more than one navaid is found, you will
               be given a list from which to choose.  Pressing
               CANCEL will return you to the Navaid Selection
               menu.
ID:If you select ID, you are asked for the
               3-characters of the ID.  The characters can be
               letters, numbers, or a combination. When you press
               ENTER, the computer will search for the ID.  If
               more than one is found, you will be given a list
               from which to choose.  Pressing CANCEL will return
               you to the Navaid Selection menu.
     STATE:    Selecting STATE allows you to search the database
               for all navaids found within a certain state.  When
               you select STATE, you are asked to enter the
               2-letter postal code for the state.  If you select
               CANCEL, you will return to the Navaid Selection
               Menu.  If you enter the 2 letter code, the program
               will search the database for all navaids in the
               state you selected.  You will be given a list from
               which to select the navaid.  To select the navaid,
               move the cursor to the navaid on the list and press
               the left mouse button (or the ENTER key).  If you
               decide not to select one of the navaids,  selecting
               CANCEL will cancel the operation and return you to
               the  Navaid Selection Screen.
     DATABASE: The DATABASE selection will give a list (after the
               program generates the list) of all navaids in the
               database.  The list could never be long enough to
               display all of the navaids at once, so the first
               fifteen or so will be displayed.  Along the side of
               the list is a bar.  Selecting the UP or DOWN arrow
               on the bar will scroll the list up or down.  You
               can manually (and quickly) move through the list by
               selecting and holding the small box between the
               arrows, and moving it (using the mouse or arrow
               keys) up or down.  When you release the box, the
               list will display the navaids for that section of
               the list.  To select the navaid, move the cursor to
               the navaid on the list and press the left mouse
               button (or the ENTER key).  If you decide not to
               select one of the navaids,  selecting CANCEL will
               cancel the operation and return you to the  Navaid
               Selection Screen.

     Once you are finished selecting the navaids, select FINISHED
     from the menu to continue with the flight planning.

    PREVIOUS:
          The PREVIOUS option allows you to work with previously
          saved routes.  If no routes have been saved, a message
          will appear stating this.  From the Previous Route
          Screen, you may select:
          NEXT:     To see the next page of routes, if it exists
                    (four are displayed per page).
          PREV:     To see the previous page of routes, if it
                    exists.
          EXIT:     To return to the Main Screen.

          For each saved routes, you may:
          DELETE:   Delete a saved route.  You will be asked to
                    confirm this.
          VIEW:     To view the waypoints for the route.
          RECALL:   To recall a saved route for flight planning.


     After you either select FINISHED from the Navaid Selection
     Menu or have recalled a saved route, the Flight Planning
     module is loaded.

     NOTE:     The Screen will go blank while the Flight Planning
               module is loading.  THIS IS NORMAL.
     
     After the Flight Planning module is loaded, the screen will
     clear, and the navaid selection begins.  The program searches
     the database (in alphabetical order) to find all the navaids
     along you route.  You will be shown which waypoints the
     program is searching between and which navaids are found.

     When all of the navaids have been found, the screen will again
     blank and the Route Selection Screen will be shown.  This
     screen shows all of the navaids that were found along your
     route.  If you have selected an automatic flight plan, the
     waypoints for the route will be automatically selected.  If
     you have selected a manual flight plan, the only waypoints
     selected will be the ones you selected.  If you have recalled
     a previously saved route, the selected waypoints will be those
     that were selected when the route was saved.

     The colors of the navaids will tell you what type of navaid it
     is.  Blue is a Navaid (VOR or NDB) with an Airport, Green is
     a VOR only, Yellow is an Airport only, and Red is an NDB only.

     The three character ID of the navaid is shown in white.  If
     you move the cursor to ANY navaid on the screen, you will be
     shown the ID, Name, and State of the navaid.


    SELECTING A NAVAID FOR THE ROUTE:
          If a navaid is not selected as part of the route, you may
          include it in the route by moving the cursor to it and
          pressing the left mouse button (or pressing HOME).  If
          you press the left button again, the navaid will be
          de-selected.
     NAVAID INFORMATION:
          Getting information about any navaid on the screen is
          quite easy.  You simply move the cursor to the navaid and
          press the RIGHT mouse button (or PG UP key).  The
          information you are given depends on the type of navaid
          it is.  If the navaid contains an airport, you will be
          shown information (ID, Name, State, Elevation, Latitude,
          Longitude, etc.) about the airport.  There will also be
          two buttons shown.  Select the FREQUENCIES button to get
          the frequency information about the airport.  Select the
          RUNWAYS button to see the runways for the airport.

          If the Navaid is a VOR or NDB only, you will be shown
          only the navaid information (ID, Name, State, Elevation,
          Latitude, Longitude, etc.) and the frequency.

          Additionally, if the navaid you have selected is a
          waypoint (part of the route), you will be shown the
          distance and true course to/from the next/previous
          waypoint.

          To return to the Route Selection Screen, select the OK
          button.  When you are satisfied with the route, select
          the CONTINUE button to continue the flight planning
          process.  If you want to abort the flight plan and return
          to the Main Screen, select EXIT.


         The next step for flight planning is entering the
          altitude and wind information:
          VFR Flight:    If you are flying a VFR Flight, the 
                         altitude you fly is determined by the
                         direction you are flying.  If your
                         direction is between 000 and 179 degrees,
                         you must fly an ODD altitude + 500 ft. 
                         If the direction is between 180 and 359
                         degrees, the altitude must be an EVEN
                         altitude + 500 ft.  If you select this
                         item, then the computer will
                         automatically change the altitude if you
                         change directions.  For example: Your
                         true course is 200 degrees, and you
                         select an altitude of 4,500 degrees. 
                         Along the route, your true course becomes
                         165 degrees.  The computer will change
                         your altitude to 5,500 ft..  If your
                         course then changes to 195 degrees, the
                         computer will change the altitude back to
                         4,500 ft.
          ALTITUDE:      This is where you enter the altitude you
                         wish to fly.  NOTE:  If you select VFR
                         Flight, the computer will NOT check to
                         ensure you enter a proper altitude.
          WIND:          If you selected a Waypoint to Overfly
                         from the Main Screen, this waypoint will
                         be the VIA waypoint.  If not, the VIA
                         waypoint will be the one closest to the
                         middle of your route.  Enter the Wind
                         Direction and speed for the Starting,
                         Ending, and VIA navaids.  The computer
                         will calculate the wind correction angle
                         for each leg of the flight.
          DESCENT:       Select this to descend to pattern
                         altitude (800 ft. MSL) for the Ending
                         airport.
          DESCENT Input: If you do not select a pattern altitude
                         descent, you will need to enter the
                         altitude you wish to descend to. 
                         ROUTENAV will calculate when you should
                         start to descend based upon this
                         altitude.
          CONTINUE:      Select CONTINUE to display the Flight
                         Plan.
          EXIT:          Select EXIT to abort the flight plan and
                         return to the Main Screen.


    When you select CONTINUE, the flight plan will be displayed. 
     
     In the upper left corner of the screen you will see your name,
     the three main waypoints (Starting, Ending, and VIA), and the
     Totals (Distance, Time, and Fuel).

     The upper right portion of the screen displays the aircraft
     and its parameters.

     The lower left portion of the screen displays descent
     information for the destination airport.

     The lower right portion of the screen provides the various
     button selections.

     The actual flight plan is displayed in the center of the
     screen.  Full descriptions are given for the Starting and
     Ending airports (Runways, Frequencies, etc.).  Brief
     descriptions are given for each waypoint along the route
     (navaid specifications, frequencies, etc.)

     The Altitude, Distance (in the unit of measure you selected),
     True Course, Magnetic Heading (True Course compensated for
     magnetic variation and wind), Groundspeed, Indicated Airspeed
     (for the altitude you are flying), Estimated Time Enroute
     (ETE), and Fuel consumption are also given for each leg of the
     route.

     MENU SELECTIONS:
          The following menu selections are available from the
          Flight Plan Screen:

          NEXT:     Display the next page of the route (if
                    available).
          PREV:     Display the previous page of the route (If
                    available).
          SAVE:     Saves the route for later recall.  
                    NOTE: The program allows up to 999 routes to
                    be saved.  The routes are stored as ROUTE.XXX
                    files, where XXX is a consecutive number from
                    001 to 999.  The directory will be the DATA
                    DIRECTORY you defined in SETUP.  A message
                    will be displayed to tell you the flight plan
                    was saved.

         OUTPUT:   The OUTPUT selection provides the following
                    selections:
                    PRINT:    prints the flight plan (if the
                              printer is connected and on-line).
                    FILE:     Saves the flight plan to an ASCII
                              file.  The file will be labeled
                              FLITEPLN.XXX where XXX is a
                              consecutive number from 001 to 999. 
                              The file will be saved to the DATA
                              DIRECTORY you defined in SETUP.  A
                              message will be shown to tell you
                              the file was saved.
                    BOTH:     The flight plan will be printed and
                              saved to an ASCII file.
                    CANCEL:   Selecting CANCEL will abort the
                              OUTPUT selection.

          EXIT:     Select EXIT to return to the Main Screen.

DISCLAIMER:   The author is not liable for any damage or injury
               resulting from the use of this product.

     You, as pilot, should always double check the resultant flight
     plan against your charts for accuracy.  ROUTENAV will not
     account for minimum heights along your route.

CREDITS:  Flight Simulator (tm) is a product of Microsoft
          Corporation.


Help or Information:    You may call (716) 647-2643 and get help 
                        or information on any questions concerning 
                        ROUTENAV.  If I am not available to answer 
                        the call, leave a message and I will call 
                        you back.