EZPLACE HELP FILE

                          Version 3.10

                        SEPTEMBER 6, 1991



                     Leading Edge Industries

                       2120 Myrtle Avenue

                    St Paul, Minnesota 55114

                         (612) 645-5254


                              and


                         101 Eagle Drive

                  Balsam Lake, Wisconsin 54810
$TOF

                      THE PURPOSE OF EZPLACE

 EZPLACE is a program designed to allow ANYONE to enter parts,
 placements and geometries of existing or custom Wire Wrap boards
 and Printed Circuit Boards (PCBs).  EZPLACE has several purposes:

     o   Simplify entry and reduce errors inherent in placing
         parts on pre-pinned wire wrap boards.

     o   Allow users to place components where THEY want them.


 The data created by this program allows Leading Edge to deliver
 to the user a Wire Wrapped assembly or PCB.  The user should:

     o   Specify a board geometry or template

     o   Specify board outlines and keep-out areas

     o   Create special parts

     o   Place parts where desired

     o   Send the data to Leading Edge


 EZPLACE was written by Rod May in 1990.  Dan Stover and Greg
 Volk modified it in 1991 to include Library Part Creation,
 Excellon Board Template Input, Redac Output, Keep Out Areas,etc.
$TOF

                        TABLE OF CONTENTS

I.   INTRODUCTION

     1.  License to Use
     2.  About Leading Edge
     3.  Free Updates
     4.  Hardware Requirements
     5.  Definitions

II.  USING EZPLACE

     1.  Setup
     2.  Files
     3.  Operation

III. MENU REFERENCE

     1.  [A]DVANCED MENU
     2.  [F]ILE MENU
     3.  [K]EEP OUT MENU
     4.  [L]IBRARY MENU
     5.  PART COMMANDS
     6.  CURSOR AND MAGNIFICATION COMMANDS

IV.  BOARD TEMPLATES

     1.  Sources
     2.  Format
     3.  Example

V.   LIBRARY

     1.  Definition
     2.  Supplied Library Parts
     3.  Creating Library Parts
     4.  Editing  Library Parts
     5.  Duplicating Library Parts
     6.  Removing Library Parts
     7.  DON'T INITIALIZE LIBRARY
         UNTIL YOU READ THIS!
$TOF
VI.  PLACING PARTS

     1.  Locating
     2.  Rotating
     3.  Inserting
     4.  Deleting
     5.  Moving

VII. KEEP OUT AREAS

     1.  Definition
     2.  Placing 'Keep Out' Lines
     3.  Uses for 'Keep Out' Lines

VIII.OUTPUT

     1.  What is Redac?
     2.  Redac Output
     3.  Net Lists

IX.  FUTURE

     1.  Board Templates
     2.  Net List Entry
     3.  Off-Grid Parts
$TOF

I.   INTRODUCTION

     1.  License to Use

         There are NO restrictions on using EZPLACE!  You may
         use it for Personal, Commercial or Industrial purposes.
         You may give it to ANYONE (including competitive
         companies) as long as the credits are displayed when
         it is executed.

         You will note the output is in ASCII, Redac format,
         possibly the most common interface specification known.
         No attempt is made to make use of the output difficult,
         please use it.

     2.  About Leading Edge

         Leading Edge Industries are Minnesota Corporations
         with Corporate offices in St Paul, MN and manufacturing
         plants in St Paul, MN and Balsam Lake, WI.

         Leading Edge Design (LED) produces PCB designs,
         layouts and custom software in response to an engineers
         manual or CAE design.

         Leading Edge Assembly (LEA) is a quality vendor of Quick
         Turn and production volume Wire Wrap assemblies.  LEA
         does board stuffing, mechanical and electronic assembly
         and miltary subcontracting. LEA claims 7 Vertical, 3
         Horizontal and 5 Semi-Automatic Wire Wrap Machines.

         Leading Edge Circuits (LEC) produces Quick Turn and
         small production quantities of Printed Circuit Boards
         (PCB) for a wide range of customers and usages.  LEC
         fabricates PCB boards, down to 5 mil lines and up to
         10 layers.

         If you need it done, Leading Edge can do it!

     3.  Free Updates

         Write or call Leading Edge with your Company, Name,
         Address and Telephone Number and we'll mail you free
         updates and bug corrections.

         There are more board templates available, if interested
         please call.  If you have a board template you wish to
         make available to the world, send it in.

     4.  Hardware Requirements

         A.  IBM PC 512K minimum memory

         B.  Floppy disk drive or method of transferring files

         C.  Hard Disk drive

         D.  EGA or VGA monitor

     5.  Definitions

         A.  CURSOR

             A cursor indicates where attention is currently
             being focused.  For the purposes of EZPLACE a
             part acts as the cursor, the default being a one-
             pin 'TPOINT', shown as a white box.  When you
             [C]hange Part, say to a 14-pin DIP, the new part
             becomes the cursor and is shown in white.  Power
             (Light Red) and Ground (Light Cyan) pins are shown
             to aid placement.  Position the cursor where you
             want to [I]nsert parts onto the board.

             In [L]ibrary Mode the cursor is the next pin to be
             placed and in [K]eep Out Mode the cursor is the next
             'Keep Out' Line to be placed.

         B.  SCROLL

             While positioning a part or drawing a line, Pin 1
             of the part or cursor might go beyond the viewport
             on screen.  In this case the board is redisplayed
             with Pin 1 of the cursor centered on the screen.

         C.  ZOOM

             The viewport on screen shows up to 20 x 20 inches
             of the board.  Since this looks small on a CRT, a
             magnification factor ranging from 2 (whole board)
             to 16 (chip level view) dots per 100 mils has been
             included.  Change the magnification with [Shift]
             PgUp/PgDn and [A]dvanced [M]agnification keys.
$TOF

II.  USING EZPLACE

     1.  Setup


         Create your directory by typing MKDIR EZPLACE
         Move to that directory by typing CD EZPLACE
         Prepare to use easy place by then typing
         'pkunzip a:\ezplace'. This will load all necessary
         files into the directory "EZPLACE" as well as a
         "DEMO" design.

     2.  Files

         There are several file types generated at one point
         or another in the EZPLACE process:

         A.  *.BRD and *.GRD files are the Excellon (Text) and
             binary formats of board templates.

         B.  LIBRARY.BIN contains the library parts.  [F]ile
             [R]estoring from the floppy archive overwrites
             this file, therebye deleting any custom parts
             which were not present when the archive was created.

         C.  *.JOB files hold the actual EZPlace parts data.
             At this time the user is allowed 1000 parts per
             design.

         D.  *.KOA files contain the 'Keep Out Area' lines and
             'Board Outlines'.  At this time the user is allowed
             1000 lines per design.

     3.  Operation

         A.  If you desire a specific board template, assure that
             the *.BRD template file is in your directory.  If no
             Board template is specified, EZPlace will assume all
             grid locations are valid for placement.  See BOARD
             TEMPLATES(IV) for how to create a *.BRD Excellon file.

         B.  Type 'EZPLACE'.

         C.  Place your board or print on a convenient surface,
             COMPONENT side up.

         D.  Establish a reference point (0,0) at the UPPER
             LEFT corner of your board.  This point should be on
             a 100 mil grid, but need not be an actual pin.  ALL
             placed pins must be below and to the right of this
             point as EZPLACE uses only positive coordinates.

         E.  To begin a new JOB enter the desired Board Template,
             if you want one (see Step A), selected from the
             [F]iles [B]oard menu entry.  Please note that the
             Board Template is optional and exists to only to aid
             the user.

             OR...

             To load an existing JOB use the [F]iles [L]oad or
             [F]iles [M]erge menu entries.  The Board Template
             formerly assigned to the job will be loaded.

         F.  If creating a new design use the [K]eep Out Menu to
             draw a board outline.

         G.  [C]hange cursor to the first part you wish to place
             or do a [L]ibrary [C]reate Part if the specified part
             does not yet exist.

         H.  Move the cursor part using the arrow keys or shifted-
             arrow keys and the [R]otate option.  Use [I]nsert Part
             to place a part at the current cursor position and the
             [D]elete and [M]ove Part options to alter previously
             placed parts. Continue placing, using [C]hange Part to
             get a new Library Part.

         I.  After placing all parts on the board use the
             [K]eep Out Menu to enter your 'Keep Out Lines'.
             Note that these 'lines' need not describe a closed
             figure.

         J.  Save the JOB using the [F]iles [S]ave option.
             Enter a new job name or confirm the old name.

         K.  After completing the job, use the [F]iles [A]rchive
             option to save all relevant files to a floppy.  Send
             this floppy to Leading Edge for wrapping or layout.

             Please note that only one job may be archived per
             floppy disk.  Only the last job archived on a floppy
             is available for use.
$TOF

III. MENU REFERENCE

     1.  [A]DVANCED MENU

         [I]nitilize LIB
             Delete ALL existing parts from the library with
             the exception of the 'TPOINT' part.  BEWARE!

         [M]agnification
             Set the magnification factor directly (from 2 to
             16 dots per 100 mils).

         [P]rint Menu

             [B]oard Description
                 Print a graphical representation of the board
                 template onto a generic printer.

             [M]anual Print
                 Prints this manual to LPT1.

             [E]pson Printer
                 Print the board on an Epson printer.

             [8]0 Column Printer
                 Specifies 80 column printer.

             [1]32 Column Printer
                 Specifies 132 column printer, default value.


     2.  [F]ILE MENU

         [D]elete Job
             The *.JOB and *.KOA files are deleted from Disk.

         [L]oad Job
             Input *.JOB and *.KOA files.

         [M]erge Job
             Input *.JOB and *.KOA files to current job.

         [S]ave Job
             Output *.JOB and *.KOA files.


         [A]rchive
             Copy all required files to floppy disk.  The
             disk then may be sent to Leading Edge for Wire
             Wrapping or PCB Layout.

         [R]etrive Archive
             Bring data in from an archive floppy and put it
             into the current directory.  Display the job.


         [B]oard Template
             Input *.BRD Excellon Board Template file.

         [W]rite Template
             Output current template to *.BRD Excellon file.

         [O]utput Redac
             Output the *.CDI Redac file.


     3.  [K]EEP OUT MENU

         [I]nsert Line
             Enter the cursor line as a 'Keep Out' and begin a new
             line at the movable end.

         [D]elete Line
             Delete the closest 'Keep Out' line to the cursor.

         [BACK]up Line
             Delete the last 'Keep Out' line entered.

         [CR] New Line
             Move the fixed end of the cursor line to the movable
             end, thus allowing a new line to be entered.


     4.  [L]IBRARY MENU

         [C]reate Part
             Create a new library part from scratch.

         [D]uplic Part
             Duplicate an existing part and edit the copy.

         [E]dit Part
             Edit the selected library part.  Addition pins may
             be added as in [C]reate or existing pins deleted
             with the backspace key.

         [R]emove Part
             Remove a library part from the library.  BE CAREFUL!


     5.  PART COMMANDS

         [C]hange Part
             Highlight cursor device type using the arrow keys
             and Select it with [CR].  The new cursor device type
             will be used each [I]nsert Part until changed again.

         [D]elete Part (also [DEL])
             Highlight device to delete using the arrow keys and
             Select it with [CR].  Confirm the deletion.

         [I]nsert Part (also [INS])
             Place a new part at the current cursor location and
             name the part.  The part will not be placed if any
             portion of the part is outside the placement area
             or if the name is already used on the board.

         [M]ove Part
             Highlight device to move using the arrow keys and
             Select it with [CR].  Use the arrow keys and [R]otate
             Part to reposition and [I]nsert Part as above.

         [R]otate Part
             Rotate the cursor part 90 degrees clockwise.

         [BACK]up Part
             Delete the last device entered.


     6.  CURSOR AND MAGNIFICATION COMMANDS

         [->] and all other arrows
             Move the cursor 1 pin in the arrow direction.

         [Shift] [->] and all other arrows
             Move the cursor 10 pins in the arrow direction.

         PgUp/PgDn
             Increase/decrease magnification incrementally.

         [Shift] PgUp/PgDn
             Increase/decrease magnification by 2.

         Home/End
             Refresh the display centered on cursor/center.

         [Shift] Home/End
             Zoom all the way in/out.
$TOF

IV.  BOARD TEMPLATES

     1.  Sources


      a) If you desire a custom board template, then you must
         first design a part or parts which results in the desired
         hole pattern, duplicate that part where needed, adding
         it and other parts until all the holes on the custom
         board exist.

         To save this template then you enter [F][W] and give the
         new *.BRD file a name; for example "BILL".  EZPlace will
         write a file "BILL.BRD" which may be used ever after as
         your Wire-Wrap Board Template.

         The board you described may be either one you purchase
         or Leading Edge can fabricate and pin or socket that
         board for you.  [F][A] produces all the files to send
         Leading Edge for a quote to be generated.


      b) If you desire a specific board, drilled, socketed or
         pinned you place parts until all the holes on the custom
         board exist and all parts are in place.

         To save this template then you enter [F][W] and give the
         new *.BRD file a name; for example "BILL".  EZPlace will
         write a file "BILL.BRD" which may be used ever after as
         your Wire-Wrap Board Template.

         The board you described may be either one you purchase
         or Leading Edge can fabricate and pin or socket that
         board for you.  [F][A] produces all the files to send
         Leading Edge for a quote to be generated and the board
         built.


      c) If you have a fully pinned board or complete confidence
         (snicker,snicker) in your measurements, the default
         grid is there waiting for you.
$TOF
     2.  Format

         You can also hand enter a board template using the
         following format.  All normal Excellon punctuation is
         acceptable, but not required.  The default format for
         EZPLACE is Leading Zeros, two integer places:

             o   X 1"       Y 2"       entered as  X010Y020

             o   X 1.5"     Y 2.1"     entered as  X015Y021

             o   X 0.1000"  Y 0.2000"  entered as  X001Y002

     3.  Example

           X001Y001
           X002
           X003
           X004
           X001Y002
           X002
           X003
           X004
$TOF

V.   LIBRARY

     1.  Definition

         The library is a collection of Supplied and Custom part
         types from which the user selects the cursor, which in
         turn is used for part placement.  Magnification will be
         initialized to 16 dots per 100 mils in library mode.

     2.  Supplied Library Parts

         EZPLACE is shipped with a supplied library composed of
         Single Inline Packages (SIP) and Dual Inline Packages
         (DIPS) of various sizes.  The normal makeup of the
         default library will be SIPs from one(1) to forty(40)
         pins, DIPS from six(6) to forty(40) pins. The user may
         not edit or delete these parts.

         From version to version this library may change,
         therefore you should keep the old versions of EZPLACE
         when a new one arrives.  The library structure may be
         different and your old design could have problems.
         Each new primary version (3.xx,4.xx,5.xx) will remain
         compatable and should have its own directory.

     3.  Creating Library Parts:  [L]ibrary [C]reate

         Using the arrow keys, position the cursor pin and press
         [INS], [I]nsert, [P]ower or [G]round. The cursor becomes
         part of the device and an incremented cursor is positioned
         in the same direction as the last arrow key pressed.
         If you make an error, [D]elete/[DEL]ete the last pin
         placed.  Press [ESC] to finish and confirm the new part.
         When you add a Library Part, it will appear at the end of
         the displayed list of available parts.

         The part pins MUST be on a 100 mil grid.  If you need
         to place an off-grid part, create a part which takes
         up the same space as this and has the same number of
         pins.  Add a note to the files sent regarding the exact
         part description.  This will be added into your board.

     4.  Editing Library Parts:  [L]ibrary [E]dit

         Much the same as creating a new part, except you start
         where you left off last time.

     5.  Duplicating Library Parts:  [L]ibrary [D]uplic

         A cross between creating and editing a part.  Select an
         existing part, name the new part as in [C]reate and edit
         as in [E]dit.
$TOF
     6.  Removing Library Parts:  [L]ibrary [R]emove

         Move the arrow to the part you want to delete, press
         [CR] and presto, it's gone.  EZPlace will check that
         you have no parts on the current board of this type.
         You must use caution with this option since you may
         have boards not currently loaded which use this part
         type.  You cannot delete the supplied library parts
         with this option (see Initialize Library).

     7.  DON'T INITIALIZE LIBRARY UNTIL YOU READ THIS!

         The entire Parts Library is stored in a file called
         LIBRARY.BIN.  If for any reason this file disappears,
         you will have only the TPOINT part to work with.

         [L]ibrary [I]nitialization develops a completely new
         Parts Library and will destroy ALL but the TPOINT part.
         You should use this option ONLY for unusual situations
         and place your new LIBRARY.BIN in a special directory.
$TOF

VI.  PLACING PARTS

     1.  Locating

         Once a part has been [C]hanged from the Parts Library
         selection menu, it appears in the placement window as
         a rectangular box with pin one indicated by a small
         square.  This is your cursor.  Use the arrow keys and
         [Shift] arrow keys to position the cursor and PgUp/PgDn
         or [Shift] PgUp/PgDn to increase/decrease the
         magnification.

     2.  Rotating

         Press [R]otate to rotate the cursor part 90 degrees
         clockwise about pin one.

     3.  Inserting

         Once the part properly located, press [I]nsert to fix
         it at that location.  Then respond to the part name
         prompt (U01,P3,R16,etc).

     4.  Deleting

         Press [D]elete and select which part to delete from the
         parts menu.  Confirm your deletion with [Y]es.

     5.  Moving

         To Re-place an existing part use [M]ove Part and select
         which part to move from the parts menu.  Then move or
         [R]otate the cursor as before, remembering that the next
         time you [I]nsert a part, it will move the part you
         just selected to the current cursor location.  You can
         type [ESC] to leave the part where it was.
$TOF

VII. KEEP OUT AREAS

     1.  Definition

         Every board has some area in which wires are not desired,
         even if merely the extents of the board itself.  The
         EZPlace 'Keep Out' capability allows the user to exclude
         wires from entering restricted areas, thereby controlling
         wire placement.

     2.  Placing 'Keep Out' lines

         Using this feature requires that you:

             o   Enter [K]eep Out mode from the Main Menu

             o   Use the arrow keys for cursor movement

             o   Use [Shift] PgUp/PgDn for magnification

             o   [I]nsert/[INS]ert 'Keep Out' when positioned

             o   [D]elete/[DEL]ete the last 'Keep Out' entered

             o   [ESC] to return to the Main Menu

         Please note that the lines are kept with the JOB, not
         the board template.  This allows different 'Keep Out
         Areas' on the same physical board.

         Don't overdo the 'Keep Out Areas'.  You could make it
         IMPOSSIBLE to build the board!  If this is done, you'll
         be hearing from the programming group.

     3.  Uses for 'Keep Out' lines

         One obvious use is to keep wires from going over an area
         where something exists that might hinder assembly or
         cause reliability issures in the future.

         Another usage is to use just a single line, not a 'Keep
         Out', but rather a 'Don't Cross' line.  This is useful
         to make the finished product look neater, control the
         direction of wires leaving a connector, isolate a noisy
         section of the board, etc.

         Leading Edge's Wire Wrap program will not allow a wire
         to touch any 'Keep Out' line.  Vertical 'Keep Out' lines
         tend to make the wires follow vertical channels, but too
         many lines tend to make wire lengths longer.

$TOF

VIII.OUTPUT

     1.  What is Redac?

         The Redac CAD system is one of the oldest CAD systems
         available in the US.  As such, Leading Edge Assembly
         selected it to be the output format for EZPLACE.

         At LEA information from EZPLACE is read directly into
         a Redac CAD system for plotting, error checking and
         output to the Wire Wrap program.

     2.  Redac Output

         When this is selected, from the [F]iles option, a Redac
         *.CDI file is generated which is an initial data file
         for the Redac system.  A new job is created in the
         Redac CAD system and the input is error checked and
         brought up for display and plotting.

         An incidental benefit to this is that since Leading
         Edge Assembly has a sister company, Leading Edge
         Design, which does PCB layout, the output from EZPLACE
         is also direct input to the Layout group.  The users
         board can be turned into a PCB at a 25% cost reduction
         over other options.  This is because the user has
         already specified the components and locations,
         reducing the designer's work.

     3.  Net Lists

         The Redac Netlist format is:

             .REM NET23               { Net Name           }
             U01 1 U02 2 U03 3 U04 4  { Any Number of Pins }
             U04 4 U05 5 U06 6        { Continuation line  }
             U06 6 U07 7              { Duplication OK     }
             .REM NET24               { Start of new net   }
             U22 2 U23 3
             .REM POWER

         Alpha pin designators are allowed but discouraged.
         Although Redac format is preferred, a netlist in any
         format is acceptable, for example:

             o OrCad         o ViewLogic     o Valid
             o PCad          o Mentor        o Calay
             o Case          o Daisy         o FutureNet
$TOF

IX.  FUTURE

     1.  Board Templates

         There are plans to indicate Power(Red) and Ground(Cyan)
         pins on the board templates to aid proper placement.

     2.  Net List entry

         Facility will be added to enter, check and transmit
         Power/Ground/Signal nets.  This will aid layout and
         Wire Wrap of the boards and reduce production times,
         errors and programming cost significantly!

     3.  Off Grid Parts

         Some faculty will be added to allow parts which either
         are placed on a location which is not on a 100 mil
         grid, or has pins which are not on a 100 mil grid.

         For now, enter the correct number of pins, make a part
         which takes up the correct amount of space, and send a
         part description with the floppy for fabrication.