Warning
                      =======

1: Design Filters:
------------------

The filter design section is based upon theoretical mathematical
models.  Attenuation levels beyond 90 db for Bandpass and Lowpass,
and beyond 70 db for Highpass and Notch are difficult to obtain
with real world hardware.  The passband noise for any filter is
directly proportional to the highest Q value used to implement 
that filter. Therefore, the best possible dynamic range in the 
filter passband can be obtained by avoiding Q values higher than 10.


3: Implement Filter:
--------------------

********************************************************************
* This filter program works with theoretical calculations and      *
* assumes perfect SCF biquads.  Unrealistic, unrealizable resistor *
* values may be generated for extreme filter cases.  Since LTC     *
* devices are real world ICs, designs must be verified first by    *
* breadboarding to ensure they are realistic.                      *
* LTC will support all filter designs with its devices.            *
* For help call Applications : 408-432-1900                        *
********************************************************************

1. Dynamics are optimized in this version for all sections
   implemented in mode 3A.

2. Modes can be mixed, ie 1, 2, and/or 3 when applicable, and R1
   values have been adjusted to maintain less than or equal to 0 db
   at the filter's output.  Extreme filter cases (i.e. decade wide
   bandpass filters) may cause nodes other than the output node to
   exceed 0 db.  Be careful, breadboard and/or call LTC for advice.

More Information about filter design is contained below:
	A filter Mode defines a specific filter topology.  LTC
data sheets define many such modes for a variety of reasons.  In
the design of FCAD, it was decided to limit the mode choices to 
1, 2, 3, 3A, 6A and 6B because these modes will cover all
practical designs.  However, in some specific cases a few
additional modes may be required for optimum performance.  In 
these cases assistance is available from the LTC Applications
group to help optimize your design.
  	LTC fully supports all filter hardware design efforts that 
involve LTC parts.  LTC is a linear integrated circuit manu-
facturer, not a software vendor, and as such cannot promise to
fully correct all FCAD software errors or omissions (although
we will try). It is hoped that the text that follows explains the 
mode selection criteria.
	Feedback from users is always appreciated and solicited.

	LOWPASS FILTERS:

	Case 1:  All Fn are infinite  such as Butterworth, 
Bessel, Chebyshev and custom filters with infinite Fn.  This case
allows only Modes 1, 2, 3, 6A or 6B to be used.  Modes 6A and 6B
are 1st order circuits and can be used only in the last stage
of an odd order filter where there is a finite fo and Q=0.
However, instead of Modes 6A or 6B you may use a 1st order low-
pass RC network whose resistor and capacitor are calculated
using the formula fo (last stage)= 1/(2piRC).  Of course, this
network is not clock tuneable.

	Case 2:  All Fn are finite.  Only Mode 3A is allowed in
this case where each stage has a finite Fn or each stage has a
finite Fn except the last stage which has either Fn=Infinity 
(2nd order section) or Q=0 (1st order section).  Although Mode 3A
is a second order circuit, FCAD requires entering Mode 3A in the 
last stage of an odd order even though a 1st order section is
indicated.  The program will then calculate the proper resistor
and capacitor values.

	HIGHPASS FILTERS:

	Case 1:	 All Fn equal 0 such as Butterworth, Chebyshev
and custom filter with all Fn equal 0.  Only Mode 3 and 6A
are allowed in this case.  If the last stage is 1st order (Q=0),
only Mode 6A is allowed by FCAD.  Mode 6A can be replaced by
a 1st order RC highpass network whose resistor and capacitor
values can be calculated by the formula fo (last stage) = 1/
(2piRC).

	Case 2:  All Fn are finite and not 0.  Only Mode 3A is 
allowed in designs with a finite Fn (not equal to zero) in each
stage, or with a finite Fn (not equal to zero) in each stage except
the last which has Fn=0 (2nd order section) or Q=0 (1st order 
section).  When the last section is 1st order, FCAD requires
Mode 3A be selected (See Lowpass).  The resistor and capacitor
values are calculated by the program.  Of course, this network
is not tuneable.

	BANDPASS FILTERS:

	Case 1:  All Fn equal 0 or infinity (Butterworth, Bessel 
and Chebyshev bandpass designs).  Only Modes 1, 2 and 3 are allowed
for this case.

	Case 2:  All Fn are finite and not 0.  Only Mode 3A is
allowed in this case where each stage has a finite Fn (and not 0)
or each stage has a finite Fn (and not 0) except the last stage
has Fn equal to zero.

	NOTCH FILTERS:

	Only Mode 3A is allowed for all Notch filter cases.  

	CUSTOM FILTERS:

	Custom filter design is a non-trivial pursuit.  Experts in
the topic are few and far between.  Design of a custom or non-
traditional filter presumes a fair amount of knowledge about filter
design.  A good example occurs in the design of Mode 3A sections
useful in the design of Elliptic filters or custom filters with
"notches" (also known as Fn's).  The calculations of FCAD do not
allow Mode 3A to be used with an infinite Fn value except if this
value occurs in the last filter section.  But, what can be done
is to make Fn large to the extent that it does not affect the filter
response while not making it infinite. This allows the program to
not deal with divide by zero and other related pure mathematical
problems.  Choosing an Fn value that is 100 times the cutoff
frequency of the filter is often a good method to "drop the
notch" (move it toward infinity) for lowpass filters.
Likewise, in a highpass filter, a Fn can be moved towards zero by
choosing a Fn value that is fo divided by 100.  This effectively
places this notch at zero.

Please contact LTC for more information.