January 8, 1992

TurBoard Version 0.25 Technical Document
(c) Copyright Shawn Rhoads 1991,92, All Rights Reserved
(c) Copyright Software @ Work 1991,92, All Rights Reserved 




TurBoard Version 0.25 Technical Document
(c) Copyright Shawn Rhoads 1991,92, All Rights Reserved
(c) Copyright Software @ Work 1991,92, All Rights Reserved



January 8, 1992

This document written by Shawn Rhoads





TurBoard is an ASNI asynchronous telecommunications program designed to
provide server E-Mail, data exchanges and information exchange for a group of
users.  The system can be used in a public or private environment and over a
LAN or Modem connection.


If you wish detailed information about TurBoard and how to register your copy
for $35, contact:
 
Shawn Rhoads
Software @ work
P.O. Box 283
Chattanooga, TN 37415
(615) 756-7801 (voice)
(615) 756-7810 (data)


Unfortunately, time has not yet been taken to write a detailed specification
of the TurBoard BBS System.  This document has been written to enlighten
TurBoard Sysops of the commands they can use to configure their system.


You can always leave a message on the support bulletin board in the TURBOARD
forum.
















Table of Contents:


 1. Requirements . . . . . . . . . . . . . . . . Page 3

 2. Installation Instructions  . . . . . . . . . Page 3

 3. Initial Configuration  . . . . . . . . . . . Page 4

 4. Changing System Options  . . . . . . . . . . Page 4

 5. Adding and Maintaining Bulletins . . . . . . Page 5

 6. Mail Forums  . . . . . . . . . . . . . . . . Page 6

    A. Maintaining Mail Forums . . . . . . . . . Page 6

    B. Chairmanship  . . . . . . . . . . . . . . Page 7

 7. File Directories . . . . . . . . . . . . . . Page 7

    A. Adding and Maintaining File Directories . Page 7

    B. UPLOADS and how they work . . . . . . . . Page 8

 8. Doors  . . . . . . . . . . . . . . . . . . . Page 8

 9. The YAK Subsystem  . . . . . . . . . . . . . Page 9

10. User Commands  . . . . . . . . . . . . . . . Page 10

11. Classifieds  . . . . . . . . . . . . . . . . Page 11

12. BBS List . . . . . . . . . . . . . . . . . . Page 11

13. Keyboard Commands  . . . . . . . . . . . . . Page 12

14. Colors?  . . . . . . . . . . . . . . . . . . Page 12

15. Full Screen Editor . . . . . . . . . . . . . Page 13

16. Line Editor  . . . . . . . . . . . . . . . . Page 13

17. Internal Operations  . . . . . . . . . . . . Page 14





Requirements

TurBoard requires that you have a PC-DOS based machine with at least 512
kilobytes of RAM. A serial port, modem and LAN hardware are optional.

It is suggested that you use a asychronous communications FOSSIL and have DSZ
loaded into your PATH.  Other than this, no other software is required.


Installation Instructions

Ensure you have a copy of DSZ (file transfer program) and it is included in
your current path, TurBoard requires this.  Also, you should have a FOSSIL
loaded, I suggest using X00.SYS.  You can install X00.SYS in your CONFIG.SYS
with the statement DEVICE=X00.SYS.

UnZip the file TB021EXE.ZIP in the directory you wish TurBoard to reside.

To configure your TurBoard system for the first time, simply type:
  TB

This is how you should always start the TurBoard BBS system.  If you do not,
the system will stop whenever someone enters a door or downloads a file.

Answer the questions.  If you have a problem configuring your modem, (you do
not get the "Waiting . . ." status after you have configured everything, we
may need to set up a special modem definition for your specific modem.

You may wish to unzip the following files into their respective directories
(ones you specified when configuring TurBoard).

TEXT.ZIP  - Includes Help Files, Welcome, and Logoff Screens.
YAK.ZIP   - Includes the menu files, news files, and the yak data files.
              (more on this later)

After this you may delete these ZIPs, you will no longer need them all the
other files are created automatically as they are needed.






Initial Configuration

Once you are at the call waiting screen, you will probably want to customize
your system to reflect the BBS name, open or closed, etc.

To log on for the first time, type Alt-L for local login.  Give the name and
password you specified when you installed TurBoard.  When you see the ">"
symbol, this is the primary TurBoard command prompt.  Any command may be
entered whenever you see this prompt.

Enter the "SE" (for setup) command and choose option 1.  Now you may change
your system name and some other parameters.  To change how your system
displays news and other options, you may wish to read "The YAK Subsystem"
section below.


Changing System Options

You are already familiar with the SE command.  Option 1 allows you to change
some of the primary system settings.  They are explained below:

Name:
This is the system name (ex: PC Chattanooga) that you wish to refer to you BBS
system as.  Setting this option will cause your system name to appear
throughout the system menus, such as the file directory screens.

Password:
If you desire, you may require a logon password for EVERYONE to use every time
they log on.  Some Sysops desire a private board, but one you don't have to be
pre-registered to log into, this is a method to accomplish that.

Sysop Password:
For added Sysop access security, this option will require all users with Sysop
access to enter this password.  This is good if your Sysops use their password
on another system.

Sysop Avail:
Toggles the message the user gets when O option is used.  Same as Alt-O at the
keyboard, but allows the Sysop to turn this option on and off remotely.

Sound:
If this option is turned on, the BBS will beep (ASCII 7) when the user does. 
This is defalted to off.

Zone:
Used to specify the primary FidoNet zone of the BBS.  Normally 0 for a
non-FidoNet system.

Net:
Used to specify the primary FidoNet network of the BBS.  Normally 0 for a
non-FidoNet system.

Node:
Used to specify the primary FidoNet node of the BBS.  Normally 0 for a
non-FidoNet system.

Point:
Used to specify the primary FidoNet point of the BBS.  Set this option to 0
for a non-FidoNet, or a primary node system.

Total Callers:
How many people have called the BBS to date.

Open System:
Normally yes, this option can disallow new users to log on.

Time Zone:
Specifies which time zone the BBS resides.

Log Records:
Specifies how the system log is kept.  If None, then no monthly files are kept
of the user activity.  Set this option to 1 for monthy files.

The TurBoard security levels can be cusomized by choosing option 2 from the SE
command.  You can add new security definitions as well as change names and
time limits on currently defined levels.  You can enter colors at the command
input line, but you will need some additional information, refer to the
"Colors?" section below.


Adding and Maintaining Bulletins

Bulletins are controlled solely in the TurBoard environment.  You never need
to go outside the system unless you wish to import data or text from another
source.

Initially, TurBoard has no bulletins.  If you wish to create one, you will
need to use the AB command.  Once you issue the AB command, you will be
prompted for the description of the Bulletin.  This is the text that will
appear in the main bulletin menu.

Once you've entered the description, you will enter the editor (either full
screen or line, depending on your setup).  Here is where you will enter the
actual bulletin text.  If you are in the full screen editor, you can enter
colors with the Ctrl-W command.

After the bulletin is saved, you will be prompted for the security level of
persons with access to the bulletin, as well as a read flag.  This flag
displays "No" or "Yes" depending if the person has read the bulletin or not. 
(It does require some file space, but only 1 bit per person, very small.)


Mail Forums

The basis for any bulletin board or other telecommuncations program is the
ability for users to communicate with one another.  I've attempted to make
TurBoard as communications intensive as I could.  While some packages refer to
message forums as "bases," "areas" or "conferences."  I choose "forum" because
that is what messaging should be:  a forum for discussion!

In any case, TurBoard allows unlimited message forums (limited, rather, by
your available hard disk space).  I choose names rather than numbers to give a
more human feel to each forum (and if a BBS has 200 forums, who knows what
#132 is?)  I am, however, considering switching to a number format if there
are enough requests.

Create the message forums with the AF command (standing for Add Forum).  The
first forum you create is very important!  It is the all time default forum. 
I choose to call mine "PRIMARY".  Unless another forum is joined first or
someone reads all the messages and automatically joins the next forum,
messages entered with the E command get sent to this forum.

The primary message forum will always be displayed at the top of the forum
list.  Everything below that is sorted in alphabetical order.

Maintaining Mail Forums

Usually, there are no requirements placed upon the Sysop for maintaining the
message forums.  And assuming you had unlimited disk space, everything would
be okay.

But, for networking reasons, when messages are deleted, they are NOT removed. 
They are mearly flagged for deletion until some process (currently the sysop
only, but events are planned) comes along and physically removes them.

The PM (for pack messages) is a local forum command that removes all messages
flagged for deletion as well as all private mail that has been read.

Another problem that Sysops run into is messages entered into a forum that
really belong somewhere else (like in the primary forum).  The MM (for move
message) command will copy a message to the specified forum and flag the
original message for deletion.

Conference Charimen have the ability to PM and MM in their respective forum
(and only in their respective forum).

Chairmanship

It is profitable for everyone when you assign a leader or "Chairman" to a
forum.  People can identify him/her with the forum topic and have a direction
to ask questions and enter comments.  The Sysop benifits by not having to
police every forum and allowing the Chairman to pack and move messages.

Chairmen have the power to read private mail, delete and undelete any message
in their forum.  Chairmen also have the power to set the security level
required to read/enter messages as well as changing the description line for
the conference via the CH command.

Chairmen can also assign away their chairmanship.


File Directories

File directories in TurBoard are kind of abstract.  In reality all the files
descriptions are stored in one file (this may prove to be a problem with large
networks).  A seperate file contains information on the "directories".

When a file belongs to a directory, it is specifing where it resides on the
BBS system physically.  In addition it is giving a general description of what
the file does/is.

Adding and Maintaining File Directories

Adding a new file directory is easy.  Use the AF (Add File directory) command
to specify a name for the directory, path on the disk drive, and description. 
The name is of little importance, but you should note that the directory menu
sorts the descriptions based on your directory name.

For example:

UPLOADS   Recent Uploaded Files
DOSGAMES  DOS Game Programs
DOSGRAPH  DOS Graphics Programs

Will appear as:

1] DOS Game Programs          2] DOS Graphics Programs
3] Recent Uploaded Files

This is useful when you want to group like directories together.

Another function you should be aware of is the FF command.  This command will
scan all of your disk drive directories specified in the file descriptions for
new files.  If one is found, it will prompt you for information about that
file.

To list the files you currently have on-line, use the F command.  You will see
the file directory menu, and at this point you may choose a number or type in
a search keyword.  For example, you may type DOS and GAME to get files that
match those keywords.

UPLOADS and how they work

There is no rule governing how the file directories should appear except one: 
In order to recieve uploaded files, the Sysop needs to create an UPLOADS file
directory.  This directory says that all uploaded files will be placed in this
directory, otherwise they go to the root file directory.

When a file is uploaded (or placed in the upload directory and FF function
used), you will be asked for a one line description of the file.  Following
that, you will enter the full screen editor where you will be tempted to write
a paragraph or two on the file.  This is purely optional, you can abort the
edit and continue on.

There is a text file that is displayed whenever the U command is issued.  It
is called UPLOADS.TXT.  If you have used the default subdirectories, use the
command:

> edit text\uploads.txt

You can include TurBoard colors and text to be displayed, formatting is
automatic.


Doors

A "doorway" or "door" is actually an external program that the bulletin board
software passes control to.  It is TurBoards responsibility to initilize any
information files that the door requires.

TurBoard uses the AD (add door) and CD (change door) command to maintain the
door system.

The YAK Subsystem

YAK really doesn't stand for anything other than "to talk, probably more than
one should."  In any case, the YAK subsystem in TurBoard is where specialized
information such as logon news, mail notifications and even the main menu come
from.

To start the YAK subsystem, type "YAK" at the TurBoard prompt.

To use YAK requires that you understand what you want to happen.  For
instance, if the first thing the user sees is the logon news, the NEWS
information should come first.

There are currently 9 checks, and YAK supports 4 different checks at a time. 
These are the criteria that must be met before a message (text file) is sent
to the user.

case  Checkvalue  Description
====  ==========  =======================================
1     Mail>X      OK if user has mail waiting.
2     Logons>X    OK if user has called more than X times
3     Logons=X    OK if user has called exactly X times
4     Logons<X    OK if user has called less than X times
5     LastOn<X    OK if last date on < X value
6     SecLvl>X    OK if security level > X
7     SecLvl=X    OK if security level = X
8     SecLvl<X    OK if security level < X
9     expert mod  OK if expert mode is turned off

For example, the main menu should be the last item in your YAK list.  It
should use only 1 check value (number 9).  

In case 5, the X value is an interal TurBoard (DOS format, actually) format. 
To use the integer for exactly the point in time you are intering the
information, use the NOW keyword.  This will insert the DOS date/time stamp
for that point in time.

Whenever TurBoard is finished processing, it checks the YAK List, it goes
through each item in the list to see if that item meets all the criteria.  If
so, TurBoard remembers that displays the file associated with that information
and sets the different responce information.

Perhaps you want the BBS to ask a user if they want to read their mail now, if
they have mail waiting.  This can be done with the YAK subsystem.

Make a new YAK entry:

Display file:  MAILNOW
Check1: 1
Checkval1: 0
... [leave the rest of the checks as default]
Blankarea: 0
Blankoperation: 0
Yesarea: 7
Yesoperation: 5     [this is the P command settings]
Noarea:0
Nooperation:0

Using your TurBoard editor edit the MAILNOW.YAK file.  Ex:  EDIT
YAK\MAILNOW.YAK.  It should read:

You have new mail waiting, do you wish to read it now?


User Commands

Following commands can be entered at the > prompt.  Most of the two letter
commands require extended access.


B - Bulletin List

C - Classified Ads

D - Download File

DO - DOOR menu

E - Enter Message

F - File directory List

G - Goodbye (log off)

H - ANSI toggle

I - Inquiry (history)

J - Join Mail Forum

K - Delete message

L - BBS List

N - New Files

O - Operator page

P - Personal Mail

Q - Display the Main Menu

R - Read Mail

U - Uploads

V - Versoin

W - who's on

X - eXpert toggle

Y - Your information

Most two letter commands are for maintainance, but there are some exceptions.

CH - Chairman Utilities

Chairman or Sysop access.  Allows the assigning (or assigning away) of
chairmanship, setting of certain forum options.

AM - Add Mail Forum

Starts a new message forum and adds all the associated information.

DM - Delete Mail Forum

Deletes a message forum (data files remain intact, you must physically, ie via
DOS, remove the files in that subdirectory).

MM - Move message

Moves a message from the current forum to another specified forum.

PM - Pack Message Forum

Deletes messages that have been "deleted" and private mail that has been read.
 Removes data files and header records.


File Commands

AF - Add new file directory

Will add the file forum and include it on the forum choice list.

DF - Delete file directory

Remove an empty file directory from the directory menu.

FF - Fix File Information

Will search all the file storage directories for new files not included in the
list and add them (you must type in the descriptions).


YAK - YAK subsystem

TYPE - print specified text file

EDIT - edit specified text file

Door Commands

AD - Add new DOOR

This command will add a new door (be sure you know what you're doing!)

CD - Change existing DOOR

After a door has been added, you can change the setup with this command.

Classifieds

The Classifieds feature of TurBoard is not a standard bulletin board feature. 
It's function is to provide a place for the buying and selling of goods
through the public (not retail).

Most bulletin boards will include a "For Sale" forum to accomplish this
function.  I found that this was difficult for people to use because it didn't
organize the information in a way people could easily get at it.  They are
required to scan the subject of every message and pick the one's they are
interested in.

This will work okay so long as there are only a few ads to scan though.  So I
thought to myself, "What do people normally use to buy and sell idems? 
Classified ads!"  So I decided to implement an "electronic" version of the
classified ads.

I have included a rather detailed catagory file (in TBADS.ZIP on PC
Chattanooga 615/756-7810) that is based on the Atlanta Journal/Constitution. 
Of course, you can create your own, but it's tedious!

You may add new classified catagories with the C command.  Simply choose the
"Add new catagory" option.  Other than this, the system is completely self
maintaining.

BBS List

This is a fairly standard BBS feature.  There are some doors that perform the
same function available.  The advantage to the TurBoard BBS List command (L at
the main prompt) is the ability to comment and review each BBS entry
individually.

The BBS List also does not require any maintainance on the Sysop's part.

Once you choose the L command, you have several options.  A complete BBS list,
a local BBS list, add a new BBS entry or create the BBS text file.

The difference between the complete and local BBS list is the "Is this BBS a
local call?" flag.  Only those that answered yes are displayed in the local
BBS list, thereby eliminating toll call BBS's.

To add a new BBS entry, you can accomplish that one of two ways.  You may use
the ADD command while displaying the entire BBS list, or you may simply choose
option 3.  If you use the ADD function, you will see the BBS inserted in the
list as you are listing it, so you can ensure that it was indeed added.

Option 4, create the BBS text file, is an option you can use to publish your
BBS list.  It will create a text file with two sections, a short BBS list and
a detailed BBS list.  Before the first section the file "BBSLIST.TXT" will
also be included from the text file path.

If you wish to edit this file, and you have used the default path names, use
the command:

> edit text\bbslist.txt

After you have edited the file, save your changes and it will be included in
your next BBS text file creation.  


Keyboard Commands

Alt-T  Chat mode on/ Terminal Mode
Alt-O  Operator available Toggle
Alt-X  Exit
Alt-I  Information
Alt-L  Local log on

Colors?

Turboard uses single ASCII characters to indicate different colors, you can
take advantage of this in the editor and input prompts.

The colors are:

ForeGround     ASCII (dec)
  Black          128
  Blue           129
  Green          130
  Cyan           131
  Red            132
  Magneta        133
  Brown          134
  LightGray      135
  DarkGray       136
  LightBlue      137
  LightGreen     138
  LightCyan      139
  LightRed       140
  LightMagneta   141
  Yellow         142
  White          143

Background
  Black          144
  Blue           145
  Green          146
  Cyan           147
  Red            148
  Magneta        149
  Brown          150
  LightGray      151

Misc.
  Attributes Off 152
  Underscore     153
  Blink On       154
  Invisible      155
  Clear Screen   12
  Line Feed      <none>
  End of Parag.  13

To enter these numbers in manually on a line (the file directory description
prompt, for example), use the alt key.  While holding down the ALT key, type
the 3 digit number on the numeric keypad and then release the ALT key.  At
that point the color of the text you type will change.  TurBoard treats this
character as a full character, so if you make a mistake, be sure to backspace
as far as you can go before trying again.


Full Screen Editor

The full screen editor work with WordStar commands.  If you are logging on
remotely be sure to use doorway mode to get maximum function from your
keyboard.  F1 or Ctrl-H for additional help.

Colors are stored in TurBoard format (see colors above) but in the full screen
editor do not take up a character of space.


Line Editor

The line editor in TurBoard works as most BBS line editors.  Word wrapping is
automatic, and when you are finished editing, hit return on a blank line.

You will be prompted to Continue, Abort, Quote or Save.  If you are replying
to a message, you may quote by choosing line number in the message you want to
quote.

Colors are not supported in the Line editor.  (Quoting will still have the
highlighted ">".)


Internal Operation Numbers

If you are working with YAK subsystems, you will need to know TurBoards
internal operation numbers.  The following list contains the "area" and
"operation" of each function:

Area 1

Area 2

Area 3

Area 4

Area 5

Area 6

Area 7

Area 8

Area 9

Area 1