NoFBoot 
                    Copyright 1991 by Padgett
                            Alpha v.50

     NoFBoot   is  a  small  (500  byte)  TSR  designed  to   prevent 
inadvertant  booting from a floppy disk. It will intercept warm  boot 
requests  (Ctrl-Alt-Del)  and check for a floppy in  drive  A  before 
continuing.  If  a floppy is found in drive A, the  request  will  be 
aborted  with  a warning message. With NoFBoot, a cold  start  (reset 
button or cycle power) will be necessary to boot from a floppy.

     SumFBoot is an alternative to NoFBoot that may also be used.  It 
allows  a floppy boot when Ctrl-Alt-F is pressed. In this case  if  a 
floppy is NOT present the boot will be aborted.

     Use of either  of these  program is  designed to  give the  user 
control of the resetting of a PC and to protect against "accidents".

     The programs will run under versions of MS-DOS from 2.10 to 5.00
and are designed to be transparent to the user unless a warm boot  is
requested from a floppy. In that case a warning message will appear.

     In most cases, denial of a warm boot should have no effect  on a
running program.

     It  must  be remembered that once the boot process  starts,  all 
control  is  lost  and  NoFBoot cannot override a BIOS decision or  a �
fast  disk insertion/door closure. It will protect against accidents,
not deliberate attempts.

     Additionally, any program that issues a direct BIOS  call to the 
reboot function will bypass NoFBoot as will  any subsequent TSR (e.g. 
McAfee Associates VSHIELD) that trap the warm boot function.

     If  such  other TSRs exist, for NoFBoot to be effective, it must 
be loaded LAST.

     These  programs are presented as  FREEWARE,  e.g.  there  is  no 
charge  for  their use however a copyright to the  original  code  is
retained by the author, no changes to the code are permitted  without 
permission and distribution must include this document.

     Comments should be addressed to the author: A. Padgett Peterson
     Telephone: (407)352-6007                    POB 1203 
     Internet: padgett%tccslr.dnet@mmc.com       Windermere, Florida
                                                 USA       34786