ADI Driver for HP ThinkJet Printers

        ADITJET.COM  is a TSR (Terminate and Stay Resident) program  that
        uses the AutoDesk Device Interface (ADI) specification to drive a
        Hewlett  Packard ThinkJet printer.  Switch 5 on the back  of  the
        printer should be down (HP mode).  To use this program, you  must
        load  it  into memory before you use AutoCAD or  AutoSketch.   To
        load  it into memory, make the drive and/or directory  containing
        ADITJET.COM the default drive/directory, and enter

          ADITJET

        at the system prompt, and press return.  This should be done once
        each time you boot your computer.  If you want to unload  ADITJET
        from memory later, enter

          ADITJET U

        and press return.

        Before  you can use ADITJET.COM for the first time, you must  con-
        figure  AutoCAD  or AutoSketch.  If you use AutoCAD,  select  the
        "Configure  printer plotter" option from the configuration  menu,
        and  select  "ADI  printer plotter" from the  list  of  available
        devices.   (You  will need your disk of  printer  plotter  device
        drivers  unless you have copied them to your hard disk.)  If  you
        use AutoSketch, start it by entering SKETCH /R, and when you  get
        to  the  Select plotter menu, select item 3.  Then,  with  either
        program, answer the questions asked as shown below.  (Note:  With
        AutoCAD, The first two questions are asked later, after the "dots
        per inch" questions.)

        Select output format: 2
        Interrupt number in hex <7B>: (press Return)
        Specify plot size in millimeters <N> (press Return)
        Maximum horizontal (X) plot size in inches? <11.0> 6.66
        Printer dots per inch in the horizontal (X) direction <100.0> 192
        Maximum vertical (Y) plot size in inches? <8.5>
             Answer  10.5  to the above question if you want  to  confine
             your drawing to a single sheet of paper, or any larger  num-
             ber  if  you  want to allow it to "spill  over"  onto  other
             sheets.
        Printer dots per inch in the vertical (Y) direction <100.0> 96
        Does the printer/plotter support color? <N> (press Return)
             Note: Some versions of AutoCAD will not ask the above  ques-
             tion.

        The  rest  of the configuration for AutoCAD is the  same  as  for
        supported printers, and you can consult your AutoCAD installation
        manual for more information.  When you are asked

        Rotate plot 90 degrees? <N>

        type  Y if you have a drawing that is wider than it is  high  and
        you  want it to fill the page as much as possible, especially  if


                                        1




        you want a very wide drawing to spill over more than one sheet of
        paper.  When you plot a drawing, you will have the opportunity to
        change this and some of the other settings.

        When  you  want to plot with AutoSketch, set up a plot  box,  and
        fill  in the X and Y sizes yourself.  Be sure that they  are  not
        greater  than the X and Y values you entered when you  configured
        the  program.   If you have a drawing that is wider  than  it  is
        high,  you will have to turn on the "Rotate plot 90 degrees"  op-
        tion if the plot is to fill the paper.















































                                        2