General Instructions for
                      Patrick Swayne's ADI Printer Drivers

        Introduction

        This  is  a collection of drivers that  allow  several  different
        printers to be used as printer plotters with AutoCAD (version 2.5
        or  higher) or AutoSketch (version 2 or higher).  Most  of  these
        printers  are  not directly supported by AutoCAD  or  AutoSketch.
        Epson FX series printers are supported, but the FX driver in this
        collection  provides much higher resolution.  These  drivers  use
        the Autodesk Device Interface specification, and are accessed  by
        AutoCAD and AutoSketch as ADI printer plotters.

        Here  is  a list of the printer driver files supplied,  with  the
        printers they support.

        Driver              Printers supported

        ADIEPFX.COM         Epson FX series and comp. (incl. Alps P2000)
        ADIEPLQ.COM         Epson LQ series and compatible 24-pin prtrs.
        ADIEPLQL.COM        "
        ADIEPLQW.COM        "
        ADIEPMX.COM         Epson MX series printers with Gaftrax Plus
        ADIIDS.COM          IDS Prism P80 and P132 with Dot Plot
        ADIMPI.COM          MPI 150, 99G, and Sprinter
        ADITJET.COM         Hewlett Packard Thinkjet
        SWEETP.BAS          A  BASIC  program that allows you  to  use  a
                            Sweet  P model 100 plotter or  Heath  IR-5208
                            plotter with AutoSketch.

        There  is also a program called ADITEST.COM that can be  used  to
        test the driver you choose with your printer.

        This  collection also includes a driver that lets you use a  Sum-
        maSketch graphics tablet with AutoSketch.  The documentation  for
        this  driver,  which also details the files included  in  it,  is
        called ADISUM.DOC.

        The  specific instructions for using each printer driver  are  in
        a .DOC file accompanying each driver.  For example, the  instruc-
        tions  for ADIEPFX.COM are in ADIEPFX.DOC.  The file  ADIEPLQ.DOC
        contains   instructions   for  ADIEPLQ.COM,   ADIEPLQL.COM,   and
        ADIEPLQW.COM

        Preparations Before Printing

        Before you print a drawing using one of these drivers, you should
        prepare your DOS printer driver.  These drives are all set up  to
        use printer port LPT1.  (You can change the PORT number  (0=LPT1,
        1=LPT2, etc.) in the assembly source code for a driver and  reas-
        semble  it  if you need to use another port.)  If you  are  using
        Zenith MS-DOS, and you have a parallel printer, run Configur  and
        select  "Configure  an LPT device".  Select  "Configure  parallel
        device" from the next menu, and LPT1 from the next menu.   Answer


                                        1




        N  to  "Strip parity on output" and "Map lower case to  upper  on
        output".)   Enter  0 for the number of pad  characters,  and  any
        number  you  desire for the timeout value (20 is  normal).   Then
        write  the  new configuration to memory and disk.   Note:   These
        drivers  set  the  timeout value to the maximum  while  they  are
        running, and restore it when they are done with a plot.

        If you are using a serial printer with Zenith MS-DOS, you can map
        the COM port you are using to LPT1 with Configur.  If you use the
        User Defined option when you configure your COM port, be sure  to
        answer N to the Strip and Map questions, and set the timeout to a
        high value (100 or more).

        If you are using either of my programs FASTPRN.COM or  MAPLPT.COM
        to drive a serial printer, type

          FASTPRN ,,,,,,200

        or

          MAPLPT ,,,,,,200

        and  press Enter.  You only need to enter the FASTPRN  or  MAPLPT
        command  once  each time you boot up your computer, and  you  can
        place the command in your AUTOEXEC.BAT file, if you wish.

        Testing a Driver

        You  can  test one of these drivers to see if it will  work  with
        your  printer without using AutoCAD or AutoSketch.  Just run  the
        driver program (which loads the driver into memory), and then run
        ADITEST.COM.  For example, if you wanted to test ADIEPFX.COM, you
        would  first make the drive/directory containing ADIEPFX.COM  and
        ADITEST.COM  the  default, and enter these commands  at  the  DOS
        prompt, pressing Enter or Return after each one.

          ADIEPFX
          ADITEST

        If  the driver and your printer are working correctly, two  wedge
        shapes will be printed on your paper, followed by a tiny box that
        has the word TEST in it.  The size of the wedges and the box will
        depend  on the resolution of your selected driver, and  the  word
        TEST may be so small that you will need a magnifying glass to see
        it.

        If  you  see  the message "Printer reported a  problem"  on  your
        computer screen, it could mean that your printer is off line, not
        connected, etc.

        Distribution

        These copyrighted programs are provided free of charge.  They may
        be  distributed freely as long as no charge is made for the  pro-
        grams  themselves,  or any software package with which  they  are


                                        2




        included.  The programs and all related documentation files  must
        be  distributed  together, and may not be  modified.   A  nominal
        charge may be made for the disk containing these programs.

        Warranty

        These programs are provided AS IS without any warranty, expressed
        or implied, including but not limited to fitness for a particular
        purpose.

        Disclaimer

        In no event will Patrick Swayne or the Heath/Zenith Users'  Group
        be  liable  to you for any damages, including any  lost  profits,
        lost savings, or other incidental or consequential damages  aris-
        ing out of the use of or inability to use these programs, even if
        Patrick Swayne or the Heath/Zenith Users' Group has been  advised
        of the possibility of such damages, or for any claim by any other
        party.






































                                        3