The program (VGA.COM) provides a mechanism for changing and saving
     colors on a 80x86 MSDOS VGA system.

    A resident Interrupt 10H handler (INT10.COM) has also been supplied
     (FOR 286 AND 386 PROCESSORS ONLY).  This program enhances the
     functionality of VGA.COM (See below).  Include it in AUTOEXEC.BAT if
     it will be used.
 
    Written 11/13/88 - 11/20/88  by RJ Schwartz   ˆ‰Š

    An optional filename may be specified on the VGA.COM command line.  This
     file is used to load (if it exists and is the right size) and/or store
     the DAC (Digital to Analog Converter) register values (the default file
     extension is VGA and the default filename is DEFAULT.VGA).

    If INT10.COM has been previously installed, other optional parameters
     may be specified.  Each must be preceeded by '-'.

          bN    -   enable(-b1) or disable(-b0) BLINK attribute
          rN    -   enable(-r1) or disable(-r0) RESIDENT int10 routine
          p     -   make changes PERMANENT (so mode reset does not change)
          n     -   do NOT bring up color change screen
          cNN   -   set default background/foreground COLOR (the N's
                     are hex digits).                                                     


       example:   C:> INT10            <- run resident video handler
                  C:> VGA -p -c1e      <- run color selection program
                                          loading DAC registers from
                                          DEFAULT.VGA (if it exists), making
                                          changes permanent and setting
                                          the default foreground/background
                                          attributes to 1e (background color
                                          = 1 and foreground color = eH (14).

          The VGA COLOR SELECTOR screen will appear.  The key functionality
           should be clear from the legend descriptions.  L or S will
           only reload or save to the VGA file originally specified on the
           command line (or DEFAULT.VGA if none was specified).

    
    While INT10 is active all function 10h (AH=10h) calls to INT 10h are
     ignored.  If it is necessary to use function 10h while INT10 is active 
     call INT 10h with AH=90h.

    These programs are distributed as SHAREWARE. ie. distribute freely 
     (including this file), but if you use the programs (beyond the initial
     examination) please recognize the author with a contribution ($15 
     suggested).  Checks should be payable to RJ Schwartz and mailed to:
                        
                         RJ Schwartz
                         218 Broad Hill Rd
                         W Granby  CT  06090

    Comments and/or questions may be sent to me at the above address (include
     a phone # where you can be reached (COLLECT) after 7 Eastern Time) or
     via BIX rjs2.


    The program FNTIPL.COM loads an alternate font which may be enabled
     and disabled with FNTON.COM and FNTOFF.COM.