The following is a list of all the 3 X 3 image processing filters for use 
with a program such as IMPROCES.  These kernals can be used in the custom 
filter  and boost items of the enhance section in the improces program.  
This text file is being supplied with two PCX files which have a variable 
frequency bar taget and variable frequency sinusoidal targets for use with 
the image filters contained within this document.  The following kernal 
information was taken from the program CONVOLVE.  The program CONVOLVE uses 
text files to describe the filter function.  The image filter information 
presented here is from the CONVOLVE program.  The limitation of the program 
CONVOLVE is that it can only work on 320 X 200 images; the program IMPROCES 
has no such limitation.  The kernal information from CONVOLVE can now be used
on all VGA/SVGA resolutions using the IMPROCES program.  IMPROCES allows the 
user to manipulation the 3 X 3 kernal in the images enhancement menu. However 
the interger data is manually entered in to the kernal.  IMPROCES also has a 
boost function linear multiplier which allows some of the low pass filters to be 
realized. Thus some of the filter function can not be achieved yet with the 
IMPROCES program but it is hoped that  shortly this particular feature can be 
delivered by this fantastic program.

The following text is taken almost directly from the CONVOLVE program user
documentation.

CONVOLUTION
The concept of convolution is the application of a filter function to an 
image to enhance specific aspects of it.  Convolution is an area process.  
What is meant by an area process is that each pixel in the resultant image is 
determined a group of pixels in the imediate area, in the original image.  
Specifically this group of pixels is a 3x3 filter, or kernal,  that gets 
applied to our original image.  Each of the filters provided has a certain 
mathematical significance.  Using the test patterns provided will help the 
user see exactly what is happening to the image as each filter is applied.  
Also this document contains other filter functions for items which are 
contained in the Enhance menu of the IMPROCES program; the filters here can 
be used as an alternative to filters provided to yield an additional degree 
of freedom.

Blurring Filter
	The purpose of this filter is to blurr the image
	
	BLUR: The blurring filter               
1  1  1
1  1  1
1  1  1

Gradient Directional Edge Enhancement :

Using Gradient edge detectors allows you to specify a direction for the 
edges other than just horizontal or vertical.  Diagonal edges can be 
specified as well.  This is accomplished by using directions to indicate 
the exact direction of the edges desired. If a positive slope in the 
direction of the filter exists, a light-colored pixel will be placed in the 
resultant image.  For example if the East Kernal is used, a light-colored 
pixel will be placed in the output image if there is a transition from 
black to white in the east (left to right) direction of image.  Constant 
regions will be attenuated while regions of high frequency change will be 
accentuated.

	GRADEAST: The gradient East filter
-1  1  1
-1 -2  1
-1  1  1
	GRADNE: The gradient North East filter
 1  1  1
-1 -2  1
-1 -1  1
	GRADN: The gradient North filter
 1  1  1
 1 -2  1
-1 -1 -1
	GRADS:  The gradient South filter.
-1 -1 -1
 1 -2  1
 1  1  1
	GRADNW:  The gradient North West filter.
 1  1  1
 1 -2  1
-1 -1 -1
	GRADIENT SE:  The gradient South East filter.
-1 -1  1
-1 -2  1
 1  1  1
	GRADSW:  The gradient South West filter.
1 -1 -1
1 -2 -1
1  1  1
	GRADW:  The gradient West filter.
1  1 -1
1 -2 -1
1  1 -1


High-Pass Spatial Filters

High-pass filters accentuate the high- frequency details of an image while 
leaving  the low-frequency content intact.  High pass filtering is used 
whenever objects with high spacial-frequency content need to be examined. 
The higher-frequency portions of an image will be highlighted while the 
lowe frequency portions become black.  The use of High pass filters may 
highlight images at the expense of adding noise to the image.  High 
frequency in images can be found by looking at edges of objects.  Edge 
enhancement of an image is  possible with the use of High-pass filtering.
 
HIGHPASS191:  High pass spatial filter 
-1 -1 -1
-1  9 -1
-1 -1 -1
HIGHPASS150:
 0 -1  0
-1  5 -1
 0 -1  0
HIGHPASS125:
 1 -2  1
-2  5 -2
 1 -2  1

Laplacian Edge Enhancement    

Laplacian edge enhancement differs from the other enhancement methods since 
it is omni- directional.  It highlights edges regardless of direction.  
Laplacian edge enhancements generate sharper edge definition than do most 
other enhancment operation.  Additionally, it highlights edges having both 
positive and negative brightness slopes.  All regions in the image which 
illustrate a rapid change will be accentuated and non-varing regions 
attenuated.

LAP1:
0  1  0
1 -4  1
0  1  0
LAP2:
-1 -1 -1
-1  8 -1
-1 -1 -1
LAP3:
-1 -1 -1
-1  9 -1
-1 -1 -1
LAP4:
 1 -2  1
-2  4 -2
 1 -2  1

Low-Pass Spatial Filters 

Low-pass filters leave the low-frequency content of an image intact while 
attenuating the high frequency content.  Low-pass filters are good at 
reducing the visual noise contained in an image.  Noise is garbage found 
in image that does not pertain to image.  Low frequency areas in an image is 
where the color of the pixels vary slowly or remains constant.  

LOWPAS10:  
0.1 0.1 0.1
0.1 0.2 0.1
0.1 0.1 0.1

LOWPAS19:

0.1111 0.1111 0.1111
0.1111 0.1111 0.1111
0.1111 0.1111 0.1111

LOWPAS486:

0.0625 0.125 0.0625
0.125  0.25  0.125
0.0625 0.125 0.0625

Shift and Difference Edge Enhancement 

As the name implies, these filters enhance image edges by shifting an 
image pixel and then substracting the shifted image from the original.  The 
result of the substraction is a measure of the slope of the brightness trend. 
In an area of constant pixel intensity, the substraction will yield a slope 
of zero.  Zero results in black pixel values.  In an area with large changes 
in intensity, an edge, for example, the subtraction will yield a large value 
for the slope, which will become a light colored pixel.  The larger the 
difference in intensities, the lighter the pixel.

SDVEDGE: Shift and difference vertical edge
-1  0  0
 0  1  0
 0  0  0
SDHEDGE:  Shift and difference horizontal edge
 0 -1  0
 0  1  0
 0  0  0
SDHVEDGE:  Shift and difference vertical and horizontal edges
 0  0  0
-1  1  0
 0  0  0