PCroute source code description
                                Vance Morrison


    PCroute is distributed with source for essentially one reason, I would 
like to involve many people in the design and debugging of PCroute, and for 
them to do this, they need the source.   Since I will not be the only one
fixing bugs and adding enhancements, PCroute will continue to develop as long
as there are people who think it is a worthwhile program to support.  As
creator of PCroute, however I request/demand the following


        1) Please let me know about any bug fixes so that I can incorporate
           them into the 'official' release.

        2) You may make local enhancements to PCroute and use them LOCALLY
           (that is within the same organization) but you may NOT distribute
           this code.  

    The reason for the second demand (it is in the copywrite) is very simple,
I don't want PCroute to fragment into many versions.   That is my ONLY 
concern.  Thus just tell me what you want to do, and I will give you
an copy of the working source code, and you can be sure that the part that
you are working on is not being worked on by anyone else, and when you are
done it will be ready to integrate into the official release.   I do
reserve the right NOT to integrate features that I regard as counterproductive
and code that simply is too poorly written or buggy to risk, but I do not
see myself exercising that option.  

    All of these conditions are simply to insure that PCroute has a long
and productive life.   I have no monetary interest in PCroute.  

    I could like to thank David Johnson for his contribution of the 
first generation SLIP code to PCroute.  Great work!  Thanks for the excellent 
contribution.

============================================================================
DESIGN CRITERIA

    PCroute had to be designed to squeeze all the power it could out
of an 8088 CPU.  As such I had to make some rather drastic measures.
These include

        1) Programming the main packet routing loop in assembler
        2) NO procedure call in the main packet routing loop

    Since assembler have very good macro expansion capabilities, the
second decision is relatively painless.  Simply use macros instead
of procedure calls.   This can make the code large, but memory has
not been a problem yet.  

    Once we are out of the main packet loop, these optimizations are
not really necessary anymore.  Thus if/when SNMP support is added
to PCroute, it will be done in C, since all of this code is only 
executed when SNMP operations are being done.

===========================================================================

CONVENTIONS

    Despite the use use of assembler, I have tried to make the code 
as modular as possible, and to adopt conventions that I have found quite
useful in preventing common assembly code errors.   Some of these 
conventions are

    1) function prefixing - Macros are groups into modules that provide
          a set of related services.  All function in this group are 
          prefixed by the same short string.  This improves readability
          and prevents name conflicts

    2) Naming input, output and constant registers - The most common
          error in assembly code is calling a macro that changes registers
          that you believed where held constant.  To prevent this type
          of error Macro names have the following form

                <NAME>_in_<REG LIST>_out_<REG_LIST>_const_<REG_LIST>

          For example

              WD_IF_COPY_in_CX_SI_DI_ES_out_SI_DI_const_BX_BP_ES name

          It is quite clear from the name that this macro has its parameters
          passed in CX,SI,DI,ES, it returns values in SI,DI and it holds
          the registers BX,BP,ES constant.  While this may seem long-winded
          (it is) it is VERY useful and has prevented many bugs and I
          will DEMAND that any new assembly code follow these conventions.

          Note that since the CS,DS,SS registers are NEVER changed, you
          may assume that EVERY macro preserves these registers. 

    3) file naming - There are two type of files in the source code at
         present, INC files and ASM files.  INC files contain ONLY macro
         definitions and admit NO code and are meant to be included in
         ASM files.  INC file are thus the 'meat' of the code.  The ASM
         files contain NO macro definitions, but do instantiate the macros
         to generate the actual code.  Originally (an ideally), there was
         only one ASM file (namely PCROUTE.ASM) and assembling this file
         generated all code.  As PCroute grew, however, the assembler could
         no longer compile it all in one piece, so I had to break the
         program into into many parts that are assembled separately and
         then linked together.  All of these ASM file are generally quite
         boring because all they do is instantiate a few macros.  The
         INC files is where the action is.

===========================================================================

Overall structure

    The OSI model served as the basic 'backbone' of the PCroute structure,
however, there were some problems with the model, and I had to make a few
changes.  The basic layering is


        1) IF.INC       (the interface (ethernet card) interface)
        2) DL_IP.INC    (the data link interface for IP)
        3) IP.INC       (the IP interface)
        4) UDP.INC      (the User datagram protocol (UDP) interface)

    Notice this is ROUGHLY analogous to the first 4 layers of the OSI stack,
but the major difference is the realization that a interface is a separator
BETWEEN two layers and as such must explicitly KNOW what is on at least
one of the sides.  For example there cannot be a generic interface for the DL 
(data link) layer that will interface ANY data link level code with ANY network
level code.  The interface must know about one layer or the other.  In this
case the interface KNOWS that the network layer is IP (hence DL_IP), and 
as long as the Data link layer below this conforms to this DL_IP interface
IP can use it.  

    In the case of IF interface, the interface KNOWS that the code above it
will treat it like an ethernet.  Conversely, the only thing the upper layer
sees is the IF interface, thus any ethernet board board can be used as long 
as there is code that conforms to the IF interface for it.  

    DL_IP.INC and IF.INC are also examples of an abstract interface.  These
modules to no real useful work themselves.   Instead, they act as dispatchers,
calling the proper code that will do the actual work.  The advantage doing
this is that it allows multiple interface types (in the case of DL_IP) or
multiple ethernet cards (in the case of IF) without having to change any
code.

    In the case of Ethernet, there is an additional layer between the IF
and DL_IP layer.  This layer (ETHER.INC) encapsulates the (old) Ethernet
style of addressing (as opposed to 802.3).  This layer was added to add
easy addition of the 802.3 type addressing and to support other networking
protocols (Decnet, XNS) if desired (conceivably all on the same cable!).  

   The complete layering for ethernet is

        WD8003E.INC     IF interface specific to the WD8003E card

        WD8003.INC      A more generic IF interface that will work with
                        WD8003E (ethernet) as well as WD8003S (starlan),
                        the major difference is that this module has 
                        output queuing which is needed for starlan but
                        not for ethernet.  It is not recommended for ethernet
                        since it will be slower than the WD8003E code.

        WD.INC          Constant declarations needed by the above two
                        modules to manipulate the WD8003 card.

        IF.INC          Supplies a standard interface for all card specific
                        code and dispatches the proper code when generic
                        routines are called.

        ETHER.INC       Describes the Ethernet header and packet dispatching 
                        on packet type. 
        
        ARP.INC         Provides a DL_IP interface for ethernet by using the
                        standard Address Resolution Protocol (ARP)

        DL_IP.INC       Supplies a standard interface for data link specific
                        code and dispatches the proper code when generic
                        routines are called.

        IP.INC          Provides the routing service between the data link
                        layers and a higher level interface for those packets
                        directed to and from this program.  It also supports
                        fragmentation if necessary.  This is the heart of the
                        program.

        ICMP.INC        Uses the IP services to provide the ICMP control
                        datagrams need to fully support the IP protocol.

        UDP.INC         Uses the IP services to provide the User datagram
                        protocol needed for routing (RIP) and logging (syslogd).

==========================================================================

    For the packet driver support, only one module is needed.  This module
conforms to the IF interface.  The file associated with this module is

        PACKET.INC      An IF interface that then talks to the packet 
                        driver software though a software interrupt.

==========================================================================

    For the localtalk support, only one module is needed.  This module
conforms to the DL_IP interface.  There are two files associated with this
module.

        ATALK.INC       A DL_IP interface that then talks to the localtalk
                        driver to encapsulate the IP packets in localtalk.

        AT.INC          A list of constant declarations needed to use the
                        localtalk driver supplied with PC localtalk boards

==========================================================================

    For SLIP support, four modules are needed.   They are

        I8250.INC       Does all the stuff needed to get a single character
                        on and off the PC.  Interrupt code, and hardware 
                        specific code is all in here.

        SLIP.INC        Defines the code that provides data transparency
                        and packetizing.  This is the code that places
                        packets into a read queue.

        QIF.INC         Implements the 'other side' of the read queue
                        that SLIP.INC is filling.   It looks like an
                        IF interface to calling code.


        PP.INC          Implements a DL_IP interface for point to point
                        links give an point to point IF link (like the
                        one QIF provides).
    
==========================================================================

Additional functionality

    In addition to the basic networking layers, there are a variety of
support functions that are needed to have a complete, functioning router.
These include

        RIP.INC         Provides a routing interface and implements the
                        RIP protocol.  This module has complete control
                        over the routing table and IP calls though this
                        interface to determine how to route a packet 
                        (thus another routing protocol could replace RIP
                        by changing ONLY this module)


        BOOTP.INC       Implements bootp forwarding by listening on the
                        appropriate UDP port.

        LOG.INC         Implements logging functions and the syslogd code
                        needed to get these messages to the logging host.
                        These routines violate convention in that they
                        preserve ALL registers but do not have a CONST
                        part in their name (for the practical reason that
                        it simply would not fit on a line anymore)

        DLOG.INC        Very similar to LOG, but the messages go to the
                        disk instead of the syslogd host.  These routines
                        and only be used at boot up since disk access is slow.
                        These routines violate convention in that they
                        preserve ALL registers but do not have a CONST
                        part in their name.

        CONFIG.INC      This module is responsible for configuring all of
                        other modules that need configuration time data.
                        I am unhappy with this module, since it has to
                        be change whenever ANY module needs different config
                        info.  I think instead of its present structure it
                        should simply provide a standard interface for getting
                        configuration data and let each module manage its
                        configuration data itself.

        DECLARE.INC     Contains actually hardware configuration of the router.
                        It is this file that is changed (and ONLY this file)
                        when new hardware is added to the router.

===========================================================================

Support routines

    In addition to the major functional blocks, there are some modules that
provide rather generic services that are used by the other functional blocks.
These modules include

        DEBUG.INC       Provides simple routines that print to screen routines.
                        They should not be in production code (use log routines)
                        These routines violate convention in that they
                        preserve ALL registers but do not have a CONST
                        part in their name.

        ARPTAB.INC      Provides a simple table 'object' that is used to
                        hold hardware-ip address translation data, used in
                        ARP.INC and ATALK.INC.

        BUFFER.INC      Provides simple buffer allocation routines used in
                        output (and possibly input) queuing.  Used in
                        ATALK.INC and WD8003.INC

        QUEUE.INC       Provides simple queuing routines used for packet
                        queues.  Used in ATALK.INC and WD8003.INC

        
        TASKS.INC       Provides SIMPLE time slicing routines (they aren't
                        even coroutines, but they are sufficient).

        
        TIMER.INC       Provides the ability to schedule a routine to be
                        executed some time in the future.  Used in RIP.INC
                        and other places.

==========================================================================

Experimental Routines


        BRIDGE.INC      This takes several WDE interfaces and returns
                        several IF interfaces, but it also provides ethernet
                        bridging between the interfaces.  Incorporated into
                        the rest of the code it implements a b-router.  
                        Used by itself (in BRIDGE.ASM) it implements just
                        a bridge.

==============================================================================

ASM files

The ASM file frankly are not too interesting, nevertheless, for completeness
their description follows.  The only reason for most of these (with the
exceptions of bridge.asm and pcroute.asm) is simply to get around the macro 
size limitation in TURBO ASSEMBLER.

        ATALK.ASM       appletalk code declarations 
        DLOG.ASM        disk logging code declarations
        LOG.ASM         syslog logging code declarations
        ETHER.ASM       ethernet code declarations
        IP.ASM          ip code declarations
        IP_DL#.ASM      ip code associated with interface #
        RIP.ASM         rip routing code declarations
        SLIP.ASM        SLIP code declarations 
        WD8003.ASM      wd8003 card code declarations
        WD8003E.ASM     wd8003e card code declarations
        I8250.ASM       Serial line code declarations
        PP.ASM          declarations for the point-to-point DL_IP code
        PACKET.ASM      packet driver code declarations
        PCROUTE.ASM     the main program!!!!
        BRIDGE.ASM      an independent program implementing a two interface
                        ethernet bridge. (Three or more interface are possible,
                        but you will want a fast machine for this use)