================================================================================
       DOSMAX.EXE :  Ver. 1.7, Copyright (1992) by Philip B. Gardner
       DOSM86.EXE (8086):  Ver. 1.7, Copyright (1992) by Philip B. Gardner
================================================================================

  DOSMAX.EXE is a device driver which will maximize the use of low memory
  by moving MS-DOS 3.1 and above system data to upper memory blocks provided
  by your upper memory manager.  It is not necessary to use any other
  programs to create upper memory data types like FILES, BUFFERS, FCBS,
  or LASTDRIV from Quarterdeck's QEMM386.  These data types are referred
  to as "sub-segments" in the rest of this document.

  In addition, if you are a DOS 5.0 user and are loading DOS high, then
  DOSMAX can prevent DOS from loading into the HMA and move the DOS kernel
  to an upper memory block.  This improves performance and allows programs
  which use the HMA more efficiently to utilize the HMA instead.  Such 
  programs include Microsoft WINDOWS and Quarterdeck's DESQVIEW.  DOSMAX
  can also move a portion of COMMAND.COM into an upper memory block instead
  of the HMA.  This feature recovers space in low memory which is available
  when DOS is in the HMA.

  Support is automatically provided for Microsoft WINDOWS 3.0 so that all
  FILES in your CONFIG.SYS can be loaded high.  Normally this would prevent
  WINDOWS from running, but the problem is circumvented.

  Support is provided for:

    * allowing DOS the HMA, but still moving the sub-segment data types
    * forcing DOS low, sub-segments still moveable
    * moving only the DOS SYSTEM code block into upper memory
    * providing only WINDOWS high file support
    * moving a portion of COMMAND.COM into high memory instead of the HMA
    * moving the primary COMMAND.COM's environment (master environment)
    * DOS Versions 3.1 - 3.31, DOS 4.x, and DOS 5.x (or better?)

  DOSMAX automatically moves all the data that can be moved dependent only
  upon the availability of upper memory.  It will automatically stop moving
  data when it determines that memory would be fragmented if the move was
  completed.

  Finally, a command line mode is provided to move the Master Environment,
  control Windows support, and check and report on the status of the high
  memory area reserved for COMMAND.COM.

================================================================================

(Requirements)::

        * 186 processor or better
          (DOSM86.EXE now included to support 8086/8088 processors)
        * Requires MS-DOS Version 3.10 or better

================================================================================

(Installation)::

        (CONFIG.SYS)::

        Installation of DOSMAX.EXE requires modifying the contents of
        your CONFIG.SYS file.

(Generic Configuration)::

        This configuration should work and be the most efficient in 95%
        of all configurations.  For a few real world examples see
        EXAMPLES.DOC
       
        DOS=HIGH[,UMB]                    (DOS 5.0 only)
        DEVICE=STOPMAX.SYS [options]      (Stops kernel from loading in HMA)
        DEVICE=(xms/umb memory manager)
        DEVICE=DOSMAX.EXE [options]       (DOSMAX loads high automatically)
        SHELL=COMMAND.COM /P
        BUFFERS=20
        FILES=40
        LASTDRIVE=Z

        DOS 5.0 users should configure DOS to load high into the HMA.  The
        UMB parameter is optional, since both DOS 5.0 upper memory management
        and XMS upper memory blocks are supported.

        DOS=HIGH[,[UMB][NOUMB]] (Both DOS 5.0 UMB's and XMS UMB's supported)

        Insert a DEVICE= line for DOSMAX.EXE in your config.sys.  Version 1.5
        of DOSMAX recommended that DOSMAX be loaded before the XMS and UMB
        memory manager, but DOSMAX should now be loaded after the XMS manager
        (DOSMAX will automatically load itself high if UMB's are available
        or you may use your memory manager's device loader).  Version 1.7
        provides another way to ensure that the DOS 5.0 kernel is moved into
        a UMB by DOSMAX.  The driver STOPMAX.SYS is inserted "before" the
        XMS manager and DOSMAX is inserted "after" the XMS manager (see
        STOPMAX.DOC).

        HIMEM.SYS from Microsoft always puts the DOS 5.0 kernel into the
        HMA before it is through initializing and then puts its own code
        into the HMA.  If you are able to load HIMEM.SYS high (using some
        upper memory providers, not EMM386.EXE), you can now use the /I+
        switch or /B+ switch to stop HIMEM from loading the DOS kernel into
        the HMA, and DOSMAX will put it into a UMB instead.  The /B+ switch
        is the default for STOPMAX because it requires no resident memory.
        If you use only DOS 5.0 memory management, meaning HIMEM.SYS and
        EMM386.EXE, you should not load the DOS kernel into a UMB (see /I+
        switch), but use /H+ to maximize low memory.

        The /A0 option disables high memory support for COMMAND.COM.  This
        switch should be used if the primary shell is not COMMAND.COM (for
        DOS 5.0 and above).  You should also use /A0 if you are using
        SHELLMAX.COM to load COMMAND.COM high, unless you elect to allow
        DOS into the HMA (/H+), in which case, /A0 is automatic.

        DEVICE=STOPMAX.SYS [options]
        DEVICE=(Memory Manager)
        DEVICE=DOSMAX.EXE [/A0][other options]

        One advantage of using DOSMAX.EXE, is that the STACKS=, BUFFERS=,
        FCBS=, FILES=, and LASTDRIVE= parameters may be configured normally.

        STACKS=9,256            (or =0,0 or default 9,128...etc...)
        BUFFERS=XX[,YY]         (XX = # of buffers, YY = lookahead cache)
        FCBS=XX,YY              (XX = # of FCBS, YY = # of protected FCBS)
        FILES=NN                (NN = # of system files)
        LASTDRIVE=Z             ( Z = Last reserved drive)

        Remove all INSTALL= lines from your CONFIG.SYS, or the sub-segment
        data types will not be moveable.  This action is not necessary if
        the program leaves no resident portion of itself in lower memory.

        REM INSTALL=(TSR)       (Remove to maximize memory)

        By default, DOSMAX.EXE will generate a message for each successful
        operation or event.  The display then pauses to allow you to
        read the report.  After you are satisfied with the configuration
        and you want to disable the REPORT and PAUSE feature, use:

        DEVICE=DOSMAX.EXE /R- /P- 

        (AUTOEXEC.BAT)::

        It is not necessary to modify the contents of AUTOEXEC.BAT, but
        since DOS data creators like FILES and BUFFERS are no longer
        required, it is recommended that these lines be removed

        REM BUFFERS=XX          (Remove FILE and BUFFER creator TSR's)
        REM FILES=NN

        In addition, the AUTOEXEC may be modified to automatically move
        the master enviroment to high memory.  This feature will only
        work with COMMAND.COM and is unlikely to work with other primary
        shells like 4DOS from J.P. Software.  4DOS already has a feature
        to move most of the primary shell and the master environment high.
        Use the /E- switch to disable the master environment move.

        DOSMAX.EXE [/E-]        (Add a command line invocation of DOSMAX)

        By default, DOSMAX.EXE, invoked from the command line, will generate
        a message for each successful operation or event.  The display will
        not pause in the command line mode unless the /P+ switch is used.
        After you are satisfied with the configuration and you want to disable
        the REPORT feature, use:

        DOSMAX.EXE /R- [/E-]
 
        All switch options and possible messages for DOSMAX are detailed
        below:

(Loading DOSMAX High)::

        You may load DOSMAX high with your high memory loader, or DOSMAX
        will now load itself high if upper memory is available.  If you
        want DOSMAX to move the DOS 5.0 kernel to a UMB, then DOS must
        not be in the HMA already when DOSMAX loads.  DOSMAX will report
        that "DOS is HIGH already" and abort if this condition is true.
        Use STOPMAX.SYS to stop the kernel from moving into the HMA.
        STOPMAX must be loaded before the xms/umb memory manager, so that
        the DOS kernel is not high when DOSMAX initializes.  If DOS is
        already in the HMA (not using STOPMAX), then you must use the
        /H+ switch to optimize low memory correctly.

================================================================================

(Syntax)::

        The only thing to remember about syntax for the command line is
        that just about anything works.  What this means is that you
        should be able to type in the options on the command line the
        way they make sense to you.

        To illustrate this point, the following command line example
        is mutated several different ways.

        DEVICE=DOSMAX.EXE /H+ /R- /P- /A0
        DEVICE=DOSMAX.EXE -H+ -R- -P- -A0
        DEVICE=DOSMAX.EXE H R- P- A0
        DEVICE=DOSMAX.EXE HR-P-A
        DEVICE=DOSMAX.EXE -H+-R-P-A

        ... and so on.

(Switch Options)::

        (REPORT)::      R[+ or -]        (toggle:  default +)

        Use /R- to disable the report after you are satisfied
        with the configuration of DOSMAX.EXE

        (PAUSE)::       P[+ or -]        (toggle:  default +)

        Use /P- to disable the pause after the report as long
        as there are no errors or warnings.

        (WINDOWS)::     W[+ or -]        (toggle:  default -)

        Use /W+ to enable the old Windows high file support.  This
        switch is mainly provided for diagnostic purposes, but can
        be used if the new method does not work with your configuration.
        The new method uses 2 system file handles and cannot not be enabled
        or disabled from the command line.  This switch will not
        work from the command line unless /W+ was used in the device
        line or /Y- (disable new method) was used in the device line.
        This switch is also not possible if DOSMAX.EXE is loaded into
        upper memory.

        (NEW WINDOWS):: Y[+ or -]        (toggle:  default +)

        Use /Y- to disable the new windows support added in Version 1.7
        of DOSMAX.  This switch is for non-windows users who wish to
        recover the 2 system file handles used by this method, but no
        low memory.  The new method automatically supercedes /W+ if DOSMAX
        is loaded into upper memory, otherwise using /W+ overrides this
        method automatically.  The new method cannot be enabled or disabled
        from the command line.  If you disable both methods, you may still
        start Windows with FW4&5.BAT for DOS Versions 4.x and 5.x, or
        with FW3.BAT for the rare user who has a Version of DOS 3.x higher
        than 3.31.

        (SKIPSUBS)::    S[+ or -]        (toggle:  default -)

        Use /S+ to tell DOSMAX to not move sub-segments data types.
        The switch is provided mainly for diagnostic purposes, but
        may be useful when not enough high memory is available to
        move both the DOS code block and the sub-segments, or if
        you find this feature does not work in your configuration.

        (LOW)::         L[+ or -]        (toggle:  default -)

        Use /L+ to allocate DOS code block in low memory.  As
        long as DOS=HIGH is still in your CONFIG.SYS, the
        sub-segments should be moveable.  This switch may be useful
        if there is not enough high memory to load both the DOS code
        block and the sub-segment data types into High Memory and a
        free HMA is desired.

        (HIGH)::        H[+ or -]        (toggle:  default -)

        Use /H+ to allow DOS to load into the HMA anyway.  This
        switch may also be used with DOS=LOW, since DOSMAX simply
        ignores whether DOS is HIGH or LOW when it initializes
        and checks later to see if it is safe to move sub-segments.
        There is a problem which will be encountered by DOS 5.0
        HIMEM.SYS users, DOSMAX will be unable to prevent DOS from
        going into the HMA, because HIMEM automatically puts itself
        in the HMA when initializing and before any other program can
        reserve the HMA.  The sub-segments will be moved anyway, but
        the space will still be reserved in low memory.  Use /H+ to
        change the timing of the sub-segment moves so that this low
        space is freed, or use an alternative XMS manager like QEXT.SYS
        from Quarterdeck.  DOSMAX 1.7 adds the /I switch to inhibit
        this behavior of HIMEM.SYS (see /I+ below).

        (INHIBIT HIMEM) I[+ or -]        (toggle:  default -)

        Use /I+ to stop HIMEM.SYS from loading DOS HIGH.  This switch
        is intended for users who load HIMEM.SYS from Microsoft high
        after their UMB provider.  This option is not very useful if
        HIMEM.SYS is not loaded high because HIMEM will grow to about
        30k in size.  If you still want to inhibit HIMEM, then load it
        last, to minimize the "growth."  The reason HIMEM "grows" is
        because the code which normally goes to the HMA is fixed at
        offset 0A000, so if HIMEM is loaded below 0A00h, the size of
        HIMEM grows to 0A00h + the size of the HMA code + the size of
        the XMS handle table.  This option affects the size of DOSMAX
        and adds 32 bytes.

        (NOPAUSE)::     N[+ or -]        (toggle:  default -)

        Use /N+ to never pause after the report, even if there
        are errors.  This switch can be used if your configuration
        generates a warning or error message which you choose to ignore.

        (VDISKHDR)::    V[+ or -]        (toggle:  default -)

        Use /V+ to use an alternate method of stopping DOS from
        allocating the HMA.  This switch is only necessary if
        DOSMAX reports that the DOS version is incompatible, and
        it will only work with memory managers which can detect a
        VDISK Header in the HMA when the memory manager initializes
        and mark's it as allocated.

        (FILE SIZE)::   Fnn                (value:  nn = 59 )

        Use /Fnn to set the System File Size:  The upper limit of nn
        is 61 in device mode, and 82 in command line mode.  The lower
        limit is 40.  Values other than the MS-DOS 4.0 - 5.0 System 
        File Size of 59 are only allowed if the true MS-DOS version is
        greater than 5.0.  The /Fnn switch is only necessary if DOSMAX.EXE
        can't determine the System File Size automatically.

        (ALLOCATION SIZE)::     Annnnn    (value:  nnnnn = 2080)

        Use /Annnnn to set the number of bytes reserved in upper memory
        for COMMAND.COM and other DOS 5.0 and above programs which have
        the capability of moving a portion of themselves into the HMA.
        These programs use INT 2Fh Function 4Ah to allocate a fixed number
        of bytes from the HMA.  DOSMAX has the capability of emulating
        this function in high memory.  By default, DOSMAX reserves 2080
        bytes, which is the space needed to shrink COMMAND.COM.  To
        reserve more memory, increase this value.

        The command line mode of DOSMAX reports the size and allocation
        status of this area.  If the amount allocated or requested is not
        equal to the amount reserved, DOSMAX will report what the proper
        value should be.  Users of replacement shells like 4DOS.COM from
        J.P. Software, should disable this option with /A0. Disabling the
        option or using the report feature of the command line mode to
        set the exact amount of memory required, is recommended since
        INT 21h 3306h (Get True Ver.), which is also hooked by DOSMAX,
        must return with a bit set which indicates that DOS is in the HMA
        until the amount of memory reserved is completely exhausted.

        (ENVIRONMENT)::         E[+ or -]       (toggle:  default +)     

        Use /E- to disable finding and moving the master environment to
        upper memory.  This feature is for COMMAND.COM users, so, the
        option should be disabled for other shells such as 4DOS from
        J.P. Software which have their own option to move the environment
        to upper memory.  DOSMAX does not support the master environment
        for these alternative shells independently and the feature is
        unlikely to function with these alternative shells.

        (TEST ENVIRONMENT)::    T[+ or -]       (toggle:  default -)

        Use /T+ to enable a master environment move with a special test
        mode enabled.  This feature implements an extra level of security.
        The algorithum verifies that the master environment is both found
        and that it is moveable, by testing with a shell command which
        affects the master environment through the INT 2Eh interface.  It
        is recommended that this switch not be used in a batch file.  When
        the shell processes an INT 2Eh command, it first completes the
        current batch file, then performs the INT 2Eh command.  This
        means that if DOSMAX.EXE is run from the AUTOEXEC.BAT file to move
        the master environment and the /T+ option is set, then its command
        line always appears to be the last line of the batch file.  Do not
        execute DOSMAX.EXE from a nested batch file with the /T+ option.

        (MEMORY STRATEGY)::     Mn              (value:  n = 0)   

        Use /Mn to control the memory allocation strategy which DOSMAX
        uses to allocate upper memory blocks.  The default strategy is
        is First Fit (/M0).  This means that DOSMAX will use the
        first upper memory block returned by the XMS manager.  The other
        available options are Best Fit (/M1) and Last Fit (/M2).  Best Fit
        uses the block which most closely matches the size needed, and
        Last Fit uses the last block big enough to handle the request.
        Values other than 0, 1, or 2 are ignored and the previous setting
        of this option is used.
 
        (LOAD HIGH)::           X[+ or -]       (toggle:  default +)

        Use /X- to stop DOSMAX.EXE from loading itself high if upper
        memory is available.  This switch is intended for diagnostic
        purposes only, since if you use your memory manager to load
        DOSMAX.EXE high this condition is detected and no second upper
        memory block will be allocated.

        (STOP DOS)::            B[+ or -]       (toggle:  default -)

        Use /B+ to stop DOS from loading in the HMA using a method
        which patches the copy of DOS 5.0 initialization code in memory
        when DOSMAX initializes.  This method will search and "patch out"
        the DOS to HMA code.  This option was developed and tested under
        MSDOS 5.0 and is not guaranteed to work with DOS versions later
        than 5.0, but then many of the algorithums in DOSMAX depend upon
        "undocumented" features of DOS which are always subject to change
        anyway.  The advantage of this method is that it works no matter
        which memory manager is used or how it is configured.

        (UNHOOK INT)::          Unn            (value:  default none)

        Use /Unn to tell DOSMAX that INT nn is to be "unhooked" from
        DOS STACKS when the STACKS are moved high.  This switch is useful
        for controlling which hardware interrupts are routed through the
        DOS STACKS mechanism.  Microsoft's EMM386 may cold-boot or lock-up
        if STACKS are present and moved to high memory, CTRL-ALT-DEL is
        pressed (warm-boot), and INT 09h is hooked by DOS STACKS.  The
        DOSMAX option /U09 maybe used to work-around this problem.  The
        interrupt number is in Hex-Notation and the valid values are
        the hardware interrupts 02, 08, 09, 0A, 0B, 0C, 0D, 0E, 70, 72,
        73, 74, 76, & 77.  Invalid interrupt numbers are ignored.  Multiple
        invocations of this switch are permissable.
        
        *  everything in square brackets "[]" is optional

(CONFIG.SYS Line)::

        DEVICE=DOSMAX.EXE [/-][R-P-W-Y-X-L+H+I+N+V+B+FnnAnnnnMnUnn]

        device default: /R+/P+/Y+/N-/X+/A2080/M0     (E & T ignored)

        *  Report status messages
        *  Pause after report
        *  Enable New Windows Support
        *  Pause on errors or warnings
        *  Reserve 2080 bytes for INT 2Fh Function 4Ah (COMMAND.COM)
        *  Use the First Fit memory allocation strategy
        *  Load DOSMAX high if upper memory available

(Command Line Mode)::

       C:\> DOSMAX.EXE [/-][R+P+W-N+E+T-Fnn]

        command line default: /R+/P-/W+/N+/E+/T-/Mn (ignore Y,S,L,H,I,V,A,X,B,U)

        *  Report status messages
        *  Don't pause after report
        *  Enable Windows Support
           (only if /Y- or /W+ is on the device line)
        *  Never Pause even on errors or warnings
        *  Find and move the master environment
        *  No special environment test
        *  Use Allocation Strategy set in device
           (can be overridden with /Mn)

================================================================================

(Report Format)::

        DOSMAX.EXE :  Ver. 1.7, Copyright (1992) by Philip B. Gardner
             ERROR :  (Error Messages)
           WARNING :  (Warning Messages)
            ADVICE :  (Advisory Messages)
                   :  (Report Messages)
                   :  (Allocation Status)
             PAUSE :  Press any key to continue... 

================================================================================

(Error Messages)::

        MS-DOS version 3.10 or above is required
        Can't load in High Memory
        DOS version is not compatible
        An 80186 processor or better is required
        Include DOS=HIGH in CONFIG.SYS
        Couldn't write VDISK Header
        Device not found, or version mismatch
        Stop DOS to HMA patch not successful

================================================================================

(Warning Messages)::

        Unknown option in command line
        Extra characters on command line
        DOS is HIGH already
        Unable to free HMA
        A20 Not Disabled
        INT 00h is not pointing into STACKS
        DOS Sub-Segment list is unmoveable
        System File Size not determined or out of range
        Unable to validate System Data area
        Couldn't size System File Table
        Couldn't size System FCB Table
        Couldn't trace Buffer Chain
        Couldn't find Lastdrive Array
        Master Environment is not moveable$

================================================================================

(Advisory Messages)::

        Should be the first DEVICE= in CONFIG.SYS
        Set STACKS=0,0 in CONFIG.SYS
        Possible INSTALL= in CONFIG.SYS
        Try using /Fnn switch
        Try using /H+ switch (forced)
        Try using /V+ switch
        Try using /B+ switch
        For maximum efficiency use /A00000

================================================================================

(Report Messages)::

        HMA was reserved, but is now free
        A20 Disabled
        DOS System forced low
        DOS System in HMA
        DOS System not in HMA
        DOS Sub-Segments skipped
        Old Windows support enabled
        Old Windows support disabled
        Windows support enabled
        Windows support method may have failed
        System File Size set to 00
        Unhooked DOS STACKS INT 00h
        Found 00000 bytes allocated of 00000 bytes

================================================================================

(Allocation Status)::

        SYSTEM   moved to 0000
        Not enough Hi Memory for SYSTEM  
        STACKS   moved to 0000
        Not enough Hi Memory for STACKS
        LASTDRIV moved to 0000
        Not enough Hi Memory for LASTDRIV
        BUFFERS  moved to 0000
        Not enough Hi Memory for BUFFERS 
        WKBUFFER moved to 0000
        Not enough Hi Memory for WKBUFFER
        FCBS     moved to 0000
        Not enough Hi Memory for FCBS    
        FILES    moved to 0000
        Not enough Hi Memory for FILES   
        COMMAND  space at 0000
        Not enough Hi Memory for COMMAND
        DOSMAX moved to 0000
        Not enough Hi Memory for DOSMAX

================================================================================

(Sub-Segment List)::

        The Sub-Segment List is searched from bottom to top for a block
        of moveable sub-segments, then moved in reverse order.  The
        termination of the list must be the MCB of the PSP of DOSMAX.EXE.
        This prevents fragmentation of memory.  This means INSTALL=
        should not be used in CONFIG.SYS or else the sub-segments will
        not be moveable.

        The following chart attempts to show what can and cannot be moved
        with DOSMAX.EXE

                        Sub-Segment Type                Not Moved  Moved
        ----------------------------------------------- ---------  -----
        "D"        DEVICE DRIVER                            x 
        "E"        DEVICE DRIVER APPENDAGE                  x
        "I"        IFS (Installable File System) DRIVER     x
        "F"        FILES=                                            x
        "X"        FCBS=                                             x
        "C"        BUFFERS /X Option (EMS workspace area)            x
        "B"        BUFFERS=                                          x
        "L"        LASTDRIVE=                                        x
        "S"        STACKS=                                           x
        "T"        INSTALL=                                 x (ignored)

================================================================================

(Changes)::

    (Version 1.1)::

    (1) Fixed problem not cleaning up properly, when DOS goes to HMA
        anyway, (only /V+ switch, and some XMS Managers).

    (2) Fixed problem that occurred if no XMS UMB's available, and DOS 5
        UMB's tried, and if no DOS UMB's available either (not just not
        enough), memory was allocated from low memory, even though
        allocation strategy was set to try UMB's only.  Made sure UMB
        Link state was set properly.

    (3) Added support for DOS Versions 3.10 - 3.31 and DOS Version 4.x

    (4) Improved File Size determination algorithum

    (Version 1.2)::

    (1) Improved detection of DOS=LOW, and reduced the possibility of
        an errant "Should be the first DEVICE= in CONFIG.SYS" message.

    (Version 1.3)::

    (1) Added support for INT 2Fh, Function 4Ah, so that COMMAND.COM
        (and others??) can move a portion of their code to high memory
        too.  For COMMAND.COM users with DOS 5.0, this saves 2.1k of
        low memory.  Added the /Annnn switch to support this feature,
        plus an allocation status check for the command line mode.
        4DOS users should disable this feature with option /A0.

    (Version 1.4)::

    (1) Added capability to find and move the master environment for
        COMMAND.COM users.  Also implemented a special test mode with
        the /T+ option, which verifies that the master environment
        has been found and that it is moveable.  This test mode should
        only be necessary for diagnostic purposes.

    (Version 1.5)::

    (1) Added base 10 number display for /A parameter and changed
        System File Size message to base 10.

    (Version 1.6)::

    (1) Added /Mn option, to allow general control of memory allocation
        strategy.  First Fit = 0, Best Fit = 1, and Last Fit = 2 were
        implemented for both DOS 5 UMB's, and XMS UMB's.

    (2) Added check for a 186 processor or better (allows V20/V30).

    (3) DOSMAX will now move STACKS, so setting STACKS=0,0 is not
        necessary.  In most cases though, STACKS=0,0 is still a good
        idea.  Windows 3.1 supposed requirement for STACKS=9,256 is
        not really necessary in most cases.

    (4) Removed the check for an XMS manager and a check for extended
        memory.  This allows machines without extended memory to use
        UMB providers, which do not require extended memory, with DOSMAX.
        These checks were redundant since if DOS is in the HMA when
        DOSMAX loads, the message "DOS is HIGH already" is reported.
        It is still possible to use DOSMAX, but the /H switch must be
        used if DOS is HIGH first.

    (5) Added /I option which inhibits HIMEM.SYS from loading DOS HIGH.
        This switch is not very useful if HIMEM.SYS is not loaded high,
        since HIMEM will be about 30k in size.  This switch is intended
        for users who load HIMEM high after their UMB provider is installed.

    (6) Changed default WINDOWS high file support method to a new method
        which uses 2 system file handles, but no low memory, so it works
        when DOSMAX is loaded high.  The new method may be disabled with
        /Y-, or /W+ (/W+ enables the old method since it was proven to work
        and the code was already written).  The new method cannot be
        enabled or disabled from the command line.

    (7) Now supporting separate program DOSM86.EXE.  This program is 
        functionally identical to DOSMAX.EXE, but is compiled to work
        on 8086/8088 processors also.  I have learned that there are
        8086/8088 machines which can be configured with High Memory
        using some High Memory Managers, and this variation will make
        it possible for those users to put DOS in a UMB even though
        there is no HMA.  DOSM86.EXE requires 32 more bytes of memory.

    (8) Fixed high loading so it really works...Also added an automatic
        move to high memory of DOSMAX, if UMB's are available via DOS
        or the XMS manager.  If there is some reason you don't want
        DOSMAX loaded high when loaded after UMB's are available then
        use /X- to stop it.  If DOSMAX is high, then it takes 272 bytes,
        because extra code was needed to securely find and identify
        the DOSMAX stub in memory.

    (9) Fixed a problem which hung DOSMAX after loading high if DOS was
        not in the HMA yet and /V+ switch not used.
        
   (10) Changed order of first 5 handles in new windows support, and
        enhanced error checking to only warn when support will not
        work.  The new order maintains the AUX CON order and seems 
        more compatible.

   (11) Added routine to stop "Incompatible DOS" message if loaded high
        with a "device loader."  DOSMAX will now load high with a
        device loader like LOADHI.SYS or HIGHDRVR.SYS

   (12) Try DOS high memory allocation even if NO XMS manager present.
        This was necessary for PC's which don't have extended memory,
        and don't even load an XMS manager (UMB_DRVR creates DOS high
        memory and disappears).

   (13) Fixed DOSMAX not running second time if loaded high with LOADHI.

   (14) Fixed DOSMAX not moving anything high (sometimes) if loaded
        high by any device loader.  I broke this in fix (13).

   (15) Added /B+ option which will stop DOS from going to the HMA by
        patching the DOS initilization code in memory.  This method
        works no matter which memory manager is in use or how it is
        configured.  It also requires no resident memory.

    (Version 1.7)::

    (1) Added /Unn option to tell DOSMAX to unhook hardware INT nn from
        DOS STACKS if the STACKS are present and moved.  At the time
        which DOSMAX moves the STACKS it is safe to restore the interrupt
        to the pre-STACKS value.  This switch was added as a work-around
        to a warm-reboot problem in EMM386.EXE when STACKS are high.  To
        fix the warm-reboot problem use /U09.  The value is in Hex-Notation.

    (2) Fixed DOSMAX not removing remnants of the sub-segments low when
        the size of the DOS data area should have been 0.  This occurred
        when using a memory manager with no code low, no drivers low, and
        DOS in a UMB.  Changed method of recording sub-segment movement.

    (3) Removed DOS Version 3.x use of new windows method, it worked, but
        wasn't completely compatible.  Use FW3.BAT instead if your version
        of DOS is higher then 3.31 (rare).

    (4) Move master environment function now sets the MCB owner of the new,
        high environment back the primary shell.  This corrects a minor
        incompatiblity.

================================================================================