FixMBR v1.7 (beta)

            FixMBR is a combination recovery/integrity management program 
        for  the protection of hard disks. In the case of an Master  Boot 
        Record  infection  FixMBR  may  be used  to  restore  either  the 
        original  Master Boot Record or to rebuild it using  an  original 
        Partition Table taken from either inside the virus or from one of 
        the "hidden" sectors (where most MBR infectors hide them).

            FixMBR also provides for capture/storage of an off-line  copy 
        of the MBR sector that may be used for recovery.

            FixMBR  requires no complicated switches and will prompt  for 
        all  necessary information and permissions. Further  FixMBR  will 
        suggest  only legitimate partition tables found in the "track  0" 
        area that have not overwritten vital information.

                                  Suggested Use

            FixMBR  is  best utilized before infection strikes.  In  this 
        case, save the original MBR, select the partition table found  in 
        sector one, and allow use of the SafeMBR code.

            In the event of an identified infection (e.g. STONED), simply 
        boot  from a known clean floppy, run FixMBR and increment to  the 
        sector  in  which the virus stores the real MBR (e.g.  sector  7) 
        then  use  this  to either restore the original MBR  or  use  the 
        SafeMBR code.

            In the case of an unknown infection, the best bet would be to 
        select  a  partiton  table from a sector other  than  sector  one 
        following a clean floppy boot.

            In  the event that a valid partition table is only  found  in 
        sector  one (e.g. Azusa) then the SafeMBR code must  be  selected 
        again only after a known clean floppy boot.
            
	WARNING: For  FixMBR  to  work properly, it is essential that any
                 disk cacheing be turned OFF !



                                  SAFEMBR v1.5
        
            An  integrity  checking Master Boot Record for  IBM-PCs  and 
        Clones by Padgett. Copyright (C) 1991, all rights reserved.
       
            This  program  is designed to replace  the  standard   MS-DOS         
        master  boot  record program with code that does more  than  just 
        find  the  active  partition and jump to  the  O/S  boot  record, 
        SAFEMBR   first  checks  the  disk  access  integrity,  its   own 
        integrity, and validates the indicated partition.
        
             SAFEMBR  will  detect  all known Master  Boot  Record  virus 
        infections including those using "stealth" such as JOSHI and  the 
        EVIL EMPIRE as well as the most common infector, STONED.
        
             Used  in conjunction with NoFBoot (C), the likelyhood of  an 
        undetected  BIOS level infection going undetected drops  to  near 
        zero.
        
             Invocation  is  simple:  from  the  DOS  command  line  type 
        >SAFEMBR.  SAFEMBR with then retrieve tha current MBR, check  the 
        partition table for validity, incorporate the table into its  own 
        code,  copy the MBR to the second (hidden - SAFEMBR verifies  the 
        presence of hidden sectors) sector, and places itself in the MBR.
        
             Using the techniques proven by its more rigourous commercial 
        relative,  DISKSECURE,  SAFEMBR  can  provide  immediate  generic 
        front-line  detection of viruses both known and unknown  for  the 
        individual PC.
        
             Being  a MBR replacement only, SAFEMBR does not go  resident 
        and  thus  does  not require any  dedicated  RAM.  Following  the 
        IBM/MicroSoft specifications for a MBR, SAFEMBR is effective even 
        with  validating  BIOSes such as the TANDON  and  "unrully"  disk 
        controllers which write to the MBR.
                
             When installed, SAFEMBR will display its logo on each boot.
        
             Should an exception occur, the boot will halt with an  error
        message such as "Low Interrupt Vector", "Invalid  First  Sector",
        "Invalid Master Boot Record", or "Missing Operating System".  The
        system can then be booted with  a floppy disk  and  investigation 
        made to determine the cause of the exception.

             It should be noted that many  security  products  using  MBR
        relocation techniques  are  incompatable  with SAFEMBR. If such a 
        product  uses  MBR  redirection  to prevent booting from a floppy 
        disk, this will be the case.

                                           Padgett Peterson
                                           Orlando, Florida
                                           (407)352-6007
                                           padgett@tccslr.dnet@mmc.com        

        DISCLAIMER: This software is furnished "as is" and all  liability 
             for  the effects of the use of this software rests with  the 
             user. Adequate backups are the best protection from loss.
        
        Note: This distribution consists of two files:
             FixMBR17.exe - 1659 bytes - the program
             FixMBR17.doc - this document

	v1.7 - multiple drive handler added
        v1.6 - fixes "Invalid Partition Table" error with SafeMBR when 
	       active partition is not first in table.
        v1.5 - first beta version released