The IBM Anti-Virus Product Version 2.1.2
Copyright (c) IBM Corporation 1989, 1990, 1991.  All rights reserved.


1.0  TABLE OF CONTENTS
______________________



2.0  INTRODUCTION TO THE IBM VIRUS SCANNING PROGRAM
2.1  How to Use the IBM Virus Scanning Program
2.2  The IBM Virus Scanning Program: Capabilities and Limitations
2.3  Files Associated with the IBM Anti-Virus Product

3.0  SAFE USE OF THE IBM VIRUS SCANNING PROGRAM
3.1  Safely Using the IBM Virus Scanning Program
3.2  Safely Creating a Bootable Diskette
3.3  Safely Copying the IBM Virus Scanning Program
3.4  Examples of Output from the IBM Virus Scanning Program
  3.4.1  Scanning an Uninfected System
  3.4.2  Scanning an Infected System
  3.4.3  If VIRSCAN.EXE Has Been Accidentally Modified
  3.4.4  If VIRSIG.LST Has Been Accidentally Modified
  3.4.5  If VIRSCAN.MSG Has Been Accidentally Modified

4.0  TECHNICAL DETAILS
4.1  Operating Systems
4.2  What The IBM Virus Scanning Program Checks
4.3  The Format of the Signature Files
  4.3.1  Scanning Files
  4.3.2  Scanning Boot Records
4.4  Adding More Virus Signatures
4.5  Command-Line Options
4.6  Values of ERRORLEVEL Returned
4.7  Limitations
  4.7.1  The IBM Virus Scanning Program Is Not a Cure-All
  4.7.2  The IBM Virus Scanning Program Does Not Remove Viruses
  4.7.3  The IBM Virus Scanning Program May Not Find Viruses in Archives
  4.7.4  Scanning Boot Sectors
4.8  Common Problems
  4.8.1  Systems With Damaged Directory Trees
  4.8.2  Incompatible Versions of PC-DOS and COMMAND.COM
  4.8.3  Limitation When Scanning Boot Records of Network Drives
  4.8.4  False Alarms When Scanning Memory

5.0  VIRUSES DETECTED BY THE IBM VIRUS SCANNING PROGRAM
5.1  Virus List and Characteristics
5.2  Cross-Reference of Common Virus Names




2.0  INTRODUCTION TO THE IBM VIRUS SCANNING PROGRAM
___________________________________________________



This  document describes the IBM Virus Scanning Program version 2.1.2,
which is part of the IBM  Anti-Virus  Product  version  2.1.2.    This
section provides an introduction to using the program.  Later sections
describe further technical details.




2.1  HOW TO USE THE IBM VIRUS SCANNING PROGRAM
______________________________________________



The  IBM  Virus  Scanning  Program  can be used to test files and boot
sectors on disks for patterns that are found  in  some  common  PC-DOS
computer  viruses.    To  scan  for these viruses on the C: drive, for
instance, type the following at the DOS or OS/2 command prompt:

VIRSCAN C:

To scan a diskette in the A: drive, for instance, type the following:

VIRSCAN A:

For further instruction on the program, and to view the on-line  help,
simply type VIRSCAN without any arguments.  Type VIRSCAN ? for a short
description  of  the  available command line options.  Type VIRSCAN ??
for some usage examples.

We recommend that the IBM Virus Scanning Program  be  run  only  after
cold-booting your system from a write-protected diskette.  This is the
safest  way  to  ensure that a virus infection does not interfere with
the scan.   See "Safely Using the  IBM  Virus  Scanning  Program"  for
further details.




2.2  THE IBM VIRUS SCANNING PROGRAM: CAPABILITIES AND LIMITATIONS
_________________________________________________________________



This  program  is  designed  to  detect  many  common  PC-DOS computer
viruses.  It is used internally by IBM to detect computer viruses.  It
scans boot records and executable files,  looking  for  signatures  of
viruses  known  to  IBM  when  this  version  of  the program was made
available.  A signature is a bit pattern that is found in a particular
virus.   The virus signatures were  obtained  by  performing  "reverse
engineering"  on  virus  samples.   The files that are scanned by this
program must be in their native executable form (e.g.,  not  encrypted
and  not  packed)  in  order  for the signatures to be found.  The IBM
Virus Scanning  Program  does  *not*  remove  viruses,  inhibit  virus
propagation,  or recover from any damage caused by viruses to programs
or data.  It simply scans files looking for bit patterns matching  the
virus  signatures.  There may be viruses that currently exist, or that
will exist in the future, that this program will not detect.  We  know
of  no  available,  guaranteed solution to the computer virus problem.
For this reason, we recommend that you  continue  to  perform  regular
backups  of  your  data,  and  exercise caution in acquiring and using
software.



2.3  FILES ASSOCIATED WITH THE IBM ANTI-VIRUS PRODUCT
_____________________________________________________


There are five files distributed with the IBM Anti-Virus Product.  You
should verify that each one has the length stated below, and  not  use
the IBM Anti-Virus Product if any are different.

VIRSCAN.EXE  This  is  the  executable file for the IBM Virus Scanning
             Program.   It is 74,863 bytes long.

VIRSIG.LST   This file contains signatures for  viruses.    These  are
             viruses  of  which  IBM was aware at the time the program
             was distributed.  This file must be located in  the  same
             directory as VIRSCAN.EXE.  It is 68,411 bytes long.

VIRSCAN.MSG  This  file  contains  message text used by VIRSCAN.  This
             file  must  be  located  in   the   same   directory   as
             VIRSCAN.EXE.  It is 23,034 bytes long.

READ.ME      This  file contains the IBM License Agreement for the IBM
             Anti-Virus Product.  It is 6,876 bytes long.

VIRSCAN.DOC  This is the document you are currently reading.    It  is
             104,485 bytes long.

In  addition,  you  may  create  two  other files which can be used by
VIRSCAN.  The file ADDENDA.LST can contain signatures  for  additional
viruses.   See "Adding More Virus Signatures" (below) for more details
on this file.  The file LOCAL.MSG can contain  a  message  (up  to  10
lines long) that will be displayed at program termination if any virus
signatures  were found.  See "Scanning an Infected System" (below) for
more details on this file.



3.0  SAFE USE OF THE IBM VIRUS SCANNING PROGRAM
_______________________________________________



You  should  be  careful when copying and using the IBM Virus Scanning
Program.   The  procedures  in  this  section  will  help  you  create
diskettes  containing  the  IBM Virus Scanning Program, minimizing the
chance of contaminating them with viruses.   This  section  will  also
help you use the IBM Virus Scanning Program most effectively.



3.1  SAFELY USING THE IBM VIRUS SCANNING PROGRAM
________________________________________________


We  recommend  running  the  IBM  Virus  Scanning  Program  only after
cold-booting your PC or PS/2 from a write-protected diskette  that  is
known  to be virus-free.  It is possible to use the IBM Virus Scanning
Program without cold-booting your system from a  virus-free  diskette.
If  this  is done, however, it is possible for a virus to be active in
your system during the scan.   This could potentially  cause  the  IBM
Virus Scanning Program to miss the presence of a virus in your system.

It  is also possible to run the IBM Virus Scanning Program from a hard
disk rather than a write-protected floppy diskette.  If this is  done,
however,  it  is possible for the IBM Virus Scanning Program itself to
become infected with a virus.   While there are features  in  the  IBM
Virus  Scanning  Program to help detect these conditions, it is always
safest to cold-boot your system from a virus-free diskette.

The procedure for cold-booting your system from a diskette  containing
the  IBM  Virus  Scanning  Program,  and  scanning  the  C: drive (for
instance), is as follows.

1.  Cold-boot  your  system  from  your  write-protected,   virus-free
    diskette containing the IBM Virus Scanning Program.

    a.  Turn your PC or PS/2 off.

    b.  Insert  your write-protected, bootable diskette containing the
        IBM Virus Scanning Program.  (See "Safely Creating a  Bootable
        Diskette"   for   instructions  on  creating  this  virus-free
        diskette.)

    c.  Turn your PC or PS/2 on and let it boot from the A: drive.

2.  Scan any hard disks or floppy diskettes that you wish to check  by
    typing (for instance):

    VIRSCAN C:



3.2  SAFELY CREATING A BOOTABLE DISKETTE
________________________________________


We  recommend  running  the  IBM  Virus  Scanning  Program  only after
cold-booting  your  PC  or  PS/2  from  a  diskette  is  known  to  be
virus-free;  this procedure is for creating such a virus-free bootable
diskette.

We assume here that you will be formatting your new diskette in the A:
drive.  If not, you should modify the "FORMAT" step (2) that  follows.
We  also assume that you either have a non-bootable diskette in the B:
drive containing all of the files  necessary  to  run  the  IBM  Virus

Scanning  Program,  or  have  downloaded  all of these files (and only
these files) into the directory C:\VIRSCAN.   If you  have  put  these
files elsewhere, you should modify the "COPY" step (3) that follows.

1.  Cold-boot  your system.  This is important to ensure that no virus
    is active when you copy the IBM Virus Scanning Program.

    a.  Turn your PC or PS/2 off.

    b.  Insert your  original  manufacturer's  write-protected  PC-DOS
        diskette into the A: drive.  If you are using DOS 4.0, use the
        "install" diskette.

    c.  Turn your PC or PS/2 on and let it boot from the A: drive.  If
        you  are  using DOS 4.0 from the "install" diskette, press the
        "Esc" key and then the "F3" key to end the install process.

2.  At the DOS prompt, type:

    FORMAT A: /S

    and follow the prompts to format a new diskette.

    Note: If you are  using  DOS  4.0,  you  may  wish  to  create  an
    AUTOEXEC.BAT  file  that  automatically installs the SHARE program
    when a PC or PS/2 is booted  from  this  diskette.    If  you  are
    planning  to  use  the  diskette  to scan disk partitions that are
    greater than 32 megabytes in size, then you *must* use DOS 4.0 and
    SHARE.EXE.  Refer to your PC-DOS manual for further instructions.

3.  Copy the files necessary to run the IBM Virus Scanning Program  to
    the A: diskette.

    o   If  these  files  are  on a diskette in the B: drive, type the
        following at the DOS prompt:

        COPY B:\*.* A:\

        and follow the prompts on the screen to copy the  contents  of
        the  diskette containing the IBM Virus Scanning Program to the
        A: diskette.

    o   If  you  have  downloaded  these  files   to   the   directory
        C:\VIRSCAN, type the following at the DOS prompt:

        COPY C:\VIRSCAN\*.* A:\

        and  follow  the prompts on the screen to copy the contents of
        the subdirectory containing the IBM Virus Scanning Program  to
        the A: diskette.

4.  Remove  the new diskette and write-protect it with a write-protect
    tab (on a 5.25" diskette) or by moving the  write  protect  switch
    (on  a 3.5" diskette) so that you can see through the hole located
    in the bottom right while looking at the back of the diskette.  We
    recommend leaving this  diskette  write-protected  at  all  times.
    This  is  important to prevent the diskette from becoming infected
    with a virus at a later time.

5.  To test your new, bootable diskette, turn your  PC  or  PS/2  off,
    insert  your  new, bootable diskette in the A: drive, turn your PC
    or PS/2 on and let it boot from the A: drive.  At the DOS  prompt,
    type:

    VIRSCAN A:

6.  If  the  IBM  Virus  Scanning  Program  tells  you that a virus is
    present on the A: drive, or  that  any  of  the  files  have  been
    modified, do *not* use the diskette!!  The files may not have been
    installed  correctly on the diskette, or it may be infected with a
    virus.   Go back to the beginning of this procedure and follow the
    steps very carefully to install the files on your diskette.    If,
    after  repeated attempts, the IBM Virus Scanning Program continues
    to tell you that something is wrong  with  the  diskette,  contact
    competent technical personnel for help.




3.3  SAFELY COPYING THE IBM VIRUS SCANNING PROGRAM
__________________________________________________



The  following  procedure  is for making a copy of a bootable diskette
containing the IBM Virus Scanning Program.

1.  Cold-boot your system.  This is important to ensure that no  virus
    is active when you copy the IBM Virus Scanning Program.

    a.  Turn your PC or PS/2 off.

    b.  Insert  your  original  manufacturer's  write-protected PC-DOS
        diskette into the A: drive.  If you are using DOS 4.0, use the
        "install" diskette.

    c.  Turn your PC or PS/2 on and let it boot from the A: drive.  If
        you are using DOS 4.0 from the "install" diskette,  press  the
        "Esc" key and then the "F3" key to end the install process.

2.  At the DOS prompt, type:

    DISKCOPY A: B:

    and  follow  the prompts on the screen to copy the contents of the
    original the IBM  Virus  Scanning  Program  diskette  (the  source
    diskette) to a new diskette (the target diskette).

3.  Remove  the new diskette and write-protect it with a write-protect
    tab (on a 5.25" diskette) or by moving the  write  protect  switch
    (on  a 3.5" diskette) so that you can see through the hole located
    in the bottom right while looking at the  back  of  the  diskette.
    This  is  important to prevent the diskette from becoming infected
    with a virus at a later time.  We recommend leaving this  diskette
    write-protected  at  all times.   This is important to prevent the
    diskette from becoming infected with a virus at a later time.

4.  Scan the new diskette by reinserting it  into  the  A:  drive  and
    typing at the DOS prompt:

    VIRSCAN A:

5.  If  the  IBM  Virus  Scanning  Program  tells  you that a virus is
    present on the A: drive, or  that  any  of  the  files  have  been
    modified, do *not* use the diskette!!  The files may not have been
    copied  correctly  to  the  diskette, or it may be infected with a
    virus.  Go back to the beginning of this procedure and follow  the
    steps  very  carefully  to copy the diskette.   If, after repeated
    attempts, the IBM Virus Scanning Program  continues  to  tell  you
    that  something  is  wrong  with  the  diskette, contact competent
    technical personnel for help.


3.4  EXAMPLES OF OUTPUT FROM THE IBM VIRUS SCANNING PROGRAM
___________________________________________________________


The IBM Virus Scanning Program always displays  the  following  banner
when it scans for viruses.

----------------------------------------------------------------------

The IBM Virus Scanning Program Version 2.1.2
(c) Copyright International Business Machines Corporation 1989, 1990, 1991
    Licensed Material - Program Property of IBM, All Rights Reserved.

                        NOTICE TO USERS

For users in the United States and Puerto Rico:
THE IBM VIRUS SCANNING PROGRAM IS LICENSED "AS IS."  Your use of this program
is subject to the IBM Program License Agreement for the IBM Virus Scanning
Program, which is set out in the "READ.ME" file distributed with this program.

For users outside the United States and Puerto Rico:
See your IBM representative or IBM authorized supplier for contract terms.

Press Y to accept the license agreement, or press any other key to exit.

----------------------------------------------------------------------



3.4.1  SCANNING AN UNINFECTED SYSTEM
____________________________________


When you use the IBM Virus Scanning Program to scan a disk or diskette
that  does  not  contain  viruses,  it  will  display the banner, then
something similar to the following.
----------------------------------------------------------------------

Starting virus scan on Thu Feb 08 09:18:43 1991
Scan completed.
24 files were scanned.
1 system boot sector was scanned.
1 master boot record was scanned.
System memory was scanned for dangerous and/or well hidden resident viruses.
Total bytes scanned = 2661470, in 26 seconds.
No viruses listed in the signature files were found.

----------------------------------------------------------------------

This indicates  that  none  of  the  scanned  files  or  boot  records
contained any of the virus signatures listed in the signature files.




3.4.2  SCANNING AN INFECTED SYSTEM
__________________________________


If  the  IBM Virus Scanning Program finds any of the signatures listed
in the signature files, it will display the name of the files or  boot
sectors  in which they were found, as well as the signatures found and
the name of the viruses to which they correspond.  The total number of
viral signatures that were found is displayed when the program  exits.
Here  is  a  sample  run, where the IBM Virus Scanning Program found a
virus signature.
----------------------------------------------------------------------


Starting virus scan on Thu Feb 08 09:18:43 1991
Found signature in (C:\UTIL\PAPAYA.COM)
This file may be infected with the 1813 virus.
(Continuing Scan)

Scan completed.
24 files were scanned.
1 system boot sector was scanned.
1 master boot record was scanned.
System memory was scanned for dangerous and/or well hidden resident viruses.
Total bytes scanned = 2661470, in 26 seconds.
1 Viral signature found in 1 object.

----------------------------------------------------------------------

After  all  other  messages  are  displayed, if the IBM Virus Scanning
Program  can find a file called "LOCAL.MSG", in the same directory  as
"VIRSCAN.EXE",  it  will display lines from that file, up to a maximum
of 10 lines.

If the IBM Virus Scanning Program finds signatures of any viruses,  it
is  very  likely  that  the  indicated objects are infected with those
viruses.  You should get expert technical help immediately,  to  clean
up the infection.



3.4.3  IF VIRSCAN.EXE HAS BEEN ACCIDENTALLY MODIFIED
____________________________________________________


The  IBM Virus Scanning Program checks the program file VIRSCAN.EXE to
verify that it has not been modified.  (This may happen  accidentally,
or  it  may indicate that VIRSCAN.EXE has been infected with a virus.)
If it has been modified for any reason, the IBM Virus Scanning Program
will display the following message:
----------------------------------------------------------------------

The program (A:\VIRSCAN.EXE) has been modified.
This may be due to a virus, or to other causes.
Scan terminated early due to error

----------------------------------------------------------------------

In this event, an original (unmodified) copy of VIRSCAN.EXE should  be
used  to replace the modified copy.  If, after it is replaced, the IBM
Virus Scanning Program continues to tell you that something is  wrong,
it  is  possible  that  your original copy of VIRSCAN.EXE was damaged.
Contact competent technical personnel for help.



3.4.4  IF VIRSIG.LST HAS BEEN ACCIDENTALLY MODIFIED
___________________________________________________


The IBM Virus Scanning Program also  checks  the  file  VIRSIG.LST  to
verify that it has not been modified.  If it has been modified for any
reason,  the  IBM Virus Scanning Program will inform you, then it will
terminate.  If VIRSIG.LST has been modified, a message similar to  the
following will be displayed.
----------------------------------------------------------------------

Starting virus scan
The file (A:\VIRSIG.LST) has been modified.
Scan terminated early due to error


----------------------------------------------------------------------

If the signature file has been modified, it should be replaced with an
original  (unmodified) copy.   If, after it is replaced, the IBM Virus
Scanning Program continues to tell you that something is wrong, it  is
possible  that  your  original copy of the signature file was damaged.
Contact competent technical personnel for help.



3.4.5  IF VIRSCAN.MSG HAS BEEN ACCIDENTALLY MODIFIED
____________________________________________________


The IBM Virus Scanning Program also checks  the  file  VIRSCAN.MSG  to
verify that it has not been modified.  If it has been modified for any
reason,  the  IBM Virus Scanning Program will inform you, then it will
terminate.  If VIRSCAN.MSG has been modified, a message similar to the
following will be displayed.
----------------------------------------------------------------------

The file (A:\VIRSCAN.MSG) has been modified.
Scan terminated early due to error

----------------------------------------------------------------------

If the message file has been modified, it should be replaced  with  an
original  (unmodified) copy.   If, after it is replaced, the IBM Virus
Scanning Program continues to tell you that something is wrong, it  is
possible  that  your  original  copy  of the message file was damaged.
Contact competent technical personnel for help.



4.0  TECHNICAL DETAILS
______________________



This  section  describes  further  technical  details of the IBM Virus
Scanning Program.  While it is not necessary to read this  section  to
use   the   program  in  simple  situations,  we  recommend  that  you
familiarize yourself with it, so that you understand the operation  of
the program more completely.




4.1  OPERATING SYSTEMS
______________________



The  IBM  Virus  Scanning  Program will run in the following operating
systems:

o   PC-DOS versions 2.0, 2.1, 3.0, 3.1, 3.2, 3.3, 4.0 and 5.0.

o   OS/2, both Standard Edition and Extended  Edition,  versions  1.0,
    1.1,  1.2,  and 1.3.  It supports both the DOS ("FAT") file system
    and OS/2's High Performance File System.  It will run in  an  OS/2
    Presentation Manager window and in OS/2's DOS compatibility box.




4.2  WHAT THE IBM VIRUS SCANNING PROGRAM CHECKS
_______________________________________________



The  IBM  Virus  Scanning  Program  checks  to  make  sure  that it is
operating properly, and then checks for  viruses.    Specifically,  it
checks  your  system  in  the  following  sequence  (though  there are
command-line options that can alter this):

1.  The executable file VIRSCAN.EXE is checked to ensure that  it  has
    not  been modified.  If it has been modified, it may indicate that
    it has been accidentally changed, or that it has been infected  by
    a virus.  The program will not continue if it has been modified.

2.  The  file  VIRSCAN.MSG  is  checked to ensure that it has not been
    modified. (Precisely, this step actually  occurs  when  the  first
    message  is displayed.)  If VIRSCAN.MSG has been modified, the IBM
    Virus Scanning Program will not continue.

3.  The file VIRSIG.LST is checked to ensure  that  it  has  not  been
    modified.  If VIRSIG.LST has been modified, the IBM Virus Scanning
    Program will not continue.

4.  When  run  under PC-DOS (or in the DOS compatibility box of OS/2),
    system memory is scanned for resident viruses.

5.  Files are scanned for viruses.  The default is to scan  EXE,  COM,
    OV?,  INI,  SYS,  and  BIN  files.    Boot records are scanned for
    viruses.  The default is to scan the system  boot  sector  of  any
    specified  drives,  and  the  master boot record of the first hard
    drive if any drive letter  C:  or  higher  is  specified.    These
    defaults can be changed by command-line options.




4.3  THE FORMAT OF THE SIGNATURE FILES
______________________________________


The  IBM  Virus Scanning Program uses the signatures found in the file
VIRSIG.LST.  and (if it is present) ADDENDA.LST to scan  for  viruses.
Both  of  these  files  must  be in the same directory as VIRSCAN.EXE.
Both of these files has the same basic format:

o   Comment  lines  have  an  asterisk ("*") as their first character.
    The IBM Virus Scanning Program does not use  these  lines  in  its
    virus scan.  (The entire contents of VIRSIG.LST, including comment
    lines,  is checked during self-test to ensure that it has not been
    modified.  The file ADDENDA.LST is not checked.)    Comment  lines
    are  used  to  give  additional, human-readable comments about the
    information in the signature files.

o   One of the comment lines at the beginning of the  file  VIRSIG.LST
    contains  the  string  "CRCVMARK"  followed  by  eight hexadecimal
    digits.  This line is used by the IBM Virus  Scanning  Program  to
    ensure  that these files have not been modified.  This line is not
    used in ADDENDA.LST.

o   The body of the file consists of entries that tell the  IBM  Virus
    Scanning Program what to do for each virus.  Each entry is made up
    of three lines:

    1.  A  hexadecimal  string, which is the string that the IBM Virus
        Scanning Program looks for in order  to  determine  that  this
        particular  virus is contained in the file.  We recommend that
        you use at least 24 hexadecimal digits (that is, at  least  12
        bytes)  in any signature that you add to ADDENDA.LST, and more
        whenever possible.  Shorter signatures have a larger chance of
        being found in normal programs which are not infected with any
        virus, leading to false reports of  viruses.    The  signature
        should  be  taken from a code area of the virus, rather than a
        data area, to minimize the possibility of false  alarms.    We
        also  recommend  that  you  test  any new signatures against a
        number of programs before using them widely, to ensure that no
        common programs give false alarms for the signature.

        Two question mark characters ("??") may be used in place of  a
        pair  of hexadecimal characters representing a signature byte.
        This  indicates  that  the  specified  byte  position  in  the
        signature string may have any value.  Don't count these "don't
        care"  bytes when following the signature length guidelines in
        the  previous  paragraph.   If a signature string has any "??"
        substrings in it, no scan for variations on the signature will
        be performed, even if the "-m" command line  option  is  used.
        If  a  signature  string has any "??"  strings in it, any "FF"
        values in the signature string will be treated as "don't care"
        bytes.

        A "%N" sequence, where 'N' is a single hexadecimal digit,  may
        also  be  used  in  place  of a pair of hexadecimal characters
        representing a signature byte.  This tells virscan that 0 to N
        arbitrary filler bytes may be  at  that  position  in  a  real
        virus,  and  that  they  should  be  ignored.    For  example,
        "ABCD77%4888C5A31663499001277" tells virscan  that  it  should
        search  for  the  hex  string  "ABCD77", followed by zero to 4
        arbitrary bytes, followed by the rest of  the  search  string.
        Don't  count  these  "don't  care"  bytes  when  following the
        signature length guidelines.  If a signature  string  has  any
        "%"  characters in it, no scan for variations on the signature
        will be performed, even if the "-m"  command  line  option  is
        used.  If a signature string has any "%" characters in it, any

        "FE"  values in the signature string will be treated as "don't
        care" bytes.

    2.  A  message  that  is  displayed  if the string is found in the
        specified files, to indicate that the virus was  found.    The
        text of this message can be in either upper or lower case.  If
        the  message  contains  a  %s,  the %s will be replaced with a
        message  appropriate  for  the  object  in  which  the   virus
        signature was found.  For instance, if the virus signature was
        found  in a file, the %s would be replaced with "This file may
        be infected with".

    3.  A line containing one or more strings which indicate what  the
        IBM  Virus  Scanning  Program  should  do  if the signature is
        found.

        COM             Used to tell the IBM  Virus  Scanning  Program
                        that  it  should expect to find this signature
                        in COM files.  (Currently this string  is  not
                        used,  and the IBM Virus Scanning Program will
                        display the indicated message if the signature
                        is found in any file or boot sector.)

        EXE             Used to tell the IBM  Virus  Scanning  Program
                        that  it  should display the indicated message
                        if the signature is found in a file which  has
                        an EXE header.  The IBM Virus Scanning Program
                        will not display messages for signatures found
                        in  files  with  EXE  headers unless the "EXE"
                        string is specified.  The IBM  Virus  Scanning
                        Program  does  not  rely on the filetype being
                        .EXE to determine this.  Instead, it checks to
                        see  if  the  file's  first  two   bytes   are
                        hexadecimal 4D and 5A, which are the first two
                        bytes  of  an EXE header.  (If the "-G" option
                        is  specified  on  the   command   line,   the
                        indicated  message will be displayed no matter
                        where the signature is found.)

        Offset          The next string after "Offset"  (delimited  by
                        blanks)  must be a numeric string, and is used
                        as an integer offset into the object (file  or
                        boot  sector)  at which the virus signature is
                        expected to be found.   If  the  signature  is
                        found  elsewhere,  the  indicated message will
                        not be displayed.   (If  the  "-G"  option  is
                        specified,   the  indicated  message  will  be
                        displayed no matter  where  the  signature  is
                        found.)

        Boot            Used  to  tell  the IBM Virus Scanning Program
                        that it should expect to find  this  signature
                        in  boot  records.   By default, the IBM Virus
                        Scanning Program  won't display  messages  for
                        "boot"  signatures  found  in files unless the
                        "COM" or "EXE" keywords are used (on the  same
                        line  as  "Boot").    (If  the  "-G" option is
                        specified on the command line,  the  indicated
                        message  will be displayed no matter where the
                        signature is found.)

        Pause if found  Used to tell the IBM  Virus  Scanning  Program
                        to  pause  with  a dire warning the first time
                        during a scan that the signature is  found  in
                        system  memory,  or  if the system memory scan

                        has been bypassed  using  option  "-nms",  the
                        first  time  that  the signature is found in a
                        file.   If you  encounter  this  warning,  you
                        should   make   very   certain  that  you  are
                        executing the IBM Virus Scanning Program after
                        having cold-booted from a write-protected  DOS
                        diskette  containing  the  IBM  Virus Scanning
                        Program, which has been certified to  be  free
                        of  viruses.    Otherwise,  the  dire  warning
                        indicates that continuing the scan may  result
                        in  corruption of other files by a virus.  (No
                        pause will occur if  the  IBM  Virus  Scanning
                        Program   is  run  in  an  OS/2  protect  mode
                        session.)

        Scan memory     This tells the IBM Virus Scanning  Program  to
                        report  any  instances  of  this virus that it
                        finds as it scans system memory.   It is  used
                        for   viruses   which  can  cause  significant
                        problems if they are resident in system memory
                        when  the  IBM  Virus  Scanning   Program   is
                        executed.    (If the "-G" option is specified,
                        the indicated message  will  be  displayed  if
                        *any*  of  the  signatures  is found in system
                        memory.   This is  not  done  as  the  default
                        behavior  because  signatures  can  be left in
                        system memory by other programs,  particularly
                        other  virus  scanners, even though no viruses
                        are resident.)

        No mutants      This tells the IBM Virus Scanning Program   to
                        not  search  for variations on this virus even
                        when the "-M"  option is used.  If a signature
                        is found to be prone  to  false  alarms  (most
                        likely  when  the "-M"   option is used), this
                        keyphrase will eliminate these false alarms.

For example, suppose that you discover a new virus, which you call the
"Purple   Virus."   You    have    determined    that    the    string
EA6061626364786566676869716A6B6C6D6E516FC0C1C8C958D6F1    appears   in
every copy of the virus, that the virus infects boot sectors, and that
the virus installs  a  resident  extension  that  tries  to  hide  the
infection  from virus detectors.  You could add the following lines to
your ADDENDA.LST file to scan for this virus:    (Naturally,  this  is
just an example, not a real virus.  Please don't use this signature or
entry.)
----------------------------------------------------------------------

*
* Entry for the non-existent Purple virus (just an example).
*
EA6061626364786566676869716A6B6C6D6E516FC0C1C8C958D6F1
A boot record of this disk may have the Purple virus.
(Boot records, Scan memory.)

----------------------------------------------------------------------

To  view  VIRSIG.LST, use the TYPE command to display the file on your
monitor, or use the PRINT command to print it on your printer.  If you
wish to view VIRSIG.LST with an editor, make a copy of  the  file  and
edit  the  copy.   Some editors make subtle changes to files.  The IBM
Virus Scanning Program will detect changes in VIRSIG.LST,  and  refuse
to run if it is changed.



4.3.1  SCANNING FILES
_____________________


VIRSIG.LST  contains  the  virus  signatures, including signatures for
viruses that can infect executable files.  Its format is described  in
the  preceding  section  entitled "The Format of the Signature Files".
By default, the IBM Virus Scanning Program scans files of  type  .EXE,
.COM,  .OV?,  .INI,  .BIN, and .SYS.  This can be changed with command
line options.



4.3.2  SCANNING BOOT RECORDS
____________________________


VIRSIG.LST also contains signatures for viruses that can  infect  boot
records  of  diskettes and hard disks, and for viruses that can infect
both files and boot records.  The IBM Virus Scanning Program will test
system boot sectors of any drives that are specified,  and  will  test
the master boot record of the first hard drive if a drive letter C: or
higher  is specified.  There are also command line options to scan any
particular drive for boot sector viruses.   System  boot  sectors  are
sometimes  known  as  partition boot sectors or DOS boot sectors.  The
master boot record contains the partition table for  a  physical  hard
disk.

Reference  "Limitations"  for further technical details about scanning
boot sectors.



4.4  ADDING MORE VIRUS SIGNATURES
_________________________________


If you want the IBM Virus Scanning  Program  to  scan  for  signatures
other  than  those  in  VIRSIG.LST,  you  should  create a file called
ADDENDA.LST and put the new signatures in this file.  ADDENDA.LST must
be placed in the same directory as VIRSCAN.EXE in order  for  the  IBM
Virus  Scanning Program to find it.  If the IBM Virus Scanning Program
can find an ADDENDA.LST file, it will load it along  with  VIRSIG.LST.
You  can  use  the "-V"   option to verify that the IBM Virus Scanning
Program  is loading your ADDENDA.LST file correctly.  ADDENDA.LST  (if
it  exists)  has  the  same format as VIRSIG.LST.   ADDENDA.LST is not
checked for modifications.



4.5  COMMAND-LINE OPTIONS
_________________________


Options to the IBM Virus Scanning Program  may  be  specified  on  the
command line as follows:

VIRSCAN [options]


[options]  may  be specified in any order, in upper or lower case, and
may consist of one or more of the following.

-A    Scan all files on the indicated drives.  This is useful when you
      are cleaning up after a virus  infection,  to  check  absolutely
      every  file  on  a  drive for the presence of viruses.  (See the
      "-G" option, which is also useful during cleanup.)

      The following will scan all files on the C: and D: drives:


      VIRSCAN C: D: -A

      By  default,  the IBM Virus Scanning Program only scans files of
      type EXE and COM, and boot sectors, on specified disks.

-B    Scan a boot sector.   If a logical  drive  letter  is  specified
      (e.g.  -BC:),  then  the  system  boot  sector  of  the drive is
      scanned.  If a physical drive number is specified  (e.g.  -B80),
      then the master boot record of the drive is scanned.

      The following scans only the system boot sector of the C: drive:

      VIRSCAN -BC:

      The  following  scans  only  the  master boot record of physical
      drive 80, which is the first physical hard disk.

      VIRSCAN -B80

      By default, the IBM Virus Scanning Program scans the system boot
      sector of specified drives (see the description  of  the  "path"
      that  follows),  and  the  master  boot record of the first hard
      drive if drive C:  or above is specified.

-C    Continue scan if there is an error opening a file for  scanning.
      In  some  operating  environments, a few files may be locked for
      some reason. If  the  IBM  Virus  Scanning  Program  is  failing
      because  it can't open such a file, use this option to force the
      IBM Virus Scanning Program to continue the scan.

-CAD  Continue if access denied.   If this option  is  used,  the  IBM
      Virus  Scanning  Program  will  continue  the scan even if it is
      unable to scan a particular subdirectory tree because access was
      denied.

-E    Do not scan boot sectors unless explicitly specified with the -B
      option.  This is useful if there is a problem scanning the  boot
      sector  of  a  drive  (for instance, a network drive).   If this
      option is used, the IBM Virus Scanning  Program  will  not  find
      boot sector viruses unless the -B option is used.

-G    The  Guru  option,  for  use  primarily  by technically inclined
      users.  By default, the IBM Virus Scanning Program only  reports
      signatures found in places where it expects them.  For instance,
      signatures  that are not specified as EXE file signatures in the
      signature file are not reported if they are  found  in  EXE-type
      files  (that is, files that have EXE headers).  If an offset for
      a signature is specified in the signature file, it will  not  be
      reported  if  it  is  found  at another location.   If the "Scan
      memory" keyphrase is not specified in the  signature  file,  the
      signature  will  not  be reported if it is found in memory.  The
      Guru option tells the IBM Virus Scanning  Program  to  report  a
      signature  no  matter  where  it  is  found.   This is useful in
      cleaning up after a virus infection, to make sure that you  have
      scanned  absolutely everything that could be harboring a copy of
      the virus.  It can cause false alarms, though, for instance when
      remnants of infected files remain in memory even though they are
      not dangerous.   (See the "-A"  option,  which  is  also  useful
      during cleanup.)

-H    Help.  A brief summary of the command-line options is displayed.

-L    Scan   the   files  listed  in  the  specified  file  for  viral
      signatures.  The specified file should contain one filename  per

      line.   The files to be scanned may be specified relative to the
      current drive and directory, or may  be  given  fully  qualified
      pathnames.

      The  following  scans  the  files  listed in FILES.DAT for viral
      signatures:

      VIRSCAN -LFILES.DAT

-M    Maybe detect mutants.  This tells the IBM Virus Scanning Program
      to try to detect small variations on the viruses listed  in  the
      signature  files.    Virus  signatures  are  broken  into random
      fragments, and the IBM Virus Scanning Program  will scan for the
      fragments as well as for the original signatures.  Additionally,
      this option tells the IBM Virus Scanning Program to report *all*
      signatures that are partially matched.  the IBM  Virus  Scanning
      Program  doesn't require that all bytes in a a long signature be
      matched; the number of mismatched bytes allowed is a function of
      the  length  of  a signature; the longer the signature, the more
      mismatched bytes are allowed.   By default,  if  the  IBM  Virus
      Scanning  Program    finds  one  or  more  partial match (and no
      complete matches) it will report the closest partial match.   If
      this option is used, the IBM Virus Scanning Program  will report
      *all*  partial  matches.   There is a small possibility of false
      alarms if this option is used,  since  short  fragments  may  be
      found  in  files  which  do  not contain viruses.   So, use this
      option with care, and be prepared to investigate in more  detail
      any  reports  of  signatures  found.   By default, the IBM Virus
      Scanning Program uses the entire signature string in the scan.

-MEM  Scan system memory By default, the IBM  Virus  Scanning  Program
      will scan memory before it scans anything else.  The -mem switch
      tells  the  IBM Virus Scanning Program to scan memory even if it
      scans nothing else.  Switches -nhms, -g and -m  all  modify  the
      behavior of the memory scan.  By default, the IBM Virus Scanning
      Program  will  only  scan  memory for certain viruses; if the -g
      switch is used, when the IBM Virus Scanning Program scans memory
      for viruses, it will scan for all of the viruses that  it  knows
      about.

-NB   No  beep.  By default, the IBM Virus Scanning Program  will beep
      when a virus signature is found.   This  switch  turns  off  the
      beep.   If the both the -NB and -Z switch are used, -NB will not
      turn off the beeps at program termination; only the beeps issued
      when a virus signature is found are disabled.

-NMBRS No master boot record scan.  Do not scan the master boot record
      of the first hard drive unless explicitly specified with the  -b
      option.    This  is  useful  if  there is a problem scanning the
      master boot record for some reason, but other boot  sectors  can
      be  scanned.  If  this  option  is  used, the IBM Virus Scanning
      Program won't find master  boot  record  viruses  (such  as  the
      Stoned  virus)  on  the first hard drive unless the -B option is
      used. (-B80 tells the IBM Virus Scanning  Program  to  scan  the
      master boot record of the first hard drive.)

-NLA  Do  not  display  the banner containing the copyright notice and
      license agreement when scanning for viruses, and do not  require
      the  user  to type "Y" before starting the scan.  This is useful
      when running the IBM Virus Scanning Program from a  BAT  or  CMD
      file  that should not require user interaction.  Your use of the
      IBM Virus Scanning Program is still subject  to  the  terms  and
      conditions  set  out  in the license agreement for this program.
      (For users in the United States and Puerto Rico, these  are  set
      out  in  the  READ.ME  file distributed with this program.   For

      users in other locations, see your  IBM  representative  or  IBM
      authorized supplier for contract terms.)  See the "-Q" and "-QQ"
      options for related functions.

-NHMS No  high  memory  scan.    Under  PC-DOS, the IBM Virus Scanning
      Program scans system memory for  indications  of  some  resident
      viruses.   This is because it is important for your system to be
      free of certain resident viruses when  the  IBM  Virus  Scanning
      Program is executed.  This option disables the memory scan above
      absolute  address  A0000. That means that the first 640K will be
      scanned, but not the memory between 640K and  1MB.  Most  memory
      resident  viruses  install  themselves  in the first 640K.  This
      option can be useful if you are having trouble with  the  memory
      scan,  but  we do not recommend its use in general.  This option
      is slightly risky, because it  may  miss  viruses  installed  in
      memory higher than the first 640K.

-NMS  No  memory  scan.   Under PC-DOS, the IBM Virus Scanning Program
      scans system memory for indications of  some  resident  viruses.
      This  is  because  it is important for your system to be free of
      resident  viruses  when  the  IBM  Virus  Scanning  Program   is
      executed.   This option disables the memory scan completely.  It
      can be useful if you are having trouble with  the  memory  scan,
      but  we  do not recommend its use in general.  If you are having
      trouble with the memory scan, we suggest that  you  try  "-nhms"
      first.  Use this option at your own risk!

-NMUT No  mutant  detection.    By  default, if the IBM Virus Scanning
      Program  finds one or more partially matched  signature  strings
      (and  no  complete  matches)  it will report the closest partial
      match.  If this option is used, the IBM Virus  Scanning  Program
      will not report partial matches.  This is useful if false alarms
      are being encountered with the default mutant detection.

-NP   No  progress  indicator.    By  default,  the IBM Virus Scanning
      Program displays the name of each file or boot sector as  it  is
      scanned,  to  give  you an indication of what it is doing.  This
      option tells the IBM Virus Scanning Program not to display these
      names.  (It will continue to display the names of files or  boot
      sectors containing any of the virus signatures.)  This is useful
      if  you  are  redirecting  the  output of the IBM Virus Scanning
      Program to a file and only want the summary of the scan.

      The following will produce a summary of a scan of the  C:  drive
      in  the  file  VIRSCAN.OUT in the current directory, without the
      long list of all files that were scanned:

      VIRSCAN C: -NP  >  VIRSCAN.OUT

-NST  No self-test.   By  default,  the  IBM  Virus  Scanning  Program
      verifies  that  VIRSCAN.EXE, VIRSIG.LST and VIRSCAN.MSG have not
      been modified, either accidentally or by a virus.   This  option
      disables  the test.  While the self-test takes a little time, it
      is an important aid in maintaining the integrity of the  program
      and the signature files.  Use this option at your own risk!

-P    Build  a  list of files that tested positive.  This is useful if
      you want to have a list of infected files for use in  a  cleanup
      process.    If no filename is specified, the default output file
      POSITIVE.VIR in the current directory will be used.    The  file
      will  not  be  created  unless  one or more virus signatures are
      found.




      The following will scan the C: and E: drives, and put the  names
      of  any infected files into the file POSITIVE.VIR in the current
      directory:

      VIRSCAN E: C: -P

      The following will scan D:\MANGO and its subdirectories, and put
      the names of any infected files into the file C:\INFECTED.LST:

      VIRSCAN D:\MANGO -PC:\INFECTED.LST

path  Scan  a  PC-DOS  or  OS/2  logical  drive  or directory.   (Also
      available as -Dpath) This is the most common option  to  specify
      to  the IBM Virus Scanning Program.  If you specify only a drive
      letter, the IBM Virus Scanning Program will scan the system boot
      sector of that drive, and all subdirectories on the drive.    If
      you specify a path, the IBM Virus Scanning Program will scan the
      directory specified by that path, and all of its subdirectories.
      If  a  drive  letter is given as part of the path specification,
      its system boot sector will be scanned as well.  If drive C:  or
      above  is  specified  (e.g.  C:,  D:, E:, etc.), the master boot
      record of the first hard drive will be scanned.

      The following two commands are equivalent,  and  will  scan  the
      master  boot record on physical drive 80, the system boot sector
      on the C: drive, and all subdirectories on the C: drive:

      VIRSCAN C:

      VIRSCAN -DC:

      The following scans the subdirectory \LIME\GUAVA  on  drive  D:,
      all  of its subdirectories, as well as the master boot record of
      physical drive 80 and the system boot sector of drive D:

      VIRSCAN D:\LIME\GUAVA

      The following scans the subdirectory  GUAVA  under  the  current
      directory of the current drive, and all of its subdirectories:

      VIRSCAN .\GUAVA

      Note  that  it  does  not  scan  the boot sectors of the current
      drive, since no drive letter was specified.

-Q    Quiet  output.    Do  not  display  the  banner  containing  the
      copyright  information for this program.  The only messages that
      will be displayed are those that indicate that a viral signature
      has been found, error messages,  and  warnings  if  particularly
      troublesome  viruses are found (as indicated by "Pause if found"
      in the signature files).  This is useful when executing the  IBM
      Virus  Scanning  Program  from a BAT or CMD file that checks the
      error level and takes its own action if a virus is found.

      Your use of the IBM Virus Scanning Program is still  subject  to
      the  terms  and  conditions set out in the license agreement for
      this program.  (For users in the United States and Puerto  Rico,
      these  are  set  out  in  the READ.ME file distributed with this
      program.    For  users  in  other  locations,   see   your   IBM
      representative or IBM authorized supplier for contract terms.)

      "-QQ"  option  for  similar  function.   See the"-NLA" and "-QQ"
      options for similar functions.

-QQ   Very quiet output.   Do not display the  banner  containing  the
      copyright  information for this program. Also disable display of
      any other messages, except for fatal error messages and warnings
      if particularly troublesome viruses are found.   (The latter  is
      indicated by "Pause if found" in the signature files.)  The only
      indication  that  viral  signatures have been found is the error
      level returned by the IBM  Virus  Scanning  Program.    This  is
      useful  when executing the IBM Virus Scanning Program from a BAT
      or CMD file that checks the error level and takes its own action
      if a virus is found.

      Your use of the IBM Virus Scanning Program is still  subject  to
      the  terms  and  conditions set out in the license agreement for
      this program.  (For users in the United States and Puerto  Rico,
      these  are  set  out  in  the READ.ME file distributed with this
      program.    For  users  in  other  locations,   see   your   IBM
      representative or IBM authorized supplier for contract terms.)

      "-QQ"  option  for  similar  function.   See the"-NLA" and "-QQ"
      options for similar functions.

-R    Removable media support.  This indicates that a given drive  has
      removable  media,  such  as floppy diskettes.   If that drive is
      then specified as a drive to be scanned, The IBM Virus  Scanning
      Program  will  prompt the user to insert additional diskettes to
      be scanned in that drive.  This is useful when you are  scanning
      a number of floppy diskettes, which is a common thing to do when
      first scanning a system, or when cleaning up after an infection.

      The  following  will  let  you  scan  every diskette in a box of
      diskettes in the A:  drive:

      VIRSCAN -RA: A:

      Note that the "-RA:" option just tells the  IBM  Virus  Scanning
      Program  that  drive A:  has removable media.  The separate "A:"
      option tells the IBM Virus  Scanning  Program  to  scan  the  A:
      drive.

-S    Use a non-default signature file for this scan.  By default, the
      IBM  Virus  Scanning  Program  uses  the signatures in the files
      VIRSIG.LST, and (if it is present)  ADDENDA.LST  for  its  scan.
      This option allows you to use other files instead.

      If  this  option is used, the default signature file isn't used,
      unless it is also specified explicitly  with  the  "-S"  option.
      For  this  reason,  you should use this option with care, and at
      your own risk!

      The following scans the C: drive using  the  signatures  in  the
      file  MYSIG.DAT, as well as the file VIRSIG.LST.  in the current
      directory.

      VIRSCAN C: -SVIRSIG.LST -SMYSIG.DAT

      The following scans the D: drive using only  the  signatures  in
      the file C:\UTIL\MYSIG.DAT.  It does *not* use the signatures in
      VIRSIG.LST.

      VIRSCAN D: -SC:\UTIL\MYSIG.DAT


-T    Scan a single, specified file for viral signatures.

      The following scans the file PRUNE.OVL in the current directory:


      VIRSCAN -TPRUNE.OVL

      The following scans the file C:\UTIL\PLUM\PRUNE.OVL:

      VIRSCAN -TC:\UTIL\PLUM\PRUNE.OVL

-V    Verbose  output.  This displays a list of files and boot sectors
      as they are  scanned,  and  in  general  forces  the  IBM  Virus
      Scanning  Program  to  display more information than normal.  It
      forces the IBM  Virus  Scanning  Program  to  do  a  hexadecimal
      display  of  any  virus  signatures that are found.   It is very
      helpful to use this option to help diagnose  the  problem  if  a
      scan  terminates  early  due to error.  It is also useful if you
      are experimenting with command line options, to verify that what
      you think you specified is what you specified.  Note: If you use
      the "-V" option, you should  specify  it  on  the  command  line
      before any other options.

-VV   Very verbose output.  This is similar to the "-V" option, except
      that a hexadecimal dump of boot sectors is also displayed.  This
      is  useful  when diagnosing problems with scanning boot sectors.
      Note: If you use the "-VV" option, you should specify it on  the
      command line before any other options.

-VL   Create  a  log file.   This tells virscan to create a log of the
      virus scan. The default log file name is "virscan.lgf",  in  the
      current directory. A file name may also be specified explicitly.
      The  following  scans  the  C:  drive  and  creates the log file
      "virus.log" in the root directory of the C:  drive.

      VIRSCAN C: -VLC:\VIRUS.LOG

-W    Wildcard file specification.  By default, the IBM Virus Scanning
      Program only scans files of type EXE, COM, OV?,  INI,  and  SYS.
      (and  boot  sectors,  of  course).    This option can be used to
      specify arbitrary file types to scan.

      The following will scan files of type OVL and MEM on the C:  and
      D:  drives:

      VIRSCAN C: D: -W*.OVL,*.MEM

      The  following will scan all files with file name KIWI on the E:
      drive:

      VIRSCAN E: -WKIWI.*

-Z    Pause with beeps if any virus signatures were found.   When  the
      scan  finishes,  if any virus signatures were found, this switch
      will force the IBM Virus Scanning Program    to  beep  once  per
      second and wait for the user to press a key.

*     Scan  all fixed disks. (Not supported under DOS 2.0 or 2.1) This
      option  tells  virscan  to  scan  all  of  the  system's   local
      non-removable  disks.  For  example,  if  the system has 2 fixed
      disks partitioned into 3 disk partitions "C:", "D:",  and  "E:",
      and a virtual disk "F:"

      VIRSCAN *

      is equivalent to

      VIRSCAN C: D: E: F:

      Similarly, all network drives can be scanned with

      VIRSCAN *n

      and  all  network  and local non-removable drives can be scanned
      with

      VIRSCAN *fn

?     Help.  A brief summary of the command line options is displayed.

??    Usage examples.  Examples are given showing how to use  the  IBM
      Virus Scanning Program in some of the most common circumstances.



4.6  VALUES OF ERRORLEVEL RETURNED
__________________________________


The  IBM  Virus Scanning Program sets the DOS or OS/2 error level upon
exit to one of several values, depending upon what it found.

0         No virus signatures were found, and no  other  fatal  errors
          occurred.

1         No  virus  signatures were found, but the program terminated
          with some other error before the scan was complete.

2         One or more virus signatures were found.

These error levels can be used within BAT and CMD files  that  execute
the  IBM  Virus  Scanning  Program, to respond differently to what the
program finds.



4.7  LIMITATIONS
________________


While the IBM Virus Scanning Program can help you detect the  presence
of  many  viruses,  it  does have its limitations.  It is important to
understand what these are, and how  to  use  the  IBM  Virus  Scanning
Program properly, in order to best protect your system.



4.7.1  THE IBM VIRUS SCANNING PROGRAM IS NOT A CURE-ALL
_______________________________________________________


In  typical  computing  systems, it is not possible for any program to
detect all possible viruses that may exist in the  future.    The  IBM
Virus  Scanning Program is designed to help you detect the presence of
many of the viruses that we already know  about.    It  does  this  by
scanning  for  the  signatures  found  in  the  file  VIRSIG.LST,  and
ADDENDA.LST if it is  present.    Viruses  whose  signatures  are  not
contained in these files will probably not be detected.



4.7.2  THE IBM VIRUS SCANNING PROGRAM DOES NOT REMOVE VIRUSES
_____________________________________________________________


The  IBM  Virus  Scanning  Program  does  not  attempt to remove viral
infections from a system.    If  you  discover  that  your  system  is

infected  with a virus, you should seek competent technical assistance
to prevent the infection from spreading to other systems, and to clean
up the infection safely.



4.7.3  THE IBM VIRUS SCANNING PROGRAM MAY NOT FIND VIRUSES IN ARCHIVES
______________________________________________________________________


The  IBM  Virus Scanning Program cannot find virus signatures in files
that are compressed or encrypted.  This includes files that have  been
compressed by archiving programs.

To scan such files, unpack them first, and then scan their constituent
files.

Self-extracting  archives  are  programs (typically files of type EXE)
that are compressed, but decompress themselves into their  constituent
files   when   they  are  executed.    Some  viruses  can  infect  the
decompression part of these  programs,  and  the  IBM  Virus  Scanning
Program    will  detect them.   It is also possible for the compressed
programs stored within these files to be  infected.    The  IBM  Virus
Scanning Program  will not detect this while they are compressed.



4.7.4  SCANNING BOOT SECTORS
____________________________


When  the  IBM  Virus Scanning Program  is run in an OS/2 protect mode
session, it cannot scan the master boot record of the hard disk.  As a
result, it cannot find master-boot-record viruses (such as the  Stoned
virus) on hard disks, when it is executed under OS/2.  The master boot
record  is  scanned  when  the  IBM Virus Scanning Program is executed
under PC-DOS, including the DOS Compatibility Box of OS/2.

When the IBM Virus Scanning Program is asked to scan any drive with  a
drive  letter  of C: or greater, it scans the partition boot sector of
each requested drive, and the master boot record of the physical  hard
disk  80,  which  is  the  first physical hard disk.   This is usually
sufficient, since most systems only use this master boot record.    If
you  want  to  scan  the master boot record of any other physical hard
disk, you must specify it explicitly.   For  instance,  the  following
will  scan  the  master  boot  record  of  physical  disk 81, which is
typically the second physical disk:

VIRSCAN -B81



4.8  COMMON PROBLEMS
____________________


There are a few circumstances in which users  have  difficulties  with
the  IBM  Virus  Scanning  Program.    This section discusses the most
common problems and tells you what to do about them.



4.8.1  SYSTEMS WITH DAMAGED DIRECTORY TREES
___________________________________________


On some systems, the IBM Virus Scanning Program will terminate with an
error (usually "run-time error 6000").   This  is  often  due  to  the
system  having a damaged directory tree, in which one part of the tree

appears to contain the entire directory all over again.    While  this
condition  is  not  caused  by the IBM Virus Scanning Program, it will
prevent  the  IBM  Virus  Scanning  Program  from  scanning  the  disk
correctly.

You  should  run the CHKDSK program to diagnose any such problems.  If
CHKDSK reports errors, refer  to  your  PC-DOS  or  OS/2  manuals  for
instructions on correcting them.



4.8.2  INCOMPATIBLE VERSIONS OF PC-DOS AND COMMAND.COM
______________________________________________________


Occasionally,  users  will  have a version of COMMAND.COM which is not
compatible with the version of PC-DOS that they are using.   This  may
happen  when  PC-DOS  is  updated,  but  the  user  forgets  to update
COMMAND.COM.   It causes the  following  message  when  attempting  to
execute  the  IBM  Virus  Scanning  Program:   "SYS2090: The system is
unable to load the program." While this is not caused by the IBM Virus
Scanning Program, it will prevent the IBM Virus Scanning Program  from
executing.

If  you  encounter  this error, type VER to determine which version of
the operating system you are  using.    Then  replace  all  copies  of
COMMAND.COM with the version contained on the manufacturer's original,
write-protected  diskette  for  the  correct  version of the operating
system.  Reboot the system and try  running  the  IBM  Virus  Scanning
Program again.



4.8.3  LIMITATION WHEN SCANNING BOOT RECORDS OF NETWORK DRIVES
______________________________________________________________


Some local area network programs allow you to access a disk drive on a
remote  system  as  if  it were one of your own local drives.  The IBM
Virus Scanning Program sometimes cannot scan the boot sectors of these
drives, due to limitations in the local area  network  software.    In
these cases, it will display a message similar to the following.
----------------------------------------------------------------------

There was an error reading system boot sector for drive G:, INT 25 rc=000D
Error scanning system boot sector of drive G:
(This is normal if drive G: is a network drive.)
(Continuing Scan)

----------------------------------------------------------------------

This  indicates that the IBM Virus Scanning Program could not scan the
boot sector of that drive, but that the scan continued normally.  This
is not a fatal error.



4.8.4  FALSE ALARMS WHEN SCANNING MEMORY
________________________________________


When the IBM Virus Scanning  Program  scans  system  memory,  it  will
occasionally find remnants of virus signatures left over from programs
that  had  been  run  previously.    In  particular,  some other virus
scanning programs will leave remnants of the signatures  they  use  in
memory.    (This includes the IBM Virus Scanning Program version 1.0.)
This can cause the IBM Virus Scanning Program to report  the  possible
presence of a virus in memory when there is none.  This is most likely
to  happen  when  the  "-G"  option  is used, which asks the IBM Virus
Scanning Program to report any signatures found, regardless  of  where
they are found.

If  this problem is suspected, cold-boot the system from a virus-free,
write-protected floppy diskette  (see  "Safely  Using  the  IBM  Virus
Scanning Program" for details), and run the IBM Virus Scanning Program
again.    This  will  ensure  that  there  are no remnants of previous
programs in memory when the IBM Virus Scanning Program executes.



5.0  VIRUSES DETECTED BY THE IBM VIRUS SCANNING PROGRAM
_______________________________________________________



This  section describes the viruses scanned for by this version of the
IBM Virus Scanning Program.



5.1  VIRUS LIST AND CHARACTERISTICS
___________________________________


The following table  summarizes  the  characteristics  of  the  PC-DOS
viruses  that  the IBM Virus Scanning Program version 2.1.2 scans for.
The meaning of the columns is as follows.

o   Infects COM.  The virus infects COM files.

o   Infects EXE.  The virus infects EXE files.

o   Uses "MZ" for criterion.   The virus  looks  for  an  EXE  header,
    rather  than a file type of EXE, in order to determine which files
    to infect.  An EXE header has the ASCII characters MZ (hexadecimal
    4A and 5D) as the first two bytes of the file.  If it finds  these
    two bytes, the virus will infect that file.  Viruses that use this
    infection  criterion  can infect files of any type, as long as the
    files have an EXE header.  (This is the same criterion used by the
    DOS loader to decide if a file has an EXE format.)

o   Infects diskette boot.   The virus infects  the  boot  sectors  of
    floppy  diskettes  and  will  become  active  in a system which is
    booted from an infected floppy diskette.

o   Infects HD system boot.  The virus infects the system boot  sector
    of  hard  disks and will become active in a system which is booted
    from an infected hard disk.

o   Infects HD master boot.  The virus infects the master boot  record
    of  hard  disks and will become active in a system which is booted
    from an infected hard disk.

o   Resident.         The    virus    installs     itself     as     a
    terminate-and-stay-resident (TSR) extension to DOS when it is run.
    This  TSR  is  then  used to spread the infection.  The virus will
    remain active in a system even  after  the  infected  program  has
    finished  running.   Some of these viruses will remain active even
    if the system is rebooted using Ctl-Alt-Del.  They will not remain
    active if the system is cold-booted from a disk or  diskette  that
    is known to be free of viruses.

An "x" is placed in a column if a virus possesses that characteristic.
A "." is placed in the column if it does not.

New or name changed with this release---+
Resident------------------------------+ |
Infects HD master boot--------------+ | |
Infects HD system boot------------+ | | |
Infects diskette boot-----------+ | | | |
Uses "MZ" for criterion-------+ | | | | |
Infects EXE-----------------+ | | | | | |
Infects COM---------------+ | | | | | | |
                          | | | | | | | |
Virus                     V V V V V V V V Notes
----------------------------------------  ----------------------------------
1067                      x . . . . . x .

1253                      x . . x . x x .
1381                      . x ? . . . x .
1392                      x x x . . . x .
1536                      x . x . . . x .
1575                      x x . . . . x .
1624                      . x x . . . . .
1701                      x . x . . . x .
1701-Jojo                 x . x . . . x .
1704                      x . x . . . x .
1704-B                    x . x . . . x .
1704-C                    x . x . . . x .
1704-Format               x . x . . . x .
1704-Y                    x . x . . . x .
1813                      x x . . . . x .
1813-00                   x x . . . . x . Minor variant, virscan says "1813".
1813-1605                 x x . . . . x .
1813-ANARKIA              x x . . . . x .
1813-Discom               x x . . . . x .
1813-Groen Links          x x . . . . x .
1813-Not-13               x x . . . . x .
1813-Puerto               x x . . . . x .
1813-Swiss                x x . . . . x .
1813-Westwood             x x . . . . x .
2086                      x x . . . . x .
3445                      x x . . . x x x Infects MBR with Campana virus.
382                       x . . . . . . x
4096                      x x x . . . x .
453                       x . . . . . . .
5120                      x x ? ? ? ? ? .
555                       x x x . . . x .
637                       . x x . . . . .
9800:0000                 x x x . . . x .
Agiplan                   x x ? ? ? ? ? .
Aircop                    . . . x . . x .
Alabama                   . x . . . . x .
Ambulance                 x . . . . . . .
ANTHRAX                   x x ? ? ? x ? .
AntiPascal-400            x . . . . . . .
AntiPascal-440            x . . . . . . .
AntiPascal-480            x . . . . . . .
AntiPascal-529            x . . . . . . .
AntiPascal-605            x . . . . . . .
April 1st COM             x . . . . . x .
April 1st EXE             . x . . . . x .
Armagedon                 x ? ? ? ? ? ? .
Azusa                     . . . x . x x .
Black Monday              x x . . . . x .
Blood                     x . . . . . . .
Bloody!                   . . . x . x x .
Bouncing Ball             . . . x x . x .
Bouncing Ball/286         . . . x x . x .
Brain                     . . . x . . x .
Brain-Ashar               . . . x . . x .
Brain-Shoe                . . . x . . x .
Brunswick                 . . . x . x x .
Burger-405                x . . . . . . .
Burger-537                x x . . . . . .
Burger-541                x x . . . . . .
Burger-542                x x . . . . . .
Burger-560                x . . . . . . .
Campana                   . . . x . x x .
CARA                      x . . . . . x .
Carioca                   x ? ? ? ? ? ? .
Casino                    x . . . . . x .
CHV 2.1                   x . . . . . x .
Crash-1075                x x . . . . x .
Crazy Eddie               x x ? ? ? x ? .
Crew-2480                 x . . . . . . .
CSSR-528                  x . . . . . . .
Dark Avenger              x x x . . . x .
Dark Avenger-2100         x x x . . . x .
DataCrime II              x x x . . . . .
DataCrime II-B            x x x . . . . .
DataCrime-1168            x . . . . . . .
DataCrime-1280            x . . . . . . .
DataLock                  x x x . . . x .
DBF                       x . . . . . x .
December 24th             . x x . . . x .
DEICIDE                   x . . . . . . .
Den Zuk                   . . . x . . x .
Devil's Dance-941         x . . . . . x .
DIRVIR                    x ? ? ? ? ? x .
Disk Killer               . . . x x . x .
Doom 2                    x x . . . . x x
Do-Nothing                x . . . . . x .
Do-Nothing 2              x . . . . . x .
Eddie-651                 x x x . . . x .
EDV                       . . . x . x x .
Eight Tunes-1971          x x x . . . x .
Evil Empire               . . . x . x x .
Evil Empire-B             . . . x . x x .
Falling Letters Boot      . . . x . . x .
Fellowship                x x . . . . x .
FILLER                    . . . ? ? ? ? .
Fish 6                    x x x . . . x .
FLASH                     x x . . . . x .
Flip-2153                 x x x . . x x . Also changes 1 byte HD system boot
Flip-2343                 x x x . . x x . Also changes 1 byte HD system boot
FORM                      . . . x x . x .
Friday the 13th COM       x . . . . . . .
Fumble-867                x . . . . . . . Has a non-viral resident extension
Guppy                     x . x . . . x .
Halloechen                x x x . . . x .
Happy Day                 x . . . . . . .
Iceland II                . x . . . . x .
ITAVIR                    . x x . . . . .
Japanese Christmas        x . ? ? ? ? ? .
Jeff                      x . x . . . . .
Joshi                     . . . x . x x .
July 13th                 . x ? ? ? ? ? .
June 16th                 x . . . . . . .
Kamikaze                  x x x . . . x .
Kennedy-163               x . . . . . . .
Kennedy-333               x . . . . . . .
KeyPress                  x x ? ? ? ? x .
Klaeren                   x x . . . . x .
LAO DOUNG                 . . . x x . x x
LBC                       . . . x . . x .
Lehigh I                  x . . . . . x . Only infects COMMAND.COM
Leprosy                   x . . . . . . .
Leprosy-B                 x . . . . . . .
Liberty                   x x x . . . x .
Mardi Bros                ? ? ? ? ? ? ? . Infects boot records for sure.
MG1                       x ? ? ? ? ? ? .
MG3                       x ? ? ? ? ? ? .
Michelangelo              . . . x . x x .
MICROBE                   . . . x . . x .
Mirror                    x x . . . . x .
MIX1                      . x . . . . x .
MIX1-B                    . x . . . . x .
Murphy 1                  x x ? ? ? ? x .
Murphy 2                  x x ? ? ? ? x .
MusicBug                  . . . x ? ? x .
Nobock                    x . . . . . . .
Noint                     . . . x . x x .
Nomenklatura              x x x . . . x .
Ohio                      . . . x . . x .
Ohio0                     . . . x . . x .
Ontario                   x x x . . . x x
OROPAX                    x . . . . . x .
Pentagon                  . . . x . . x .
Perfume-765               x . . . . . x .
Pixel-277                 x . . . . . . .
Pixel-299                 x . . . . . . .
Pixel-345                 x . . . . . . .
Pixel-740                 x . . . . . . .
Pixel-847                 x . . . . . . .
Pixel-852                 x . . . . . . .
Plastique 4.51            x x ? . . . ? .
Plastique 5.21            x x ? x ? x x .
Plastique-2576            x x ? ? ? ? ? .
Plastique-2900            x x ? ? ? ? ? .
Plastique-Invader         x x . x . x x .
POLIMER                   x . ? . . . . .
PrtSc                     . . . x . x x .
Prudents-1210             . x x . . . . .
PSQR-1720                 x x . . . . x .
Raubkopi                  x x x . . . . .
SADAM                     x . . . . . x .
Saratoga 1                . x . . . . x .
Saratoga 2                . x . . . . x .
Saturday 14th             x x x . . . x .
Shake                     x . . . . . x .
Slow                      x x x . . . x .
Slow-2131                 x x ? ? ? ? x .
Smiley Worm               . . . x x . x x
Solano                    x . x . . . x .
Sparse                    x . . . . . x .
STAF                      x . . . . . . .
Stardot-600               x . x . . . . .
Stardot-789               x x x . . . . x
Stardot-801               x x x . . . . .
Stoned                    . . . x . x x .
Stoned 2                  . . . x . x x .
Stoned-Alberta            . . . x . x x .
Stoned-ZAPPED             . . . x . x x .
Sunday                    x x . . . . x .
Sunday 2                  x x . . . . x .
Suomi                     x . ? ? ? ? . .
sURIV 3.00                x x . . . . x .
SVIR                      . x . . . . . .
Swedish Disaster          . . . x . x x .
Sylvia                    x . . . . . . .
SYSLOCK                   x x x . . . . .
Taiwan                    x . . . . . . .
Taiwan 2                  x . . . . . . .
Talentless Jerk           x . . . . . . .
Tequila                   . x . . . x x .
Telecom                   x . . . . x x x Infects MBR with Campana virus
Tiny-134                  x . x . . . x .
Tiny-138                  x . x . . . x .
Tiny-143                  x . x . . . x .
Tiny-154                  x . x . . . x .
Tiny-156                  x . x . . . x .
Tiny-158                  x . x . . . x .
Tiny-159                  x . x . . . x .
Tiny-160                  x . x . . . x .
Tiny-167                  x . x . . . x .
Tiny-198                  x . x . . . x .
TP06VIR                   x ? ? ? ? ? x . Relatives of the 2885 and VACSINA
TP16VIR                   x ? ? ? ? ? x .
TP23VIR                   x ? ? ? ? ? x .
TP24VIR                   x ? ? ? ? ? x .
TP25VIR                   x ? ? ? ? ? x .
TP33VIR                   x ? ? ? ? ? x .
TP34VIR                   x ? ? ? ? ? x .
TP41VIR                   x ? ? ? ? ? x .
TP42VIR                   x ? ? ? ? ? x .
TP45VIR                   x ? ? ? ? ? x .
TP46VIR                   x ? ? ? ? ? x .
Traceback-2930            x x x . . . x .
Traceback-3066            x x x . . . x .
Turbo-448                 x . ? . . . x .
Turbo-Kukac               x . ? . . . x .
Typo Boot                 . . . x x . x .
V1024                     x x x . . . x .
V2000                     x x x . . . x .
V512                      x . . . . . x .
V512-B                    x . . . . . x .
V512-C                    x . . . . . x .
V512-D                    x . . . . . x .
V800                      x x ? ? ? ? ? .
VACSINA                   x . x . . . x . Changes EXE files to COM files
VCS 1.0                   x . . . . . . .
VHP-348                   x . . . . . . .
VHP-353                   x . . . . . . .
VHP-367                   x . . . . . . .
VHP-435                   x . . . . . . .
VHP-623                   x . . . . . . .
VHP-627                   x . . . . . . .
Victor                    x x ? ? ? ? x .
Vienna-535                x . . . . . . .
Vienna-646                x . . . . . . .
Vienna-648                x . . . . . . . Puts reboot code in COM files
Vienna-Choinka            x . . . . . . .
Vienna-Ghost              x . . . . . . . Puts non-viral code in boot sectors
Vienna-Ira                x . . . . . . .
Vienna-Lisbon             x . . . . . . . Puts the string "@AIDS" in COM files
Vienna-Monxla             x . ? . . . . . Sometimes installs non-viral int hdlr
Vienna-Viola              x . . . . . . .
Vienna-Viola B4           x . . . . . . .
VIRDEM                    x . . . . . . .
VIRDEM 2                  x . . . . . . .
VIRUS-90                  x . x . . . . .
VP                        x . . . . . . .
Vriest                    x . . . . . x .
W13-A                     x . . . . . . .
W13-B                     x . . . . . . .
Washburn-1260             x . . . . . . .
Washburn-Casper           x . . . . . . .
Washburn-V2P2             x . . . . . . .
Whale                     x x ? ? ? ? x .
Whale-B                   x x ? ? ? ? x .
Wisconsin                 x . ? ? ? ? . .
XA1                       x . . . . . . . Overwrites boot records on April 1
Yale                      . . . x . . x .
Yankee Doodle-2772        x x x . . . x .
Yankee Doodle-2885        x x x . . . x .
Yankee-1961               . x x . . . . .
Yaunch                    . x . . . . . x
Zero Hunt                 x . x . . . x .
Zero Hunt-B               x . x . . . x .
ZK-900                    x x x . . . x .



5.2  CROSS-REFERENCE OF COMMON VIRUS NAMES
__________________________________________


Computer  viruses  are  called  by  a  variety  of names.   Sometimes,
different people refer to the same virus by  different  names,  or  to
different  viruses by the same name.  This table attempts to translate
some of the more common names into the name  used  by  the  IBM  Virus
Scanning Program.  Since these names are used differently by different
people,  the  entries in this table may not reflect every use of these
names by others.  Sometimes different people use the same name, but it
differs in capitalization (e.g.   ANTHRAX v.s.   Anthrax).    In  such
cases, this table only includes an entry for our capitalization.

Nickname                 Name Used By the IBM Virus Scanning Program


100 Years                4096
1008                     Suomi
1022                     Fellowship
1024                     V1024
1168                     DataCrime-1168
1210                     Prudents-1210
1253                     1253
1260                     Washburn-1260, Washburn-V2P2 or Washburn-Casper
1260-Casper              Washburn-1260, Washburn-V2P2 or Washburn-Casper
1280                     DataCrime-1280
1381                     1381
1392                     1392
1392 (Amoeba)            1392
1514                     DataCrime II
1536                     1536
1536 (Zero Bug)          1536
1539                     XA1
1554                     9800:0000
1559                     9800:0000
1575                     1575
1605                     1813-1605
1624                     1624
1701                     1701
1701-Jojo                1701-Jojo
1701-Jojo                1701-Jojo
1701/1704 - Version B    1701, 1704, 1704-B, 1704-C, 1704-Format, 1704-Y
1704                     1704
1704 Format              1704-Format
1704-B                   1704-B
1704-C                   1704-C
1704-Format              1704-Format
1704-Y                   1704-Y
170X                     1701, 1704, 1704-B, 1704-C, 1704-Format, 1704-Y
1720                     PQSR
17XX                     1701, 1704, 1704-B, 1704-C, 1704-Format, 1704-Y
17Y4                     1704-Y
1808(EXE)                1813
1813                     1813
1813(COM)                1813
1813-00                  1813
1813-1605                1813-1605
1813-ANARKIA             1813-ANARKIA
1813-Mendoza             1813           (Not differentiated by VIRSCAN)
1813-not-13              1813-not-13
1813-Puerto              1813-Puerto
1813-Swiss               1813-Swiss
1813-Tuesday-1st         1813           (Not differentiated by VIRSCAN)
1813-Westwood            1813-Westwood
1917                     DataCrime II-B
1961 (Yankee)            Yankee-1961
1971                     Eight Tunes-1971
1971(Eight Tunes)        Eight Tunes-1971
2086                     2086
2131                     Slow-2131
2153 (Flip)              Flip-2153
2343 (Flip)              Flip-2343
2772                     Yankee Doodle-2772
2885                     Yankee Doodle-2885
2930                     Traceback-2930
3066                     Traceback-3066
3066/2930 Traceback      Traceback-2930, Traceback-3066
333                      Kennedy-333
3445                     3445
3551                     SYSLOCK
3551 (Syslock)           SYSLOCK
3555                     SYSLOCK
382                      382
3880                     ITAVIR
405                      Burger-405
4096                     4096
453                      453
4711                     Perfume-765
512                      V512
5120                     5120
537                      Burger-537
541                      Burger-541
555                      555
560                      Burger-560
637                      637
640k                     Do Nothing
648                      Vienna-648
648-Lisbon               Vienna-Lisbon
651                      Eddie-651
688                      FLASH
765                      Perfume-765
847                      Pixel-847
867                      Fumble-867
903                      CHV 2.1
941                      Devil's Dance-941
9800:0000                9800:0000
Agiplan                  Agiplan
Aircop                   Aircop
Alabama                  Alabama
Alameda                  Yale
Ambulance                Ambulance
Ambulance Car            Ambulance
AMOEBA                   1392
Amstrad                  Pixel-847
ANARKIA                  1813-ANARKIA
ANTHRAX                  ANTHRAX
AntiCad                  1253
AntiCad 4.Mozart         Plastique-Invader
AntiCad 5                Plastique-2576
Anticad 3.a              Plastique 4.51
Anticad 1.a              Plastique 5.21
AntiPascal-400           AntiPascal-400
AntiPascal-440           AntiPascal-440
AntiPascal-480           AntiPascal-480
AntiPascal-529           AntiPascal-529
AntiPascal-605           AntiPascal-605
April 1st                April 1st COM, April 1st EXE, Suriv 1.01
April 1st COM            April 1st COM
April 1st EXE            April 1st EXE
Arab Star                1813
Armagedon                Armagedon
Armagedon the First      Armagedon
Armagedon the GREEK      Armagedon
Ashar                    Brain-Ashar
Austrian                 Vienna-648
Austrian 2               1701, 1704
Autocad 2                Plastique-2900
Autumn                   1701, 1704
Autumn Leaves            1701, 1704
Azusa                    Azusa
BASIC                    5120
Better world             Fellowship
Black Avenger            Dark Avenger
Black Friday             1813
Black Hole               1813
Black Monday             Black Monday
Black Window             1813
Blackjack                1704B
Blood                    Blood
Bloody                   Bloody!
Bloody!                  Bloody!
Bouncing Ball            Bouncing Ball
Bouncing Ball/286        Bouncing Ball/286
Bouncing Dot             Bouncing Ball
Brain                    Brain
Brain-Ashar              Brain-Ashar
Brain-Shoe               Brain-Shoe
Brunswick                Brunswick
Burger-405               Burger-405
Burger-537               Burger-537
Burger-541               Burger-541
Burger-542               Burger-542
Burger-560               Burger-560
Campana                  Campana
CARA                     CARA
Carioca                  Carioca
Cascade                  1701, 1704
Cascade-B                1704-B
Casino                   Casino
Casper                   Washburn-1260, Washburn-V2P2 or Washburn-Casper
Chameleon                Washburn-1260
Choinka                  Vienna-Choinka
Christmas in Japan       Japanese Christmas
CHV 2.1                  CHV 2.1
Columbus Day             DataCrime-1280, DataCrime-1168, DataCrime II, DataCrime II B
COM                      Friday the 13th COM
Computer Ogre            Disk Killer
Crash-1075               Crash-1075
Crazy Eddie              Crazy Eddie
Crew-2480                Crew-2480
CSSR                     CSSR-528
CSSR-528                 CSSR-528
Cursey                   EDV
Dark Avenger             Dark Avenger
Dark Avenger 2           Eddie-651
Dark Avenger II          V2000
Dark Avenger III         V1024
Dark Avenger-2100        Dark Avenger-2100
DataCrime                DataCrime-1280, DataCrime-1168
DataCrime B              DataCrime-1168
DataCrime II             DataCrime II
DataCrime II B           DataCrime II-B
DataCrime II b           DataCrime II-B
DataCrime II-B           DataCrime II-B
DataCrime-1168           DataCrime-1168
DataCrime-1280           DataCrime-1280
DataCrime-2              DataCrime II
DataLock                 DataLock
DBASE                    DBF
DBase                    DBF
DBF                      DBF
Dead Kennedy             Kennedy-333
Dead Kennedys            Kennedy-333
Death to Pascal          Wisconsin
December 24th            December 24th
DEICIDE                  DEICIDE
Den Zuk                  Den Zuk
DENZUKO                  Den Zuk
Devil                    Devil's Dance-941
Devil's Dance            Devil's Dance-941
Devil's Dance-941        Devil's Dance-941
Diamond                  V1024
Diana                    Dark Avenger
DIRVIR                   DIRVIR
Discom                   Discom
Disk Crunching           Icelandic II, Saratoga 1, Saratoga 2, December 24th
Disk Killer              Disk Killer
Disk Ogre                Disk Killer
Do Nothing               Do-Nothing, Do-Nothing 2
Do Nothing 2             Do-Nothing 2
Donald Duck              Stoned 2
Doom 2                   Doom 2
DOS-62                   Vienna-648
DOS-68                   Vienna-648
Durban                   Saturday 14th
EB 21                    PrtSc
Eddie                    Dark Avenger
Eddie 2                  Eddie-651
Eddie 3                  Eddie-651
Eddie-651                Eddie-651
EDV                      EDV
Eight Tunes              Eight Tunes-1971
Eight Tunes-1971         Eight Tunes-1971
European Fish Viruses    Fish 6
Evil Empire              Evil Empire
Evil Empire-B            Evil Empire-B
Fall                     1701, 1704
Falling Letters Boot     Falling Letters Boot
Falling Tears            1701, 1704
Father Christmas         Vienna-Choinka
Fellowship               Fellowship
FILLER                   FILLER
First Austrian           Vienna-648
Fish                     Fish 6
Fish 6                   Fish 6
FLASH                    FLASH
Flip                     Flip-2343, Flip-2153
Flip-2153                Flip-2153
Flip-2343                Flip-2343
FORM                     FORM
Form Boot                FORM
FORM-Virus               FORM
Friday 13th              Friday the 13th COM
Friday the 13th          Friday the 13th COM
Friday the 13th COM      Friday the 13th COM
Frodo                    4096
Fu Manchu                2086
Fu Manchu - Version A    2086
Fumble                   Fumble-867
Fumble-867               Fumble-867
Ghost                    Vienna-Ghost
Ghost Boot               Vienna-Ghost
Ghost COM                Vienna-Ghost
Ghost Version of DOS 62  Vienna-Ghost
Ghostballs               Vienna-Ghost
Guppy                    Guppy
Hacker                   Ohio
Halloechen               Halloechen
Happy Birthday Joshi     Joshi
Happy Day                Happy Day
Hawaii                   Stoned
Hebrew University        1813
Hello (1A)               Halloechen
Hemp                     Stoned
Herbst                   1701, 1704
Holland                  Sylvia
Holland Girl             Sylvia
Iceland                  Iceland II, Saratoga 1, Saratoga 2, December 24th
Iceland I                Saratoga 2
Iceland II               Iceland II
Icelandic                Iceland II, Saratoga 1, Saratoga 2, December 24th
Icelandic II             Iceland II
Icelandic III            December 24th
Icelandic-3              December 24th
IDF                      4096
Invader                  Plastique-Invader
Ira                      Vienna-Ira
Israeli                  1813
Israeli Boot             Falling Letters Boot
Israeli Defense Forces   4096
Italian                  Bouncing Ball
ITAVIR                   ITAVIR
Japanese Christmas       Japanese Christmas
Japanese-Xmas            Japanese Christmas
Jeff                     Jeff
Jeru-Discom              1813-Discom
Jeru.Swiss               1813-Swiss
Jeru-Sunday              Sunday
Jeru-Sunday2             Sunday 2
Jerusalem                1813
Jerusalem Strain B       1813, 1813-ANARKIA, 1813-not-13, 1813-Swiss
Jerusalem-B              1813
Jerusalem-E              sURIV 3.00
Jerusalem.Not13          1813-not-13
JOJO                     1701-Jojo
Joshi                    Joshi
July 13th                July 13th
June 16th                June 16th
June-the-16th            June 16th
JUNE16                   June 16th
JV                       1813
Kamikaze                 Kamikaze
Kennedy                  Kennedy-333
Kennedy-163              Kennedy-163
Kennedy-333              Kennedy-333
KeyPress                 KeyPress
KHETAPUNK                1392
Klaeren                  Klaeren
Korea                    LBC
Kukac-2                  Turbo-Kukac
LBC                      LBC
LBC Boot                 LBC
Lehigh                   Lehigh I
Lehigh I                 Lehigh I
Leprosy                  Leprosy
Leprosy 1.00             Leprosy
Leprosy-B                Leprosy-B
Liberty                  Liberty
Lisbon                   Vienna-Lisbon
Live After Death         V800
MACROSOFT                SYSLOCK
Mardi Bros               Mardi Bros
Marijuana                Stoned
Marti Brothers           Mardi Bros
Mendoza                  1813         (Not differentiated by VIRSCAN)
Merritt                  Yale
Mexican                  Devil's Dance
MG1                      MG1
MG3                      MG3
Miami                    Friday the 13th COM
Michelangelo             Michelangelo
MICROBE                  MICROBE
Mirror                   Mirror
Mistake                  Fumble-867, Typo Boot
MIX1                     MIX1, MIX1-B
MIX1-B                   MIX1-B
MIX1/Icelandic           Saratoga 1, Saratoga 2, Iceland II
Mixer1                   MIX1
Monxla                   Vienna-Monxla
Morbus Waiblingen        1813
Mother Fish              Whale
Munich                   Friday the 13th COM
Murphy                   Murphy 1
Murphy 1                 Murphy 1
Murphy 2                 Murphy 2
Murphy-1                 Murphy 1
Murphy-2                 Murphy 2
Music                    OROPAX
MusicBug                 MusicBug
Musician                 OROPAX
MYSTIK                   Liberty
New Zealand              Stoned
Nobock                   Nobock
Noint                    Noint
Nomenclature             Nomenklatura
Nomenklatura             Nomenklatura
Number of the Beast      V512
Ogre                     Disk Killer
Ohio                     Ohio
Ohio0                    Ohio0
Old Yankee-1             Yankee-1961
Omicron                  Flip-2343, Flip-2153
OMICRON Psychoblaster    Flip-2343, Flip-2153
Ontario                  Ontario
One-In-Eight             Vienna-648
OROPAX                   OROPAX
Pakistani                Brain
Pakistani Brain          Brain
Palette                  1536
Payday                   1813-not-13
Peking                   Yale
Pentagon                 Pentagon
Perfume                  Perfume-765
Perfume-765              Perfume-765
Ping Pong-B              Bouncing Ball
Ping-Pong                Bouncing Ball
Pixel                    Pixel-847
Pixel-277                Pixel-277
Pixel-299                Pixel-299
Pixel-345                Pixel-345
Pixel-740                Pixel-740
Pixel-847                Pixel-847
Pixel-852                Pixel-852
Plastique 4.51           Plastique 4.51
Plastique 5.21           Plastique 5.21
Plastique Boot           Plastique-Invader
Plastique-2576           Plastique-2576
Plastique-2900           Plastique-2900
Plastique-Invader        Plastique-Invader
PLO                      1813
POLIMER                  POLIMER
Polimer-2                POLIMER
Pretoria                 JUNE16
Print Screen             PrtSc
PrtSc                    PrtSc
Prudents                 Prudents-1210
Prudents-1210            Prudents-1210
PSQR                     PSQR-1720
PSQR-1720                PSQR-1720
Raubkopi                 Raubkopi
Red X                    Ambulance
RPVS                     453
Russian                  1813
SADAM                    SADAM
San Diego                Stoned
Saratoga                 Iceland II, Saratoga 1, Saratoga 2, December 24th
Saratoga 1               Saratoga 1
Saratoga 2               Saratoga 2
Saratoga 3               Iceland II
SAT14                    Saturday 14th
Saturday 14th            Saturday 14th
Saturday-the-14th        Saturday 14th
Scott's Valley           Slow-2131
Search                   Den Zuk
Second Austrian          1704
Seoul                    Yale
Shake                    Shake
Shoe                     Brain-Shoe
Shoe_Virus               Brain-Shoe
Slow                     Slow
Slow-2131                Slow-2131
Smiley Worm              Smiley Worm
Smithsonian              Stoned
Solano                   Solano
South African            Friday the 13th COM
Sparse                   Sparse
STAF                     STAF
Stardot-600              Stardot-600
Stardot-789              Stardot-789
Stardot-801              Stardot-801
Stealth                  4096, EDV, Fish 6, Joshi, Murphy 1
Stoned                   Stoned
Stoned 2                 Stoned 2
Stoned-Alberta           Stoned-Alberta
Stoned-ZAPPED            Stoned-ZAPPED
Stupid                   Do-Nothing
Stupid-2                 Do-Nothing 2
sUMsDos                  1813
Sunday                   Sunday,Sunday 2
Sunday 2                 Sunday 2
Suomi                    Suomi
SuperHacker              Talentless Jerk
sURIV 1.01               April 1st COM
sURIV 2.01               April 1st EXE
sURIV 3.00               sURIV 3.00
Suriv A                  April 1st COM, April 1st EXE
Suriv B                  sURIV 3.0
SURIV01                  April 1st COM
SURIV02                  April 1st EXE
SURIV03                  sURIV 3.00
SVIR                     SVIR
Swap                     Falling Letters Boot
Swedish Disaster         Swedish Disaster
Sylvia                   Sylvia
SYSLOCK                  SYSLOCK
System                   Iceland II
T1                       1813               (Not differentiated by VIRSCAN)
Taiwan 1                 Taiwan
Taiwan                   Taiwan, Taiwan 2
Taiwan 2                 Taiwan 2
Taiwan 3                 Plastique-2900
Taiwan 4                 Plastique-2576
Talentless Jerk          Talentless Jerk
Telecom                  Telecom
TELEFONICA               Campana
Ten Bytes                9800:0000
TenBytes                 9800:0000
Tequila                  Tequila
Thanksgiving             1253
Tiny-134                 Tiny-134
Tiny-138                 Tiny-138
Tiny-143                 Tiny-143
Tiny-154                 Tiny-154
Tiny-156                 Tiny-156
Tiny-158                 Tiny-158
Tiny-159                 Tiny-159
Tiny-160                 Tiny-160
Tiny-163                 Kennedy-163
Tiny-167                 Tiny-167
Tiny-198                 Tiny-198
Toothless                W13-A, W13-B
TP06VIR                  TP06VIR
TP16VIR                  TP16VIR
TP23VIR                  TP23VIR
TP24VIR                  TP24VIR
TP25VIR                  TP25VIR
TP33VIR                  TP33VIR
TP34VIR                  TP34VIR
TP39VIR                  Yankee Doodle-2772
TP41VIR                  TP41VIR
TP42VIR                  TP42VIR
TP44VIR                  Yankee Doodle-2885
TP45VIR                  TP45VIR
TP46VIR                  TP46VIR
Traceback                Traceback-2930, Traceback-3066
Traceback II             Traceback-2930
Traceback-2930           Traceback-2930
Traceback-3066           Traceback-3066
TUQ                      453
Turbo-448                Turbo-448
Turbo-Kukac              Turbo-Kukak
Turin                    Bouncing Ball
Typo                     Fumble-867, Typo Boot
Typo Boot                Typo Boot
Typo COM                 Fumble-867
UIUC                     Brain-Ashar
UIUC                     Brain-Shoe
Unesco                   Vienna-648
V-277                    Pixel-277
V-299                    Pixel-299
V-345                    Pixel-345
V-Alert                  9800:0000
V1024                    V1024
V1277                    Murphy 1
V1539                    XA1
V2000                    V2000
V2100                    Dark Avenger-2100
V2P1                     Washburn-1260, Washburn-V2P2 or Washburn-Casper
V2P2                     Washburn-1260, Washburn-V2P2 or Washburn-Casper
V512                     V512
V512-B                   V512-B
V512-C                   V512-C
V512-D                   V512-D
V651                     Eddie-651
V800                     V800
VACSINA                  VACSINA
Vacsina-39 virus         Yankee Doodle-2772
Vacsina-44 virus         Yankee Doodle-2885
VBASIC                   5120
VCOMM                    637
VCS 1.0                  VCS 1.0
Venezuelan               Den Zuk
Vera Cruz                Bouncing Ball
VHP-348                  VHP-348
VHP-353                  VHP-353
VHP-367                  VHP-367
VHP-435                  VHP-435
VHP-623                  VHP-623
VHP-627                  VHP-627
Victor                   Victor
Vienna                   Vienna-648
Vienna (DOS62) Version B Vienna-648
Vienna-535               Vienna-535
Vienna-646               Vienna-646
Vienna-648               Vienna-648
Vienna-Choinka           Vienna-Choinka
Vienna-Ghost             Vienna-Ghost
Vienna-Ira               Vienna-Ira
Vienna-Lisbon            Vienna-Lisbon
Vienna-Monxla            Vienna-Monxla
Vienna-Viola             Vienna-Viola
Vienna-Viola B4          Vienna-Viola B4
Viola                    Vienna-Viola
Viola B4                 Vienna-Viola B4
Violator                 Vienna-Viola
VIR13J                   July 13th
VIRDEM                   VIRDEM
VIRDEM 2                 VIRDEM 2
VIRUS-90                 VIRUS-90
Virus-B                  Friday the 13th COM
VP                       VP
Vriest                   Vriest
W13                      W13-A, W13-B
W13-A                    W13-A
W13-B                    W13-B
Washburn-Casper          Washburn-1260, Washburn-V2P2 or Washburn-Casper
Weinacht                 XA1
Westwood                 1813-Westwood
Whale                    Whale
Whale-B                  Whale-B
Wisconsin                Wisconsin
XA1                      XA1
XA1 (1539) Christmas     XA1
Yale                     Yale
Yale Boot                Yale
Yankee 2                 Yankee-1961
Yankee Doodle            Yankee Doodle-2885, Yankee Doodle-2772
Yankee Doodle-2772       Yankee Doodle-2772
Yankee Doodle-2885       Yankee Doodle-2885
Yankee-1961              Yankee-1961
Yaunch                   Yaunch
Z the Whale              Whale
ZAPPER                   Stoned-ZAPPED
ZBug                     1536
Zero Bug                 1536
Zero Hunt                Zero Hunt
Zero Hunt-B              Zero Hunt-B
Zerotime                 SLOW
ZK-900                   ZK-900