This is general information which applies to ALL CompuCom modems.
Other files may provide additional detail on specific modem models.
         
         
         COMMAND SUMMARY
         
         
         AT        ATTENTION COMMAND
         A/        REPEAT COMMAND
         A         ANSWER MODE COMMAND
         B/B0      SELECT CCITT V.22 IN 1200 BPS
         B1        SELECT BELL 212A
         Dn        DIAL COMMAND (n = DIAL STRING, 0-9, *, #, !, W, R, AND,
         E         DISABLE ECHO
         E1        ENABLE ECHO 
         H         ON HOOK (HANG UP)
         H1        OFF HOOK
         I/I0      IDENTIFY
         I1        DISPLAY 000
         I2        DISPLAY OK
         I3        DISPLAY MESSAGE PROGRAM ROM
         L/L0      LOW VOLUME
         L1        LOW VOLUME
         L2        MEDIUM VOLUME
         L3        MAXIMUM SPEAKER VOLUME
         M/M0      DISABLE SPEAKER
         M1        SPEAKER ON UNTIL CARRIER
         M2        SPEAKER ALWAYS ON
         M3        DISABLE SPEAKER WHEN DIALING OR CARRIER
         O         GO ON LINE
         O1        RETRAIN (2400 BPS MODE ONLY)
         Q/Q0      ENABLE RESULT CODES
         Q1        DISABLE RESULT CODES
         Sn=X      S REGISTER WRITE (n = VALID S REG, X = ALLOWED VALUE SEE        
                   &F COMMAND)
         Sn?       READ SPECIFIED S REGISTER (n = ANY VALID S REGISTER)
         V0        SELECT DIGIT RESULT CODE
         V1        SELECT WORD RESULT CODE
         X0        BLIND DIAL, DISPLAY "CONNECT"
         X1        BLIND DIAL, DISPLAY "CONNECT 1200/2400"
         X2        DETECT DIAL TONE, DISPLAY "CONNECT 1200/2400"
         X3        DETECT BUSY TONE, DISPLAY "CONNECT 1200/2400"
         X4        DIAL AND BUSY TONE DETECT, DISPLAY "CONNECT 1200/2400"
         Y0        DISABLE LONG SPACE DISCONNECT
         Y1        ENABLE LONG SPACE DISCONNECT 
         Z         SOFTWARE RESET
         +++       ESCAPE CODE (GO TO COMMAND MODE IF ON LINE)
         &C0       DCD ALWAYS ON 
         &C1       DCD FOLLOWS REMOTE CARRIER STATUS
         &D0       IGNORE DTR
         &D1       GO TO COMMAND WHEN DTR ON TO OFF
         &D2       HANGUP AND GO TO COMMAND WHEN DTR ON TO OFF
         &D3       POWER UP RESET WHEN DTR ON TO OFF
         &F        FETCH FACTORY CONFIGURATION for S REGESTERS
         &G0       NO GUARD TONE 
         &G1       550 HZ GUARD TONE
         &G2       1800 HZ GUARD TONE 
         &J0       SELECT RJ-11/RJ-41S/RJ-45S
         &J1       SELECT RJ-12/RJ-13
         &M0       SELECT ASYNCHRONOUS MODE
         &P0       MAKE BREAK RATIO FOR US (40/60)
         &P1       MAKE BREAK RATIO FOR FOREIGN STANDARD (33/66)
         &R0       CTS TRACKS RTS
         &R1       CTS ON WHEN MODEM READY IN DATA MODE
         &S0       DSR ALWAYS ON
         &S1       DSR FOLLOWS RE232 SPECIFICATION
         &T0       STOP TEST 
         &T1       LOCAL ALB TEST
         &T3       LOCAL DLB
         &T        ENABLE DLB REQUEST
         &T5       DISABLE DLB REQUEST
         &T6       REMOTE DLB
         &T7       REMOTE DLB AND SELF TEST
         &T8       LOCAL ALB AND SELF TEST
         &V        VIEW PROFILE
         
         
         S-REG   ADDRESS  DEFAULT  VALID RANGE   DESCRIPTION
         
         S0      228      0        0-255         RING TO ANSWER ON
         S1      229      0        0-255         RING COUNT
         S2      230      43       0-127         ESCAPE CODE CHARACTER
         S3      231      13       0-127         CR CHARACTER
         S4      232      10       0-127         LF CHARACTER
         S5      233      8        0-127         BS CHARACTER
         S6      234      2        0-255         WAIT FOR DIAL TONE
         S7      235      30       1-99          WAIT FOR DATA CARRIER
         S8      236      2        0-255         PAUSE TIME FOR COMMA
         S9      237      6        1-255(.1SEC)  CARRIER DET RESP. TIME
         S10     238      14       1-255(.1SEC)  LOST CARRIER TO HANG UP        
                                                    DELAY
         S11     239                             TOUCH TONE DURATION
         S12     240      50       0-255         ESCAPE CODE GUARD TIME
                                    (1/50SEC)
         S13     241                             NOT USED
         S14     242      AAH                    BIT MAPPED OPTION REG
         S15     243                             NOT USED
         S16     244      0                      MODEM TEST OPTIONS
         S17     245                             NOT USED
         S18     246      0        0-255         TEST TIMER
         S19     247                             NOT USED
         S20     248                             NOT USED
         S21     249      0                      BIT MAPPED OPTIONS REG
         S22     250      76                     BIT MAPPED OPTIONS REG 
         S23     251      7                      BIT MAPPED OPTIONS REG
         S24     252                             NOT USED
         S25     253      5        0-255(.01SEC) DELAY TO DTR (SYNC ONLY)
         S26     254      1        0-255(.01SEC) RTS TO CTS DELAY (HALF                   
                                                    DUP)
         S27     255      40H                    BIT MAPPED OPTION REG
         
         
                                          2
         
                                   HOST INTERFACE
         
         This section describes the way in which the host interfaces to the
         modem.  The  modem communicates to the host in either the  command
         mode  or the data mode. The Model 2400 controls the switching  be-
         tween  the  two modes. The staus of the modem is communicated  via
         result codes.
         
         COMMUNICATION MODES
         
         The  modem communicates to the host in one of two possible  modes:
         the  command  mode or the data mode. Upon powerup or after  reset,
         the  modem  performs a selftest. Immediately following this  test,
         the  modem  enters the command mode and configures itself  in  the
         default  configuration. The modem then enters the autobaud routine
         and waits for the attention code 'AT' from the host. 
         
         4.1.1  Command Mode
         
         In  the command mode, the user communicates with the modem via the
         host  computer.  This  mode  is used for  modem  configuration  or
         dialing.  The modem executes local commands from the host computer
         and  returns  the  result codes. After the autodialing  and  modem
         handshake sequences are completed, the modem enters the data mode,
         unless otherwise specified by the dial subcommand.
         
         4.1.2  Data Mode 
         
         In  the data mode, the modem receives characters from the host and
         processes  the data before transmitting it to the telephone  line.
         The  modem  also checks the data from the host for an escape  code
         sequence. It does not execute any local commands in the data mode.
         The modem returns to the command mode only when it receives an es-
         cape code sequence from the host, or one of the data call termina-
         tion procedures described in Section  6.5 occurs.
         
         4.2  MODE CONTROL 
         
         Upon  powerup,  the Model 2400 modem is in the command  mode.  The
         modem  can enter the data mode while connected to another modem or
         when  using diagnostics. The escape code is used to return to  the
         command  mode.  To return back to the data mode, the ATO  (online)
         command is used.
         
         The  escape  code forces the modem to return to the  command  mode
         from  the data (online) mode. The escape code character and escape
         code guard time are defined by the values set in register S12. The
         escape  code  guard time is defined as the time delay between  the
         last  character  of  escape  code transcitted and  the  next  data
         character. The default guard time is defined as the time delay be-
         tween  the last character of escape code transmitted and the  next
         data  character.  The  default guard time is one  second  and  the
         default  code character is "+". The escape code character must  be
         entered  three  consecutive  times.  To execute  the  escape  code
         (default values), proceed as followe:
                                          3
         
         1)  Type "+++"
         2)  Wait one second before transmitting another command character.
         
         The  modem  returns to the command mode and sends the result  code
         "OK".  The  telephone  line connection is retained or  aborted  as
         defined  by  the value in register S10. The connection is  aborted
         automatically if the carrier signal from the remote modem is lost. 
         
         If  the  modem is forced into the command mode from the data  mode
         using the escape sequence, the ATO (online) command can be used to
         return  to  the  data mode. The modem can be reconfigured  to  the
         default state by executing the software reset ATZ command.
         
         4.3  RESULT CODES
         
         Result  codes  are  the  responses  to  commands  that  have  been
         executed. Result codes may be selected as English words or numeric
         digits.   Word   result   codes  are  followed   by   a   carriage
         return/linefeed  sequence; numeric result codes are followed by  a
         carriage return only. Table 3-1 lists the result codes.
         
         DIGIT     WORD            RESULT
         CODE      CODE
         
         0         OK              Command executed without error.
         
         1         CONNECT         Carrier detected (300 bbs or 1200 bbs if      
                                      X0 is set.)
         2         RING            Phone is ringing (will answer only if    
                                      auto answer is enabled.)
         3         NO CARRIER      Carrier lost or never detected.
         
         4         ERROR           Error in command line, line too long, or 
                                      invalid character format.
         5         CONNECT 1200    Carrier detected at 1200 bbs if X1 set.
         
         6         NO DIALTONE     Displayed if no dialtone is detected        
                                      within 5 seconds and X2 or X4 is set.
         7         BUSY            Displayed when a busy signal is         
                                     detected and Z2 or X4 is set.
         8         NO ANSWER       Displayed when "@" dial modifier is used 
                                      and phone continues to ring.
         10        CONNECT 2400    Carrier detected at 2400 bbs. X1 or X2 
                                      must be set.
         
         4.4  DATA TRANSMISSION RATE
         The  Model  2400  will  transmit  and receive  data  at  the  rate
         specified  by the table below. The transmission rate is determined
         at the time of connection by three facrtors:  the data rate of the
         data  terminal  connected to the Model 2400 modem; the  speed  and
         standard of the remote modem; and whether or not the Model 2400 is
         answering or originating the call.
         
         
                                          4
                                         ANSWERING MODEM
           ORIGINATING                                                     
           MODEL 2400     BELL 103    BELL 212    V.22        V.22 bis
                          300         1200        1200        2400
         
           BELL 300       300         300         300**       300**
         
           BELL 1200      1200*       1200        1200        1200
         
           CCITT 1200     1200*       1200        1200        1200
         
           CCITT 2400     2400*       1200        1200        2400
         
                                         ORIGINATING MODEM
           ANSWERING
           MODEL 2400     BELL 103    BELL 212     V.22        V.22 bis
                          300         1200         1200        2400
         
           BELL 300       300         1200         1200         2400
         
           BELL 1200      300         1200         1200         2400
         
           CCITT 1200     300*        1200         1200         2400
         
           CCITT 2400     300*        1200         1200         2400
         
         *  The connect rate shown results when a Model 2400 calls  another
         Model  2400. The connect rate may differ when a Model 2400 is con-
         necting with a different type of modem.
         
         ** Connection will be made if the answering modem is configured to
         fallback  to  Bell 103. No connection will be made if fallback  is
         set to V.21.
         
         
                                5.  MODEM COMMAND SET

                         See also HAYESCMD.DOC and MNP.DOC files.
         
         Direct  communication  with the modem is performed using the  "AT"
         command  set.  The modem accepts commands from the host when it is
         in the command mode only. To issue a command while the modem is in
         the data mode, it must be placed in the command mode by issuing an
         escape code sequence.
         
                           MODEL 2400 "AT" COMMANDS
         
         COMMAND             DESCRIPTION
         
         AT                  COMMAND LINE PREFIX (ATTENTION CODE);
                             PRECEDES COMMAND LINES EXCEPT +++ (ESCAPE)
                             AND A/ (REPEAT) COMMANDS.
         
         A/                 RE-EXECUTE LAST COMMAND LINE; (A/ IS NOT
                            FOLLOWED BY A CARRIAGE RETURN).
         
         A                  OFF-HOOK IN ANSWER MODE.
                                          5
         
         B                  SELECTS CCITT V.22 OPERATION WHEN 
                            COMMUNICATING AT 1200 BPS.
         
         B1  (Default)      SELECTS BELL 212A OPERATION WHEN
                            COMMUNICATING AT 1200 BPS.
         
         D                  DIAL NUMBER WHICH FOLLOWWD IN THE COMMAND
                            LINE.
         
         E                  MODEM DOES NOT "ECHO" COMMANDS BACK TO
                            TERMINAL.
         
         
         E1  (Default)      MODEM SECHOS COMMANDS BACK TO TERMINAL.
         
         H  (Default)       ON-HOOK (HANG-UP) COMMAND.
         
         H1                 GO OFF-HOOK.
         
         I                  REQUEST PRODUCT IDENTIFICATION CODE.
         
         I1                 PERFORMS CHECKSUM ON FIRMWARE ROM; RETURNS
                            CHECKSUM.
         
         I2                 PERFORMS CHECKSUM ON FIRMWARE ROM; RETURNS
                            OK OR ERROR.
         
         M                  SPEAKER OFF.
         
         M1  (Default)      SPEAKER ON UNTIL CARRIER DETECTED.
         
         M2                 SPEAKER ALWAYS ON.
         
         M3                 SPEAKER ON UNTIL CARRIER DETECTED EXCEPT
                            DURING DIALING.
         
         O                  RETURN TO ON-LINE STATE.
         
         O1                 RETURN TO ON-LINE STATE AND INITIATE RETRAIN.
         
         Q  (Default)       MODEM RETURNS RESULT CODES.
         
         Q1                 MODEM DOES NOT RETURN RESULT CODES.
         
         SRT=N              SET REGISTER R TO VALUE N.
         
         SR?                REQUEST CONTENTS OF REGISTER R.
         
         
         V                  SHORT FORM NUMERIC RESULT CODES.
         
         V1  (Default)      FULL WORD RESULT CODES.
         
         X                  300 BPS COMPATIBILITY MODE; CONNECT RESULT
                                          6
                            CODE ENABLED.
         
         X1                 MODEM BLIND DIALS; ALL CONNECT XXXX RESULT
                            CODES ENABLED; BUSY SIGNAL NOT DETECTED.
         
         
         X2                 MODEM WAITS FOR DIAL TONE BEFORE DIALING;
                            ALL CONNECT XXXX RESULT CODES ENABLED; MODEM
                            SEND BUSY RESULT CODE IF BUSY DETECTED.
         
         X3                 MODEM BLIND DIALS; ALL CONNECT XXXX RESULT
                            CODES ENABLED; MODEM SENDS BUSY CODE IF BUSY
                            DETECTED.
         
         X4  (Default)      MODEM WAITS FOR DIAL TONE BEFORE DIALING;
                            ALL CONNECT XXXX RESULT CODES ENABLED; BUSY
                            SIGNAL DETECTED.
         
         Z                  LOAD STORED CONFIGURATION PROFILE.
         
         &C                 DCD ALWAYS ON.
         
         &C1  (Default)     DCD ON INDICATES PRESENCE OF DATA CARRIER.
         
         &D   (Default)     MODEM IGNORES DTR.
         
         &D1                MODEM ASSUMES COMMAND STATE WHEN ON-TO-OFF
                            TRANSITION DETECTED ON DTR.
         
         &D2                MODEM HANGS UP & ASSUMES COMMAND STATE.
                            AUTO ANSWER NOT DISABLED UNLESS EXTERNALLY
                            IMPLEMENTED BY (RI- # DTR-)= A6-.
         
         &D3                MODEM ASSUMES INITIALIZATION STATE UPON
                            DETECTING AN ON-TO-OFF TRANSITION ON DTR.
         
         &F                 LOAD FACTORY CONFIGURATION PROFILE.
         
         &P  (Default)      PULSE DIAL MAKE/BREAK RATIO = 39/61 (UK/HK).
         
         &P1                PULSE DIAL MAKE/BREAK RATIO = 33/67 (UK/HK).
         
         &S                 DSR ALWAYS ON.
         
         &S1                DSR OPERATES IN ACCORDANCE WITH EIA RS-232-C
                            SPEC.
         
         &T                 TERMINATE TEST PROGRESS.
         
         &T1                INITIATE LOCAL ANALOG LOOPBACK TEST.
         
         &T8                INITIATE LOCAL ANALOG LOOPBACK WITH SELF TEST.
         
         &Z                 STORE TELEPHONE NUMBER.
         
                                          7
         
                         MODEL 2400 "AT" COMMAND DEFINITIONS
         
         A     Go off hook and answer phone immediately. The Model 2400 
               immediately goes off hook, transmits the answer tone and 
               waits for a carrier from the remote mode.
               Commands entered after the A command are ignored.
         
         A/    Repeat previous command. The last command executed by the 
               Model 2400 will execute again. This command does not require
               the "AT" prefix or <cr> termination.
         
         Bn    Bell/CCITT mode select.
         
               B0 - Selects CCITT V. 22 operation at 1200 bps.
               B1 - Selects BELL212A operation at 1200 bps (Default).
         
               Most 1200 bps modems in the United States operate using the 
               BELL212A specification. In order to communicate with a modem
               conforming to the international CCITT V.22 standard, issue
               the B0 command before dialing.
         
         Dn    Dial the number immediately following this command where
               n = digits 0 through 9 together with the dial modifiers 
               listed below.
         
               The Model 2400 will dial the number specified in the manner 
               determined by the dial modifiers. The dial modifiers may 
               appear anywhere within the dial string with the exception
               of the ; modifier which must appear at the end of the
               string.
         
               Dial Modifiers:  P  Pulse dial
                                T  Tone dial
                                R  Originate call in answer mode
                                W  Wait for dial tone before dialing
                                ,  Pause before dialing next digit
                                ;  Return to command mode after dialing
                                @  Wait for quiet answer before dialing
                                !  Flash-hook
                                S  Dial the number stores in RAM
         
               EXAMPLE:  ATDP9WT713,SS;
         
               In this example the Model 2400 pulse dials a 9 digit, waits
               for a dial tone, them tome dials the digits 713. Next, the
               modem pauses the length of time specified in register S8. It 
               them dials the number stored in the Model 2400 controller's
               RAM which can be up to 32 digits in length. Finally, the
               modem returns to the command mode after the final digit has
               been dialed.
         
               The P modifier causes the modem to pulse or rotary dial at a
               fixed rate of 10 pulses per second. (The make/break ratio   
               for pulse dialing is determined by the &P command.)
                                          8
         
         DIAL MODIFIERS
         
         P                   PULSE DIAL
         
         T                   TONE DIAL
         
         ,                   PAUSE
         
         !                   FLASH
         
         @                   WAIT FOR SILENCE
         
         W                   WAIT FOR SECOND DIAL TONE
         
         ;                   RETURN TO COMMAND STATE AFTER DIALING
         
         R                   ORIGINATE CALL IN ANSWER MODE
         
         D                   DIAL STORED NUMBER
         
         
                                     6.  DIALING
         
         The  Model 2400 originates a call by dialing a remote modem, using
         either  pulse or DTMF (dual-tone multifrequency) dialing depending
         on  the dial subcommand issued by the user. The tandem mode can be
         used  in call progress dialing to switch between pulse and tone in
         the middle of a dial sequence.
         
         Dialing can be performed in one of two possible modes:
         
         1)  Call  progress mode where the modem monitors the  progress  of
         the call, or
         2)  Blind mode where the modem does not monitor the call  progress
         signal after dialing is completed.
         
         When  a  dial  command  is entered, the  modem  places  itself  in
         originate  mode  unless  reverse  mode dialing  is  specified.  If
         reverse  mode dialing is specified, the modem reconfigures  itself
         in the answer mode when dialing is completed.
         
         If  call  progress  mode  is enabled, the modem  will  detect  the
         presence  of  a  dial tone before proceeding with  the  dialing  o
         numbers. When call progress mode is disabled, the modem uses blind
         dialing  in  which the numbers are dialed without waiting for  the
         presence  of a dial tone. The modem is also capable of  overriding
         its  dialer,  thus  allowing  manual  dialing  using  an  external
         telephone  handset.  After dialing, the modem waits for an  answer
         tone from the remote modem.
         
         6.1  CALL PROGRESS DIALING
         
         Once  the dialing is entered, the modem places itself off hook and
         looks  for the dial tone indicate signal. It assumes tone  dialing
         (unless pulse dialing is requested) and dials the entered number.
                                          9
         
         If  a "W" is encountered while numbers are being dialed, the modem
         searches  for another dial tone indicate signal before  proceeding
         with  the remainder of the dialing sequence. When the dialing  se-
         quence  is complete, the modem searches for a remote ring  signal.
         If this signal is detected, it them searches for an answer carrier
         tone. The modem waits for an originate carrier tone if the reverse
         mode is selected (see "R" command).
         
         When  the  carrier  tone is detected, the modem is placed  in  the
         originate  mode  and completes the modem handshake  sequence.  The
         modem is then automatically placed in the data mode.
         
         6.2  BLIND DIALING
         
         Blind  dialing is similar to call progress dialng except that  the
         call  progress signals are disabled and ignored by the modem. Once
         offhook,  the  modem  delays  the dialing  sequence  by  the  time
         specified  in status register S5 (wait for dial tone). If a "+" is
         encountered  in the dialing sequence, it is ignored. To wait for a
         second dial tone (for PBX systems), a comma "," (pause subcommand)
         must be inserted between the numbers to be dialed. After the dial-
         ing  sequence is complete, the modem searches for an answer  tone.
         The  remainder  of the sequence is identical to the call  progress
         dialing modem handshake sequence, described in Section 6.1.
         
                                6.3  AUTO ANSWER MODE
         
         When   the  auto-answer  configuration  is  selected,  the   modem
         automatically  answers the phone after "n" rings. The parameter  n
         is  set using the command "Sr=n". The value in status register  S0
         controls  the  number of rings that must occur  before  answering.
         After  the  telephone  is answered, the modem  waits  two  seconds
         (billing  delay) during which the modem sends only an answer  car-
         rier  tone  to the originating modem, and then proceeds  with  the
         call  establishment  handshake  as  specified  by  the  respective
         protocol.  After  the  handshake is completed, the modem  sends  a
         result  code  to  the host (unless disabled) and enters  the  data
         mode.
         
         If the "A" command is used and status register S0 is set to 0, the
         modem answers the phone without wating for a ring.
         
         6.4  DATA CALL TERMINATION
         
         Connection may be teminated by either the host or the remote modem
         in the following ways:
         
         Data  Terminal Ready.....When the Data Terminal Ready (DTR) signal
         goes  low  for more than 50 ms, the modem begins a disconnect  se-
         quence  (except for certain test modes). The modem then returns to
         the command mode.
         
         Carrier  Loss.....If the carrier signal is lost for more than  300
         ms, the modem returns to the command mode. The telephone line con-
                                         10
         nection is automatically broken and the modem placed onhook if the
         command mode is re-entered as a result of a carrier loss.
         
         Abort.....If the carrier signal is not detected within a specified
         time  interval  after  dialing,  the modem goes  onhook  and  then
         returns to the command mode.
         
         6.5  HANDSHAKE PROTOCOL
         
         Modem handshake protocols for Bell 103J, Bell 212A, V.22, and V.22
         bis   are   specified   by   the   respective   Bell   and   CCITT
         recommendations.  After  the handshake sequence is  complete,  the
         modem  automatically enters the data mode. An exception occurs  if
         the modem has been given the command to return to the command mode
         after dialing.
         
         
         
                                         11