A dBASE-compatible B-tree Access Method
                         for QuickBASIC/PDS Programmers



                                  QBXDBF v1.0

                                30-September-91
                              (C)1991 Cornel Huth


                           1  2  3  4  5  6  7  8  9



      --This file has been mechanically reproduced from the DTP source
      of the documentation with manual touchup. Page numbers, table of
      contents, and other facilatators have not been incorporated into
      this reproduction. A printed manual is available.

      --This product is distributed as shareware. The 3 QLBs distributed
      in the shareware release allow you to use QBXDBF in the QuickBASIC
      or QBX/PDS environment. I give you permission to use the QLBs for as
      long as you like without any consideration due. However, to create
      executable programs outside of the QB or QBX environment requires
      that you register this product. See the !ORDER.FRM for details.







     OVERVIEW
      
      QBXDBF is a mid-level file manager for Microsoft QuickBASIC and 
      BASIC 7 Professional Development System compilers. It is based on 
      the B-Tree sorting method and provides fast and efficient database 
      functions using the .DBF industry-standard data file format for the 
      QB/PDS programmer. 
      
      Some features of QBXDBF are:
      
      1) Maintain up to 250 key and data files opened at one time.
      2) Find any key and data record quickly - any key in a million in 
      at most 5 disk accesses.
      3) Forward and reverse sequential inorder access to the data file 
      using just one key file(ISAM).
      4) dBASE III/IV .DBF data file compatible.
      5) Automatic key file balancing.
      6) DOS-compatible file locking network support.
      7) Very fast pack/reindex module. Typically 15,000-50,000 records 
      indexed/minute.  
      
      QBXDBF, which evolved from QBTree (also available for QB/PDS 
      compilers), includes network support, Dbase compatibility, and fast, 
      compact B-Tree indexing all combined in one package and at one low 
      price. Compare this to other packages at $200-$600+. But best of 
      all, QBXDBF was designed specifically for QuickBASIC and PDS 
      compilers. There is no separate TSR to be loaded nor is there a 
      cryptic language interface. You'll find QBXDBF easy to use, just 
      like QuickBASIC, with only a few of the routines needed to start 
      creating database applications. From there, as you gain experience, 
      you'll find that even sophisticated database applications will 
      become easy to design and quick to code.

      





     INSTALLATION
      
      There are 3 libraries distributed with QBXDBF. QBXDBF.LIB is for 
      QuickBASIC compilers, QBXDBFF.LIB and QBXDBFN.LIB are for BASIC 7 
      compilers. Your source code needs to REM $INCLUDE: 'QBXDBF.BI'.
      
      To install for QuickBASIC:  The BASIC interface portion of 
      QBXDBF.LIB was compiled with BC 4.50 (/O) and is intended for use 
      with QuickBASIC 4.xx. To use QBXDBF in the QB environment create a 
      QLB:
           
          C>link /qu QBXDBF.LIB<+other>,qbxdbf.qlb,nul,bqlb45
           
      When you create an EXE file of your program, add QBXDBF.LIB to the 
      library prompt from LINK. If you have a version of QB other than 4.5 
      you should recompile the BASIC source, update the library, and 
      create a QLB:
           
          C>ren BTDBFZ.BAS BTDBF.BAS
          C>ren INDEXDBZ.BAS INDEXDB.BAS
          C>bc BTDBF.BAS /O;
          C>bc INDEXDB.BAS /O;
          C>lib QBXDBF -+BTDBF -+INDEXDB;
          C>link /qu QBXDBF.LIB,qbxdbf.qlb,nul,bqlb4x
           (where x=0 for 4.00, x=1 for 4.00b)
      
      To install for BASIC 7/PDS:  The BASIC interface portion of 
      QBXDBFF.LIB was compiled with BC 7.1 (/O/Fs) and is intended for use 
      with BASIC 7.x and QBX using far-string support. QBXDBFN.LIB (/O/Ot) 
      is intended for use with BASIC 7.x using near-string support. To use 
      QBXDBF in the QBX environment create a QLB:
           
          C>link /qu QBXDBFF.LIB<+other>,qbxdbff.qlb,nul,qbxqlb;
      
      When you create an EXE file of your program, add QBXDBFF.LIB (or 
      QBXDBFN.LIB) to the library prompt from LINK. If you have a version 
      of BASIC other than 7.1 you should recompile the BASIC source, 
      update the libraries, and create a QLB:
           
          C>ren BTDBFZ.BAS BTDBFF.BAS
          C>ren INDEXDBZ.BAS INDEXDBF.BAS
          C>bc BTDBFF.BAS /O/Fs;
          C>bc INDEXDBF.BAS /O/Fs;
          C>lib QBXDBFF -+BTDBFF -+INDEXDBF;

          C>ren BTDBFF.BAS BTDBFN.BAS
          C>ren INDEXDBF.BAS INDEXDBN.BAS
          C>bc BTDBFN.BAS /O/Ot;
          C>bc INDEXDBN.BAS /O/Ot;
          C>lib QBXDBFN -+BTDBFN -+INDEXDBN;

          C>link /qu QBXDBFF.LIB,qbxdbff.qlb,nul,qbxqlb;
      
      Follow these rename/compile/link instructions to the letter unless 
      you are using alternate link library switches such as /FPa, etc..

      





     FUNCTION SUMMARY
      
      All QBXDBF routines are FUNCTIONs and return an integer code which 
      is detailed in APPENDIX D. ERROR CODES. Special note: In many code 
      examples the argument list will contain the variables vseg,voff. You 
      should assume that vseg=VARSEG(datarec) and voff=VARPTR(datarec) 
      eventhough vseg,voff have not been explicitly assigned in the code 
      examples.
      
       1) AddKeyDBF(kyfile,recordno&,vseg,voff)
       2) AddRecordDBF(dbfile,vseg,voff,recordno&)
       3) CloseDataDBF(dbfile)
       4) CloseKeyDBF(kyfile)
       5) CopyDataStrucDBF(dbfile,copyfile$)
       6) CopyKeyStrucDBF(kyfile,copyfile$)
       7) CreateDataDBF(filename$,NoFields,FldList() AS DBFFieldListTYPE)
       8) CreateKeyDBF(filename$,kx$,dbfile)
       9) DeleteRecordDBF(dbfile,recordno&)
      10) ExitDBF()
      11) FlushDataDBF(dbfile,dup)
      12) FlushKeyDBF(kyfile,dup)
      13) FreeDataFileDBF()
      14) FreeKeyFileDBF()
      15) GetCurrKeyDBF(kyfile,Qkey$)
      16) GetDirectDBF(dbfile,recordno&,vseg,voff)
      17) GetEqualDBF(kyfile,dbfile,Qkey$,vseg,voff)
      18) GetFirstDBF(kyfile,dbfile,vseg,voff)
      19) GetGTDBF(kyfile,dbfile,Qkey$,vseg,voff)
      20) GetGTEDBF(kyfile,dbfile,Qkey$,vseg,voff)
      21) GetLastDBF(kyfile,dbfile,vseg,voff)
      22) GetLTDBF(kyfile,dbfile,Qkey$,vseg,voff)
      23) GetLTEDBF(kyfile,dbfile,Qkey$,vseg,voff)
      24) GetNextDBF(kyfile,dbfile,vseg,voff)
      25) GetPositionDBF(kyfile,recordno&)
      26) GetPrevDBF(kyfile,dbfile,Qkey$,vseg,voff)
      27) InitDBF(KeyFiles,DBFfiles,DBFfields)
      28) MKN$(dbfile,FieldNumber,zNum#,errc)
      29) OpenDataDBF(filename$,dbfile,asmode)
      30) OpenKeyDBF(filename$,kyfile,dbfile,asmode)
      31) PackDBF(dbfile,kyfile,packfile$,keyfile$)
      32) ReindexDBF(kyfile,dbfile,NewKeyFile$)
      33) StatDataDBF(dbfile,RecLen,norecs&,bfileno,NoFields,LUdate$,ID)
      34) StatKeyDBF(kyfile,keylen,keys&,bfileno)
      35) UndeleteRecordDBF(dbfile,recordno&)
      36) UpdateRecordDBF(dbfile,recordno&,vseg,voff)
      37) VersionDBF(version$)

      





     AddKeyDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat=AddKeyDBF(kyfile,recordno&,vseg,voff)
      
      PARAMETERS kyfile - INTEGER. Number used as fileno in OpenKeyDBF().
                 recordno& - LONG. Record number that this key is to
                 index, as returned by AddRecordDBF().
                 vseg - INTEGER. Segment address of data record.
                 voff - INTEGER. Offset address of data record.
      
      USE        Automatically construct, and then insert, the key for 
                 the data record located at vseg:voff based on the key 
                 expression, into the key file.
                 
      RULES      The first byte of the key must not begin with an ASCII 0 
                 or 255.
      
      NOTES      See CreateKeyDBF() for specifying the key expression.

                 The recordno& number to use is that which is returned by 
                 the function AddRecordDBF().

                 The vseg:voff values are determined using QB's
                 VARSEG(datarec) and VARPTR(datarec) routines where 
                 datarec is a FIXED-LENGTH data structure, typically a 
                 simple, non-arrayed TYPE-allocated structure. This area 
                 of memory at vseg:voff is used as a transfer buffer to 
                 and from the disk files and your program.

                 This routine inserts a single index entry into the key
                 file. This is ideal for online systems where entries are 
                 made one at a time. For indexing several thousand entries 
                 at a time use ReindexDBF().
      
      RETURN     Errors 201, 219, 221, 222, 224 and DOS. 
      
      EXAMPLE    'This example is a complete, albeit simple, 'program and 
                 is referenced by later function 'descriptions (see next 
                 page).

      

      DEFINT A-Z
      REM $INCLUDE: 'QBXDBF.BI'

      TYPE dbStrucTYPE
      tag AS STRING * 1   'dBASE-required delete tag 
      ID AS STRING * 20   'first field in data record, say, a name
      RK AS STRING * 6    'second field (range "0.00"-"100.00")
      END TYPE
      DIM datarec as dbStrucTYPE  'allocate the record I/O buffer
      datarec.tag = " "           'init tag to not deleted (*=deleted)

      'allocate and assign the two field descriptors
      REDIM FLA(1 TO NoFlds) AS DBFFieldListTYPE 
      FLA(1).FieldName = "IDENTITY" : FLA(2).FieldName = "RANK"
      FLA(1).FieldType = "C"        : FLA(2).FieldType = "N"
      FLA(1).FieldLen = 20          : FLA(2).FieldLen = 6
      FLA(1).FieldDC = 0            : FLA(2).FieldDC = 2

      'assign key expression as first 5 characters of ID field (IDENTITY)
      'assign file names; 'handles'; access-sharing mode; number of fields
      kx$ = "upper(substr(IDENTITY,1,5))"
      dbfile$ = "DATA.DBF" : kyfile$ = "KEY.DEX"
      dbfile = FreeDataFileDBF
      kyfile = FreeKeyFileDBF
      asmode = 2 : NoFlds = 2

      'note that this example does not handle any errors (where stat # 0)
      'init: 1 open key file,1 open data file,2 max fields per record
      'create and open data file, create and open key file
      stat = InitDBF(1,1,NoFlds)
      stat = CreateDataDBF(dbfile$,NoFlds,FLA())
      stat = OpenDataDBF(dbfile$,dbfile,asmode)

      'the data file must be created and opened before creating its key file
      stat = CreateKeyDBF(kyfile$,kx$,dbfile)
      stat = OpenKeyDBF(kyfile$,kyfile,dbfile,asmode)

      'the data base is ready for input; here we just INPUT the data, add the
      'data to the dbfile file, insert the key to kyfile, repeat until done
      'dBASE data format specifies numeric data to be in ASCII form
      DO
         INPUT "ID, RANK"; id$,rank!
         IF LEN(id$) = 0 THEN EXIT DO
         datarec.ID = id$
         datarec.RK = MKN$(dbfile,2,CDBL(rank!),errc)
         stat = AddRecordDBF(dbfile,VARSEG(datarec),VARPTR(datarec),recordno&)
         stat = AddKeyDBF(kyfile,recordno&,VARSEG(datarec),VARPTR(datarec))
      LOOP UNTIL stat

      'all names and ranks have been entered; display them in key
      'order until an error is returned--at the end of file stat=202.
      stat = GetFirstDBF(kyfile,dbfile,VARSEG(datarec),VARPTR(datarec))
      DO UNTIL stat
         PRINT datarec.ID;" ";datarec.RK
         stat = GetNextDBF(kyfile,dbfile,VARSEG(datarec),VARPTR(datarec))
      LOOP
      stat = ExitDBF   'shut down and end program
      END

      





     AddRecordDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = AddRecordDBF(dbfile,vseg,voff,recordno&)
      
      PARAMETERS dbfile - INTEGER. Number used as fileno in OpenDataDBF().
                 vseg - INTEGER. Segment address of data record.
                 voff - INTEGER. Offset address of data record.
                 recordno& - LONG. Returned record number at which QBXDBF
                 put the data record.
      
      USE        Add the data record located at vseg:voff to the data 
                 file, dbfile.
      
      RULES      None.
      
      NOTES      For vseg:voff information see AddKeyDBF().

                 Record add rates of 10,000 records/minute on mid-level 
                 machines is typical and 50,000 per minute on 
                 high-performance machines. See ReindexDBF() for 
                 reindexing rates.
      
      RETURN     Errors 219, 222, and DOS
      
      EXAMPLE    datarec.ID = id$
                 datarec.RK = MKN$(dbfile,2,CDBL(rank!),errc)
                 stat=AddRecordDBF(dbfile,vseg,voff,recordno&)
                 'see the example under AddKeyDBF() for more.

      





     CloseDataDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = CloseDataDBF(dbfile)
      
      PARAMETERS dbfile - INTEGER.  Number used as fileno in OpenDataDBF().
                 
      USE        Write the data header from memory to disk and release 
                 the handle used by dfile. Tell DOS to close the file and 
                 update the directory entry.
                 
      RULES      All QBXDBF files must be closed before ending your 
                 program.
                 
      NOTES      An alternate method of closing QBXDBF files is to use 
                 ExitDBF().

                 See FlushDataDBF().
      
      RETURN     Errors 219, 222, and DOS.
      
      EXAMPLE    'done with data file 0, close it
                 stat = CloseDataDBF(0)

      





     CloseKeyDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = CloseKeyDBF(kyfile)
      
      PARAMETERS kyfile - INTEGER. Number used as fileno in OpenKeyDBF().
      
      USE        Write the key header from memory to disk and release the 
                 handle used by kyfile. Tell DOS to close the file and 
                 update the directory entry.
      
      RULES      All QBXDBF files must be closed before ending your 
                 program.
      
      NOTES      An alternate method of closing QBXDBF files is to use 
                 ExitDBF().

                 See FlushKeyDBF().
      
      RETURN     Errors 219, 222, and DOS.
      
      EXAMPLE    'done with key file 0, close it
                 stat = CloseKeyDBF(0)

      





     CopyDataStrucDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = CopyDataStrucDBF(dbfile,copyfile$)
      
      PARAMETERS dbfile - INTEGER. Number used as fileno in OpenDataDBF().
                 copyfile$ - STRING. Pathname of new data file.
      
      USE        Copy the data header including field descriptors of the 
                 opened file, dbfile, to a new file.
      
      RULES      copyfile$ must not already exist.
      
      NOTES      A typical use for this routine is to extract specified 
                 records out of an existing data file into another file.

                 The file header of the created copyfile$ will indicate
                 an empty file but otherwise will be structurally similar 
                 to dbfile.
      
      RETURN     Errors 219, 222, 230, and DOS.
      
      EXAMPLE    'given the code example in AddKeyDBF()
                 'copy all records with rank >= 90 to ASCORE.DBF (no indexing)
                 stat = CopyDataStrucDBF(dbfile,"ASCORE.DBF")
                 stat = OpenDataDBF(dbfile2,"ASCORE.DBF,asmode)
                 stat = GetFirstDBF(kyfile,dbfile,vseg,voff)
                 DO WHILE stat = 0
                    IF VAL(datarec.RK) >= 90 THEN
                       stat = AddRecordDBF(dbfile2,vseg,voff,recno&)
                       'could add key here if index wanted
                    ENDIF
                    stat = GetNextDBF(kyfile,dbfile,vseg,voff)
                 LOOP

      





     CopyKeyStrucDBF
      
      TYPE       FUNCTION

      SYNTAX     stat = CopyKeyStrucDBF(kyfile,copyfile$)
      
      PARAMETERS kyfile - INTEGER. Number used as fileno in OpenKeyDBF().
                 copyfile$ - STRING. Pathname of new key file.
      
      USE        Copy the key header of the opened file, kyfile, to a new 
                 file.

      RULES      copyfile$ must not already exist.
      
      NOTES      This routine is typically used with CopyDataStrucDBF() 
                 where an index of an extracted file is needed.

                 The file header of the created copyfile$ will indicate
                 an empty file but otherwise will be structurally similar 
                 to kyfile.
                 
      RETURN     Errors 219, 222, 230, and DOS.
                 
      EXAMPLE    'given the code example in AddKeyDBF()
                 'copy all records with rank >= 90
                 'to ASCORE.DBF (WITH indexing)
                 stat = CopyDataStrucDBF(dbfile,"ASCORE.DBF")
                 stat = OpenDataDBF("ASCORE.DBF,dbfile2,asmode)
                 stat = CopyKeyStrucDBF(kyfile,"ASCORE.DEX")
                 stat = OpenKeyDBF("ASCORE.DEX",kyfile2,dbfile2,asmode)
                 stat = GetFirstDBF(kyfile,dbfile,vseg,voff)
                 DO WHILE stat = 0
                    IF VAL(datarec.RK) >= 90 THEN
                       stat = AddRecordDBF(dbfile2,vseg,voff,recno&)
                       stat = AddKeyDBF(kyfile2,recno&,vseg,voff)
                    ENDIF
                    stat = GetNextDBF(kyfile,dbfile,vseg,voff)
                 LOOP

      





     CreateDataDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = CreateDataDBF(filename$,NoFields, 
                         FieldList() AS DBFFieldListTYPE)
                 
      PARAMETERS filename$ - STRING. Pathname of data file to create.
                 NoFields - INTEGER. Number of fields in the data record,
                 excluding the delete tag, for this data file.
                 FieldList() - ARRAY of DBFFieldListTYPE.Field 
                 descriptors of data record. DBFFieldListTYPE is defined 
                 in the QBXDBF.BI include file.
      
      USE        Create a new data file with the given number of fields, 
                 as described by the FieldList() array. This does not 
                 leave the file open - you must OpenDataDBF() to use it.
      
      RULES      filename$ must be <= 64 characters.
                 NoFields must be <= the number of fields allocated in 
                 InitDBF() function.
      
      NOTES      filename$ maximum length can be changed, see the BASIC 
                 source file for information on doing this.
                 
      RETURN     Errors 220, 230, 233, and DOS.
      
      EXAMPLE    REDIM FLA(1 TO NoFlds) AS DBFFieldListTYPE 
                 FLA(1).FieldName = "IDENTITY"
                 FLA(2).FieldName = "RANK"
                 FLA(1).FieldType = "C"
                 FLA(2).FieldType = "N"
                 FLA(1).FieldLen = 20
                 FLA(2).FieldLen = 6
                 FLA(1).FieldDC = 0
                 FLA(2).FieldDC = 2
                 stat = CreateDataDBF(dbfile$,NoFlds,FLA())
                 'see the example under AddKeyDBF() for more.

      





     CreateKeyDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = CreateKeyDBF(filename$,kx$,dbfile)
      
      PARAMETERS filename$ - STRING.   Pathname of key file to create.
                 kx$ - STRING.   Key expression.
                 dbfile - INTEGER. File number of the opened data file
                 that this key file is to index.
      
      USE        Create a new key file and store the key expression, kx$, 
                 in the key file header. This does not leave the file open 
                 - you must OpenKeyDBF() to use it.
      
      RULES      filename$ must be <= 64 characters.
                 kx$ must be <= 104 characters and may include the 
                 following functions and operators:
                 UPPER(), SUBSTR(), +, =
                  
                 All variables within the key expression must be a 
                 FieldName as defined in the dbfile FLA() descriptors.
      
      NOTES      UPPER() causes all letters within the scope of UPPER() 
                 to be interpreted as upper-case. This only affects the 
                 key data.

                 SUBSTR() operates like the BASIC function MID$ returning
                 a portion of a given CHARACTER field. Both starting and 
                 ending positions in the field must be specified.

                 All functions operate on a single variable only. These 
                 are examples of valid key expressions for the example 
                 given in AddKeyDBF():

                 kx$ = upper(ID)
                 kx$ = upper(substr(ID,1,5))+upper(substr(ID,16,55D))
                 
                 This is not valid:
                 kx$ = upper(substr(ID,1,5)+substr(ID,16,5))
                 
                 filename$ maximum length can be changed, see the BASIC 
                 source file for information on doing this.
      
      RETURN     Errors 221, 230, 233, and DOS.
      
      EXAMPLE    See the code example for AddKeyDBF()

      





     DeleteRecordDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = DeleteRecordDBF(dbfile,recordno&)
      
      PARAMETERS dbfile - INTEGER. Number used as fileno in OpenDataDBF().
                 recordno& - LONG. Number of record to delete.
      
      USE        Mark a record as deleted by changing the delete tag to 
                 ASCII 42.
      
      RULES      None.
      
      NOTES      See GetPositionDBF() for information on determining 
                 recordno&.

                 Dbase file managers do not physically remove or reuse 
                 records that have been deleted. Instead, a delete tag is 
                 changed from ASCII 32 (space) to ASCII 42 (*). Any key 
                 file remains unaltered in any case. It is up to your 
                 program's logic to handle 'deleted' records.

                 The QBXDBF routine PackDBF() will physically remove any
                 records marked as deleted.
      
      RETURN     Errors 219, 222, 224, and DOS.
      
      EXAMPLE    stat = GetNextDBF(kyfile,dbfile,vseg,voff)
                 IF LEFT$(datarec.ID,4) = "DONE" THEN
                    stat = GetPositionDBF(kyfile,recordno&)
                    stat = DeleteRecordDBF(dbfile,recordno&)

      





     ExitDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = ExitDBF
      
      PARAMETERS None.
      
      USE        Close all QBXDBF files and release the RAM used by the 
                 buffers. Use is optional.
      
      RULES      None.
      
      NOTES      Once ExitDBF() is called you must InitDBF() before using 
                 any other QBXDBF function. This is the only way you can 
                 release the RAM used by the data buffers other than 
                 exiting your program.
      
      RETURN     Error 233.
      
      EXAMPLE    PRINT "done."
                 nul = ExitDBF
                 END

      





     FlushDataDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = FlushDataDBF(dfile,dup)
      
      PARAMETERS dfile - INTEGER. Number used as fileno in OpenDataDBF().
                 dup - INTEGER. Non-zero to force a directory update.
      
      USE        Flush the data file by writing the data file header in 
                 RAM to the data file header on disk. If dup is non-zero 
                 then also update the directory entry. 
      
      RULES      If the file is on a network device set dup=0.
      
      NOTES      If DOS 3.3+ is detected, the header is written as above 
                 but the directory information is updated using the DOS 
                 commit function (func 68h), regardless the value of dup. 
                 When programming for network environments, always use 
                 dup=0. 

                 Flushing buffers should be done whenever processing can 
                 handle the delay. Once a file has been flushed (and no 
                 further changes have been made), a power-outage can bring 
                 your system down with no ill-effects to the QBXDBF file - 
                 all will be intact. Closing and then reopening the file 
                 will have the same effect as this routine but will incur 
                 a much higher overhead.
      
      RETURN     Errors 219, 222, 225, and DOS.
      
      EXAMPLE    IF IsOnNetwork THEN dup = 0 ELSE dup = -1
                 stat = FlushDataDBF(dfile,dup)

      





     FlushKeyDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = FlushKeyDBF(kfile,dup)
      
      PARAMETERS kfile - INTEGER. Number used as fileno in OpenKeyDBF().
                 dup - INTEGER. Non-zero to force a directory update.
      
      USE        Flush the key file by writing the key file header in RAM 
                 to the key file header on disk. If dup is non-zero then 
                 also update the directory entry. 
      
      RULES      If the file is on a network device set dup=0.
      
      NOTES      If DOS 3.3+ is detected, the header is written as above 
                 but the directory information is updated using the DOS 
                 commit function (func 68h), regardless the value of dup. 
                 When programming for network environments, always use 
                 dup=0. 
                 Flushing buffers should be done whenever processing can 
                 handle the delay. Once a file has been flushed (and no 
                 further changes have been made), a power-outage can bring 
                 your system down with no ill-effects to the QBXDBF file - 
                 all will be intact. Closing and then reopening the file 
                 will have the same effect as this routine but will incur 
                 a much higher overhead.
      
      RETURN     Errors 219, 222, 225, and DOS.
      
      EXAMPLE    IF IsOnNetwork THEN dup = 0 ELSE dup = -1
                 stat = FlushKeyDBF(kfile,dup)

      





     FreeDataFileDBF
      
      TYPE       FUNCTION
      
      SYNTAX     dbfile = FreeDataFileDBF
      
      PARAMETERS None.
      
      USE        Obtain a free QBXDBF data file handle.
      
      RULES      None.
                 
      NOTES      The handle returned will be a number between 0 and MDF 
                 where MDF is specified in InitDBF().

                 This function is analogous to QB's FREEFILE.
      
      RETURN     Available free data file handle or -1 if none are 
                 available.
      
      EXAMPLE    dbfile = FreeDataFileDBF
                 IF dbfile < 0 THEN DoNoDataHandlesAvailable
                 stat = OpenDataDBF(dfname$,dbfile,asmode)

      





     FreeKeyFileDBF
      
      TYPE       FUNCTION
      
      SYNTAX     kyfile = FreeKeyFileDBF
      
      PARAMETERS None.
      
      USE        Obtain a free QBXDBF key file handle.
      
      RULES      None.
      
      NOTES      The handle returned will be a number between 0 and MKF 
                 where MKF is specified in InitDBF().

                 This function is analogous to QB's FREEFILE.
      
      RETURN     Available free key file handle or -1 if none are 
                 available.
      
      EXAMPLE    kyfile = FreeKeyFileDBF
                 IF kyfile < 0 THEN DoNoKeyHandlesAvailable
                 stat = OpenKeyDBF(kfname$,kyfile,dbfile,asmode)

      





     GetCurrKeyDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = GetCurrKeyDBF(kyfile,Qkey$)
      
      PARAMETERS kyfile - INTEGER. Number used as fileno in OpenKeyDBF().
                 Qkey$ - STRING.   The current key for kyfile is placed in
                 this variable.
      
      USE        Get the current/last accessed key for kyfile. The 
                 returned key will include a 2-byte enumerator attached to 
                 the key proper.
                 
      RULES      None.
                 
      NOTES      This routine is used to get the actual key used to index 
                 the last accessed record used by the Get() routines 
                 (excluding GetDirect()).

                 QBXDBF uses an enumerator word to differentiate
                 identical keys. For instance, let's say you're indexing a 
                 mailing list. One index to this mailing list is by name. 
                 While you could index on the three fields of the name 
                 (LASTNAME+FIRSTNAME+MI), it would be a pretty big index 
                 term and still no guarantee that you won't have identical 
                 names. To improve index performance you could elect to 
                 use only the first 5 characters of the last name, plus 
                 the first and middle initials. So instead of having a 
                 51-byte index term (25+25+1) the index term is only 7 
                 bytes. (5+1+1),substr(LASTNAME,1,5)+substr(FIRSTNAME,1,1)+MI.
                 Still, what to do when two people have the same names?
                 Since having even the full 51-byte index won't help
                 differentiate two identical names QBXDBF uses an 
                 enumerator.

                 The enumerator is a 2-byte identifier tacked on to the
                 end of each key by the QBXDBF AddKeyDBF() routine. You 
                 need only be aware that the enumerator is there; its use 
                 is automatically maintained by QBXDBF. The enumerator is 
                 a 2-byte binary value with the most significant byte 
                 first, for proper sorting. It is the last two bytes of 
                 the key, e.g., the 7-byte key above is physically 9 bytes 
                 LONG.  The key proper can be obtained with
                 LEFT$(Qkey$,keylen) and the enumerator proper with 
                 MID$(Qkey$,keylen+1,2). The logical keylen is returned by 
                 StatKeyDBF().







                 When calling GetCurrKeyDBF() the key returned in Qkey$
                 will be the key plus the enumerator. Typically, you won't
                 be interested in the key, anyway, but rather the data 
                 record returned by the Get() routines. However, let's say 
                 you want to process as much of the mailing list as can be 
                 done by a certain time. When that time is reached the 
                 computer must stop processing the mailing list and start 
                 another task. By using GetCurrKeyDBF() you can save the 
                 exact key that the mailing list program was doing and 
                 then start it up again (after the interruption) by doing 
                 a GetEqualDBF() with Qkey$ as returned by GetCurrKeyDBF().

                 Still, how does one determine if this key is for the 
                 record one wants? Here it takes a human's intervention. 
                 Let's say that instead of a mailing list we are working 
                 with an online system. A caller requests the status of an 
                 order. For the sake of demonstration, the index to orders 
                 is by customer name. His name is DEE B. MURRAY. 
                 Wonderful, MURRADB, 5 matches. The operator then asks 
                 additional information from the caller: street address? 
                 With this information the operator scans each of the five 
                 records with MURRADB as the key until the street address 
                 given matches. The proper record has been found and the 
                 order status can be given. 

                 Ideally, the key expressions you develop will evaluate
                 to unique keys.
      
      RETURN     Errors 219, 222, 224, and DOS.
                 
      EXAMPLE    ON UEVENT GOSUB DoNextProcess
                 DoPrep
                 DoMailing
                 END
                 DoNextProcess:
                 DoProcessFlag = 1
                 RETURN
                 SUB DoMailing
                 DO
                    stat = GetNextDBF(kyfile,dbfile,vseg,voff)
                    stat = MailThisRecord(datarec)
                    IF DoProcessFlag = 1 THEN 
                       stat = GetCurrKeyDBF(kyfile,Last$)
                       DoInterruptProcess
                       'do another process and come back here
                       stat=GetEqualDBF(kyfile,dbfile,Last$,vseg,voff)

      





     GetDirectDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = GetDirectDBF(dbfile,recno&,vseg,voff)
      
      PARAMETERS dbfile - INTEGER. Number used as fileno in OpenDataDBF().
                 recno& - LONG. Number of record to get.
                 vseg - INTEGER. Segment address of data record.
                 voff - INTEGER. Offset address of data record.
      
      USE        Get a data record from the data file without using any 
                 index file. recno& = 1 gets the very first data record in 
                 dfile, 2 gets then next, and so on. 
      
      RULES      recno& must be > 0 and <= the last possible record.
      
      NOTES      This function can be used to get records from the data 
                 file to reindex a key file, although ReindexDBF() is much 
                 faster and creates a smaller index file.

                 See AddKeyDBF() for more info on vseg:voff
      
      RETURN     Errors 219, 222, 224, and DOS.
      
      EXAMPLE    INPUT "Retrieve which record number ";recno&
                 stat = GetDirectDBF(0,recno&,vseg,voff)
                 IF stat = 0 THEN
                    PRINT "Record=";datarec.ID;datarec.RK

      





     GetEqualDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = GetEqualDBF(kyfile,dbfile,Qkey$,vseg,voff)
      
      PARAMETERS kyfile - INTEGER. Number used as fileno in OpenKeyDBF().
                 dbfile - INTEGER. Number used as fileno in OpenDataDBF().
                 Qkey$ - STRING.   The key (or partial key) to search for.
                 vseg - INTEGER. Segment address of data record.
                 voff - INTEGER. Offset address of data record.
      
      USE        Search for the key Qkey$ in kyfile. If it's found, 
                 return the data record to which it's pointing to the 
                 record buffer pointed to by vseg:voff. If it's not found 
                 the QBXDBF tracking pointers are positioned so that by 
                 using GetNextDBF() or GetPrevDBF() the data record of the 
                 key after or before Qkey$ could be found.
      
      RULES      Qkey$ must not begin with an ASCII 0 or 255.
      
      NOTES      For partial searches use a key that you want to start 
                 the search on.

                 For instance, to find all surnames starting with a key 
                 of KING in your database, use a Qkey$ = "KING". Even if 
                 there is no exact match with GetEqualDBF() you can still 
                 get all other records starting with KING, e.g., KINGMAN, 
                 KINGSTON, etc., by using the GetNextDBF() routine while 
                 LEFT$(Qkey$,4) = "KING", or until the end of file is 
                 reached.

                 See AddKeyDBF() for more information on vseg:voff.
      
      RETURN     Errors 200, 202, 204, 219, 222, 223, and DOS.
      
      EXAMPLE    INPUT "Get which key ";Qkey$
                 stat = GetEqual(0,0,Qkey$,vseg,voff)
                 IF stat = 0 THEN 
                    PRINT "Record=";datarec.ID;datarec.RK

      





     GetFirstDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = GetFirstDBF(kyfile,dbfile,vseg,voff)
      
      PARAMETERS kyfile - INTEGER. Number used as fileno in OpenKeyDBF().
                 dbfile - INTEGER. Number used as fileno in OpenDataDBF().
                 vseg - INTEGER. Segment address of data record.
                 voff - INTEGER. Offset address of data record.
      
      USE        Get the first data record in keyfile order and return it 
                 in the data record at vseg:voff. Since QBXDBF sorts on 
                 ASCII values, the first record will be the record with 
                 the lowest ASCII value key.
      
      RULES      None.
      
      NOTES      See GetCurrKeyDBF() to obtain the key for this data 
                 record.

                 See AddKeyDBF() for more information on vseg:voff.

                 For sequential in-order processing of the entire data 
                 file in keyfile order, you would want to start at the 
                 very first record; this function does just that. After 
                 processing this first record, use GetNextDBF() and 
                 continue processing until end of file (error 202).
      
      RETURN     Errors 204, 219, 222, and DOS.
      
      EXAMPLE    stat = GetFirstDBF(0,0,vseg,voff)
                 IF stat = 0 THEN 
                    PRINT "First key=";datarec.ID;datarec.RK

      





     GetGTDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = GetGTDBF(kyfile,dbfile,Qkey$,vseg,voff)
      
      PARAMETERS kyfile - INTEGER. Number used as fileno in OpenKeyDBF().
                 dbfile - INTEGER. Number used as fileno in OpenDataDBF().
                 Qkey$ - STRING.   Get the data record of the first key
                 greater than Qkey$.
                 vseg - INTEGER. Segment address of data record.
                 voff - INTEGER. Offset address of data record.
      
      USE        Get the data record that is indexed by the first key 
                 which is greater than Qkey$.
      
      RULES      None.
      
      NOTES      See GetCurrKeyDBF() to obtain the key for this data 
                 record.

                 See AddKeyDBF() for more information on vseg:voff.
      
      RETURN     Errors 202, 204, 219, 222, and DOS.
      
      EXAMPLE    INPUT "Get first key greater than ";lastkey$
                 stat = GetGT(0,0,lastkey$,vseg,voff))
                 IF stat = 0 THEN
                    PRINT "First key GT=";datarec.ID;datarec.RK

      





     GetGTEDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = GetGTEDBF(kyfile,dbfile,Qkey$,vseg,voff)
                 
      PARAMETERS kyfile - INTEGER. Number used as fileno in OpenKeyDBF().
                 dbfile - INTEGER. Number used as fileno in OpenDataDBF().
                 Qkey$ - STRING.   Get the data record for then key greater
                 or equal to Qkey$.
                 vseg - INTEGER. Segment address of data record.
                 voff - INTEGER. Offset address of data record.
      
      USE        Get the data record that is indexed by the first key 
                 which is greater than or equal to Qkey$.
      
      RULES      None.
      
      NOTES      See GetCurrKeyDBF() to obtain the key for this data 
                 record.

                 See AddKeyDBF() for more information on vseg:voff.
                 
      RETURN     Errors 202, 204, 219, 222, and DOS.
                 
      EXAMPLE    INPUT "Get first key GTE to ";lastkey$
                 stat = GetGTEDBF(0,0,lastkey$,vseg,voff)
                 IF stat = 0 THEN
                    PRINT "First key GTE=";datarec.ID;datarec.RK

      





     GetLastDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = GetLastDBF(kyfile,dbfile,vseg,voff)
      
      PARAMETERS kyfile - INTEGER. Number used as fileno in OpenKeyDBF().
                 dbfile - INTEGER. Number used as fileno in OpenDataDBF().
                 vseg - INTEGER. Segment address of data record.
                 voff - INTEGER. Offset address of data record.
      
      USE        Get the last data record in keyfile order and return it 
                 in the data record at vseg:voff. Since QBXDBF sorts on 
                 ASCII values, the last record will be the record with the 
                 highest ASCII value key.
      
      RULES      None.
      
      NOTES      See GetCurrKeyDBF() to obtain the key for this data 
                 record.

                 See AddKeyDBF() for more information on vseg:voff.

                 For reverse sequential in-order processing of the entire
                 data file in keyfile order, you would want to start at 
                 the very last record; this function does just that. After 
                 processing this last record, use GetPrevDBF() and 
                 continue processing until top of file (error 203).
      
      RETURN     Errors 204, 219, 222, and DOS.
      
      EXAMPLE    stat = GetLastDBF(0,0,vseg,voff)
                 IF stat = 0 THEN
                    PRINT "Last key=";datarec.ID;datarec.RK

      





     GetLTDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = GetLTDBF(kyfile,dbfile,Qkey$,vseg,voff)
      
      PARAMETERS kyfile - INTEGER. Number used as fileno in OpenKeyDBF().
                 dbfile - INTEGER. Number used as fileno in OpenDataDBF().
                 Qkey$ - STRING.   Get the data record of the first key less
                 than Qkey$.
                 vseg - INTEGER. Segment address of data record.
                 voff - INTEGER. Offset address of data record.
      
      USE        Get the data record that is indexed by the first key 
                 which is less than Qkey$.
      
      RULES      None.
      
      NOTES      See GetCurrKeyDBF() to obtain the key for this data 
                 record.

                 See AddKeyDBF() for more information on vseg:voff.
      
      RETURN     Errors 203, 204, 219, 222, and DOS.
      
      EXAMPLE    INPUT "Get key less than ";lastkey$
                 stat = GetLTDBF(0,0,lastkey$,vseg,voff)
                 IF stat = 0 THEN
                    PRINT "Last key LT=";datarec.ID;datarec.RK

      





     GetLTEDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = GetLTEDBF(kyfile,dbfile,Qkey$,vseg,voff)
      
      PARAMETERS kyfile - INTEGER. Number used as fileno in OpenKeyDBF().
                 dbfile - INTEGER. Number used as fileno in OpenDataDBF().
                 Qkey$ - STRING.   Get the data record of the first key less
                 than or equal to Qkey$.
                 vseg - INTEGER. Segment address of data record.
                 voff - INTEGER. Offset address of data record.
                 
      USE        Get the data record that is indexed by the first key 
                 which is less than or equal to Qkey$.
      
      RULES      None.
      
      NOTES      See GetCurrKeyDBF() to obtain the key for this data 
                 record.

                 See AddKeyDBF() for more information on vseg:voff.
                 
      RETURN     Errors 203, 204, 219, 222, and DOS.
                 
      EXAMPLE    INPUT "Get key LTE to ";lastkey$
                 stat = GetLTE(0,0,lastkey$,vseg,voff)
                 IF stat = 0 THEN
                    PRINT "Last key LTE=";datarec.ID;datarec.RK

      





     GetNextDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = GetNextDBF(kyfile,dbfile,vseg,voff)
      
      PARAMETERS kyfile - INTEGER. Number used as fileno in OpenKeyDBF().
                 dbfile - INTEGER. Number used as fileno in OpenDataDBF().
                 vseg - INTEGER. Segment address of data record.
                 voff - INTEGER. Offset address of data record.
      
      USE        Get the data record that is indexed by the next key 
                 after the last found key.
      
      RULES      None.
      
      NOTES      See GetCurrKeyDBF() to obtain the key for this data 
                 record.

                 See AddKeyDBF() for more information on vseg:voff.

                 This function is usually used after a GetFirstDBF() or
                 GetEqualDBF(). If you are searching for a key based on a 
                 partial key, use GetEqualDBF() with the partial key and 
                 continue searching with GetNextDBF() until you either 
                 find the key you want, determine that it's not in the key 
                 file, or reach the end of file.
                 
      RETURN     Errors 202, 204, 219, 222, and DOS.
                 
      EXAMPLE    partkey$ = "73ST"
                 stat = GetEqualDBF(0,0,partkey$,vseg,voff)
                 IF stat = 200 THEN 
                    DO
                       stat = GetNextDBF(0,0,vseg,voff)
                       IF stat = 0 THEN 
                          stat = GetCurrKeyDBF(0,Qkey$)
                          IsKey = AskIfWantedKey(Qkey$)
                          IF IsKey THEN EXIT DO
                       ENDIF
                    LOOP WHILE stat = 0

      





     GetPositionDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = GetPositionDBF(kyfile,recno&)
      
      PARAMETERS kyfile - INTEGER. Number used as fileno in OpenKeyFile().
                 recno& - LONG. The current record number last used by
                 kyfile is placed in this variable.
      
      USE        Get the last data record number accessed by kyfile. This 
                 record number is updated everytime you use any of the Add 
                 or Get functions (excluding GetDirectDBF), or 
                 UpdateRecordDBF().
      
      RULES      None.
      
      NOTES      Use this to get the record number needed by 
                 UpdateRecordDBF(), DeleteRecordDBF(), and UndeleteRecordDBF().
      
      RETURN     Error 219, 222.
      
      EXAMPLE    stat = GetFirstDBF(kyfile,dbfile,vseg,voff)
                 PRINT "First key is using record#";
                 stat = GetPositionDBF(kyfile,recno&)
                 PRINT recno&

      





     GetPrevDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = GetPrevDBF(kyfile,dbfile,vseg,voff)
      
      PARAMETERS kyfile - INTEGER. Number used as fileno in OpenKeyDBF().
                 dbfile - INTEGER. Number used as fileno in OpenDataDBF().
                 vseg - INTEGER. Segment address of data record.
                 voff - INTEGER. Offset address of data record.
      
      USE        Get the data record that is indexed by the previous key 
                 relative to the last found key.
      
      RULES      None.
      
      NOTES      See GetCurrKeyDBF() to obtain the key for this data 
                 record.

                 See AddKeyDBF() for more information on vseg:voff.

                 This function is usually used after a GetLastDBF() or
                 GetEqualDBF(). If you are searching for a key based on a 
                 partial key, use GetEqualDBF() with the partial key and 
                 continue searching with GetPrevDBF() until you either 
                 find the key you want, determine that it's not in the key 
                 file, or reach the top of file.
      
      RETURN     Errors 203, 204, 219, 222, and DOS.
      
      EXAMPLE    partkey$ = "73STZZZZ"
                 stat = GetEqualDBF(0,0,partkey$,vseg,voff)
                 IF stat = 200 THEN 
                    DO
                       stat = GetPrevDBF(0,0,vseg,voff)
                       IF stat = 0 THEN 
                          stat = GetCurrKeyDBF(0,Qkey$)
                          IsKey = AskIfWantedKey(Qkey$)
                          IF IsKey THEN EXIT DO
                       ENDIF
                    LOOP WHILE stat = 0

      





     InitDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = InitDBF(MKF,MDF,NoFields)
      
      PARAMETERS MKF - INTEGER. Maximum number of key files that you plan
                 on using this session (0-based).
                 MDF - INTEGER. Maximum number of data files that you plan
                 on using this session (0-based).
                 NoFields - INTEGER. Maximum number of fields in a single
                 data record (1-based).
      
      USE        Initialize the QBXDBF file system and allocate the 
                 required buffers.
      
      RULES      This function must be called before any other QBXDBF 
                 function.
      
      NOTES      NoField should be set to the maximum number of fields 
                 that you expect any data record to contain of any data 
                 file you open or create this session. Note that for each 
                 data file requested (MDF) a full request of NoField field 
                 descriptors is allocated. For example, if MDF=5 files and 
                 NoFields=10 then (10*(MDF+2)*32) bytes of far heap is 
                 allocated (2240 bytes) even if only 1 data file has 10 
                 fields and then rest, say, have 4 fields each.
                 QBXDBF sets aside buffers for each file request you make 
                 with MKF and MDF. These buffers are created dynamically, 
                 e.g., REDIM keybuff(-1 TO MKF) AS keynodeTYPE, where each 
                 element in the array is reserved for a separate file. 

                 Note that array subscript -1 is used internally by QBXDBF.
                 Using QBXDBF functions without having first called this 
                 function may cause various BASIC run-time errors.

                 QBXDBF lets you open and use up to 250 files at one time
                 using DOS 3+. However, the FILES= statement in CONFIG.SYS 
                 will be the limiting factor in how many you can actually 
                 use. The internal routine SFTFiles() can be used to 
                 determine what the FILES= is.
                 
      RETURN     Errors 225, 234.
                 
      EXAMPLE    'need 30 key,10 data files,and 10 max fields/record
                 'this session
                 stat = InitDBF(29,9,10)
                 'can OpenKeyDBF(file$,numkey,dbfile,asmode) where numkey
                 'is 0-29 and OpenDataDBF(file$,numdat,asmode) where numdat
                 'is 0-9 and where the maximum number of fields in any
                 'data file is 10.

      





     MKN$
      
      TYPE       FUNCTION
      
      SYNTAX     ASCIInum$ = MKN$(dbfile,FieldNumber,zNum#,errc)
      
      PARAMETERS dbfile - INTEGER. Number used as fileno in OpenDataDBF().
                 FieldNumber - INTEGER. Field number in the data record
                 that zNum# coincides with.
                 zNum# - DOUBLE. Value to convert to a STRING.
                 errc - INTEGER. Status of conversion process is placed in
                 this variable.
      
      USE        Since dBASE format specifies that all data be in ASCII 
                 form any NUMERIC data types must be converted. The format 
                 is automatically determined from the field descriptor 
                 information.
      
      RULES      dbfile and FieldNumber must be valid.
      
      NOTES      You can call GetFieldDBF() for each field in the data 
                 record if you do not know the physical field number but 
                 do know the field name. See GetFieldDBF() in Appendix A. 
                 for more.
      
      RETURN     errc returns:   (4.2 below means field length=4 decimals=2)
                 0 = okay, valid return string
                 1 = significance error (zNum#=97651.5 in 4.2, returns "9765")
                 2 = integer overflow (zNum#=165.51 in 5.2, returns "165.5")
                 3 = exponent in number value, returns all "#"
                 4 = not a numeric field
      
      EXAMPLE    stat = GetNextDBF(kyfile,dbfile,vseg,voff)
                 IF VAL(datarec.RK) < 70 THEN
                    datarec.RK = MKN$(dbfile,2,CLNG(70),errc)
                    'datarec.RK is AS STRING * 6
                    stat = GetPositionDBF(kyfile,recordno&)
                    stat = UpdateRecordDBF(dbfile,recordno&,vseg,voff)

      





     OpenDataDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = OpenDataFile(filename$,fileno,asmode)
      
      PARAMETERS filename$ - STRING.   Pathname of data file to open.
                 fileno - INTEGER. Number to associate the data file with
                 for future operations. Valid range is 0 to MDF.
                 asmode - INTEGER. Network. When asmode (Access/Sharing
                 mode) is:

           &H42 open file with shared R/W access (others have R/W access),
              2 open file in DOS 2.x compatible R/W mode (not for networks),
           &H12 open file with exclusive R/W access (others have no access),
           &H22 open file with exclusive W access (others have read access),
           &H32 open file with exclusive R access (others have write access),
                any valid DOS value permitted.
                 
      USE        Open an existing QBXDBF data file with the mode 
                 determined by asmode.
      
      RULES      fileno can be any unused fileno 0 to MDF. See InitDBF. 
                 SHARE.EXE must be installed for any of the exclusive 
                 access modes to share or lock files.
      
      NOTES      See also FreeDataFileDBF().

                 For simplified network programming where the file can be 
                 opened for exclusive use set asmode to &H12. As long as 
                 the file remains open no other process may access any 
                 part of it.

                 The fileno actually represent the data buffer index that
                 this file will be using.
      
      RETURN     Errors 219, 227, 228, 233, and DOS.
      
      EXAMPLE    dbfile = 0
                 asmode = &H42
                 stat = OpenDataDBF(filename$,dbfile,asmode)

      





     OpenKeyDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = OpenKeyDBF(filename$,fileno,
                                   dbfile,asmode)
      
      PARAMETERS filename$ - STRING.   Pathname of key file to open.
                 fileno - INTEGER. Number to associate the key file with
                 for future operations. Valid range is 0 to MKF.
                 dbfile - INTEGER. File number of the OPENED data file
                 that this key file is for.
                 asmode - INTEGER. Network. When asmode (Access/Sharing
                 mode) is:

           &H42 open file with shared R/W access (others have R/W access),
              2 open file in DOS 2.x compatible R/W mode (not for networks),
           &H12 open file with exclusive R/W access (others have no access),
           &H22 open file with exclusive W access (others have read access),
           &H32 open file with exclusive R access (others have write access),
                any valid DOS value permitted.
      
      USE        Open an existing QBXDBF key file with the mode 
                 determined by asmode.
      
      RULES      fileno can be any unused fileno 0 to MKF. See InitDBF.
                 SHARE.EXE must be installed for any of the exclusive 
                 access modes to share or lock files..
                 
      NOTES      dbfile is required because when the key file is opened 
                 the key expression within its header is evaluated. This 
                 key expression evaluation, performed automatically, 
                 requires access to the data file's field descriptors.

                 See also FreeKeyFileDBF().

                 For simplified network programming where the file can be
                 opened for exclusive use set asmode to &H12. As long as 
                 the file remains open no other process may access any 
                 part of it.

                 The fileno actually represent the key buffer index that
                 this file will be using.
      
      RETURN     Errors 219, 227, 228, 233, and DOS.
      
      EXAMPLE    'see AddKeyDBF() for more
                 kyfile = 0
                 asmode = &H42
                 stat = OpenKeyDBF(filename$,kyfile,dbfile,asmode)

      





     PackDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = PackDBF(dbfile,kyfile,packfile$,keyfile$)
                 
      PARAMETERS dbfile - INTEGER. Number used as fileno in OpenDataDBF().
                 kyfile - INTEGER. Optional. Number used as fileno in
                 OpenKeyDBF().
                 packfile$ - STRING.   Destination pathname of new packed file.
                 keyfile$ - STRING.   Optional. Destination pathname of new
                 index file for packfile$.
      
      USE        Reconstruct dbfile by removing all deleted records and 
                 optionally reindexing it.
                 
      RULES      None.
                 
      NOTES      This routine can operate in two modes: 

                 First, to pack dbfile without also creating a new index, 
                 set kyfile=0 and keyfile$="" (null string). Each record 
                 of dbfile is scanned and if it is not marked as deleted, 
                 it is copied to the new file packfile$. After all records 
                 have been copied dbfile remains open. packfile$ is not 
                 open. To use packfile$ in place of the current dbfile see 
                 the example below.

                 Second, if kyfile is a valid open key file, and keyfile$
                 is not a null string ("") then after the packing has been 
                 completed, packfile$ is reindexed based on the key 
                 expression in kyfile. After reindexing kyfile remains 
                 open. To use packfile$ with its index file keyfile$ see 
                 the example below.

                 If packfile$ or keyfile$ already exist they will be 
                 overwritten.

                 If more than one file indexes the data file use
                 ReindexDBF() to reindex the others.

                 See ReindexDBF() for more information.
      
      RETURN     Errors 219, 222, 225 and DOS.
      
      EXAMPLE    'dbfile/kyfile already open (dbfile$/kyfile$)
                 packfile$ = "$datpack.$$$"
                 keyfile$ = "$keypack.$$$"
                 'pack and reindex dbfile
                 stat = PackDBF(dbfile,kyfile,packfile$,keyfile$)
                 'use new files instead
                 stat = CloseDataDBF(dbfile)
                 stat = CloseKeyDBF(kyfile)
                 stat = DeleteFile(dbfile$+CHR$(0))
                 stat = DeleteFile(kyfile$+CHR$(0))
                 stat = RenameFile(packfile$+CHR$(0)),dbfile$+CHR$(0))
                 stat = RenameFile(keyfile$+CHR$(0)),kyfile$+CHR$(0))
                 stat = OpenDataDBF(dbfile$,dbfile,asmode)
                 stat = OpenKeyDBF(kyfile$,kyfile,asmode)
                 'dbfile/kyfile the new packed/reindexed files

      





     ReindexDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = ReindexDBF(kyfile,dbfile,keyfile$)
      
      PARAMETERS kyfile - INTEGER. Number used as fileno in OpenKeyDBF().
                 dbfile - INTEGER. Number used as fileno in OpenDataDBF().
                 keyfile$ - STRING.   Destination pathname of new index file
                 for dbfile.
      
      USE        Reindex data file dbfile using the key expression in 
                 kyfile to a new file, keyfile$.
                 
      RULES      kyfile and dbfile must be open.
                 
      NOTES      No validation is done on kyfile or dbfile so make sure 
                 they are valid. Use the StatDBF() routines if necessary. 
                 This because ReindexDBF() is called by PackDBF() with 
                 system handles (-1).

                 This reindex routine will optimize the B-tree by packing
                 key nodes to 90-95% of capacity. Most of the sorting 
                 takes place in memory so this routine is CPU-bound, 
                 unlike the incremental indexing of AddKeyDBF() which is 
                 mostly disk I/O-bound. Indexing rates of 15,000 
                 records/minute on mid-level machines is typical and 
                 50,000 per minute on high-performance machines.

                 If keyfile$ already exists it will be overwritten.

                 A temporary work file called "$<RUNS>$.TMP" is created
                 by ReindexDBF(). The current directory is used to store 
                 the file unless a DOS environment variable called QBXTMP 
                 is defined. E.g., SET QBXTMP=C:\TMP creates the work file 
                 on drive C: in the \TMP subdirectory. This work file is 
                 deleted.

                 If you need to reindex a data file than has more than
                 one index file call ReindexDBF() for each of them.
      
      RETURN     Errors DOS.
      
      EXAMPLE    'dbfile/kyfile already open (dbfile$/kyfile$)
                 keyfile$ = "$keypack.$$$"
                 'reindex dbfile
                 stat = ReindexDBF(kyfile,dbfile,keyfile$)
                 'use new index file instead
                 stat = CloseKeyDBF(kyfile)
                 stat = DeleteFile(kyfile$+CHR$(0))
                 stat = RenameFile(keyfile$+CHR$(0)),kyfile$+CHR$(0))
                 stat = OpenKeyDBF(kyfile$,kyfile,asmode)
                 'kyfile is now a new index file for dbfile

      





     StatDataDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = StatDataDBF(dbfile,reclen,recs&,
                                    bfileno,NoFields,LUdate$,ID)
      
      PARAMETERS dbfile - INTEGER. Number used as fileno in OpenDataDBF().
                 reclen - INTEGER. The record length of dbfile is returned
                 in this variable.
                 recs& - LONG. The number of total records, including
                 'deleted', in dbfile is placed in this variable.
                 bfileno - INTEGER. The DOS file handle for dfile is
                 placed in this variable.
                 NoFields - INTEGER. The number of fields in each data
                 record is placed in this variable.
                 LUdate$ - STRING.   The current Last Update date is placed
                 in this variable. The format is 'MM/DD/YR'.
                 ID - INTEGER. If ID=99 then the LUdate$ determination is
                 not performed.
      
      USE        Obtain basic information on the opened data file.
                 
      RULES      None.
                 
      NOTES      ID=99 was added for internal use to avoid the overhead 
                 of the date conversion routine since this function is 
                 called by nearly every high-level QBXDBF routine.
      
      RETURN     Errors 219, 222.
                 
      EXAMPLE    stat=StatDataDBF(0,reclen,recs&,bfile,NoFields,LUdate$,0)
                 IF stat = 0 THEN PRINT "Last update="; LUdate$

      





     StatKeyDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = StatKeyDBF(kyfile,keylen,keys&,bfileno)
      
      PARAMETERS kyfile - INTEGER. Number used as fileno in OpenKeyDBF().
                 keylen - INTEGER. The key length of kyfile is returned in
                 this variable.
                 keys& - LONG. The number of total keys in kyfile is
                 placed in this variable.
                 bfileno - INTEGER. The DOS file handle for kyfile is
                 placed in this variable.
                 
      USE        Obtain basic information on the opened key file.
      
      RULES      None.
      
      NOTES      keylen is returned 2 less than the physical key length. 
                 This is because all keys have a 2-byte enumerator 
                 attached to create unique keys. See GetCurrKeyDBF() for 
                 more information.
      
      RETURN     Errors 219, 222.
      
      EXAMPLE    stat = StatKeyDBF(0,keylen,keys&,bfileno)
                 IF stat = 0 THEN PRINT "Key length="; keylen

      





     UndeleteRecordDBF
      
      TYPE       FUNCTION
                 
      SYNTAX     stat = UndeleteRecordDBF(dbfile,recordno&)
                 
      PARAMETERS dbfile - INTEGER. Number used as fileno in OpenDataDBF().
                 recordno& - LONG. Number of record to undelete.
      
      USE        Unmark a record marked as deleted by changing the delete 
                 tag to ASCII 32.
      
      RULES      None.
      
      NOTES      See GetPositionDBF() for information on determining 
                 recordno&.

                 Dbase file managers do not physically remove or reuse
                 records that have been deleted. Instead, a delete tag is 
                 changed from ASCII 32 (space) to ASCII 42 (*). Any key 
                 file remains unaltered in any case. It is up to your 
                 program's logic to handle 'deleted' records.

                 The QBXDBF routine PackDBF() will physically remove any
                 records marked as deleted.
      
      RETURN     219, 222, 224, and DOS.
      
      EXAMPLE    stat = GetNextDBF(kyfile,dbfile,vseg,voff)
                 IF datarec.tag = "*" THEN
                    stat = GetPositionDBF(kyfile,recordno&)
                    stat = UndeleteRecordDBF(dbfile,recordno&)

      





     UpdateRecordDBF
      
      TYPE       FUNCTION
                 
      SYNTAX     stat = UpdateRecordDBF(dbfile,recordno&,vseg,voff)
      
      PARAMETERS dbfile - INTEGER. Number used as fileno in OpenDataDBF().
                 recordno& - LONG. Number of record to update.
                 vseg - INTEGER. Segment address of data record.
                 voff - INTEGER. Offset address of data record.
      
      USE        Update information within an existing data record.
      
      RULES      No part of the record that contains any part of any key 
                 should be updated without also reflecting that change in 
                 the respective index.
      
      NOTES      See GetPositionDBF() for information on determining 
                 recordno&.

                 This routine should be used with extreme caution. 
                 Changing parts of a record that contain any type of key, 
                 be it primary or foreign, may cause referential integrity 
                 problems, without due care taken. (For information of 
                 referential integrity consult a text on 'Relational 
                 Databases'.)
      
      RETURN     219, 222, 224, and DOS.
      
      EXAMPLE    stat = GetNextDBF(kyfile,dbfile,vseg,voff)
                 IF VAL(datarec.RK) < 70 THEN
                    datarec.RK = MKN$(dbfile,2,CLNG(70),errc)
                    stat = GetPositionDBF(kyfile,recordno&)
                    stat = UpdateRecordDBF(dbfile,recordno&,vseg,voff)

      





     VersionDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = VersionDBF(version$)
      
      PARAMETERS version - STRING.   The version of QBXDBF in use is placed
                 in this variable.
      
      USE        Return the version of QBXDBF in use.
      
      RULES      None.
      
      NOTES      Returns the version in ASCII form. Version 1.00 returns 
                 'QBXDBF V1.00 PRO'.
      
      RETURN     Always 0.
      
      EXAMPLE    nul = VersionDBF(version$)
                 PRINT "This program is using "; version$

      





     APPENDIX A. SUPPORT FUNCTIONS
      
      These functions are used in support of QBXDBF and can also be used 
      by you in your programs. All are FUNCTIONs except GetDiskInfo.
      
      Note that there are several other routines in the BTDBF.BAS code 
      that are not documented--they are low-level routines called by 
      documented functions and are subject to change until they are 
      documented.
      
       1) ExpandDataDBF(dfileno,norecs&)
       2) ExpandKeyDBF(kfileno,nokeys&)
       3) FileExists(filename$)
       4) GetDefaultDrive()
       5) GetDiskInfo(drive$,ACL,MCL,BPS,SPCL,freebytes&)
       6) GetDosVersion()
       7) GetFieldDBF(dbfile,FieldNumber,FldList AS DBFFieldListTYPE)
       8) GetXEInfo(class,action,locus)
       9) SFTFiles()
      10) CreateFile(filenameZ$,attribute)
      11) OpenDevice(filenameZ$,mode,handle,flen&)
      12) ReadDevice(handle,start&,bytes&,vseg,voff)
      13) WriteDevice(handle,start&,bytes&,vseg,voff)
      14) CloseDevice(handle)
      15) DeleteFile(filenameZ$)
      16) RenameFile(oldfileZ$,newfileZ$)

      





     ExpandDataDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat=ExpandDataDBF(dbfile,norecs&)
      
      PARAMETERS dbfile - INTEGER. Number used as fileno in OpenDataDBF().
                 norecs& - LONG. The number of records to expand dbfile by.
      
      USE        Expand the physical size of dbfile so that it can 
                 contain at least norecs& more records without file 
                 fragmentation.
      
      RULES      None.
      
      NOTES      This routine is optional.

                 Two uses of this routine are: 1) tell DOS to allocate 
                 disk space for norecs& more records beforehand to 
                 minimize file fragmentation, and 2) ensure that your 
                 program will have room for norecs& more records, now and 
                 in the future. In other words, if you know your program 
                 will ultimately need room for 60,000 records then you 
                 could reserve the space all at once.

                 Deleted records are not included when calculating the
                 number of records to add. In other words, if you ask for 
                 100 records to expand by then 100 records it is.
                 Existing data in the newly added record space is not 
                 cleared. This expands only the physical file allocation. 
                 The dBASE header information is not changed.

                 The space added will be as contiguous as the current
                 state of fragmentation on the disk. If the disk is highly 
                 fragmented then this routine will get highly-fragmented 
                 space from DOS.
      
      RETURN     Errors 209, 219, 222, 224, and DOS.
      
      EXAMPLE    INPUT "Records to expand data file ";xrecs&
                 stat=ExpandDataDBF(dfileno,xrecs&)

      





     ExpandKeyDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat=ExpandKeyDBF(kyfile,nokeys&)
      
      PARAMETERS kyfile - INTEGER. Number used as fileno in OpenKeyDBF().
                 nokeys& - LONG. The number of keys to expand kyfile by.
      
      USE        Expand the physical size of kyfile so that it can 
                 contain at least nokeys& more keys without file 
                 fragmentation.
      
      RULES      None.
      
      NOTES      This routine is optional.

                 Two uses of this routine are: 1) tell DOS to allocate
                 disk space for nokeys& more keys beforehand to minimize 
                 file fragmentation, and 2) ensure that your program will 
                 have room for nokeys& more keys, now and in the future. 
                 In other words, if you know your program will ultimately 
                 need room for 60,000 keys then you could reserve the 
                 space all at once.

                 The keys in the key file are never deleted. To
                 reorganize a key file use ReindexDBF() or PackDBF().
                 QBXDBF is approximately 67% efficient in using node 
                 space. This is factored in when calculating the space 
                 required to allocate nokeys& more keys so the expansion 
                 is an approximation.

                 Existing data in the newly added key space is not
                 cleared.

                 The space added will be as contiguous as the current
                 state of fragmentation on the disk. If the disk is highly 
                 fragmented then this routine will get highly-fragmented 
                 space from DOS. 
      
      RETURN     Errors 208, 219, 222, 224, and DOS.
      
      EXAMPLE    INPUT "Keys to expand key file ";xkeys&
                 stat=ExpandKeyDBF(kyfile,xkeys&)

      





     FileExists
      
      TYPE       FUNCTION
      
      SYNTAX     stat=FileExists(filename$)
      
      PARAMETERS filename$ - STRING.   Pathname of file to verify exists.
      
      USE        Determine if filename$ exists and can be accessed.
      
      RULES      None.
      
      NOTES      This function returns -1 if the file exists. Other 
                 return values are DOS error codes.

                 For instance, if the file is currently locked, 5 is 
                 returned (access denied). To determine if a file exists 
                 or not, check for a return value of -1 (exists and is 
                 accessible), or 2 (file does not exist).
                 
      RETURN     -1 if file is accessible,
                  2 if file does not exist,
                 or other DOS errors.
      
      EXAMPLE    stat=FileExists("C:\HIST\AR91.KEY")
                 IF stat=2 THEN
                    DoCreateNewKeyFile
                 ELSEIF stat=-1 THEN
                    DoFileAlreadyExistsError
                 ELSE
                    DoHandleFileAccessError stat

      





     GetDefaultDrive
      
      TYPE       FUNCTION
      
      SYNTAX     CurrDrive=GetDefaultDrive
      
      PARAMETERS None.
      
      USE        Determine the current default DOS drive.
      
      RULES      None.
      
      NOTES      This function returns the ASCII representation of the 
                 current default DOS drive.

                 For instance, if the current drive is C:,
                 GetDefaultDrive returns the ASCII representation of C, or 
                 67. To convert this to a string use CHR$().
                 
      RETURN     ASCII representation of current DOS drive letter.
                 
      EXAMPLE    CurrDrive$=CHR$(GetDefaultDrive)
                 PRINT "Current drive=";CurrDrive$+":"

      





     GetDiskInfo
      
      TYPE       SUB
      
      SYNTAX     GetDiskInfo(drive$,ACL,MCL,BPS,SPCL,freebytes&)
      
      PARAMETERS drive$ - STRING.   Drive letter to get disk info from
                 (first character significant).
                 ACL - INTEGER. The number of available clusters on drive$
                 is placed in this variable.
                 MCL - INTEGER. The number of total, or maximum, clusters
                 on drive$ is placed in this variable.
                 BPS - INTEGER. The number of bytes per sector for drive$
                 is placed in this variable.
                 SPCL - INTEGER. The number of sectors per cluster for
                 drive$ is placed in this variable.
                 freebytes& - LONG. The number of free bytes left on
                 drive$ is placed in this variable.
                 
      USE        Obtain information for the given DOS drive.
      
      RULES      None.
      
      NOTES      This function uses DOS function 36h to get information 
                 on drive$.

                 For information on the default drive use drive$ = "@".

                 freebytes& = -1 if drive$ is not a valid DOS drive.
      
      RETURN     None.
      
      EXAMPLE    GetDiskInfo("C:",ACL,MCL,BPS,SPCL,freebytes&)
                 PRINT "Bytes remaining on drive C:=";freebytes&

      





     GetDosVersion
      
      TYPE       FUNCTION
      
      SYNTAX     DOSver=GetDosVersion
      
      PARAMETERS None.

      USE        Determine the DOS version in use.
                 
      RULES      None.
                 
      NOTES      This function returns the DOS version that your program 
                 is running on x100. 

                 For instance, if the system is running on DOS 3.31
                 GetDosVersion returns 331.
      
      RETURN     DOS version x100.
      
      EXAMPLE    DOSver=GetDosVersion
                 PRINT USING "DOS version ##.##";DOSver/100

      





     GetFieldDBF
      
      TYPE       FUNCTION
      
      SYNTAX     stat = GetFieldDBF(dbfile,FieldNumber,FldList
                                    AS DBFFieldListTYPE)
      
      PARAMETERS dbfile - STRING.   Number used as fileno in OpenDataDBF().
                 FieldNumber - INTEGER. Number of field to get information
                 on. The first field is 1.
                 FldList - DBFFieldListTYPE.TYPEd data structure to fill 
                 with field information. 
      
      USE        Get information on the specified field in dbfile.
      
      RULES      dbfile and FieldNumber must be valid.
      
      NOTES      You can call GetFieldDBF() for each field in the data 
                 record if you do not know the physical field number but 
                 do know the field name:
                 
      RETURN     Always 0, no validation checks made. Be careful.
                 
      EXAMPLE    DIM FldList AS DBFFieldListTYPE  'in QBXDBF.BI
                 DIM ZR AS STRING * 1
                 ZR = CHR$(0)
                 'find field number that corresponds to FldName$
                 FldName$ = "LASTNAME"+ZR+ZR
                 'note FldName$ ZERO-filled to 10 characters
                  
                 stat=StatDataDBF(dbfile,rl,recs&,bf,NoFields,LUdate$,ID)
                 found = 0
                 FOR i = 1 TO NoFields
                    stat = GetFieldDBF(dbfile,i,FldList)
                    IF FldList.FieldName = FldName$ THEN
                       found = i
                       EXIT FOR
                    ENDIF
                 NEXT
                 IF found THEN
                    PRINT FldName$; "is field number:"; found

      





     GetXEInfo
      
      TYPE       FUNCTION
      
      SYNTAX     Xerror=GetXEInfo(class,action,locus)
      
      PARAMETERS class - INTEGER. The error class code is placed in this
                 variable.
                 action - INTEGER. The recommended action code is placed
                 in this variable.
                 locus - INTEGER. The error locus code is placed in this
                 variable.
      
      USE        Obtain detailed error information after a previous DOS 
                 error.
      
      RULES      Requires DOS 3+.
      
      NOTES      Use this function after a QBXDBF function returns a DOS 
                 error.

                 See Appendix D, DOS Error Codes, for a listing of all
                 DOS error, class, action, and locus code descriptions.
      
      RETURN     Extended DOS error code.
      
      EXAMPLE    stat=OpenKeyFile(filename$,0)
                 IF stat>0 AND stat<200 THEN 
                    Xerr=GetXEInfo(class,action,locus)
                    PRINT "Extended error:";ExtendErrMsg$(Xerr)
                    PRINT "Error class:";ClassErrMsg$(class)
                    PRINT "Recommend:";RecommendMsg$(action)
                    PRINT "Error locus:";LocusMsg$(locus)

      





     SFTFiles
      
      TYPE       FUNCTION
      
      SYNTAX     MaxFiles=SFTFiles
      
      PARAMETERS None.
      
      USE        Determine the number of file slots allocated in the 
                 System Files Table.
      
      RULES      None.
      
      NOTES      This function returns the number after FILES= in 
                 CONFIG.SYS.

                 For instance, if you have FILES=30 in your CONFIG.SYS
                 file, SFTFiles() returns 30.

                 This uses an undocumented DOS function. See the BASIC
                 source for more.
      
      RETURN     The maximum number of DOS system-wide handles.
      
      EXAMPLE    MinFiles=40+4
                 Files=SFTFiles
                 IF Files<MinFiles THEN
                    PRINT "Set FILES=44 in CONFIG.SYS"

      





     CreateFile
      
      TYPE       FUNCTION
      
      SYNTAX     stat=CreateFile(filenameZ$,attribute)
      
      PARAMETERS filenameZ$ - STRING.   Pathname of file to create.
                 attribute - INTEGER, BYVAL.DOS directectory attribute to 
                 give the file.
      
      USE        Create a new file using DOS function 3Ch. 
      
      RULES      filenameZ$ must not already exist.

                 filenameZ$ must end with a CHR$(0).
      
      NOTES      By using these file functions you can save 15K in EXE 
                 file size by not needing BASIC's file functions.
                 attribute can take the following values:

                    0 normal
                    1 read-only
                    2 hidden
                    4 system
                 
      RETURN     -1 if filenameZ$ either has zero length or is not ASCIIZ,
                 Errors DOS.
                 
      EXAMPLE    filename$ = "F:\AR91\CONFIG.QBT"
                 stat=CreateFile(filename$+CHR$(0),0)

      





     OpenDevice
      
      TYPE       FUNCTION
      
      SYNTAX     stat=OpenDevice(filenameZ$,mode,handle,flen&)
      
      PARAMETERS filenameZ$ - STRING.   Pathname of file/device to open.
                 mode - INTEGER, BYVAL.Open mode.
                 handle - INTEGER. The DOS handle for this file is placed
                 in this variable.
                 flen& - LONG. The length of the file at time of open is
                 placed in this variable.
      
      USE        Open a file/device using DOS function 3Dh.
      
      RULES      filenameZ$ must exist.

                 filenameZ$ must end with a CHR$(0).
      
      NOTES      By using these file functions you can save 15K in EXE 
                 file size by not needing BASIC's file functions.
                 mode values are (bit-mapped):

                 bit 7 = inheritance flag (DOS 3+)
                   4-6 = sharing mode (DOS 3+)
                     3 = reserved (should=0)
                   0-2 = access type

                 For read/write non-network access to a file use mode=2.

                 For exact uses of mode consult a DOS programmer reference.
      
      RETURN     -1 if filenameZ$ either has zero length or is not ASCIIZ,
                 Errors DOS.
      
      EXAMPLE    stat=OpenDevice("TEST.DAT"+CHR$(0),2,han,flen&)
                 IF stat=0 THEN
                    PRINT "DOS handle=";han
                    PRINT "File length=";flen&

      





     ReadDevice
      
      TYPE       FUNCTION
      
      SYNTAX     stat=ReadDevice(handle,start&,bytes&,vseg,voff)
      
      PARAMETERS handle - INTEGER, BYVAL.DOS handle to read from.
                 start& - LONG, BYVAL.If block device then byte offset 
                 into file to start reading from.
                 bytes& - LONG, BYVAL.Number of bytes to read from the 
                 device.
                 vseg - INTEGER, BYVAL.Segment of buffer.
                 voff - INTEGER, BYVAL.Offset of buffer.
      
      USE        Read from a DOS device to RAM using DOS function 3Fh.
                 
      RULES      handle must be open.
      
      NOTES      The first byte is 0.

                 To continue reading from the last position+1 use start&= -1.

                 By using these file functions you can save 15K in EXE
                 file size by not needing BASIC's file functions.

                 You can read/write to DOS's predefined handles without
                 first needing to open them (they're already open):

                    0 STDIN  (CON)
                    1 STDOUT (CON)
                    2 STDERR (CON)
                    3 STDAUX (AUX)
                    4 STDLST (PRN)
                 
      RETURN     Errors DOS.
                 
      
      EXAMPLE    REDIM buffer(1 TO 16384) AS INTEGER
                 vs=VARSEG(buffer(1))
                 vo=VARPTR(buffer(1))
                 stat=OpenDevice("TEST.DAT"+CHR$(0),2,han,flen&)
                 'read 32K of the file at a time
                 IF stat=0 THEN
                    stat=ReadDevice(han,0,32768,vs,vo)
                    DoProcessBuffer vs,vo
                    DO WHILE stat=0
                       vs=vs+(32768\16)
                       stat=ReadDevice(han,-1,32768&,vs,vo)
                       DoProcessBuffer vs,vo
                    LOOP

      





     WriteDevice
      
      TYPE       FUNCTION
      
      SYNTAX     stat=WriteDevice(han,start&,bytes&,vseg,voff)
      
      PARAMETERS handle - INTEGER, BYVAL.DOS handle to write to.
                 start& - LONG, BYVAL.If block device then byte offset 
                 into file to start writing to.
                 bytes& - LONG, BYVAL.Number of bytes to write to the 
                 device.
                 vseg - INTEGER, BYVAL.Segment of buffer.
                 voff - INTEGER, BYVAL.Offset of buffer.
                 
      USE        Write from RAM to a DOS device using DOS function 40h.
                 
      RULES      handle must be open.
                 
      NOTES      The first byte is 0.

                 To continue writing to the last position+1 use start&= -1.

                 By using these file functions you can save 15K in EXE 
                 file size by not needing BASIC's file functions.

                 You can read/write to DOS's predefined handles without
                 first needing to open them (they're already open):

                    0 STDIN  (CON)
                    1 STDOUT (CON)
                    2 STDERR (CON)
                    3 STDAUX (AUX)
                    4 STDLST (PRN)
      
      RETURN     Errors DOS.
      
      EXAMPLE    REDIM buffer(1 TO 16384) AS INTEGER
                 vs=VARSEG(buffer(1))
                 vo=VARPTR(buffer(1))
                 stat=OpenDevice("TEST.DAT"+CHR$(0),2,han,flen&)
                 'write 5 32K blocks of the file
                 FOR i=1 TO 5
                    DoSetupBuffer vs,vo
                    stat=WriteDevice(han,-1,32768&,vs,vo)
                    IF stat THEN EXIT FOR
                    vs=vs+(32768\16)
                 NEXT

      





     CloseDevice
      
      TYPE       FUNCTION
      
      SYNTAX     stat=CloseDevice(handle)
      
      PARAMETERS handle - INTEGER. The DOS handle to close.
      
      USE        Close a DOS device using DOS function 3Eh.
      
      RULES      Handles 0-4 cannot be closed.
      
      NOTES      By using these file functions you can save 15K in EXE 
                 file size by not needing BASIC's file functions.
      
      RETURN     Errors DOS.
      
      EXAMPLE    stat=OpenDevice("TEST.DAT"+CHR$(0),2,han,flen&)
                 IF stat=0 THEN
                    PRINT "DOS handle=";han
                    PRINT "File length=";flen&
                    stat=CloseDevice(han)

      





     DeleteFile
      
      TYPE       FUNCTION
      
      SYNTAX     stat=DeleteFile(filenameZ$)
      
      PARAMETERS filenameZ$ - STRING.   Pathname of file to delete.
      
      USE        Delete a file using DOS function 41h. Similar to BASIC's 
                 KILL.
      
      RULES      filenameZ$ must exist.

                 filenameZ$ must end with a CHR$(0).
      
      NOTES      By using these file functions you can save 15K in EXE 
                 file size by not needing BASIC's file functions.
      
      RETURN     -1 if filenameZ$ either has zero length or is not ASCIIZ,
                 Errors DOS.
      
      EXAMPLE    IF FileExists(fileZ$) = -1 THEN
                    stat=DeleteFile(fileZ$)

      





     RenameFile
      
      TYPE       FUNCTION
      
      SYNTAX     stat=RenameFile(oldfileZ$,newfileZ$)
      
      PARAMETERS oldfileZ$ - STRING.   Pathname of original file.
                 newfileZ$ - STRING.   Filename to replace original with.
      
      USE        Rename a file using DOS function 56h. Similar to BASIC's 
                 NAME.
      
      RULES      oldfileZ$ must exist. newfileZ$ must not exist.

                 oldfileZ$ and newfileZ$ must end with a CHR$(0).
      
      NOTES      By using these file functions you can save 15K in EXE 
                 file size by not needing BASIC's file functions.
      
      RETURN     -1 if oldfileZ$ or newfileZ$ either have zero length or 
                 aren't ASCIIZ,
                 Errors DOS.
      
      EXAMPLE    IF FileExists(fileZ$) = -1 THEN
                    stat=RenameFile(fileZ$,newfileZ$)

      





     APPENDIX B. TECHNICAL SPECIFICATIONS
      
      Technical Specifications:
      
      Key length   : 3-62 bytes(ASCII sort),fixed-len,2-byte enumerator
      Record length: 2-32767 bytes, fixed-len, .DBF format
      Node size    : 512 bytes
      Keys per node: 7-63 keys, (512-3)\(key length+5)
      Max keys/file: 5.5 million keys (65534 nodes)
      Max recs/file: 16.7 million records
      Max key files: 250 (total combined files <=250 DOS 3+)
      Max data file: 250 (total combined files <=15 DOS 2)

      Key file header format (first sector (512 bytes) of key file):
      
      filetype  char ; 0 file type, ASCII '0', 30hex
      rootnode  int  ; 1 sector in file of root node
      nokeyslo  int  ; 3 number of keys (low word)
      nokeyshi  byte ; 5 - (high byte)
      internal  int  ; 6 internal use                 
      nxkeysec  int  ; 8 next free node/sector
      keylen    byte ;10 length of key +2
      maxkeys   byte ;11 maximum keys per node
      keyexpr   char ;12-115 key expression
      dbfile    char ;116-147 link data file (optional) 
      internal  byte ;148-511 internal use
      
      Some structures above use a 24-bit value. These use 3 bytes 
      (word+byte) to store information. For example, the value of the 
      datavlo/hi structure in the data file header is:
      
      DataAvailRec&=1&*datavlo+(datavhi*65536)
      
      Data file header format (first 32 bytes of data file):

      fileID    byte ; 0 data file type id, 03 standard (43,63,83,88h)
      LastYR    byte ; 1 last update year
      LastMo    byte ; 2 last update month 
      LastDA    byte ; 3 last update day
      NoRecs    long ; 4 number of records in file
      HdrLen    int  ; 8 length of header including field descriptors+1
      RecLen    int  ;10 length of data record including delete tag
      internal  byte ;12-31 internal use








      Field Descriptor format:
     
      FieldName char ; 0 field name (see below)
      FieldType char ;11 field type (C N L D M, see below)
      internal  long ;12 internal use
      FieldLen  byte ;16 length of this field (see below)
      FieldDC   byte ;17 decimal count (see below)
      internal  byte ;18-31 internal use
      
      Each field is described by a 32-byte descriptor. The first field's 
      descriptor starts right after the header proper, at offset +32. 
      After the last field descriptor is data byte ASCII 13. Immediately 
      following this is the actual record information.
      
      The field name may contain from 1 to 10 characters. It must start 
      with a letter, contain only alphanumeric values, CAPITALIZED, and be 
      zero-filled/zero-terminated. The underscore (ASCII 95) is permitted 
      within the name.
      
      The field type specifies the data type. C is for character data. 
      Maximum FieldLen for character data type is 255 characters. FieldDC 
      is 0. 
      
      N is for numeric data. There is no further distinction on numeric 
      type. Maximum FieldLen is 19. FieldDC is either 0, 2, or any value 2 
      less than FieldLen but no more than 15. This specification varies 
      slightly depending on the implementation of the database manager. 
      FieldDC should never be 1. See the QBXDBF function MKN$() (make 
      number a string) to convert BASIC numeric data types to that 
      required. 
      
      L is for logical data. This 1-byte field may be left null (space), 
      or may contain either the characters T or Y for true; F or N for 
      false. If left null the displayed character should be a question 
      mark (ASCII 63). The implementation of this data type is left to the 
      programmer.
      
      D is for date data. This 8-byte field is an ASCII date in the form 
      MM/DD/YY. The implementation of this data type is left to the 
      programmer.
      
      M is for a memo field. This 10-byte field is a pointer to the 
      corresponding memo data in the memo file (.DBT). Implementation of 
      this data type is not standard in the industry and its 
      implementation is left to the programmer.
      
      By adhering to these specifications any data file that you create 
      will be readable by other programs that handle the DBF file format. 
      However, there is nothing to stop you from storing binary data in a 
      field (except non-compatibility). This way you can avoid MKN$() and 
      VAL() and the conversion processing time. See Appendix C., Using 
      Non-string Data TYPEs for more information.







     Key Record Format:
      
      There is an internal first key with a null value that logically 
      marks the top of the key file.
      
      Beginning each node is a count key byte. This is the count of valid 
      keys on that node. Then for each key is a 16-bit previous node 
      pointer, the key itself, the 24-bit data record pointer for that 
      key, and a 16-bit next node pointer (node pointers are zero at the 
      leaf nodes).
      
      02  00 00  000000  00 00 00  00 00  KEY001  01 00 00  00 00 ... 
       1.   2.     3.       4.       5.     6.       7.       8.   9.
      
      1. Key count for that node
      2. Node back pointer (for non-leaf nodes)
      3. The internal null key
      4. The 24-bit data record pointer (low word/hi byte)
      5. Node forward ptr/back ptr (for non-leaf nodes)
      6. First logical key (here 'KEY001')
      7. Its data pointer (record number in data file)
      8. Its forward node pointer (for non-leaf nodes)
      9. Repeat 6 to 8 for each key on node.
      
      QBXDBF makes some allowances on the strict B-TREE and ISAM 
      definitions. For all practical purposes, consider QBXDBF superior to 
      the text-book implementations of these.






      
      Data Record Format:
      
      The first data record is located at offset  +HdrLen. The first byte 
      of each data record is a delete tag. This tag is maintained 
      automatically by the QBXDBF routines. Following this is the data for 
      each field, not delimited. The second record is at offset +HdrLen 
      +reclen. The start offset of any record in the file can be computed 
      as (recordnumber - 1) * reclen + HdrLen. All data is in ASCII form.
      
      Resource Allocation:
      
      Storage for the data buffers and headers are allocated at run-time 
      in far memory. This means that very little string space is used by 
      QBXDBF. Data allocation is as follows (arrays are stored in far 
      memory):
      
      2 integer arrays (-1 to MKF) + (-1 to MDF) for file handles.
      1 key hdr array (0 to MKF) for key file headers, ea 64 bytes.
      1 data hdr array (0 to MDF) for data file headers, ea 32 bytes.
      1 key node array (0 to MKF) for node buffers, ea 512 bytes.
      1 field descriptor array (0 TO NoFields,-1 TO MDF) ea 32 bytes.
      1 long integer array (0 to MKF) to track current record numbers.
      1 array (-1 to MKF) AS STRING * 104 for key expression.
      1 type variable for interfacing with QBXDBF low-level, 18 bytes.
      ... and other miscellaneous variables totalling about 1000 bytes.

      





     APPENDIX C. PROGRAMMING TIPS.
      
      Using Non-string Data TYPEs:
      
      DBF files store numeric data in ASCII form, i.e., the integer value 
      20000 is stored in a minimum of 5 bytes (5.0). The simplest method 
      to program with this requirement is to use the QBXDBF supplied 
      function MKN$() to convert QB numerics to ASCII and use QB's VAL() 
      function to convert the DBF ASCII to QB numeric.
      
      Another method if you are seeking maximum performance is to 
      implement two data structures. One for the DBF format and the other 
      for QB itself. Take for example the program under AddKeyDBF(). Here 
      we have the TYPE definition:
      
      TYPE dbStrucTYPE
      tag AS STRING * 1   'dBASE-required delete tag 
      ID AS STRING * 20   'first field in data record, say, a name
      RK AS STRING * 6    'second field (range "0.00"-"100.00")
      END TYPE
      DIM datarec as dbStrucTYPE  'allocate the record I/O buffer
      
      Note the RK type, STRING * 6. RK in the program is required to be a 
      single-precision floating-point variable (see the INPUT statement). 
      What we could do is define a type for both the DBF file and the QB 
      program. In addition to the dbStrucTYPE, define another type called 
      qbStrucTYPE:
      
      TYPE qbStrucTYPE
      tag AS STRING * 1 
      ID AS STRING * 20 
      RK AS SINGLE      
      END TYPE
      DIM qbrec as qbStrucTYPE  'allocate the record qb work
      
      When reading from or writing to the DBF file, we use datarec. When 
      working within QB itself we use qbrec. To assign one to the other 
      you must code the proper translator. In some cases this may be more 
      trouble than what it's worth but it can significantly improve 
      performance by not repeatedly calling MKN$() and VAL().

      





     APPENDIX D. ERROR CODES.
      
      DSAM generated error codes (200-218):
      
        0  No error - the operation was successful.
      
      200  Key not found - the key is not in the index file.
      
      201  Key already exists - more than 32767 'identical' enumerated keys.
      
      202  End of file - reached the end of file.
      
      203  Top of file - reached the top of file.
      
      204  Empty file - there are no keys in the index file.
      
      205  Reserved - previously disk full error. This error is now 
      indicated by DOS error -2 - disk full or unexpected end of file.
      
      206  Reserved.
      
      207  Reserved.
      
      208  Node exceeds limit - more than 65534 nodes used by index file.
      
      209  Record exceeds limit - more than 16777215 records used by data file.
      
      210  Corrupt index - index file is probably corrupt.
      
      211  Invalid function - an invalid DSAM function was called.
      
      212-218  Reserved.
      
      BTDBF.BAS generated error codes (219-239):
      
      219  File number invalid - the file number used is greater than the 
      highest allocated in InitDBF().
      
      220  Reserved.
      
      221  Key length invalid - length must be from 1-62 bytes when 
      creating a key file.
      
      222  File not open - the fileno for a key or data file operation is 
      not open.
      
      223  Invalid null key assignment - a null key cannot be used. Null 
      is defined in QBXDBF as either ASCII 0 or ASCII 255 in the first 
      character of a key.
      
      224  Invalid record number - a record number less than 1 or a 
      record number greater than the maximum records possible was used.







      225  No handles available - no DOS handles are available. Use a
      greater value in config.sys FILES= (FILES=20). Max FILES=255 with 
      DOS 3+ or FILES=20 with DOS 2.
      
      226  Reserved.
      
      227  File number already open - the fileno is already in use.
      
      228  File not QBXDBF - the filename in OpenFile() is not recognized 
      as a QBXDBF file.
      
      229  Reserved.
      
      230  File already exists - the CreateFile() filename already exists.
      
      231  File not found - the filename$ specified in OpenFile() does 
      not exist or is not valid.
      
      232  Reserved.
      
      233  Init not active - using QBXDBF Create() and Open() routines 
      without having called InitDBF().
      
      234  Init already active - calling InitDBF() more than once.
      
      235-239  Reserved.
      
      240  Invalid key expression - key expression is longer than 104 
      characters or is not properly constructed.
      
      241-242  Reserved.
      
      243  Invalid number of fields - the field count is < 1 or is > 
      MaxFields in InitDBF().
      
      Error numbers are not exclusively generated by the module 
      indicated. It is possible for BTDBF to issue error 208, for instance.

      






      
      DOS Error Codes:
      
      Possible stat return codes in decimal.
      
       -2 disk full or unexpected end of file
       -1 bad filename
        0 no error
        1 function not supported
        2 file not found
        3 path not found
        4 too many open files
        5 access denied
        6 handle invalid
        7 MCBs destroyed
        8 not enough memory
        9 memory block address invalid
       10 environment invalid
       11 format invalid
       12 access code invalid
       13 data invalid
          reserved-0Eh
       15 disk drive invalid
       16 cannot remove current directory
       17 not same device
       18 no more files
       19 disk write protected
       20 unknown unit
       21 drive not ready
       22 unknown command
       23 data error (CRC)
       24 bad request structure length
       25 seek error
       26 unknown medium type
       27 sector not found
       28 printer out of paper
       29 write fault
       30 read fault
       31 general failure
       32 sharing violation
       33 lock violation
       34 disk change invalid
       35 FCB unavailable
       36 sharing buffer overflow
          reserved-25h
          reserved-26h
          reserved-27h
          reserved-28h
          reserved-29h
          reserved-2Ah
          reserved-2Bh







          reserved-2Ch
          reserved-2Dh
          reserved-2Eh
          reserved-2Fh
          reserved-30h
          reserved-31h
       50 network request not supported
       51 remote computer not listening
       52 duplicate name on network
       53 network name not found
       54 network busy
       55 network device no longer exists
       56 NETBIOS command limit exceeded
       57 network adapter hardware error
       58 incorrect response from network
       59 unexpected network error
       60 incompatible remote adapter
       61 print queue full
       62 queue not full
       63 not enough space to print file
       64 network name deleted
       65 access denied
       66 network device type incorrect
       67 network name not found
       68 network name limit exceeded
       69 NETBIOS session limit exceeded
       70 temporarily paused
       71 network request not accepted
       72 print/disk redirection paused
          reserved-49h
          reserved-4Ah
          reserved-4Bh
          reserved-4Ch
          reserved-4Dh
          reserved-4Eh
          reserved-4Fh
       80 file exists
       81 reserved-51h
       82 cannot make
       83 fail on INT24
       84 out of structures
       85 already assigned
       86 invalid password
       87 invalid parameter
       88 network write fault
      
      DOS Class Codes:
      
        1 out of resources
        2 temporary situation
        3 authorization







        4 internal
        5 hardware failure
        6 system failure
        7 application error
        8 not found
        9 bad format
       10 locked
       11 media failure
       12 already exists
       13 unknown
      
       DOS Action Codes:
      
        1 retry
        2 delay retry
        3 reenter input
        4 abort
        5 immediate exit
        6 ignore
        7 user intervention
      
      DOS Locus Codes:
      
        1 unknown
        2 block device
        3 reserved
        4 serial device
        5 memory






                           QBXDBF v1.0 ORDER FORM


                                                      Qty     Extended

      QBXDBF v1.0 . . . . . . . . . . . . . $55.00 x _____ = __________

      QBXDBF v1.0 printed 75-page manual  .  15.00 x _____ = __________
      *Manual on disk is similar in content to printed manual
       and is included with all orders

                                                  Subtotal:  __________

              (Texas residents only add 8.25%)   Sales tax:  __________

      SHIPPING COSTS   USA   CAN   Foreign  Shipping costs:  __________
      QBXDBF        : none  $2.00  $ 3.00
      printed manual: 3.00   5.00   10.00            TOTAL: $
                                                             ==========

      Please remit TOTAL amount in US funds on US bank only, to:

                Cornel Huth
                6402 Ingram Rd.
                San Antonio, Texas  78238  USA


      Name: ___________________________________________________________

      Mailing address: ________________________________________________

      _________________________________________________________________

      _________________________________________________________________

      _________________________________________________________________

      Special instructions or comments (continue on reverse if needed):



      Please indicate how you obtained QBXDBF 1.0. If from a BBS please
      indicate which one and its telephone number:

      _________________________________________________________________

      BBS:_____________________________ Tele: (     )______-___________