NISTIR 4481







THE NIST "BUILDING LIFE-CYCLE COST" (BLCC) PROGRAM 
(Version 3.2 for 1993)

User's Guide and Reference Manual





Stephen R. Petersen
Office of Applied Economics 
Computing and Applied Mathematics Laboratory





Sponsored by
The Federal Energy Management Program
U.S. Department of Energy
Washington, D.C. 20585

January 1991


























ABSTRACT


The NIST Building Life-Cycle Cost computer program (BLCC 3.2) provides
economic analysis of proposed capital investments that are expected to reduce
long-term operating costs of buildings or building systems.  It is especially
useful for evaluating the costs and benefits of energy conservation projects
in buildings.  Two or more alternative designs can be evaluated to determine
which has the lowest life-cycle cost.  Economic measures, including net
savings, savings-to-investment ratio, and adjusted internal rate of return,
can be calculated for any design alternative relative to the designated base
case.  BLCC can be used for evaluating both Federal and private-sector
projects.  It complies with ASTM standards related to building economics as
well as FEMP and OMB A-94 guidelines for economic analysis of Federal building
projects.  BLCC is designed to run on an IBM-PC or compatible microcomputer
with approximately 640K of random access memory, with or without a hard disk. 
The BLCC program supersedes both the FBLCC and NBSLCC computer programs
previously released by NIST (NBS).



Note: Please see file README.1 for updated information about BLCC that is not 
included in this user's guide.

































                                      iii

PREFACE


The Building Life-Cycle Cost computer program, version 3.2, has been prepared
as an aid to implementing life-cycle cost evaluations of potential energy
conservation and renewable energy projects in new and existing Federal
buildings.  It can also be used for evaluating similar projects in the private
sector and at the state and local government levels.  BLCC 3.2 supersedes and
incorporates both the Federal Building Life-Cycle Cost (FBLCC) and the
National Bureau of Standards Life-Cycle Cost (NBSLCC) programs.  For the
economic analysis of energy conservation investments in Federal buildings,
BLCC complies with NBS Handbook 135, Life-Cycle Costing Manual for the Federal
Energy Management Program.  For other investments in Federal buildings, BLCC
complies with OMB Circular A-94, "Discount Rate to Be Used in Evaluating Time-
distributed Costs and Benefits," March 27, 1972.  BLCC complies with the
American Society for Testing and Materials (ASTM) standard practices for
building economics, including E917 (Practice for Measuring Life-Cycle Costs of
Buildings and Building Systems), E964 (Practice for Measuring Benefit-to-Cost
and Savings-to-Investment Ratios for Buildings and Building Systems), E1057
(Practice for Measuring Internal Rates of Return for Investments in Buildings
and Building Systems), and E1074 (Practice for Measuring Net Benefits for
Investments in Buildings and Building Systems).

BLCC is the third of a four-volume set of reports which together provide a
comprehensive set of methods, data, and computational tools for economic
evaluation of such projects.  Included in the four-volume set are the
following:

(1) Life-Cycle Costing Manual for the Federal Energy Management Program,    
      National Institute of Standards and Technology, Handbook 135 (revised
      1991).

Handbook 135 is a guide to understanding life-cycle costing and related
methods of economic analysis as they are applied to Federal decisions.  It
describes the required procedures and assumptions, defines and explains how to
apply and interpret economic performance measures, gives examples of Federal
decision problems and their solutions, explains how to use the energy price
indices and discount factors which are updated annually in the supplement (2),
and provides worksheets and other computational aids and instructions for
calculating the required measures.


(2) Energy Prices and Discount Factors for Life-Cycle Cost Analysis, National
      Institute of Standards and Technology, (Annual Supplement to NIST
      Handbook 135 and NBS Special Publication 709), NISTIR 85-3273 (updated
      annually).

This report, which is updated annually, gives the energy price and discount
factor multipliers needed to estimate the present value of energy and other
future costs.  The data are based on energy price projections developed by the
Energy Information Administration of the U.S. Department of Energy.  Request
the latest edition.




                                      iv

(3) The NIST "Building Life-Cycle Cost" (BLCC) Computer Program (version 3.2),
National Institute of Standards and Technology, 1990.

The NIST Building Life-Cycle Cost computer program (BLCC 3.2) provides
economic analysis of proposed capital investments that are expected to reduce
long-term operating costs of buildings or building systems.  It is especially
useful for evaluating the costs and benefits of energy conservation projects
in buildings.  Two or more alternative designs can be evaluated to determine
which has the lowest life-cycle cost.  Economic measures, including net
savings, savings-to-investment ratio, and adjusted internal rate of return,
can be calculated for any design alternative relative to the designated base
case.  BLCC can be used for evaluating both Federal and private-sector
projects.  It complies with ASTM standards related to building economics as
well as FEMP and OMB A-94 guidelines for economic analysis of Federal building
projects.  BLCC is designed to run on an IBM-PC or compatible microcomputer
with approximately 640K of random access memory, with or without a hard disk. 
The BLCC program supersedes both the FBLCC and NBSLCC computer programs
previously released by NIST (NBS).


(4) DISCOUNT--A Program for Discounting Computations in Life-cycle Cost
Analyses (version 3.2), NISTIR 4513, National Institute of Standards and
Technology, 1991.

The DISCOUNT program computes discount factors and related present values,
future values, and periodic payment values of cash flows occurring at known
points in time.  DISCOUNT is especially useful for solving life-cycle cost
analysis problems which do not require the comprehensive summation and
reporting capabilities provided by the BLCC program.  DISCOUNT performs all of
the functions of standard discounting tables, computing present values of
future amounts, future values of present amounts, present and future values of
periodic payments, periodic payments corresponding to present and future
amounts, and corresponding discount factors.  In addition, DISCOUNT computes
the present value of periodic payments which increase at known rates over
time, and the present value of energy costs which increase at rates projected
by the U.S. Department of Energy for use in Federal life-cycle cost analyses. 
DISCOUNT provides the added flexibility of accepting non-integer discount
rates, time periods, and escalation rates in its computations.  DISCOUNT runs
on most IBM PC and compatible microcomputers with no special equipment
requirements.  The user's guide and reference manual is included on the
program diskette. 

Both the BLCC and DISCOUNT computer programs access DOE energy prices
projections from the same two disk files included with these programs
(currently ENCOST93.SEQ and ENCOST93.RAN).  These files are updated and
released at the same time that NISTIR 85-3273, Energy Prices and Discount
Factors for Life-Cycle Cost Analysis, is released each year.  These disk files
ensure that BLCC and DISCOUNT are compatible with computations performed using
the factors in NISTIR 85-3273.  







                                      v

For representatives of Federal government agencies and contractors to the
Federal government, these publications can be ordered from:

    Advanced Sciences, Inc.
    2000 North 15th Street
    Suite 407
    Arlington, VA 22201
    (703) 243-4900

Please request the publications by name and number.

For others interested in obtaining the BLCC or DISCOUNT computer programs,
please contact one of the following organizations:

National Technical Information Service
5285 Port Royal Road
Springfield, VA 22161
(703) 487-4650

PC Software Interest Group
1030D East Duane Avenue
Sunnyvale, CA 94086
(408) 730-9291

MTS Software
5 Oak Forest Court
Saint Charles, MO 63303
(314) 441-1022

Energy Ware
PO Box 254
Littleton, NH 03561
(800) 522-4485

Workshops on the life-cycle costing method and energy analysis are conducted
at locations around the country each year.  The workshops include training and
software for both BLCC and an energy analysis computer program called "A
Simplified Energy Analysis Method" (ASEAM).  A schedule of workshops can be
obtained from the Office of Applied Economics, National Institute of Standards
and Technology, Bldg. 101, Room A415, Gaithersburg, MD 20899, (301) 975-6132.

An introduction to the workshop is provided in a video training film, "Least-
Cost Energy Decisions:  An Introduction to Life-Cycle Cost Analysis."  The
video film and companion workbook can be ordered from Video Transfer, Inc.,
5709-B Arundel Avenue, Rockville, MD 20852, (301) 881-0270.  Additional
training films in the series are in preparation.

Further information on the Federal Energy Management Program can be obtained
from the Federal Energy Management Program Staff, Office of the Assistant
Secretary for Conservation and Renewable Energy, U.S. Department of Energy. 
Please direct communication to:  FEMP, CE 10.1, U.S. Department of Energy,
1000 Independence Avenue, SW, Washington, D.C. 20585.




                                      vi

ACKNOWLEDGMENTS

The author wishes to thank Mr. Richard W. Brancato and Mr. K. Dean DeVine of
the Federal Energy Management Program of the U.S. Department of Energy (DOE)
for their continued support and direction of this work.  Appreciation is also
extended to Harold Marshall, Rosalie Ruegg and Barbara Lippiatt of the Office
of Applied Economics and Stephen Treado of the Center for Building Technology
for their careful review of this User's Guide.
















































                                      vii


                                   CONTENTS

                                                                          Page


ABSTRACT. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .  iii

PREFACE . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .   iv

ACKNOWLEDGMENTS . . . . . . . . . . . . . . . . . . . . . . . . . . . . .  vii


1.  INTRODUCTION. . . . . . . . . . . . . . . . . . . . . . . . . . . . .    1

2.  INSTALLING AND RUNNING BLCC . . . . . . . . . . . . . . . . . . . . .    4

3.  CONDUCTING A BLCC ANALYSIS. . . . . . . . . . . . . . . . . . . . . .    5

     3.1  The Main BLCC Menu. . . . . . . . . . . . . . . . . . . . . . .    5
     3.2  Creating or Editing Input Data Files for a Project Alternative.    5
     3.3  Calculating Life-Cycle Costs and Cash-Flow analyses . . . . . .   10
     3.4  Lowest LCC and Comparative Economic Analysis. . . . . . . . . .   14

4.  REPORTS GENERATED BY BLCC . . . . . . . . . . . . . . . . . . . . . .   16

5.  GENERALIZED INPUT DATA FILE STRUCTURE FOR BLCC. . . . . . . . . . . .   17

6.  STANDARD DEPRECIATION TABLES. . . . . . . . . . . . . . . . . . . . .   19

7.  COMPUTATIONAL CONVENTIONS USED IN BLCC. . . . . . . . . . . . . . . .   20

8.  DEFINITIONS AND ACCEPTABLE RANGES OF INPUT VARIABLES USED IN THE 
    BLCC PROGRAM. . . . . . . . . . . . . . . . . . . . . . . . . . . . .   21

INDEX . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .   32




















                                      viii


                                LIST OF TABLES

                                                                          Page

Table 1.  New or Enhanced BLCC Features . . . . . . . . . . . . . . . . .   2

Table 2.  Reports Generated by BLCC . . . . . . . . . . . . . . . . . . .  16

Table 3.  Input Data File Structure . . . . . . . . . . . . . . . . . . .  18


                                LIST OF FIGURES

Figure 1.  Main BLCC Menu . . . . . . . . . . . . . . . . . . . . . . . .   5

Figure 2.  The "Save Data" Menu . . . . . . . . . . . . . . . . . . . . .   7

Figure 3.  Input Data File Report for DEMO1 . . . . . . . . . . . . . . .   8

Figure 4.  BLCC Summary for DEMO1 . . . . . . . . . . . . . . . . . . . .  10

Figure 5.  Detailed BLCC Report (example) . . . . . . . . . . . . . . . .  11

Figure 6.  Cash Flow Report for File DEMO1. . . . . . . . . . . . . . . .  12

Figure 7.  Lowest LCC Analysis for Files DEMO1, DEMO2, DEMO3, and DEMO4 .  14

Figure 8.  Project Data Input Form. . . . . . . . . . . . . . . . . . . .  17

Figure 9.  Example of an ASCII File of Standard Depreciation Factors. . .  19

























                                      ix

1.  INTRODUCTION

The NIST Building Life-Cycle Cost computer program (BLCC 3.2) provides
economic analysis of proposed capital investments that are expected to reduce
long-term operating costs of buildings or building systems.  It is especially
useful for evaluating the costs and benefits of energy conservation projects
in buildings.  Two or more alternative building designs that have the same
general purpose can be evaluated to determine which has the lowest life-cycle
cost.  Economic measures, including net savings, savings-to-investment ratio,
and adjusted internal rate of return, can be calculated for any design
alternative relative to the designated base case.  BLCC runs on most IBM-PC
and compatible microcomputers with approximately 640K RAM.  No graphics
capability, math coprocessor, or other special equipment are needed.

BLCC 3.2 supersedes and incorporates both the Federal Building Life-Cycle Cost
(FBLCC) and the National Bureau of Standards Life-Cycle Cost (NBSLCC)
programs.  Table 1 lists a number of BLCC features which improve upon or
differ significantly from those programs.

Five types of LCC analyses can be performed with the BLCC program:

 (1) Federal Analysis:  Energy Conservation Projects
 (2) Federal Analysis:  Projects subject to OMB's A-94 guidelines
 (3) Private Sector:  Projects with tax analysis
 (4) Private Sector:  Owner-occupied houses (tax deductions on interest and 
                      property taxes only)
 (5) Generic LCC Analysis:  No tax analysis (e.g., state & local government)

BLCC complies with the American Society for Testing and Materials (ASTM)
standard practices for building economics, including E917 (Practice for
Measuring Life-Cycle Costs of Buildings and Building Systems), E964 (Practice
for Measuring Benefit-to-Cost and Savings-to-Investment Ratios for Buildings
and Building Systems), E1057 (Practice for Measuring Internal Rates of Return
for Investments in Buildings and Building Systems), and E1074 (Practice for
Measuring Net Benefits for Investments in Buildings and Building Systems).   
For the economic analysis of energy conservation investments in Federal
buildings, BLCC complies with NBS Handbook 135, Life-Cycle Costing Manual for
the Federal Energy Management Program.  For other investments in Federal
buildings, BLCC complies with OMB Circular A-94, "Discount Rate to Be Used in
Evaluating Time-Distributed Costs and Benefits," March 27, 1972.  

ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³    Note:  BLCC is a public domain program, not subject to copyright.       ³
³    It can be freely copied and distributed.  However, it is requested      ³
³    that attribution be given to the National Institute of Standards        ³
³                            and Technology.                                 ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ









                                      1




                                                                              
                  Table 1.  New or Enhanced BLCC Features                    
ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³ o  All program modules are contained in a single executable file.          ³
³                                                                            ³
³ o  Data files and reports can now be saved to and retrieved from any drive.³
³    Use "Setup" in the main BLCC menu to specify the target drive.          ³
³                                                                            ³
³ o  LCC computations are automatically made when the input data file is     ³
³    saved.                                                                  ³
³                                                                            ³
³ o  New cash flow report details all dollar amounts (not discounted) year-  ³
³    by-year over the entire study period.                                   ³
³                                                                            ³
³ o  Up to 100 alternative projects can be compared simultaneously to        ³
³    determine which has the lowest LCC.  Simply tag the LCC files for each  ³
³    alternative to be considered and press <Enter>.                         ³
³                                                                            ³
³ o  Only questions relevant to current analysis are displayed on screen.    ³
³                                                                            ³
³ o  Standard depreciation tables can be read from depreciation files in the ³
³    current directory to minimize data entry.                               ³
³                                                                            ³
³ o  Depreciation variables are now entered separately for replacements.     ³
³    Project capital costs can be entered as aggregate investment-related    ³
³    costs or divided into as many as six components.                        ³
³                                                                            ³
³ o  Operating and maintenance (O&M) costs, replacement costs, and depre-    ³
³    ciation data are specified separately for each component if capital     ³
³    costs are divided into components.  (Energy and mortgage costs are      ³
³    entered for the overall project and are not component specific.)        ³
³                                                                            ³
³ o  Price escalation rates for non-annually recurring O&M costs are now     ³
³    assumed to be the same as specified for annually-recurring O&M costs.   ³
³                                                                            ³
³ o  Price escalation rates for initial capital assets, O&M, and energy      ³
³    prices must include general inflation if the analysis is conducted in   ³
³    current dollars (private sector and designated generic analyses only).  ³
³    Previously all escalation rates were entered in real terms.             ³
³                                                                            ³
³ o  Up to four energy types can now be included in an input data file.      ³
³                                                                            ³
³ o  Energy usage from year to year can be assumed constant or adjusted with ³
³    annual energy usage indexes.                                            ³
³                                                                            ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ







                                      2

BLCC retrieves the U.S. Department of Energy's (DOE) projections of energy
price escalation rates from the ENCOST93.SEQ and ENCOST93.RAN files on the
disk.  These DOE projections are needed for Federal energy conservation
analyses but can be used with other LCC analyses as well.

This user's guide provides an overview of BLCC capabilities, tells the user
how to install and run it, and defines all of the variables needed to conduct
an LCC analysis.  Detail regarding the computational methodology used in BLCC
can be found in Appendix H of Comprehensive Guide for Least-Cost Energy
Decisions, by Rosalie T. Ruegg and Stephen R. Petersen, NBS Special
Publication 709, National Bureau of Standards, Gaithersburg, MD, 1987.
The BLCC program was developed at the National Institute of Standards and
Technology (formerly the National Bureau of Standards).  For further
information, write to:

             National Institute of Standards and Technology
             Applied Economics Group
             Bldg. 101, Room A415
             Gaithersburg, MD 20899





































                                      3

2.  INSTALLING AND RUNNING BLCC

BLCC can be run from a hard disk or directly from the BLCC diskette.  To
install BLCC on a hard disk, use the following steps:

 (1) Make a subdirectory called BLCC on the drive of your choice (say C:).
     To make a subdirectory called "BLCC", type "MD \BLCC" at the ready        
     prompt.  
 (2) Type "CD \BLCC" to make this the current directory.
 (3) Insert the BLCC disk into the A drive and copy all of the files from the  
     BLCC disk to the BLCC subdirectory by typing "COPY A:*.*".
 (4) Type "BLCC" at the ready prompt to start BLCC.

To run BLCC directly from the BLCC diskette, use the following steps:

 (1) Make a back-up copy of the BLCC diskette.  If you are going to run BLCC   
     in a high-density (1.2 MB) disk drive, copy BLCC to a high-density        
     diskette formatted on that drive.  

      IMPORTANT:  BLCC writes temporary and permanent files to the disk.  If
      you use the original double-density (360K) diskette in a high-density
      drive, you may destroy the original disk during the write process. 

 (2) Insert your new copy of the BLCC diskette into the A drive.
 (3) Make the A drive the current drive by typing "A:".
 (4) Type "BLCC" at the ready prompt to start BLCC.

If you run BLCC from the diskette rather than from a hard disk, space for file
storage is limited and you should therefore save your own input and output
files to a second diskette in another drive.  BLCC data entry screens and
reports will be displayed somewhat more slowly when BLCC is run directly from
the diskette.  This is because screen and report formatting files must be
accessed from the disk as data input and analysis are underway. 

The executable program, BLCC.EXE, and the following supporting files must be
available in the current directory to run BLCC:

MORT.SCR         DEPDATA.SCR        COMPARE.FLD       HELP.1
CAPDATA.SCR      ARCDATA.SCR        CASHFLOW.FLD      ENCOST93.SEQ
ENDATA.SCR       ESCDATA.SCR        PRINTDAT.FLD      ENCOST93.RAN
PROJ.SCR                            PRINTLCC.FLD      SETUP.FIL

There are also several demonstration files on the diskette for use in learning
how to use the program.  These are files:

  DEMO1.DAT    DEMO1.LCC    DEMO3.DAT    DEMO3.LCC  TABLE1.DEP
  DEMO2.DAT    DEMO2.LCC    DEMO4.DAT    DEMO4.LCC  

File README.1 provides updated information on BLCC that is not included in 
this user's guide.






                                      4

3.  CONDUCTING A BLCC ANALYSIS

3.1 The Main BLCC Menu

When you enter "BLCC" at the DOS ready prompt, the BLCC logo appears on the
screen.  Press any key to display the Main BLCC Menu, shown in figure 1.  This
menu shows the major functions of the BLCC program.  Use the up/down arrows to
highlight the desired function and press the <Enter> key.  As each function is
highlighted, a brief description of that function will be displayed at the
bottom of the screen.  Alternatively, simply press the highlighted character
for the function desired.    



                      ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                      º Create New Input Data File      º
                      º Edit Existing Input Data File   º
                      º Print Input Data File Report    º
                      º Print Detailed LCC Report       º
                      º Compute Cash-Flow Analysis      º
                      º Lowest LCC                      º
                      º Comparative Economic Analysis   º
                      º Information on BLCC             º
                      º Setup                           º
                      º Quit/Go To DOS                  º
                      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
                          Figure 1.  Main BLCC menu.



The first time you run BLCC, select the "setup" option on the master menu. 
This option allows you to define the type of monitor you are using, the
directory or subdirectory location of the data files and output files that are
created and saved while running BLCC, and the common filename of the DOE
energy price files on the BLCC disk (currently ENCOST93).  These responses are
saved to a file called SETUP.FIL in the BLCC subdirectory, and are retrieved
each time you run BLCC.  



3.2  Creating or Editing Input Data Files for a Project Alternative

To use BLCC, you must have an input data file for each alternative building or
system design to be evaluated.  The input data file for any project
alternative contains assumptions for the LCC analysis, initial costs,
operating and maintenance costs, replacement costs, energy costs, resale
value, and (where relevant) data related to taxes and financing analysis.  The
input data file is retrieved when editing the input data file, computing the
LCC of a project alternative, computing a cash flow analysis for the
alternative, or printing an input data file report.  Read section 5 of this
manual for additional information on the input data requirements and BLCC
input data file structure.  Section 8 provides definitions of all variables
requested on the data input screens.



                                      5

If you are going to create a new input data file, select "Create New Input
Data File" from the Main BLCC Menu.  If you are going to edit an existing
input data file, select "Edit Existing Input Data File" from the menu and a
list of the existing input data files in your current directory will be
displayed.  To designate the file to be edited, use the cursor keys to
highlight the desired filename, and then press <Enter> to begin.  All input
data files are automatically tagged with the filename extension ".DAT".


                                     NOTE

      You must make a separate input data file for each project
      alternative to be evaluated.  Don't try to combine several
      alternatives into a single input data file by using multiple
      components. 

      After creating and saving an initial file for one project
      alternative, it is usually easier to modify that file in the edit
      mode with data for a related alternative and save it under a new
      name than to create a new file from the beginning.   


When creating a new input data file, you must select the type of LCC analysis
to be conducted Federal energy conservation from the following:

    (1) Federal Analysis:  Energy Conservation Projects
    (2) Federal Analysis:  Projects subject to OMB's A-94 guidelines
    (3) Private Sector:  Projects with tax analysis
    (4) Private Sector:  Owner-occupied houses 
    (5) Generic LCC Analysis:  No tax analysis 

Once this analysis type is specified, and the first data entry screen is
completed, it cannot be changed.  (This is the only variable in BLCC that
cannot be changed, since it determines how the data file is set up.)

If the analysis is for Federal buildings, the LCC analysis will be conducted
in CONSTANT DOLLARS.  This requires that the discount rate and price
escalation rates be entered in real terms, i.e., net of general inflation.  If
the analysis is designated as private sector, the LCC analysis will be
conducted in CURRENT DOLLARS.  This requires that the discount rate, price
escalation rates, and mortgage interest rates (if any) be entered in nominal
terms, i.e., including general inflation.  If a generic LCC analysis is
selected, the user must designate whether this analysis will be performed in
constant or current dollars and enter all rates accordingly.  

From most screen displays in BLCC, you can back up to the previous screen by
pressing <Esc>.  From data input screens you can move backward or forward by
pressing <PgUp> or <PgDn>, respectively.  However, if the cursor is located at
a mandatory input variable, you must fill in a valid response before moving







                                      6

backward to a previous screen.  You cannot move forward to the next screen
until all required data fields are filled with valid responses.  If you are
editing an existing data file, you can move to the "save data" menu by
pressing F10 at any point.  

After completing the data entry or review, the "save data" menu is displayed,
as shown in figure 2.  Be sure to save your input data file if you intend to
use it for BLCC analysis.  You can review the data file in the edit mode if
you select this option from the menu.  If you are editing an existing file,
you can save it under a new file name or default to the old file name; in the
latter case it will replace the old file.  Filenames must follow the DOS file-
naming convention (i.e., up to eight alpha-numeric characters). 



                          Data entry is now complete.
                          ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                          º Save Input Data File    º
                          º Review Input Data File  º
                          º Exit without Saving     º
                          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
                        Figure 2.  The "Save Data" Menu.



Any input data file can be printed for documentation purposes by selecting
"Print Input Data Report" from the main BLCC menu.  As with all BLCC reports,
this report can be displayed to the screen, sent to the printer, or saved to
an ASCII file in a designated subdirectory.  Figure 3 shows the input data
file report for demonstration file DEMO1.DAT, which is included on the BLCC
disk.

For first-time users of BLCC, it is suggested that you select "Edit Existing
Input Data File" from the main menu, and then retrieve file DEMO1.DAT.  This
is one of four demonstration input data files on the BLCC diskette.  The data
in all of these demonstration files are for "generic" LCC analyses (without
income tax considerations).  Press the <PgDn> key after examining each of the
input data screens in order to familiarize yourself with the data entry
process.  Refer to section 8 for definitions of all input variables.  When
data review has been completed, the menu shown in figure 3 will be displayed. 
Save the output file under its default name (DEMO1.LCC) and select the screen
display of the summary LCC file.














                                      7

   FILE NAME: DEMO1
   FILE LAST MODIFIED ON 01-10-1991/16:29:55
   PROJECT TITLE: demo1
   COMMENT: This is a BLCC demonstration file 

   GENERAL DATA:
   -------------
   ANALYSIS TYPE: Generic LCC Analysis: No Tax Analysis
   BASE DATE FOR LCC ANALYSIS: 1990 
   STUDY PERIOD:  20 YEARS
   PLANNING/CONSTRUCTION PERIOD:  2 YEARS
   OCCUPANCY DATE: 1992
   DISCOUNT AND INTEREST RATES Real (exclusive of general inflation)
   DISCOUNT RATE:  5.0%
   
   CAPITAL ASSET COST DATA:
   ------------------------
   INITIAL COST ($)                    10,000     
   EXPECTED COMPONENT LIFE(YRS)            20     
   RESALE VALUE FACTOR                  0.00%     
   AVG PRICE ESC RATE(PLAN/CONST)       0.00%     
   AVG PRICE ESC RATE (OCCUPANCY)       0.00%     
   Escalation rates do not include general inflation
   NUMBER OF REPLACEMENTS                   1     
   
   COST-PHASING SCHEDULE BY YEAR OF CONSTRUCTION AND AT OCCUPANCY:
                                1      33.00%     
                                2      33.00%     
                      AT OCCUPANCY     34.00%     
   
   
     REPLACEMENTS TO CAPITAL ASSETS:
     -------------------------------
   
     REPLACEMENT NUMBER                    1    
     YEAR OF REPLACEMENT                  10    
     COST OF REPLACEMENT ($)           5,000    
     EXPECTED REPL. LIFE (YRS)            10    
     RESALE VALUE FACTOR               0.00%    
   
   
     OPERATING AND MAINTENANCE COST DATA:
     ------------------------------------
     ANNUAL RECUR O&M COST ($):   1,000
     ESCALATION RATE FOR O&M:     0.00%
     Escalation rates do not include general inflation


     NON-AN RECURRING O&M COSTS ($):
      YR   AMOUNT 
      10   $1,000 
      20   $1,000 
   ____________________________________________________________________
 
            Figure 3.  Input Data File Report for DEMO1

                                      8

ENERGY COST DATA:
-----------------
NUMBER OF ENERGY TYPES = 1 
User entered energy price escalation rates used with Energy Type(s) 1 

                             TYPE 1   
ENERGY TYPE:              Electricity
AVG ANNUAL CONSUMPTION:        100,000 
UNITS:                         KWH   
PRICE PER UNIT ($):            0.10  
ANNUAL DEMAND CHARGE ($):      0.00  
ESCALATION RATES BY YEAR:   Escalation rates do not include general inflation

       1990        2.00                       2000        2.00
       1991        2.00                       2001        2.00
       1992        2.00                       2002        2.00
       1993        2.00                       2003        2.00
       1994        2.00                       2004        2.00
       1995        2.00                       2005        2.00
       1996        2.00                       2006        2.00
       1997        2.00                       2007        2.00
       1998        2.00                       2008        2.00
       1999        2.00                       2009        2.00

ENERGY TYPE:  Electricity
ENERGY USE INDEXES BY YEAR:

       1992      100.00                       2001      100.00
       1993      100.00                       2002      110.00
       1994      100.00                       2003      110.00
       1995      100.00                       2004      110.00
       1996      100.00                       2005      110.00
       1997      100.00                       2006      110.00
       1998      100.00                       2007      110.00
       1999      100.00                       2008      110.00
       2000      100.00                       2009      110.00
    ________________________________________________________________

       Figure 3.  Input Data File Report for DEMO1 (continued).

















                                      9

3.3  Calculating Life-Cycle Costs and Cash-Flow Analyses

At the time that a new or existing input data file is saved, the corresponding
LCC computations are automatically performed and saved in an LCC output file. 
The default filename for the LCC output file is the same as that assigned to
the input data file, with the filename extension ".LCC" automatically tagged. 
You can change the filename to any other valid DOS filename (up to eight
alpha-numeric characters) if you wish, but it is usually easier to keep track
of pairs of corresponding input and output files when they have the same
filename.  This LCC output file is retrieved when printing a detailed LCC
report, conducting comparative LCC analyses, or determining which of several
mutually-exclusive project alternatives has the lowest LCC.  

At the time that the LCC computations are performed, a summary report of the
LCC computations is generated.  This summary can be printed to the screen,
printer, or a disk file (for later retrieval).  An example of this summary
file is shown in figure 4 for the DEMO1 example file.  To regenerate the
summary report at any time, retrieve the corresponding input data file in the
file edit mode and resave the file.




ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³                                          PRESENT VALUE      ANNUAL VALUE  ³
³  INITIAL COST (AT OCCUPANCY)                   $9,527              $764   ³
³  ANNUALLY RECURRING O&M COSTS                 $10,603              $851   ³
³  NON-AN. RECURRING O&M COSTS                     $557               $45   ³
³  ENERGY COSTS                                $135,406           $10,865   ³
³  REPLACEMENT COSTS                             $2,784              $223   ³
³  LESS: REMAINING VALUE                  (          $0)    (          $0)  ³
³ --------------------------------------------------------------------------³
³  TOTAL LCC                                   $158,876           $12,749   ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
                     Figure 4.  BLCC Summary for DEMO1.




To generate a detailed LCC analysis for a project alternative once its input
data file and LCC output files have been saved, select "Print Detailed LCC
Report" from the main menu and use the cursor keys to highlight the LCC output
file to be used for this report.  An example of the detailed BLCC report for
the DEMO1 example file is shown in figure 5.

A year-by-year cash flow report can also be generated and printed from the
input data file by selecting "Compute Cash Flow Analysis" from the main menu. 
An example of the cash flow report for file DEMO1 is shown in figure 6.  For
LCC analyses which require depreciation calculations, the depreciation
schedules used in the analyses are included at the end of the cash flow
report.  





                                      10
                  
                                                                        
              PART I - INITIAL ASSUMPTIONS AND COST DATA                      
                                                                              
     Project name: demo1                                                      
     Run date:01-10-1991 16:35:18                                             
     Comment: This is a BLCC demonstration file                                
     Input data file: DEMO1.BCF, last modified: 01-10-1991/16:29:55           
     LCC output file: DEMO1.LCC, created: 01-10-1991 16:30:03                 
     Study period:        20 years (1990 through 2009)                        
     Plan/constr. period:  2 years (1990 through 1991)                        
     Occupancy period:    18 years (1992 through 2009)                        
     Discount rate:   5.0%  Real (exclusive of general inflation)             
     Run type: Generic LCC Analysis: No Tax Analysis                          
     BLCC uses end-of-year discounting convention                             
                                                                              
          INITIAL CAPITAL INVESTMENT COSTS (NOT DISCOUNTED)                   
   (ADJUSTED FOR PRICE CHANGES DURING PLAN/CONST. PERIOD, IF ANY)             
 ---------------------------------------------------------------------        
                     YEAR    COST PHASING    YEARLY COST      TOTAL COST      
                     ----    ------------   -------------   -------------     
                     1990        33.0%           $3,300                       
                     1991        33.0%           $3,300                       
  AT OCCUPANCY:      1992        34.0%           $3,400                       
  TOTAL INITIAL COST (ACTUAL)                                    $10,000      
                                                                              
                    ENERGY-RELATED COSTS                                      
 ---------------------------------------------------------------------        
      ENERGY      UNITS/     PRICE     DEMAND      TOTAL                      
       TYPE        YEAR     ($/UNIT)    COST     P.V. COST                    
    -----------  --------  ---------  -------    ---------                    
    Electricity   100,000     $0.10        $0     $135,406                    
                                                                              
                                                                              
                     PART II  -  LIFE-CYCLE COST ANALYSIS                     
                                                                              
                                           PRESENT VALUE      ANNUAL VALUE    
                                          (1990 DOLLARS)     (1990 DOLLARS)   
                                          --------------     --------------   
 A. CASH REQUIREMENTS AS OF OCCUPANCY                                         
    DURING CONSTRUCTION                           $6,443               $517   
    AT OCCUPANCY                                  $3,084               $247   
                                            ------------       ------------   
     SUBTOTAL                                     $9,527               $764   
 C. OPERATING, MAINTENANCE & RELATED COSTS:                                   
    ANNUALLY RECURRING COSTS (NON-ENERGY)        $10,603               $851   
    NON-ANNUALLY RECURRING COSTS                    $557                $45   
    ENERGY COSTS                                $135,406            $10,865   
                                              ------------       ------------ 
     SUBTOTAL                                   $146,565            $11,761   
 D. REPLACEMENTS TO INITIAL CAPITAL ASSETS        $2,784               $223   
 F. REMAINING VALUE AT END OF OCCUPANCY    (          $0)     (          $0)  
 G. TOTAL LIFE-CYCLE PROJECT COST               $158,876            $12,749   
______________________________________________________________________________

               Figure 5.  Detailed BLCC report (example).                       
                            
                                      11



      PROJECT NAME: demo1
      COMMENT: This is a BLCC demonstration file
      RUN DATE: 01-11-1991 08:50:55
      INPUT DATA FILE: DEMO1.BCF, LAST MODIFIED 
      STUDY PERIOD:        20 YEARS (1990 THROUGH 2009)
      PLAN/CONSTR. PERIOD:  2 YEARS (1990 THROUGH 1991)
      OCCUPANCY PERIOD:    18 YEARS (1992 THROUGH 2009)
      ANALYSIS TYPE: Generic LCC Analysis: No Tax Analysis

                          INITIAL CAPITAL COSTS 
     (AS INCURRED DURING PLANNING/CONSTRUCTION PERIOD AND AT OCCUPANCY)

                                           TOTAL
                                         (BY YEAR)
                                YEAR     ---------
                                1990          3300
                                1991          3300
                                1992          3400
                              TOTAL:     ---------
                                             10000

           CAPITAL INVESTMENT COSTS

                 INIT CAPITAL   CAPITAL     CAPITAL    TOTAL CAP.
          YEAR    INVESTMENT  REPLACEMTS    DISPOSAL   INVESTMENT
          1990         3,300           0           0        3,300
          1991         3,300           0           0        3,300
          1992         3,400           0           0        3,400
          1993             0           0           0            0
          1994             0           0           0            0
          1995             0           0           0            0
          1996             0           0           0            0
          1997             0           0           0            0
          1998             0           0           0            0
          1999             0           0           0            0
          2000             0           0           0            0
          2001             0       5,000           0        5,000
          2002             0           0           0            0
          2003             0           0           0            0
          2004             0           0           0            0
          2005             0           0           0            0
          2006             0           0           0            0
          2007             0           0           0            0
          2008             0           0           0            0
          2009             0           0           0            0
          TOTAL       10,000       5,000           0       15,000
       _____________________________________________________________
   
                 Figure 6.  Cash flow report for file DEMO1.         





                                      12

              OPERATING-RELATED COSTS DURING OCCUPANCY 
   
       YEAR   --OPERATING AND MAINTENANCE COSTS---      TOTAL
              AN RECURRING  NON-AN REC      ENERGY   OPER. COST
       ----   ------------  ----------    --------   ----------
       1992          1,000           0      10,612       11,612 
       1993          1,000           0      10,824       11,824 
       1994          1,000           0      11,041       12,041 
       1995          1,000           0      11,262       12,262 
       1996          1,000           0      11,487       12,487 
       1997          1,000           0      11,717       12,717 
       1998          1,000           0      11,951       12,951 
       1999          1,000           0      12,190       13,190 
       2000          1,000           0      12,434       13,434 
       2001          1,000       1,000      12,682       14,682 
       2002          1,000           0      14,230       15,230 
       2003          1,000           0      14,514       15,514 
       2004          1,000           0      14,805       15,805 
       2005          1,000           0      15,101       16,101 
       2006          1,000           0      15,403       16,403 
       2007          1,000           0      15,711       16,711 
       2008          1,000           0      16,025       17,025 
       2009          1,000           0      16,345       17,345 
       TOTAL        18,000       1,000     238,332      257,332 


                        SUM OF ALL CASH FLOWS
   
                       CAPITAL   OPERATING        TOTAL
             YEAR    INVESTMENT    COSTS           COST
             ----    ----------  ----------   ---------
             1990         3,300           0       3,300 
             1991         3,300           0       3,300 
             1992         3,400      11,612      15,012 
             1993             0      11,824      11,824 
             1994             0      12,041      12,041 
             1995             0      12,262      12,262 
             1996             0      12,487      12,487 
             1997             0      12,717      12,717 
             1998             0      12,951      12,951 
             1999             0      13,190      13,190 
             2000             0      13,434      13,434 
             2001         5,000      14,682      19,682 
             2002             0      15,230      15,230 
             2003             0      15,514      15,514 
             2004             0      15,805      15,805 
             2005             0      16,101      16,101 
             2006             0      16,403      16,403 
             2007             0      16,711      16,711 
             2008             0      17,025      17,025 
             2009             0      17,345      17,345 
             TOTAL       15,000     257,332     272,332 
        ______________________________________________________

        Figure 6.  Cash flow report for file DEMO1 (continued)

                                      13

3.4  Lowest LCC and Comparative Economic Analysis

After an LCC analysis has been computed for two or more mutually-exclusive
project alternatives, the life-cycle cost calculations for each alternative
can be compared to determine which has the lowest LCC.  Select "Find Lowest
LCC" from the main menu.  Highlight and tag the LCC output file for each
alternative to be included in the analysis.  Up to 100 files can be tagged
for a lowest LCC analysis.  The alternatives will be displayed in order of
increasing initial cost, and the alternative with the lowest LCC will be
flagged.  An example of the lowest LCC calculation for files DEM01, DEMO2,
DEMO3, and DEMO4 is shown in figure 7.  

Note that for a comparative analysis to be performed, alternatives must have
been evaluated over the same study period and planning/construction period (if
any), using the same discount rate and the same analysis type (e.g., Federal
energy conservation projects, private sector taxable projects).  In general,
comparison of life-cycle costs is only meaningful when these costs are
representative of mutually-exclusive design alternatives in the same operating
context.  For example, the comparison of two alternative office building
designs with different shapes and orientation (and thus having different
energy consumption requirements), but with the same amount of usable space and
the same potential rental income, is a legitimate use of LCC analysis. 
Comparison of the life-cycle cost of an office building with that of a
hospital is not likely to be useful in a decision-making context.



         COMPARATIVE PRESENT-VALUE COSTS OF ALTERNATIVE PROJECTS  
        (Shown in ascending order of initial cost, * = lowest LCC)

           PROJECT          LCC        INITIAL      LIFE CYCLE
             NAME         FILENAME    COST (PV)      COST (PV)
         -------------    --------   -----------   ------------
         demo1            DEMO1           $9,527       $158,876
         demo2            DEMO2          $10,479       $145,451
         demo3            DEMO3          $11,432       $139,382*
         demo4            DEMO4          $14,290       $139,532
 _______________________________________________________________________

 Figure 7.  Lowest LCC analysis for files DEMO1, DEMO2, DEMO3, and DEMO4.


A comprehensive comparative economic analysis of any two project alternatives
can be performed by selecting the "Comparative Economic Analysis" option on
the main menu.  Tag the two LCC output files corresponding to the project
alternatives to be compared.  The project alternative with the lower initial
cost is automatically designated as the base case; the project alternative
with the higher initial cost is designated as the alternative case for which
the economic measures are computed.  A summary of the major cost elements (in







                                      14

present-value dollars) for the two alternatives will be displayed side by
side, and the difference shown.  The net savings, savings-to-investment ratio
(SIR), and adjusted internal rate of return (AIRR) are shown for the
alternative case relative to the designated base case.  

In general, if a project alternative is to be considered cost effective on a
life-cycle cost basis, it must have a lower LCC than the base case, positive
net savings, an SIR greater than 1.0, and an AIRR greater than the opportunity
cost of capital (i.e., the discount rate).  These are all consistent measures
of economic analysis; that is, they will all show that a given project
alternative is either cost effective or not cost effective relative to the
specified base case.

If a single project is to be evaluated with BLCC to determine whether or not
it is economically justified, it must be compared against a "do-nothing" base
case.  An input data file must be created for the do-nothing case as well as
for the project.  This input data file will not generally include initial
costs, but will include replacement costs, O&M costs, and energy costs
reflecting the existing (before capital improvement) situation.  The same base
year, study period, and discount rate must be used for both cases.  For
example, to evaluate the cost effectiveness of storm windows added to an
existing house, a separate input data file is required for the base case (no
storm windows) without capital investment costs and with higher annual energy
costs over the period of analysis than the storm window alternative.  
































                                      15

4.  REPORTS GENERATED BY BLCC

Six different type of reports can be generated by the BLCC program.  These
reports can be displayed directly to the screen, sent to the printer, or saved
to a disk file in the directory designated in the "Setup" option.  Table 2
shows the six report types and the corresponding filename extension
automatically tagged to the file when the reports are saved to a disk file.  



                     Table 2.  Reports Generated by BLCC 
              ______________________________________________

                                             Filename      
                     Report Types            Extension     
              ______________________________________________

                     Input Data File report   .DTS         
                     Summary LCC report       .SUM         
                     Detailed LCC report      .RPT         
                     Cashflow report          .CFR         
                     Comparative LCC analysis .CMP         
                     Lowest LCC report        .LOW         
              ______________________________________________



The longer reports generated by BLCC, including the input data summary report,
detailed LCC report, cash flow report, and comparative economic analysis
report, do not have page breaks for printing purposes.  Instead, the reports
are printed continuously, assuming fan-fold paper output.  If you wish to
print these reports in presentation quality, save them to the disk and
retrieve them into a word processor as a text file.  You can then format them
for your specific printing requirements.  A form-feed control character is
sent to the printer at the end of each report to force a new page at that
point.




















                                      16

5.  GENERALIZED INPUT DATA FILE STRUCTURE FOR BLCC

When creating or modifying an input data file for life-cycle cost analysis,
data input is accomplished by choosing among options from a menu or by
entering data into a "form" displayed on the screen.  Figure 8 shows an
example of such a form for the general project data.



                                 PROJECT DATA:                             
         ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»     
         º Project title: Storm windows                              º     
         º Base year (1990-2000): 1991                               º     
         º Study period (2-60): 20 Years                             º     
         º Planning/Construction period (0-9): 0 Year(s)             º     
         º Discount rate:  7.00%                                     º     
         º Comment: This run is for demonstration purposes only      º     
         ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼     
                     Figure 8.  Project data input form.


Input data is generally requested in the order shown in table 3.  Definitions
for each of the variables requested while creating or modifying an input data
file are provided in section 8 of this User's Guide.  If your response is
above or below the allowable range, the allowable range will be displayed at
the bottom of the screen.  If the input requested is mandatory, you will not
be allowed to continue until a valid response has been entered.

The project type and the inflation treatment can be specified only when 
creating an input data file.  These two variables are fixed.  That is, they
cannot be changed in the file edit mode.  

Note that percentages are entered as percentages, not as decimals (e.g., 7.0,
not 0.07).  Do not include signs such as $ or % with your entries.  Do not use
commas for marking off thousands or millions.





















                                      17


                                                                             
                  Table 3.  Input Data File Structure                     
_____________________________________________________________________________  
                                                                           
   Fixed Data:                                                                
     Type of Analysis                                                         
     Inflation Treatment (Constant dollars or Current dollars)                
                                                                              
   Project-Level Data:                                                        
     General LCC Assumptions                                                  
     Tax-Related Data (private sector only)                                   
                                                                              
   Capital-Asset Data (may be divided into six major components):              

     Initial Cost Data                                                        
     Cost Phasing (if Planning/Construction period specified)                 
     Depreciation Data (project with full tax analysis only)                  
     Annually Recurring O&M Costs                                             
     Non-annually Recurring O&M Costs                                         
     Replacements:                                                            
       Timing and Cost                                                        
       Depreciation Data (project with full tax analysis only)                
                                                                              
   Energy-related Data:                                                       
     Types, Annual Usage, and Cost                                            
     Escalation Rate Projections                                              
     Energy Use Indexes                                                       
                                                                              
   Mortgage Data (non-Federal only):                                          
     Temporary Construction Financing (if Planning/Construction period        
           is specified)                                                      
     Permanent Financing at Occupancy                                         
_____________________________________________________________________________  
                                                                           
                                                                              
  



















                                      18

6.  STANDARD DEPRECIATION TABLES

When creating or modifying an input data file that requires depreciation data,
several types of depreciation calculations can be specified, including
straight-line, sum-of-years digits, accelerated depreciation, and standard
table computations.  If the standard table option is specified, the
depreciation computations are based on depreciation factors retrieved from a
disk file previously prepared for this purpose.  This allows you to access
standard depreciation tables without having to re-enter them for each
component and each project.  (IRS publishes such tables for different classes
of depreciable assets.)  Standard depreciation tables can be used repeatedly
without typing in lengthy schedules for each component in each project.  The
same tables can be used with both initial capital components and capital
replacements.

Before running BLCC, you must create a file of depreciation factors using a
text editor (or word processor in the text mode) and save it as an ASCII file. 
Files with a depreciation factors must have the filename extension ".DEP".  
This file must be accessible from the BLCC directory (not the data file
subdirectory specified in the "setup" option).  

Depreciation tables have the following format:
            n
            factor 1
            factor 2
              .
              .
              .
            factor n

      where:   
            n = number of factors in file (i.e., the number of years over 
                which the asset is to be depreciated), and
     factor i = percent of asset cost allowed as depreciation in year i, i = 1 
                to n, in decimal form (e.g., 10% = .1).  The sum of these      
                factors must equal 1.0.

Figure 9 shows an example of such a file.  This file contains the number of
years that an asset is to be depreciated and the percent (in decimal terms) of
its depreciation basis that is allowed as depreciation in each of those years. 
Separate tables must be created for each depreciation schedule to be
retrieved.  Note:  the actual depreciation schedules used in the BLCC analysis
are printed at the end of the cash flow report for any project.


                                     5 
                                    .2 
                                    .2 
                                    .2 
                                    .2 
                                    .2 
    _____________________________________________________________________

    Figure 9.  Example of an ASCII file of standard depreciation factors.


                                      19

7.  COMPUTATIONAL CONVENTIONS USED IN BLCC

All time periods in BLCC are assumed to be integer (whole) years, including
the study period, planning/construction period, and occupancy period.  Initial
costs and property taxes (if any) are assumed to be incurred at the beginning
of the designated year.  All other costs are assumed to occur at the end of
the designated year and are discounted from that time, with one exception:
mortgage payments with more than one payment per year are assumed to occur at
times which correspond to the number of payments per year designated. (That
is, if 12 payments per year are designated for a mortgage loan, a mortgage
payment is assumed to be made at the end of each month in the year and each
payment is discounted from that time.)  All tax savings (if any) are assumed
to occur at the end of the designated year, regardless of when that savings
was generated.  

Extensive documentation of the computational methods used in BLCC can be found
in Appendix H of Comprehensive Guide for Least-Cost Energy Decisions, by
Rosalie T. Ruegg and Stephen R. Petersen, NBS Special Publication 709,
National Bureau of Standards, Gaithersburg, MD, 1987.





































                                      20

8.  DEFINITIONS AND ACCEPTABLE RANGES OF INPUT VARIABLES 
    USED IN THE BLCC PROGRAM

General LCC assumptions:

   o  Type of analysis--Choose the type most appropriate to your project:

      (1) Federal Analysis:  FEMP (Federal Energy Management Program) projects 
          related to energy conservation in federal facilities.
      (2) Federal Analysis:  OMB A-94 projects (most other federal government  
          construction projects, but not water resource projects).
      (3) Private Sector:  Taxable projects such as commercial and industrial  
          buildings and residential rental properties.
      (4) Private Sector:  Owner-occupied houses (where only mortgage interest 
          and property taxes are tax-deductible from federal and state income  
          tax).
      (5) Generic LCC Analysis:  LCC projects which do not need to conform to  
          Federal rules and do not require income tax analysis.

   o  Exclude Inflation or Include Inflation (Generic LCC analysis only)--
      If the analysis is to be performed in constant dollars, the discount
      rate, mortgage interest rates, and all price escalation rates must be
      entered in real terms (i.e., excluding general inflation).  If the
      analysis is to be performed in current dollars, these rates must be
      entered in nominal terms (i.e., including general inflation).  For
      Federal projects, the analysis is always performed in constant dollars
      and thus these rates are entered in real terms.  For private sector
      analyses (taxable and owner-occupied house), the analysis is always
      performed in current dollars and thus these rates are entered in nominal
      terms.  Note:  Regardless of whether the analysis is performed in
      constant or current dollars, all cost data must be entered in base-year
      dollars.  


Project-level Data:

  o   Project Title--The user may supply any name desired to identify the
      project to be evaluated.  Up to 12 characters may be used.  A distinct
      project title should be assigned to each project to be evaluated since
      the comparative analysis will list the costs of each project under this
      title.

  o   Base Year--The year in which the study period begins.  This must be an
      integer between 1990 and 2000.  All cost data must be entered in
      constant dollars as of this date.  All costs will be discounted back to
      this date.

  o   Study Period (Years)--The number of years over which project-related
      costs will be summed.  The Study Period includes both the planning/
      construction period, if any, and the Occupancy Period.  (Integer between
      2 and 60)  





                                      21

  o   Planning/Construction Period--The number of years from the beginning of
      the Study Period to the beginning of occupancy.  Initial costs can be
      phased in during the Planning/Construction Period, but operating and
      maintenance costs (including energy), replacement costs, and
      appreciation (if any), are not incurred during this period.  (Integer
      between 0 and 9)

  o   Discount Rate (%)--The discount rate is used to convert cash flows
      occurring at different points in time to present value (as of the base
      date) and its equivalent annual value.  Use the nominal (i.e., inclusive
      of inflation), after-tax discount rate for private sector projects or a
      Generic LCC analysis designated as using current dollars.  Use a real
      (i.e., exclusive of inflation) discount rate for Federal projects and
      Generic LCC analyses designated as using constant dollars.  (0 to 25)

  o   Comment--Additional information to identify this project can be included
            in the data file and printed out with the various BLCC reports. 
            Optional.  (Up to 50 characters) 


Tax-related Data (Private sector analyses only):

  o   Marginal Federal Income Tax Rate (%)--The Federal income tax rate
      applied to the last dollar of income to the investor.  (0 to 50)

  o   Marginal State Income Tax Rate (%)--The state tax rate applied to the
      last dollar of income to the investor.  If income taxes are imposed by
      local jurisdiction, this can be included in the analysis by replacing
      the state tax rate with a composite state and local rate.  Note:  BLCC
      computes a composite income tax rate from the marginal Federal and state
      income tax rates, based on the assumption that state and local income
      taxes are deductible from Federal income tax.  All tax deductions are
      assumed to be the same for both Federal and state taxes.  (0 to 20)

o     Property Tax Rate (Nominal, %)--This is the quoted property tax rate for
      this type of property in this location.  Note that the property tax rate
      is assumed to be the same for all capital components, but that the
      percentage of each component that is subject to this property tax rate
      (i.e., the assessment rate) can be specified separately for each
      component.  (0 to 20)

o     Capital Gains Adjustment Factor (%)--Use 100 percent if there is no
      capital gains preference.  At the end of the study period, if the resale
      value of the project is greater than its initial cost, the difference is
      assumed to be taxable as long-term capital gains.  The effective capital
      gains tax may be lower than the ordinary income tax rate (although this
      was not the case at the time of this writing.)  The Capital Gains
      Adjustment Factor adjusts the ordinary income tax rate to an effective
      capital gains tax rate.  (For example, in the early 1980's this factor  
      was 40 percent for individuals; that is, the marginal tax rate of the
      individual was multiplied by 40 percent to arrive at an effective
      capital gains tax rate.)  Note:  For owner-occupied houses, the capital




                                      22

      gains tax is usually deferred indefinitely if another house is purchased
      within a specified amount of time.  To defer capital gains taxes
      indefinitely, enter a zero for this factor.  (0 to 100)

  o   Depreciation Recapture Code--At the end of the study period, if the
      resale value of the project is greater than its depreciated book value
      (i.e., the remaining undepreciated portion of its actual cost at
      occupancy), the difference (up to the total amount of depreciation
      claimed) may be subject to a depreciation recapture tax.  This
      depreciation recapture tax can be computed in one of several different
      ways, as designated by the following input codes:
            
            0--no depreciation recapture
            1--recapture as capital gain
            2--recapture as ordinary income
            3--depreciation calculated at straight-line rates, recaptured as   
            capital gains; any excess depreciation (due to accelerated
            calculation procedures), recaptured as ordinary income

      Note:  IRS rules for recapture vary with the type of property involved,
      method of depreciation used, and date of asset acquisition.  If there is
      no capital gains preference (i.e., the capital gains adjustment factor
      is 100 percent), codes 1,2, and 3 all produce the same results.

  o   Depreciation Basis Adjustment Factor (%)--If an investment (or energy)
      tax credit is claimed for any component, this may reduce the original
      cost basis for depreciation calculations by a specific percentage of the
      tax credit.  For example, if one half of the tax credit must be deducted
      from the original cost basis for depreciation, enter 50.  If no
      investment tax credit is to be claimed for capital assets (as described
      below), enter 0.  (0 to 100)


Capital Asset data:

  o   Capital components--The user must specify whether the capital assets of
      this project will be subdivided into specific components or systems
      (e.g., land, building, HVAC equipment, etc.).  If the capital assets are
      to be subdivided, initial costs, operating and maintenance costs (O&M),
      replacement costs, and depreciation (if any) must be assigned to the
      corresponding component.  In general, for analyses which include
      depreciation calculations, capital assets should be differentiated by
      the type and length of depreciation schedule that is to be used.  (For
      example, land, which cannot be depreciated, should be entered as a
      separate component.)  Price escalation rates for initial costs and O&M
      costs are specified separately for each component.  Thus, if these rates
      are expected to differ significantly among the various capital assets of
      the project, these assets can be divided into separate components.  Up
      to six capital components can be specified for any project.  (Integer
      from 1 to 6) 






                                      23

      (Note:  Energy and mortgage financing costs are assigned to the overall
      project and not to specific components.)


  o   Component names--if the capital assets are to be subdivided into
      components, a name must be assigned to each component before data entry
      for those components can begin.  Components can also be added or deleted
      at this point.  (Names can have up to 12 characters.)


      The following variables are to be specified for each component or for
      the overall project if not subdivided into components:

  o   Initial Cost ($)--The total installed cost of the component, unadjusted
      for price escalation during construction.  If the Planning/Construction
      Period is one year or more, the "Cost-Phasing Schedule" and the "Average
      Price Escalation Rate During the Planning/Construction Period"
      (discussed below) are used to determine the actual component cost
      incurred in each year of the Planning/Construction Period and at
      occupancy.  (0-99999999)

  o   Expected Life (Years)--The useful life of the component (in years)
      anticipated by the investor.  This is intended to be a realistic
      assessment of the component life, independent of the depreciation life
      assigned to the component for income tax purposes, if any. (Integer
      between 2 and 100)

  o   Resale Value Factor (% of initial cost)--This is the percent of the
      initial component cost which remains at the end of the study period (or
      at the end of the component life, if this comes first), unadjusted for
      price escalation.  This factor is intended to reflect a decrease in
      value due to wear, deterioration, or obsolescence, but not inflation or
      price escalation.  In computing the actual resale value of the
      component, BLCC uses the Average Price Escalation Rate During Occupancy
      (see below) to adjust for price changes during the Study Period.  The
      resale value is treated as a negative cost element in the life-cycle
      cost equation even if the investor does not intend to dispose of the
      property at the end of the Study Period.  

  o   Average Price Escalation Rate During the Planning/Construction Period
      (%)--This is the average annual rate at which the cost of this component
      increases during the Planning/Construction Period, if any.  No
      adjustment is made to component costs phased in during the first year of
      construction since component costs are assumed to be incurred on the
      first day of the assigned year.  All component costs phased in after the
      first year of the Planning/Construction Period are adjusted using this
      rate.  If the study is performed in constant dollars (Federal analyses
      and designated Generic LCC analyses), this rate should not include
      general inflation.  (-5 to 20)







                                      24

  o  Average Price Escalation Rate During Occupancy (%)--This is the average
      annual rate at which the cost of this type of capital component is
      expected to change during the occupancy period.  This variable is used
      in calculating replacement costs for this component, and in establishing
      the resale value of this component after adjustments for wear,
      deterioration, and obsolescence.  If the study is performed in constant
      dollars (Federal analyses and designated Generic LCC analyses), this
      rate should not include general inflation.  (-5 to 20)

  o   Tax Credit Factor (% of initial cost)--This factor represents the
      percent of the initial cost of the component (or project, if no
      components are specified) which can be claimed as an income tax credit
      in the first year of occupancy.  (If the tax credit is taken, the
      depreciation basis may need to be reduced by some percentage of this
      credit.  The percentage of the tax credit by which the depreciation
      basis is to be reduced can be specified using the Depreciation Basis
      Adjustment Factor, described above.)  (0 to 20)

  o   Property Tax Assessment Factor (%)--This is the percentage of the
      initial component cost to which the Property Tax Rate specified above
      for the project is applied in order to calculate the actual property tax
      obligation.  Property taxes are calculated only during occupancy years,
      and are assumed to be paid at the beginning of each year, based on the
      assessed value of that component at that time.  In computing the
      assessed value of the component for each year of occupancy, the initial
      component cost is decreased annually--in straight-line fashion--to its
      estimated resale value (unadjusted for price changes) at the end of the
      study period (or at the end of the component life, if this occurs before
      the end of the study period).  These values are then adjusted for price
      changes using the "Average Price Escalation Rate During Occupancy," and
      then adjusted by the Property Tax Assessment Factor to determine the
      amount to which the Property Tax Rate is applied.  Note that this is
      necessarily an approximation technique; the actual assessment depends on
      the taxing authority's own assessment methods.  (0 to 100)


  o   Depreciation Method Code--The method to be used for depreciating each
      capital component is determined by the following codes:

            0--no depreciation calculated
            1--straight line
            2--declining balance (accelerated)
            3--sum of years digits
            4--depreciation table

  o   Cost phasing by year--if a Planning/Construction Period is used, a
      specified percentage of initial capital costs can be allocated to each
      year and to the first day of occupancy.  If these factors do not add up
      to 100 percent, the unallocated percentage will automatically be
      assigned to the first day of occupancy.  (0 to 100 for each year, with
      total for all years = 100)





                                      25

Depreciation data when Depreciation Method Code 1, 2, or 3 is specified (See
section 6 of this report for information regarding the depreciation table
method):

  o   Depreciation Life (Years)--The number of years over which the component
      will be depreciated.  (2-45)

  o   Depreciation Acceleration Rate (%)--If Depreciation Method Code 2, the
      declining balance method, is selected, the Acceleration Rate must be
      specified.  For example, for 125 percent declining balance, enter 125. 
      (100 to 300)

  o   Salvage Value Factor (% of initial cost)--If the IRS depreciation rules
      require that salvage value be deducted from the initial asset cost
      before calculating depreciation, a Salvage Value Factor must be
      specified.  Otherwise enter zero.  The Salvage Value Factor is specified
      as a percentage of the initial component cost.  Negative values are not
      allowed.  Note:  The Salvage Value Factor is specified only for
      depreciation purposes here; this is not the same as the Resale Value
      Factor.  (0 to 50)

  o   Additional First Year Depreciation Factor--If additional first year
      depreciation is allowed, enter this factor as a percent of the actual
      component cost.  Additional first year depreciation is deducted from the
      original depreciation basis before the depreciation schedule is set up
      for this component and added to the first year of the depreciation
      schedule.  (0 to 20)


Operating and Maintenance (O&M) Costs (other than energy costs) are specified
for each component if capital assets are subdivided into components. 
Otherwise these costs are allocated to the overall project.  There are two
types of O&M costs, annually recurring costs (ARCs) and non-annually recurring
costs (NARCs): 

  (1) Annually-recurring O&M costs occur in substantially the same amount 
      every year or change at a relatively constant rate over the study period
      (in base year dollars).  Two data entries are needed:

      o     Amount (in base year dollars).

      o     Average Annual Rate of Increase--This is the average annual rate
            at which both annually-recurring O&M costs and non-annually-
            recurring O&M costs are expected to change over the study period. 
            If Federal analysis or Generic LCC analysis in constant dollar
            terms, enter real rate (net of general inflation); otherwise enter
            nominal rate (including general inflation).  (-5 to 20)









                                      26

  (2) Non-annually-recurring O&M costs do not follow a regular pattern.  These
      costs must be specified individually for each occurrence.  (More than
      one occurrence per year is permitted though all occurrences within a
      year are assumed to occur at the end of that year.)  For each NARC, the
      following pair of data entries must be specified:
      
      o     Year of Occurrence--The year during occupancy in which the NARC  
            is incurred (e.g., 5 for the fifth year).  If the year entered is
            beyond the end of the study period, the NARC will be ignored.  (1
            to 60)

      o      Amount (in base-year dollars).


Capital Replacements:

      o     Year of Replacement--The year during occupancy in which the
            replacement cost is incurred (e.g., 5 for the fifth year).  If the
            year entered is beyond the end of the study period, the
            replacement cost will be ignored.  (2 to 60)

      o     Initial Cost of Replacement--The installed cost of the replacement
            (in base year dollars).  The actual replacement cost will be
            calculated using the Average Price Escalation Rate During the
            Planning/Construction Period (if any) and the Average Price
            Escalation Rate During Occupancy assigned to the original
            component.

      o     Expected Life (Years)--The useful life of the replacement (in
            years) anticipated by the investor.  (2 to 99)

      o     Resale Value Factor (% of initial replacement cost)--This is the
            percent of the initial replacement cost remaining at the end of
            the study period (or at the end of the expected useful life of the
            replacement, whichever is less) in base year dollars, i.e.,
            unadjusted for inflation or price escalation.  The Average Price
            Escalation Rate During the Planning/Construction Period (if any)
            and the Average Price Escalation Rate During Occupancy are used
            with this factor to compute the actual resale value.  (0-200)

      o     Property Tax Assessment Rate (%)--The percent of the initial
            replacement cost to which the nominal property tax rate will be
            applied.  (0 to 100)

      o     Depreciation Method Code--See Depreciation Codes for capital
            assets above.  The same codes and depreciation tables are used for
            replacements. (0 to 4)









                                      27

Energy Costs

Annual energy costs are treated like annually recurring costs except that up
to four individual energy types may be specified and the rate of price change
can vary during the study period.  In addition, annual consumption of each
energy type can vary from year to year during occupancy, as a function of the
energy use index for that year.  (Energy costs are not calculated during the
Planning/Construction Period, if any.)  Annual energy costs consist of direct
energy costs (i.e., those costs computed directly from annual energy
consumption and corresponding unit prices) and indirect costs (e.g., demand-
related or other energy costs that cannot be computed directly from the amount
of annual energy consumption).


Energy-related variables are entered as follows:

  o   Energy Type Code (designated units)--choose one:

      1--Electricity (kWh)
      2--Distillate Fuel Oil (gallons)
      3--Residual Fuel Oil (gallons)
      4--Natural Gas (therms, 100,000 Btu)
      5--Liquified Petroleum Gas (pounds)
      6--Coal (tons)
      7--Other (unspecified)

      Note:  The same energy type can be entered more than once for a given
      project.  For example, electricity usage subject to winter kWh rates
      might be entered separately from electricity usage subject to summer kWh
      rates.

  o   Annual Energy Consumption (in designated units)--The base annual energy
      consumption of the specified energy type (unadjusted by the Energy Use
      Indexes).

  o   Energy price ($/Unit)--The price per designated unit to be used in
      calculating direct energy costs for the project.  This price should be
      entered in base-year dollars.  

  o   Annual Demand (or Other Fixed) Energy Charge ($/yr)--Annual costs
      related to energy consumption but not directly accounted for in the
      energy prices used to compute direct energy costs.  Example:  Charges
      for peak kilowatt demand, summed over the entire year.  This cost should
      be entered in base-year dollars.  This cost is assumed to increase
      annually at the same escalation rate specified for the energy price.

  o   Price Escalation Method--The user has two alternatives for specifying
      rates of energy price increases:  

      (1)   Escalation rates will be entered by the user.
      (2)   Escalation rates will be automatically retrieved from
            ENCOSTXX.RAN, a disk file with DOE projections of energy price




                                      28

            escalation rates that is distributed with BLCC.  (XX represents
            the year in which the file is released, e.g., ENCOST93.RAN was
            released in fall, 1992.)  Once escalation rates have been retrieved 
            from ENCOSTXX.RAN, they can be modified by the user by backing up 
            to the energy data screen (press <PgUp>) and respecifying the Price
            Escalation Method as 1.  The DOE projections will still be active
            until modified.

      If energy price escalation rates are to be entered by the user, up to 50
      discrete escalation rates and the number of years of duration for each
      rate can be specified.  

      o     Duration (Years)--The number of consecutive years that the
            corresponding energy price escalation rate is to be used.  Note:
            For each energy type, the sum of these duration periods must equal
            or exceed the study period.  (0-60)

      o     Energy Price Escalation Rate (%)--This is the average annual rate
            of price increase for this energy type during the designated
            duration period.  If the analysis is to be performed in real terms
            (Federal analyses and some generic LCC analyses, this rate should
            be in real terms, i.e., net of general inflation.)  (-10 to 20)

     Note:  Only 50 Energy Price Escalation Rates can be displayed on the
            screen.  If each rate is given a duration of one year (as in the
            case when DOE rates are used), and the study period exceeds 50
            years, the last years will all be given the same rate used for the
            50th year.

If DOE projected Energy Price Escalation rates are to be retrieved from the
disk, the following input variables are needed to select the appropriate data
from the file:

  o   Rate schedule type--The type of utility rate schedule used for the
      project.  Choose one:

           (1) residential    (2) commercial    (3) industrial

  o   State abbreviation (2 characters)--The official U.S. Postal Service
      abbreviation for the state in which the project is to be located.  This
      code is used to determine in which of the (currently) four DOE regions
      the project will be located.

  o   General Inflation Rate--The projected rate of general price inflation
      over the study period.  This is required only when the LCC analysis is
      performed in current dollars (private sector and designated Generic LCC
      analyses only).  This rate is used to convert DOE projections of future
      energy price increases from real (excluding inflation) to nominal rates. 
      However, it should be consistent with the user's projection of general
      inflation implicit in the discount rate, escalation rates used for
      capital assets and O&M costs, and mortgage interest rates, if any.





                                      29

Annual Energy Consumption Patterns--After energy price escalation rates are
entered (or retrieved from the disk), the pattern of annual energy consumption
can be specified as constant or variable.  If energy consumption is expected
to be approximately the same from year to year, specify "constant".  If the
amount is expected to change in some predictable manner (e.g., anticipated
switch in heating fuels in the year 2000), specify "variable".  If "variable"
is selected, up to 50 discrete energy use indexes and the number of years of
duration for each index can be specified separately for each energy type:  

  o   Duration (Years)--The number of consecutive years that a corresponding
      Energy Use Index is to be used.  For each energy type, the sum of these
      duration periods must equal or exceed the occupancy period.  Note: 
      These duration periods begin with occupancy (since energy consumption
      calculations begin with occupancy), while the duration periods for
      energy price escalation rates begin with the start of the study period
      (since all prices are entered in base year dollars).  (0 to 60)

  o   Energy Use Index (%)--This is the average rate of energy use during the
      corresponding duration period, as a percent of the Annual Energy
      Consumption specified for that energy type.  An index of 100 percent
      leaves the Annual Energy Consumption unchanged for the corresponding
      years.  (0 to 999)


Finance-related data (non-Federal projects only).  If borrowing costs are an
integral part of the project economics, these can be incorporated into the LCC
analysis.  If there is a Planning/Construction Period, temporary financing can
be specified.  Temporary financing is assumed to expire at occupancy. 
Permanent financing begins with occupancy; one or two permanent mortgage loans
can be specified.  Data for temporary financing during Planning/Construction
Period (if any) and for permanent financing are entered on separate screens. 

Note:  Adjustable-rate mortgages (ARMs) cannot be computed by BLCC.  However,
since the underlying rate of general inflation is assumed to be constant
throughout the study period, the assumption of a constant interest rate over
the same period of time is reasonable.

Data requirements for temporary and permanent mortgages are essentially the
same, except that the life of the loan does not need to be specified for
temporary financing.  (It is assumed to end at the date of occupancy.)


Financing-related variables (non-Federal projects only):

  o   Percent of Initial Project Cost Borrowed--Initial project cost is the
      sum of all component costs (if any), including inflation adjustments
      during construction.  During the Planning/Construction Period, this
      factor is assumed to be the same in each year.  For permanent financing,
      the sum of these factors for two loans cannot exceed 100 percent.







                                      30

  o  Loan Type Codes (choose one):
      (1) fully amortized loan with periodic payments of equal amount
      (permanent financing only), 

      (2) interest only loan with periodic interest payments and repayment of
      principal at end of loan life, and 

      (3) both interest payments and principal repayment deferred to end of
      financing period.

  o   Annual Interest Rate (%)--If the analysis is to be performed in constant
      dollars (designated Generic LCC analyses only), the annual interest rate
      should be entered in real terms (net of general inflation).  A nominal
      interest rate should be specified, without compounding effects or loan
      placement costs considered (i.e., the interest rate to be used is not
      the effective interest rate or "APR").  (0 to 25)

  o   Number of Payments per Year--This is the number of equal payments made
      at periodic intervals through the year.  (Integer between 1 and 52)

  o   Points Paid (% of loan amount)--This is a loan placement fee assessed as
      a percentage of the loan amount (i.e., one "point" equals one percent of
      the loan amount).  (0 to 6)

  o   Life of Loan (Years)--The loan life can be longer or shorter than the
      study period.  If it is longer, any remaining principal and accrued
      interest at the end of the study period are assumed to be paid at the
      end of the study period.  (Integer between 2 and 40)




























                                      31

                                     Index

additional first-year depreciation, 26
annual demand energy charge, 28
annual energy consumption, 28
annual interest rate,  31
annually recurring costs,  26
average price escalation rate during planning/construction,  24
base year,  21
calculating life-cycle costs,  10
capital asset data,  23
capital components,  23
capital gains adjustment factor,  22
capital replacements,  27
comparative economic analysis,  14
component names,  24
cost phasing,  25
definitions of variables,  21
depreciation acceleration rate,  26
depreciation basis adjustment factor,  23
depreciation codes:    
  capital components,  25
  replacements,  27
depreciation life,  26
depreciation recapture code,  23
depreciation tables,  19, 25
discount rate,  22
energy,  28
energy use index,  30
energy consumption,  28
energy consumption pattern (see 'energy use index')
energy costs,  28
energy price,  28
energy rate schedule type,  29
energy types,  28
expected life:    
  capital components,  24
  replacements,  27
federal income taxes,  22
finance-related variables,  30
general inflation rate,  29
general LCC assumptions,  20, 21
income taxes,  22
inflation,  21, 29
initial cost:     
  capital components,  24
  percent borrowed,  30
  replacements,  27
input data file structure,  18







                                      32

installation,  4
loan life,  31
loan type,  31
lowest LCC,  14
main menu,  5
marginal federal income tax rate, 22
marginal state income tax rate,  22
non-annually recurring costs,  27
number of payments per year (loan),  31
operating and maintenance (O&M) costs,  26
percent of initial project cost borrowed,  30
planning/construction period,  22
points (loan),  31
price escalation rates:
  during occupancy,  25
  during planning/construction,  24
  energy,  29
  O&M,  26
price escalation method (energy prices),  28
project-level data,  21
project title,  21
property tax assessment factor:
  capital components,  25
  replacements,  27
property taxes,  22
rate schedule type (energy),  29
replacements,  27
reports,  16
resale value:
  capital components,  24
  replacements,  27
salvage value factor,  26
standard depreciation tables,  19, 25
state income taxes,  22
study period,  21
tax credit factor,  25
type of analysis,  21
year of replacement,  27


 















                                      33