====================
                                  +----+ |         | |
                                  |    | +--+  --+ | |
                                  |  -+| |  | +--| | |
                                  |   || |  | |  | | |
                                  +---|+ +--+ +--+ + +
                                      +-      ver 2.01
                                  ====================

                                       SMALL ARMS
                                   EXTERIOR BALLISTICS


                                           FOR


                                IBM PC's and COMPATIBLES
                                      equipped with
                               Enhanced Graphics Adapters



                                           by


                                   Benjamin W. Hartley
                                Forest Park Estates #103
                                Jaffrey, NH        03452

                                 Voice#: (603) 532-6248






            ( This is ASCII-formatted QBALL.DOC, the On-disk documentation.)

              "QBALL" -- Source code, executable files, and documentation
               are (c) 1992 by Benjamin W. Hartley.  All rights reserved.




         [ QBALL               --   Exterior Ballistics   --               ii ]

                                    TABLE OF CONTENTS
                                    -----------------
          Dedication, Disclaimer, License, Copyright Information..........i
          Table of Contents..............................................ii
          Introduction..................................................iii
          
          Chapter                                                      page
          -------                                                      ----
          1. Getting started..............................................1
               1.1 Files required......................................1
               1.2 Will It Work ?......................................1
               1.3 Copying the program.................................2
               1.4 Printing the documentation..........................2
               1.5 General Instructions................................3
               1.6 Starting QBALL......................................4
          2. Computing ballistic or gun data..............................7
               2.1 Preliminary data entry..............................7
               2.2 Computing and displaying a range table..............8
               2.3 Displaying graphics................................11
               2.4 Changing input data................................14
               2.5 Other ballistic procedures.........................15
          3. Inferring ballistic coefficients............................20
               3.1 First Run: r1 = 0..................................21
               3.2 Second Run: r1 = 25................................22
          4. Printing tables.............................................23
               4.1 Printer warnings...................................23
               4.2 Screen dumps.......................................23
               4.3 Printer setup......................................23
               4.4 Print functions....................................23
               4.5 Typical printed output.............................24
          5. Configuring display and default starting values.............25
               5.1 The Configuration Menu.............................25 
               5.2 Switch toggles (set defaults)......................25
               5.3 Configuring display colors.........................26
               5.4 Using the values you've set........................26
               5.5 Some other considerations..........................27

          Some afterthoughts and Some Wrinkles...........................28

          Appendices:--
          A. Glossary....................................................29
          B. Example of Ballistic Coefficient from Tabular Data..........35
          C. Example QBALLSAV.* file.....................................37
          D. Selected bibliography.......................................39
          E. Error analysis..............................................40
          F. Error Messages, Default Starting Values.....................43
          G. Enhancement form............................................49
          H. Registration form...........................................51


         [ QBALL               --   Exterior Ballistics   --                1 ]

                                     Chapter 1
                                     ---------

                                  GETTING STARTED
                                  """""""""""""""

              1.1  Files Required.
                   --------------

               QBALL.ZIP -- or whatever the name of your downloaded archive 
          file is -- is initially distributed with the following files:

                      QBALL    EXE -- The QBALL executable file.
                      QBALL    CFG -- The QBALL configuration file.
                      QBALLODD DOC -- Odd-numbered documentation pages.
                      QBALLEVN DOC -- Even-numbered documentation pages.
                      QBREADME BAT -- Prints short intro on screen.
                      QBALLENH FRM -- The QBALL enhancement form.
                      QBALLREG FRM -- The QBALL registration form.
                      ADDENDA  DOC -- Additions to the documentation
                      HISTORY  DOC -- A short history of QBALL versions.

               (Note: Registered copies of QBALL are distributed in 
                      non-compressed format, with no *.DOC files)

              The only absolutely, positively, gotta-have file is QBALL.EXE.  
         The documentation is nice, but extra until you've played with the 
         program; the built-in configuration routines will write QBALL.CFG for 
         you if it is not present.

              1.2  Will It Work ?
                   --------------

              In its present incarnation, QBALL is written in and compiled as a 
         stand-alone .EXE file using Microsoft QuickBASIC 4.5.

              QBALL was written on a Gateway 2000 AT clone, with an 80286 pro- 
         cessor, AMI BIOS, MS-DOS 5.0 with 4DOS 4.0 command processor, 5 1/4"
         (1.2 meg) and 3 1/2" (1.44 meg) floppy drives, 40 megabyte hard-disk,
         and Samsung CM4531 EGA monitor.  No coprocessor was used.  Several
         routines from Thomas G. Hanlin's BASWIZ library are included; acknow-
         ledgment for the use thereof is hereby made.  

              QBALL requires an EGA (or better) monitor.  If enough requests
         are received, a CGA-capable version will be developed and released.

              Given an EGA monitor, QBALL should run on any PC-DOS or MS-DOS
         computer.


         [ QBALL               --   Exterior Ballistics   --                3 ]

              1.5  General instructions.
                   --------------------

              Selecting menu options.  Press the key corresponding to the
         letter which is highlighted/bracketed in that option.  For example, to
         choose option "P", press upper- or lower-case "P."  QBALL's menus are
         not case sensitive.  If the option does not appear, or appears in low-
         intensity color, QBALL will "beep", and do nothing further.

              Response to "Y or N".  Press upper- or lower-case "Y" or "N". 
         "Enter" is default for "Y". If any other character is pressed, QBALL 
         will "squeak" and do nothing further.

              ESC key.  "ESC" will "back up" one menu providing a menu is dis-
         played on the screen.  Each menu specifies where "ESC" will take you.
         There is one exception: "Quit to DOS" requires that you press "Q" and
         confirm with "Y," and respond to one further prompt.

              Data entry and error trapping.  Type the value or string to be 
         used, then press [Enter].  QBALL will not accept the wrong data type;
         values which are outside QBALL's ability to use will produce an error
         message.  You may edit your entries before entering them.

              Special case of [Enter] in data entry.  [Enter] pressed when a
         value appears in [brackets] on the prompt line will use that value in
         subsequent computations.

              Swap Units option.  The unit of range measure may be swapped back
         and forth between Yards and Meters using the "New Input Data" menu.  
         As distributed, QBALL defaults to "Yards"; this may be changed using 
         the configuration routines.

              Noises.  QBALL will "squeak" upon erroneous data value entry, and
         "chirps" upon completion of a computation, or upon invocation of 
         <S>wap units.  QBALL defaults to sounds "on"; sounds may be toggled 
         "off" for peace and quiet.  A "flash" replaces noises in quiet mode.

              Graphics.  If appropriate, QBALL will query "Do Graphic ?".
         Press "Y" to display a graphic representation of trajectory data, or
         "N" to skip the display.  There is no provision for toggling graphics
         "off."

              Print options.  QBALL may query "Print This Table?" after every
         data table/listing is displayed on the screen.  Press "Y" to get hard
         copy, "N" to return to the previous menu.  ENSURE that your printer
         is on/on-line if you want hard copy; QBALL will detect whether or not
         your printer is on, but not "paper out"!  Display of the printer
         prompt may be toggled "on" or "off;" QBALL defaults to "on."

              Redirection of data output.  QBALL does not support redirection
         of data output, e.g., to a disk file, except as otherwise provided 
         within the graphics routines.



         [ QBALL               --   Exterior Ballistics   --                5 ]

              Assuming everything is working, the screen has cleared, and you 
         are now looking at the following screen:

          ++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++

                       > Ballistic Computations: Typical Firearm <





                         +=====================================+
                         |     *** M A I N   ME N U ***        |
                         |  ---------------------------------  |
                         |  <C>ompute Ballistic or Gun Data    |
                         |  Infer <B>allistic Coefficient      |
                         |  Use <U>tilities / Configure QBALL  |
                         |  <N>ew or Changed Input Data        |
                         |  ---------------------------------  |
                         |  <Q>uit -- Return to DOS            |
                         +=====================================+





          ----------------------------------------------------------------+
          [ MV:      ][ C1:      ][ Wt:     ][ Met: 59d 0' 29.53" 78%    ]|
            |           |           |           |                         |
            |           |           |           |                         |
           Muzzle      Ballistic   Bullet     Metro --                    |
           Velocity   Coefficient  Weight,    Temperature, degrees F.     |
           (FPS)                   (grains)   Gun Altitude, feet          |
                                              Barometric Pressure, "Hg    |
                                              Relative Humidity, percent  |
                                                                          |
                                                          +---------------+
                                                          |               
               (Please make note of the  information)     +--------------
               (contained in the "Information Line",)     [ H: 1.00][Yds]
               (here shown "folded".   The "Informa-)       |         |
               (tion"  or  "Info Line" is updated if)       |         |
               (changes are  made  to any of the in-)      Sight    Range
               (formation it shows.   Note that some)      Height   Units
               (of the items are  blank; values will)     (inches) (Inverse)
               (be filled in presently.             )

          ++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++

              Go on to the next page...



         [ QBALL               --   Exterior Ballistics   --                7 ]


                                       Chapter 2
                                       ---------

                            Computing Ballistics or Gun Data
                            """"""""""""""""""""""""""""""""

              2.1  Preliminary data entry.
                   ----------------------

              Before doing anything else, we're going to have to enter some 
         information for QBALL to chew on.  QBALL will ask you for data which
         it does not already have.  The items of information for which QBALL 
         will prompt you are, in order, (with suggested "for practice" 
         entries):

                    a. The ballistic coefficient (C1) for the
                       projectile in question . . . . . . . . . . .  .250

                         (Note the leading decimal point!)

                    b. The bullet weight in grains . . . . . . . . .  125

                    c. Whether or not to use the displayed metro . .  "Y"

                         (QBALL will default to "Standard Metro";  you)
                         (can use nonstandard metro, but, just to keep)
                         (things simple,  stay with standard metro for)
                         (now.                                        )

                    d. The muzzle velocity . . . . . . . . . . . . .  2300

              Enter values at the appropriate places when prompted.  Try
          entering an impossible value or two, and see what happens.  A
          complete list of QBALL's error messages is in Appendix E, with
          the most common causes for their display.

              (Here are some "impossible" values to try, just to see what
         happens: Ballistic Coefficient: 1.000; Bullet Weight: 0; Muzzle
         Velocity: 4700 FPS.)

              For purposes of this tutorial, the gun/bullet is identified as
         "Typical Firearm."  This may be changed using the "<N>ew or Changed"
         menu option.  Continue with "Typical Firearm" for the time being.


         [ QBALL               --   Exterior Ballistics   --                9 ]
         
              Take a close look at the menu: it is telling you that the range 
         at which you wish to be zeroed must be set.  Press "<S>et Zero..." and
         enter: "150" -- without the quotes, of course.  (Until you set a zero
         range, "Range <T>able..." won't do anything but make a rude noise.)

              Back where we started, eh?  Take a closer look.

                          +=================================+
                          |    *** Computations Menu ***    |
                          |  ------------------------------ |
                          |  <S>et/Reset Current Zero Range |
                          |  Range <T>able (0 = 150 Yards)  |
                          |  <O>ther Ballistics Procedures  |
                          |  <N>ew or Changed Input Data    |
                          |  ------------------------------ |
                          |  <ESC> to  M A I N   M E N U    |
                          +=================================+

              The zero range for your range table is now set.  In future, if 
         QBALL has been provided a zero range, it will be displayed in the 
         computations menu.  If no valid zero range exists, then the phrase
         "Range <T>able (0 MUST BE SET)" will be displayed in low intensity
         color instead.

              One of the useful tables that QBALL will generate is a range
         table from zero to a designated range with a fixed range increment.
         Press "T" and  enter the following data when prompted:

                       Range for List/Table/Comp.........: 200
                       Range Increment...................:  25

               QBALL will clear the screen and display the following table,
          (here shown in somewhat compressed format):

                        Range Table, Zeroed at Highlighted Range
                        ----------------------------------------
             Range  R e m a i n i n g  Total  Path/Sight Line  Defl'n  Time
             Yards  Velocity   Energy   Drop  M.O.A.   Inches  10 MPH  Flght
             -----  -----------------  -----  ---------------  ------  -----
                 0    2300      1468     0.0   0.0      -1.0     0.0   0.000
                25    2218      1365     0.2   1.5       0.4     0.1   0.033
                50    2138      1268     0.9   2.7       1.3     0.5   0.068
                75    2059      1176     2.0   2.4       1.8     1.0   0.104
               100    1982      1090     3.6   1.7       1.7     1.8   0.141
               125    1906      1008     5.8   1.0       1.2     2.8   0.179
             [ 150    1832       932     8.6   0.0       0.0     4.1   0.219 ]
               175    1761       861    12.0  -1.1      -1.9     5.8   0.261
               200    1693       795    16.2  -2.2      -4.5     7.7   0.305
                          -----------------------------------
                                Do Graphic ? ([Y] or N)


         [ QBALL               --   Exterior Ballistics   --               11 ]
          
              2.3  Displaying Graphics.
                   -------------------

              You should at this time be looking at a graphic representation of
         the projectile's trajectory as viewed from the side.  Note the empha-
         sized line indicating the line of sight, and the curved line which 
         delineates the bullet's path from the muzzle (0) to the maximum range
         (200).  Unfortunately, there's no way to provide a picture of the 
         graphics part of the screen.  The bottom of the screen, however, dis-
         plays some valuable information, something like this:

                                                    +=========================+
                   > Current <    > Previous <      |     Graphics Menu       |
          Max Ht:   1.8" @ 86                       +-------------------------+
          Min Ht:  -4.5" @ 200                      | <Q>uit Graphics Routine |
          MuzVel:     2300 FPS                      | <G>rid Toggle           |
          BCoeff:     .250                          | <S>ave Current Data     |
          ZeroRg:   150 Yards                       | On Disk: none           |
          Metro :   Standard                        +=========================+

              The information provided is pretty much self-explanatory.  The 
         options in the menu, i.e., <Q>uit <S>ave <G>rid, allow you to quit 
         the graphics routine, save the current trajectory data to disk, and 
         toggle the background grid on and off, respectively.
              Press "G" to see what happens; the screen is redrawn without the
         background grid lines.  Press "G" again to re-display the grid lines.
         (In its default configuration, QBALL will display the grid.)
              Now press <S>ave to write this trajectory data to a disk file.
         (It'll go into the current directory.)  After some grinding noises
         from your disk drive, during which you're shown some other informa-
         tion, here's what the bottom of the screen looks like:

                                                    +=========================+
                   > Current <    > Previous <      |     Graphics Menu       |
          Max Ht:   1.8" @ 86                       +-------------------------+
          Min Ht:  -4.5" @ 200                      | <Q>uit Graphics Routine |
          MuzVel:     2300 FPS                      | <G>rid Toggle           |
          BCoeff:     .250                          | <S>ave Current Data     |
          ZeroRg:   150 Yards                       | On Disk: <0>            |
          Metro :   Standard                        +=========================+

              "On Disk" now tells you that you have one set of trajectory data
          on disk.  Also note that "<S>ave..." has been disabled; you don't
          want two sets of identical data, do you?

              Now press "Q" to quit the graphics routine.

              The previously-displayed range table is again displayed, but with
         a different prompt:
                             Print this Table ? ([Y] or N).

              If your printer is ON and ON-LINE, press "Y" to obtain a hard 
         copy of the range table.  If no printer is available, or you don't
         want to use up paper, press "N," to return to the computations menu.


         [ QBALL               --   Exterior Ballistics   --               13 ]

              As you can see, the screen display is somewhat different.  The 
         differences between trajectories are graphically presented, and the 
         information blocks reflect those differences.  Note that the previous
         value of the parameter which we changed, the muzzle velocity, is high-
         lighted in the new information block.  All values so changed will be
         thus highlighted, except for "Metro" which will be displayed as either
         "Standard" or "Non-standard."

              Now, let's save this "current data" data to disk.  Press "S". 
         The new bottom-of-screen should look like this:

                                                    +=========================+
                   > Current <    > Previous <      |     Graphics Menu       |
          Max Ht:   1.5" @ 86        1.8" @ 86      +-------------------------+
          Min Ht:  -3.5" @ 200      -4.5" @ 200     | <Q>uit Graphics Routine |
          MuzVel:     2500 FPS         2300         | <G>rid Toggle           |
          BCoeff:     .250             .250         | <S>ave Current Data     |
          ZeroRg:   150 Yards        150 Yards      | On Disk: <0> thru 1     |
          Metro :   Standard         Standard       +=========================+

              QBALL lets you save up to 16 "QBALLSAV" files, 000 through 015;
         the Graphics Menu accesses the saved files using "1" through "9: and
         "A" through "F".  (Quick introduction to hexadecimal, anyone?)  An
         example of "QBALLSAV" is to be found in Appendix C., page 37.

              Should the display become cluttered with too many trajectory
         plots, you may erase all of them (except "Current") by toggling the
         grid.  You retain the ability to call up data from all disk files.

              Remember that "specialized *.INI file" that QBALL couldn't find?
         It now exists as "QBALLSAV.INI" in the current directory, along with 
         two sets of saved trajectory data: "QBALLSAV.000" and "QBALLSAV.001."

              When you decide to quit QBALL, you will be prompted to:

                             Retain Saved Data ? ([Y] or No)

         It is recommended that you press "N" at that point, at least until you
         have played with QBALL for awhile.  (Answering "N" erases all the
         "QBALLSAV" files, including "*.INI.")

              Press "Q" at this point to re-display the range table.


         [ QBALL               --   Exterior Ballistics   --               15 ]

              Sight Height.  Allows fine-tuning QBALL to a specific weapon.
         The supplied sight height of 1.00 inches is a "generic" value, and 
         should be changed to reflect the actual sight height.  Acceptable val-
         ues: -2 to +5 inches.

              Swap Units.  This option toggles QBALL between yards and meters,
         and will cause QBALL to make all range calculations in the chosen unit
         of measure.  Note well, however, that while computations using meters
         are accurate, they may produce some rather strange looking displays;
         specifically, the range increment may not appear as expected.  This is
         unavoidable, as meters and yards to not take kindly to being convert-
         ed, one to the other.  You may return to "yards" by swapping units
         again.  Note that only ranges are affected; heights and deflections
         will still be displayed or printed in inches, and velocities will
         continue to be shown in feet per second (FPS).

                     (A rough  approximation  to convert inches)
                     (to centimeters  is to multiply the inches)
                     (dimension  by 2 1/2.   (A  more  accurate)
                     (multiplier is 2.5404.)   If you're a real)
                     (glutton  for  punishment,  you can divide)
                     (velocities in  FPS  by 3.28083  to obtain)
                     (velocities in Meters per second.   QBALL,)
                     (however, will not perform either of these)
                     (conversions for you.                     )

              2.5  Other Ballistic Procedures.
                   --------------------------

              Five "other ballistic procedures" are described in this section.
         The first two, point-blank range and wind vector corrections, directly
         interface with the range table/graphics procedures; slant angle of
         fire, sectional density, and free recoil may be invoked for the infor-
         mation they produce.  From the computations menu, press "O" to access
         the "Other Procedures Menu:"

                           +===============================+
                           |   * Other Procedures Menu *   |
                           |  ---------------------------  |
                           |  <P>oint-blank Range          |
                           |  <W>ind Vector Corrections    |
                           |  Slant <A>ngle of fire        |
                           |  <S>ectional Density          |
                           |  <F>ree Recoil of Gun         |
                           |  ---------------------------  |
                           |  <ESC> to Computations Menu   |
                           +===============================+



         [ QBALL               --   Exterior Ballistics   --               17 ]

                   Wind Vector Corrections.
                   -----------------------
              One of the columns in the range table gives the wind deflection,
         in inches, for a 10 MPH "pure" crosswind.  To compute the deflection 
         for other windspeeds and directions, press "W", and enter the wind
         speed (in MPH), and the direction from which the wind is blowing,
         relative to the line of sight, from 0 to 360 degrees.  QBALL will
         compute the vector effects of the wind values entered, and will dis-
         play them as shown:

         +++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
                             ------------------------------
                      Wind velocity      [ 10 MPH ]            20
                      Wind direction     [  270d  ]           135
                             ------------------------------

                            Range wind =  21 feet per second
                            Cross wind =  14 miles per hour

                             Crosswind correction =   -1.40

                    Use correction factor(s) in tables ? ([Y] or N)

         +++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++

         A "Y" response will cause the deflection values in the range table to
         be displayed for the computed crosswind; in this case, 14 MPH.  QBALL
         takes crosswinds from left to right as positive; from right to left,
         as negative.  No correction is applied for the range wind, as that 
         effect becomes significant only at very long range, with a low muzzle
         velocity, and small ballistic coefficient.  (Try entering a new muzzle
         velocity using the range wind correction and see.)  Should you wish to
         return to the default wind values, simply press "enter" when prompted
         for wind values when starting this routine.


         [ QBALL               --   Exterior Ballistics   --               19 ]

                   Free Recoil Energy.
                   ------------------
              We all know that a firearm "kicks."  Simple Newtonian physics,
         right?   But how hard does it kick?  One way to compare absolute num-
         bers, and without getting into the mare's nest of "actual" versus
         "perceived" recoil, is to compare the recoil velocity and energy im-
         parted to the weapon upon firing.  Press "F," and enter the powder
         weight in grains.  The example uses 38 grains powder weight, which
         seems to be a fair "average" powder weight from several random exam-
         ples taken from the SPEER Reloading Manual.  You must also enter the
         weapon's weight, in either pounds and ounces or in pounds and decimal
         fractions of a pound.  For an 8 1/2 pound rifle, for example, enter
         either "8.5" or "8<space>8".  The result is displayed:

                             ------------------------------
                             Gun Recoil Velocity:  7.83 FPS
                             Free Recoil Energy :  8.11 Ft#


                                ===> press any key <===

         Unfortunately, these figures are relatively meaningless without some
         basis for comparison.  Here are three for starters, all data computed
         using QBALL:
                                              --------- G U N --------
                                              Velocity          Energy
                                                FPS             Ft-Lbs
                                              --------          ------
              1. Ruger M77R (6.75 pounds)
                 .22-250 Remington               7.86             6.49
                    Muz Vel = 3680
                    Bul Wt  =   55
                    Pow Wt  =   36

              2. Marlin 336CS (7 pounds)
                 .30-30 Winchester              10.67            12.39
                    Muz Vel = 2390
                    Bul Wt  =  150
                    Pow Wt  =   35

              3. M1 Garand (9.5 pounds)
                 .30-'06 Springfield            10.88            17.47
                    Muz Vel = 2700
                    Bul Wt  =  180
                    Pow Wt  =   50.5

              The ammunition specified is a "best estimate" using published
         Winchester data for velocities and bullet weights, and powder weights
         from the HORNADY HANDBOOK.  The weapon weights were taken from the
         1991 edition of GUN DIGEST.


         [ QBALL               --   Exterior Ballistics   --               21 ]

              3.1 First Run: r1 = 0
                  -----------------

              When prompted for the "first range," press "enter;" for "second
         range," enter "100."  The following screen will be displayed.  Enter
         the appropriate velocity values as shown.  QBALL will quickly return
         the value of the ballistic coefficient, and ask if you wish to calcu-
         late another round.  Responding "Y" clears the velocity inputs, and
         you'll be prompted for another velocity pair.  In this case, press
         "N."  (In all probability, you're working from published tables, and
         using the same numbers twice would be meaningless.)

          ++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++

                       *** Inferring a Ballistic Coefficient ***
                       -----------------------------------------
                                  Metro: as displayed
                 Relative Air Density = 1.000; Sonic Velocity =   1.000
                       -----------------------------------------


                                   For Round Number 1
                        First Velocity        (Ft/Sec)      2300
                        Second Velocity       (Ft/Sec)      1982

                           For Standard Atmosphere, C1 = .250

                          Calculate another Round? ([Y] or N)



                       [ Lower & Upper Ranges (yards) [0] & 100 ]

         +++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++

              The center of the screen will clear, and the following informa- 
         tion is displayed:

                       -----------------------------------------
                             Average C1 for 1 round = .250
                         Between Mean Velocities 2300 and 1982
                           Calculated Muzzle Velocity = 2300
                       -----------------------------------------

              QBALL will ask if you wish to print the table.  For now, press
         "N" to return to the main menu.  Note that the information line now
         shows the muzzle velocity and the computed ballistic coefficient.  If
         you so desired, you could now go on to compute ballistic or gun data,
         but let's try the infer ballistic coefficient routine again, with r1
         set to something other than zero.  (You should be at the main menu;
         press "B.")


         [ QBALL               --   Exterior Ballistics   --               23 ]


                                       Chapter 4
                                       ---------

                                     Printing Tables
                                     """""""""""""""

              4.1 Printer warnings.
                  ----------------

              QBALL will detect "device fault" if your printer is off or off-
         line.  You must, however, ensure that paper is installed and the pro-
         per printer setup has been accomplished BEFORE you try to print ANY
         QBALL output!  (QBALL does not detect "paper out.")

              4.2 Screen dumps.
                  ------------

              It is possible to print a screen's worth of information using the
         Shift-PrtScr key combination available in DOS.  This is NOT recom-
         mended, however, as you may very well lose information which has al-
         ready scrolled past on the screen.

              4.3 Printer setup.
                  -------------

              You need not set up your printer to skip perforations in fanfold
         paper; QBALL keeps track of the number of lines printed and issues a
         formfeed when appropriate.  Continuation tables are sequentially num-
         bered, and each page will have the appropriate column headers printed
         on it.
              There is no need to set your printer to indent from the left
         margin, either.  It is best, in fact, to use a printer setup of "left
         margin = 0," as QBALL is set up to indent each table it prints an
         appropriate number of spaces.
              You may also toggle the print prompt "off," in which case, you
         will not be asked if you wish hard copy.  This feature is useful if
         you are sure you won't want printouts, or if you have no printer.
         QBALL defaults to printer "on," and displays the print prompt.

              4.4 Print functions.
                  ---------------

              You may obtain hard copy of any table which is followed by the
         prompt:
                              Print this table? (Y or N).

              Press "Y" to print the table. The prompt will be replaced with
         the statement "Printing table" in highlighted text.  If you have a
         printer with a sizable buffer, QBALL will return you to the previous
         menu quite quickly.  If not, QBALL will finish printing out the table,
         then return you to the previous menu.


         [ QBALL               --   Exterior Ballistics   --               25 ]


                                       Chapter 5
                                       ---------

                     Configuring display and default starting values
                     """""""""""""""""""""""""""""""""""""""""""""""

              5.1  The Configuration Menu.
                   ----------------------

              You may wish to change some or all of QBALL's start-up data.
         Press "U" at the main menu, to display this "Utilities Menu:"

                          +=================================+
                          |   ***   Utilities Menu   ***    |
                          |  -----------------------------  |
                          |  <T>oggle Units/Grfx/Noise/PRN  |
                          |  Change Display <C>olors        |
                          |  <W>rite QBALL.CFG File         |
                          |  Invoke a <D>OS Shell           |
                          |  -----------------------------  |
                          |  <ESC> to M A I N  M E N U      |
                          +=================================+

              5.2  Toggle Units/Grfx/Noise/PRN.
                   ---------------------------

              Press "T" to display this "Switch Toggle Menu."  Pressing the
         appropriate key toggles that particular item; the current setting is
         reflected immediately, and QBALL will act accordingly until it is
         again changed.

                           +================================+
                           |   *** Switch Toggle Menu ***   |
                           |  ----------------------------  |
                           |  Yds/Mets <S>wap (Now Yards)   |
                           |  Graphics <G>rid (Now ON)      |
                           |  <P>rinter on/off (Now ON)     |
                           |  <N>oises on/off (Now ON)      |
                           |  ----------------------------  |
                           |  <ESC> to Utilities Menu       |
                           +================================+

              You may also toggle the unit of range measure between yards and
         meters from the "New/changed Input Data" menu, which is accessed from
         the main menu and the computations menu.
              If you toggle the printer off, all "Print This Table" prompts are
         suppressed, and "====> Press any key <====" is displayed instead.
              If noises are toggled off, they are replaced with a short-dura-
         tion "flash" in the lower right corner of your screen.
              Toggling the graphics grid merely changes the appearance of the
         first display of "pictures;" you will retain the option of changing
         that appearance in the graphics routine.


         [ QBALL               --   Exterior Ballistics   --               27 ]

         Upon invocation of the "Write QBALL.CFG File," the new .CFG file will
         also include the values of these items which are currently in effect.
         This allows you to "tailor" your copy of QBALL to match your own con-
         ditions: your weapon, and the actual (or anticipated) metro which is
         encountered at your own firing range.

              (A description of the *.CFG file may be found in Appendix F.)

              Specific times you might very well want to use metro values other
         than standard are, for example, if your range is not at sea level, or
         if you're shooting during the summer, when the temperature might very
         well exceed 59 deg.F.  You can configure QBALL to start with the alti-
         tude of your range, or an expected temperature, without the hassle of
         changing the values after start-up.

              In similar fashion, you may configure QBALL to start with the
         name of your own weapon, say, "Ruger M77 .270" and the actual measured
         height of that weapon's sight, say, 1.25 inches.



         [ QBALL               --   Exterior Ballistics   --               29 ]



                                       Appendix A
                                       ----------


                                        Glossary
                                        """"""""


         ABSOLUTE ZERO - Properly, that temperature at which all molecular mo-
         tion ceases.  For practical purposes, -459.67 degrees Fahrenheit, or 0
         degrees Rankine.

         AIR DENSITY - The mass (weight) of a unit volume of air.

         AIR RESISTANCE - The retardation of a bullet's forward flight due to
         the atmosphere.

         ALTITUDE - The vertical distance above or below sea level.  Altitudes
         above sea level are taken as positive; those below, as negative.

         BALLISTICS - The study of moving projectiles.  Commonly, what is meant 
         is "exterior" ballistics: that portion of the bullet's flight between
         the muzzle and the target.

         BALLISTIC COEFFICIENT - The ratio of the sectional density of a pro-
         jectile to its coefficient of form. A measure of how well a bullet re-
         tains its velocity.  Commonly supplied by reloading manufacturers, or
         it may be derived from their ballistic tables.  In QBALL, the ballis-
         tic coefficient is always taken at standard metro.  The program cor-
         rects for nonstandard conditions, but does not display the corrected
         ballistic coefficient(s).  See STANDARD METRO

         BALLISTIC EFFICIENCY - The relative ability of a bullet in flight to
         overcome air resistance.

         BORE - The inside of a firearm's barrel.  In rifled firearms, the bore
         diameter is the original dimension of the barrel before the rifling
         grooves are cut or swaged in it.  Bore diameter may also be taken as
         the transverse dimension between the lands of the rifling.  See LANDS

         BRASS - Alloy of copper and zinc commonly used in the fabrication of
         cartridge cases.  Also, one or more cartridge cases containing neither
         powder, nor primer, nor bullet.

         BULLET - The actual projectile in small arms ammunition. Commonly
         corrupted to mean the entire cartridge.

         BULLET WEIGHT - Weight of the actual projectile, usually stated in
         grains.  See GRAIN


         [ QBALL               --   Exterior Ballistics   --               31 ]

         GRAIN - A unit of weight equal to 1/7000 of a pound.  437.5 grains
         equal one ounce.   May also refer to an individual particle, or ker-
         nel, of powder.  In cartridge specifications, always refers to the
         weight, never to individual particles.

         GROOVES - Spiral impressions cut or swaged lengthwise through a bore
         to impart spin to projectiles.  See LANDS.

         GROUP - The pattern made, at the target, by a number of shots fired at
         a single point of aim and (usually) a common sight setting.  Usually
         measured from center-to-center of the two most widely spaced holes.

         GUN - In popular usage, refers to firearms, generally.

         HANDGUN - A firearm designed to be held and fired with one hand.

         HOLD OFF - The distance a shooter must shift his point of aim to the
         left or right to compensate for wind deflection.

         HOLD OVER - The distance a shooter must raise his point of aim to be
         on target when his firearm is zeroed at a lesser range.

         HORIZONTAL FIRE - That type of fire occurring when the barrel of the 
         firearm is not elevated significantly above the horizontal.  Generally
         may be taken as 1 degree of arc or less.

         INGALLS' TABLES - A  set of ballistic tables first calculated by Col.
         J. M. Ingalls in 1918. Probably the most widely used tables for small
         arms ballistics calculations.

         IRON SIGHTS - Colloquial term for metallic sights.

         LANDS - Those portions of a rifled bore not cut away by rifling
         grooves.  See GROOVES

         LEAD - (leed) How far ahead of a moving target a shooter must aim to
         be assured of hitting it.

         LEAD - (led) Soft, dense, silvery-gray metal with relatively low melt-
         ing point which forms the basis for many bullets.

         LINE OF DEPARTURE - An imaginary line formed by extending the axis of
         a firearm's bore in a downrange direction.

         LINE OF SIGHT - An  imaginary line from the center of the sights to
         the point of aim. The bullet typically crosses this line only twice;
         once, a few yards from the muzzle, and again at the targeted distance.

         MASS - Properly, the weight of an object divided by the acceleration
         due to gravity.  Commonly taken to mean "weight."



         [ QBALL               --   Exterior Ballistics   --               33 ]

         POWDER - The propellant material used in firearms.  Usually not in
         powder form, but as small rods, spheres, or flakes.

         PRIMER - Impact-sensitive component of a cartridge which ignites the
         powder charge upon being struck by the firing pin or the striker of a
         firearm.

         PROJECTILE - A bullet, shell, golfball or other object shot, hit,
         thrown, or hurled in space;  a projectile receives a single impetus,
         and continues in motion by its own inertia.  A bullet is not properly
         a projectile until it is in motion.

         RELATIVE AIR DENSITY - The density of air at the measured metro divid-
         ed by the density of air at standard metro, expressed as a dimension-
         less decimal fraction, e.g., 1.000.

         RELATIVE SONIC VELOCITY - The velocity of sound at the measured metro
         divided by the velocity of sound at standard metro, expressed as a di-
         mensionless decimal fraction, e.g., 1.000.

         REMAINING ENERGY - A projectile's energy in foot-pounds at a given
         range.

         REMAINING VELOCITY - A projectile's velocity in FPS at a given range.

         ROUND - One complete cartridge.  Also used to refer to the sequential
         number of a shot in a number of shots, as "Round #3."

         SCOPE - optical, as opposed to metallic, sights.  Generally compounded
         as in "scope sight", "scope equipped", "scoped."

         SIGHT HEIGHT - The measured vertical distance between the horizontal
         centerline of the sights and the axis of the bore.

         SIGHTING IN - The process of firing to determine point of impact at a
         given range and adjusting the sights so that the point of impact has
         the desired relationship to the point of aim.  See also ZERO.

         SIGHT RADIUS - The distance between the rear and the front sight, on
         those weapons equipped with metallic sights.

         SONIC VELOCITY - The speed of sound through air.

         STANDARD MET - Atmospheric conditions as follows:  Temperature is 59
         degrees Fahrenheit, barometric pressure is 29.53 inches mercury, gun
         altitude is zero (sea level), and relative humidity is 78 percent.
         Firing tables are usually corrected to standard met conditions.

         STP - Standard Temperature and Pressure.  See STANDARD MET.

         STRING - A number of rounds fired at a common point of aim, often for
         the purposes of sighting in or zeroing a firearm.


         [ QBALL               --   Exterior Ballistics   --               35 ]

                                      Appendix B
                                      ----------

                   Example of Ballistic Coefficient from Tabular Data
                   """"""""""""""""""""""""""""""""""""""""""""""""""

              The following table summarizes the determination of a ballistic
         coefficient using tabular values.  The table is the one published in
         the 1990 GUN DIGEST, page 229.

                +-----------------------------------------------------+
                | From Gun Digest Table for 30-06 Spfd, 180 gr bullet:|
                |                                                     |
                |                          Range in Yards             |
                |               ------------------------------------  |
                |               Muz     100      200     300     400  |
                |               ------------------------------------  |
                | Velocity      2700   2469     2250    2042    1846  |
                | Energy        2913   2436     2023    1666    1362  |
                | Trajectory    -1.5    2.5      0.0    -9.3   -27.0  |
                +-----------------------------------------------------+
                      Table B1.  Data Taken From Published Table.

              Using the routines to infer a ballistic coefficient, plugging in
         100 and 200 yards for the required ranges, and using the associated 
         velocities, QBALL reports that C1 (the ballistic coefficient) is equal
         to 0.384.
              Returning to the main menu, selecting the ballistic computations
         option, and entering the appropriate values for muzzle velocity and
         bullet weight and zero range, QBALL produces the data shown in Table
         B2.
                +-----------------------------------------------------+
                | QBALL Data Table for 30-06 Spfd, 180 gr bullet:     |
                |                                                     |
                |                          Range in Yards             |
                |               ------------------------------------  |
                |               Muz     100      200     300     400  |
                |               ------------------------------------  |
                | Velocity      2700   2470     2251    2043    1846  |
                | Energy        2913   2437     2024    1668    1362  |
                | Trajectory    -1.5    2.1      0.0    -9.0   -26.2  |
                +-----------------------------------------------------+
                        Table B2.  Data Calculated Using QBALL.

              The maximum variations are: Velocity, 1 FPS; Energy, 2 FtLbs; and
         Trajectory 0.8 inches.  QBALL, therefore, can produce results in sub-
         stantial agreement with published data.
              It may be found that QBALL's computation of ballistic coefficient
         from tabular data may not exactly agree with the value known to be
         correct.  A series of successive approximations can compensate for
         QBALL's built-in roundoff characteristics, and the small errors re-
         sulting from them.


         [ QBALL               --   Exterior Ballistics   --               37 ]

                                       Appendix C
                                       ----------


                               Typical QBALLSAV.00n File
                               """""""""""""""""""""""""


              The following table represents, in part and in somewhat compress-
         ed form, one of the QBALLSAV file produced using the data entered in
         Chapter 2.  The first column is the range; the second, the trajectory
         height relative to the sight line.  Note that the range increment is
         1/100 of the maximum range.  This is true of all QBALLSAV.00n files.

                                       ----------

         Yards
                     0.0                          -1.00
                     2.0                          -0.89
                     4.0                          -0.78
             ////////////////////////////////////////////////
              ... major portion of data omitted
             ////////////////////////////////////////////////
                   196.0                          -3.17
                   198.0                          -3.36
                   200.0                          -3.55
         2500     .25      150      1.49034     -3.548949      86
         200   166.53      01-08-1992 / 12:00:00 / Typical Firearm
         Misc Info:  Wt  Tmp Alt  BPr  Hum SHt
                     125  59  0  29.53  78  1
         --------------[ end QBALLSAV.001 ]------

                                       ----------
                         =====================================
                         Key to values listed at end of table:
                         -------------------------------------
         First line:
             [Muzzle velocity] [Ballistic Coefficient] [Zero Range]
                            [Max Height] [Min Height] [Range at Max Height]
         Second line:
             [Max Range] [Metro constant] [Date/Time/Identifier]
         Third and fourth lines:
             [Bullet weight] [Temperature] [Gun altitude] [Barometric Pressure]
                            [Relative humidity] [Sight height]
         Fifth line:
             End of file indicator with Filename and number
                         =====================================

              The metro constant in line 2 keeps track of whether this trajec-
         tory data was computed using standard or nonstandard met.  It is the
         sum of the four metro values: temperature, altitude, barometric pres-
         sure, and relative humidity.

              Important Note: QBALLSAV files generated by earlier versions of
         QBALL are NOT --  I say again, NOT -- compatible with QBALL v2.01.
         Sorry 'bout that.


         [ QBALL               --   Exterior Ballistics   --               39 ]

                                       Appendix D
                                       ----------


                                 Selected bibliography
                                 """""""""""""""""""""



              Davis, William C., Jr. "Ballistics on the Home Computer,"
                American Rifleman, CXXXI, 6 (June, 1983), p. 36.

              Davis, William C., Jr. "Ballistics on A Pocket Calculator,"
                American Rifleman, CXXXV, 6 (June, 1987), p. 42.

              Davis, William C., Jr. "Calculate Ballistic Coefficients,"
                American Rifleman, CXXXVII, 3 (March, 1989), p. 44.

              Davis, William C., Jr. "What Is The Ballistic Coefficient?,"
                American Rifleman, CXXXVII, 3 (March, 1989), p. 12.

              HODGDON BASIC DATA MANUAL, Shawnee Mission: Hodgdon Power
                Company, Incorporated, 1987

              Ramage, C. Kenneth (ed.).  LYMAN RELOADING HANDBOOK.  46th ed.
                Middlefield: Lyman Products Corporation, 1982.

              Reiber, Ron L., and Heers, Edward A. (eds.).  HORNADY HANDBOOK
                OF CARTRIDGE RELOADING, RIFLE-PISTOL.  3d ed.  Grand Island:
                Hornady Manufacturing Company, 1980.

              SPEER RELOADING MANUAL #11, Lewiston: Omark Industries, Incorp-
                orated, 1987

              Warner, Ken (ed.). GUN DIGEST, 1990.  Northbrook: DBI Books,
                1989.

              Warner, Ken (ed.). GUN DIGEST, 1991.  Northbrook: DBI Books,
                1989.

              WINCHESTER PRODUCT INFORMATION AND BALLISTICS GUIDE, East
                Alton:  Winchester/Olin Corporation, 1989


         [ QBALL               --   Exterior Ballistics   --               41 ]

              An examination of the data in Table D1 indicates that computa-
         tion of remaining velocities using QBALL will be, on average, 0.47%
         high relative to the Speer data, and 0.42% low relative to the Hornady
         data.  The Hornady data, however, must be considered suspect, as the
         actual ballistic coefficients available in the Hornady table do not
         exactly match those specified.  Even so, it would appear that QBALL's
         velocity results are certainly within one or two percent of published
         data.  In practical terms, there is probably one or two percent vari-
         ation in velocity between successive rounds in a string, if not more.
         QBALL, it would appear, can produce velocity figures which are accu-
         rate enough for practical purposes.
              Trajectory comparisons are presented in the following table.

           +----------------------------------------------------------------+
           |         Trajectory Comparisons  -  Conditions as Shown         |
           |         ==============================================         |
           |                    [ All at Standard Met ]                     |
           +----------------------------------------------------------------+
           | Range = 250 yards, zeroed at 50 yards; C1 =.12, MuzVel = 2100  |
           |                                                                |
           |         Inches above/below line of sight at...(yards)          |
           |         ---------------------------------------------          |
           |         Muzzle     50       100       150       200       250  |
           |         ------    ---      ----      ----      ----      ----  |
           | QBALL    -1.5     0.0      -1.3      -6.4     -16.9     -34.3  |
           | SPEER    -1.5     0.0      -1.3      -6.4     -17.0     -34.7  |
           | HORNADY  -1.5     0.0      -1.2      -6.3     -16.7     -33.2  |
           +----------------------------------------------------------------+
           | Range = 400 yards, zeroed at 200 yards; C1 =.26, MuzVel = 2500 |
           |                                                                |
           |           Inches above/below line of sight at...(yards)        |
           |           ---------------------------------------------        |
           |           Muzzle       100        200        300        400    |
           |           ------      ----       ----       ----       ----    |
           | QBALL      -1.5        2.9        0.0      -13.0      -39.5    |
           | SPEER      -1.5        3.0        0.0      -13.0      -39.6    |
           | HORNADY    -1.5        3.0        0.0      -13.1      -39.7    |
           +----------------------------------------------------------------+
           | Range = 400 yards, zeroed at 200 yards; C1 =.50, MuzVel = 3300 |
           |                                                                |
           |           Inches above/below line of sight at...(yards)        |
           |           ---------------------------------------------        |
           |           Muzzle       100        200        300        400    |
           |           ------      ----       ----       ----       ----    |
           | QBALL      -1.5        1.1        0.0       -5.2      -15.2    |
           | SPEER      -1.5        1.1        0.0       -5.2      -15.2    |
           | HORNADY    -1.5        1.1        0.0       -5.3      -15.7    |
           +----------------------------------------------------------------+
              (Key: MuzVel = Muzzle Velocity  C1 = Ballistic Coefficient)

             Table D2.  Trajectory Comparisons Under Specified Conditions.


         [ QBALL               --   Exterior Ballistics   --               43 ]

                                      Appendix F
                                      ----------

                      Error messages and default starting values
                      """"""""""""""""""""""""""""""""""""""""""


          Error Messages
          --------------

              Following are all the QBALL error messages, with a description
         of the circumstances under which they will be encountered.

          +-----------------------------------------------+
          | .CFG File Not Found -- Using Internal Values. |
          +-----------------------------------------------+
               QBALL.CFG not found.  Either it doesn't exist, or QBALL.EXE
               and QBALL.CFG are not in the same directory/on the same disk.
               (On a fast enough machine, you probably won't see this one.)

          +------------------------------------------------+
          | Not Enough Velocity Remains - Input Greater MV |
          +------------------------------------------------+
               QBALL is unable to complete a computation because the remaining
               velocity is less than 300 FPS.

          +--------------------------------+
          | Enter  Range greater than zero |
          +--------------------------------+
               You're really trying to enter "zero" -- no can do.

          +-------------------------------------+
          | Enter  0 < Range Increment <= Range |
          +-------------------------------------+
               You're trying to enter a range increment of zero, or to enter
               a range increment greater than the maximum range chosen.

          +------------------------------------+
          | Enter  300 <= Velocity <= 4500 FPS |
          +------------------------------------+
               Trying to enter a velocity less than 300 or greater than 4500
               FPS.

          +----------------------------------------------+
          | Enter  0.000 < Ballistic Coefficient < 1.000 |
          +----------------------------------------------+
               Trying to enter a value outside acceptable range of values.
               (Ballistic coefficients are, by definition, greater than zero
               and less than unity.)


         [ QBALL               --   Exterior Ballistics   --               45 ]

          Error Messages (continued)
          --------------

          +-----------------------------------+
          | Enter  Second Range > First Range |
          +-----------------------------------+
               In inferring ballistic coefficients, attempting to enter a
               second range which is smaller than the first range you have
               entered.

          +---------------------------------------+
          | Inferred C1 exceeds 1.00 - check data |
          +---------------------------------------+
               Input data is probably incorrect; ballistic coefficients
               cannot, by definition, exceed unity.

          +-----------------------------------+
          | Enter  0 < Powder Weight < 100 gr |
          +-----------------------------------+
               You're attempting to enter a zero propellant weight, or one
               more suited to artillery pieces, in determination of recoil.

          +---------------------------------+
          | Enter  0 < Gun Weight <= 20 lbs |
          +---------------------------------+
               Attempting to enter a value which is out of range.  (Are
               you really using a howitzer?)

          +-----------------------------------------+
          | Enter  Lbs + [space] + 0 <= Ounces < 16 |
          +-----------------------------------------+
               QBALL can't figure out how much your weapon weighs in the
               determination of recoil.

          +------------------------------+
          | Enter  Maximum Deviation > 0 |
          +------------------------------+
               In determining point blank range, the maximum deviation
               must exceed zero.

          +----------------------------+
          | Enter  Bullet Diameter > 0 |
          +----------------------------+
               In determining a sectional density, the bullet must have
               a diameter.

          +-----------------------------------------+
          | Maximum Deviation Reset to Sight Height |
          +-----------------------------------------+
               In determining point blank range, the maximum deviation
               cannot be less than the sight height.  (Sorry.)


         [ QBALL               --   Exterior Ballistics   --               47 ]

          Default Starting Values
          -----------------------

               QBALL uses a separate initialization file, QBALL.CFG, to set
               its display colors and several of the values with which it
               starts.  As supplied, QBALL.CFG is as follows:

                    "Typical Firearm",15,10,7,1,"Yards ","Meters",1,
                               -1,59,0,29.53,78,1,-1,-1

              Taking these in order, the individual entries result in the
         following:

          "Typical
           Firearm"  ...  Cartridge/bullet identifier 
                 15  ...  Foreground (text) color  ( = HI white)
                 10  ...  Highlighted text color   ( = HI green)
                  7  ...  Title/Info line color    ( = white   )
                  1  ...  Background color         ( = blue    )
            "Yards " ...  Unit of range measure (trailing space necessary)
            "Meters" ...  Alternate unit of range measure
                  1  ...  Sight height in inches
                 -1  ...  Noises on or off         ( = on      )
                 59  ...  Air temperature, degrees Fahrenheit
                  0  ...  Gun altitude in feet
              29.53  ...  Barometric pressure in inches of mercury
                 78  ...  Relative humidity, in percent
                 1!  ...  Relative air density at given metro
                 -1  ...  Graphics grid on or off  ( = on      )
                 -1  ...  Print prompt on or off   ( = on      )

                 (The metro values are for the STANDARD atmosphere)

              These values are also used for QBALL's internal defaults.

              If, for some reason, QBALL.EXE cannot find QBALL.CFG (either
         QBALL.CFG doesn't exist, or it's not in the current directory) QBALL
         will start with its default values, which are made available inter-
         nally through an error-trapping routine.

              Should you be VERY brave, you can modify QBALL.CFG with any text
         editor which will produce plain vanilla ASCII files.  THIS IS NOT
         RECOMMENDED; better by far to use the QBALL configuration routines



                         (There  are those  who would say that)
                         (using a text editor to modify a .CFG)
                         (file  isn't  brave;  it's foolhardy!)



         [ QBALL               --   Exterior Ballistics   --               49 ]

                                      Appendix H
                                      ----------

                                 Suggested Enhancements
                                 """"""""""""""""""""""

         Version of QBALL you are using?
              (appears in the box on screen one)______________

         What should QBALL do that it doesn't do now? _____________________

         __________________________________________________________________

         __________________________________________________________________

         __________________________________________________________________

         What does QBALL do now, but could do better? _____________________

         __________________________________________________________________

         __________________________________________________________________

         __________________________________________________________________

         Other comments, requests, gripes? ________________________________

         __________________________________________________________________

         __________________________________________________________________

         __________________________________________________________________


              If you are the first to suggest an improvement which is subse-
         quently implemented, you'll receive a free copy of the first release
         incorporating your suggestion.  It will take awhile, so please be
         patient.


                  Your name ___________________________________________

                  Street    ___________________________________________

                  City/State/Zip ______________________________________



              Send this form to:       Benjamin W. Hartley
                                       Forest Park Estates #103
                                       Jaffrey, NH        03452.


         [ QBALL               --   Exterior Ballistics   --               51 ]

                                      Appendix G
                                      ----------

                                   Registration Form
                                   """""""""""""""""

          User Questionnaire (optional)
          -----------------------------

          Version and Registration number of QBALL you are using?

               (appears in the box on screen one) V:________Reg#:__________

          Where did you initially find QBALL?
               (Bulletin Board, CompuServe, etc.)__________________________

          Do you use other ballistics programs?_____  Which one(s)?________

          _________________________________________________________________

          Order Form
          ----------
             (Author-supplied media is 5 1/4" 360k floppy formatted to be)
             (read by a standard  360k floppy drive.   Since not everyone)
             (has the same  de-archive utilities,  registered  copies are)
             (distributed in non-compressed form.                        )

          Please send the following (check appropriate box):
            +--+
            |  |  Register QBALL (most recent release) with
            |  |  all files*, source code, and manual @$60.00:   $____.___
            +--+
            +--+
            |  |  Register QBALL (most recent release) with
            |  |  all files and manual @25.00:                   $____.___
            +--+
                                              TOTAL ENCLOSED:    $____.___


                  Your name ___________________________________________

                  Street    ___________________________________________

                  City/State/Zip ______________________________________

         Please make checks payable in US funds drawn upon a US bank, or use
         USPS money orders payable to Benjamin W. Hartley, and mail to:

                                Benjamin  W. Hartley
                                Forest Park Estates #103
                                Jaffrey, NH        03452

         * less on-disk documentation