Appendix A.  (Beta test release 22 May 91)


Internal Data Structures Used by PGP
====================================

This appendix describes the data structures used internally by Pretty
Good Privacy (PGP), the RSA public key cryptography application.  The
intended audience mainly includes software engineers trying to port
PGP to other hardware environments or trying to implement other PGP-
compatible cryptography products.

Some of these data structures may change before PGP is released.  
Also, CRC-16 frame checks may be added to some packets.


Byte Order
----------

All integer data used by PGP is externally stored least significant
byte (LSB) first, regardless of the byte order used internally by the
host CPU architecture.  This is for cross-compatibility of messages
and keys between hosts.  This covers multiprecision RSA integers, bit
count prefix fields, byte count prefix fields, key IDs, and
timestamps.


Multiprecision Integers
-----------------------

RSA arithmetic involves a lot of multiprecision integers, often
having hundreds of bits of precision.  PGP externally stores a
multiprecision integer (MPI) with a 16-bit prefix that gives the
number of significant bits in the integer that follows.  The integer
that follows this bitcount field is stored LSB first, with the MSB
padded with zero bits if the bitcount is not a multiple of 8.  The
bitcount always specifies the exact number of significant bits.  For
example, the integer value 5 would be stored as these three bytes:

    03 00 05

An MPI with a value of zero is simply stored with the 16-bit bitcount 
prefix field containing a 0, with no value bytes following it.



Key ID
------

Some packets use a "key ID" field.  The key ID is the least
significant 64 bits of the RSA public modulus that was involved in
creating the packet.  For all practical purposes it unique to each 
RSA public key.


User ID
-------

Some packets contain a "user ID", which is an ASCII string that
contains the user's name.  Unlike a C string, the user ID has a
length byte at the beginning that has a byte count of the rest of the
string.  This length byte does not include itself in the count.


Timestamp
---------

Some packets contain a timestamp, which is a 32-bit unsigned integer
of the number of seconds elapsed since 1970 Jan 1 00:00:00 GMT.  This
is the standard format used by Unix timestamps.  It spans 136 years. 



Cipher Type Byte (CTB)
----------------------

Many of these data structures begin with a Cipher Type Byte (CTB),
which specifies the type of data structure that follows it.  The CTB 
bit fields have the following meaning (bit 0 is the LSB, bit 7 is the
MSB):

Bit 7:     Always 1, which designates this as a CTB
Bit 6:     Reserved.
Bits 5-2:  CTB type field, specifies type of packet that follows
           0001 - RSA public-key-encrypted packet
           0010 - RSA secret-key-encrypted (signed) packet
           0011 - Message digest packet
           0100 - Conventional key packet
           0101 - Secret key certificate
           0110 - Public key certificate
           1000 - Compressed data packet
           1001 - Conventional-Key-Encrypted data
           1100 - Raw literal plaintext data
           Other CTB packet types are unimplemented.
Bits 1-0:  Length-of-length field:
           00 - 1 byte packet length field follows CTB
           01 - 2 byte packet length field follows CTB
           10 - 4 byte packet length field follows CTB
           11 - no length field follows CTB, unknown packet length.
           The 8-, 16-, or 32-bit packet length field after the CTB 
           gives the length in bytes of the rest of the packet, not
           counting the CTB and the packet length field.



RSA public-key-encrypted packet
-------------------------------

Offset  Length  Meaning
0       1       CTB for RSA public-key-encrypted packet
1       2       16-bit length of packet
3       8       64-bit Key ID
11      ?       RSA-encrypted integer, encrypted conventional key
                packet.  (MPI with bitcount prefix)

The conventionally-encrypted ciphertext packet begins right after the 
RSA public-key-encrypted packet that contains the conventional key.



RSA secret-key-encrypted (signed) packet
----------------------------------------

Offset  Length  Meaning
0       1       CTB for RSA secret-key-encrypted (signed) packet
1       2       16-bit length of packet
3       8       64-bit Key ID
11      ?       RSA-encrypted integer, encrypted message digest
                packet.  (MPI with bitcount prefix)

If the plaintext that was signed is included in the same file as the
signature packet, it begins right after the RSA secret-key-signed 
packet that contains the message digest.  The plaintext has a
"literal" CTB prefix.



Message digest packet
---------------------

Offset  Length  Meaning
0       1       CTB for Message digest packet
1       1       8-bit length of packet
2       1       Message digest algorithm selector byte
3       16      128-bit message digest
19      4       32-bit timestamp



Conventional key packet
-----------------------

Offset  Length  Meaning
0       1       CTB for Conventional key packet
1       1       8-bit length of packet
2       1       Conventional encryption algorithm selector byte
3       ?       Key material for conventional algorithm



Conventional Key Encrypted data packet
--------------------------------------

Offset  Length  Meaning
0       1       CTB for Conventional-Key-Encrypted data packet
1	?	conventionally-encrypted data, no length field

The conventionally-encrypted ciphertext begins right after the 
CTB.  No length field follows CTB, unknown packet length.
The decrypted ciphertext may contain a compressed data packet or a
literal plaintext packet.

The conventionally-encrypted data has a 4-byte "key-check" prefix. 
This key-check prefix is inserted before encryption and discarded
after decryption.  The key-check prefix is only visible only after
decrypting the ciphertext in the packet.  The key-check prefix is
composed of two identical copies of a 16-bit random number.  During
decryption, the first 4 bytes of decrypted plaintext are checked to
see if the first 2 bytes match the second 2 bytes.  If this key-check
prefix meets this criterium, then the conventional key is assumed to
be correct.  



Compressed data packet
----------------------

Offset  Length  Meaning
0       1       CTB for Compressed data packet
1	1	Compression algorithm selector byte
2	?	compressed data, no length field

The compressed data begins right after the algorithm selector byte.
No length field follows CTB, unknown packet length.
The compressed data may decompress into a raw literal plaintext data
packet with its own CTB.



Literal data packet
-------------------

Offset  Length  Meaning
0       1       CTB for raw literal data packet
1	?	raw literal plaintext data, no length field

The raw literal plaintext data begins right after the 
CTB.  No length field follows CTB, unknown packet length.



RSA secret key certificate
--------------------------

Offset  Length  Meaning
0       1       CTB for RSA secret key certificate
1       2       16-bit length of packet
3       4       Timestamp
7       ?       User ID
?       ?       MPI of RSA public modulus n
?       ?       MPI of RSA public encryption exponent e
?       ?       MPI of RSA secret decryption exponent d
?       ?       MPI of RSA secret factor p
?       ?       MPI of RSA secret factor q
?       ?       MPI of RSA secret multiplicative inverse u
                (All MPI's have bitcount prefixes)

All secret fields in the secret key certificate may be password-
encrypted.  The public fields are not encrypted.



Public key certificate
----------------------

Offset  Length  Meaning
0       1       CTB for RSA public key certificate
1       2       16-bit length of packet
3       4       Timestamp
7       ?       User ID
?       ?       MPI of RSA public modulus n
?       ?       MPI of RSA public encryption exponent e
                (All MPI's have bitcount prefixes)



"Secret key compromised" certificate
------------------------------------

Note that a "secret key compromise" certificate is exactly the same 
as a public key certificate, but with public exponent e=0.

The current version of PGP does not generate any secret key
compromise certificates.