P O R T   L O C K I N G   H E L P
ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ


The following information is provided by PRE-Mail Systems - DIGITAL
X-Connect BBS to assist Sysops of WILDCAT! Bulletin Boards to set up
external protocols with the PORT LOCKING feature turned on in the
WILDCAT! MAKEWILD utility.

This also applies to users of QModem who lock their serial ports!  This
can, and should be done when using high speed modems with V.32 or V.42
capability to increase throughput capability.


DISCLAIMER:
ÍÍÍÍÍÍÍÍÍÍÍ

Sorry folks...gotta say the next couple of words...

We have made every effort possible to test all the options of all the
protocols listed in this file.  We do not guarantee that these externals
will work BUG FREE with your modem and hardware set-up. In fact,
PRE-Mail Systems, hereby wherefore hitherto, is not liable for any
damage caused by the recommendations or information contained herein.

If you feel brave enough to try what I'm going to tell you - please do
yourself a BIG favor....write down all your settings before you start
messing with them....that way you can at the very worst return to normal
operation.

The PORT LOCKING feature presents some unusual problems in modem setup that
must receive adjustments for the external protocols to operate correctly.


INTRODUCTION
ÍÍÍÍÍÍÍÍÍÍÍÍ

If oversimplifies for some of you experts, please bear with me.  There is so
much misunderstanding out there about modem setups and all....I wanted to
get to the basics.


RULE #1:

Port Locking is not for everyone.  In fact, the primary users of this feature
are the Courier HST or V.32 modem owners who have the ability to upspeed
to 14.4Kbps on a 9600bps CONNECT.

    [see enclosed modem 101 text file for further technical details]

If you do not own this type of modem, you will NEED a modem that can
buffer the computers data to transmit to the connected modem.

If you have neither of these - DO NOT USE PORT LOCKING - it does not buy you
anything and is not worth the trouble!!!

RULE #2:

You have to understand the language I'm going to use.

Here is a simple diagram that explains the whole shooting match:

ÚÄÄÄÄÄÄÄÄÄÄ¿          ÚÄÄÄÄÄÄÄÄ¿         ÚÄÄÄÄÄÄÄÄ¿         ÚÄÄÄÄÄÄÄÄÄÄÄ¿
³ (DTE)    ³          ³ (DCE)  ³         ³  (DCE) ³         ³    (DTE)  ³
³   #1     ³<-------->³   #1   ³<=======>³   #2   ³<------->³      #2   ³
³          ³  Cable   ÀÄÄÄÄÄÄÄÄÙ  Phone  ÀÄÄÄÄÄÄÄÄÙ   Cable ³           ³
ÀÄÄÄÄÄÄÄÄÄÄÙ                       Line                     ÀÄÄÄÄÄÄÄÄÄÄÄÙ

           DTE: Data Terminating Equipment
           DCE: Data Communication Equipment

The DTE equipment above are the computers - the DCE's are the modems...for
the sake of further discussion - your computer and your modem are DTE#1 and
DCE#1....the caller to your board is DTE#2 and DCE#2.


BASIC APPLICATION
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ-

When you "port Lock" WILDCAT! or QMODEM - the DTE#1 to DCE#1 connection
is always going to be at the speed you choose WILDCAT! or QMODEM to
default to. HST users will simply modify the MAKEWILD utility to reflect
19200 or 38400 (for HST DS) in the port lock speed entry.

Now, you will have to adjust your modem to the understand that DTE is set at
one speed and the DCE connection (i.e. to DCE#2) will be variable, depending
on the caller speed.

To do this with the Courier HST modem, you must change the &B switch from "0"
to "1".  Normal setting is &B0 which is the DCE follows the DTE connection
rate (i.e. if CONNECT 2400, the computer to modem, DTE to DCE, rate is 2400,
if the CONNECT 1200, the DTE to DCE rate is 1200 -- how wasteful)!

Do this from WCMODEM terminal or your comm package by typing:

AT &B1

Also, I suggest you set the compression OFF...this is the &K switch.  This
is optional as the normal &K1 setting auto sets to the callers setting, but
to get faster speeds - why compress already compressed ZIP or ARC files?
Again, from your terminal:

AT &K0


HANDSHAKING:
ÄÄÄÄÄÄÄÄÄÄÄ-

Now, the last step is to make sure the correct and most reliable "handshaking"
is going to occur.  Let's spend a sentence or two on handshaking:  basically,
if the DTE to DCE rate is 19200 and locked at that speed, and a caller
connects at say 2400, there is a mismatch.  The modem has to do the buffering
between the cable and the phone line!  All modems have some kind of ability
to buffer and they all have a limited size.  So they want to be able to tell
the DTE that it should stop - hold for a bit - then keep sending more when
the buffer is empty enough.  Think of it as a traffic cop!

There are two ways for the modem or DCE to do this:  Hardware or Software.

The most reliable (to me) is the Hardware...this is accomplished by turning off
the CTS pin voltage...the DTE is stopped!  So the modem must be told to do so.
This is done on the HST by assumring the &H is changed to "1".  Normally, this
setting is turned off completely as you will never need the buffering or
traffic management between the DTE and DCE.  Using your terminal:

AT &H1

The &I switch allows receive data control also....although since the DCE to DTE
rate is 19200, this should never be needed, but I suggest setting this switch
to &I2 just in case:

AT &I2


That should do it for the modem setup if you have an HST.  If there are other
modem setup's that sysops would like to give me for furthering the depth of
this document, I welcome them.  I hope this is a good starter and helps those
who are new, understand the process.


EXTERNAL PROTOCOLS & PORT LOCKING
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

Some protocols require you add special commands to the command line to
advise of port locking, for example, some versions of TModem requires
you install a COM1=19200 in your environment (i.e. autoexec.bat file) in
order that it knows the port is locked at 19200. Others, like MPt [old
PUMA] which requires the '-L 19200' addition to the command line.  While
others, like DSZ, require no additional changes to their command string.

Unfortunately, without these changes, protocols may be unaware of the
difference in port speed versus modem connect speed which provides for
erroneous transfer time estimations.  WILDCAT! does provide the %4
parameter which passes the DCE connect speed rather than the DTE connect
speed (the DTE will always be the same since it is locked!).  QMODEM
does the same with %1 as the serial port speed and %3 as the connect
speed.


I suggest you carefully read both the external protocol documentation
provided in the WILDCAT! and QMODEM manuals and each individual protocol
manual and choose what best suits your needs....but first, read on....





AndyW  <<Sysop>>  The Digital X-Connect WILDCAT!
214-517-8443  9600 V.32