CMOS_RAM.EXE:                                                       

    I. INTRODUCTION 
         Inside (almost) each and every one of the 47.2 billion IBM AT 
    clones sold daily there lives an elegant solution to the problem of 
    configuring a flexible yet easy to use computer system: the internal 
    CMOS configuration RAM. 
         When IBM designed the AT they listened to their customer's 
    grumblings enough to know that one of the major stumbling blocks for 
    the average PC and XT user was figuring out how to set the motherboard 
    DIP switches.  Business users also complained about not having a built 
    in real time clock.  (I guess the sales racked up by companies like AST 
    on their multifunction boards with clocks didn't hurt any either!)  So 
    now all AT's also have battery backed up clocks.  IBM solved both 
    problems with one IC - a clock calendar chip made by Motorola 
    (MC146818) which includes 50 bytes of user addressable non volatile 
    RAM.  This same chip is also used by many clone makers, but other 
    configurations which perform identically are possible.  
         So now, instead of flipping DIP switches to configure your 
    computer, the AT uses software to store the machine's configuration.  
    This software takes the form of a setup program provided by the BIOS 
    manufacturer, either resident in the BIOS ROM or in a disk based 
    utility called (you guessed it) SETUP.  True Blue IBM users will find 
    it on their Advanced Diagnostics Diskette.  The idea is that with this 
    program, you can quickly install or remove equipment from the computer 
    without having to search for the documentation.  In reality, the 
    success of this approach depends on the quality of the software.  Most 
    of the programs I've seen are pretty bare bones, but passable. 
         And what kind of information is stored in this ROM?  Quoting from 
    IBM's Personal Computer AT Technical Reference Manual - an excellent 
    way for those who feel their bank account is $125 too heavy to correct 
    the situation - the following information is stored in the CMOS ROM: 
         1. Clock information 
         2. Diagnostics status byte 
         3. Shutdown status byte 
         3. Diskette drive type byte - drives A and B 
         4. Fixed disk drive byte - drives C and D 
         5. Equipment byte (# of diskette drives, display adapter and math 
         coprocessor) 
         6. Low and high base memory bytes 
         7. Low and high expansion memory bytes 
         8. A checksum byte to confirm the validity of the stored data 
         In addition, there are several bytes of memory whose use IBM does 
    not specify, but instead marks them as reserved.  Perhaps they are 
    there to allow DOS to smash the 640K barrier with an additional 3 bytes 
    of slow memory. 
    
    II. THE SNAG 
         Well, this all sounds very nice and possibly even remotely 
    interesting but probably fits in the same category as general 
    relativity theory: Interesting But Of Little Use In Everyday Life (move 
    over, Albert).  Ah, but here's the rub: much like the IRS, it can cause 
    you grief without warning. 
         Think about it: what's been the problem with every battery 
    operated toy you've ever had?  That's right, (unless you broke it 
    first) eventually the batteries died!  And there's little more useless 
    than a toy with dead batteries - including your AT. 
         How long can you expect the battery life to be?  It's difficult to 
    say; many different battery types are in use.  However, two kinds 
    dominate the marketplace:  the lithium cell and the alkaline battery 
    pack.  (A few manufacturers use a rechargeable NICAD pack and claim 
    infinite life.  If you buy one of these, write to the manufacturer and 
    demand complete test results.)  The batteries are being used at a very 
    low current drain, so their lifetime is essentially equal to what the 
    manufacturer calls the shelf life.  This number varies widely, but 2 to 
    3 years is probably a typical number.  Your mileage may vary. 
         What would the symptoms of a dead battery be?  Again, it varies 
    among BIOS manufacturers, but most of them do a check of the CMOS RAM 
    at power up.  If the check bounces, the boot process will generally 
    halt with an error message.  BIOS's with disk based setup programs will 
    then assume some kind of default state, usually a lowest common 
    denominator type of setup with 512K of RAM and 1 floppy drive; those 
    with internal setup programs often just halt.  Now you have to 
    recognize that this machine - which worked fine yesterday but is now 
    mysteriously broken - only needs a new battery to be back on it's feet.  
    Otherwise, you're in for an expensive service call and some downtime. 
         Oh yes, it does need one other thing - it needs to be 
    reconfigured!  I hope you remember how many cylinders and heads your 
    hard disk has...  Well, it should be in the documentation - if only you 
    could find it.  And the diskette with the SETUP program?!  Or maybe you 
    don't really know that much about computers so the dealer you bought it 
    from configured it for you and maybe THAT GUY WENT OUT OF BUSINESS 2 
    YEARS AGO 'cause you bootlegged LOTus and WordPerfect from your brother 
    in law and maybe YOU DON'T EVEN KNOW WHAT KIND OF DISK DRIVES ARE IN 
    THE MACHINE and maybe YOU DON'T KNOW HOW TO SETUP YOUR MACHINE because 
    you've NEVER DONE IT BEFORE...  Well, no time like the present to 
    learn!  Will there be snags the first time you try it?  Of course there 
    will be!  Will there be a crucial job whose deadline comes and goes 
    while you pore over reams of documentation as the rest of the free 
    world sleeps soundly?  Of course there will be!  
         A gloomy picture isn't it?  But don't worry, be happy, now there's 
    
    III.  HOPE FOR THE DAMNED: CMOS_RAM.EXE 
         CMOS_RAM.EXE is a program whose sole purpose in life is to 
    minimize the pain of silicon senility, premature or otherwise.  How 
    does it do that?  Simple!  By storing the contents of your CMOS RAM in 
    a file while the computer is up and running, it can be quickly and 
    easily restored when the unthinkable - but inevitable - occurs.  Here's 
    how you do it: 
         Make up what I call a "disaster" floppy.  This is a bootable 
    floppy disk (consult your DOS manual or the little kid next door if you 
    don't know how to do that) with AUTOEXEC.BAT and CONFIG.SYS files 
    almost exactly the same as those which reside on your hard disk.  
    However, since you could be using this disk when things are flaky, 
    leave out most of the memory resident stuff - they might confuse the 
    issue.  In addition, I'd include a copy of your hard disk restore 
    program, a simple ASCII text editor, and something like PC TOOLS to 
    allow you to play around trying to fix whatever the problem might be.  
    Try booting from this floppy to ensure that you haven't forgotten 
    anything. 
         Oh, and one more thing should be included (flourish of trumpets): 
    CMOS_RAM.EXE!  With the disaster floppy in the diskette drive, simply 
    type cmos_ram, press return, and after a short but delightful 
    introductory screen the program will present you with 5 choices: 
         1: About the CMOS RAM 
         2: Save the contents of your CMOS RAM to a disk file 
         3: Restore the CMOS RAM from the disk file 
         4: Set the CMOS clock 
         5: Exit 
         Pressing 1 brings up a series of help screens, which basically 
    repeat the text in this document in a shorter and less witty fashion.  
    Perhaps you will prefer this. 
         Option 2 is the one you'll use first to save the CMOS RAM's 
    contents.  As long as there is around 250 bytes of available space on 
    the disk, a file called CMOS.RAM will be written and checked for validity.
         The third option is the one employed to bring your system back 
    from the dead.  As long as the program can find the CMOS.RAM data file 
    in the current subdirectory, RAM restoration will take place very 
    quickly (less than one second).  Everything should be copasetic now, 
    except that the time will be set to whatever time it was when you saved 
    the RAM.  No problem, that's what option 4 is for. 
         Option 4 allows the setting of the clock to the current date and 
    time.  This option does not affect the current DOS time, so the change 
    will not take effect until you reboot.  You can use this option 
    whenever you have to change the date or time, such as going on and off 
    daylight savings time.  Curiously, although the MC146818 has a daylight 
    savings time function, DOS does not use it.  It also has a day of the 
    week function, but DOS works that out on it's own.  Go figure. 
         One caveat: the routines I wrote for setting the time and date 
    will work for any BIOS that follows the IBM guidelines.  I have tested 
    the program on machines with Phoenix, Award, and AMI BIOS's, and it 
    works on all of them.  However, it would be possible to design a 
    hardware/software system for which this program would not work 
    correctly.  However, it should not damage the system in any way. 
         Do I have to explain the fifth option? 
    
    IV.  DEALING WITH DISASTER 
         So it's finally happened - your AT won't boot up.  Does it give 
    you a message relating to an invalid configuration, or anything else 
    that makes you think it could be the CMOS RAM?  A typical example would be:

    Invalid configuration information - please run SETUP program Strike the 
    F1 key to continue 
         Your next move depends on your machine.  Units with ROM based 
    setup programs usually won't proceed any further no matter what you do.  
    You must press a key, or combination of keys, to enter the setup 
    routine and configure the system to at least recognize the A: floppy 
    drive.  Don't bother with the rest of the information; running CMOS_RAM 
    as explained in the next paragraph will take care of that as long as 
    the machine will boot. 
         Computers with disk based SETUP programs have it easier.  These 
    machines usually allow the A: floppy to work no matter what the 
    contents of the CMOS RAM are, so just whip out your disaster floppy and 
    run CMOS_RAM.  Select option 3, and then set the time and date with 
    option 4.  If no error messages result, open the drive A: door and 
    reboot the machine with CTRL-ALT-DEL.  You should be up and running 
    that fast!  
         But now you're faced with replacing the battery.  This means you 
    or a technically oriented friend upon whom you can impose are going to 
    have to open up the machine and get a replacement for the battery.  The 
    more conservative among us might be well advised to make a hard disk 
    backup before opening the machine.  If you just know how to use a 
    screwdriver, and how to replace the batteries in a flashlight, you 
    should be able to do the work yourself.  Computer hardware knowledge is 
    usually not required.  A hint: most batteries are either stuck to the 
    back wall of the computer in a holder or on the motherboard in a "coin 
    cell" holder.  
         However, in some cases it still may be worthwhile to take your 
    computer to an authorized repair station.  An example of such a case 
    would be if opening the computer required a tool you've never seen 
    before, or if you really are just all thumbs with hardware.        
    
         A WORD OF WARNING: 
         Do I really have to remind you to unplug the computer before 
    opening the case?  Please do.  Also, never touch anything on a printed 
    circuit board without touching a large metal object first.  This is not 
    a good time to wear your knit sweaters... anything with "static cling" 
    is a bad idea! 
         If your machine uses 4 alkaline AA cells, you can just run to the 
    corner convenience store and pick up replacements.  Be sure to get a 
    reliable alkaline brand, such as Eveready, Duracell, Radio Shack, or 
    Kodak.  Look for a good expiration date.  If the batteries simply slip 
    into the holder, put a sturdy rubber band around the holder to hold 
    them securely in case of rough handling.  
         Those with lithium batteries are in for a little rougher time 
    locating a replacement.  Luckily, our friends at Radio Shack have a 
    rather nice selection of replacement batteries, including some which 
    look as though they should do the job for most models.  If not, the 
    Radio Shack catalog says they will special order any battery, although 
    I don't know how good they are.  As a last resort, you may have to 
    contact your manufacturer. 
         ANOTHER WORD OF WARNING: 
         NEVER EVER EVER carry a lithium battery loose in your pocket or in 
    a purse.  When shorted - such as with coins or keys - lithium batteries 
    are an explosion and burn hazard.  These cells pack a hefty wallop, and 
    while current types have an over-pressure venting system DON'T TRY IT!  
    Put the cell in an envelope, wrap tape around it, or figure out some 
    other way to insulate it.  Leave the new cell in it's protective 
    packaging until you're ready to use it.  Also, be sure to dispose of 
    the old cell per the manufacturer's instructions. 
         Another thought to share with you:  you can't ease the replacement 
    process the next time by buying two sets of batteries and keeping one 
    aside.  Since the battery's lifetime is essentially equal to it's shelf 
    life, when the one in use quits the other will be at the end of it's 
    life also.  Buy a fresh one. 
         Once the battery is in place, go through the ritual outlined above 
    one last time, and then you're back in business. 
    
    V. WAIT, THERE'S MORE 
         Well, it seems that CMOS_RAM has made the world safe for truth, 
    justice, and the American way.  By taking a few minutes to prepare 
    before disaster strikes, I say BEFORE DISASTER STRIKES, a potentially 
    expensive service call can be handled by anyone with a basic knowledge 
    of tools and the inside of a computer. 
         However, one problem with a program like CMOS_RAM is that it's 
    easy to use it and forget about it.  After all, it could be several 
    years until you need it.  In that time, you could easily change your 
    hardware and forget to update CMOS.RAM, defeating the program's purpose 
    and increasing your hassles. 
         Enter CHEKCMOS.  Just install this program in your AUTOEXEC.BAT 
    file along with a copy of CMOS.RAM in the same directory.  This program 
    helps you two ways.  First, it checks two self test status functions of 
    the MC146818 IC to ensure that it's data is valid and that the battery 
    voltage is within the allowable limits.  If either of these checks 
    fails, a warning is generated.  In theory, this should serve notice 
    that the battery is on it's last legs in time to replace it.  However, 
    in the real world, batteries often fail suddenly, so don't count on 
    knowing in advance. 
         The other function of CHEKCMOS is to make sure that the contents 
    of the file CMOS.RAM match what's in the CMOS RAM itself, with the 
    exception of the time and date.  This will remind you to update 
    CMOS.RAM when you make a hardware change.  Also, it will absolutely 
    find any CMOS RAM failures which go undetected by the IC's self test 
    features.