DISKBUF

                   A Program to Optimize the BUFFERS= Setting
                                 Version 2.20(4)

                                       by

                                  W. G. Madison


                               Copyright 1987, '89 
                        W.G. Madison and Associates, Ltd.
                              All rights reserved.


                                November 6, 1989


        NOTICE: The program DiskBuf and this associated documentation are 
        copyrighted products. They may be freely distributed, provided 
        only that both the program and documentation are distributed 
        together, that no modification is made to either the program or 
        the documentation, and that no charge other than a copying charge 
        not to exceed $6.00 is levied on the recipient. Disk distributors 
        may include promotional text with this program, provided that 
        such text appears as a separate file or as text appended to this 
        documentation. If appended to this document, such text must be 
        readily identifiable as to its source and must appear ONLY at the 
        end of the document file. Finally, neither the author nor MADISON 
        AND ASSOCIATES assume any responsibility or liability for actual 
        or consequential damages arising from the use of this program, 
        even if they have been notified in advance of the possibility of 
        occurrence of such damages.

        We would like to know of your experience with DiskBuf. Please 
        address any criticisms or comments to:

                        W.G. Madison and Associates, Ltd.
                        Consultants / Information Systems
                                  P. O. Box 898
                               Greenbelt, MD 20770
                                  (301)552-7234
                             (CompuServe  73240,342)


                * * * * * * * * * * * * * * * * * * * * * * * * *


        Acknowledgment: Release 1 of this program was based upon ideas 
        gleaned from the public domain program THRASHER, by Monte Fergu-
        son of Ravenna, OH. This release, 2.00(2), has been enhanced as a 
        result of several user suggestions received over the intervening 
        two years. My thanks to all who have contributed.




                                   1




        Disclaimer: This program is provided AS IS, with no claim for 
        suitability for any particular purpose. Specifically, since the 
        program is necessarily extremely disk intensive and therefore 
        exercises the head positioning mechanism far more than is custom-
        ary in normal use, the Author and W. G. Madison and Associates, 
        Ltd. disclaim any and all responsibility for actual and/or con-
        sequential damages to hardware and/or files resulting from the 
        use of this program.


        INTRODUCTION:

             All personal computers using the DOS operating system (PC-
        DOS, MS-DOS, etc.) use buffered I/O when reading from or writing 
        to the disk, unless the programmer who wrote the software being 
        used went to great lengths to avoid it. The number of buffers 
        used is specified in the file CONFIG.SYS, which is read at the 
        time the computer is booted up.

             If you are not familiar with the CONFIG.SYS file or with the 
        concept of buffered I/O, it is strongly suggested that you refer 
        to your DOS reference manual before proceeding further.

             The problem of determining the proper number of buffers with 
        which to configure a DOS computer is, at best, inadequately add-
        ressed in most DOS reference manuals. Generally, the suggested 
        approach is "Try a number, then use your computer, then try 
        another number. Keep repeating this process until you are either 
        fed up or have arrived at something which gives acceptable per-
        formance." Some reference manuals give a suggested value to be 
        used by those looking for an easy out. This suggested value may 
        or may not yield performance which is close to optimum.

             DiskBuf provides a method for scanning through an entire 
        range of values while you go out for coffee (or something 
        stronger).


        WHY WORRY ABOUT THE NUMBER OF BUFFERS?

             As might be expected, buffering uses RAM. Specifically, each 
        buffer added to a DOS system uses 33 paragraphs (528 bytes) of 
        RAM. Assuming that plenty of RAM is available, it might be tempt-
        ing to take the approach, "Let's just set the number of buffers 
        way up, and fly with that." Unfortunately, one can reach the 
        point where more time is spent searching buffers for information 
        than is necessary or desirable. A point of diminishing returns is 
        reached.

             Similarly, too few buffers will cause the computer to go to 
        the disk more often than necessary. And, since disk operations 
        are dreadfully slow in comparison to memory operations, unaccept-
        able performance degradation will result.




                                   2




        WHY USE THE DISKBUF PROGRAM TO SOLVE THE PROBLEM?

             Basically, without an intimate knowledge of the insides of 
        DOS plus a penchant for solving complex mathematical problems, 
        there are three feasible methods for attacking the problem. The 
        first is to pick a number (based either upon your liking for 
        indulging in Russian roulette, or upon recommendations from 
        friends or the DOS reference manual) and put your trust in the 
        tooth fairy as to the appropriateness of the number. The second 
        is to try to determine the number by systematic trial and error, 
        editing your CONFIG.SYS file over a period of time. The third 
        method is to set up an automatic process which can sweep through 
        a series of values, perform a realistic test with each value, and 
        record the results for later analysis.

             The DISKBUF program permits this third approach to be taken 
        easily. By using DISKBUF, you can readily determine the optimum 
        number of buffers to be used, based not only upon time to perform 
        the test but also upon the amount of RAM occupied by the buffers. 
        You can decide, and have some rational basis for the decision, 
        whether you are willing to sacrifice X bytes of additional RAM in 
        order to gain an additional Y% performance improvement from your 
        disk operations.


        HOW DO I USE DISKBUF?

             CAUTIONARY NOTE: If you are using cache in other than normal 
        memory, under certain circumstances the automatic re-boot will be 
        inhibited; you will have to manually re-boot at the end of each 
        test cycle. No other ill effects seem to occur, however, and the 
        test results appear to be still valid. We have not yet been able 
        to determine the cause or specifically state the exact circum-
        stances under which this will occur.

             Nine files are included in the file DISKBUF.ZIP. They are, 
        respectively:

                  DISKBUF.DOC    (This file)
                  DISKBUF.EXE    (The operational program)
                  AUTOEXEC.BAT   (A specimen AUTOEXEC file)
                  BUFTST-1.EXE   (One of the two provided test modules. 
                                 This is the test you would probably want 
                                 to use if your typical activity involved 
                                 accessing many files scattered over the 
                                 disk.)
                  BUFTST-2.EXE   (The second of the two provided test 
                                 modules. This is the test you would 
                                 probably want to use if your typical 
                                 activity involved random accessing of a 
                                 relatively few large files.)
                  BUFFTEST.EXE   (A copy of BUFTST-1.EXE. This copy is 
                                 the one which will actually be used in 
                                 testing.)



                                   3




                  PLOTFM.EXE     (A stand-alone program to produce plots 
                                 of figures of merit.)
                  PLOTBUF.COM    (The plot driver program to produce a 
                                 screen plot of the test results. Used by 
                                 both DISKBUF and by PLOTFM. Assumes a 
                                 CGA card. DO NOT ATTEMPT TO RUN PLOTBUF 
                                 AS A STAND-ALONE PROGRAM.) 
                  UPDATE.DOC     (The revision history of DISKBUF.)

             Examine the AUTOEXEC.BAT file. You will see, as the last 
        line of the file, the line invoking DISKBUF. In the REMark lines 
        preceding this, you will see guidelines for setting the switch 
        values to be passed to DISKBUF. The switches are:

                            /TARGET=     (Sets the disk to be tested)
                            /MAXBUF=     (Sets the stopping point (maxi-
                                         mum number of buffers) for the 
                                         test)
                            /MINBUF=     (Sets the starting point (mini-
                                         mum number of buffers) for the 
                                         test)
                            /PLOT        (If present, a screen plot of 
                                         the test results will be pro-
                                         duced)

             The first two switches, /TARGET= and /MAXBUF= are required; 
        the other two, /MINBUF= and /PLOT are optional.

             /TARGET=xx     takes as an argument a valid disk device 
        designator, with the appended colon being optional. This deter-
        mines the device or partition which is to be tested. (Required)

             /MAXBUF=nn     takes as an argument an integer between 1 and 
        99, and determines the greatest number of buffers to be used in 
        the test. (Required)

             /MINBUF=nn     also takes as an argument an integer between 
        1 and 99, and determines the starting number of buffers to be 
        used in the test. If this switch is omitted, a starting value of 
        3 will be used. (Optional)

             /PLOT          determines by its presence or absence whether 
        or not a screen plot of the test results will be produced at the 
        completion of the test. NOTE: If your computer does not have a 
        graphics card, this switch must not be included! (Optional)


             To use DISKBUF, the following steps are required.

             STEP 1.   Format a floppy disk using the /S switch to make 
        the disk bootable.

             STEP 2.   Edit the AUTOEXEC.BAT file provided with the 
        DISKBUF distribution set, to invoke DISKBUF with the switch set-
        tings you want used.


                                   4





             STEP 3.   Copy the edited AUTOEXEC.BAT file and the program 
        file DISKBUF.COM onto the disk prepared at Step 1.

             STEP 4.   Copy your own CONFIG.SYS file onto the disk 
        prepared at Step 1. If necessary, edit the CONFIG.SYS to make 
        sure that the BUFFERS= parameter is ***OUTSIDE*** the range 
        determined by the MAXBUF= and MINBUF= parameters in the 
        AUTOEXEC.BAT file. (For that matter, if you simply delete the 
        BUFFERS= line from the CONFIG.SYS file, DISKBUF will manage it 
        appropriately.)

             STEP 5.   Copy any device drivers to be installed by the 
        CONFIG.SYS over to the floppy. Do the same for any resident 
        programs to be installed by the AUTOEXEC.BAT.

             STEP 6.   Copy DISKBUF.EXE to the floppy. If /PLOT is 
        selected in the AUTOEXEC.BAT, copy PLOTBUF.COM and, optionally, 
        PLOTFM.EXE to the floppy.

             STEP 7.   Decide, based on the descriptions given above, 
        which of the two test modules you wish to use. Copy the desired 
        module to the floppy as BUFFTEST.EXE using the DOS COPY command. 
        (For the average user, we believe that BUFTST-1.EXE more nearly 
        reflects typical usage; it is therefore the one already set up.)

             STEP 8.   Re-boot your computer.

             STEP 9.   Go to lunch, and come back in an hour or so. 
        (Optional)


             When the test is completed, a new file will be on the 
        floppy disk:

                  BUFFERS.RPT contains the test results, giving for each 
                              number of buffers tested a figure of merit 
                              and the minimum requirement of RAM (in 
                              bytes) for DOS (given the set of device 
                              drivers and resident programs present dur-
                              ing the test.)


             The figure of merit for a given number of buffers is propor-
        tional to the time required for the test. Thus, SMALLER is 
        BETTER. The minimum figure of merit is the one you want (ignoring 
        the amount of space occupied by the buffers).

             Note that, if /PLOT was selected, the screen plot only dis-
        plays a limited range of the figure of merit values. Specific-
        ally, the range displayed is from the minimum figure of merit to 
        5% greater than this value. All figures of merit greater than 
        this are clipped at this level for plotting purposes. This was 
        done in order to better present the detail of the values only 
        slightly worse than the minimum value.


                                   5





             The screen plot may be recreated at any time by running 
        PLOTFM. The only restriction is that the file BUFFERS.RPT and 
        PLOTBUF.COM must be in the current disk and directory. 

             Should you wish to test against two different disks or re-
        test a disk using two different tests, the file BUFFERS.RPT must 
        be copied or renamed before the second test is conducted. If this 
        is not done, the files will be over-written and the results of 
        the earlier test will therefore be lost.

             Should you wish to re-test the disk using the other provided 
        test, simply return to Step 7 above and proceed from there. It 
        will not be necessary to edit the CONFIG.SYS file, since (unless 
        you are also increasing the MAXBUF= setting in the AUTOEXEC.BAT 
        file) the BUFFERS= setting is guaranteed to be outside the 
        testing range.


        CAN I INCLUDE A DOS SIZE CONSIDERATION IN THE FIGURE OF MERIT?
        RUNNING PLOTFM.

             As mentioned above, the calculated figure of merit is pro-
        portional to the time required to run the test. In most cases, it 
        is felt that this is an appropriate indicator.

             We recognize, however, that there may be installations in 
        which RAM is critical. For these installations, or if you just 
        want to re-display the results of an earlier test, the module 
        PLOTFM.EXE is provided.

             PLOTFM.EXE accepts one required and two optional command 
        line parameters. 

               PLOTFM <rpt-file> [<time-weight> [<space-weight>]]

             <rpt-file> is the name of the DISKBUF output file to be 
        used. If no extension is provided, .RPT is assumed.

             <time-weight> is the relative weight to be given to the time 
        variable in the calculation of figure of merit.

             <space-weight> is the relative weight to be given to the 
        space variable (i.e., DOS paragraphs) in the calculation of 
        fighre of merit.

             If the two weight factors are omitted from the command line, 
        the plot produced at the completion of testing will be repro-
        duced. (<time-weight> defaults to 1; <space-weight> defaults to 
        0).

             Thus, the following are equivalent:

                                 PLOTFM TEST-A



                                   6




                                 PLOTFM TEST-A.RPT

                                 PLOTFM TEST-A 1 0

                                 PLOTFM TEST-A.RPT 1

        and each will produce the same plot display as that produced at 
        the conclusion of the DISKBUF test run.

             We have found that many installations will wish to take 
        space into account, but not very heavily. In nearly all cases, 
        basing BUFFERS= settings on plots produced with time weights 20 
        to 30 times greater than the space weight seems appropriate. 

             Should RAM be an **EXTREMELY** scarce resource for you, you 
        might wish to examine the display produced with a time weight as 
        small as 5 times the space weight.

             In calculating the figure of merit, both the time and space 
        factors are normalized; each time factor is divided by the mini-
        mum observed time factor and each space factor is divided by the 
        minimum observed space factor. The normalized factors are then 
        multiplied by the appropriate weight, and the weighted factors 
        are added. This sum is then divided by the sum of the weights to 
        give a normalized figure of merit. Finally, this normalized fig-
        ure of merit is multiplied by the minimum observed time factor to 
        yield the actual figure of merit. 

             


        HOW CAN I DESIGN MY OWN TEST MODULES?

             Two fundamentally different test modules are provided which 
        represent quite different testing scenarios. 

             BUFTST-1.EXE examines the directory entry for each file in 
        every directory on the disk being tested. Thus, it simulates a 
        situation in which the user is accessing many files in any given 
        session.

             BUFTST-2.EXE writes a single large (1000 record, 100 bytes 
        per record) file in the root directory of the target disk. It 
        then interchanges record 1 with record 1000, record 2 with record 
        999, etc. Having completed this sub-test, it then interchanges 
        record 1 with record 2, record 2 with record 3, ... record 999 
        with record 1000. Thus, it simulates both sequential and random 
        usage of large files.

             You are free to generate your own tests as you will. These 
        tests can be implemented in either executable (.EXE or .COM) 
        files, or in batch control (.BAT) files. In either case, the file 
        name **must** be BUFFTEST (i.e., BUFFTEST.COM, BUFFTEST.EXE, or 
        BUFFTEST.BAT). The test module must expect a single command line 
        parameter of the form <d>:\ where <d> is the drive letter of the 


                                   7




        drive to be tested. 

             One word of caution. It is important that the operations 
        being performed be exactly duplicated from run to run, if the 
        output data are to accurately reflect your system behavior. Thus 
        if you have, e.g., put together a batch file (BUFFTEST.BAT) which 
        performs a MAKE, it is important that you recognize ahead of time 
        just which files will be created as a result of the MAKE, and 
        delete them prior to terminating your BUFFTEST.BAT.
















































                                   8




        HOW DOES DISKBUF DO ALL THAT GOOD STUFF?

             When DISKBUF is invoked, it performs the following 
        steps:

             STEP 0.   Read and parse command tail. Set operating par-
             ameters, based on the contents of the command tail.

             STEP 1.   Edit the file CONFIG.SYS on the floppy disk.

                  STEP 1A.   If the BUFFERS= line is present, read it to 
                  extract the current BUFFERS=  setting. 


                       STEP 1A1. If this setting is not between MINBUF 
                       and MAXBUF then re-write CONFIG.SYS with a 
                       BUFFERS=  setting equal to the value of MINBUF, 
                       and go to STEP 1C.

                       STEP 1A2. If the setting is between MINBUF and 
                       MAXBUF then go to STEP 2.

                  STEP 1B.  If not present, append a BUFFERS= statement 
                  with a BUFFERS= setting equal to the value of MINBUF.

                  STEP 1C.  Delete the BUFFERS.RPT file if it is pres-
                  ent, and re-boot the system.

             STEP 2.   Start the timer. 

             STEP 3.   Perform the selected test.

             STEP 4.   Stop the timer.

             STEP 5.   Calculate the figure of merit, and append a record 
             to BUFFERS.RPT.

             STEP 6.   Check the current setting of BUFFERS= against the 
             value of MAXBUF.

                  STEP 6A.  If buffer setting < MAXBUF, re-edit the 
                  existing CONFIG.SYS file, incrementing the buffer set-
                  ting and re-boot the system.

                  STEP 6B.  Otherwise, the test is completed. 

                       STEP 6B1. Leave the CONFIG.SYS file on the floppy 
                       disk with a BUFFERS= setting at MAXBUF + 1.

                       STEP 6B2. If /PLOT is selected, plot the test 
                       results.

                       STEP 6B3. Exit to DOS.




                                   9

























































                                   10