Kill QWK Dupes Version 1.10                            Kill QWK Dupes Version 1.10
          (C) Copyright 1991, 1992 by Dataware, Inc.  All rights reserved.          (C) Copyright 1991, 1992 by Dataware, Inc.  All rights reserved.





                                 Table of Contents                                 Table of Contents

       System Description                                                   1
       System Requirements                                                  1
       Technical Support                                                    1
       Registration                                                         2
       Software License                                                     2
       How to use Kill QWK Dupes - Overview                                 3
       How to use Kill QWK Dupes - The command line                         3
       Command Line Options                                                 5
           -Log:[d:][path]filename                                          5
           -CF:[d:][path]filename                                           6
           -DC:nnnn                                                         6
           -DN:name                                                         6
           -MC:32-32756, default is 32756                                   7
           -MD:1-24855, default is 24855                                    7
           -NC:1-32767, default is 3                                        7
           -Com:1-4 or NNNN                                                 7
           -FSL                                                             8
           -NoFSL                                                           8
           -NDX                                                             8
           -NoNDX                                                           8
           -NoKill                                                          8
           -Kill                                                            9
           -NoBAK                                                           9
           -IS                                                              9
       Use of the KILLQDUP environment variable                             9
       Appendix A: How Kill QWK Dupes operates                             10
       Appendix B: How to install Kill QWK Dupes into the MarkMail door    11
       Appendix C: How to install Kill QWK Dupes into the Qmail door       14
       Appendix D: How to install Kill QWK Dupes into the RoseMail door    16
       Appendix E: How to install Kill QWK Dupes into the Tomcat! door     18
       Appendix F: How to install Kill QWK Dupes into the Jetmail door     20
       Appendix G: How to install Kill QWK Dupes into the Auntie door      22
       Appendix H: Multi-node considerations                               22
       Appendix I:Errorlevels returned by Kill QWK Dupes                   23
       History                                                             24



















                                          i





       System Description       System Description
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       Ever download a QWK mail packet from your favorite BBS, only to find
       an overwhelming number of duplicate messages?  Or import a netmail
       packet into your BBS and discover 1/10-1/2 of the messages are
       duplicates re-exported by some other node in the network (maybe you've
       accidentally done this yourself)?  Are you getting tired of users
       uploading old REP packets more than once causing duplicate messages to
       be stored in your message base?  Then Kill QWK Dupes is for YOU!

       Kill QWK Dupes will remove duplicate messages from your QWK and/or REP
       packets.  It accomplishes this by maintaining its own independent CRC
       table of past messages (including those from previous packets), and
       removes messages from the current packet that match the CRC of a
       message stored in the table.  It will even rebuild the *.NDX files
       such that a QWK packet continues to be usable by the QWK compatible
       offline readers (this feature can even be used to generate *.NDX files
       for a QWK packet that doesn't have them, or has had them corrupted
       somehow).


       System Requirements       System Requirements
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       Kill QWK Dupes will run on any IBM PC or compatible with DOS 2.0 or
       higher and at least 96k of free memory.  Kill QWK Dupes is very light
       on code, but heavy on data space (depending on the size of the CRC
       table you specify).


       Technical Support       Technical Support
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       If you have any questions or problems regarding Kill QWK Dupes or any
       other Dataware product, please call our office for assistance.  Our
       office hours are Monday through Friday, 9:30am-5:30pm Pacific time.
       You can also leave a message or pick up the latest versions on our 24-
       hour BBS named "The Real Batchin' Board".  You may also mail your
       comments and questions to the Dataware office.  The Dataware address
       and phone numbers are as follows:

            Dataware, Inc.
            Suite 2571
            1420 NW Gilman Boulevard
            Issaquah, Wa.  98027-7001

            Voice (9:30am to 5:30pm PT): (206) 391-9333

            The Real Batchin' Board BBS (available 24 hours): (206) 391-2330









                                          1





       Registration       Registration
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       If you find that Kill QWK Dupes is useful to you, you can become a
       registered user.  As a registered user, you will receive a diskette
       with the latest registered version on it.  The 45 day expiration code
       present in the unregistered version is disabled in the registered
       version.  You will also automatically receive, when available, a free
       upgrade to the next version of Kill QWK dupes.  You will also receive
       the password necessary to download all future registered version from
       the support BBS.  The current registration fees are as follows:

            Kill Qwk Dupes Version                               $9.95
            Laser Printed Manual                                 $5.00
            Ups Ground                                           $3.00
            Ups Second Day Air                                   $6.00
            Ups Next Day Air                                    $12.00
            All Over-seas Shipping                               $6.00
            Washington residents add 8.2% sales tax to the total


       Software License       Software License
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       You are free to use (for a 30 day evaluation period), copy and
       distribute Kill QWK Dupes IF:                                 IF

            - No fee is charged for its use, copying or distribution.
            - It is not modified in ANY way.

       Dataware hereby disclaims all warranties relating to this software,
       whether express or implied, including without limitation any implied
       warranties of merchantability or fitness for a particular purpose.
       Dataware will not be liable for any special, incidental,
       consequential, indirect or similar damages due to loss of data or any
       other reason, even if Dataware or an agent of Dataware has been
       advised of the possibility of such damages.  In no event shall
       Dataware's liability for any damages ever exceed the price paid for
       the license to use software, regardless of the form of the claim.  The
       person using the software bears all risk as to the quality and
       performance of the software.

       Sysops who run more then one BBS (as determined by the name they go
       by) are required to register one copy for each separate and distinct
       BBS name in which Kill QWK Dupes is being run on as part of a QWK
       compatible mail door.  Multi-node sysops of the same distinct BBS name
       need register only one copy for all nodes regardless of how many
       different machines and how many different QWK compatible mail doors
       Kill QWK Dupes may be running on.  Users need register only copy for
       use with all BBS's they may call.  Network connected sysops need
       register only one copy for use with all networks they are connected
       to.






                                          2





       How to use Kill QWK Dupes - Overview       How to use Kill QWK Dupes - Overview
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       Kill QWK Dupes can be used in a number of environments.  As a node in
       a network, you can use it to scan your incoming QWK packets and/or
       your outgoing REP packets.  As a sysop of a BBS that has a QWK
       compatible mail door, you can use it to scan the REP packets uploaded
       by your users.  NOTE: DO NOT use it to scan the QWK packets downloaded
       by the users unless the -NoKill parameter is used (described below),
       because all subsequent packets after the first one would appear as
       duplicates to the program and automatically removed from the users
       packet.  As a user of an offline reader, you can use it to scan the
       QWK packets you receive from your favorite BBS and/or the REP packets
       you're uploading to the BBS.

       Kill QWK Dupes does not automatically extract the files out of the QWK
       and REP packets it works on.  Nor does it automatically merge them
       back in after processing.  That was deliberately left out of the
       program due to the myriad of compression programs being used today
       with QWK/REP packets.  In addition, this makes it a perfect fit in for
       scanning a freshly extracted .REP packet.  We also wanted to stay away
       from a configuration file for this program, so you'll find everything
       is command line and environment variable driven.  In addition, it is
       intended to be run in a batch file, therefore it does no prompting for
       information.  If it doesn't have enough information, or runs into an
       error while running, it simply reports the error and exits.

       Kill QWK Dupes works on the MESSAGES.DAT file after having been
       extracted from the QWK file.  It also works on the BBS_ID.MSG file
       after having been extracted from the BBS_ID.REP file.  If you ask it
       to rebuild the *.NDX files contained in QWK packets (so that your
       offline reader can continue to read the packet), it also requires the
       CONTROL.DAT file be extracted from the QWK file.  It uses information
       contained in this file to properly rebuild the *.NDX files.


       How to use Kill QWK Dupes - The command line       How to use Kill QWK Dupes - The command line
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       Kill QWK Dupes is easy to use and fast.  You tell Kill QWK Dupes what
       to do by what you enter on the command line at the DOS prompt or via
       an environment variable (explained below).  All command line options
       that Kill QWK Dupes recognizes, along with examples, are explained in
       the following sections.

       The Kill QWK Dupes command line structure is as follows:

       KILLQDUP [d:][path]qwkfile [options]

       [d:][path]qwkfile = The name and path location of the QWK file to be
       scanned.  If you're scanning a QWK packet, the filename should be
       MESSAGES.DAT.  If you're scanning a REP packet, the filename should be
       BBS_ID.MSG (where BBS_ID is the 1-8 character ID used by your BBS).
       NOTE: Parameters listed in [] are optional.

       options = All the various Kill QWK Dupes options that you can use.


                                          3






       A simple example is as follows:

   C:\QPACKETS> KILLQDUP messages.dat

   Kill QWK Dupes v1.00. (C) Copyright 1991 by Dataware, Inc.
   UNREGISTERED version.  This version will cease to function 45 days after
   activation.  After the normal 30 day evaluation period, you will have 15 days
   in which to obtain your registered version before the software automatically
   ceases to function.  After 45 days, you will have to delete your CRC file
   (default filename MSGSDUPE.CRC) to re-enable the software.

   QWK file to be processed  : MESSAGES.DAT
   CRC tracking file         : MSGSDUPE.CRC
   Number of CRC's to track  : 32768
   Number of days to track   : 24855
   Use FOSSIL driver         : No
   Rebuild .NDX files        : No
   Remove duplicate messages : Yes

   This software will cease to function on Friday September 06,1991 @10:56PM
   Total messages checked    : 97
   Total duplicates purged   : 1
   Total processing time     : 2 seconds

       When Kill QWK Dupes starts up, it begins by displaying the copyright
       message and some status information about what it's going to do.  It
       reports the file name it will process, the logfile (if any) it will
       write its output status to, the Comm. port it will talk to, whether or
       not it will use a FOSSIL driver for accessing the Comm. port, the name
       of the CRC file it will use for checking the CRC's, whether or not the
       *.NDX files will be built, the number of CRC's it will maintain before
       throwing away the oldest ones, and finally the number of days CRC's
       will be kept in the table before being thrown away.  Additionally, if
       you have the unregistered version, it will also report exactly when
       your 45 day evaluation period will end.

       Kill QWK Dupes then starts its processing by making a .BAK copy of the
       original QWK file.  You will find a MESSAGES.BAK file, or a BBS_ID.BAK
       file after it's done, which is an exact copy of the original input
       file.  This is just a precaution in case something goes seriously
       wrong while processing.

       Next, Kill QWK Dupes looks at the file to see if it has been
       previously scanned before (every file is marked with the date it was
       last scanned, and the location it stopped scanning).  If it has been
       previously scanned, Kill QWK Dupes will automatically advance to the
       point in the file where it last stopped and resume scanning.  This
       feature is most useful to netmail sysops scanning their .REP packets
       prior to uploading to their HUB.  If a .REP packet is created by an
       EXPORT function and scanned, and then sometime later more messages
       appended to it (such as a transfer with your HUB failed), scanning the
       packet again will not result in removing all the older messages as
       duplicates.


                                          4






       During its processing, Kill QWK Dupes will display a percent
       completion status every second.  This indicator tells you what percent
       of the input file has been scanned.  When it reaches 100%, processing
       is complete and a status summary is displayed.  The status summary
       tells you how many messages in the input file were scanned, how many
       duplicates were removed from the input file and how many seconds it
       took to run.


       Command Line Options       Command Line Options
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       There are 12 command line options you may give to Kill QWK Dupes.
       They options are used to select a Logfile, the CRC file, the size of
       the CRC file, the Comm. port to use, whether or not to use a FOSSIL
       driver, whether or not to rebuild the *.NDX files, whether or not to
       actually remove duplicate messages.  Each of them will be explained in
       detail in the following sections


       -Log:[d:][path]filename       -Log:[d:][path]filename
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       This option causes the status summary that's displayed on the screen
       to also be written to a text file.  This is very useful for unattended
       operation, such as automated netmail runs, or REP packet uploads into
       a mail door.  Five pieces of information are written to the log file
       every time Kill QWK Dupes is run.  First the date & time Kill QWK
       Dupes was run is recorded.  Next the name of the mail packet file
       processed is recorded.  Next, the count of the number of messages
       scanned is recorded.  Following that the number of duplicate messages
       removed is recorded.  And lastly, the total number of seconds used in
       processing is recorded.  A logfile will look like the following:

       *****************************************
       Kill QWK Dupes run on 08/07/91 at 21:25
         QWK file MESSAGES.DAT processed
           Total messages checked   : 804
           Total duplicates purged  : 5
           Total processing time    : 42 seconds
       *****************************************
       Kill QWK Dupes run on 08/07/91 at 21:27
         QWK file MESSAGES.DAT processed
           Total messages checked   : 882
           Total duplicates purged  : 1
           Total processing time    : 52 seconds
       *****************************************
       Kill QWK Dupes run on 08/07/91 at 21:28
         QWK file MESSAGES.DAT processed
           Total messages checked   : 1014
           Total duplicates purged  : 1
           Total processing time    : 50 seconds
       *****************************************
       Kill QWK Dupes run on 08/07/91 at 21:31
         QWK file MESSAGES.DAT processed


                                          5





           Total messages checked   : 97
           Total duplicates purged  : 0
           Total processing time    : 3 seconds


       -CF:[d:][path]filename       -CF:[d:][path]filename
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       This option is useful in many circumstances.  As a user of multiple
       BBS's, you should keep separate CRC files, one for each BBS you use.
       If you try and use the same CRC file for two or more BBS's, you run
       the risk of similar messages between the two BBS's being invalidly
       removed from the QWK packets.  In addition, if you send the same
       message to two or more BBS's, that message will probably be removed
       from the REP packet as it is scanned.

       As a node calling two or more HUB's for netmail, you should keep
       separate CRC files for the same reason as a user of two or more BBS's.

       As a sysop of a BBS that has a QWK compatible mail door and is also a
       node in a network, you should use different CRC files for the REP
       packet uploads and the netmail scans.  If you try and use the same
       packet, the messages uploaded by your users will be seen as duplicates
       by Kill QWK Dupes and removed when it scans your netmail REP packet.

       As a sysop of a multi-node BBS having a QWK compatible mail door, you
       should use this option to make each node point to the same CRC file.
       Kill QWK Dupes is fully SHARE compatible allowing multiple nodes to
       access the same file without problems.  And by using this option, you
       can prevent users from uploading the same message more than once by
       using more then one node.

       It is recommended however for BBS sysops to use the same CRC file for
       multiple mail doors.  This way, no matter which mail door is used,
       Kill QWK Dupes will remove the duplicate messages without error.


       -DC:nnnn       -DC:nnnn
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       Instead of throwing away duplicate messages into the "bit bucket", you
       can optionally have them moved to a special conference for your
       review.  By specifying this option, you are telling Kill QWK Dupes
       which conference to move the duplicate messages into.  Without this
       option, all duplicate messages will simply be removed.


       -DN:name       -DN:name
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       Kill QWK Dupes recognizes the "Add/Drop/Reset" mail door commands that
       may be present in .REP packets.  It does this solely based upon the
       name in the "TO" field of the message.  If this field contains either
       QMAIL, MARKMAIL, ROSEMAIL, TOMCAT, QWIKER, or PCRELAY, it decides that
       the message is a special message to the mail door software and will
       not count it as a duplicate.



                                          6





       However, if your mail door is not one of the 5 listed above, Kill QWK
       Dupes may be fooled into believing the "Add/Drop/Reset" commands
       addressed to your mail door are duplicates and remove them from the
       packet by mistake.  To prevent this from occurring, you can use this
       option to specify what name your mail door goes by when receiving this
       type of message.  Please refer to the documentation and/or author of
       your mail door package for the specific name that needs to be
       configured in this parameter.


       -MC:32-32756, default is 32756       -MC:32-32756, default is 32756
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       This option is used to control the size of the CRC table.  Each entry
       in the CRC table uses 6 bytes of disk space and memory to store it.
       32756 entries requires a total of 196,536 bytes of disk space, and
       memory to store.  You may want to limit the number of CRC entries to
       conserve disk space and/or control the amount of time Kill QWK Dupes
       requires to scan the entire table looking for a duplicate.  Also, if
       you're running short on memory, this parameter can be used to reduce
       the amount of memory Kill QWK Dupes requires to operate.


       -MD:1-24855, default is 24855       -MD:1-24855, default is 24855
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       This is another method of controlling the size of the CRC table.  The
       difference is that this method controls the age of each CRC entry.
       CRC entries older then the specified number of days will automatically
       be purged from the table.  This allows things like the same "For Sale
       add" to be re-posted every few days.


       -NC:1-32767, default is 3       -NC:1-32767, default is 3
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       This option controls the maximum number of different conferences the
       same message may appear.  Useful to control the "letter bomb" where a
       user enters the same message in all conferences he has access to.  You
       may wish to change the default to permit messages such as "For Sale"
       to be posted in more, or less, then a maximum of 3 different
       conferences.


       -Com:1-4 or NNNN where NNNN is the ports hexadecimal address       -Com:1-4 or NNNN where NNNN is the ports hexadecimal address
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       This option causes all text displayed on the screen to also be sent
       out to the specified comm. port number.  It's only useful to BBS
       sysops using Kill QWK Dupes to eliminate duplicates as part of their
       REP packet upload process.

       If -FSL is also specified, this number can be 0-7.  Kill QWK Dupes
       will use the installed FOSSIL driver for your system instead of
       driving the comm. port directly.





                                          7





       -FSL       -FSL
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       This option is only useful to BBS sysops that use a FOSSIL driver for
       their system.  If you use a FOSSIL driver, you will need to include
       this option.  It changes the meaning of the -Com: parameter.  Instead
       of a physical comm. port number, it specifies the FOSSIL port number
       to use.  Be sure you have specified things correctly when using either
       of these two options.  Kill QWK Dupes does no error checking to see if
       the either the physical comm. port exists, or if the FOSSIL driver is
       loaded.


       -NoFSL       -NoFSL
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       This option will override the -FSL option.  Useful if you have
       included -FSL in your KILLQDUP environment variable and don't want to
       use the FOSSIL driver on a particular scan.


       -NDX       -NDX
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       This option is will be used mostly by users wishing to scan QWK
       packets before reading them with your favorite QWK compatible offline
       reader.  It can also be used to generate *.NDX files for a QWK packet
       that does not contain them, such as a netmail packet a node receives
       from its mail HUB.

       Prior to using this option, you must have extracted your CONTROL.DAT
       file along with the MESSAGES.DAT file from the QWK packet and placed
       both files in the same sub-directory.  Kill QWK Dupes will put the
       *.NDX files in this sub-directory also.  After running Kill QWK Dupes,
       you must re-pack the QWK packet with the new MESSAGES.DAT file, and
       the new *.NDX file.  The CONTROL.DAT file is only used by Kill QWK
       Dupes for information necessary to correctly rebuild the *.NDX files,
       and therefore remains unchanged.


       -NoNDX       -NoNDX
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       This option will override the -NDX option.  Useful if you have
       included -NDX in your KILLQDUP environment variable and don't want the
       *.NDX files built on a particular scan.


       -NoKill       -NoKill
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       This option is useful if you want to just scan the packet without
       actually removing any duplicate messages found in the input file.
       This option runs a lot faster because Kill QWK Dupes is not actually
       rebuilding the QWK file.  All it does is scan the input file.

       NOTE: The CRC file is not updated when this option is used.  Thus
       allowing you to do a quick scan check without effecting any of the
       data files.


                                          8







       -Kill       -Kill
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       This option will override the -NoKill option.  Useful if you have
       included -NoKill in your KILLQDUP environment variable and do want
       duplicate messages removed on a particular scan.


       -NoBAK       -NoBAK
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       This option will cause Kill QWK Dupes to pack in place.  In other
       words, no .BAK file will be created.  Instead, it'll cut out the
       duplicate messages within the existing packet.

       Since this switch is automatically used by the KQCAP program, there
       should be no need for you to put it on the command line anywhere.


       -IS       -IS
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       This option will force Kill QWK Dupes to scan an entire packet,
       regardless of the Scanned Stamp.  Normally, after Kill QWK Dupes runs,
       it stamps the file with a special stamp so that it won't re-scan the
       same messages over again when messages are being appended to the
       packet.  If they were scanned again, they would be removed as
       duplicate messages.  The problem this creates is that when a .REP
       packet is received by a HUB that was scanned by it's node, the Scanned
       Stamp would normally cause it to skip scanning it for duplicate
       messages by the HUB.

       Since this switch is automatically used by the KQCAP program, there
       should be no need for you to put it on the command line anywhere.


       Use of the KILLQDUP environment variable       Use of the KILLQDUP environment variable
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       Any of the 12 command line options may also be specified as the
       default operating mode by setting the environment variable "KILLQDUP".
       If Kill QWK Dupes finds this environment variable set, it will parse
       it's setting just like it does the command line.  For example:

       SET KILLQDUP=-Log:D:\ALLOGS\DUPES.LOG -CF:NODE.CRC

       will cause Kill QWK Dupes to always write its status output to the
       file "D:\ALLOGS\DUPES.LOG" and use the file "NODE.CRC" as the CRC
       table in the default mode.

       In the event there are conflicting options specified, those entered on
       the command line will override those set via the environment variable.






                                          9





       Appendix A: How Kill QWK Dupes operates (aka what is a duplicate       Appendix A: How Kill QWK Dupes operates (aka what is a duplicate
       message?)       message?)
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       Kill QWK Dupes works by maintaining its own table of message CRC's.
       For every message scanned, the CRC16 of the message body up to but not
       including taglines (if present) is calculated.  Next the CRC16 of the
       message headers TO field is calculated.  All other portions of the
       message header are ignored as unimportant information for the purpose
       of duplicate message detection.

       The CRC table is then scanned for a matching pair of CRC values that
       also matches the conference number the message is stored in.  If no
       match is found in that conference, the new pair is added to the table
       for that conference number.  If the addition of the CRC pair causes
       the CRC table to be filled, the 32 oldest CRC pairs are thrown away,
       making room for 32 more CRC pairs.  If on the other hand a CRC pair
       match is found in 4 or more different conferences, the excess messages
       will also be removed as duplicate messages.  This prevents the "letter
       bomb", a case where one user posts the same message to all conferences
       he has access to.

       If however a 3 way match (CRC16 of the message body, and CRC16 of the
       TO field, and the conference number) is found, the message is removed
       from the input file and the number of duplicates found counter is
       incremented by one.

       Kill QWK Dupes also maintains a table of date & time stamp table
       pointers so that it knows the exact age of each CRC pair contained in
       the table.  When it finishes scanning, Kill QWK Dupes will trim the
       CRC table size to the maximum number of CRC entries you have
       specified, and also remove CRC pairs that are older then the date you
       have specified.

       Unless the -NoKill option is specified, Kill QWK Dupes will also
       modify the first 128 bytes of the output file (a header block) with a
       signature and ending pointer such that if the file is added onto (a
       node does an additional export appending to an existing .REP packet
       for example) Kill QWK Dupes will not re-scan the entire packet, but
       resume its scan at the point where the new messages were added.  This
       prevents running Kill QWK Dupes on the same packet more then once and
       accidentally removing the already scanned messages believing they are
       duplicates.

       Each CRC pair entry in the table uses 6 bytes.  Each date & time stamp
       table pointer uses 6 bytes.  There's also 6 bytes of overhead in the
       CRC file when stored on disk.










                                         10





       Appendix B: How to install Kill QWK Dupes into the MarkMail door       Appendix B: How to install Kill QWK Dupes into the MarkMail door
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       The easiest way to install Kill QWK Dupes in the MarkMail door is by
       using the KQCAP program.  Refer to the KQCAP documenation on how to
       install it.  However that doesn't work for you, this appendix
       describes how to install it via a batch file.

       This appendix is added with kudos to Mike King of IDC BBS for figuring
       out how to install Kill QWK Dupes in the MarkMail door.

       In order to make Kill QWK Dupes work with the MarkMail door, it must
       intercept MarkMail at a point where it's about to process the .REP
       packet.  You do NOT want to intercept and scan the .QWK packets
       MarkMail sends because Kill QWK Dupes would see all messages sent to
       the various users as duplicates and remove them accordingly.  The best
       place to intercept the .REP packet processing is where MarkMail is
       shelling out to a decompression program in order to decompress the
       .REP packet.  What you do is to insert a batch file of your own that
       will decompress the .REP packet, scan for duplicates and leave the
       files just where MarkMail expects to find them.

       The following 5 steps (which assume you already have MarkMail working)
       outline the procedure on how to accomplish this:

            1) Start by running the MarkMail System Manager program "MMSM":

     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³                         MarkMail System Manager                        ³
     ³                Copyright 1989, 1990, 1991 By Mark Turner               ³
     ³                                                                        ³
     ³ ÖÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ· ³
     ³ º                         Configuration Menu                         º ³
     ³ ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶ ³
     ³ º                                                                    º ³
     ³ º               A  General Configuration                             º ³
     ³ º               B  Compression Methods                               º ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

            2) Select option B to configure Compression methods:

     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ ³
     ³ º                              Compression Methods                     ³
     ³ º                                                                      ³
     ³ º                                                                      ³
     ³ º                                                                      ³
     ³ º                                                                      ³
     ³ º                                                                      ³
     ³ º    Method #1       Name : Default                         (Default)  ³
     ³ º    Compress Cmd Line    : Pkzip                                      ³
     ³ º    Un-Compress Cmd Line : Pkunzip                                    ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ




                                         11





            3) On the third line substitute "MMKILLQ" in place of "Pkunzip".
            This is the name of the batch file that will do the decompressing
            and scanning of the .REP packets.  You can use a different name
            if you wish.  Leave all other items alone.

     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     ³ ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ ³
     ³ º                              Compression Methods                     ³
     ³ º                                                                      ³
     ³ º                                                                      ³
     ³ º                                                                      ³
     ³ º                                                                      ³
     ³ º                                                                      ³
     ³ º    Method #1       Name : Default                         (Default)  ³
     ³ º    Compress Cmd Line    : Pkzip                                      ³
     ³ º    Un-Compress Cmd Line : MmKillq                                    ³
     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

            4) After entering the change, press the Esc key twice to exit
            MMSM and save the change.

            5) Next the batch file "MMKILLQ.BAT" must be created.  Its
            contents should resemble the following (a sample MMKILLQ.BAT file
            has been included in the package for you to follow and modify as
            required):

            SET KILLQDUP = -MC:8000 -MD:14 -Com:1
            PKUNZIP %1
            KILLQ IDCBBS.MSG -CF:C:\QM4\IDCBBS.CRC -Log:C:\QM4\KILLQDUP.LOG
            DEL IDCBBS.BAK
            SET KILLQDUP =

            The first line sets the KILLQDUP environment variable such that
            the following KILLQ line doesn't become excessively long.  In
            this case the environment variable is telling Kill QWK Dupes to
            maintain a maximum of 8000 entries in the CRC table, to only
            track the last 14 days worth of CRC's and to talk to the user via
            Comm. Port 1.  The next line does the actual decompression of the
            .REP packet.  Next is the KILLQ line which does the actual
            scanning of file containing the messages from the user.  This
            line is also telling Kill QWK Dupes to use the filename
            "IDCBBS.CRC" as the CRC file and to use the file "KILLQDUP.LOG"
            to write/append its processing results to.  Be sure to replace
            "IDCBBS" with the actual BBS_ID that you go by.  The next line
            simply erases the IDCBBS.BAK file that Kill QWK Dupes creates
            during its processing.  Again, be sure to replace "IDCBBS" with
            the actual BBS_ID that you go by.  The last line clears out the
            KILLQDUP environment variable.

       It is likely that you will have to modify the MMKILLQ.BAT file to fit
       your setup.  At a minimum, the path to be used for the log file will
       have to be changed.  The Comm. Port assignment may or may not need to
       be changed (or may be removed altogether if you wish).  All the other



                                         12





       parameters may be changed as well to best fit your personal
       preferences.






















































                                         13





       Appendix C: How to install Kill QWK Dupes into the Qmail door       Appendix C: How to install Kill QWK Dupes into the Qmail door
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       The easiest way to install Kill QWK Dupes in the Qmail door is by
       using the KQCAP program.  Refer to the KQCAP documenation on how to
       install it.  However that doesn't work for you, this appendix
       describes how to install it via a batch file.

       This appendix is added with kudos to Mike King of IDC BBS for figuring
       out how to install Kill QWK Dupes in the Qmail door.

       In order to make Kill QWK Dupes work with the Qmail door, it must
       intercept Qmail at a point where it's about to process the .REP
       packet.  You do NOT want to intercept and scan the .QWK packets Qmail
       sends because Kill QWK Dupes would see all messages sent to the
       various users as duplicates and remove them accordingly.  The best
       place to intercept the .REP packet processing is where Qmail is
       shelling out to a decompression program in order to decompress the
       .REP packet.  What you do is to insert a batch file of your own that
       will decompress the .REP packet, scan for duplicates and leave the
       files just where Qmail expects to find them.

       The following 5 steps (which assume you already have Qmail working)
       outline the procedure on how to accomplish this:

            1) Start by running the Qmail Setup Utility program "QMSETUP":

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³ ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ ³
       ³ º                        Qmail Door 4.00 Setup Utility             ³
       ³ º                         Copyright 1990 by Sparkware              ³
       ³ º                                                                  ³
       ³ º    ÖÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ ³
       ³ º    º                             Main Menu                       ³
       ³ º    ºÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ ³
       ³ º    º                                                             ³
       ³ º    º               A  Paths & Filenames                          ³
       ³ º    º               B  Transfer Protocols                         ³
       ³ º    º               C  Archiver Definitions                       ³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

            2) Select option C for Archiver Definitions:

         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³ ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ ³
         ³ º                             Archiver Definitions             ³
         ³ º                                                              ³
         ³ º                                                              ³
         ³ º Archiver #1    : PkZip                                       ³
         ³ º Pack command   : PKZIP -A                                    ³
         ³ º Unpack command : PKUNZIP -O                                  ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

            3) On the third line substitute "QMKILLQ" in place of
            "PKUNZIP -O".  This is the name of the batch file that will do


                                         14





            the decompressing and scanning of the .REP packets.  You can use
            a different name if you wish.  Leave all other items alone.
         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
         ³ ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ ³
         ³ º                             Archiver Definitions             ³
         ³ º                                                              ³
         ³ º                                                              ³
         ³ º Archiver #1    : PkZip                                       ³
         ³ º Pack command   : PKZIP -A                                    ³
         ³ º Unpack command : QMKILLQ                                     ³
         ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

            4) After entering the change, press the Esc key twice to exit
            QMSETUP and save the change.

            5) Next the batch file "QMKILLQ.BAT" must be created.  Its
            contents should resemble the following (a sample QMKILLQ.BAT file
            has been included in the package for you to follow and modify as
            required):

            SET KILLQDUP = -MC:8000 -MD:14 -Com:1
            PKUNZIP %1 %2 %3
            KILLQ %2IDCBBS.MSG -CF:C:\QM4\IDCBBS.CRC -Log:C:\QM4\KILLQDUP.LOG
            DEL %2IDCBBS.BAK
            SET KILLQDUP =

            The first line sets the KILLQDUP environment variable such that
            the following KILLQ line doesn't become excessively long.  In
            this case the environment variable is telling Kill QWK Dupes to
            maintain a maximum of 8000 entries in the CRC table, to only
            track the last 14 days worth of CRC's and to talk to the user via
            Comm. Port 1.  The next line does the actual decompression of the
            .REP packet.  Next is the KILLQ line which does the actual
            scanning of file containing the messages from the user.  This
            line is also telling Kill QWK Dupes to use the filename
            "IDCBBS.CRC" as the CRC file and to use the file "KILLQDUP.LOG"
            to write/append its processing results to.  Be sure to replace
            "IDCBBS" with the actual BBS_ID that you go by.  The next line
            simply erases the IDCBBS.BAK file that Kill QWK Dupes creates
            during its processing. Again, be sure to replace "IDCBBS" with
            the actual BBS_ID that you go by.  The last line clears out the
            KILLQDUP environment variable.

       It is likely that you will have to modify the QMKILLQ.BAT file to fit
       your setup.  At a minimum, the path to be used for the log file will
       have to be changed.  The Comm. Port assignment may or may not need to
       be changed (or may be removed altogether if you wish).  All the other
       parameters may be changed as well to best fit your personal
       preferences.







                                         15





       Appendix D: How to install Kill QWK Dupes into the RoseMail door       Appendix D: How to install Kill QWK Dupes into the RoseMail door
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       The easiest way to install Kill QWK Dupes in the RoseMail door is by
       using the KQCAP program.  Refer to the KQCAP documenation on how to
       install it.  However that doesn't work for you, this appendix
       describes how to install it via a batch file.

       This appendix is added with kudos to Peter Wadsworth of Coconino BBS
       for figuring out how to install Kill QWK Dupes in the RoseMail door.

       In order to make Kill QWK Dupes work with the RoseMail door, it must
       intercept RoseMail at a point where it's about to process the .REP
       packet.  You do NOT want to intercept and scan the .QWK packets
       RoseMail sends because Kill QWK Dupes would see all messages sent to
       the various users as duplicates and remove them accordingly.  The best
       place to intercept the .REP packet processing is where RoseMail is
       shelling out to a decompression program in order to decompress the
       .REP packet.  What you do is to insert a batch file of your own that
       will decompress the .REP packet, scan for duplicates and leave the
       files just where RoseMail expects to find them.

       The following 5 steps (which assume you already have RoseMail working)
       outline the procedure on how to accomplish this:

            1) Start by running the RoseMail Manager program "RM" and go to
            the Packet decompression screen:

     ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
     º                RoseMail 1.52 System Manager (08-09-91 02:30)
     º                  Copyright (C) 1991 Rose Media Incorporated
     º
     º                         Packet decompression information
     º
     ºLetter ID Name                       Decompression program        ==>
     º  A    1A Phil Katz's PKARC          PKARC -x
     º  Z    50 Phil Katz's PKUNZIP        PKUNZIP -o
     º       00
     º       00
     º       00
     º       00
     º
     º            Press ESC (right mouse button) to return to main menu
     ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

            2) On the second line substitute "RMKILLQ" in place of
            "PKUNZIP -o".  This is the name of the batch file that will do
            the decompressing and scanning of the .REP packets.  You can use
            a different name if you wish.  Leave all other items alone.








                                         16






     ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
     º                RoseMail 1.52 System Manager (08-09-91 02:30)
     º                  Copyright (C) 1991 Rose Media Incorporated
     º
     º                         Packet decompression information
     º
     ºLetter ID Name                       Decompression program        ==>
     º  A    1A Phil Katz's PKARC          PKARC -x
     º  Z    50 Phil Katz's PKUNZIP        RMKILLQ
     º       00
     º       00
     º       00
     º       00
     º
     º            Press ESC (right mouse button) to return to main menu
     ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

            3) After entering the change, exit RM to save the change.

            4) Next the batch file "RMKILLQ.BAT" must be created.  Its
            contents should resemble the following (a sample RMKILLQ.BAT file
            has been included in the package for you to follow and modify as
            required):

       SET KILLQDUP = -MC:8000 -MD:14 -Com:%DSZPORT% -Log:D:\KILLQDUP.LOG
       PKUNZIP %1 %2
       IF "%2"=="COCONINO.MSG" KILLQ %1 -CF:F:\PCB\COCONINO.CRC
       DEL COCONINO.BAK
       SET KILLQDUP =

            The first line sets the KILLQDUP environment variable such that
            the following KILLQ line doesn't become excessively long.  In
            this case the environment variable is telling Kill QWK Dupes to
            maintain a maximum of 8000 entries in the CRC table, to only
            track the last 14 days worth of CRC's and to talk to the user via
            the Comm. Port DSZ will use.  The next line does the actual
            decompression of the .REP packet.  Next is the KILLQ line which
            does the actual scanning of file containing the messages from the
            user.  This line is also telling Kill QWK Dupes to use the
            filename "COCONINO.CRC" as the CRC file and to use the file
            "KILLQDUP.LOG" to write/append its processing results to.  Be
            sure to replace "COCONINO" with the actual BBS_ID that you go by.
            The next line simply erases the COCONINO.BAK file that Kill QWK
            Dupes creates during its processing. Again, be sure to replace
            "COCONINO" with the actual BBS_ID that you go by.  The last line
            clears out the KILLQDUP environment variable.

       It is likely that you will have to modify the RMKILLQ.BAT file to fit
       your setup.  At a minimum, the path to be used for the log file will
       have to be changed.  The Comm. Port assignment may or may not need to
       be changed (or may be removed altogether if you wish).  All the other
       parameters may be changed as well to best fit your personal
       preferences.


                                         17





       Appendix E: How to install Kill QWK Dupes into the Tomcat! door       Appendix E: How to install Kill QWK Dupes into the Tomcat! door
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       The easiest way to install Kill QWK Dupes in the Tomcat! door is by
       using the KQCAP program.  Refer to the KQCAP documenation on how to
       install it.  However that doesn't work for you, this appendix
       describes how to install it via a batch file.

       This appendix is added with kudos to William Padilla of Panasia BBS
       for figuring out how to install Kill QWK Dupes in the Tomcat! door.

       In order to make Kill QWK Dupes work with the Tomcat! door, it must
       intercept Tomcat! at a point where it's about to process the .REP
       packet.  You do NOT want to intercept and scan the .QWK packets
       Tomcat! sends because Kill QWK Dupes would see all messages sent to
       the various users as duplicates and remove them accordingly.  The best
       place to intercept the .REP packet processing is where Tomcat! is
       shelling out to a decompression program in order to decompress the
       .REP packet.  What you do is to insert a batch file of your own that
       will decompress the .REP packet, scan for duplicates and leave the
       files just where Tomcat! expects to find them.

       The following 5 steps (which assume you already have Tomcat! working)
       outline the procedure on how to accomplish this:

            1) Bring up the Tomcat! configuration file into a text editor.

       ID          = PANASIA
       CITY        = Glendale, CA
       PHONE       = 818-240-0415
       WORK        = C:\TOMCAT
       LOCAL       = E:\DOWNLDS\
       PACKER      = Z , PKZIP/PKUNZIP , ZIP , PKZIP -A ! , PKUNZIP !
       EXTERNAL    =
       HELLO       = PRELOG
       .
       .
       .

            2) On the PACKER" line substitute "COMMAND /C TCKILLQ !" in place
            of "PKUNZIP !".  This is the name of the batch file that will do
            the decompressing and scanning of the .REP packets.  You can use
            a different name if you wish.  Leave all other items alone.

       PACKER   = Z , PKZIP/PKUNZIP , ZIP , PKZIP -A ! , COMMAND /C TCKILLQ !

            3) Save the configuration file and exit the text editor.

            4) Next the batch file "TCKILLQ.BAT" must be created.  Its
            contents should resemble the following (a sample TCKILLQ.BAT file
            has been included in the package for you to follow and modify as
            required):

       SET KILLQDUP = -MC:8000 -MD:14 -Com:1
       PKUNZIP %1


                                         18





       KILLQ PANASIA.MSG -CF:D:\WC\KILLQDUP.CRC -LOG:D:\WC\KILLQDUP.LOG
       DEL PANASIA.BAK
       SET KILLQDUP =


            The first line sets the KILLQDUP environment variable such that
            the following KILLQ line doesn't become excessively long.  In
            this case the environment variable is telling Kill QWK Dupes to
            maintain a maximum of 8000 entries in the CRC table, to only
            track the last 14 days worth of CRC's and to talk to the user via
            Comm. Port 1.  The next line does the actual decompression of the
            .REP packet.  Next is the KILLQ line which does the actual
            scanning of file containing the messages from the user.  This
            line is also telling Kill QWK Dupes to use the filename
            "KILLQDUP.CRC" as the CRC file and to use the file "KILLQDUP.LOG"
            to write/append its processing results to.  Be sure to replace
            "PANASIA" with the actual BBS_ID that you go by.  The next line
            simply erases the PANASIA.BAK file that Kill QWK Dupes creates
            during its processing. Again, be sure to replace "PANASIA" with
            the actual BBS_ID that you go by.  The last line clears out the
            KILLQDUP environment variable.

       It is likely that you will have to modify the TCKILLQ.BAT file to fit
       your setup.  At a minimum, the path to be used for the log file will
       have to be changed.  The Comm. Port assignment may or may not need to
       be changed (or may be removed altogether if you wish).  All the other
       parameters may be changed as well to best fit your personal
       preferences.




























                                         19





       Appendix F: How to install Kill QWK Dupes into the Jetmail door       Appendix F: How to install Kill QWK Dupes into the Jetmail door
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       The easiest way to install Kill QWK Dupes in the Jetmail door is by
       using the KQCAP program.  Refer to the KQCAP documenation on how to
       install it.  However that doesn't work for you, this appendix
       describes how to install it via a batch file.

       This appendix is added with kudos to Ron Hossack of the Solid Rock BBS
       for figuring out how to install Kill QWK Dupes in the Jetmail door.

       In order to make Kill QWK Dupes work with the Jetmail door, it must
       intercept Jetmail at a point where it's about to process the .REP
       packet.  You do NOT want to intercept and scan the .QWK packets
       Jetmail sends because Kill QWK Dupes would see all messages sent to
       the various users as duplicates and remove them accordingly.  The best
       place to intercept the .REP packet processing is where Jetmail is
       shelling out to a decompression program in order to decompress the
       .REP packet.  What you do is to insert a batch file of your own that
       will decompress the .REP packet, scan for duplicates and leave the
       files just where Jetmail expects to find them.

       The following 5 steps (which assume you already have Jetmail working)
       outline the procedure on how to accomplish this:

            1) Bring up the Jetmail configuration file into a text editor.

       .
       .
       .
       PACK1=ZIP
       PACK1QWK=PKZIP -M
       PACK1REP=PKUNZIP -O
       PACK2=ARJ
       .
       .
       .

            2) On the "PACK1REP" line substitute "COMMAND /C JMKILLQ" in
            place of "PKUNZIP -O".  This is the name of the batch file that
            will do the decompressing and scanning of the .REP packets.  You
            can use a different name if you wish.  Leave all other items
            alone.

       PACK1REP=COMMAND /C JMKILLQ

            3) Save the configuration file and exit the text editor.

            4) Next the batch file "JMKILLQ.BAT" must be created.  Its
            contents should resemble the following (a sample JMKILLQ.BAT file
            has been included in the package for you to follow and modify as
            required):

       SET KILLQDUP = -MC:8000 -MD:14 -Com:1
       PKUNZIP -O %1 %2


                                         20





       KILLQ D:\TMP\ROCK.MSG -CF:C:\SF\JM\ROCK.CRC -Log:C:\SF\JM\KILLQDUP.LOG
       DEL D:\TMP\ROCK.BAK
       SET KILLQDUP =

            The first line sets the KILLQDUP environment variable such that
            the following KILLQ line doesn't become excessively long.  In
            this case the environment variable is telling Kill QWK Dupes to
            maintain a maximum of 8000 entries in the CRC table, to only
            track the last 14 days worth of CRC's and to talk to the user via
            Comm. Port 1.  The next line does the actual decompression of the
            .REP packet.  Next is the KILLQ line which does the actual
            scanning of file containing the messages from the user.  This
            line is also telling Kill QWK Dupes to use the filename
            "ROCK.CRC" as the CRC file and to use the file "KILLQDUP.LOG" to
            write/append its processing results to.  Be sure to replace
            "ROCK" with the actual BBS_ID that you go by.  The next line
            simply erases the ROCK.BAK file that Kill QWK Dupes creates
            during its processing. Again, be sure to replace "ROCK" with the
            actual BBS_ID that you go by.  The last line clears out the
            KILLQDUP environment variable.

       It is likely that you will have to modify the JMKILLQ.BAT file to fit
       your setup.  At a minimum, the path to be used for the log file will
       have to be changed.  The Comm. Port assignment may or may not need to
       be changed (or may be removed altogether if you wish).  All the other
       parameters may be changed as well to best fit your personal
       preferences.





























                                         21





       Appendix G: How to install Kill QWK Dupes into the Auntie door       Appendix G: How to install Kill QWK Dupes into the Auntie door
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       There is nothing you need to do special here because the Auntie mail
       door will automatically run Kill QWK Dupes of its own accord.  The
       only thing you need to do is setup your KILLQDUP environment variable
       as required for your configuration.  You should set this environment
       variable in each of your node startup batch files.  That way you will
       be able to specify the correct COM port for each node.


       Appendix H: Multi-node considerations       Appendix H: Multi-node considerations
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       Kill QWK Dupes is fully network/DESQView and multi-node compatible.
       However there are some considerations that should be discussed as they
       may affect your setup.

       First, under multi-node operation, which Comm. Port to use is
       generally passed to the door program (such as Qmail and MarkMail) via
       some sort of PCBOARD.SYS/DOOR.SYS info. file.  Since Kill QWK Dupes is
       unable to extract the Comm. Port information from your info. file,
       this information must be conveyed via some other means (or not
       specified at all such that Kill QWK Dupes doesn't attempt to talk to
       any Comm. Port).  The best and easiest way to specify it is to have
       the KILLQDUP environment variable set permanently as part of the batch
       file that brings up the individual node.  The Comm. Port to use would
       be specified in the environment variable, and the two "SET KILLQDUP"
       lines in the QMKILLQ.BAT and MMKILLQ.BAT files would have to be
       eliminated.  This method allows a common batch file be run by the mail
       door to do the scanning, and still have the correct Comm. Port used by
       Kill QWK Dupes.  Another method would be to setup each node such that
       a different batch file is run by each node when the mail door shells
       out to decompress the mail packet.  Each batch file would have to
       correctly specify the Comm. Port for Kill QWK Dupes to use.

       Secondly file sharing/locking must be discussed.  In order for a
       multi-node system to use and share the same CRC file among all the
       nodes, Kill QWK Dupes uses file sharing and locking.  But in order for
       this feature to be active, you must be running DOS 3.0 or above, and
       have SHARE loaded.  If you are not running multi-node, then DOS 2.x is
       all that's required to run Kill QWK Dupes since file sharing/locking
       is not required.















                                         22





       Appendix I:Errorlevels returned by Kill QWK Dupes       Appendix I:Errorlevels returned by Kill QWK Dupes
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       Kill QWK Dupes returns errorlevels to help make its use in a batch
       file easier.  The following is a list of the errorlevels and their
       meanings:

       0 - Normal completion. At least one duplicate message was found and
       removed (unless -NoKill was specified).

       1 - Normal completion. No duplicates were found.

       2 - Command line parameter error or no file specified to scan.

       3 - Insufficient memory to allocate required data arrays.

       4 - Unexpected system error occurred.

       5 - Disk full error while writing to file.






































                                         23





       History       History
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
       10/30/91 v1.00 - Initial public release.
       11/05/91 v1.01 - Return errorlevels for better batch file use.
       11/10/91 v1.02 - Calculate correct base comm. port address.
                      - Display message status for each message scanned.
                      - Handle case where -DN parameter is not specified.
       01/09/92 v1.03 - Ignore extra spaces at end of lines when computing
                        message CRC.
                      - Added the -DC parameter.
                      - Added PCRELAY as a recognized mail door name.
       02/24/92 v1.04 - Corrected error levels returned to match the
                        documentation.
                      - Converted to Small Memory model for faster operation.
                      - Force ON the Net Status flag for the corresponding
                        ÄDC conference.
                      - Added a Key Registration system. Eliminated the
                        "Registered Version" at the same time.
       03/23/92 v1.05 - Fixed bug where all but the first message was being
                        deleted.
       07/29/92 v1.09 - Created the KQCAP program.
                      - NoBAK switch added.
                      - IS switch added.
                      - Handle case where CRC file is larger than the -MC
                        switch setting.
       08/06/92 v1.10 - Fixed bug where all messages were being re-scanned
                        (and all old messages invalidly removed as
                        duplicates) when messages were being appended to a
                        packet, despite the presence of a Scan Stamp on the
                        packet.


























                                         24