____________________________________________________________________________
STACKER NOTE                          Stac Electronics Technical Note

Subject: Loading Stacker into Upper Memory with MS-DOS 5.0 or Windows 3.1. 

Tec015 - 6/19/92
____________________________________________________________________________

MS-DOS 5.0 and Windows 3.1 come with EMM386.EXE, an expanded memory manager 
that enables the loading of device drivers and TSRs into the Upper Memory 
area  on 386 and 486 machines.  The Stacker device driver may be loaded into 
this area if the system is configured properly and if there is an upper 
memory block (UMB) large enough to accommodate its initialization size. This 
initialization size and the size of the largest UMB are given at boot time.  
Use the pause key during boot to view these figures.  If there is no UMB 
large enough, the Stacker driver will be loaded low by default.  Optimizing
upper memory usage is an art, and may require much trial and error.  You may 
have to experiment with the order in which things are loaded.  This note 
provides the necessary configuration information to get you started.  

Requirements:

  1. This must be a 386 or 486 with at least 1MB of memory.
  2. The Config.sys file must contain the following:

         DEVICE=C:\path\HIMEM.SYS                       
         DEVICE=C:\path\EMM386.EXE   switches           
         DOS=UMB   (or DOS=HIGH,UMB)
         deviceHIGH=C:\STACKER\STACKER.COM ..........

     Notes: 
       A. Make sure HIMEM.SYS and EMM386.EXE are loaded in this order and 
          that they exist on the uncompressed drive or they will not be 
          available during system startup.
         
       B. Stacker's SSWAP program is not memory resident.  Therefore, it is
          not necessary to load it high.
         
  3. EMM386.EXE  switches
     
     There are number of possibilities depending on the memory requirements 
     of your applications.  
       
       A. If no EMS memory is required, use the NOEMS parameter.  This 
          will provide access to the UMBs but provides no EMS services.
            
              i.e.   DEVICE=c:\DOS\EMM386.EXE  NOEMS
       
       B. If some applications use EMS memory, use the RAM parameter.  This 
          will provide access to the UMBs and create a 64k EMS page frame. 
            
              i.e.   DEVICE=c:\DOS\EMM386.EXE RAM 
       
       C. In order to free up the MAXIMUM amount of upper memory, add the
          m9 parameter.  This will inform EMM386 to position the page frame
          at address E000h, freeing up an additional 64K when using the RAM 
          parameter.  When used with the NOEMS parameter, the 64k memory 
          block starting at E000h will be added to the available UMBs.  
          
             i.e.   DEVICE=c:\DOS\EMM386.EXE NOEMS m9
          
          The line above will free up the maximum amount of UMB on most 
          systems.  It is possible to specify other memory starting address 
          with the m# parameter.  Please consult your DOS or Windows manual.
     
  4. If using the Stacker XT/8 coprocessor card: 
     
     It will be necessary to exclude its 16K address range from use by 
     EMM386.  For example, if the coprocessor base address is cc00, 
     add   x=cc00-cfff  .  Exclusion ranges can be found in the Stacker 
     Readme.doc file.  Failure to exclude will result in the message 
     "Coprocessor not functioning, invoking software driver".

  5. To see if the Stacker device was successfully loaded into the UMBs, use
     the DOS MEM command.   Type ->  MEM /C.
-----------------------------------------------------------------------------
1992 Stac Electronics