MKROUTE v0.06 - The Region Router for FrontDoor/InterMail/Squish


   *   This program is useful only for nodes who      *
   *   want to route netmail for complete regions     *
   *   through a specific destination. MKROUTE was    *
   *   written for use on an Netmail-I/O-Gate.        *

   *   Read this documentation carefully before       *
   *   first use of the program, otherwise it may     *
   *   destroy your routing-file!                     *


 Introduction
 ~~~~~~~~~~~~
 Netnumbers change often and new nets are created each week.
 And if you have a special netmail-routing for many regions
 then it is a hell lot of work each friday to walk through the
 nodediff/nodelist for possible changes. MKROUTE is designed
 to do that job for you.

 The default-parameters are set to generate a ROUTE.FD for
 FrontDoor. If you are using InterMail or Squish, then continue
 reading and take a look at the commandline-parameters
 (explained later). They will allow you to configure the
 program for your environment.


 Installation
 ~~~~~~~~~~~~
 a) Rename your ROUTE.FD (or ROUTE.IM/InterMail or PACK.CF/
    Squish) to MKROUTE.CFG (and do an additional backup on
    first use of the program!). Your ROUTE.FD-file will be
    exactly rebuild line by line from MKROUTE.CFG with the
    exception of the special region-routing.

 b) For each region-specific routing include a comment-line
    in your MKROUTE.CFG. The lines have to look like:

---< Example of MKROUTE.CFG >---
[...]
; R20 2:310/7 Sweden
;
; R21 2:2405/100 %name%
;
[...]
---< End of MKROUTE.CFG >---

    The program looks for the string "; R" in the beginning
    of each line and regards the following number (no space
    between) as a region-number. The node-number after the
    region-number will be taken as the "via"-node for this
    region, the rest of the line is ignored.

    If the string "%name%" in a MKROUTE-routing-line is
    found (as above in R21) then this string is replaced
    by the name of the region according to the nodelist.

    The above example is therefor interpreted as "Route all
    independent nodes and all nets in region 20 via node
    2:310/7" and all netmail destined to region 21 will be
    routed via node 2:2405/100.

    MKROUTE generates your ROUTE.FD from the above example
    as follows:

---< Example of the resulting ROUTE.FD >---
[...]
; R20 2:310/7 Sweden
route-to 2:310/7 2:20/* 2:200/* 2:201/* 2:203/* ...
;
; R21 2:2405/100 Norway
route-to 2:2405/100 2:21/* 2:210/* ...
;
[...]
---< End of ROUTE.FD >---

    Of course only those nets really listed in the nodelist
    are included (otherwise the program wouldn't make much
    sense :)).

    If you are quite familiar with region-routing then you
    might think of the "region-independent" node-numbers
    like 2:2/0, 2:2/100 and so on. MKROUTE will include these
    nodes in the correct routing-line for the region where
    the independents are located. This is done by comparing
    the country-code in the phone-number of the independent
    node with each RC. Only those independents will be
    routed, for whose region a special region-routing-line
    in MKROUTE.CFG is found.

    Example:

---< MKROUTE.CFG >---
[...]
; R25 2:2401/1 Grossbritannien - %name%
;
[...]
---< End of MKROUTE.CFG >---

    That line could be translated to:

---< ROUTE.FD >---
[...]
; R25 2:2401/1 Grossbritannien - United Kingdom
route-to 2:2401/1 2:2/501 2:2/544 2:25/* 2:250/* 2:251/* 2:252/* 2:253/* 2:254/* 2:255/* 2:256/* 2:257/* 2:258/* 2:259/* 2:440/*
;
[...]
---< End of ROUTE.FD >---

    Note the two independents 2:2/501 and 2:2/544!

    By the way: Does anyone know if there's a limit for the
    length of a routing-line in ROUTE.FD?

 c) Run the program:

      MKROUTE <parameter-list>

    Parameter      Meaning                          Default
    ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
    /N<Dir/Name>   your Nodelist-dir and -name      NODELIST.*
    /Z<Zone>       Zone to work on                  2
    /S<String>     routing-String meaning 'all'     * (for FD)
    /R<String>     Route-command                    route-to (for FD)
    /O<Filename>   Output-filename                  ROUTE.FD (for FD)
    /D             Debug-mode (more screen-output)  disabled


    Example for FrontDoor:
     MKROUTE /n\NODELIST\NODELIST.*

    Example for InterMail:
     MKROUTE /n\NODELIST\NODELIST.* /sAll /oROUTE.IM

    Example for Squish:
     MKROUTE /n\NODELIST\NODELIST.* /sAll /rPACK-TO /oPACK.CF

    The parameters are not case-sensitive. MKROUTE.CFG must be
    in the same directory where MKROUTE is run from.
    The /n-parameter will find the first specified file with
    a "number"-extension (*.###).

    The /d-parameter (debug-mode) will give you a very detailed
    screen-output about what's going on. It will also show you
    the list of regions of the specified Zone that are not
    included in your routing-file.

 d) You can run MKROUTE as often as you like but you should
    at least run it once a week after the new nodediff has
    been processed on your system.

 e) While MKROUTE is processing your nodelist, it is possible
    to abort the program by pressing [Esc].


 Summary
 ~~~~~~~
 _All_ lines from MKROUTE.CFG are exactly copied to the output-
 file with _no_ exception! Only those lines with "; R<any_number> "
 in the beginning are translated. After these lines a special
 region-routing-line for the specified region is inserted and
 the "%name%"-macro is replaced by the name of the region
 according to the nodelist.

 That also means that you may include just a few regions which
 have to be taken care of in your routing and send all others
 to your default-uplink.

 You could also include special routing-commands for some
 nodes of a "mkroute"d region. Example:

---< MKROUTE.CFG >---
[...]
; R20 2:310/7 Die Schweden...
no-route 2:201/5
;
[...]
---< EOF >---

 Which will be translated to:

---< ROUTE.FD >---
[...]
; R20 2:310/7 Die Schweden...
route-to 2:310/7 2:20/* 2:201/* ...
no-route 2:201/5
;
[...]
--< EOF >---

 Be warned again! Any routing-modifications should only be
 done in MKROUTE.CFG, your ROUTE.FD should be regenerated
 afterwards by MKROUTE. The ROUTE.FD will be _overwritten_
 with the contents of MKROUTE.CFG!

 If you are still unsure about how the program works, I
 have included my MKROUTE.CFG and the resulting ROUTE.FD
 based on NODELIST.220 (Zone 2, 1992). The files are
 contained in the archive EXAMPLE.LZH (this is just an
 EXAMPLE! It is _not_ the current routing of 2:24/999!).


 Limitations
 ~~~~~~~~~~~
 One limitation is that a maximum number of 50 regions
 per Zone is supported. Should that ever come out to be
 not enough, then the source can be easily modified.

 Same goes for the maximum number of independent nodes per
 zone which is hardcoded to 100.

 There is no limit concerning the number of nets per region.


 Destination
 ~~~~~~~~~~~
 The program is a "quick-'n-dirty"-one. Feel free to give it
 to anyone who knows how to handle it. I'm not responsible
 for any routing-bugs resulting from use of MKROUTE. I have
 included the source so you can see what the program does
 and how it works.

 Of course the program is "free" to anyone who likes it. If
 you use it on a regular basis and think that it saves you
 a lot of time, then I would be very happy to receive a
 small netmail from you. ;-)


Tommy Roeder (2:246/61) aka I/O-Gate Germany (2:24/999)