README file for RESTKN.ZIP file
-------------------------------

  DOS/WINDOWS - IBM token-ring and LAN SUPPORT PROGRAM (LSP) Device Drivers

  When a DOS emulation session is started with LSP device drivers the
  IBM Token-Ring card will not be reset upon either EXIT from command.com,
  Close of the session from the DESKTOP, or in a VMBOOT session Close
  of the session from the DESKTOP.  To reset the card the program
  RESETOKN.EXE should be run in either an OS/2 session or a DOS session
  that explicitly does not start the LSP.  RESETOKN.EXE will reset the
  card. If run when another DOS session is attempting to startup the
  LSP device drivers the DOS session will be allowed to complete
  initialization without error.

  An example scenario would be to have these LSP device drivers in your
  config.sys.  Start a DOS session. Bring up WINDOWS to
  use 3270 support.  While running the session your controller goes down
  and you decide to close the session from the desktop.  Then the next time
  you bring up a dos session the LSP device drivers will get hung because
  the token-ring card has not been reset properly.  By executing
  RESETOKN.EXE from an OS/2 full screen or windowed session the token-ring
  card will be reset.

  Another example would be to install RESETOKN.SYS device driver in your
  config.sys as the line before the LSP device drivers.  This will cause
  the token-ring card to be reset automatically before startup of the LSP
  device drivers.

  Another example would be to add RESETOKN.SYS device drivers together
  with the LSP device drivers to the
  DOS_DEVICES list in the settings for a unique DOS session.  The same
  rule of ordering applies in this list as with config.sys.  The RESETOKN.SYS
  must appear before any of the LSP device drivers.  This ensures that
  RESETOKN.SYS will be run before the LSP device drivers to ensure
  access to the token-ring card.

  If when using the LSP device drivers the user should be aware that
  LSP device drivers are not virtual they are physical device drivers.
  The difference is that this physical device driver assumes ownership
  of the token-ring card.  By reseting the card from another session
  when LSP is in use on behalf of an application will probably cause
  the application to fail. An example conflict would be to assume
  that in one DOS session you use LSP with token-ring for 3270 support
  and at the same or later time while the token-ring card is still in
  use you attempt to use the "same" token-ring card to LAN support.
  The LSP in the session for the LAN support will hang trying to
  get the token-ring card.  The session will have to be closed from
  desktop.  By running the RESETOKN.EXE at this time will kill the
  3270 session.  If you had started the LAN session with RESETOKN.SYS
  in your DOS SETTINGS for DOS_DEVICES will kill the 3270 also.
  This may sound complicated but by understanding the capabilites of
  the hardware and software in use a good solution can be attained
  without a lot of trial and error analysis.