Pascal Library Member EM3270.INC                 Page 1


                                  INTRODUCTION                                  ____________

        The  EM3270  procedures are the copyrighted property of  Piedmont 
        Specialty Software.  They are distributed as "Shareware" to  save 
        the enormous costs of publishing,  advertising,  and distributing 
        software through the normal commercial channels.  In keeping with 
        the established "rules" of this type of distribution, we ask that 
        you:

          1. Send $20.00 to Piedmont Specialty Software,  P. O. Box 6637, 
             Macon, GA  31208, if you find the procedures useful.

          2. Use  the procedures for your personal use only.  If you wish 
             to use them in software for commercial distribution,  please 
             contact us at the above address or by telephone at (912) 474 
             2318 for details of a commercial license.

          3. Distribute the procedures freely, so long as you

                  - do not modify them,
                  - include this documentation with them,
                  - include the acompanying demonstration program.

        We  have used these procedures in many programs in the  last  two 
        years  and  have found their screen management facilities  to  be 
        well  received by all users from novice to expert.  We hope  that 
        you will find them as useful and productive as we have.




































        Pascal Library Member EM3270.INC                 Page 2


        I. PURPOSE

             Turbo  Pascal  library member EM3270.INC is an INCLUDE  file 
             containing  a  set of procedures  which  allows  full-screen 
             editing  patterned  after the IBM 3270 family of  terminals. 
             The  3270  family consists of a number  of  terminal  models 
             designed  to  connect to the System/370 family of  mainframe 
             processors.  There are hundreds of thousands of them in  use 
             by office workers all over the world.  They operate as "full 
             screen  I/O"  terminals.  That is,  the mainframe  sends  an 
             entire screen at a time to the terminal, the user enters and 
             edits  all data on the screen while "disconnected" from  the 
             mainframe,  and  when finished transmits the entire modified 
             screen back to the mainframe by pressing one of the  "atten-
             tion identifier" (AID) keys.

             The  EM3270 procedures facilitate writing programs in  Turbo 
             Pascal which give the user the impression that he is working 
             with  a 3270 terminal.  Then programming methods you use  in 
             handling the screens are very different from those used by a 
             mainframe programmer, but the appearance to the user closely 
             mimics  a  3270 with only a few compromises made to  account 
             for the differences in a PC keyboard and a 3270 keyboard.
             
             Significant features of the routines include:

               a. Attribute_bytes specifying visible or invisible, bright                   _______________                                         
                  or dim,  steady or blinking characters,  foreground co-
                  lors, and Modified Data Tags.
               b. Cursor_control consisting of character right, character                   ______________                                          
                  left,  tab forward, tab backward, home cursor, and next 
                  line.
               c. Field_selection  on  writes and reads to and  from  the                   _______________                                         
                  screen.
               d. Cursor_positioning  under program control  before  data                   __________________                                      
                  entry.

        II. USAGE

          A. Program_Requirements             ____________________

             Before  inclusion of EM3270.INC,  the  following  statements 
             must appear:

                  {$V-}
                  . . .
                  Const
                    MaxFields = xxx;
           
             Where  xxx  is the maximum number of data fields  which  can                                                   ____                    
             appear  on any screen,  and is from 1 to 255.  Any number of 
             prompt fields can appear.             ______                   

             NOTE:  DO_NOT  SET  COMPILER DIRECTIVE {$U+} IN ANY  PROGRAM              NOTE:  DO_NOT  SET  COMPILER DIRECTIVE {$U+} IN ANY  PROGRAM              ______                    ______                                                
             USING  THE EM3270 PROCEDURES.  TURBO DOES STRANGE THINGS  TO              USING  THE EM3270 PROCEDURES.  TURBO DOES STRANGE THINGS  TO 








        Pascal Library Member EM3270.INC                 Page 3                                                               


             THE KEYBOARD BUFFER WITH THIS OPTION AND THE KEYBOARD  INPUT              THE KEYBOARD BUFFER WITH THIS OPTION AND THE KEYBOARD  INPUT 
             PROCEDURES OF EM3270 BECOME FRIED.             PROCEDURES OF EM3270 BECOME FRIED.

             The EM3270 routines use the heap,  but should not  interfere 
             with any other heap operations of the calling program.
             THE  DISPOSE COMMAND IS USED IN HEAP MANAGEMENT.  A  CALLING                   _______                                                 
             PROGRAM MUST NOT USE TURBO'S MARK AND RELEASE!!!!!                          ___                                  

          B. Initialization             ______________

             Before  any other EM3270 procedure is executed,  the  EM3270                      ___                                                  
             system must be initialized by issuing the following command:                    ____                                                 

                  InitScreen;

             This command must be issued once and only once for an execu-
             tion of your program.

          C. Screen_Handling_Logic             _____________________

             The  general flow of logic in handling a screen consists  of 
             the following sequence:

                    .
                    .
                    .
             Procedure PresentScreen1;
               Const
                Strng1 : String[8] = "Prompt 1";
                Strng2 : String[8] = "Prompt 2";
                    .
                    .
                    .
             Begin 
               NewScreen;          { clear all existing fields }
               WritePrompt(1,1,Dim,8,Strng1); { write a prompt }
               WritePrompt(2,1,Dim,8,Strng2); { write a prompt }
                    .
                    .              { repeat for all prompts }
                    .
               Attr := 0;      {Bright, Steady, Visible, Unchanged}
               WriteField(10,1,Attr,14,' ')      { define field 1 }
               WriteField(10,2,Attr,16,' ')      { define field 2 }
                    .
                    .              { repeat for all data fields }
                    .
             End;  { of procedure }
                    .
                    .
                    .
             Procedure GetScreen1;
             Begin
               ReadScreen(FieldNo,FK);   { open screen for input }
               GetField(1,Varbl1,Attr);  { retrieve a data field}
               GetField(2,Varbl2,Attr);  { retrieve a data field}








        Pascal Library Member EM3270.INC                 Page 4


                    .
                    .
             End; { of procedure }
                    .
                    .
             Procedure RewriteScreen1;
             Begin
               Attr := 0;
               RewriteField(1,Varbl1,Attr); { rewrite field 1 bright }
               RewriteField(2,Varbl2,Attr); { rewrite field 2 bright }
                    .
                    .
                    .
             End; { of procedure }
                    .
                    .
             Begin     { begin mainline program }
               InitScreen;  { Initialize EM3270 }
                    .
                    .       { open files, etc. }
                    .
               PresentScreen1;  { write blank screen 1 }
               Repeat
                 GetScreen1;
                    .
                    .            { process screen 1 variables }
                    .
                 RewriteScreen1; { replace fields with new values }
               Until Finished;
                    .
                    .

             Each of the EM3270 procedures is covered in Section III.

          D. Data_Fields             ___________

             A  data field is a string which is written to the screen and                                 ______                                    
             into  which  the  cursor can be moved  during  a  ReadScreen 
             procedure.
           
             Every  data field written to the screen is assigned a  field 
             number from 1 to MaxFields.  Data fields are numbered in the 
             order in which you write them to the screen. It is up to you 
             to keep track of what each field number contains. You always                                                                    ______ 
             address a data field by its number.

             Care must be exercised in planning the sequence in which you 
             write  data fields because cursor tabbing at program  execu-
             tion  time is determined by field number.  (This is a depar-
             ture from the 3270 standard,  in which the field sequence is 
             always  left-to-right,  top-to-bottom.) If the cursor is  in 
             field 14 and the tab key pressed,  it will jump to field 15, 
             no matter where 15 is.  To keep from driving the user  nuts, 
             screens  should  normally  be designed so  that  fields  are 
             always  written  in the  3270  left-to-right,  top-to-bottom 








        Pascal Library Member EM3270.INC                 Page 5


             sequence.

             An  example  of when you might want to place fields  out  of 
             sequence  might  be a field that is almost always  the  same 
             value,  but should visually appear close to some other vari-
             able  on  the  screen (state abbreviation in  a  local  area 
             mailing list,  for example).  In such a case, you can define 
             it  as the last screen field and provide the default  value. 
             The cursor will skip over the field in normal  tabbing,  but 
             the  user can still reach it when it needs to be changed  by 
             tabbing until the cursor finally does reach it.

             You  specify  the  position  and  length  of  a  data  field      
             when  you  first  write it with  the  WriteField  procedure. 
             Position  and  length are fixed at that time and  cannot  be 
             changed afterward.  When you retrieve a data field (with the 
             GetField  procedure),  the string returned is always of  the 
             length specified when the field was first written.

             You  also  specify  the attribute of a data field  when  you 
             write it. (Attributes are discussed fully below.) The attri-
             bute  of  a data field can be changed when you  rewrite  the                                     ___                                   
             field,  and  its  Modified  Data Tag  bit  is  automatically 
             changed  if  any  data  in the field  is  changed  during  a 
             ReadScreen procedure.

             The  routines DO_NOT check for a "collision" between fields.                            ______                                         
             If you write one field on top of another, the last field out 
             will  be the one the user sees.  However,  the value of  the 
             two  fields will be maintained intact,  and if you  retrieve 
             them both you will get the correct values. The visual effect 
             to a user, though, is quite bizarre.

          E. Prompt_Fields             _____________

             Prompts are strictly for the user's benefit and are  treated 
             very different from data fields.  Once written,  a prompt is 
             forgotten - it remains on the screen, but cannot be accessed 
             thereafter,  other  than to overwrite it with another prompt 
             or a data field.

             Prompts  are not numbered and there is no limit to how  many 
             you can write to a screen,  other than the physical capacity 
             of the screen.

             The  writing of prompts and data fields may be interspersed.

















        Pascal Library Member EM3270.INC                 Page 6


          F. Attributes             __________

             An  attribute is a byte associated with a field (either data 
             or  prompt)  which defines certain  characteristics  of  the 
             field. The bits of the byte are used as follows:

                            Bit ==>  7  6  5  4  3  2  1  0
                  Attribute Byte =>  X  X  X  X  X  X  X  X
                                     ^  ^  ^  ^  ^        ^
                  0=Bright           |  |  |  |  |________|
                  1=Dim______________|  |  |  |      |
                                        |  |  |      |
                  0=Steady              |  |  |      |
                  1=Blinking____________|  |  |      |
                                           |  |      |
                  0=Visible                |  |      |
                  1=Invisible______________|  |      |
                                              |      |
                  0=Unchanged                 |      |
                  1=Modified__________________|      |
                                                     |
                  0=Use default color                |
                  1-15=Foreground color______________|

          G. Field_Appearance             ________________

             Original models of the 3270 could display a character in one 
             of  two  brightnesses:   "normal"  (dim)  or   "highlighted" 
             (bright).  Later  models extended this capability to include 
             reverse video and blinking,  as well as color attributes.

             The EM3270 procedures implement the attributes in one of two 
             ways,  depending  on  whether they are running on a  machine 
             with a monochrome or color monitor (the EGA is not  support-
             ed). The Steady/Blinking and the Visible/Invisible bits work 
             the same on either type.

             If the Steady/Blinking bit is 0, the characters of the field 
             or prompt are displayed normally; if it is 1, they blink off 
             and on in a highly attention-grabbing (and distracting) way. 
             Blinking characters are normally used in rewritten fields to 
             call attention to a data entry error.

             If  the Visible/Invisible bit is 0,  the characters  of  the 
             field are displayed normally; if it is 1, they are displayed 
             as spaces (that is,  they are invisible). Moreover, any data 
             keyed into the field will not be displayed. The cursor moves 
             to  the  right as characters are keyed,  and the  characters 
             entered are available to your program, but the person at the 
             keyboard never sees them (unless you display them  elsewhere 
             on the screen in a visible field). In the mainframe environ-
             ment  invisible  fields are commonly used for the  entry  of 
             security  passwords.  Their use in the micro environment  is 
             more limited.









        Pascal Library Member EM3270.INC                 Page 7


             On  the monochrome display,  the Bright/Dim bit  causes  the 
             characters  of the field to be displayed in normal white  on 
             black (Dim) when set to 1, or as inverse video (bright) when 
             set to 0.  In the 3270, the equivalent bit simply causes the 
             equivalent  of  Turbo's LowVideo and  NormVideo  procedures. 
             However, one of the shortcomings of the original 3270 family 
             was  that their was no easy way to show the user the  length 
             of  a  data entry field.  The cursor always moves  into  the 
             leftmost  position  of the field,  but there was nothing  to 
             show  the  user where the right end of the  field  was,  and 
             therefore no sure indication of how many characters he could 
             enter before the cursor jumped to the next field. The intro-
             duction  of inverse video models offered a solution to  this 
             problem  and  programmers quickly adopted  the  standard  of 
             setting  unprotected  (data entry) fields to  inverse.  This 
             standard is implemented in the Bright/Dim bit in EM3270.

             On the color display,  the Bright/Dim bit selects one of two 
             background/foreground  color  combinations  (see  section  I 
             below). This has nothing to do with the actual brightness or 
             dimness of the background and characters; it merely provides 
             a convenient way of selecting between two palettes.

             The  color  bits of the attribute are used to  override  the 
             foreground  color of the palette selected by the  Bright/Dim 
             bit.  If  these  four bits are 0000,  the palette  color  is 
             displayed. A value of 0001 through 1111 cause the foreground 
             color  to be the equivalent color (dark blue through white). 
             Note  that Turbo provides predefined integer  constants  for 
             each  color  which can be conveniently added or ORed  to  an 
             attribute  byte.  For example,    Attr := LightGreen    will 
             give  an attribute that will cause light green characters on 
             the "bright" background color. The color bits have no effect 
             on a monochrome monitor.

             Four  constants  are  defined in EM3270 for  convenience  in 
             working with attributes: Dim, Blinking, Invisible, Modified. 
             These constants facilitate such attribute setting statements 
             as:

                       Attr := Dim + Blinking + Magenta;

             and attribute testing statements like:

                       If (Attr and Modified) <> 0 Then . . .

          H. Modified_Data_Tags             __________________

             The modified data tag (bit 4) is normally set off (0) when a 
             data field is written.  If the user changes any data in  the 
             field during a ReadScreen procedure,  it will be set on (1). 
             You can,  however turn it on before writing the field and it 
             will  stay  on  no matter what the user does.  If  the  user 
             simply  moves  the cursor through a field  with  the  cursor 
             control keys,  the MDT will not be set.  If the user deletes 








        Pascal Library Member EM3270.INC                 Page 8


             or enters any data in the field,  the MDT will be set,  even                        ___                                                
             if the data is the same as the original contents. The MDT is 
             set  or  not in an invisible field exactly as for a  visible 
             field.

          I. Defining_Color_Palettes             _______________________

             The background and foreground colors for "bright" and  "dim" 
             fields are controlled by setting four global variables named

                            BrightBG, BrightFG
                            DimBG,    DimFG

             These are of type Byte.  The background colors may be set to 
             any of the "dark" colors,  0 (Black) through 7  (LightGray). 
             The  foreground colors may be set to any of the 16  standard 
             colors, 0 (Black) through 15 (White).

             These  variables may be set or reset at any time and can  be 
             used  to  cause some interesting effects  on  color  screens 
             (they have absolutely no effect on monochrome screens).  For 
             example,  a data entry field can be written with one palette 
             in  effect  and read with another in effect by changing  the 
             palette  variables between the WriteField (or  RewriteField) 
             and  the ReadScreen procedure calls.  As the user keys  data 
             into the field,  the background and foreground colors change 
             as each character is entered.

             These  variables  are normally reset immediately  after  the 
             InitScreen procedure call.  InitScreen sets them to white on 
             black  for dim and black on white (inverse video) for black, 
             giving  an  approximation of the apearance of  a  monochrome 
             screen.

             Note  that the entire screen background color is set to  the 
             DimBG value,  so that "bright" fields appear as "islands" of 
             the BrightBG color in a sea of DimBG.

          J. Field_Positioning             _________________

             The  position  of a data or prompt field on  the  screen  is 
             specified  by an "X,Y" pair of coordinate.  X is the  column 
             number on the screen and Y is the line number.

             X must be from 1 to 80.  Y must be from 1 to 25.  The use of 
             line 25 is discouraged, except for brief error messages. The 
             procedures  use  the  right end of line 25  to  display  the 
             Insert mode flag,  and other uses for this line may be added 
             to EM3270 in the future.  Besides, the most common models of 
             the 3270 don't have a 25th line.

          I. Field_Length             ____________

             The  length  of a data or prompt field is specified  at  the 
             time it is written.  The length must be from 1 to 79 charac-








        Pascal Library Member EM3270.INC                 Page 9


             ters.

             There  is  no necessary connection between the length  of  a 
             string written to a field and the length of the field.  A 20 
             character  long field can be initialized with a 4  character 
             string  (in which case 16 spaces will be added to the end of 
             the  displayed field),  or with a 100 character  string  (in 
             which  case  the last 80 characters will not be  displayed). 
             However,  when  retrieving  strings from  the  screen,  care 
             should  be taken to ensure that the receiving string  is  at 
             least  as  long as the defined screen field.  Defining a  15 
             character screen field and then trying to read it back  into 
             a  10 character string can cause subtle and insidious  prob-
             lems  that would bring tears to the eyes of the most experi-
             enced Turbo programmers. This flexibility (and its attendant 
             problems)  result from the {$V-} option at the beginning  of 
             your program.

             No test is made for "line-wrap".  A 20-character field writ-
             ten at X position 75 will give unpredictable results.

          J. AID_Keys             ________

             The  AID  keys recognized by EM3270 are the  ENTER  (RETURN) 
             key,   the  ESCAPE  key,   F1..F10,   Alt/F1..Alt/F10,   and 
             Alt/1..Alt/3.  An "enumerated type" is defined at the begin-
             ning of the INCLUDE file:

               AID = (Enter,Escape,F1,F2,F3,F4,F5,F6,F7,F8,F9,F10,
                      F11,F12,F13,F14,F15,F16,F17,F18,F19,F20,
                      PA1,PA2,PA3);

             Alt/F1..Alt/F2   map  to  F11..F20;   Alt/1..Alt/3  map   to 
             PA1..PA3.

             You  must define at least one variable of type AID  to  hold 
             the  value of the AID key pressed to return control to  your 
             program. The value of this variable may be tested for any of 
             its defined values with If or Case statements.

             Most  3270  keyboards  have more AID keys  than  this.  3270 
             keyboards have from 9 to 24 PF ("programmed function") keys, 
             plus ATTN,  CLEAR,  and a strange and seldom used one called 
             "Test Req". The PC keyboard's 10 function keys map nicely to 
             the 3270's PF1 through PF20,  using the Alt key to  generate 
             PF11 through PF20,  and the Alt/1 through Alt/3 key combina-
             tions  map to PA1 through PA3.  The RETURN key is mapped  to 
             the 3270 ENTER key by the EM3270 procedures.  The ESCAPE key 
             can be used to simulate the 3270's CLEAR or ATTN key at your 
             option.  If you need more AID keys,  you can modify the fol-
             lowing sections of code in EM3270.INC to add them:












        Pascal Library Member EM3270.INC                 Page 10


                  - The Const section of procedure ReadScreen 
                  - The definition of type AID
                  - Procedure GetChar
                  - The last Case option in procedure ReadScreen
                  - The "Until" test in ReadScreen

        III. PROCEDURES

          A. InitScreen             __________

             USAGE:    InitScreen;    { no parameters }

             This procedure has no visible affect.  It merely initializes 
             the heap pointers to Nil,  determines the monitor type,  and 
             sets  the background and foreground colors to their  default 
             values.

             THIS  PROCEDURE  MUST BE EXECUTED BEFORE ANY OTHER  EM3270 
             PROCEDURE AND SHOULD BE EXECUTED ONLY ONCE!!!!!

          B. NewScreen             _________

             USAGE:    NewScreen;     { no parameters }

             This procedure clears and resets the screen and deletes  all 
             fields from the heap. It should be used every time a new set 
             of prompts and fields is to be presented.  Using ClrScr will 
             clear  the  screen,  but all data fields from  the  previous 
             screen will still exist and results could be catastrophic.

          C. WritePrompt             ___________

             USAGE:    WritePrompt (X, Y, Attr, Lngth : Byte;
                                    Strngin           : ScreenLine);

                  X = Column number of prompt (1..79)
                  Y = Line number of prompt (1..25)
                  Attr = Atrribute for prompt
                  Lngth = Length of prompt field (1..79)
                  Strngin = Prompt literal (any string)

             This  procedure writes one prompt to the screen at the posi-
             tion  indicated  by  X,Y.  All  bits of  the  attribute  are 
             effective except the Visible/Invisible bit and the  Modified 
             Data Tag.

         D. WriteField            __________

             USAGE:    WriteField (X, Y, Attr, Lngth : Byte;
                                   Strngin           : ScreenLine);

                  X = Column number of data field (1..79)
                  Y = Line number of data field (1..25)
                  Attr = Atrribute for data field
                  Lngth = Length of data field (1..79)








        Pascal Library Member EM3270.INC                 Page 11


                  Strng = Data field literal (any string)

             This  procedure  defines and writes one data  field  to  the 
             screen  at the position indicated by X,Y with the character-
             istics indicated by Attr.  The field number is determined by 
             the number of executions of WriteField since the last execu-
             tion of NewScreen.

          E. ReadScreen             __________

             USAGE:    ReadScreen (FieldNo     : Byte;
                                   Var FuncKey : AID);

                  FieldNo = Data field number in wich to initially  place 
                            the cursor
                  FuncKey = A  variable  you define in which the AID  key 
                            pressed by the user is returned

             This  procedure "unlocks" the keyboard for data  entry.  The 
             procedure  maintains control allowing the user to  enter  or 
             erase data in any data field until an AID key is pressed.

             Upon return from ReadScreen,  the position of the cursor  at 
             the  time  the  user pressed the AID key is available  in  a 
             record named "Cursor". Its fields (all of type BYTE) are:

                  Cursor.Field   The field number in which the cursor was 
                                 positioned.
                  Cursor.Char    The  character number within the  field. 
                                 May be used to index the string returned 
                                 from the field.
                  Cursor.X       The screen column of the cursor.
                  Cursor.Y       The screen line of the cursor.

          F. GetField             ________

             USAGE:    GetField (FieldNo   : Byte;
                                 Var Strng : ScreenLine;
                                 Var Attr  : Byte);

                  FieldNo = Data field number to be retrieved
                  Strng = Returned  string  containing current  value  of 
                          field.  Must be at least as long as the defined 
                          field.            
                  Attr = Returned current attribute of data field

             This procedure returns the current value of a data field. It 
             is normally used after a ReadScreen procedure, once for each 
             field to be examined.

          G. RewriteField             ____________

             USAGE:    RewriteField (FieldNo : Byte;
                                     Strngin : ScreenLine;
                                     Attr    : Byte);








        Pascal Library Member EM3270.INC                 Page 12



                  FieldNo = Data field number to be rewritten
                  Strng = String to be written
                  Attr = New attribute for field

             This procedure replaces the value of a data field already on 
             the screen. Some occasions on which it is normally used are:

               1. Displaying  records  from  a file which  the  user  may 
                  change.

               2. Displaying default values which may be overkeyed.

               3. Rewriting  a field that has failed an edit test with  a 
                  blinking or alternate color attribute.

               2. The data field has been "prettied up" by editing and is 
                  being displayed in its modified form for the benefit of 
                  the user.

          H. SetVid             ______
             NormVid             _______
             LowVid             ______

             USAGE     SetVid (At : Byte);
                       NormVid (At : Byte);
                       LowVid (At : Byte);

                  At = Attribute byte

             These procedures may be used to set the video mode based  on 
             an attribute byte at any time. SetVid sets the mode based on 
             the  entire attribute except for the Visible/Invisible  bit. 
             NormVid  and  LowVid bypass the Bright/Dim bit and  set  the 
             video mode directly to "bright" or "dim" respectively,  with 
             blink and color as specified by the attribute.

             Calls  to  these procedures are normally made  before  using 
             Turbo's  Write or WriteLn procedures to add something to  an 
             existing screen (an error message on line 25, for instance). 
             You  could use TextBackground and TextColor just as  easily,                   _____                                                   
             but  the  use  of these procedures will  keep  your  program 
             "attribute oriented".

        IV. OPERATION

          A. Cursor_Control             ______________

             During  the  ReadScreen  procedure the cursor can  be  moved 
             anywhere in any data field without affecting the contents of 
             the fields by the use of several cursor control  keys.

             Cursor  movements  and  the keys which control them  are  as 
             follows:









        Pascal Library Member EM3270.INC                 Page 13


             CURSOR RIGHT:  Right Arrow. Moves the cursor one position to 
                       the right without affecting data. if the cursor is 
                       in the last position of a field,  it jumps to  the 
                       beginning of the next field.

             CURSOR LEFT:  Left  Arrow.  Moves the cursor one position to 
                       the left without affecting data.  If the cursor is 
                       in the first position of a field,  it jumps to the 
                       beginning of the preceding field.

             TAB RIGHT:  TAB  key.  Moves the cursor to the beginning  of 
                       the next data field without affecting data.

             TAB LEFT:  Shifted TAB or Backspace key. Moves the cursor to 
                       the  beginning of the preceding data field without 
                       affecting data.  The Backspace key is used because 
                       it  is in the approximate position of the  Backtab 
                       key  on most 3270 keyboards.  Shifted TAB is  also 
                       used, because of PC conventions.

             NEW LINE:  PgDn  key.  Moves the cursor to the beginning  of 
                       the  first data field on the next line down  which 
                       contains  a data field.  If the cursor line is the 
                       last  such  line on the screen  the  cursor  wraps 
                       around  to the first line containing a data field. 
                       The choice of PgDn is arbitrary, and can easily be 
                       changed to Down Arrow or some other key.  Unfortu-
                       nately, on most 3270 keyboards the New Line key is 
                       in  about  the same position as  the  PC's  Return 
                       (Enter) key,  and moreover is marked the same (ar-
                       row  down and left).  If the Return key were  used 
                       for New Line, there would be no appropriate key to 
                       use  for  Enter.  (The 3270's Enter key  is  about 
                       where  the  PC's Caps Lock key is,  except on  the 
                       3270 "data entry" keyboards,  where it is  located 
                       roughly  where the PC's left bracket key  is.  IBM 
                       was never much good at ergonomics or consistency.) 
                       Also,  you'd  think  that logically the  PgUp  key 
                       would  jump  the cursor UP one line;  there is  no 
                       such key on the 3270.

             HOME:      The Home key returns the cursor to the first data 
                       field on the screen.

          B. Editing_Keys             ____________

             INSERT MODE:  Ins key.  In insert mode,  characters typed by 
                       the  user  are inserted at  the  cursor  position, 
                       pushing characters right until a non-blank charac-
                       ter  is the last in the field.  This is a  toggle. 
                       Pressing it again turns off insert mode. (The 3270 
                       keyboard  has  a RESET key which turns off  insert 
                       mode.)

             DELETE:   Del  key.  The character at the cursor is  deleted 








        Pascal Library Member EM3270.INC                 Page 14


                       and  all characters in the field to the right  are 
                       shifted left one position. A space is shifted into 
                       the rightmost position of the field.

             ERASE EOF: End  key.  All characters in the data field  from 
                       the  cursor position to the end of the  field  are 
                       set to spaces (erased).  This is another arbitrary 
                       key choice, since there is no analogous key on the 
                       PC.

          C. Data_Entry             __________

             Any printable ASCII character entered ($20..$7E or ' '..'~') 
             will  replace the character in the cursor position and  turn 
             on the modified data tag of the field.

          D. Data_Transmission             _________________

             When all data entry has been completed,  control is returned 
             to the application program by pressing any of the AID keys.

        V. PROBLEMS

          A. One of the most common problems in using EM3270 is FORGET-
             TING TO CALL INITSCREEN before the first call to one of  the 
             other  procedures.  The symptoms of this are almost always a 
             totally "locked up" system.

          B. CALLING  WRITEFIELD  MORE THAN MAXFIELDS TIMES  will  almost 
             always send your program into never never land.

          C. FORGETTING  TO CALL NEWSCREEN before writing prompts or cal-
             ling WriteField will not lock up the system, but will result 
             in "garbage" screens and unpredictable cursor positioning.

          D. OVERLAPPING  FIELDS  AND/OR  PROMPTS are  simply  errors  in 
             specifying correct X/Y values in WritePrompt and WriteField.

          E. SPECIFYING  A FIELD NUMBER HIGHER THAN THE HIGHEST  ONE  DE-
             FINED in arguments to ReadScreen,  RewriteField and GetField 
             causes  unpredictable  results - frequently a  total  system 
             lockup.

          F. THE  RETURN KEY can cause problems to people who are used to 
             the  Teletype  (and PC) standard of hitting  it  after  each 
             field.  It  can also cause problems for some 3270  operators 
             since  on the PC keyboard it is in the sames position as the 
             NEW LINE key on most 3270 keyboards.  One way to get  around 
             this is to modify the EM3270 procedures so that the RETURN 
             key is not one of the AID keys,  but performs the same func-
             tion  as TAB or PgDn.  Another way is to eliminate the ENTER 
             function  through programming:  every time you  return  from 
             ReadScreen  with  an AID value of ENTER,  simply go back  to 
             ReadScreen  again with the cursor placed in the  next  field 
             (determined  by  adding 1 to Cursor.Field and  allowing  for 








        Pascal Library Member EM3270.INC                 Page 15


             falling  out of the last screen field).  In either of  these 
             solutions, you sacrifice the ENTER AID function and must use 
             only the function keys or ESCAPE to get your data.