SWAP-LPT.DOC -- Documentation for SWAP-LPT.COM Copyright (c) 1990 David Cowart. SWAP-LPT.COM may be freely distributed without charge, provided that this documentation file is distributed along with it. DISCLAIMER THE AUTHOR MAKES NO WARRANTY, EXPRESSED OR IMPLIED, REGARDING THE SWAP-LPT PROGRAM OR THE ACCOMPANYING DOCUMENTATION, INCLUDING BUT NOT LIMITED TO WARRANTIES OF CONTENT, PERFORMANCE, OR FITNESS FOR A PARTICULAR PURPOSE. IN NO EVENT SHALL THE AUTHOR BE LIABLE FOR ANY LOSS OF DATA OR PROFIT OR FOR ANY OTHER DAMAGE, INCLUDING BUT NOT LIMITED TO SPECIAL, INCIDENTAL, CONSEQUENTIAL, OR OTHER DAMAGES. SWAP-LPT.COM is a small TSR program that allows you to swap printer ports LPT1 and LPT2 of an IBM PC/XT/AT, IBM PS/2, or true compatible by pressing a "hot key." Each time that the hot key is pressed, the program swaps the addresses of the two ports and then beeps to indicate the current configuration of the ports. One beep means that the ports are swapped (reversed); two beeps mean that the ports have been restored to their normal configuration. When resident, SWAP-LPT occupies 480 bytes of RAM. To keep memory usage as low as possible, the program does not contain provisions for uninstalling itself without rebooting, nor does it check to see whether it is already installed. To install SWAP-LPT, simply enter its name at the DOS prompt. No command-line options are provided. As with any TSR program, do not install SWAP-LPT from a DOS shell. The default hot key for SWAP-LPT is -

. If you would like to use a different combination, see the patching information below. PATCHING SWAP-LPT.COM The following patch points are identified so that you can use either a disk editor or the DOS Debug utility to change the hot key and the frequency (pitch) and duration of the beeps. Feel free to make these changes to your own copy of SWAP-LPT, but please do not distribute any copies to which you have made any changes. Note that the offset addresses shown are for use with a disk editor; if you use Debug to do the patching, the addresses will be 100h higher. (For example, the byte that determines the scan code of the hot key will be at offset 0103h instead of at 0003h.) All values shown are hexadecimal. SWAP-LPT Patch Points: Description Offset Size Default Value scan code of hot key 0003 byte 19h shift code of hot key 0004 byte 08h beep frequency (pitch) 0005 byte 10h beep duration 0006 word 8000h (00 80) Notes: The scan-code byte contains the IBM PC keyboard scan code, not the ascii code, of the the hot key's non-shift key. The default value of 19h is the scan code for the

key. The shift-code byte determines which shift key (, , , or ) must be pressed together with the key specified by the scan-code byte. Valid values for the shift code are as follows: 01  02  04  08  To use multiple shift keys, add the appropriate values shown above and convert the result to hexadecimal form. For example, 0Ch is the shift code for  + . For the byte that determines the frequency of the beeps, lowering the value will raise the frequency (and vice versa). The two-byte word that determines the duration of the beeps can be any value between 0001h and FFFFh. The higher the value, the longer the duration. To be completely accurate, I should point out that a value of 0000 is valid too and provides the longest possible duration. When patching this word, remember that two- byte values are stored low-byte first: the value 8000h, for example, is stored as 00h 80h. If you change the hot key, you'll probably also want to change the hot-key information that is displayed when the program is first installed. The line "Press Alt-P to swap LPT1 and LPT2." should be easy to find and modify. I've added twelve space characters (ascii 20h) at the end of the line to provide room for longer hot-key names (such as "LeftShift-F10"). To avoid overwriting any code, do not lengthen this line by more than twelve characters. Acknowledgement of Trademarks: IBM, PC, XT, AT, and PS/2 are trademarks or registered trademarks of International Business Machines Corp.