A GUIDE TO THE MVP-FORTH SYSTEM
               Prepared for the BCS Amiga Group
                       by Tom Cardozo


INTRODUCTION

   FORTH is an interesting and powerful language invented by Charles H.
Moore. It was designed to be a fast, compact, and extendable language to be
used for real-time data acquisition and process control. It is a language
which is fairly easy to learn to use, but rather more difficult to master.
The best way to learn FORTH is to obtain a good book on the language, sit at
the computer, and start using it.

   The recommended good book is:
         Starting FORTH   by Leo Brodie
It is published by Prentice-Hall and it is available wherever fine books are
sold.  By tradition most Forth books have a pun in their title.

   This is not the place for an in-depth analysis of the language and
its features, but a list of its main features (with, however, minimal
explanation) is in order. Hence:

   1)  FORTH is a threaded code interpreter
   2)  it is an interactive language -- type at it and it responds
   3)  it is extendable -- new words (functions) may be defined and
      they become part of the language
   4)  it is stack-oriented -- most words take their parameters from
      the stack and leave their results there
   5)  it uses Reverse Polish Notation for nearly everything (this is a
      consequence of the previous feature)
   6)  easy interface to assembly language -- an assembler is usually
      part of the package

   There are some drawbacks to the language. The main disadvantage is
that FORTH code can be very difficult to read. The reason for this is that
most operations are performed on the stack, so there is less need for named
variables and there is a lot of stack manipulation (swapping, duplicating,
and moving stack items) to get required items on the stack and in the right
order. Because of this, it can be very difficult to determine exactly what
is on the stack when a word is executed. The stack orientation also make the
control flow features of the language a little peculiar.

IMPLEMENTATION

   This is an implementation of FORTH that is normally distributed by
Mountain View Press, but it has been put into the public domain as shareware
by its author. If you find this program useful, you are requested to send a
donation to the author:
         Glenn Tenney
         Fantasia Systems, Inc.
         P.O. Box 5260
         San Mateo, CA
            94402

   If you are interested in FORTH, then this package is well worth the
contribution.  The only thing lacking that is neccessary is documentation.
This is available through Mountain View Press and, presumably, through the
author. If you intend to do any program development, or to port any other
FORTH program to this system, you will need good documentation.

   There are three FORTH systems in this package, each executable from
the workbench or CLI. MVP-FORTH is the basic system for the Amiga. FORTH is
the basic system with some useful utilities, a 68000 assembler, and the
standard FORTH line editor added. The source code for all these are included
and this system is built from the first by loading the appropriate files.
The third system, 4TH, was built to test everything and because the standard
editor will drive anyone insane. It includes the utilities file and the
screen editor (double meaning here) by Harry Laxen.

  On activation all three Forths come up with a message.  Just type a <cr>
to get to the "ok" promt of the Forth

  You exit any of these Forths by typing bye, and it returns you to the
workbench or CLI, depending or where you came from.

   On the subject of editors: the standard FORTH line editor is
documented in Starting FORTH and the other is briefly described later in
this document. I recommend the use of the Laxen editor.

SOURCE FILES

   mvpamiga.scr   this is the source for the basic Amiga FORTH system
            it is already incorporated into MVP-FORTH and
            therefore is primarily useful as documentation

   mvpamiga.ext   a bit more Amiga stuff for system interface --
            library and DOS calls, etc.

   mvputil.scr   a bunch of useful utilities, especially extentions
            to provide compatibility with the FORTH, Inc.
            version documented in Starting FORTH

   mvpedit.scr   the standard FORTH line editor

   laxen.ed   Harry Laxen's full screen editor

   68kasm      a FORTH assembler for the 68000

   TJCutil.scr   a decompiler and other utilities provided by TJC

THE FORTH FILE SYSTEM

   Traditionally, FORTH does not use a file system; it divides the
entire disk into small chunks (usually each is 1024 bytes) called screens
and all I/O is done to specific screens. While there are conventions about
screen usage, it is up to the user to keep track of where everything is.
This version of FORTH does take advantage of the Amiga's file system, but
the standard screen orientation is retained for saving, editing, and loading
source code. Each source file is viewed as being partitioned into 1024-byte
screens and FORTH views the current file as if it were an entire disk. This
allows for easy screen organization; source code for different applications
and programs are kept in different files, so the number of screens within a
file is relatively small and they are easily organized with the traditional
FORTH techniques.

   The FORTH words used for basic interaction with source code files
are the following:
      list      ( n --- )   list screen #n of current file
      load      ( n --- )   load & compile contents of screen #n
      index     ( n1 n2 --- )   list 1st line of screens n1 thru n2
      e         ( n --- )   edit (with Laxen editor) screen #n

   The file system used by MVP-FORTH allows for eight files to be open at
the same time. One of the files is designated the active file. All file I/O
is performed with the active file; to access any other file, it is
neccessary to mark that file as the active file. Files, after they have
been opened, are refered to by an integer in the range 0-7 which is an index
into the file table.

   The basic words (and their definitions) used to interact with the
file table  are:
      files    ( --- )       display the file table
      file#    ( --- n )     return id of the active file
      select   ( n --- )     make file with index n active
      nextfile ( --- n )     return index of next open slot in the
               file table

   To open an already existing file, say mvputil.scr, type the
following command:
             from mvputil.scr
Now the usual FORTH words to list, load, and edit screens will use this file
for the FORTH screen file system as long as it is the active file. NOTE that
this command will use the current active file index for inserting the file
into the file table -- the user must insure that this does not clobber
another already open file. Use nextfile and select to make the active file
index point into the first empty slot in the file table.

   The FORTH words to open and close files are:
      open      (addr count mode --- )
               open file in designated mode; the name of
                  the file is the string pointed to
                  by addr & count
      new      ( --- mode )   sets mode needed to create a new file
      old      ( --- mode )   sets mode needed to open existing file
      closefile ( n --- )     close file with index n

   The FORTH word load really executes the code stored in the specified
screen. For source code, what is usually executed are colon definitions to
compile new words, but anything that can be typed in interactively can be
stored on a screen and can be executed by loading that screen. A typical use
of this is to create a load screen which contains all the instructions for
loading a particular application. This implementation of FORTH has a word
which will open a file, load screen one (presumably the load screen for the
file), and then close the file. The appropriate command for this is, for
example:
      include mvputil.scr

SCREEN EDITOR

  COMMANDS for the Laxen Screen Editor:
   
   ^E   move cursor up one line
   ^X   move cursor down one line
   ^R   move up four lines
   ^C   move down four lines
   
   ^S,^H   move cursor to previous character
   DEL   move to previous character
   ^D   move right one character
   ^F   move right one word
   ^A   move left one word
   
   ^I,TAB   tab
   ^V   toggle insertion mode (when off, overwrite)
   ^N   insert a Carriage Return
   
   ^G   delete character under cursor
   ^T   delete word right
   ^B   delete line contents leaving blank line
   ^Y   delete line (lower lines move up)
   ^K   delete (kill) screen
   
   ^Z   abandon screen (forget changes)
   ESC   exit editor and save screen

   NOTE:   the arrow keys also control cursor movement


NOTES

   (1)  I had a few problems building a new soucre file when using
      the standard line editor. I got around this by copying an
      existing file, clearing screens, and entering my code. If I
      did not do this, I occasionally lost screens. The problem
      involved the filesize according to the file system and the
      the FORTH system and how to make them agree. I don't know if
      the problem exists with the Laxen editor.

   (2)  MVP-FORTH uses angle brackets rather than parentheses in the
      names of certain low level words (for example, <;code> rather
      than (;code) as is usual). This is one source of difficulty
      in porting FORTH code, especially without documentation.

   (3)  There are ways to make system calls to AmigaDOS and to call
      functions in the system libraries, but I have not had the
      time to investigate them. If you are interested, the methods
      are used in mvpamiga.scr to set up the file system interface.

   (4)  Most of the information in this document was discovered by using
      the system and reading the source screens provided. I think
      that it is accurate and I have tried most of it, but if I
      have made any errors, please let me know. As I mentioned
      earlier, reading FORTH is not always easy.

(5)   These Forths all use the Forth-79 standard - the cforth is not quite
      that compatable with these because it uses some Fig-Forth type
      formats.

   I would be interested in finding out how many of the BCS Amiga group
are interested in FORTH in any serious way. I am in the process of obtaining
the documentation for this system because I would like to use the Amiga's
graphics capabilities from FORTH, but figuring everything out just from
source code is too tedious. There are a number of interesting programs that
I would like to port to the Amiga, especially if there are others interested.
Please send me any questions, comments, or requests. I can be reached at the
BCS Amiga meetings (both monthly meetings) or by mail at the following
address:
         Tom Cardozo
         P.O. Box 881
         Acton, MA  01720


Here is a simple Forth program for you to try (taken from Starting Forth)
At the "ok" promt just type the following (note the cr here is not a
carrage return, it is a command in Forth to generate a carrage return, and
do put in the colons at the beginnings of the lines where shown):

: star  42 emit ;
: stars  0 do star loop ;
: margin  cr 30 spaces ;
: blip  margin star ;
: bar  margin 5 stars ;
: f  bar blip bar blip blip cr ;

f

(Note: the interpreter will type "ok" after you put in each line )

This will then type out a large F in stars.  This program creats a number of
Forth words (functions).  The star word creats an * output, and all the
others build on this.

Do not forget to type bye to exit the program.

Glenn Chapman, BCS Amiga Software Librarian, July 9, 1986