NOHISS: Digital Noise Reduction
                           ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
                        (C) Copyright 1991, 1992 by Andy Hakim
                                 All Rights Reserved


                                U S E R   M A N U A L

                                     Version 1.2





          For a quick summary of options, type NOHISS at the dos prompt.














































                                  TABLE OF CONTENTS



     ADDRESSES ............................................................. 1

     SOFTWARE LICENSE ...................................................... 2

     DISCLAIMER  ........................................................... 2

     ABOUT NOHISS .......................................................... 3

     FILE FORMATS .......................................................... 3

     COMMAND LINE SYNTAX ................................................... 4

     COMMAND LINE OPTIONS .................................................. 5
         /? ................................................................ 5
         /HELP ............................................................. 5
         /NR=# ............................................................. 5
         /SIZE=# ........................................................... 5
         /RANGE=# .......................................................... 6
         /MIN=# ............................................................ 6
         /MAX=# ............................................................ 6
         /[NO]FANCY ........................................................ 6
         /[NO]OVER ......................................................... 6
         /[NO]PROCESS ...................................................... 6
         /[NO]PAUSE ........................................................ 6
         /[NO]PLAY[I][O] ................................................... 7
         /TIME=# ........................................................... 7
         /PORT=# ........................................................... 7
         /SAVE ............................................................. 7
         /RESET ............................................................ 7
         > NUL ............................................................. 7

     COMMAND LINE EXAMPLES ................................................. 8

     ERROR MESSAGES ........................................................ 9

     SOURCE CODE ........................................................... 10

     TRADEMARKS ............................................................ 10

     REVISION HISTORY ...................................................... 10






















     Nohiss Version 1.2                                                  Page: 1
     ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß
     

     ADDRESSES
     ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
     Direct all correspondence to:


                        US Mail ³ Andy Hakim
                                ³ 816 Pecore Street
                                ³ Houston, TX 77009-6034
                                ³
                      Telephone ³ +1 713-880-3059
                                ³ +1 713-869-6138 (alternate)
                                ³
                       Internet ³ AHakim@UH.EDU
                         BITnet ³ AHakim@UHOU
                  DECnet/THEnet ³ UHOU::AHakim
                                ³
                 Bulletin Board ³ Sands BBS           
                                ³ +1 713-961-1604
                                ³ 2400/9600/14400 baud, HST/v.32
                                ³ Userid: "Andy Hakim"










































     Nohiss Version 1.2                                                  Page: 2
     ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß
     

     SOFTWARE LICENSE
     ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
     Nohiss 1.1 is free for individual, non-commercial use, but if you find it
     of value, you are encouraged to register your copy.

     The registration fee is US $20.  Your registration will allow the author to
     continue to enhance this product and will be greatly appreciated.

     Registered users will be informed of new versions as they become available. 
     Please provide the following information along with your comments and
     suggestions:

             þ Your Name
             þ Postal address and Phone
             þ Electronic mail address (ex: Compuserve, Internet)
             þ Current PP version, and where you obtained it
             þ What computer system, mouse, and software do you
               use PP with?

     Software disk vendors, BBSs, FTP sites, and User Groups may distribute
     copies of Nohiss as long as all files from the original PP10.ZIP are
     distributed unmodified.

     Freeware software developers may distribute unmodified versions of the
     PP.EXE and PPCONFIG.EXE executables along with their program provided that
     they inform the author.

     All other users and distributors of Nohiss, including shareware and
     commercial software developers, must contact the author for licensing
     agreements.  Please call or write for more information.




     DISCLAIMER
     ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
     Users of Nohiss must accept this disclaimer of warranty:

          Nohiss is supplied as is.  The author disclaims all warranties,
          expressed or implied, including, without limitation, the warranties of
          merchantability and of fitness for any purpose.  The author assumes no
          liability for damages, direct or consequential, which may result from
          the use of Nohiss.



















     Nohiss Version 1.2                                                  Page: 3
     ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß
     

     ABOUT NOHISS             
     ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
     Nohiss reduces or removes background "noise" that is almost always present
     when a recording is made on a Soundblaster card.  Background noise is most
     apparent when using a microphone, but is also present to some degree if you
     use a direct input connection.

     Graphically, "hisssssss" looks like this:

       +128ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     A     ³                        .   Speech                             ³
     m     ³                       . .       .                             ³
     p     ³                      .   .     . .                            ³
     l     ³ . . . . . . .       .     .   .   .         Silence (nohiss)  ³
     i    0³. . . . . . . .     .       . .     .   .......................³
     t     ³               .   .         .       . .                       ³
     u     ³ Hisssssssss    . .                   .                        ³
     d     ³                 .   Speech                                    ³
     e     ³                                                               ³
       -128ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
           Time --->

     NOHISS was designed to work on speech recordings.  If you run NOHISS on a
     digitized music (ie: rock and roll song) file, there will probably be no
     improvement in quality.  There is no fixed level of reduction that works
     for all speech samples but by adjusting the command line parameters you
     will generally end up with a better sounding sample.  One of the good side
     effects of NOHISS is that the output file will probably compress (using a
     file compression program) tighter than the original.  You can also get
     better results when using the Soundblaster's "silence compression" option. 
     Run DEMO.BAT to hear a sample of the before and after versions of a speech
     sample.






























     Nohiss Version 1.2                                                  Page: 4
     ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß
     

     FILE FORMATS
     ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
     NOHISS supports the following digitized file formats:

     .VOC - Soundblaster 8-bit VOICE format.  Currently, only the unpacked
            format is supported.  Normally when you record a sound, it is
            stored in an unpacked state.  The Soundblaster/PRO Stereo sound
            format it not supported at this time.  If the VOC file contains
            special blocks such as markers, text information, they will
            automatically be copied without change.

     .SND - This is raw 8-bit data with header information.  There are two
            basic types of SND files.  Nohiss recognizes both versions and
            retains proper header information.

     .SOU - Raw 8-bit digital data.  No header information.  The extension
            may not be SOU in all cases.


     Note:  Although you can specify different extensions for the input and
            output files, nohiss will not convert between formats.  The
            output file will remain the same format as the input file
            regardless of the file extension.



     COMMAND LINE SYNTAX
     ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
     Syntax:

           NOHISS <inputfile[.ext]> [outputfile[.ext]] [options]



     <inputfile[.ext]>
          This is the name of the file that needs to be processed.  NOHISS will
          automatically look for .VOC and .SOU files if no extension is
          specified.  This filespec is required.

     [outputfile[.ext]]
          This is the name of the output file.  Again, the extension is
          optional.  NOHISS will add an appropriate extension depending on the
          input file type.  If no output file is required, a temporary file is
          created, then deleted when the program is finished.

     [options]
          Options allow you to customize various settings.  All options can be
          saved directly to NOHISS.EXE by using /SAVE.  This saves you the
          trouble of typing each parameter on subsequent uses.













     Nohiss Version 1.2                                                  Page: 5
     ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß
     

     COMMAND LINE OPTIONS
     ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
     Options allow you to customize various settings.  Options may be in upper
     or lower case, be specified in any order, not be abbreviated, must be
     preceded by slash (/) or minus (-), and must be separated by a space ( ).


     /?   (or /HELP, or NOHISS with no parameters)
          Displays the help screen and default options.

     /NR=#
          Noise reduction level, specified in a percentage ranging from
          0 to 100.  This is the factor by which a particular sample value
          will be reduced.  For example, if /NR=50 then a data value of -6 
          will be reduced by 50% yielding -3.  Normally, this should be set 
          at 100 percent, if the /RANGE is small.

     /SIZE=#
          Minimum duration of hiss specified in samples.  There must at least
          be this many consecutive values falling in the hiss RANGE as a 
          requirement for reduction.  It is necessary to have this restriction 
          because the endings of certain words (ex: THIS), often sound
          similar to background noise.  A small SIZE value (ex: 1) will cause
          words to be clipped at the end.  On the other hand, a very large 
          size value will cause no values to qualify for reduction.  In terms 
          of time the size value is closely related to the sampling rate.  For
          example, a rate of 12000 hertz means that 12000 samples are taken
          each second.  Therefore, if you set /SIZE=12000 you are saying that
          at least one second of continous hiss must be present before it is
          reduced and any portions of hiss smaller than 1 second are ignored.

          By /SIZE=# you are defining the horizontal width:

       +128ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
           ³     SIZE               .                                      ³
           ³   ÚÄÄÄÄÄÄÄÄ¿          . .       .                             ³
           ³   ³        ³         .   .     . .                            ³
           ³ . . . . . . .       .     .   .   .                           ³
          0³. . . . . . . .     .       . .     .   .......................³
           ³               .   .         .       . .                       ³
           ³                . .                   .                        ³
           ³                 .                                             ³
           ³                                                               ³
       -128ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

          As another example, suppose you specify /SIZE=1.  In this case
          any single sample that meets the /RANGE criterion will be reduced.















     Nohiss Version 1.2                                                  Page: 6
     ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß
     

     /RANGE=#
           Hiss spectrum, specified in volume units ranging from 0 to 254.
           The program will automatically center this value around 0 (which
           is considered silence.)  Data values falling into this range are
           reduced.  The MIN and MAX values are recomputed every time you
           use this option.  Normally you want to keep this value just
           large enough to catch the hiss and not affect the voice.  If
           you start hearing words being clipped, try reducing this value.
           In my experience, a value less than 3 is pretty much useless
           and a value greater than 50 takes away too much of the voice
           data.  This value varies from sample to sample.

           Example: By /RANGE=#, you are specifying the vertical width:

       +128ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
           ³                        .    no data above this line is changed³
           ³ UPPER LIMIT (MAX)     . .       .                             ³
      R ÚÄÄ³---------------------------------------------------------------³
      A ³  ³ . . . . . . .       .     .   .   .                           ³
      N ³ 0³. . . . . . . .     .       . .     .   .......................³
      G ³  ³               .   .         .       . .                       ³
      E ÀÄÄ³---------------------------------------------------------------³
           ³ LOWER LIMIT (MIN). no data below this line is changed         ³
           ³                                                               ³
       -128ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ




     /MIN=#
           Hiss spectrum lower limit, ranging from -127 to +127.  This gives
           you precise control over the hiss spectrum.

     /MAX=#
           Hiss spectrum upper limit, ranging from -127 to +127.  This gives
           you precise control over the hiss spectrum.

     /[NO]OVER
           Turn on/off file overwrite confirmation.  If set to /NOOVER, you 
           prompted when an output file exists.  If set to /OVER then output 
           files will be overwritten without any confirmation.

     /[NO]PROCESS
           Turn on/off hiss processing.  Why would you NOT want to process a
           file?  If you only want to listen to the differences between two
           files.  NOHISS can play two .VOC files one after the other.
















     Nohiss Version 1.2                                                  Page: 7
     ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß
     

     /[NO]PLAY[I][O]
           Specifies what should be played back.  Use /NOPLAY if you do not
           want to hear anything.  Use /PLAYI to hear only the input file.
           Use /PLAYO to hear only the output file.    Use /PLAYIO to hear
           both input and output files.  During playback, you can press
           any key to stop.  Only VOC files can be played back, and only 
           the Soundblaster card is supported.

     /TIME=#
           Specifies the duration of playback in seconds.  For example, if 
           you set /TIME=5 then only the first 5 seconds of a file will be 
           played back.  By default, it is set at 3600 seconds (1 hour).

     /PORT=#
           Specifies the Soundblaster IO port address in hexadecimal notation.
           By default, the SB is jumpered at 220, but you can set it from
           210, 220... to 260.  For example, /PORT=260 sets the port address
           to 260 hexadecimal.

     /SAVE
           This causes all options specified on the command line to become 
           permanent.  The options are written to NOHISS.EXE therefore 
           no configuration files are needed.  On subsequent uses, you do 
           not have to reenter command line options.   For example, 
           NOHISS /NR=50 /PORT=230 /SAVE /? saves the port number and noise 
           reduction level, then displays the help screen.

     /RESET
          Restores factory default settings.  The new settings are automatically 
          written to NOHISS.EXE.

     > NUL
           This is not really part of Nohiss, but it is a very handy DOS
           redirection command that can be used to redirect any screen
           output to a "nul" device - a block hole sort of.  You can use this
           redirection technique if you do not want anything displayed on the
           screen.  You may also use any valid dos device (ie: prn) or filename
           in place of NUL.  This must be specified as the last option on the
           command line.  One reason why you may want to use this might be if
           you use Nohiss as a VOC file player.  Something like:
           NOHISS /NOPROCESS /TIME=2 HELLO.VOC > NUL





















     Nohiss Version 1.2                                                  Page: 8
     ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß
     

     COMMAND LINE EXAMPLES (assuming factory default options)
     ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

     C:\NOHISS SAMPLE.VOC OUTPUT.VOC

           The file named sample.voc is processed and its result sent to
           output.voc.  Both files are played back.

     ...........................................................................
     C:\NOHISS SAMPLE.VOC OUTPUT.VOC /PLAYO /TIME=5

           After processing, only the output file (in this case output.voc)
           will be played back.  The playback stops after 5 seconds.

     ...........................................................................
     C:\NOHISS SAMPLE.VOC OUTPUT.VOC /NOPLAY

           File will be processed, but NOT played back.

     ...........................................................................
     C:\NOHISS SAMPLE.VOC /NOPROCESS

           File will not be processed, only played back.

     ...........................................................................
     C:\NOHISS SAMPLE OUTPUT /RANGE=10 /SIZE=100

           RANGE is set to 10, and SIZE is set to 100 while processing.

     ...........................................................................
     C:\NOHISS /RANGE=10 /SIZE=100 /SAVE

           The RANGE and SIZE parameters are permanently saved to nohiss.exe.
           If you use the /SAVE option it is not mandotary to specify a
           filename.

     ...........................................................................
     C:\NOHISS /RESET /?

           The original factory settings are restored and saved to nohiss.exe.
           The "/?" option will display the new settings.

     ...........................................................................
     C:\NOHISS SAMPLE OUTPUT /NR=75 /PLAYO /NOPAUSE /SIZE=10 /RANGE=5 /OVER

           This will set the noise reduction level to 75%, set the range
           to 5 units, set the size to 10 samples, process the file
           overwriting OUTPUT.VOC if it exists, play the output file,
           and not pause after playing.













     Nohiss Version 1.2                                                  Page: 9
     ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß
     

     ERROR MESSAGES
     ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
     Error messages are reported on the screen as well as in the ERRORLEVEL
     system variable in DOS.  A successful run will set ERRORLEVEL to 0.

     1: INPUT FILE NOT FOUND
        Cannot file the input file.

     2: INTERNAL ERROR
        But you will never, ever get this error, trust me.

     3: INVALID COMMAND LINE OPTION
        You have entered an incorrect parameter on the command line.

     4: OVERWRITE PERMISSION DENIED
        

     5: OUTPUT FILE SAME AS INPUT FILE


     6: OPTION VALUE OUT OF BOUNDS
        The option does not have the correct range value.

     7: CANNOT ACCESS PROGRAM FILE
        The program could not write to NOHISS.EXE.  Maybe the disk is
        write protected, or you do not have write privilege on your network.

     8: SOUNDBLASTER PLAYBACK ERROR
        An error occurred while playing a .VOC file, wrong format, etc.

     9: SOUNDBLASTER INTERRUPT ERROR
        Interrupt conflict.   Try using another interrupt number.

     10: SOUNDBLASTER NOT INSTALLED OR WRONG IO PORT
        The port can be set by using the /PORT= option (see above.)



























     Nohiss Version 1.2                                                 Page: 10
     ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß
     

     SOURCE CODE
     ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
     NOHISS was written using Borland C++ v2.0.  If you are interested in the 
     copy of the source code, contact me at the addresses listed at the start 
     of this document.  If you have information on the decompression algorithms 
     used by the Soundblaster, I am interested!  Share your knowledge.




     TRADEMARKS
     ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
     Borland C++ is a trademark of Borland International.
     Soundblaster is a trademark of Creative Labs, Inc.




     REVISION HISTORY
     ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
     October 17, 1991    Version 1.0    Initial Release
     December 15, 1991   Version 1.1    Added PLAYVOC.BAT file.
     December 12, 1992   Version 1.2    EGA/VGA bug fix, Documentation Revision