EMS Emulator Software

The EMS emulator software provides services for converting the
Phantom RAM on the system board to emulated EMS memory. The
software is available from your distributor or from the Wave Mate
bulletin board.

The Wave Mate EMS Memory Manager Emulator conforms to version
4.00 of the Lotus/Intel/Microsoft (LIM) expanded memory
specification. Version 4.00 of the LIM specification is upward
compatible with version 3.20 and will run programs written for
that version of the memory manager. Since the version 4.00 LIM
specification does not support multiple memory managers, this
software <MI>cannot<D> be used at the same time that another
memory manager is being used with an IO expansion bus EMS
adapter card.

Configuration:

There are two separate hardware environments for the EMS
emulator. The standard environment is the BULLET-286ii and
BULLET-286E as shipped from the factory. In the standard
environment the EMS page frame is located in system RAM. Thus, in
a standard EMS installation with a 64K EMS page frame, the user
would lose 64K of system RAM. In the enhanced environment, the
BULLET-286ii hardware is modified to create a 64K page frame at
segment E000, in the Phantom RAM, above the 640K of system
memory. The enhanced environment requires replacing a
Programmable Array Logic (PAL) device on the BULLET-286ii. The
enhanced environment is switch selectable on the BULLET-286XT+.
The enhanced environment is not available on the BULLET-286E.
The PAL is an extra cost option which is specific to the board
assembly number. It is sold only through the Tech Support service
to ensure that the correct PAL is shipped for the target board
assembly number. The PAL is always installed in location U48 on
the BULLET-286ii. Retain the old PAL in case you ever wish to
install an IO adapter which uses segment E000. In that case, you
will no longer be able to use the enhanced environment for the
EMS emulator.

In the standard environment the EMS emulator provides 384K of EMS
memory. In the enhanced environment the EMS emulator provides
320K of EMS memory. The trade-off occurs in the system RAM, since
in the standard environment the user loses 64K of system RAM.

Installation:

The EMS emulator is installed by placing a copy of the software
in the root directory of the boot disk and adding the following
line to CONFIG.SYS:

    DEVICE=WMEMM.SYS

Limitations:

Since the EMS is emulated, certain functions, such as memory
aliasing, cannot be done. Since use of this feature is not
common, most software will run without problems. The following
software which uses EMS memory has been tested and found to work
with the EMS emulator on the BULLET-286:

Lotus 123 V2.01

Symphony V2.0

Windows/286 V2.00 (requires enhanced environment)

Publisher's Paintbrush V1.61

DOS V4.01