Program STSORBIT PLUS

                  Space Shuttle and Satellite Orbit Simulation


                  (Enhanced Version for 286/386/486 Computers)







                  (C) Copyright David H. Ransom, Jr., 1989-1992
                              All rights reserved.







                                  Version 9228A
                                  July 08, 1992




                             by David H. Ransom, Jr.
                      Rancho Palos Verdes, California, USA

                               BBS: (310) 541-7299



   Program STSORBIT PLUS Satellite Orbit Simulation                   Page i





                                TABLE OF CONTENTS
                                -----------------


   INTRODUCTION ......................................................1
   HARDWARE AND SOFTWARE REQUIREMENTS ................................5
   PROGRAM DESCRIPTION ...............................................6
   STSORBIT PLUS FILES ...............................................8
   PROGRAM SETUP AND USAGE NOTES .....................................10
     Slow Computers and 80x87 Mach Coprocessor Chips .................10
     Using a RAM Disk ................................................11
     Starting Program STSORBIT PLUS ..................................12
     Predicting Visible Satellite Passes .............................13
     Known STSPLUS Problems and Bugs .................................15
   PROGRAM OPERATION .................................................18
   THE STSORBIT PLUS GROUND TRACK DISPLAY ............................20
     World Maps ......................................................20
     Quadrant Maps ...................................................20
     Zoom Maps .......................................................21
     Location Maps with Isocontours ..................................22
     Tracking Station Maps with Isocontours ..........................22
     Big Clock Options ...............................................23
     Satellite Motion Maps ...........................................23
     On-line Help (F1 Key) ...........................................24
     Satellite Position and Orbit Projections ........................24
     User's Circle of Visibility .....................................25
     Spacecraft Circle of Visibility .................................25
     TDRS Satellite Features .........................................26
     Ground Tracking Stations and .TRK Files..........................26
   ACTIVE KEYS DURING GROUND TRACK DISPLAY ...........................30
   STSORBIT PLUS MAIN MENU ...........................................33
     F1  Program STSORBIT PLUS Demonstration .........................33
     F2  Read NASA/NORAD 2-Line Elements .............................34
     F3  Read Prior Mission Information from *.INI File ..............37
     F4  Enter New Orbital Information ...............................37
     F5  Adjust Orbital Parameters ...................................39
         2-Line Elements Model .......................................39
         Simple Orbital Model ........................................40
     F6  Set Elapsed Time Option (2-line elements only)...............41
     F7  Set FILENAMES and Paths .....................................42
     F8  Set Program TIME and DATE....................................42
     F9  DOS Shell ...................................................45
     F10 Set STSORBIT PLUS Program Options and Features ..............46
     ENTER  Resume Mission ...........................................46
     ESC    Quit STSORBIT PLUS and Save Current Mission ..............46
   PROGRAM OPTIONS AND FEATURES MENU .................................47
     F1  Program STSORBIT PLUS Information ...........................47
     F2  Set New Local Coordinates ...................................47
     F3  Set Display Features ........................................49
     F6  Set Map Center and Size .....................................49
     F7  Set for SLOW COMPUTER or NO COPROCESSOR .....................50
     F9  Set UTC Time Offset and Daylight Flag .......................50

   Program STSORBIT PLUS Satellite Orbit Simulation                  Page ii


     F10 Enable/Disable Printer Logging ..............................51
   SET DISPLAY FEATURES ..............................................53
     F1  Display LOCAL Circles of Visibility .........................53
     F2  Display TDRS Coverage .......................................53
     F3  Enable/Disable Additional Map Grid Lines ....................54
     F4  Display Tracking Stations ...................................54
     F5  Show Ascending & Descending Node Data .......................54
     F6  Display Spacecraft Circle of Visibility .....................54
     F7  Display South Atlantic Anomaly Zone .........................55
     F8  Display Terminator, Sun and Spacecraft Lighting .............55
     F9  Select Distance Units: NM or KM .............................56
     F10 Select Satellite Coordinates: RA/DEC, AltAz or XYZ ..........56
   STSORBIT PLUS'S ORBITAL MODELS ....................................57
   ADJUSTING ORBITAL PARAMETERS (Simple Orbital Model) ...............59
   STSORBIT PLUS Revision History ....................................61

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 1


   INTRODUCTION
   ------------

        Program STSORBIT PLUS is an enhanced version of STSORBIT, my original 
   orbital tracking and display program. As a general rule, a 286 or better 
   computer (AT-class IBM compatible) is recommended, and a math coprocessor 
   chip will significantly improve performance. Some users report acceptable
   performance on an XT-class machine WITH a math coprocessor. See the section 
   HARDWARE REQUIREMENTS for additional information and discussion. The 
   program is intended for use during Space Shuttle missions, for simulating a 
   Space Shuttle mission, and for general satellite tracking using NASA/NORAD 
   2-Line Orbital Elements.
        STSORBIT PLUS is copyrighted software; you are hereby granted a non-
   exclusive license for non-commercial or educational use only. Agencies of 
   the U.S. Government are also hereby granted a non-exclusive license for 
   internal use. Use STSORBIT PLUS if you like it, discard it if you don't. 
   There are no warranties of any kind. If you wish to use STSORBIT PLUS 
   commercially, write for license information. The only request I make of 
   users is that they take the time to complete and return the confidential 
   questionnaire in file README. The questionnaire gives users a chance to 
   offer comments and suggestions, and lets me know that people use and 
   appreciate STSORBIT PLUS. Registration of STSORBIT PLUS is inexpensive and 
   optional -- but will be appreciated and will encourage me to continue 
   supporting and enhancing the program.
        Program STSORBIT PLUS (which I will usually refer to as STSPLUS from 
   here on) is intended to display the position and ground track of an 
   orbiting satellite on a selection of maps ranging from a full map of the 
   world to zoom maps showing considerable detail. The program has special 
   features implemented at the request of NASA astronauts and others for use 
   during a NASA Space Shuttle mission. When used with NASA/NORAD 2-Line 
   Elements, the position and ground track of a variety of satellites, such as 
   the Space Shuttle, the Hubble Space Telescope, the Gamma Ray Observatory, 
   or the Soviet MIR Space Station, may be displayed. Special Location and 
   Tracking Station displays show concentric isocontours, circles of equal 
   satellite altitude; these special maps can be especially valuable for 
   visual or amateur radio sightings.

        The initial premise for STSORBIT was to attempt to duplicate the wall 
   map in NASA's Mission Control Center in Houston, Texas. Before I started 
   this project, I had seen  several other programs which tracked satellites 
   but each fell short of my map and display objectives for one reason or 
   another. I therefore set out to do the job myself. STSORBIT and now 
   STSORBIT PLUS have been the result. Since then other programs have appeared 
   which produce similar information, most notably Paul Traufler's excellent 
   TRAKSAT (which was inspired by STSORBIT). It may be, of course, that others 
   will judge this effort lacking as well. One problem is that of size and 
   resolution: the wall map at Mission Control Center is some twenty feet wide 
   with an impressive pixel resolution, very different from the typical 
   personal computer and the size and resolution of its monitor. The NASA wall 
   map shows essentially the entire globe in a cylindrical projection; 
   STSORBIT uses a cylindrical projection but restricts the vertical display 
   to latitudes from +85 degrees to -85 degrees in order to achieve reasonable 
   proportions and vertical resolution while at the same time showing 
   recognizable land features.
        Initially, and as a consequence of a lack of accurate orbital data for 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 2


   Space Shuttle missions while they were in progress, I did not try to be 
   especially precise with respect to the orbital mathematics. Additionally, 
   mathematical complexity had to be held to a reasonable minimum if older 
   computers not equipped with a math coprocessor were to be able to maintain 
   the presentation in real time. My somewhat casual attitude toward 
   mathematical precision changed with the launch of the Hubble Space 
   Telescope (HST) and the regular availability of NASA/NORAD 2-Line Elements 
   via modem from TS Kelso's Celestial BBS. Until HST, I had been content to 
   update the orbital data occasionally during the course of a typical five 
   day mission and live with the errors inherent in my original simple orbital 
   model. The accuracy of that model degrades rapidly after five or ten orbits 
   and, although it may be manually adjusted from time to time during a 
   mission, more accurate data are now readily available prior to a launch and 
   during a mission. The NASA SpaceLink BBS in Huntsville, Alabama began 
   posting 2-line orbital elements for the Space Shuttle in early 1991 due in 
   part to my persistent and continuing suggestions; Bill Anderson and Jeff 
   Ehmen, sysops of the SpaceLink BBS, are continually upgrading the services 
   available.
        Beginning in mid-1990, therefore, STSORBIT was extensively modified to 
   read orbital data from these NASA 2-line elements and thereby maintain 
   significantly improved accuracy over long periods of time. As an incidental 
   benefit, the ground tracks of other satellites (such as the Russian space 
   station MIR) could also be displayed. At present, the orbital model (SGP4) 
   used with 2-line elements is accurate only for low Earth orbits. Deep space 
   orbits, defined as orbits having an orbital period greater than or equal to 
   225 minutes, require a more complex orbital model (SDP4) which takes into 
   account solar and lunar perturbations for best accuracy. STSPLUS calculates 
   data and displays a ground track for deep space objects but the accuracy of 
   these data has not been validated; it is believed to be "reasonably" 
   accurate.
        At about the same time, STSORBIT also found its way to the NASA 
   Johnson Space Center in Houston, Texas. Quite a few individuals from JSC 
   sent me comments and suggestions for further improving the program, among 
   them Ron Parise of the STS-35/ASTRO-1 crew. Ron suggested that I make 
   modifications to allow the display of Mission Elapsed Time (MET) for 
   shuttle missions while using the NASA 2-line elements. This would allow 
   both the higher accuracy of the NASA 2-line orbital data and permit 
   following the mission timeline using MET. Since launch time and date are 
   not included in the 2-line elements but are required to compute MET, these 
   data must be entered independently. Another suggestion from Ron and others 
   was to include the Sun, Sun terminator (calculated at Mean Sea Level), and 
   spacecraft lighting conditions to determine if the spacecraft is visible.
        Not satisfied with the somewhat rough map used with STSORBIT, I 
   upgraded the maps to use a modified version of the World Data Base II. This 
   had the desired effect, to the point where rivers and other landmarks could 
   easily be recognized on the monitor and on downlinked orbiter television. 
   As a side effect, however, the processor overhead increased dramatically -- 
   to the point where some slower computers not equipped with a math 
   coprocessor were unable to keep up. I have therefore essentially "frozen" 
   the original STSORBIT program (except for minor updates) and created a new 
   program, STSORBIT PLUS intended for the faster, more capable processors. 
   Since mid-1991, STSPLUS has also spread throughout the various NASA Centers 
   and around the world.
        In addition to NASA and individual users all over the world, STSPLUS 
   and STSORBIT are also being used in an educational setting. As many as 1100 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 3


   high schools participated in the Inspire Project, a VLF propagation test 
   flown on STS-45 and for which STSPLUS was one of the recommended tools. At 
   a middle school in Kansas, the program is projected in the school 
   auditorium from time to time during a mission to show the children 
   graphically what is happening and to give them a sense of "real time" 
   participation in our space program. At an Air Force training facility, 
   STSORBIT is one of many tools used to prepare Air Force officers for their 
   duties in the Air Force Space Command. The program was widely distributed 
   at a recent National Association of Science Teachers convention and by 
   radio amateurs at regional "ham fests". In perhaps its most prestigious 
   installtion, STSPLUS is the software used by the NASA/JPL Multimission 
   Computer Control Center in Pasadena, California, to display the ground 
   track of Earth-orbiting satellites. Most recently, Intelsat used STSPLUS 
   operationally in May of 1992 at their Mission Control Center in Washington, 
   DC, and at five tracking stations around the world during the STS-49 
   mission, the maiden flight of Endeavour and the rescue/reboost of the 
   INTELSAT-VI satellite.

        A brief biographical note: I am a retired physicist and engineer who 
   spent all of his professional life in the world of electronics, data 
   communications and, more recently, computers. As a young man I was actively 
   involved in the early American space program, including projects such as 
   Ranger, Mariner, Mercury, Gemini, and Apollo; my interest in space has 
   continued to this day. The desire to "keep in touch" with our Space Shuttle 
   missions was one of the principal incentives in the development of this 
   software. I continue to be astonished that a relatively inexpensive 
   personal computer is sufficient to perform calculations that pushed the 
   limits of our best mainframe computers only a decade or so ago. If STSORBIT 
   PLUS also serves to help spark the interest of young people in science and 
   technology or can be a learning tool at any level, I will have more than 
   achieved my goal.
        For those who are interested in our space program and who have access 
   to a modem, I recommend NASA's SpaceLink Bulletin Board System in 
   Huntsville, Alabama, (205) 895-0028, available twenty four hours per day, 
   300 to 9600 baud. NASA SpaceLink, located at the NASA Marshall Space Flight 
   Center, provides a wealth of information on NASA and its projects. 2-line 
   orbital elements for a Space Shuttle mission are usually available while 
   the mission is in progress. In addition to educational materials and 
   software (including my programs STSORBIT PLUS, STSORBIT and JPLCLOCK), 
   general information on NASA programs and plans, news releases, and graphics 
   images from prior spacecraft missions such as Voyager, SpaceLink also 
   devotes a complete section to current news and information on the Space 
   Shuttle. I particularly appreciate the STS Mission Press Kit, posted about 
   two weeks before each mission, which provides a great deal of information 
   on the upcoming mission, payload and crew as well as broadcast schedules on 
   NASA Select Television, Satellite F2-R, Transponder 13. Mission status 
   reports are generated daily during the course of a mission. I regularly 
   call SpaceLink and post files of interest on my own RPV ASTRONOMY BBS.
        No discussion of satellite tracking would be complete without thanks 
   to Major T. S. Kelso, USAF, who almost single handedly brought satellite 
   tracking within the reach of ordinary folks. TS's Celestial BBS has been 
   providing unclassified 2-line orbital elements, direct from US Space 
   Command (formerly NORAD, the North American Air Defense Command) at 
   Cheyenne Mountain, Colorado, since 1987 or so. The Celestial BBS may be 
   reached at (513) 427-0674 and is located near Dayton, Ohio.

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 4


        Special thanks to Paul Traufler for his friendship and encouragement 
   over the past several years. Our regular telephone conversations have 
   generated many a new idea and the synergism has been beneficial to us both. 
   Our two programs, STSORBIT and TRAKSAT, have engaged us in a friendly 
   rivalry which has, I think, improved both programs many fold. I may have 
   provided the initial spur to Paul to write TRAKSAT (in order to improve on 
   my "sloppy orbital math", as Paul described it) but TRAKSAT has in turn 
   kept my nose to the grindstone and is recognized by many as the standard 
   against which other satellite tracking programs are judged. The emphasis of 
   the two programs is slightly different, with STSORBIT concentrating on the 
   graphical display and TRAKSAT on high precision analytical and predictive 
   techniques. I strongly recommend TRAKSAT for the serious satellite tracker. 
   My thanks as well for Paul's help in upgrading STSORBIT to use the 
   NASA/NORAD 2-Line Elements.
        Thanks also to Rob Matson for offering comments and code to help me 
   implement some of STSPLUS's more exotic features. Rob coind the phrase 
   "isocontours" to describe the circle of equal satellite altitude around a 
   location. Rob's fine program, SKYMAP, generates high accuracy printed star 
   maps with or without satellite tracks.
        Finally, my thanks to all those individuals who have taken the time to 
   write or leave a message on my BBS with comments and suggestions. While I 
   haven't implemented every suggestion, many are now included and the 
   feedback is most welcome.
        For current orbital information (if a mission is in progress), current 
   NASA/NORAD 2-line element sets, and the most recent versions of STSORBIT, 
   STSPLUS, TRAKSAT, and SKYMAP, call my RPV ASTRONOMY BBS at (310) 541-7299. 
   If the BBS has not answered after the third ring, hang up, wait TWO 
   MINUTES, then call back; the system has a power controller and if the 
   system is off it takes that long for the computer to start up and do its 
   housekeeping chores. The system has well over 1,000 regular users and is 
   often busy, so please be patient.
        If you do not have access to a modem, you may send US$10.00 as a 
   donation to cover materials, postage and handling for a copy of the current
   version of STSORBIT PLUS; please specify 5-1/4" 360K or 3-1/2" 720K disks. 
   Please allow two to three weeks for shipment.

                                      David H. Ransom, Jr.
                                      7130 Avenida Altisima
                                      Rancho Palos Verdes, CA 90274

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 5


   HARDWARE AND SOFTWARE REQUIREMENTS
   ----------------------------------

        An AT-class computer equipped with a 286 processor (running at 8 MHz) 
   and a 287 math coprocessor chip is the minimum system used for all program 
   testing and development. While other systems may give acceptable 
   performance, this minimum configuration assures that all features will 
   execute as described and in real time. Performance with 386/387 and 486 
   systems will be considerably superior to 286 systems. Note that NO TESTING 
   is performed on systems not equipped with a math coprocessor chip. The 
   following minimum hardware is recommended:

             286/386/486 IBM-compatible computer
             287/387 math coprocessor chip
             VGA color display
             Hard disk
             RAM disk with at least 500K space

        The 287/387 math coprocessor chip is HIGHLY RECOMMENDED and is 
   required for some processors to operate in real time. The calculations 
   relating to orbital mechanics are very complex and STSPLUS will use the 
   coprocessor chip if one is equipped; performance is improved by about an 
   order of magnitude. Other "fast" processor and coprocessor combinations may 
   yield acceptable performance. A SLOW MODE is provided to accommodate slower
   machines. However, math coprocessor chips are now reasonably inexpensive, 
   particularly for 286 systems, and the performance improvement is impressive 
   and well worth the modest cost. As an example, my vintage Zenith laptop is 
   equipped with an 80C88 processor and an 8087 math coprocessor and is just 
   able to keep up in real time when running at a clock speed of 8 MHz 
   (although map drawing times are very slow). However, an 8 MHz 286 (AT-
   class) computer without a math coprocessor is NOT able to execute the 
   program correctly except in the SLOW mode and map drawing times are 
   painfully slow.
        STSPLUS is intended to be used with an EGA or VGA video adapter and a 
   color monitor; with these adapters, the display is in color. Because of its 
   improved vertical resolution, the VGA is recommended over the EGA. A 
   monochrome VGA display with shades of gray may also be used with the 
   program (with the "/M" command line option). Because of hardware 
   limitations, CGA and HGC systems can only present graphics in monochrome; 
   although those display adapters are supported in current versions of 
   STSPLUS, that support may NOT continue in future versions. The original 
   STSORBIT will continue to support CGA and HGC monitors.
        A hard disk is recommended for performance in program and file loading 
   and for storage of orbital elements files. A RAM disk with sufficient space 
   to hold the program and its various data files is also recommended for 
   improved performace, especially for reduced map drawing times. However, the 
   program will execute correctly on floppy disk based systems with 640K base
   memory provided the system is otherwise equipped as suggested.
        Although the program may execute properly on other software operating 
   systems, STSPLUS has been designed and tested using standard configurations 
   of Microsoft DOS 3.3 and 5.0. No optional Terminate and Stay Resident 
   programs (TSR's) or "shell" programs have been tested. Third party memory 
   management programs and Digital Research DRDOS 6.0 may experienc problems 
   with internal memory allocation performed by the Microsoft BASIC Compiler; 
   however, I'm told that the latest release of DRDOS 6.0 works correctly.

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 6


   PROGRAM DESCRIPTION
   -------------------

        A typical Space Shuttle orbit is nearly, but almost never exactly, 
   circular with an altitude of approximately 160 nautical miles to a maximum 
   of approximately 300 nautical miles and an inclination of about 28 degrees 
   through about 57 degrees. Occasional missions, especially military 
   missions, fly at higher altitudes and/or inclinations and often use more 
   elliptical orbits. Little of this information is known to very good 
   accuracy by the casual listener.
        Initially, therefore, the interested would-be mission observer may 
   have only the time and date of launch to initialize a tracking program. 
   Given the geographical coordinates of the Kennedy Space Center, assuming a 
   circular orbit, and using the typical altitude and inclination of a Space 
   Shuttle orbit, the data should be sufficient to give at least a rough idea 
   of the Shuttle's position for the first several orbits. After that, 
   additional information is required if the position is going to be very 
   close.
        Fortunately, NASA does announce the orbital altitude (for non-military 
   missions at least) and this information is usually reported in the media. 
   The reader is cautioned that the popular press and television often (but 
   not always) convert the orbital altitude to statute miles with the 
   inevitable confusion resulting. If a television viewer has access to NASA 
   Select Television on Satcom F2R, Transponder 13, he will periodically see 
   Mission Control Center's huge wall map on which the current position of the 
   Space Shuttle is always displayed. Using this display, the careful viewer 
   can make a visual estimate of the longitude of the ascending or descending 
   node, the point at which the orbit crosses the Earth's equator in the 
   Northbound or Southbound direction respectively. Not exactly high-tech data 
   acquisition, but better than nothing at all!
        Given all of these uncertainties, I did not feel it necessary or 
   worthwhile to try to hone the mathematics of my "simple" orbital model in 
   program STSORBIT beyond that required to give an approximate position in 
   real time. Coincident with the Hubble Space Telescope mission I added the 
   J2 perturbation factor for improved accuracy. As an example, STSORBIT was 
   used to track STS-31, Discovery and the Hubble Space Telescope, and gave an 
   accurate position over more than 25 orbits.  
        Within a day of launch, the NASA/NORAD 2-line elements are usually 
   available and will yield a more accurate position over longer time periods 
   provided no orbital maneuvers are made. Using NASA/NORAD 2-line elements is 
   quite simple. No adjustment of orbital parameters is necessary when using 
   the 2-line elements. All that is required is to obtain the current 2-line 
   elements file (from my BBS or elsewhere), enter the name of the file (for 
   example, NASA877.TXT) and the name of the desired satellite (i.e. "HST" for 
   Hubble Space Telescope or "STS" for the Space Shuttle). STSPLUS takes care 
   of all the rest. The 2-line element set available at the time of this 
   release of STSPLUS is included in the program files. The data for each 
   satellite included in the 2-line element set is referenced to a specific 
   date and time, the "Epoch" of the data. As a general rule, orbital 
   calculations will be relatively accurate for 10 to 20 days after the Epoch 
   date; the lower the orbit, the greater the effect of factors such as 
   atmospheric drag and the less accurate the calculations will be as time 
   passes. Users who prepare their own 2-line element files are cautioned to 
   make certain no extraneous lines are included, that the satellite name is 
   on a single line, and that the two data lines exactly conform to the 69-

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 7


   character/line NASA/NORAD format.
        STSPLUS displays a portion of the Earth using a cylindrical 
   projection of the surface area. For the full world map, this extends almost 
   from one pole to the other; a small area near each pole (approximately five
   degrees) is omitted to maintain optimum map proportions. The map shows most 
   of the Earth's land boundaries, and continental areas and major seas and 
   oceans are easily recognizable. Twelve quadrant maps display one quarter of 
   the Earth, and zoom maps may be selected which display a field of view 
   adjustable from 180 degrees to 45 degrees. With the quadrant and zoom maps, 
   automatic map generation may be enabled to endure that the satellite is 
   displayed. The display shows the selected satellite as a small symbol or 
   icon, the projected low-Earth orbit ground track for approximately the next 
   two orbits (three hours), and the ground track for the past orbit (one and 
   a half hours).
         The program may be operated in real time, in simulated time, or in 
   "fast time", which is ten or sixty times normal time. For the "simple 
   orbital model", the orbital parameters may be manually entered or adjusted 
   for the desired mission. A pre-programmed demonstration may be run to 
   permit the user to become familiar with the program and its display. The 
   lower section of the screen displays current data about the mission in 
   progress.

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 8


   STSORBIT PLUS FILES
   -------------------

        STSORBIT PLUS is normally distributed via bulletin board systems in 
   archived form using the ZIP format by PKWare. Note that all files for 
   STSORBIT PLUS are called "STSPLUS" in order to conform to DOS filename 
   requirements and to avoid confusion with the similarly named files for the 
   original STSORBIT. The following files are usually included:

             STSPLUS.EXE        Main program             (required)
             STSPLUS.DOC        Documentation            (not required)
             STSPLUS.ICO        Icon for WINDOWS 3       (optional)
             STSPLUS.KEY        STSPLUS Active Keys      (optional)
             STSPLUS.MVF        World map data           (required)
             STSPLUS.TRK        NASA Tracking Stations   (optional)
             STSPLUS.CTY        City coordinates         (optional)
             STSPLUS.INI        Initialization data      (optional)

             MSHERC.COM         Hercules driver          (required for HGC)

             NASAnnn.TXT        2-Line Elements          (optional)

             NASA.TRK           NASA Tracking Stations   (not required)
             USSR.TRK           Soviet Tracking Stations (not required)
             INTELSAT.TRK       INTELSAT Tracking Stns   (not required)
             SPACENTR.TRK       Other Tracking Stations  (not required)

             README             STSPLUS Confidential Questionnaire
             QUICK.DOC          Quick Start Instructions

             MAK2LINE.EXE       MAK2LINE Utility Program (optional)
             MAK2LINE.DOC       MAK2LINE Documentation   (optional)

   Files noted as "(required)" must be in the current default directory for 
   program operation. Files noted as "(optional)" do not need to be in the 
   default directory when STSPLUS is operated but provide additional features 
   or information if present. In order to minimize the disk space required, 
   all .EXE files have been compressed with PKWare's PKLITE Professional. 
   These files require a brief additional time to begin execution since they 
   are decompressed "on the fly" at load time.
        Program MAK2LINE was written at the request of local amateur radio 
   enthusiasts to facilitate converting Keplerian orbital elements, received 
   by ham broadcast or via voice link, to the 2-line format. It is available 
   separately from my bulletin board system and is included with program 
   registration (see file README).

                             ***  IMPORTANT NOTE ***

        File STSPLUS.INI contains initialization data from previous runs of 
        the program. If file STSPLUS.INI is not present it will be created. 
        Note that if STSPLUS.INI was written by a prior version of STSPLUS, 
        all data will be ignored and the program must be initialized as if 
        being run for the first time.



   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 9


        File STSPLUS.KEY is a quick reference list of the keys that are 
   active while the map is displayed and includes a brief description of the 
   function of each key. It has been extracted from this documentation.
        File NASAnnn.TXT (where "nnn" will be a number such as "014") is a set 
   of NASA/NORAD 2-line elements as of the date of the file. Note that the 
   2-line elements should only be used for ten to twenty days after the epoch 
   date for each satellite if reasonable accuracy is to be maintained. Current 
   orbital elements are posted on my bulletin board system two or three times 
   per week. Other files with 2-line elements are also available; they 
   typically have names like GSFCnnn.TXT or N2L-nnn.TXT for general 
   satellites, and STSmmNnn.TXT for Space Shuttle missions. Space Shuttle 
   orbital elements are usually posted at least daily during missions; because 
   of orbital maneuvers, Space Shuttle elements more than 24 hours old may 
   yield inaccurate positions.
        Files with filetype .TRK are tracking station locations or other 
   locations of interest which may be plotted on the map. These files may be 
   created or edited with a standard ASCII editor. File NASA.TRK is the same 
   as file STSPLUS.TRK; if you wish to use a different TRK file, use Function 
   Key F7 from the Main Menu to select the desired file.
        Other files, such as 2-line elements for an upcoming Space Shuttle 
   mission or a mission in progress, may be included from time to time. Files 
   with filetype .TXT are normally 2-line orbital elements. Some common 
   satellite name abbreviations are: "STS" = Space Shuttle; "HST" = Hubble 
   Space Telescope; "GRO" = Gamma Ray Observatory; and, "MIR" = Soviet MIR 
   Space Station. 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 10


   PROGRAM SETUP AND USAGE NOTES
   -----------------------------

        The following notes may prove helpful in setting up STSPLUS to operate 
   most efficiently on your system or to provide hints in ways that some of 
   the program features may be used to advantage.

   Slow Computers and 80x87 Math Coprocessor Chips
   -----------------------------------------------

        STSPLUS has been designed for 80286/80287 or better computers eqipped 
   with an EGA or VGA color display. While the program can be executed on 
   older 8088 (XT-class) computers equipped with the 8087 math coprocessor or 
   on 286 or better computers without a math coprocessor, performance is 
   seriously degraded. But it would seem that warnings and suggestions can 
   NEVER convince people that the calculations required for orbital mechanics 
   are very complex and tax even a powerful computer. The best mainframe 
   computers we had a decade or more ago had trouble doing what I now take for 
   granted on a personal computer!
        Not all personal computers are created equal. Further, the 80x87 math 
   coprocessor chip can do many of the calculations ten or twenty times faster 
   than the main processor. For 8088 (XT-class) and 80286 (AT-class) 
   computers, this makes a tremendous difference AND for a very modest cost, 
   often well under $100. I really don't want to hear from users how slow this 
   program can be on older machines; I recommend the original STSORBIT if you 
   want the best performance from an 8088 computer. The following table 
   illustrates the difference the processor and a math coprocessor chip make.

        Processor   Speed   Coprocessor   Time (secs)
        ---------------------------------------------
        486         33 MHz      YES               6.2
        386DX       20 MHz      YES              12.8
        386SX       20 MHZ      YES              16.8
        386SX       20 MHz       NO              66.0
        286          8 MHz      YES              30.0
        286         12 MHz       NO              86.6
        8088         8 MHz      YES              65.0
        8088         8 MHz       NO             426.4

   The tests were performed with STSPLUS by measuring the time required from 
   the Main Menu until the satellite appeared on the display. All data were 
   resident in memory (no disk operations required). All tests were made using 
   the same display options (most were enabled and the SLOW MODE was OFF). 
   Slightly better performance can be achieved from the slower computers if 
   some options, such as Sun terminator, are disabled. Clearly, the 8088 
   without the math coprocessor chip is not really acceptable, and NONE of the 
   computers without the math coprocessor chip can operate in real time unless 
   the SLOW MODE is ON.
        If, in spite of these data and hints, you insist on using STSPLUS on 
   your old clunker, here are a few cautions and reminders.

   1.   Especially at startup and when redrawing the maps, long time delays 
        can be expected -- on the order of minutes in some cases. Status 
        messages are presented on the screen during some of these delays so 
        users will at least know the program is working. Note also that the 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 11


        .EXE file is compressed to save disk space and is decompressed at load 
        time; this may cause a delay on any system, with or without a math 
        coprocessor.

   2.   The original CGA display, even when equipped with a color monitor, can 
        display reasonable resolution graphics (320x640) ONLY in monochrome. 
        Your color CGA monitor buys you nothing for graphics that are quite 
        inferior to the EGA and VGA. If you have a monochrome monitor, be sure 
        to include the "/M" command line option to force monochrome. The 
        program may otherwise fail with or without an error message.

   3.   If you don't have a math coprocessor or are using a slow computer, be 
        SURE to enable the SLOW MODE using Function Keys F10+F7. Even a 286 or 
        386 computer may be unable to keep up with the calculations in the 
        normal mode. The clue is to watch the LOCAL and SIMULATION times at 
        the lower left of the screen; if these times are not within one or two 
        seconds of each other, you must use the SLOW MODE. The SLOW MODE 
        changes the screen update interval to once every 10 seconds from once 
        every second to allow more time for calculations.

   4.   Even with the SLOW MODE, you may not be able to turn on all the 
        options and features you'd like to use and still keep up. Some 
        features, such as the solar terminator, may have to be disabled. Too 
        bad, but only a math coprocessor chip can solve that problem for 286 
        computers and there is no solution for 8088 computers running at the 
        original 4.77 MHz. Experiment with your computer to see what features 
        permit proper operation.

   Using a RAM Disk
   ----------------

        Because of program memory requirements, a RAM disk should be used only 
   if your computer is equipped with expanded or extended memory. Using a RAM 
   disk in conventional memory (the memory up to 640K) will probably use 
   memory that STSPLUS (as well as most other programs) may need to operate 
   correctly. The basic files required for operation of STSPLUS require a 
   minimum of about 256K of RAM disk; additional map or satellite data files 
   could as much as double that amount. A RAM disk of at least 500K is 
   therefore recommended. The actual size RAM disk you can provide will be 
   dependent upon how much memory is equipped in your computer.
        In order to use the RAM disk effectively, all essential files must be 
   copied from your hard disk to the RAM disk. The following program files are 
   recommended:

             STSPLUS.EXE    STSPLUS Main Program file
             STSPLUS.INI    STSPLUS Initialization file
             STSPLUS.MVF    STSPLUS Map file
             STSPLUS.CTY    STSPLUS City file               (optional)
             STSPLUS.TRK    STSPLUS Tracking Station file   (optional)

   In addition, you must copy all 2-line orbital elements files you plan to 
   use, files such as NASAnnn.TXT, GSFCnnn.TXT, and so forth. Remember that 
   all RAM disk files are lost when you turn off your computer! I recommend 
   that you build a batch file which copies all of the files from the hard 
   disk to the RAM disk and, when you are finished with STSPLUS, copies the 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 12


   file STSPLUS.INI back to your hard disk. Saving STSPLUS.INI on the hard 
   disk ensures that the next time you run STSPLUS, the previous settings will 
   be restored.
        The following is a sample batch file which will copy the STSPLUS files 
   from the hard disk (drive F: and subdirectory STSPLUS in this example) to 
   the RAM disk (drive J: in this example), run program STSPLUS with the /R 
   (resume) option, then copy the STSPLUS.INI file back to the original drive 
   on the hard disk. Many variations are possible to suit individual needs.

             J:
             COPY F:\STSPLUS\STSPLUS.EXE
             COPY F:\STSPLUS\STSPLUS.INI
             COPY F:\STSPLUS\STSPLUS.MVF
             COPY F:\STSPLUS\STSPLUS.CTY
             COPY F:\STSPLUS\STSPLUS.TRK
             COPY F:\STSPLUS\NASA*.TXT
             COPY F:\STSPLUS\GSFC*.TXT
             COPY F:\STSPLUS\STS*.TXT
             STSPLUS /R
             COPY STSPLUS.INI F:\STSPLUS

   Starting Program STSORBIT PLUS
   ------------------------------

        Versions of STSPLUS prior to 9219 attempted to read the file 
   STSPLUS.INI even if it had been created by a prior version. Since the 
   format of that file changes from time to time, STSPLUS now ignores the 
   STSPLUS.INI file unless it was created or written by the current version. 
   If the file does not exist, STSPLUS will automatically create it.
        To start program STSPLUS, enter one of the following commands:

             STSPLUS            Automatic monitor, CGA/HGC/EGA/VGA

             STSPLUS /EGA       Force EGA (or lower) monitor

             STSPLUS /CLK       Use 43 or 60 lines for graphics display of
                                data and large clock characters. NOTE: This
                                feature available with EGA and VGA displays
                                ONLY! It is ignored for CGA/HGC monitors.

             STSPLUS /CGA       Force CGA monitor

             STSPLUS /M         Force monochrome operation, EGA/VGA

             STSPLUS /R         Resume last mission automatically

        Only one display option (/EGA or /CGA or /M) may be used. Options may 
   be combined and entered in any order. For example, using the following 
   command will resume the prior mission and force EGA mode:

             STSPLUS /R/EGA



   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 13


                                    * * * * *

                       Hercules Graphics Card USERS NOTE:
                       ----------------------------------
                              
        Run the program MSHERC prior to running STSPLUS. This Microsoft 
   program works with compiled BASIC programs to enable use of the Hercules 
   Graphics Card. One user reported that setting the HGC to FULL and selecting 
   Page Zero (using software supplied with the HGC) was sufficient for proper 
   operation with program STSPLUS. At least one HGC "clone" user reported 
   improper operation.

                                    * * * * *


        If you have already run STSPLUS (or if you have file STSPLUS.INI) 
   and simply wish to resume that same mission, use the /R (resume) command 
   line option:

             STSPLUS /R

   STSPLUS will sense the monitor type, enable color for EGA and VGA systems, 
   read the map data as usual, then proceed directly to plotting the mission. 
   The data from the last run, as saved in file STSPLUS.INI, is used to 
   initialize the program. If 2-line elements were used, that file must also 
   be present. Once started in this manner, pressing the ENTER key after 
   plotting has started will return to the Main Menu.


   Predicting Visible Satellite Passes
   -----------------------------------

        One of the best uses for a satellite tracking program is to show when 
   a satellite of interest will be visible from a specified location. Using 
   STSPLUS, my wife and I have spotted three different Space Shuttle missions, 
   the Hubble Space Telescope, the Russian MIR Space Station, and many others 
   with the naked eye. The trick, of course, is knowing when and where to look 
   for the satellite.
        There are a number of satellite tracking programs, most notably Paul 
   Traufler's TRAKSAT, which can generate a tabular output for a given 
   satellite or group of satellites telling when and where the satellite will 
   be visible. STSPLUS does not have those tabular capabilities and relies 
   instead on its graphics capabilities to make pass predictions quick and 
   easy. Here are a series of suggestions to help you check for visible passes 
   for a satellite of interest.

   1.   Set up STSPLUS for the desired satellite. First, use Function Keys 
        F10+F3+F5 to set the satellite ground track to LINE or BOTH (rather 
        than DOTS). This makes the ground track more visible on the zoom map 
        displays. Then use Function Key F2 to select the satellite's 2-line 
        orbital elements from the available satellites. Typical files have 
        names like NASA971.TXT or GSFC037.TXT or, for the space shuttle, 
        STS45N03.TXT. The numbers will change from time to time or mission to 
        mission. Use one of the quadrant maps or the world map to make sure 
        that the satellite is correctly displayed.

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 14



   2.   Remember that under most circumstances a "visible pass" means that the 
        satellite is in full sunlight and the viewer is in darkness. Although 
        there are exceptions in unusual situations, this restricts the times 
        for visible passes to the several hours prior to dawn and the several 
        hours after sunset. (Note, however, that "visible" to a ham radio 
        operator simply means above his horizon!) In most cases, the Space 
        Shuttle and satellites such as MIR Space Station and Hubble Space 
        Telescope are visible with the naked eye given favorable lighting 
        conditions. Satellites in higher altitude orbits will be visible 
        sooner before dawn and longer after sunset. Satellites in very high 
        orbits, no matter how large the satellite, are seldom visible without 
        high power binoculars or a telescope.

   3.   The geometry of the pass and the attitude and geometry of the 
        spacecraft is also important. The relative angles between the Sun, the 
        satellite, and the viewer determine how light is reflected from 
        the surfaces of the spacecraft to you, the viewer. A spacecraft 
        passing between you and the Sun may not reflect much light to you and 
        may therefore not be visible even at higher altitudes. On the other 
        hand, a spacecraft nearer the horizon but on the other side of you 
        from the Sun may appear brilliantly lighted. The kinds of surfaces on 
        the spacecraft are important too; large solar panels can reflect 
        enough light to appear the most brilliant objects in the sky while 
        large but rounded spacecraft seem all but invisible.

   4.   Given otherwise good conditions and favorable weather, the single most 
        important factor is spacecraft apparent altitude during a pass. This 
        is the spacecraft's apparent elevation above your local horizion. 
        Depending upon local conditions, an altitude of at least 5 degrees 
        will generally be necessary before a spacecraft can be seen even under 
        the best lighting conditions. In the Los Angeles area, at least 20 or 
        30 degrees is a better number to use because of smog and haze (except 
        when looking out over the Pacific Ocean).

   5.   After altitude, the azimuth is the number which describes the 
        direction from the viewer to the spacecraft at any moment. This is 
        given in the sense NESW, North to East to South to West, in degrees. 
        For a good pass after sunset, for example, an azimuth ranging from 60 
        to 150 degrees would indicate a pass moving generally from the 
        Northeast to the Southeast, ideal lighting conditions with the Sun in 
        the West.

   6.   Now to look for a visible pass using STSPLUS. Use Function Keys F8+F3 
        to select a local time shortly after sunset. For example, if sunset 
        will occur at 17:30, set the local time to 18:00 and select the date 
        desired to test. Now begin the display and press the "L" key to obtain 
        the Location Map display centered on your viewing location. (If you 
        have a second location set into STSPLUS, press "L" again to toggle 
        between the two locations.) Notice the concentric spacecraft altitude 
        isocontour rings spaced at 10 degree intervals and centered on your 
        location. The outermost ring is 0 degrees, the approximate point at 
        which the spacecraft will appear over your horizon. Press "PgUp" or 
        "PgDn" to select a different zoom factor for the map. The ground track 
        will be drawn against this map background. If you see no ground track, 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 15


        there will be no visible passes that evening (or dawn)! A good visible 
        pass will arc in toward your location and reach a peak altitude of 40 
        or more degrees, which should be easily visible even over most local 
        obstructions. Since as many as three sequential ground tracks may be 
        shown, be sure you know which one occurs at what time!

   7.   Once you have found a visible pass which looks promising, pause the 
        display with Function Key F6. This freezes the satellite on your 
        display while still generating the altitude ("Alt") and azimuth 
        ("Azm") values. Move the satellite back and forth along its ground 
        track with the "+" and "-" keys and adjust the time step (1, 10, or 60 
        seconds) with Function Key F4. Now you can position the satellite at 
        the point you expect it to become visible, reach its highest altitude, 
        and disappear from view and record the time, altitude, and azimuth for 
        each of these events. The spacecraft lighting is shown as an asterisk 
        ("*") next to the "Orbit #" if the satellite is in sunlight; for color 
        displays, the satellite icon is bright white in sunlight, yellow in 
        partial shadow, and dim white in full shadow (umbra). If the lighting 
        conditions are favorable and you are using reasonably current 2-line 
        orbital elements, this method is just about foolproof.


   Known STSPLUS Problems and Bugs
   -------------------------------

        STSPLUS is being used on thousands of computers around the world 
   without any significant problems. However, like almost any computer program 
   and in spite of my best efforts to minimize such bugs, there are several 
   known problems or "bugs" with STSPLUS. Some are the result of slow 
   computers, others are in the program itself. Hopefully, some or all of 
   these problems, those I can reproduce at least, will be repaired in due 
   course. Some problems are caused by other software interfering with the 
   program's operation. Still other problems are the result of incompatible 
   "IBM-compatible" computers for which there is no remedy.
        One "problem" which I frequently hear about is that the user's CGA 
   color monitor only displays STSPLUS in monochrome. THIS IS NOT A BUG! CGA 
   systems display "high resolution" 640 x 200 graphics in monochrome ONLY. 
   Compared to the EGA or VGA, that resolution is barely acceptable. The color 
   graphics modes for the CGA are 320 x 200 which is inadequate for STSPLUS.

   1.   As quite a few users have reported, the FAST modes did NOT operate 
        correctly with automatic map generation enabled. Beginning with 
        Version 9226, enabling FAST modes (X10 and X60), will automatically 
        disable automatic map generation. Press TAB to restore automatic map 
        generation.

        I use the FAST modes successfully in conjunction with the PAUSE to 
        move a satellite back and forth on the Location Map (while the map is 
        displayed select PAUSE with F6, then set the desired time increment 
        using F4, and then use the "+"/"=" and "-" keys to move the satellite) 
        to determine the altitude and azimuth of a pass. Once the PAUSE is 
        released, the time will return to normal. Another alternative is to 
        determine the approximate time of interest and then use simulated time 
        (F8+F3 on the Main Menu) to display that time. Depending upon the 
        speed of your computer, it's pretty simple to select another time if 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 16


        you guess wrong. Return the program to real time with F8+F1 from the 
        Main Menu.

   2.   Several users have reported occasional "BASIC Error 11" problems; 
        BASIC reports this error as "Division by Zero". The only way I have 
        been able to reproduce this error is to restart the program using the 
        command line "STSPLUS /R" after I have deleted the 2-line file used on 
        the prior run; to avoid this error, do not use the "/R" command line 
        option and select a new 2-line file using F2. This error may also be 
        the result of a memory limitation (with multitasking enabled?) or it 
        may be a BIOS problem associated with a specific computer. 

   3.   STSORBIT PLUS has been run extensively on systems using Microsoft DOS 
        3.3 and 5.0 and there are no known problems with those operating 
        systems. Because of the many bugs reported, I do NOT recommend use 
        of DOS 4.xx under any circumstances; upgrade ASAP to DOS 5.0! Users 
        report memory allocation problems with some versions of Digital 
        Research DRDOS 6.0 and certain third party memory allocation programs. 
        A typical symptom of this kind of problem is that you cannot return to 
        DOS without either an error message or the computer freezing.

   4.   Some users report problems with certain Terminate and Stay Resident 
        (TSR) programs for which the only remedy is to remove the offending 
        TSR. This usually requires a "trial and error" approach to pinpoint 
        the TSR causing the problem. The best method is to remove ALL such 
        programs from your AUTOEXEC.BAT file, including the DOS 5 "DOSSHELL", 
        to make sure the program will work with your computer. Similarly, 
        delete all special memory and device drivers from your CONFIG.SYS 
        file. One user reports a problem on an IBM PS/2 when his mouse is 
        active (but I regularly execute STSPLUS on different computers with my 
        mouse active!).

   5.   All VGA adapter cards are not equal, in case any of you had some 
        illusions left. In at least one case, the aspect ratio of the display 
        is incorrect when the display is operated in the EGA mode! The 
        vertical scale is compressed by about 20% as compared to either a true 
        EGA display or other (correct) VGA displays. So far as I know, there 
        is no remedy. Early VGA cards (the 449 card from Zenith is an example) 
        are not always recognized as VGA; the card is not register compatible 
        with the IBM standard and is recognized as EGA instead.

   6.   There appears to be a subtle problem when changing to or from Daylight 
        Savings Time (which recently happened and "announced" the bug). The 
        display appears to get caught in a loop, endlessly redrawing the 
        screen. To avoid the problem, change the Daylight Flag then EXIT THE 
        PROGRAM AND RESTART.

   7.   Not all computers (especially older CGA systems) will display the 
        extended graphics characters used for the large clock characters. The 
        symptom of this problem is that the lower left portion of the data 
        block is mostly blank after pressing F2. If you have this problem and 
        your computer is running DOS 3.x or DOS 5.0, enter the command 
        "GRAFTABL" at the DOS prompt before running STSPLUS or include the 
        line "GRAFTABL" in your AUTOEXEC.BAT file; this sets the "code page" 
        to enable the computer to display the extended graphics characters. 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 17


        [The program GRAFTABL.COM is included as part of DOS in most cases.]

   8.   Finally, as noted elsewhere, all computers are NOT equal. There are 
        some computers which will not execute these programs under any 
        circumstances. Tandy is the most common offender followed by Leading 
        Edge. Some models from these manufacturers have BIOS problems or 
        errors which prevent programs compiled with the Microsoft PDS BASIC 
        compiler from operating (sometimes only in graphics modes). There is 
        no remedy. Other computers, Ergo for example, exhibit "strange" 
        behavior in some graphics and text modes. There is sometimes a 
        workaround for these problems; check with the manufacturer.

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 18


   PROGRAM OPERATION
   -----------------

        The program automatically checks for the presence of a VGA or EGA and 
   will execute in color if one is found UNLESS the /M command line option is 
   used to force monochrome operation. However, if you wish to operate STSPLUS 
   in the EGA mode when you have a VGA monitor, use the /EGA option. In cases 
   where a monochrome monitor is connected to an adapter which simulates color 
   with gray scale, the /M command line option may be omitted but the various 
   portions of the display may or may not be visible. STSPLUS depends upon the 
   Microsoft BASIC Compiler to determine whether or not a particular monitor 
   type is available. Some video adapter boards which claim to be VGA are not 
   recognized as such by BASIC and therefore cannot be used in the higher 
   resolution VGA display mode. Similarly, "clone" Hercules Graphics Cards do 
   not always perform correctly.
        The /M option is not required for HGC and CGA graphics operation, 
   since those adapters always render their "high resolution" graphics in 
   monochrome. Although color CGA systems do have a 3-color mode, the limited 
   number of colors and coarse resolution of 320x200 is not suitable for 
   STSPLUS. Naturally, the appearance of the program is enhanced by the use of 
   color. The vertical resolution is also adjusted depending upon the type of 
   adapter which has been detected. Once STSPLUS has started, the display type 
   may not be changed without halting the program at the Main Menu with the 
   ESC key, then restarting the program with the desired command line options.
        The program checks for the presence of a math coprocessor and will use 
   it if found. Since the calculations required to determine orbital data are 
   very complex, the use of a math coprocessor will improve the speed of 
   operation by a very substantial amount. Use the SLOW option on the Set 
   Program Options Menu (F10+F7) if the program has difficulty operating on 
   your system.
        STSPLUS selects the icon or symbol used to graphically represent the 
   satellite based upon the mission name. Names which start with the letters 
   "STS" will use the space shuttle icon and all other missions will use an 
   icon resembling the Hubble Space Telescope.
        STSPLUS first reads in the map coordinates from file STSPLUS.MPT, 
   which must be in the current drive and directory. These coordinates are 
   converted to screen coordinates for the type of monitor detected and stored 
   internally so that they need only be read once. After map coordinates have 
   been loaded, the initial title screen is shown on the display.
        The title screen is displayed for 15 seconds for normal program 
   operation or for 3 seconds if the /R command line option has been used. The 
   Main Menu, described in the following section is then displayed. Press any 
   key to proceed to the Main Menu immediately.


   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 19



                                Program STSORBIT PLUS

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9228



                      Current time:  16:34:24 PDT   23:34:24 UTC
                      Current date:    04/08/1992     04/08/1992


                        Last Mission = STS-45 [STS45J13]






                     (C) Copyright David H. Ransom, Jr., 1989-1992
                                 All rights reserved.


   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 20


   THE STSORBIT PLUS GROUND TRACK DISPLAY
   --------------------------------------

        The principal objective of STSPLUS is to graphically display the 
   position of the space shuttle or satellite relative to a map of the world 
   or some relevant portion of the world. Six different map displays are 
   available: World, Quadrant, Zoom, Location, Tracking Station, and Satellite 
   Motion. Each is discussed below.
        In addition to the map itself, a number of other items of interest are 
   displayed. Some features are available only with higher resolution displays 
   (EGA and VGA) in order to avoid cluttering the display screen. Other 
   features may be enabled or disabled according to the user's preference. The 
   sections which follow the map types discuss these various features.


   World Maps
   ----------

        The STSPLUS ground track display defaults to a map of the world 
   centered on the Prime Meridian (0 degrees) and extending from approximately 
   +85 degrees North latitude to -85 degrees South latitude using a linear 
   cylindrical projection. Omitting the two 5 degree bands at the poles 
   permits better detail in the mid latitudes where all space shuttle orbits 
   and many other satellite orbits are concentrated. Ground track details very 
   near the poles are therefore sacrificed for a better display in the main 
   portion of typical orbits. The vertical resolution of the display is 
   automatically adjusted for the type of display system in use from 200 lines 
   (CGA) to 480 lines (VGA). Two World Maps are available: one centered on the 
   Prime Meridian at Greenwich, England (0 degrees longitude); and, one 
   centered on the International Date Line (180 degrees longitude).
        All screen maps drawn by STSPLUS use a vector database derived from 
   the Micro World Database II. The full map of the world as used here 
   includes approximately 30,000 vector pair coordinates describing the 
   world's coastlines, islands, and major rivers. (The rivers are not 
   displayed on the world maps to avoid "cluttering" the display.)
        Pressing the "W" or "0" key will switch the display to the World map. 
   If automatic map generation is enabled, STSPLUS will select the map which 
   most nearly centers the satellite on the map. If automatic map generation 
   is disabled, pressing "W" or "0" will toggle between the two maps. When 
   automatic map generation is enabled, the letter "A" appears in the upper 
   right of the screen.


   Quadrant Maps
   -------------

        The original STSORBIT program used a digitized pixel map of the world 
   derived from an EGA display. As a consequence of the EGA source, boundaries 
   were sometimes discontinuous on VGA displays and the display on a CGA was 
   sometimes difficult to read. STSPLUS uses a vector map drawing method which 
   automatically adjusts to the display type and the scale of the map. A full 
   world map is available which is quite similar in appearance to the original 
   display. I happen to think it is a big improvement, but that's a matter of 
   personal opinion.
        However, some geographic details are still difficult to distinguish, 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 21


   even on a VGA display. STSPLUS includes twelve quadrant maps, each overing 
   1/4 of the Earth's surface. These are numbered 1 to 12 and are centered on 
   the world map roughly according to the following illustrations:
                      0                                180             
        +---------------------------+     +---------------------------+
        |             |             |     |             |             |
        |    1        4        7    |     |    7        10       1    |
        |             |             |     |             |             |
        |             |             |     |             |             |
        |             |             |     |             |             |
        |    2        5        8    |     |    8        11       2    |
        |             |             |     |             |             |
        |             |             |     |             |             |
        |             |             |     |             |             |
        |    3        6        9    |     |    9        12       3    |
        |             |             |     |             |             |
        +---------------------------+     +---------------------------+


   The center vertical quadrants in the left illustration, 4 through 6, are 
   centered on the Prime Meridian at zero degrees longitude (Greenwich, 
   England). The center vertical quadrants in the right illustration, 10 
   through 12, are centered on the International Date Line at 180/-180 
   degrees. The center horizontal quadrants, 2, 5, 8, and 11, are centered on 
   the Equator.
        Each individual quadrant map may be selected by pressing the 
   corresponding number key, "1" through "9"; use keys "!", "@", and "#" to 
   select quadrants 10, 11, and 12 respectively. Pressing any of these keys 
   for individual quadrant maps will disable automatic map generation if it is 
   enabled (indicated by the letter "A" at the upper right of the screen). 
   Pressing "Q" will allow STSPLUS to select the quadrant most appropriate for 
   the satellite's current position.


   Zoom Maps
   ---------

        Although I was pleased with the enhanced maps using the Quadrant Mode, 
   the vector map file contains far more information than can be effectively 
   displayed in that mode. The next obvious step was to add the ZOOM feature, 
   maps which yielded greater detail and which spanned as little as 45 degrees 
   across the screen, six times better than the 180 degree quadrant maps. This 
   approaches the practical limit for the vector database. Because of the 
   smaller area covered, a different approach was used for map selection. 
   There would simply be too many different possibilities for manual selection 
   so a fully automatic Zoom Mode was implemented.
        Press the "Z" key to enable Zoom Mode. STSPLUS will use the current 
   position of the satellite to select the center of the map. The initial map 
   width is 75 degrees; use PgUp to widen the map width (up to 180 degrees) or 
   PgDn to narrow the map width (down to 45 degrees, roughly the limit for 
   acceptable maps given the vector data being used). The Home key will always 
   select 75 degrees width and the End key will return to the prior field of 
   view. The width of the map is shown at the upper left of the map display. 
   Press the TAB key to enable or disable automatic map generation (the map 
   will always be redrawn). When automatic map generation is enabled, the 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 22


   letter "A" appears in the upper right corner of the screen next to the map 
   width or field of view. Zoom field of view is limited to 45, 60, 75, 90, 
   120, and 180 degrees.
        During Mission STS-48, I found the Zoom Mode extremely effective in 
   helping me to distinguish various coastlines and rivers, even on my poor 
   old Zenith CGA/LCD laptop! The only problem with all of this is that I am 
   now approaching the limit of an 80C88 with 8087 math coprocessor (8 MHz at 
   that!) in terms of its ability to get the calculations done in the time 
   allowed.


   Location Maps with Isocontours
   ------------------------------

        By popular request, especially from the amateur radio community, I 
   have added the Location Map with Isocontours. (Isocontours is a description 
   coined by Rob Matson for his SkyMap program and for which he supplied 
   sample code.) Press the "L" key when the map display is present to select 
   this display. The map will be drawn with the current zoom factor and 
   centered on the user's location. The usual circle of visibility will be 
   drawn and within that "circle" are seven isocontours representing viewing 
   angles of 10 through 70 degrees in ten degree increments. The balance of 
   the Location Map includes the usual features.
        If you have entered a second location (using F10+F2 from the Main 
   Menu), pressing the "L" key when the Location Map is already displayed will 
   toggle between your primary location and the second location. The data 
   displayed at the lower right of the screen (Location, Altitude, Azimuth, 
   etc.) is calculated with respect to the indicated location. If no second 
   location has been entered, pressing the "L" key while the Location Map is 
   displayed will have no effect.
        The principal advantage of the Location Map is, of course, the 
   isocontours -- lines of equal viewing altitude (line of sight not taking 
   into account any refraction near the horizon) from the user's own location. 
   The user can immediately tell by inspection whether current or upcoming 
   passes will be "good" and what approximate maximum satellite viewing 
   altitude can be expected. Amateur radio buffs who need to know if a pass 
   will appear above some altitude threshold, say 20 degrees, now have that 
   information available visually.
        Since this map mode uses the ZOOM map algorithms, the usual zoom map 
   features (PgUp, PgDn, Home, End) are active.


   Tracking Station Maps with Isocontours
   --------------------------------------

        The Tracking Station Maps with Isocontours are similar to the Location 
   Maps except that they use the current TRACKING STATION file locations 
   rather than the user's location(s). This feature was implemented at the 
   request of folks working on the STS-49 Intelsat Reboost Mission. Pressing 
   the "T" key will select this map mode. STSPLUS calculates which of the 
   available tracking stations is nearest to the current satellite position 
   and centers that tracking station on the screen. This is calculated by 
   determining the angular difference between the sub-satellite point and each 
   tracking station. However, this means that depending upon the Zoom factor 
   in effect, the satellite may or may not be visible on the screen. For 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 23


   example, if the sub-satellite point is in South America and the only 
   tracking station in the Western Hemisphere is in the United States, the 
   satellite cannot be seen at narrower fields of view.
        The "tracking stations" may be any locations the user chooses and 
   included in the current TRACKING STATION file. Several different tracking 
   station files are included with the normal STSPLUS distribution as 
   described in the section "NASA Ground Tracking Stations" below. Use 
   Function Key F7 from the Main Menu to select the desired file.
        Since this map mode uses the ZOOM map algorithms, the usual zoom map 
   features (PgUp, PgDn, Home, End) are active.


   Big Clock Options
   -----------------

        STSPLUS defaults to a standard display with a text block shown on the 
   lower five lines of the display; three different times are shown at the 
   lower left of this display: Launch/Epoch date and time, UTC date and time, 
   and local date and time. Pressing Function Key F2 while the map is 
   displayed switches between this default mode and three Big Clock modes: UTC 
   date and time, local date and time, and MET/T+Epoch.
        For EGA and VGA users, an additional command line option, "/CLK", is 
   available which changes the number of lines per screen to 43 and 60 lines 
   respectively. The big clocks are then placed below the standard data 
   instead of overwriting the regular data area.


   Satellite Motion Maps
   ---------------------

        It is sometimes instructive and interesting to see the ground track 
   from the satellite point of view. The Satellite Motion Map, available 
   ONLY with EGA and VGA displays, centers the satellite in the display and 
   draws the ground map accordingly. Unlike all other map displays, this mode 
   takes advantage of the dual-page capability of the EGA display and the VGA 
   display (operating in the EGA mode); the current map is always displayed 
   and the new map is drawn "off screen" and updated every ten seconds (or as 
   frequently as the capability of the processor will permit). Users with slow 
   computers or computers without math coprocessors may prefer this display 
   because, once the map has been drawn the first time, a complete map is 
   always displayed. For VGA users, the vertical map resolution in this mode 
   is reduced from 400 lines to 280 lines.
        The Satellite Motion Map is enabled by pressing the "M" key when the 
   map is displayed. When switching to this map mode, the message "Switching 
   to EGA Dual-Page Mode ..." is displayed on the screen; all EGA and VGA 
   systems display the Satellite Motion Map in EGA resolution: 640 x 350 
   pixels. The complete map is then drawn off-screen and will require the 
   "usual" time during which the screen will be unchanged. (My 386 systems 
   update every 10 seconds but my 286 systems can only manage every 20 or 30 
   seconds -- and they all have math coprocessors!) As with other zoom modes, 
   the zoom magnification may be adjusted by pressing the Hone, End, PgUp, or 
   PgDn keys. Note that ONLY the "M", Home, End, PgUp, PgDn, and ENTER keys 
   are active while the Satellite Motion Map is displayed; press the "M" key 
   or ENTER to return to normal operation.


   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 24



   On-line Help
   ------------

        An on-line Help Screen is available during the ground track display to 
   remind the user of the available functions and which keys to press to 
   trigger those functions. When the ground track display is active, press 
   Function Key F1 to display the Help Screen in the lower portion of the 
   display:

    F1=Resume Data   F6=Pause (+,-)    TAB=Auto Maps On/Off  L=Location Maps
    F2=Sat Blink     F7=Circle of Vis    W=World Maps        T=Tracking Maps
    F3=Printer Log   F8=SUN and Term     Q=Quadrant Maps     M=Motion Map
    F4=Time Step     F9=Units (nm/km)    Z=Zoom Maps: Home,
    F5=MET/T+Epoch  F10=Sat Coordinates         PgUp,PgDn    STSPLUS Version 9228

        The ground track display will continue to be updated in real time 
   while the help screen is displayed. If only the graphical display of the 
   ground track is of interest, the help screen may be kept on the display 
   continuously. Press Function Key F1 again to return to the normal data 
   display in the lower portion of the screen. Note that the Help Screen is 
   disabled when the Motion Map is displayed.


   Satellite Position and Orbit Projections
   ----------------------------------------

        The focus of the display, and the reason for program STSORBIT, is to 
   show the position of the spacecraft or satellite. For the space shuttle 
   (and provided the mission name begins with the letters "STS"), a symbol has 
   been chosen which resembles that spacecraft. For all other satellites, a 
   symbol has been chosen which resembles the Hubble Space Telescope. In 
   either case, the symbol is shown in the following colors (EGA and VGA 
   displays only):

             Satellite is sunlit           Bright White
             Satellite is in penumbra      Yellow
             Satellite is in umbra         Dim White

   In addition, an asterisk ("*") is shown to the right of "Orbit #" when the 
   satellite is sunlit or in penumbra; this will assist users of monochrome 
   monitors where colors cannot be distinguished. For better visibility, the 
   satellite symbol will normally "blink" on CGA monitors; the symbol may be 
   made to blink on any system if desired by pressing Function Key F2 while 
   the ground track is displayed. Note however that for very slow computers, 
   the blink may appear erratic if most of the time is spent performing 
   calculations.
        Just seeing the spacecraft or satellite on the map display yields 
   information as to its present position. However, for satellite viewing and 
   planning purposes, STSPLUS calculates the predicted ground track for 
   approximately three hours in the future and the past ground track for 
   approximately one and a half hours in the past. The predicted ground track 
   is shown as a series of light green dots, and the past ground track is 
   shown as light red dots. These dots are plotted at one minute intervals and 
   "move" as the spacecraft or satellite changes position; one new dot is 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 25


   added to the predicted track each minute and one dot is removed from the 
   past track at the same time.
        The ground track may optionally be omitted, be shown as a light green 
   line, or be shown with both dots and line.


   User's Circle of Visibility
   ---------------------------

        Centered around the user's geographic location, and marked with a 
   small cross on EGA and VGA systems, is a magenta "circle" of the 
   approximate line of sight visibility for the mission in progress. The 
   "circle" appears on the display approximately as a circle near the Equator 
   and as a rounded triangle in higher latitudes. These strange shapes are 
   entirely an artifact of the map projection; if projected on the surface of 
   a sphere, they would be true circles. The radius of this circle of 
   visibility is calculated for each satellite based upon its altitude at the 
   instant the map is first drawn as well as the user's elevation above mean 
   sea level and corresponds to "line of sight" visibility for that satellite.
        When a satellite is within the circle, direct visual, radio or radar 
   communications with the satellite should be practical. Actual visibility, 
   of course, depends upon more than simply whether or not the satellite is 
   above the viewer's horizon. Most important is the sun to satellite to 
   viewer geometry; the satellite must be in sunlight and the viewer in 
   darkness for reasonable visibility. Almost as important is the size and 
   geometry of the satellite itself; a large, bright-metal satellite with huge 
   solar arrays reflects far more sunlight than a small dark satellite. In 
   addition to the satellites themselves, many booster rockets and other 
   "spare parts" are orbiting the Earth. Since they are not attitude 
   stabilized, booster rockets usually are tumbling and may therefore appear 
   to flash on and off as they pass over.
        For the Space Shuttle as well as most other satellites with near 
   circular orbits, the circle of visibility calculations are reasonably 
   accurate; however, the position of the sun and the effect of atmospheric 
   refraction are not taken into account, only whether or not the satellite is 
   in line of sight view from the observing location. For highly eliptical 
   orbits, however, the accuracy is substantially degraded since the radius of 
   the circle of visibility changes dramatically depending upon whether the 
   satellite is nearer apogee or perigee at the time the calculation is made, 
   and the period of the orbit. In the course of a single orbit, the altitude 
   of such a satellite may change by thousands of miles. Satellite "DE 1", 
   usually included in the NASAnnn.TXT 2-line elements file, is in a highly 
   elliptical orbit with long period and illustrates the problem.


   Spacecraft Circle of Visibility
   -------------------------------

        The spacecraft circle of visibility is calculated using the same 
   alrorithm as for the user's circle of visibility. Like the user's circle, 
   the spacecraft circle appears on the display as an ellipse because of the 
   scaling factors used by the map projection. The difference is that the 
   spacecraft circle moves with the spacecraft and illustrates the approximate 
   area visible from the spacecraft at any given moment. The circle is updated 
   at the same rate as the spacecraft symbol, normally every ten seconds. 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 26


   Comparisons with a VGA display system during the STS-35/ASTRO-1 mission in 
   December, 1990 confirmed that the circle shown is quite close to that shown 
   by one of the special graphics displays occasionally shown on NASA Select 
   Television.


   TDRS Satellite Features
   -----------------------

        TDRS Satellite features are shown only on HGC, EGA and VGA monitors. 
   The three TDRS satellites (Tracking and Data Relay Satellites), used for 
   most communications to and from the Space Shuttle and the Hubble Space 
   Telescope, are each shown as a dot inside a small yellow circle on the 
   Equator. There are three TDRS satellites in geosynchronous orbit, TDRS East 
   at approximately 72 degrees West longitude and the TDRS West Cluster 
   consisting of two satellites at approximately 170 degrees West longitude. 
   Both of the TDRS West Cluster satellites have partially failed but between 
   them they can provide the facilities of a fully operational satellite.
        Each TDRS location provides communications coverage for almost half of 
   the Earth. However, since the ground station is at White Sands, New Mexico, 
   the coverage overlaps to provide good communications. This, in turn, means 
   that there is a narrow band, known by NASA as the Zone of Exclusion, off 
   the East coast of Africa which is not covered by either TDRS. Four slightly 
   curved vertical red lines on the display show the limits of coverage for 
   each TDRS location. With the map centered on the United States and scanning 
   from left to right, the red coverage lines are acquisition of TDRS East, 
   loss of TDRS West, loss of TDRS East, and acquisition of TDRS West.
        During most of an orbit, the satellite being used for communications 
   will be shown in the data block opposite the title "Com:"; the messages 
   "TDRS-West" or "TDRS-East" will appear. Approximately five minutes before 
   the spacecraft reaches loss TDRS East, the message will change to "LOS 
   5:07" with the numbers indicating the minutes:seconds until anticipated 
   signal loss. Once the signal is lost, the message will change to "AOS 7:35" 
   to show the time remaining until acquisition by TDRS West. The algorithm 
   used for the calculation of the TDRS coverage is very approximate but is 
   usually accurate to within approximately 30 seconds.

   Ground Tracking Stations and .TRK files
   ---------------------------------------

        NASA maintains a number of ground tracking stations around the world. 
   Some of these tracking stations are essential for the ascent or landing 
   phases of a space shuttle flight; others are used for in-flight 
   communications. Files STSPLUS.TRK and NASA.TRK contain the information for 
   these ground tracking stations. Other files with filetype .TRK contain the 
   information for other launch and/or tracking stations.
        Each ground tracking station is shown as a small symbol surrounded by 
   a brown or light yellow "circle of visibility" which gives the approximate 
   area of antenna coverage and shows how small a proportion of each orbit can 
   be monitored without the TDRS system. When for some reason the TDRS system 
   is down (as has occurred during infrequent computer failures at White 
   Sands, New Mexico, the TDRS Ground Station), these ground tracking stations 
   become the only means of communication with the Space Shuttle. Because of 
   budget constraints, many of these ground tracking stations may be (or have 
   already been) shut down. Some, such as MIL and BDA (see list below) will be 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 27


   retained because they are required for the ascent phase of a space shuttle 
   mission. Others, such as HAW, CTS and GWM, are operated jointly with, or 
   independently by, the U. S. Air Force.
        The shape of the antenna range "circle of visibility" varies as a 
   function of the latitude and is an artifact of the map projection; if 
   projected on a sphere, they would be true circles. In order to avoid 
   cluttering the display with countless meaningless lines, tracking station 
   circles of visibility are shown only if that circle has an angular diameter 
   of 90 degrees or less. For all systems except CGA, the locations of the 
   three TDRS (Tracking and Data Relay Satellite) are shown as small circles 
   on the Equator at -41 degrees and at -171 degrees; on CGA displays the TDRS 
   coverage is NOT shown in order to avoid confusing the display.
        The following table lists the internal ground tracking stations as of 
   early 1989 which are shown along with their abbreviations and approximate 
   map coordinates (longitude, latitude):

             MIL     -81,28         Merritt Island, FL
             BDA     -64,32         Bermuda
             DKR     -17,14         Dakar, Senegal
             ACN     -14,-8         Ascension Island
             MAD     -5,41          Madrid, Spain
             IOS      56,-5         Indian Ocean
             HAW     -156,20        Hawaii
             GWM      143.33,14     Gwam
             VAN     -120.57,34.73  Vandenberg, CA
             YAR      115,-29       Yargidy, Australia
             CAN      149,-36       Canberra, Australia
             GDS     -116.88,35.93  Goldstone, CA
             CTS     -105,38        Colorado Springs, CO
             AGO     -71,-34        Santiago, Chile
             NGT     -106,33        White Sands, NM

        STSPLUS first checks for the presence of file STSPLUS.TRK for its 
   ground tracking station information. This is the default TRACKING STATION 
   filename used if no other selection has been made using F7 from the Main 
   Menu. If that file is present, its data is used instead of the internal 
   data above. The supplied STSPLUS.TRK has the following format:

             "Maui, Hawaii",-156.7,20.9,0,"HAW"
             "Vandenberg, CA",-120.5667,34.7333,112,"VAN"
             "White Sands, NM",-106,33,0,"NGT"
             "Colorado Springs, CO",-105,38,0,"CTS"
             "Merritt Island, FL",-81,28,0,"MIL"
             "Santiago, Chile",-71,-34,0,"AGO"
             "Bermuda",-64,32,0,"BDA"
             "Dakar, Senegal",-17,14,0,"DKR"
             "Ascension Island",-14,-8,0,"ACN"
             "Madrid, Spain",-5,41,0,"MAD"
             "Indian Ocean Stn",56,-5,0,"IOS"
             "Yargidy, Australia",115,-29,0,"YAR"
             "Guam",143.3333,14,0,"GWM"
             "Canberra, Australia",149,-36,0,"CAN"

        These files are ASCII and may be prepared or edited with any standard 
   ASCII editor; if using a word processor, select the "non-document" mode. 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 28


   Five items are required for each location; the longitude and latatude are 
   expressed in degrees and fraction of a degree, elevations above Mean Sea 
   Level are expressed in meters, and names or abbreviations are included in 
   double quotation marks. The following example illustrates the .TRK file 
   format:

             "Merritt Island, FL",-81.0,28.0,0,"MIL"
             --------+----------- --+-- --+- + --+--
                     |              |     |  |   |
                     |              |     |  |   +--- 3-Letter Abbreviation
                     |              |     |  +------- Elevation (meters)
                     |              |     +---------- Latitude (degrees)
                     |              +---------------- Longitude (degrees)
                     +------------------------------- Location Name

        For those interested in the Russian space program, a list of Russian
   ground tracking stations is provided in file USSR.TRK (data courtesy 
   Ellwood Marshall). With the breakup of the Soviet Union, some of these 
   installations may no longer be active.

             "Baikonur Cosmodrome",63.3392,45.9235,0,"BAI
             "Dzhusaly USSR",63.85,46.15,0,"DZH"
             "Kalingrad Control Ctr",37.816,55.916,0,"KAL"
             "Plesetsk Cosmodrome",40.7,45.9235,0,"PLS"
             "Petropavlovsk USSR",158.933,53.216,0,"PTR"
             "Tbilisi USSR",44.75,41.66,0,"TBL"
             "Ulan Ude USSR",107.683,51.983,0,"ULN"
             "Ussuriysk USSR",132.15,43.8,0,"USS"
             "Yevpatoria USSR",33.3666,45.2166,0,"YEV"

        Other nations also have facilities for satellite launches. As of early 
   1992, file SPACENTR.TRK includes the following locations:

             "Alcantara LC Brazil",-44.3999,-2.3999,0,"ALC"
             "Esrange,Kiruna Sweden",21.067,67.883,0,"ESR"
             "Jiuquan Space LC China",100.033,40.83,0,"JIU"
             "Kagoshima Center Japan",131.083,31.25,0,"KAG"
             "Kourou Space Ctr Fr.Gu",-52.7669,5.23,0,"KOU"
             "San Marco Platform",40.2,-2.9329,0,"SMP"
             "Sriharikota Ctr India",80.25,13.78,0,"SRI"
             "Tanegashima SC Japan",130.967,30.4,0,"TAN"
             "Xichang Space LC China",102.217,27.967,0,"XUC"

        The first mission of Endeavour, STS-49, was in May, 1992. This 
   dramatic and exciting mission captured the INTELSAT VI (F3) satellite, 
   stranded in a useless orbit by its booster rocket failure since January, 
   1990, and attached a new booster rocket which placed the satellite in its 
   proper orbit. STSPLUS was used operationally during the mission by 
   Intelsat, another "first" for the program. Intelsat used its own ground 
   tracking stations for communications with INTELSAT VI (F3); the ground 
   stations which participated in the mission are listed in file INTELSAT.TRK 
   (information courtesy Dee Smith):

             "Paumalu, Hawaii",-158.0342,21.6711,157.86,"PAU"
             "Tangua, Brazil",-42.7845,-22.7442,35.38,"TAN"

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 29


             "Jatiluhur, Indonesia",107,-6.5213,161.49,"JAT"
             "Perth, Australia",115.25,-31.8,0,"PER"
             "Gandoul, Senegal",-17.4745,14.43,0,"GAN"

        These TRK files are standard ASCII files and may be edited with any 
   editor; word processor users be sure to use the ASCII or non-document mode. 
   The files use a standard comma-delimited format as shown; positions are 
   given in longitude (degrees) and latitude (degrees), rounded to the nearest 
   degree. A maximum of 25 ground stations is permitted. Note that although 
   the two quoted strings at the beginning and end of each line are not 
   presently used, they are required for proper operation. The use of TRK 
   files is not restricted to tracking stations, of course. So long as the 
   correct data format is observed, any desired location may be included in 
   the tracking station file up to the maximum of 25 locations.

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 30


   ACTIVE KEYS DURING GROUND TRACK DISPLAY
   ---------------------------------------

        The following table lists the various keys which are active when the 
   tracking display is shown on the screen. Some of these features are more 
   fully described elsewhere.

      ENTER  Return to Main Menu (cancel this simulation).

         F1  On-line HELP. Press F1 to display a help screen in the lower 
             portion of the screen. Press F1 again to resume normal data 
             display.

         F2  Selects the Big Clock mode. These modes are selected in the 
             following order:

                  0    No clock displayed
                  1    UTC date and time
                  2    Local date and time
                  3    MET or T+Epoch (select with F5)

             Note that not all computers (especially older CGA systems) will 
             display the extended graphics characters used for the large clock 
             characters. The symptom of this problem is that the lower left 
             portion of the data block is mostly blank after pressing F2. If 
             you have this problem and your computer is running DOS 3.x or DOS 
             5.0, enter the command "GRAFTABL" at the DOS prompt before 
             running STSPLUS or include the line "GRAFTABL" in your 
             AUTOEXEC.BAT file; this sets the "code page" to enable the 
             computer to display the extended graphics characters. [The 
             program GRAFTABL.COM is included as part of DOS in most cases.]

         F3  Enable or disable printer logging. If logging is enabled, the 
             word LOG appears in the lower right of the screen. Be sure the 
             printer is turned on BEFORE using the L command. The "L" command 
             automatically enables the display of ascending and descending 
             node information.

         F4  Toggle FAST mode from x1 to x10 to x60 to x1, etc. When either of 
             the fast modes is enabled, "(x10)" or "(x60)" will appear at the 
             upper right of the data block in red. This feature operates in 
             both the normal (real or simulated time) and PAUSE modes. When 
             x10 or x60 fast modes are used, automatic map generation is 
             disabled; use the TAB key to restore automatic map generation.

         F5  When using 2-line elements, the elapsed time may be switched 
             between "T+Epoch" and "MET" by using the "T" command. If no 
             launch time and date have been entered, this command will have no 
             effect.

         F6  Enable/Disable PAUSE mode; only the local date and time are 
             updated. The plot is frozen at the current position and the "+" 
             and "-" commands are enabled.

         F7  Enable or disable the spacecraft circle of visibility.

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 31



         F8  Enable or disable the SUN, solar terminator, and spacecraft 
             lighting feature. NOTE: The SUN and spacecraft lighting are not 
             available on CGA systems.

         F9  Change units of distance between kilometers (km) and nautical 
             miles (NM).

        F10  Change satellite coordinates between Altitude and Azimuth, Right 
             Ascension and Declination, and Geocentric Rectangular (XYZ) 
             systems.

          +  During PAUSE mode only, moves the satellite to the NEXT 
             calculated position based upon the FAST mode then in effect: 
             simulated time is advanced 1, 10, or 60 seconds. (NOTE: The "=" 
             key may be used instead of "+" to avoid the SHIFT KEY.)

          -  During PAUSE mode only, moves the satellite to the PREVIOUS 
             calculated position based upon the FAST mode then in effect: 
             simulated time is backed up 1, 10, or 60 seconds.

             NOTE: Since this "-" or reverse feature was implemented primarily 
             for testing and demonstration, the ground track logic does not 
             recognize these reverse movements and will become slightly 
             confused. To restore the ground track and current times properly, 
             press ENTER TWICE to stop the display and then to resume the 
             mission.

        TAB  Enable or disable automatic map generation. When automatic map 
             generation is enabled, the letter "A" will appear in the upper 
             right of the display screen. Pressing the TAB key will always 
             cause the map to be redrawn.

       PgUp  When in one of the zoom modes, increases the field of view up to 
             a maximum of 180 degrees. Press rapidly to execute multiple zoom 
             steps without redrawing the map for each keypress.

       PgDn  When in one of the zoom modes, decreases the field of view down 
             to a minimum of 45 degrees. Press rapidly to execute multiple 
             zoom steps without redrawing the map for each keypress.

       Home  When in one of the zoom modes, returns the field of view to 75 
             degrees.

        End  When in one of the zoom modes, returns the field of view to the 
             last zoom factor used prior to pressing the HOME key.

          B  Toggle the BLINK mode of the satellite symbol between blinking 
             and steady.

        W,0  Select World Map display, showing the full world from +85 degrees 
             North latitude to -85 degrees South latitude. If automatic map 
             generation is disabled, pressing "W" or "0" will toggle between 
             the two world map displays.


   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 32


          Q  Select Quadrant Map display, showing 180 degrees field of view 
             and selected so as to approximately center the satellite.

         1-9 Select the indicated Quadrant Map. Automatic map generation is 
         !@# disabled when a specific quadrant map is selected. See the chart
             in the section Quadrant Maps for the map numbers.

          Z  Select Zoom Map display, showing from 180 to 45 degrees field of 
             view and selected so as to approximately center the satellite. 
             The default is 75 degrees.

          L  Select Location Map display, showing concentric isocontours for 
             your location. If a second location has been enabled, press "L" 
             again for that location.

          T  Tracking Station Map display, showing concentric isocontours for 
             the tracking station closest to the current ground track position 
             of the satellite. Uses the data in the current TRACKING STATION 
             file to select the tracking station(s); if the file is not found, 
             STSPLUS defaults to an internal set of tracking stations. Use F7 
             from the Main Menu to select the TRACKING STATION filename.

          M  Satellite Motion Map display, available on EGA and VGA systems 
             only. Displays a zoom map with the satellite centered. Maps are 
             drawn "off screen" and a complete map is always displayed. The 
             map is updated every 10 seconds or as rapidly as the computer 
             processor will permit.

          R  Resynchronize MET or T+Epoch with Local Time. Resets plot to real 
             time.

             NOTE: The Resynchronization feature was originally intended only 
             for testing and should only be performed when the simulated time 
             and local times are reasonably close to each other. The plot may 
             otherwise have some extraneous pixels left around! This feature 
             has not been extensively tested. To restore the ground track 
             completely, press ENTER to stop the display and return to the 
             Main Menu, then press ENTER again to resume the mission.

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 33


   STSORBIT PLUS MAIN MENU
   -----------------------

        Once the map coordinates have been stored internally, STSORBIT PLUS
   presents its Main Menu:



                                Program STSORBIT PLUS

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9228

                      Current time:  16:34:24 PDT   23:34:24 UTC
                      Current date:    04/08/1992     04/08/1992

            F1     Program STSORBIT PLUS Demonstration
            F2     Read NASA/NORAD 2-Line Elements       (from *.TXT File)
            F3     Read Prior Mission Information        (from *.INI File)
            F4     Enter New Orbital Information    (Simple Orbital Model)
            F5     Adjust Launch Time and/or Launch Date
            F6     Display MET & Launch Times     (now 2-Line Epoch Times)
            F7     Set FILENAMES and Paths 
            F8     Set program TIME and/or DATE
            F9     DOS Shell             (CAUTION: DOS Version 3.x+ ONLY!)
            F10    Set STSORBIT PLUS Program Options and Features
            ENTER  Resume Mission                      (STS-45 [STS45J13])

            ESC    Quit STSORBIT PLUS and Save Current Mission

            Select desired function:


   F1     Program STSORBIT PLUS Demonstration
   ------------------------------------------

        The F1 command may be used to demonstrate the operation of STSPLUS and 
   to verify that the program will operate correctly. No other information is 
   required. The demonstration automatically sets up the data to simulate a 
   mission and clears the screen. A slight delay may follow while the program 
   calculates the initial parameters of the orbit. Then the world map is 
   drawn, the ground track for the first three orbits (approximately) is drawn 
   as a series of dots (green for color monitors), and mission data is 
   displayed at the bottom. Mission Elapsed Time (MET) is set to shortly 
   before launch time and counts down to zero.
        When MET reaches zero, the shuttle symbol appears over Cape Canaveral. 
   For CGA and HGC systems, the shuttle will blink; for EGA and VGA systems, 
   the shuttle will be steady. At first the shuttle will move along the ground 
   track very slowly, simulating the ascent phase of the mission. After about 
   ten minutes the shuttle reaches orbital altitude and proceeds along the 
   ground track normally, passing a dot every minute. Press F4 (for Fast time) 
   once or twice to speed up the progress of the simulation. Press ENTER to 
   return to the Main Menu.
        Data are displayed by STSPLUS in several standard formats:


   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 34


            4/05/1990       Date in month/day/year
             14:33:00       Time in hours:minutes:seconds
           3/09:23:15       MET in days/hours:minutes:seconds
               -69.34       Longitude and Latitude in degrees
                            WEST longitude and SOUTH latitude are negative
               320.50 nm    Altitude in nautical miles

   F2     Read NASA/NORAD 2-Line Elements from *.TXT File
   ------------------------------------------------------

        In order to read the NASA/NORAD 2-line elements, you must have a file 
   with that data. A current file is included in the standard distribution of 
   STSPLUS. These files have names such as "NASA014.TXT" where the "014" 
   corresponds to the particular NASA Prediction Bulletin number from T. S. 
   Kelso's Celestial BBS and may change several times per week. 
        Pressing F2 will display a list of all available files (the example 
   has been edited to show only 8 lines):

        Select NASA/NORAD 2-Line Elements File

        Enter 2-Line Filename  [STS50N38.TXT]:
        Use ARROW KEYS or press ENTER to use the current
        default file as shown in square brackets [...].

         16 Available .TXT files in directory E:\STSPLUS

        COS851R.TXT    STS49N12.TXT
        GSFC035.TXT    STS49N16.TXT
        GSFC055.TXT    STS49N19.TXT
        GSFC071.TXT    STS49N26.TXT
        GSFC096.TXT    STS49N28.TXT
        GSFC097.TXT    STS49N29.TXT
        GSFC100.TXT    STS49R05.TXT
        GSFC101.TXT    STS50N38.TXT

        The list of files is sorted in alphabetical order then displayed using 
   up to five columns. The default filetype is ".TXT". The display mode is 
   adjusted for the maximum number of lines permissible for the active monitor 
   type: 25 lines for CGA and HGC, 43 lines for EGA, and 50 lines for VGA. The 
   maximum number of files which may be displayed for each monitor type is 
   shown in the following table:

                       Screen     File      Max
             Monitor    Lines    Lines    Files
             ----------------------------------
             VGA           50       42      210
             EGA           43       35      175
             CGA/HGC       25       17       85

        To accept the default file shown in the square brackets, STS50N38.TXT 
   in the example, press ENTER. To manually enter a filename, type the name 
   (the filetype .TXT will be appended if no filetype is typed) and press 
   ENTER. To select one of the displayed files, use the ARROW KEYS (UP, DOWN, 
   LEFT, RIGHT), Home, End, PgUp, or PgDn to move through the list until the 
   desired file is highlighted and shown in the square brackets, then press 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 35


   ENTER.
        STSPLUS defaults the drive and directory to the current directory, the 
   one from which STSPLUS is being executed. However, some users prefer to use 
   a separate directory for 2-line elements files. To specify a different 
   drive and/or directory, enter the drive (followed by a colon) and the 
   desired directory (followed by a trailing backslash, "\"). The specified 
   drive, directory, and filename are saved in file STSPLUS.INI and will be 
   used the next time STSPLUS is executed. The following examples illustrate 
   this method:

             D:\            Use the root directory on drive D:

             \ELEMENTS\     Use the current drive and directory ELEMENTS

             C:\TLE\        Use drive C: and directory TLE

   Failing to include the trailing backslash will cause STSPLUS to interpret 
   what you intended as a directory to be a filename! The complete path with
   filename and filetype mask may also be entered:

             C:\TLE\*.TXT   Use .TXT files on Drive C: and directory TLE

             D:\TLE\*.*     Display all files on drive D: and directory TLE

   Although STSPLUS defaults to "*.TXT", you may use this command to 
   temporarily specify a different filename and filetype mask if desired.
        If no files with filetype .TXT (or files corresponding to the current 
   filename and filetype mask) are found in the specified directory, the 
   following error message will be displayed:

        No .TXT files found in specified drive/directory: E:\JUNK
        Press any key to continue ...

   where the filetype, ".TXT" in the example above, is the default filetype or 
   whatever filetype was specified. To specify NO fileltype, enter the 
   filename followed by a period, i.e. "ELEMENTS.". Any desired filetype may 
   be used, but the program will always default to ".TXT" each time F2 is 
   used.
        If you include a drive (such as "D:") and/or directory (the directory 
   MUST be followed by a trailing backslash, "\"), and the drive or directory 
   cannot be found, the following error message will be displayed:

        Drive or path error: E:\JUNK
        Press any key to continue ...

        Once the file has been selected, a default satellite name will appear 
   in the next prompt:

        Enter 2-Line Filename  [STS50N38.TXT]:    STS50N38.TXT
        Enter Satellite Name/Number  [STS...]:
        (Enter '*' to match any satellite name)

        STSPLUS will normally display the first three characters of a 
   satellite name, enclosed in square brackets, as the default choice. If no 
   prior satellite has been selected, the satellite name will default to 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 36


   "STS..." for space shuttle missions (provided the filename begins with 
   "STS") and to "HST..." for all other satellites; otherwise, it will be the 
   first three letters of the currently selected satellite. If you wish to 
   change the information (or if no default is shown), enter the required 
   information followed by ENTER. For the satellite name, only sufficient 
   letters to unambiguously identify the desired satellite, upper or lower 
   case, are required. For example, "Alou" would select "Alouette 1". However, 
   note that entering "MIR" could select "MIRANDA" before it finds "MIR" 
   depending upon the ordering of the 2-line elements within the file.
   Alternatively, you may enter the NORAD number for the desired satellite; 
   leading zeroes may be omitted.
        Once the information has been entered, STSPLUS will attempt to locate 
   the data for the requested satellite. If a satellite matching the requested 
   name is found, the data for that satellite are displayed. Certain non-
   essential data are not always included in the 2-line elements and may be 
   replaced by spaces, indicated by "(n/a)".


        Satellite Name:              STS-50
        Satellite NORAD Number:      22000
        Elements File:               STS50N38.TXT
        Elements File Record#:       1
                                     (*)
        Element Set Number:          38
        Elements Epoch:              92187.57342677
                                     05 JUL 1992 @ 13:45:44 UTC
        Orbit # at Epoch:            159
        Launch Year:                 1992
        Launch Number:               34
        Launch Piece:                A
        Inclination:                 28.467
        RA of Ascend Node:           275.07
        Eccentricity:                .0007237
        Arg of Perigee:              340.7929
        Mean Anomaly:                19.153
        Mean Motion:                 15.91359642
        Acceleration/Drag:          -.00032668
        BSTAR Drag:                 -.000097874

        Press ENTER to ACCEPT this satellite, OR
        Press any other key to REJECT and continue searching:


        (*) This line is normally blank. However, one of the following 
        messages will appear here if a checksum error is detected in the 
        element set:

             BAD CHECKSUM in line 1 ignored!
             BAD CHECKSUM in line 2 ignored!
             BAD CHECKSUM in both lines ignored!

        In all three cases, STSPLUS will accept the data and attempt to use 
        it. Be advised, however, that the checksums are included to help 
        detect errors that might otherwise yield an incorrect position!


   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 37


        If this is the satellite you wish, press ENTER and the data will be 
   entered into STSPLUS. If, on the other hand, a different satellite is 
   desired, press any other key (such as the SPACE BAR) and STSPLUS will 
   search for another name matching the requested satellite. For example, 
   there are a number of NAVSTAR Global Positioning Satellites usually 
   included in the file with official names such as "GPS-0001", "GPS-0002", 
   "GPS BII-01" and so forth; requesting "GPS" will allow you to cycle through 
   all the available choices. The file NASAnnn.TXT is an ASCII file; it may be 
   helpful to view the file to see the available satellite names. 
        Once the satellite has been selected, STSPLUS will require a brief 
   time to calculate certain required orbital parameters, then will proceed 
   directly to the display of the ground track.
        As a point of interest, the NASA 2-line elements for the Space Shuttle 
   Mission STS-50 used in the example above are as follows:

        STS-50
        1 22000U 92 34  A 92187.57342677 -.00032668  00000-0 -97874-4 0   380
        2 22000  28.4670 275.0700 0007237 340.7929  19.1530 15.91359642  1596


   F3     Read Prior Mission Information from *.INI File
   -----------------------------------------------------

        The F3 command displays all files in the current directory with a 
   filetype of .INI and then prompts the user to enter the name of the desired 
   data file. File STSPLUS.INI is the file which has the data from the last 
   time the program was run; to use file STSPLUS.INI, press ENTER. STSPLUS 
   will automatically supply the filetype .INI if you do not include it. If 
   the requested file is not present, an error will be reported. To create new 
   command to copy STSPLUS.INI into a file with a the desired name.
        STSPLUS also expects your computer clock to be set to the correct 
   local time and date; use the DOS TIME and DATE commands. See the F10+F10 
   command below for information on setting the UTC Zone Offset. Of course, 
   you could "fool" STSPLUS by setting your computer to a desired time and 
   date using the DOS TIME and DATE commands, but be aware that for most 
   computers using MS-DOS/PC-DOS 3.3 or greater the hardware clock is also set 
   with these commands. Instead of setting your computer clock to some 
   fictitious time, use STSPLUS's internal time setting functions (F8 on the 
   Main Menu) to set a desired simulation time. This method does not affect 
   your computer's internal hardware or software clocks.


   F4     Enter New Orbital Information (Simple Orbital Model)
   -----------------------------------------------------------

        The F4 command uses the "simple" orbital model and allows the user to 
   enter the orbital altitude, inclination, launch time, and launch date 
   using your local time or UTC (Coordinated Universal Time) or GMT (Greenwich 
   Mean Time, essentially identical to UTC for the purposes of this program) 
   to determine the orbital parameters. If you enter the time and date using 
   local time, it will internally be converted to UTC so that the .INI file 
   will be valid in any time zone. To manually enter orbital data, you will be 
   prompted for the required information. 



   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 38


                                Program STSORBIT PLUS

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9228

                      Current time:  16:34:24 PDT   23:34:24 UTC
                      Current date:    04/08/1992     04/08/1992


                 Enter mission title:             STS Mission Simulation
                 Enter orbit altitude (nm):       160.00 nm  (  296.52 km)
                 Enter orbit inclination (deg):    28.450 degrees
                 Enter Launch Time (HH:MM:SS):     15:58:12 PST  23:58:12 UTC
                 Enter Launch Date (MM/DD/YYYY):      4/08/1992     4/08/1992




                       Press ENTER to accept, SPACE BAR to repeat: _


   The sample above illustrates the data required to generate the simple 
   orbital model. A brief discussion follows for each item.

        Enter mission title:

   Enter the title of the mission, such as "STS-45 ATLANTIS" without the 
   quotation marks. If you press ENTER, the title "STS Mission Simulation" 
   will be used.

        Enter orbit altitude (nm):
           [Add 'km' for altitude in kilometers.]

   Enter the orbit altitude (or average orbit altitude for non-circular 
   orbits), in nautical miles. If you wish to use kilometers, add the letters 
   "KM" (upper or lower case) at the end of the number.

        Enter orbit inclination:

   Enter the inclination of the orbit in degrees; a decimal fraction is 
   allowed. For example, STS-30 was flown at an inclination of 28.85 degrees 
   and STS-28 used an inclination of 57 degrees. Press ENTER to use the 
   default value of 28.45 degrees.

        Enter Launch Time (HH:MM:SS):
           [Press ENTER for ASAP; add 'U'or 'G' for UTC/GMT]

   Enter the time in the format shown using 24-hour notation and local time. 
   Add the letter "U" to signify UTC (Coordinated Universal Time) or the 
   letter "G" to signify GMT (Greenwich Mean Time, essentially identical to 
   UTC for the purposes of this program). If you enter "U" or "G", the 
   abbreviation used in the menus will be set to "UTC" or "GMT" respectively.
   One or two digit numbers may be used as required. [The comma is also 
   acceptable as a separator in place of the colon.] You may omit seconds [or 
   minutes and seconds] if desired. For example, an entry of "16" will be 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 39


   entered as 16:00:00 or 4:00 PM. Press ENTER for "launch" ASAP, as soon as 
   possible; depending upon the system, this will be in from 30 to 60 seconds 
   from the current time.

        Enter Launch Date (MM/DD/YYYY):
           [or press ENTER for TODAY]

   Enter the date in the format shown. Note that if you requested UTC or GMT 
   when entering the time, the date is interpreted as the UTC/GMT date. The 
   full four digit year may be used OR you may use two digits as in "92". Be 
   sure to use the SLASH "/" rather than the MINUS "-" as the separator; 
   STSPLUS's internal date algorithms will interpret the minus sign as just 
   that and some rather strange dates can result! You may also use relative 
   dates: -1 will use the prior day, +2 will use two days hence, and so forth. 
   Press ENTER to use today's date.

        Press ENTER to accept, SPACE BAR to repeat:

   When all data have been entered, the program pauses for your approval. If 
   all data are correct, press ENTER. Press the SPACE BAR to start over.


   F5     Adjust Orbital Parameters
   --------------------------------

   ADD/CHANGE LAUNCH DATE AND TIME (2-line elements)

        The full F5 command assumes the "simple" orbital model and is 
   abbreviated when using NASA 2-line elements; only the LAUNCH DATE and 
   LAUNCH TIME may be set when NASA 2-line elements have been selected; all 
   other orbital parameters are included in the 2-line elements and may not be 
   altered within STSPLUS. A 2-line element set must have been previously 
   loaded using the F2 command on the Main Menu before the launch date and 
   time may be set or changed.
        Since estimated NASA 2-line elements are usually available prior to a 
   launch, and actual 2-line elements within about 24 hours after a launch 
   (and are far more accurate than the manually entered "simple orbital 
   data"), those data should be used when available. However, since most 
   events occuring during a space shuttle mission follow the MET (Mission 
   Elapsed Time) timeline, the time elapsed since launch, it is convenient to 
   show MET. This requires that you obtain the launch date and launch time 
   independent of the 2-line elements and manually enter that data into 
   STSPLUS. Note that STSPLUS retains the launch date and time information 
   from one set of 2-line elements to another. Be sure to reset these data 
   when you change from one mission to another!

        Enter Launch Time (HH:MM:SS):
           [Press ENTER for ASAP; add 'U'or 'G' for UTC/GMT]

   Enter the time in the format shown using 24-hour notation and local time. 
   Add the letter "U" to signify UTC (Coordinated Universal Time) or the 
   letter "G" to signify GMT (Greenwich Mean Time, essentially identical to 
   UTC for the purposes of this program). If you enter "U" or "G", the 
   abbreviation used in the menus will be set to "UTC" or "GMT" respectively.
   One or two digit numbers may be used as required. [The comma is also 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 40


   acceptable as a separator in place of the colon.] You may omit seconds [or 
   minutes and seconds] if desired. For example, an entry of "16" will be 
   entered as 16:00:00 or 4:00 PM. Press ENTER for "launch" ASAP, as soon as 
   possible; depending upon the system, this will be in from 30 to 60 seconds 
   from the current time.

        Enter Launch Date (MM/DD/YYYY):
           [or press ENTER for TODAY]

   Enter the date in the format shown. Note that if you requested UTC or GMT 
   when entering the time, the date is interpreted as the UTC/GMT date. The 
   full four digit year may be used OR two digits as in "92". Be sure to use 
   the SLASH "/" rather than the MINUS "-" as the separator; STSPLUS's 
   internal date algorithms will interpret the minus sign as just that and 
   some rather strange dates can result! You may also use relative dates: -1 
   will use the prior day, +2 will use two days hence, and so forth. Press 
   ENTER to use today's date.

        Press ENTER to accept, SPACE BAR to repeat:

   When all data have been entered, the program pauses for your approval. If 
   all data are correct, press ENTER. Press the SPACE BAR to start over.
        Once the launch date and time have been set, this information is 
   saved in file STSPLUS.INI. Remember, when changing from one satellite to 
   another this information is NOT cleared automatically.


   ADJUST ORBITAL PARAMETERS (Simple Orbital Model)

        When the orbital parameters change in mid-mission for the "simple" 
   orbital model, use this command to adjust the orbital period/altitude, 
   orbital longitude, and time along orbital track. This technique allows the 
   "launch time" to remain correct, which in turn assures that Mission Elapsed 
   Time is correct, while adjusting the orbital parameters so that the 
   position is displayed correctly in later orbits. The following items may be 
   adjusted; in each case, the required units or input format is shown in 
   parentheses (...) and the current value of the item is shown within square 
   brackets [...]. Press ENTER to leave an item unchanged.

                                Program STSORBIT PLUS

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9228

                      Current time:  16:34:24 PDT   23:34:24 UTC
                      Current date:    04/08/1992     04/08/1992



   Enter MISSION TITLE [STS Mission Simulation]:    STS Mission Simulation
   Enter LAUNCH TIME (HH:MM:SS)    [23:58:12 UTC]:  16:58:12 PDT   23:58:12 UTC
   Enter LAUNCH DATE (MM/DD/YYYY)    [04/08/1992]:     4/08/1992      4/08/1992
   Enter ORBIT INCLINATION (degrees) [28.4500x]:    28.4500
   Enter ORBITAL ALTITUDE (nm)        [ 160.00]:   160.00 nm  (  296.52 km)
   Enter LONGITUDE adjust (deg)     [   0.000x]:     0.000

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 41


   Enter TIME adjust (min)            [  0.000]:     0.000

                       Press ENTER to accept, SPACE BAR to repeat:


        In order to make these adjustments, the current orbital altitude is 
   required, along with the longitude and time of one or more equator 
   crossings (obtained from the NASA Television wall map). NASA is not too 
   good about making sure that the map is on the screen when the Shuttle makes 
   an equator crossing (Northbound is Ascending Node, Southbound is Descending 
   Node); they have a distressing tendency to cut away just before the 
   crossing. With sufficient patience, however, the data can be interpolated 
   from the television screen. See the section ADJUSTING ORBITAL PARAMETERS 
   below for more information.


   F6     Set Elapsed Time Option
   ------------------------------

        When using NASA 2-line elements, STSPLUS by default displays the time 
   elapsed since the epoch date of the elements in the upper right portion of 
   the data block. This is marked on the display as "T+Epoch". While this 
   information is not of particular value for satellite viewing purposes, it 
   does indicate the relative age of the orbital data. As a general rule, 
   especially for lower Earth orbits, the effects of orbit decay make position 
   predictions less accurate as time passes. Data which are more than 10 or 20 
   days old may produce less accurate positions.
        For a space shuttle mission, however, all mission events are scheduled 
   against the mission timeline and are reckoned in Mission Elapsed Time 
   (MET), the time elapsed since launch. It is therefore useful to be able to 
   display MET during the course of a mission or to review the flight post-
   mission. Unfortunately, the standard NASA/NORAD 2-line element format does 
   not include the launch time and launch date and therefore this information 
   must be secured independently and manually entered into STSPLUS. Once 
   entered, STSPLUS saves the information in file STPLUS.INI.
        The F6 command may be used to switch the display between Time Since 
   Epoch ("T+Epoch") and Mission Elapsed Time ("MET"). The command description 
   on the Main Menu indicates which mode will be selected if Function Key F6 
   is pressed:

            F6     Display MET & Launch Times     (now 2-Line Epoch Times)

            F6     Display 2-Line Epoch Times     (now MET & Launch Times)

   The first example (the default) indicates that MET will be displayed if the 
   function key is pressed; the second example indicates that the display will 
   return to Time Since Epoch if the function key is pressed. (The elapsed 
   time option may also be switched at any time during the tracking display by 
   pressing Function Key F5.)
        The F6 command checks that you have already entered the launch time 
   and launch date or that it has been read from a previous STSPLUS session 
   from file STSPLUS.INI. However, since the launch time and date are not 
   included in the 2-line orbital elements, no validity check can be made; if 
   you change satellites, be sure to either clear or change the launch time 
   and date. If no launch time and date are present, you will be prompted for 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 42


   the information as if you had pressed function key F5 (see above). The F6 
   command is inactive unless you have read in 2-line elements using function 
   key F2.


   F6     Set FILENAMES and Paths
   ------------------------------

        Function Key F7 allows the user to select the filenames (and drive and 
   path, if included) for the files that STSPLUS uses to select satellites and 
   tracking stations.

             Select filename to set or press ENTER when done:

               F1  Set 2-LINE ELEMENTS filename   [NASA975.TXT]
               F2  Set TRACKING STATION filename  [STSPLUS.TRK]

             Enter selection or ENTER:

   The current filename is shown in square brackets for each selection. Press 
   F1 to set the 2-LINE ELEMENTS filename or F2 to select the TRACKING STATION 
   filename. Press ENTER to leave a filename unchanged. The following is a 
   typical prompt for filename:

             Enter TRACKING STATION filename: _
             (Press ENTER to leave unchanged)

        If no filetype is entered, STSPLUS will automatically supply ".TXT" 
   for 2-line elements files and ".TRK" for tracking station files. If the 
   desired file has no filetype, include the period in the filename entered 
   (for example: "STATION.") to prevent the automatic addition of a filetype. 
   After each entry, the Filenames Menu is again displayed with the current 
   selections. Press ENTER when done to return to the STSPLUS Main Menu.


   F8     Set Program TIME and DATE
   --------------------------------

        It is often convenient to set the TIME and DATE within STSPLUS to 
   something other than the current system time and date, or to return to the 
   current system time and date if the program time and date have been 
   changed. Press F4 to go to the TIME and DATE Menu:


                                Program STSORBIT PLUS

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9228

                      Current time:  16:34:24 PDT   23:34:24 UTC
                      Current date:    04/08/1992     04/08/1992

                       ACTUAL SYSTEM DATE AND TIME SHOWN ABOVE



   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 43


            F1     Restore SYSTEM date and time (use "real time")
            F2     Set DOS SYSTEM CLOCK using calendar date and time
            F3     Set SIMULATED date and time using calendar date and time
            F4     Set SIMULATED date and time using Mission Elapsed Time

            ENTER  Return to MAIN MENU

            Select desired function:

        The Date and Time Menu, shown above, displays the available time 
   setting functions along with the actual system date and time as determined 
   by the DOS software clock in your computer (even if simulated time is in 
   effect). Both your local date and time, "PDT" or Pacific Daylight Time in 
   the example, and "UTC" (Coordinated Universal Time) date and time are 
   displayed. If times have been set using the letter "G", the abbreviation at 
   the right will be "GMT" (Greenwich Mean Time).
        If you wish to execute STSPLUS in "real time", cancelling any 
   simulated time that may be in effect, use the F1 command. This will restore 
   the time and date used for the tracking display to that shown at the top of 
   the menu.
        If the actual system date or time displayed is incorrect, use the F2 
   command to correctly set your system clock. If the zone abbreviation or UTC 
   date or UTC time is incorrect, use the Set Program Options command from the 
   Main Menu (F10+F9) to correctly set the UTC Offset and the Daylight Flag.
        Some organizations, NASA for example, continue to use the wording 
   "Greenwich Mean Time" or "GMT" for what is now usually referred to as 
   "Coordinated Universal Time" or "UTC" (and sometimes, depending upon the 
   application, as "UT", "UT1" or "UT2"). STSPLUS uses Coordinated Universal 
   Time or "UTC", the time used for civil timekeeping and broadcast by radio 
   stations such as WWV and the BBC. Although technically these different time 
   standards are not exactly the same, the difference is only a maximum of 0.9 
   seconds and the program treats them all as identical. STSPLUS defaults to 
   the abbreviation "UTC" but if you prefer to use "GMT", enter any simulated 
   time using F3 and include the letter "G" (upper or lower case) at the end. 
   The time abbreviation at the top of the screen will change from "UTC" to 
   "GMT" and will continue using that abbreviation until a time is entered 
   suffixed with "U". 
        Times are always entered as "HH:MM:SS" where HH is HOURS, MM is 
   MINUTES, and SS is SECONDS. The time entry format is very flexible. Leading 
   zeroes are not required. The comma (",") may be used in place of the colon 
   (":") as a separator if desired. SECONDS or MINUTES and SECONDS may be 
   omitted if desired. Time entries are assumed to be local time; to enter UTC 
   or GMT times, add the letter "U" or "G" (upper or lower case) respectively 
   following the entry. For example, the following are valid time entries:

             Entry          Interpreted as
             ------         --------------
             12             12:00:00
             13,1           13:01:00
             4:1:15         04:01:15
             1,1,1          01:01:01
             13,45U         13:45:00 UTC 
             1:20g          01:20:00 GMT

        Dates are always entered as "DD/MM/YYYY" where DD is DAYS, MM is 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 44


   MONTHS, and YYYY is the full four-digit year. The full date must always be 
   entered; leading zeroes are not required. The date entered is assumed to be 
   for the same time zone as the time entered. If local time is entered, the 
   date will be treated as the local date; if UTC (or GMT) time is entered, 
   the date will be treated as the UTC/GMT date.
        After a time or date entry has been read (after you press the ENTER 
   key), STSPLUS reformats the entry to its standard format, clears the 
   characters you entered, and replaces them by the standard format. This 
   provides a double check that the program has interpreted your entry as you 
   wished.
        Press F1 to restore the program date and time to the system date and 
   time. This command reads the DOS clock and restores the program to "real 
   time" operation. If the program date and time have not been changed with 
   the F3 or F4 commands, this command will have no effect.
        Press F2 to set the DOS system clock. Use this command if you wish to 
   change the actual date and time on your system. Note that on many systems 
   using DOS 3.3 or higher, this command will set BOTH the software clock AND 
   the hardware clock.

                                Program STSORBIT PLUS

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9228

                      Current time:  16:34:24 PDT   23:34:24 UTC
                      Current date:    04/08/1992     04/08/1992

           CAUTION: This function will change the computer's SYSTEM CLOCK!

                        Press ENTER to leave an item unchanged

                 Enter TIME (HH:MM:SS):                16:34:24 PST
                 Enter DATE (MM/DD/YYYY):                 4/08/1992

            Press ENTER to accept, SPACE BAR to repeat: _

   The sample above shows the screen after the time and date entries have been 
   completed. The current ACTUAL system date and time are displayed for 
   approval. Press ENTER to accept the time and date displayed, or press the 
   SPACE BAR to repeat the entries.
        Press F3 to set a simulated date and time. The date and time may be 
   either in the past or in the future. This command does NOT affect the DOS 
   clock in your system! Use the F2 command above to restore the date and time 
   to "real time".

                                Program STSORBIT PLUS

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9228

                     Simulated time:  13:00:08 PST   21:00:08 UTC
                     Simulated date:    11/08/1991     11/08/1991




   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 45


                        Press ENTER to leave an item unchanged

            Enter SIMULATED TIME  [12:05:06]:     13:00:00 PST   21:00:00 UTC
            Enter SIMULATED DATE  [11/11/1991]:     11/09/1991     11/09/1991

            Press ENTER to accept, SPACE BAR to repeat: _

   The sample above shows the screen after the time and date entries have been 
   completed. The new SIMULATED date and time are displayed (and counting) for 
   approval. Press ENTER to accept the time and date displayed, or press the 
   SPACE BAR to repeat the entries.
        Press F4 to set a simulated date and time using MET (Mission Elapsed 
   Time). Note that this command will appear ONLY if the mission name begins 
   with the letters "STS", signifying a Space Transportation System (Space 
   Shuttle) mission AND if a launch time and date have previously been 
   entered.

                                Program STSORBIT PLUS

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9228

                     Simulated time:  00:17:18 PST   08:17:18 UTC
                     Simulated date:    10/09/1991     10/09/1991



                       Enter desired Mission Elapsed Time (MET)

                       Enter MET DAY (NN):             3 day(s)
                       Enter MET TIME (HH:MM:SS):      04:30:00 MET

                       Press ENTER to accept, SPACE BAR to repeat: _

   The sample above shows the screen after the day and time entries have been 
   completed. The Mission Elapsed Time is immediately converted to actual date 
   and time and the current SIMULATED date and time, based upon the MET just 
   entered, are then displayed (and counting) for approval. Press ENTER to 
   accept the time and date displayed, or press the SPACE BAR to repeat the 
   entries.
        Press ENTER to return to the Main Menu with the date and time as 
   displayed on the screen (Current or Simulated).


   F9     DOS Shell (CAUTION: DOS Version 3.x+ ONLY!)
   -------------------------------------------------

        If a system function is desired at the Main Menu, press F9 to execute 
   BASIC's DOS SHELL function. This will return you to a DOS prompt and most 
   DOS commands may be executed immediately. When the Shell is executed, 
   STSPLUS remains in memory and the map data will not be re-read when you 
   return. However, this means that a substantial amount of memory is in use 
   and not available to DOS during the shell operations. Enter "EXIT" (without 
   the quotation marks and followed by ENTER) at the DOS prompt when you wish 
   to return to STSORBIT. 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 46



        CAUTION: The BASIC SHELL function is only reliable for versions of DOS 
        of 3.0 or higher! Systems with less than 640K memory may fail to 
        execute the shell and applications requiring large amounts of memory 
        may also fail.

   F10    Set STSORBIT PLUS Program Options and Features
   -----------------------------------------------------

        A number of program features and display options are set using the F10 
   Program Options Menu. These selections are further described in the section 
   "Program Options Menu" below.

   ENTER  Resume Mission
   ---------------------

        Pressing ENTER resumes the current mission shown in parentheses to the 
   right of the command on the Main Menu. The 2-line elements file from which 
   the data was read is shown in square brackets.

            ENTER  Resume Mission                  (STS-41 [STS41F])

   Any manually entered data is retained. "ENTER" means the key marked ENTER, 
   RETURN, or with a left pointing arrow -- but not the backspace or cursor 
   position keys which may also be marked with arrows! (I am afflicted with 
   too long a memory; once upon a time this function was known as Carriage 
   Return and was often shortened to RETURN or even CR. With the advent of 
   electronic typewriters, video terminals, dot matrix printers and all the 
   rest, "carriages" have long since disappeared but old habits die hard! Most 
   PC keyboards are now marked with "ENTER".)
        Use ENTER to resume plotting a mission in progress after returning to 
   the Main Menu to perform some change (such as enabling the node display, 
   enabling the NASA tracking stations, or adjusting the time or date).


   ESC    Quit STSORBIT PLUS and Save Current Mission
   --------------------------------------------------

        Press ESC (the key marked "ESC" or "Esc", not the letters E+S+C) to 
   quit program STSORBIT PLUS. If you press ESC to quit the program and have 
   manually entered orbital data, STSPLUS will save all required mission data 
   in file STSPLUS.INI prior to terminating. This will be the data available 
   with the ENTER key the next time you execute the program. The demonstration 
   data will not be saved, preserving any previously saved mission data.
        When you have finished with STSPLUS, press ESC at the Main Menu to 
   return to DOS. The data (and any adjustments you have made) for the current 
   mission are saved in file STSPLUS.INI, but the map data is lost and will be 
   re-read when you next use program STSPLUS.

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 47


   PROGRAM OPTIONS AND FEATURES MENU
   ---------------------------------

        A number of program features and display options are set using the F10 
   Program Options Menu. When used with CGA displays, the features shown below 
   as selected by function keys F3 and F4 are not available because of the low 
   resolution of the CGA display. The following Options Menu is displayed when 
   the F10 command is entered from the Main Menu:


                                 Program STSORBIT PLUS

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9228

                      Current time:  16:34:24 PDT   23:34:24 UTC
                      Current date:    04/08/1992     04/08/1992


            F1             Program STSORBIT PLUS Information
            F2             Set New Local Coordinates (Rancho Palos Verdes, CA)
            F3             Select Display Features
            F5     OFF     Show Ascending & Descending Node Data
            F6     ZOOM    Set Map Center and Size
            F7     OFF     Set for SLOW COMPUTER or NO COPROCESSOR
            F9    -8.00    Set UTC Time Offset and Daylight Flag
            F10    OFF     Enable/Disable Printer Logging

            ENTER          Return to MAIN MENU

            Select desired function:


   F1     Program STSORBIT PLUS Information
   ----------------------------------------

        Function Key F1 displays information about program STSORBIT PLUS 
   including the copyright notice, version number, my name and address, and 
   the telephone number of my RPV ASTRONOMY BBS (Bulletin Board System). The 
   current version of STSORBIT PLUS is always posted on the BBS. The BBS has a 
   power controller; if it hasn't answered after the THIRD RING, hang up and 
   call back in two minutes. The BBS is available 24 hours per day at 9600, 
   2400 and 1200 baud.


   F2     Set New Local Coordinates
   --------------------------------

        In order to perform the calculations related to satellite visibility 
   and altitude/azimuth, STSPLUS must know the geographic coordinates for the 
   user's location. The name of the current location is shown in parentheses. 
   When STSPLUS is first started, the default coordinates are set to Rancho 
   Palos Verdes, California, near Los Angeles. The current location is 
   indicated by the name in parentheses on the Options Menu. The program 
   provides two methods for setting your own coordinates: reading a file of 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 48


   city names and coordinates (STSPLUS.CTY); or manually entering the 
   information.
        Pressing F2 will display the following reminder:

        STSPLUS will search for the CITYNAME you enter anywhere in the city 
        names in the file. For example, 'SAN' appears in 'SAN FRANCISCO', 'SAN 
        DIEGO', 'SANTA ANA', 'THOUSAND OAKS', etc. Press ENTER to cancel the 
        search or enter '*' to enter a new city name and coordinates.

        In other words, when you enter a name or partial name, STSPLUS will 
   attempt to match that group of characters anywhere in the names which 
   appear in the city file. For example, 'SAN' matches 'SAN diego' as well as 
   'SAN jose' and 'thouSANd oaks'. To get 'SAN FRANCISCO' on the first try, 
   enter 'SAN F' with a space between the 'N' and 'F'. Case is not 
   significant; upper and lower case letters are treated identically. If you 
   change your mind and wish to cancel the operation, simply press ENTER by 
   itself. Use BACKSPACE to make corrections.
        To begin the search, enter the desired name after the prompt. In the 
   example which follows, the name 'ran' was entered for the search.

        Enter CITYNAME to search for:  ran

        Processing record  1
          City Name:  Rancho Palos Verdes CA
          Latitude:     33.7675
          Longitude:  -118.4033
          Elevation:   186 meters

        Press ENTER to ACCEPT this city as your location, OR
        Press TAB to also display this city's location, OR
        Press SPACE to search for next city:  _

        If the city displayed is the one you wish to use as your local 
   coordinates, press ENTER. If you wish to display this city as a second 
   location on the display, press TAB. The data will be entered into STSPLUS 
   and subsequently saved in file STSPLUS.INI. If you wish to search further 
   in the file, press the SPACE BAR.

        NOTE: The elevations contained in file STSPLUS.CTY are almost all zero 
        except for Rancho Palos Verdes, CA for which I have accurate elevation 
        above mean sea level. If you know the correct elevation for your 
        location, edit the file using any ASCII text editor and change the 
        last number on the line. STSPLUS.CTY contains over 800 cities. If 
        users send me their correct elevations (or additional cities they wish 
        added), I will incorporate that data into subsequent versions of file 
        STSPLUS.CTY.

        To enter location data manually, press "*" (without the quotation 
   marks) followed by ENTER. You will be prompted for the city name, latitude, 
   longitude, and elevation. Latitude and longitude may be entered using three 
   different formats for convenience (note the use of comma and decimal 
   point):

             DDD.DDDDD           Degrees and decimal fraction
             DD,MM.MMM           Degrees, minutes and decimal fraction

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 49


             DD,MM,SS.SS         Degrees, minutes, seconds and fraction

   Note that SOUTH latitude and WEST longitude must be entered as NEGATIVE 
   numbers as measured south of the Equator or west of the Prime Meridian at 
   Greenwich, respectively. The default unit for elevations is meters above 
   mean sea level; add "F" (upper or lower case without the quotation marks) 
   if you wish to use feet.
        After the elevation has been entered, the data will be displayed for 
   approval. All data are converted to degrees or meters as appropriate, 
   regardless of the units used on input.

          City Name:  Rancho Palos Verdes CA
          Latitude:     33.7675
          Longitude:  -118.4033
          Elevation:   186 meters

        Press ENTER to ACCEPT this city, OR
        Press SPACE to cancel this data:  _

   Press ENTER to accept the data as shown or SPACE to cancel the data and 
   return to the Options Menu. If the data is accepted, STSPLUS will ask if 
   you wish to append (add) this city/location to the existing file 
   STSORBIT.CTY so that it will be automatically available thereafter.

        Do you with to append this data to file STSPLUS.CTY (Y/n):  _

   Press "Y" or ENTER to append the data to the file, or press "N" to not 
   modify the STSPLUS.CTY file.


   F3     Set Display Features
   ---------------------------

        A number of display features may be enabled or disabled using a 
   separate sub-menu. See complete description below.

   F6     Set Map Center and Size
   ------------------------------

        The F6 command selects the size and field of view of the displayed 
   map. By default, the map is of the full world and is centered on the Prime 
   Meridian at Greenwich, England at 0 degrees longitude. (Most Americans are 
   accustomed to viewing the map centered somewhere in the Western Hemisphere, 
   and this orientation may be selected by pressing the "W" or "0" keys while 
   the map is displayed.) It is sometimes convenient to shift the map center 
   when the Space Shuttle is near the edge of the map.
        Pressing F6 will select between WORLD, QUAD, and ZOOM maps. Selecting 
   QUAD will select one of twelve Quadrant Maps showing a field of view 
   (horizontal size) of 180 degrees. Selecting ZOOM will select a Zoom Map 
   with field of view adjustable from 45 degrees to 180 degrees; the default 
   field of view is 75 degrees. The Zoom Map is approximately centered on the 
   current ground track position of the satellite. See the sections QUADRANT 
   MAPS, ZOOM MAPS, and AUTOMATIC MAP GENERATION for additional information.



   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 50


   F7     Set for SLOW COMPUTER or NO COPROCESSOR
   ----------------------------------------------

        IMPORTANT NOTE:     ALWAYS select the Slow Mode if your computer is 
                            not equipped with a math coprocessor.

                            When operating in real time, if the seconds 
                            portion of the times shown as "Local:" and 
                            "Simulation:" do not agree to within 1 or 2 
                            seconds, your computer is NOT able to maintain 
                            real time operation without the SLOW MODE!

        Press F7 to switch the SLOW MODE between "ON" and "OFF". "ON" means 
   that the SLOW MODE is active; "OFF" means normal operation.
        As features have been added to STSPLUS, it has become increasingly 
   difficult for very slow computers or computers not equipped with a math 
   coprocessor to keep up with real time orbital calculations. For example, my 
   old vanilla Zenith Z-148, operating at 4.77 MHz and no math coprocessor, 
   takes approximately 4.5 seconds to make a full set of orbital position 
   calculations; when switched to 8.0 MHz, the same calculations require only 
   2.5 seconds. In either case, the program gets hopelessly behind itself and 
   can never catch up when operated in the normal program mode.
        While perhaps not the "ideal solution" as compared to having a math 
   coprocessor, setting STSPLUS for SLOW MODE can help in all but the most 
   severe cases. Instead of attempting to update its position calculations 
   every second, the update is slowed to every ten seconds in this mode. This 
   allows the computer to more or less keep up at a cost of not having data 
   quite in real time on a second-by-second basis. Except for the frequency of 
   updates, all program features are unchanged. When STSPLUS is operating in 
   the SLOW MODE, the phrase "SLO" appears at the lower right of the tracking 
   display.
        Since STSPLUS makes no test to see if it is keeping up with real time 
   (the program cannot tell the difference between the PAUSE or SIMULATED TIME 
   modes versus REAL TIME) and since most features are available for all 
   computer configurations, it is the responsibility of the user to make sure 
   that the appropriate options have been selected. Even in the SLOW MODE, 
   certain very slow computers (such as an old XT-class computer running at 
   4.77 MHz) cannot keep up if the solar terminator is enabled when using the 
   2-line elements orbital data.


   F9     Set UTC Time Offset and Daylight Flag
   --------------------------------------------

        STSPLUS uses UTC or Coordinated Universal Time, an adjusted version 
   of Universal Time (which STSPLUS considers the same as GMT or Greenwich 
   Mean Time), for certain functions such as launch time. The difference 
   between UT, UT1, UT2 and UTC is never more than 0.9 seconds. UTC is used 
   because it is the standard for civil timekeeping and agrees with standard 
   atomic time, TDB or Terrestrial Barycentric Time, used by astronomers. 
   However, NASA continues to use the GMT designation, a holdover from earlier 
   days before the introduction of UTC. Using UTC permits critical data to be 
   used across many time zones without conversion. However, it also means that 
   STSORBIT must know what number of hours to add to UTC in order to obtain 
   your local time, and whether or not you are currently using daylight 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 51


   savings time (summer time in the UK).
        When prompted, enter the time offset in hours from your local time to 
   Coordinated Universal Time. Examples are shown for most time zones in North 
   America. STSPLUS then asks if you are using daylight savings time; enter 
   "0" if not, and "1" if so. The sum of these two values is shown on the Main 
   Menu; for example, if the computer is set to Pacific Daylight Time (UTC 
   offset is -8.00 hours and Daylight Flag = 1), the sum will be -7.00. For 
   most time zones in North America, the correct zone abbreviation will be 
   shown on the ground track display for Local date and time. When you change 
   your computer from/to daylight savings time, use this command to update 
   STSPLUS. The following shows the display when using the F9 command:


   Set UTC TIME ZONE OFFSET and DAYLIGHT FLAG

             STSPLUS must know the difference between your local time zone 
        and Coordinated Universal Time (UTC), also sometimes known as 
        Greenwich Mean Time (GMT). With this information, STSPLUS can 
        automatically adjust launch or Epoch times and dates for your local 
        time zone. In addition, STSPLUS must know if your computer is now set 
        to STANDARD or DAYLIGHT time.
             First, enter the difference between your STANDARD time zone and 
        UTC in hours. Do NOT include the hour for daylight time if you are now 
        on DAYLIGHT time; it will be entered separately. For most time zones 
        in the United States and Canada, the entries required are:

             Eastern Standard Time     EST    -5.0
             Central Standard Time     CST    -6.0
             Mountain Standard Time    MST    -7.0
             Pacific Standard Time     PST    -8.0

             Enter UTC Offset (hours):          -8
             Enter DAYLIGHT Flag (0=OFF, 1=ON): 1


        Once this information has been entered, it will be saved in file 
   STSPLUS.INI and will not be requested again. If you change from Standard 
   to Daylight Time or vice versa, use the F10+F9 command to update the 
   Daylight Flag. INI files obtained from other users may be from a prior 
   version of STSPLUS and the time information may have to be corrected.


   F10    Enable/Disable Printer Logging
   -------------------------------------
        I have found it interesting to log the orbital data and the ascending 
   and descending node information on my printer when analyzing the mission 
   data over long periods of time. The F10 command toggles the printer logging 
   function on and off. The first page of the log includes the current orbital 
   data and subsequent pages contain only node information. In addition to the 
   information presented on the display, the printer log also calculates the 
   current orbital time, the time from one ascending (descending) node to the 
   next, for the third and subsequent nodes. A typical log is shown below. 

        IMPORTANT:     BE SURE THE PRINTER IS TURNED ON PRIOR TO ENTERING THE 
                       F10 COMMAND. 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 52



   STSORBIT: Space Shuttle Tracking Program, Version 9228          Page 1

   ORBITAL DATA for STS-31 Discovery/HST

             NORAD Number:            20580
             Launch Date:             04/24/1990
             Launch Time:             05:33:52
             Orbit Inclination:       28.4695
             Orbit Altitude:         329.50 nm

             Adjust Longitude:         9.80
             Adjust Orbit Time:        8.40 min
                                                                    ORBIT
                   UT DATE   UT TIME ORBIT    LONG           MET     TIME
   Ascend Node: 04/28/1990  20:32:52    70  -69.95    4/14:58:07
   Dscend Node: 04/28/1990  21:20:52    70   97.64    4/15:46:35
   Ascend Node: 04/28/1990  22:09:52    71  -94.77    4/16:35:02  1:36:55


        When printer logging is enabled and the ground track is displayed, the 
   word "LOG" will appear in red at the right of the text area. Enabling 
   printer logging also automatically enagles the display of ascending and 
   descending node information.
        When a printer log is prepared for a satellite using 2-line elements, 
   the Adjust Longitude and Adjust Orbit Time entries will not be shown in the 
   header data. The Launch Date and Launch Time entries are given if that 
   information has been entered indepentently. The Epoch Date and Epoch Time 
   are always shown for 2-line element simulations. Note also that the orbit 
   altitude shown is the altitude at the time the log was started and will not 
   be correct for subsequent entries, especially if the satellite has an 
   elliptical orbit (high eccentricity).
        A printer log may be prepared in advance of a mission by enabling 
   printer logging from the Set Options Menu (with the F10+F10 command), 
   setting the desired simulation time (F8+F3 command), then starting the 
   ground track display with ENTER; once the ground track has appeared on the 
   screen, pressing the F key twice to set STSPLUS in the X60 fast time mode 
   will generate the date relatively quickly (although the UT TIME printed may 
   be off by as much as one minute in the X60 mode). Allow the simulation to 
   run for the desired length of time, then press ENTER to return to the Main 
   Menu. While the ground track is active Function Key F3 performs the same 
   function as the F10+F10 command to enable or disable printer logging.

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 53


   SET DISPLAY FEATURES
   --------------------

        Depending upon the satellte and personal preferences, a variety of 
   display features may be enabled or disabled. Not all features are available 
   with monochrome or CGA monitors. Pressing F3 on the Set Program Options and 
   Features Menu will display the following menu:


                                 Program STSORBIT PLUS

                     Space Shuttle and Satellite Orbit Simulation
                                     Version 9228

                      Current time:  09:42:13 PST   17:42:13 UTC
                      Current date:    04/09/1992     04/09/1992

            F1     ON      Display LOCAL Circles of Visibility
            F2     OFF     Display TDRS Coverage
            F3     ON      Display Additional Map Grid Lines
            F4     OFF     Display Tracking Stations
            F5     BOTH    Display Ground Track: DOTS/LINE
            F6     ON      Display Spacecraft Circle of Visibility
            F7     OFF     Display South Atlantic Anomaly Zone
            F8     ON      Display Terminator, SUN, and Spacecraft Lighting
            F9     NM      Select Distance Units: NM or KM
            F10    A/A     Select Satellite Coordinates: RA/DEC, Alt/Az, XYZ

            ENTER          Return to MAIN MENU

            Select desired function:


   F1     Display LOCAL Circles of Visibility
   ------------------------------------------

        Function Key F1 enables and disables the local circles of visibility, 
   centered on your location and a second location if enabled. In some 
   situations (geosynchronous satellites, for example), these circles of 
   visibility cover so large an area that they simply confuse and clutter the 
   display. Use this command to disable the circles.


   F2     Display TDRS Coverage
   ----------------------------

        This command will display the approximate communications coverage for 
   the Tracking and Data Relay Satellites (TDRS) EAST and WEST. The coverage 
   boundaries overlap between the East and West TDRS satellites and Mission 
   Control may select either satellite during the overlap period. STSPLUS 
   assumes, as is often the case, that TDRS East will be selected when it is 
   available.



   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 54


   F3     Enable/Disable Additional Map Grid Lines
   -----------------------------------------------

        This command is not available for CGA systems. The basic world map 
   includes the Equator and the meridians at 0 degrees, 90 degrees, and -90 
   degrees shown in blue on color monitors; the Equator and the prime meridian 
   are shown in bright blue. Turning on the map grid adds lines of longitude 
   every 30 degrees and lines of latitude every 10 degrees. Displaying the 
   additional grid lines on monochrome monitors usually makes the screen too 
   "busy" and is not recommended.
        In the Quadrant and Zoom Map modes, the spacing of the additional grid 
   lines is adjusted for the map field of view. For EGA and VGA systems, each 
   grid line is labeled at the left or bottom of the display screen.


   F4     Display Tracking Stations
   --------------------------------

        The F4 command enables/disables the display of the tracking stations 
   included in file STSPLUS.TRK or the current TRACKING STATION filename as 
   set by Function Key F7 on the Main Menu. If that file is not found, 
   internal data are used for NASA's 14 original ground tracking stations plus 
   the NASA Ground Terminal at White Sands, NM. Each tracking station is 
   located with a small red circle. The circle of visibility is also shown if 
   that circle has an angular diameter of 90 degrees or less. For all map 
   modes EXCEPT the World Maps, each tracking station is also labeled with its 
   3-character abbreviation. This command is not available for CGA monitors.


   F5     Show Ascending & Descending Node Data
   --------------------------------------------

        The nodes of an Earth orbit are the points on the ground track where 
   the path crosses the Equator. The ascending node crosses from South to 
   North and the descending node crosses from North to South. Orbit numbers 
   normally increment at the ascending node. This command adds two additional 
   lines of data at the lower left of the screen giving the time (MET or time 
   since epoch) and longitude of the most recent ascending and descending 
   nodes. This information is useful when comparing STSPLUS's data against 
   other sources such as the wall map in Mission Control.


   F5     Display Spacecraft Circle of Visibility
   ----------------------------------------------

        STSPLUS can calculate the approximate circle of visibility from the 
   spacecraft, the area of the Earth's surface which is visible from the 
   cockpit windows and television cameras or, for unmanned spacecraft, the 
   direct line of sight visibility from the ground. Note that the shape of the 
   "circle" varies from approximately a circle near the Equator to something 
   like a rounded triangle at higher latitudes. Near the poles, the "circle" 
   spreads out across the map. This is an artifact of the map projection; 
   plotted on the surface of a sphere, it would be a true circle.
        This feature may be enabled for all spacecraft using 2-line elements. 
   When the program is run in the normal mode, the circle of visibility is 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 55


   recalculated every 10 seconds based upon the spacecraft's current altitude. 
   This means that orbits with a high eccentricity (that is, a highly 
   elliptical orbit whose apogee and perigee are very different) will exhibit 
   a constantly changing circle of visibility. When the program is run in the 
   SLOW MODE, the radius of the circle of visibility is constant, as 
   calculated at the moment the ground track display is started. This feature 
   may also be enabled or disabled during the ground track display using 
   Function Key F7.


   F7     Display South Atlantic Anamoly Zone
   ------------------------------------------

        The South Atlantic Anamoly (SAA) is an area in the southern hemisphere 
   lying between southern tip of Africa and South America which can cause 
   severe electromagnetic disturbances on spacecraft. For example, the 
   semiconductor memory on the Hubble Space Telescope (which regularly passes 
   through the SAA) was being changed by this phenomenon until a patch was 
   uplinked to work around the problem. The area is shown on the ground track 
   as an ellipse for simplicity; its actual outline is more nearly shaped like 
   a kidney bean. Using NASA Mission Charts for various Space Shuttle 
   missions as a reference, the SAA is adjusted for spacecraft altitudes from 
   160 nm to 350 nm (although it extends out to geosynchronous orbits).


   F8     Display Terminator, Sun, and SpaceCraft Lighting
   -------------------------------------------------------

        Many types of observations, especially Earth observations, often 
   require that the target or terrain be in sunlight. The solar terminator is 
   a series of yellow points on the display which represent the line at which 
   the center of the Sun is at an observer's horizon for mean sea level. 
   Although a quick glance outside should suffice to determine which side of 
   the terminator line is in sunlight and which in darkness, EGA and VGA 
   systems also display the Sun as a small yellow circle. The terminator is 
   partially updated every 10 seconds (and is fully updated every 60 seconds) 
   and the sun is updated every 60 seconds. Because of the additional 
   calculations and plotting required, these solar features may not be 
   suitable for slow processors or computers without a math coprocessor. NOTE: 
   Only the terminator is available with CGA systems.
        The terminator is sometimes confused with a line denoting sunrise and 
   sunset. Two factors make the terminator only an approximation: first, the 
   terminator is based upon the center of the Sun, while sunrise and sunset 
   are based upon the upper limb of the Sun; and second, the terminator is 
   calculated for mean sea level rather than a specific local elevation. These 
   two factors combined can result in a difference of ten minutes or more when 
   the times are compared against published values or those calculated by my 
   program ASTROCLK, sunrise being earlier and sunset being later.
        The performance of solar panels and certain other instruments on a 
   spacecraft is dependent upon whether or not the Sun is in view. Similarly, 
   it is usually impossible to visually see a spacecraft which is not in 
   sunlight. STSPLUS calculates whether the spacecraft is in full sun, 
   penumbra (partial shadow) or refracted sunlight, or umbra (full shadow) and 
   adjusts the color of the spacecraft icon accordingly: bright white, yellow, 
   and dim white respectively. This feature is not available on CGA and HGC 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 56


   monitors. Note also that the spacecraft lighting is indicated by an 
   asterisk ("*") next to the "Orbit #"; the asterisk is present when the 
   spacecraft is in full or partial sunlight and is absent otherwise.


   F9     Select Distance Units: NM or KM
   --------------------------------------

        Spacecraft altitude, range, and satellite geocentric rectangular 
   coordinates (X, Y, and Z) may be expressed in either nautical miles (nm) or 
   kilometers (km). This feature selects which units will be displayed for 
   those data.


   F10    Select Satellite Coordinates: RA/DEC, AltAz or XYZ
   ---------------------------------------------------------

        This feature selects between topocentric (horizon) coordinates 
   (referenced to the Earth's surface and in this case the current local 
   geographical coordinates), equatorial coordinates for the satellite's 
   position (Right Ascension and Declination), or geocentric rectangular 
   coordinates (X, Y, and Z, referenced to the center of the Earth). Press F10 
   until the desired coordinate system is selected. The abbreviations "R/D", 
   "A/A", and "XYZ" are used on the menu. You may also use Function Key F10 to 
   switch between coordinate systems while the ground track display is in 
   progress. NOTE: The geocentric rectangular coordinates are only available 
   when using 2-line orbital elements.
        For most purposes, such as aiming an antenna or visually spotting the 
   satellite, the horizon coordinates of Altitude and Azimuth are desired. If 
   you wish to determine the star background, however, the equatorial 
   coordinate system of Right Ascension and Declination (referenced to the 
   epoch of date) is needed. For both of these coordinate systems, the range 
   from the current local coordinates to the satellite is also given, 
   expressed in either nautical miles or kilometers as selected by F9 above.

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 57


   STSORBIT PLUS'S ORBITAL MODELS
   ------------------------------

        The original version of STSORBIT was first prepared without reference 
   materials of any kind and the simplest possible orbital model was therefore 
   selected. The primary objective was to duplicate the NASA wall map at 
   the Mission Control Center in Houston, Texas. This "simple" model assumed 
   that the orbit was perfectly circular at a specified altitude and 
   inclination which never degraded due to other factors such as drag or 
   perturbation. Some simplifying assumptions were incorporated to handle the 
   initial ascent portion of a mission and the launch site was hard coded to 
   Cape Canaveral, Florida. With only minor modifications, the program was 
   essentially unchanged for the next year.
        The launch of STS-31 and the Hubble Space Telescope highlighted the 
   need for improved accuracy because of public interest and the length of the 
   mission. The orbital calculations were modified (STSORBIT Version 9015) to 
   include the J2 factor, the perturbation of low Earth orbits due to 
   variations in the gravitational field related to the non-spherical shape of 
   the Earth (among other factors); omission of the J2 factor caused errors in 
   longitude of approximately -5 to -7 degrees per day. That is, the orbital 
   track drifted Westward from its true position by that amount. More accurate 
   models of low orbits also include the J3 and J4 perturbation factors, 
   atmospheric drag, and a host of other less significant items.
        Although by now reasonably accurate for the first day or so of a space 
   shuttle mission, the "simple" model is by no means ideal. In calculating 
   the current orbital longitude, for example, the "simple" model assumes a 
   circular orbit. For orbits with low inclinations, as is typical for 
   launches from Kennedy Space Center, the errors are not particularly 
   significant and are probably overshadowed by the fundamental uncertainties 
   in orbital parameters and by the limitations imposed by display resolution. 
   Orbits with higher inclinations, as would be the case if near-polar 
   launches from Vandenburg AFB in California are ever initiated, would have 
   much larger periodic errors which would be both noticeable and 
   objectionable. More important for longer missions and for general satellite 
   tracking is the fact that due to the method used, errors in the orbital 
   calculations tend to be cumulative. Although it may be the only method 
   available at launch, after about a week the errors can become unacceptably 
   large.
        The real problem with the simple method, of course, is that the Earth 
   is not a perfect sphere and actual satellite orbits are never perfectly 
   circular. Satellite orbits are significantly perturbed by the non-spherical
   gravitational field of the Earth, by the Sun and Moon, atmospheric drag, 
   and other factors. Accurate satellite tracking over longer periods of time 
   therefore demands more accurate data and a more rigorous treatment of 
   satellite orbits. The only practical alternative is to use the NASA/NORAD 
   2-line orbital element sets. Not only are these data readily available 
   publicly, but they are relatively accurate and are updated regularly. 
   Therefore, STSORBIT PLUS, while retaining the capability of using the 
   simple orbital model (primarily for demonstrations), relies on the 2-line 
   element sets for orbit predictions. 2-line element sets for non-military 
   space shuttle missions are typically available on the same day as the 
   launch. Amateur astronomers and satellite tracking experts often generate 
   "unofficial" 2-line element sets even for military missions.
        Six quantities are required by classical gravitational theory to 
   completely characterize the orbit of one body about another in time and 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 58


   space, the "Two Body Problem". These six quantities, often referred to as 
   Keplerian orbital elements, are included in the NASA/NORAD 2-line element 
   sets along with other numerical and statistical data. NORAD, the North 
   American Air Defense Command headquartered in Cheyenne Mountain, Colorado, 
   (and now known as the U. S. Space Command) developed the 2-line element 
   format many years ago as part of their satellite tracking efforts and NASA 
   subsequently adopted the same format -- more or less. My own analyses of 2-
   line element sets obtained independently from other NASA centers indicate 
   that NASA and NORAD do not always use the same definition for revolution 
   (orbit) numbers; NASA frequently gives a number one greater than NORAD, 
   calling the first partial orbit number one while NORAD calls that same 
   partial orbit number zero. Except for short duration missions, such as the 
   Space Shuttle, revolution numbers are of no practical importance.
        Having timely and accurate orbital data is of little help without a 
   computer model or program which can use those data. NORAD has rather 
   arbitrarily divided satellite orbits into two categories: near Earth orbits 
   and deep space orbits. Near Earth orbits are defined as those with orbital 
   periods of 225 minutes or less and deep space orbits are all others. 
   Computer models are described in the literature for each category. STSORBIT 
   PLUS employs the SGP4 Near Earth Model only, using a composite of code of 
   my own combined with translated Fortran and Basic source supplied by Paul 
   Traufler and C source by Paul Hirose. Not only are the near Earth orbits 
   generally of more interest to observers, but the errors associated with 
   deep space orbits processed with the SGP4 model (rather than the correct 
   SDP4 model) are not particularly significant for the purposes of a program 
   such as STSORBIT PLUS. Further, watching a geostationary satellite orbit on 
   the screen is not unlike watching grass grow and is about as exciting.
        For the past several years, T S Kelso has been making the NASA/NORAD 
   data available as a public service on his Celestial BBS at (513) 427-0674. 
   The 2-line element sets are prepared by Kelso using data received directly 
   from NORAD by special arrangement. I regularly post a slightly edited 
   version of the current element sets on my own RPV ASTRONOMY BBS as file 
   NASAnnn.TXT, where "nnn" is the NASA Prediction Bulletin number. Kelso 
   provides data for several categories of satellites:  Amateur Radio, Earth 
   Resources, Manned Spacecraft, Navigation, Weather, and NASA's 30 Day 
   Specials (which contain objects launched within the last 30 days and are 
   often easy to spot visually). More specifically, these include the 
   following satellites or satellite series: OSCAR, Radio Sputnik, UOSAT, 
   Cosmos, LandSat, SeaSat 1, SPOT, Mir, Salyut 7, Soyuz, Space Shuttle, 
   NAVSTAR (GPS), GOES, Meteor, and NOAA.
        The Canadian Space Society BBS, (416) 458-5907, also regularly posts 
   NORAD 2-line elements. Note that the CSS format is slightly non-standard, 
   having additional information on the first (title) line for each satellite, 
   and may have to be edited for use with some tracking programs. The CSS 
   files also have considerable additional text material (including current 
   satellite news) before and after the actual 2-line elements data.
        Finally, the NASA SpaceLink BBS in Huntsville, Alabama, (205) 895-
   0028, 8 lines @ 300-9600 baud, provides mission information for all space 
   shuttle missions and current 2-line orbital elements both pre-mission and 
   while a mission is in progress. In addition, SpaceLink has a wealth of 
   other NASA information.

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 59


   ADJUSTING ORBITAL PARAMETERS (Simple Orbital Model)
   ---------------------------------------------------

        NOTE: This section applies ONLY if you are using the simple orbital 
        model for simulation. When using 2-line elements, all orbital 
        parameters are completely defined by the 2-line elements and may not 
        be modified from within STSORBIT PLUS. For accurate satellite 
        tracking, obtain 2-line elements from my BBS or elsewhere.

        The original "simple" orbital model used in STSPLUS is imperfect, to 
   say the least. The data generally available from NASA prior to launch often 
   does not describe upcoming shuttle orbits at all precisely. In particular, 
   STSPLUS's initial orbital calculations, those related to the time from 
   liftoff to orbital insertion, are more or less guesswork. Once a mission is 
   established in orbit, it may be therefore desirable to adjust the orbital 
   parameters to make STSPLUS's displayed ground track correspond more closely 
   to that displayed on the wall map in Mission Control Center. To make the 
   adjustment, use the following procedure:

   1.   Start program STSPLUS. After the map data has been read in, select the 
        program options command, F10, then press F5 to enable display of the 
        data for the ascending and descending nodes. Enter the original launch 
        time and orbital data using the F4 command or restore prior data using 
        the ENTER key or F3 command if no adjustments have been entered. The 
        plot will appear on the screen.

   2.   Observe the crossing time and longitude of the node of interest and 
        calculate the difference from the desired crossing time. Note that 
        NASA performs all orbital calculations referenced to the Ascending 
        Node, the point at which the ground track crosses the Equator in a 
        North-bound direction. In order to view a given node crossing 
        repeatedly, you may find it convenient to reset the DOS clock to a 
        minute or two prior to the expected time.

        HINT: Use the F9 command to go back to DOS, then use DOS's TIME 
        command to set the clock. BE SURE TO RESET YOUR COMPUTER CLOCK WHEN 
        YOU HAVE COMPLETED ALL ORBITAL ADJUSTMENTS!

   3.   When adjusting orbital parameters, it is preferable to adjust the TIME 
        before adjusting the LONGITUDE. This is because the longitude of the 
        node is affected by the rotation of the Earth (by 15 degrees per hour) 
        when the time is changed. Calculate the difference between the time of 
        the observed node crossing and the time of crossing plotted by 
        STSORBIT. If the observed time is earlier than the plotted time, the 
        time adjustment must be positive, otherwise it must be negative. The 
        time must be calculated in minutes and decimal fractions of a minute.

   4.   Press ENTER to return to the Main Menu, then press F5 to enter 
        adjusted data. Enter the new orbital altitude in nautical miles (or 
        altitude in kilometers by adding "km"); usually, the orbital altitude 
        has not changed and you should press ENTER to leave this item 
        unchanged.

   5.   Press ENTER to leave the longitude adjustment set at zero.


   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 60


   6.   Enter the calculated time difference for the node crossing as the time 
        adjustment (in minutes).

   7.   Press ENTER to leave the launch time unchanged.

   8.   Inspect the data displayed to be sure it is correct. If it is not, 
        press the SPACE BAR to re-enter data; if it is correct, press ENTER to 
        accept the data. STSPLUS will immediately begin plotting the new 
        ground track. If necessary, interrupt the plot with the ENTER key, 
        reset your computer's clock, return to STSPLUS, and press ENTER to 
        resume current mission.

   9.   Again observe the plotted time of crossing and repeat from Step 4 if 
        the time is not correct. If the time is correct, note the longitude of 
        the node and calculate the difference from the observed longitude. If 
        the plotted longitude is less than the observed longitude, the 
        adjustment must be positive, otherwise it must be negative. The 
        longitude adjustment must be entered in degrees and decimal fractions 
        of a degree.

   10.  Press ENTER to return to the Main Menu, then press F5 to enter 
        adjusted data. Enter the calculated longitude adjustment, then press 
        ENTER twice to leave the time adjustment and launch time unchanged.

   11.  Inspect the data displayed to be sure it is correct. If it is not, 
        press the SPACE BAR to re-enter data; if it is correct, press ENTER to 
        accept the data. STSPLUS will immediately begin plotting the new 
        ground track. If necessary, interrupt the plot with the ENTER key, 
        reset your computer's clock, return to STSORBIT, and press ENTER to 
        resume current mission.

   12.  This procedure should enable you to set the orbital parameters with 
        considerable accuracy. However, even minor changes of the orbit in 
        flight can cause a significant cumulative error in the ground track 
        displayed by STSPLUS. If all this seems like too much effort, just 
        enjoy the program "as it comes from the box"!

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 61


   STSORBIT PLUS Revision History
   ------------------------------

         Each released version of STSPLUS uses a four digit revision code such 
   as 9218. The first two digits indicate the year and the second two digits 
   indicate the week of the year. In some cases, an additional letter suffix 
   is added to distinguish changes occurring within the same week or to 
   identify special versions. A partial week at the beginning or end of the 
   year is counted as a full week. Using this method, a year will typically 
   have 53 weeks although it is possible to have 54 weeks in a leap year (1972 
   is an example). The current year-week revision code is shown on the Julian 
   Date display, Display Mode 7, in my program ASTROCLK.
        This file records the revision history of program STSPLUS through all 
   of the minor twists and turns that usually accompany the evolution of such 
   a complex program.  It illustrates the tortuous process of maintaining and 
   refining a program as ideas and problems are reported from every quarter. 
   These notes may also be helpful to users who are upgrading from one version 
   to another to find out what has changed.

                                                 David H. Ransom, Jr.


   Version 9228A -- July, 1992
   ---------------------------
   -In response to many user requests, I have improved the 2-line elements 
   file directory functions using F2 from the Main Menu. The list of available 
   files is now alphabetized and you may use the ARROW KEYS to move through 
   the list. The selected file is highlighted and is shown as the new default 
   file. See the section "F2  Read NASA/NORAD 2-Line Elements" for a complete 
   explanation.
   -Corrected a bug that displayed the incorrect city label for the primary 
   location if the Location Map for the second location was last displayed. 
   Thanks again to Joel Runes for spotting this one!
   -Corrected a minor bug that caused the "BAD CHECKSUM ..." error message to 
   scroll off the screen when reading 2-line elements (F2). The message now 
   appears in RED following the File Record Number.


   Version 9228 -- July, 1992
   --------------------------
   -Fixed bug when too many .TXT files were present and the list overflowed 
   the available screen columns and aborted with "BASIC PDS Error 5". The file 
   listing now stops when the screen is full (and some files may therefore NOT 
   be displayed).
   -Changed screen mode for EGA and VGA monitors to use 43 or 50 lines for 
   display of available .TXT files. Screen returns to 25 lines after file 
   search. This slows the display slightly but greatly increases the number of 
   files that may be displayed on EGA and VGA systems.
   -Fixed bug associated with help screen (F1 with the map displayed) which 
   caused big clocks to overwrite the help information and then display only 
   changed digits when F1 was pressed again.
   -Changed the satellite elements data display shown when selecting 2-line 
   elements to add the acceleration/drag and to move the Element Set Number to 
   the top of the data for clarity.
   -Changed colors for satellite position data (Range, Altitude, Azimuth, etc. 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 62


   at the right of the data block) such that when the satellite is in view of 
   the current location, the color is LIGHT GREEN, otherwise YELLOW (all map 
   modes except TRACKING STATION) or LIGHT RED (TRACKING STATION).
   -Corrected Location Map so that the primary location and name are displayed 
   when the map is centered on the secondary location.


   Version 9227C -- June, 1992
   ---------------------------
   -This version NOT released publicly.
   -The Big Clock mode has been added for all display monitors -- for those of 
   us who want big characters due to impaired eyesight. This displays UTC date 
   and time, Local date and time, or MET/T+Epoch in large characters and is 
   enabled by Function Key F2 (see following item).
   -Changed the operation of Function Key F2 while map is displayed. Instead 
   of controlling the satellite blink (which may now only be controlled by the 
   "B" key), F2 now selects the Big Clock mode. The Big Clock modes are 
   selected in the following order:
        0    No clock displayed
        1    UTC date and time
        2    Local date and time
        3    MET or T+Epoch (select with F5)
   -Note that not all computers (especially older CGA systems) will display 
   the extended graphics characters used for the large clock characters. The 
   symptom of this problem is that the lower left portion of the data block is 
   mostly blank after pressing F2. If you have this problem and your computer 
   is running DOS 3.x or DOS 5.0, enter the command "GRAFTABL" at the DOS 
   prompt before running STSPLUS or include the line "GRAFTABL" in your 
   AUTOEXEC.BAT file; this sets the "code page" to enable the computer to 
   display the extended graphics characters. [The program GRAFTABL.COM is 
   included as part of DOS in most cases.]
   -Changed the extended clock feature to use command line option "/CLK" 
   instead of "/60". In this mode, the text portion of the map display uses 43 
   (EGA) or 60 (VGA) lines instead of the normal 25 lines and positions the 
   clocks below the normal data block. This feature now operates correctly on 
   both EGA and VGA systems but when enabled, the Motion Map is disabled.
   -Various minor cosmetic changes.


   Version 9227B -- June, 1992
   ---------------------------
   -Corrected persistent bug present in Versions 9226/9227/9227A which caused 
   the program not to recognize Hercules (HGC) monitors even after MSHERC was 
   executed. Thanks to Roger Guilemette for reporting the problem.
   -Corrected problem when second location was present and displayed on the 
   Location Map. Switching back to World/Quadrant/Zoom maps gave altitude and 
   aximuth data for second location instead of standard location.
   -Corrected Location Map for second location to remove overprinting of the 
   local name on top of the second location's name. Thanks to Joel Runes!
   -Moved location names to above location in the Location Map to avoid 
   overprinting the altitude data.
   -Added circle of visibility for second location (if present).
   -Modified the block number "5" so as not to be confused with "6".
   -Various minor cosmetic repairs.


   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 63



   Version 9227A -- June, 1992
   ---------------------------
   -This has NOT been a good day. Just as soon as I released Version 9227, 
   another bug was reported. Versions 9226 and 9227 will not execute on an EGA 
   system, reporting that they do not recognize the monitor type. This has now 
   been repaired. Thanks to Roger Pettengill for reporting the problem!


   Version 9227 -- June, 1992
   --------------------------
   -Removed a "Clear Screen" that caused the MOTION MAP not to work in Version 
   9226. It never fails that I seem to break something while fixing something 
   else. For some reason, that got missed in testing ... sorry!
   -The standard program version now can be used in Read/Only Networks. Set up 
   the program the way you wish, then edit STSPLUS.INI so that the version 
   number on the first line is negative, e.g. "-9227" instead of "9227". With 
   the STSPLUS.INI file set up this way, the program will NEVER write a new
   Remind users to use the command line "STSPLUS /R" for immediate startup.
   -As an experimental test, VGA users ONLY may include the command line 
   option "/60" to force 60-line mode and display a large clock at the bottom 
   of the data block. (Not yet configured for use with the Motion Map!!)


   Version 9226 -- June, 1992
   --------------------------
   -Corrected (I think) a problem in zoom mode which caused the program to 
   hang on startup using the command "STSPLUS /R" if the time was prior to the 
   time of epoch. Thanks to Joel Runes for reporting this one!
   -Corrected a bug with higher inclination orbits which caused the map to be 
   redrawn repeatedly near the poles. I've only seen the problem with orbit 
   inclinations greater than 60 degrees AND with automatic map generation 
   enabled. The problem was related to the map centering and map projection.
   -By popular request, I've restored the "feature" which allows the user to 
   interrupt map drawing by pressing ENTER. This slows down map drawing 
   slightly but so many folks have complained since I removed it ...
   -Corrected the circle of visibility algorithms to correctly plot circles 
   which overlap a pole. The "overlap" portion of the circle appeared near the 
   opposite pole instead of where it belonged! Thanks to Don Nicholson for 
   pointing out the error!
   -Because of frequent user complaints, setting fast time (X10 or X60 using 
   F4 while the map is displayed) will now disable automatic map generation. I 
   recommend using fast time ONLY on the world map, or using it when PAUSE is 
   enabled. Press TAB to restore automatic map generation.
   -Changed the algorithm for calculating orbit numbers to account for the 
   drag and other effects that caused the orbit number calculation to fall 
   behind by approximately 0.1 orbits every 15 days (measured from the Epoch 
   of the elements) for satellites in low Earth orbits. The "new and improved" 
   algorithm is now accurate to better than 0.01 orbits when the simulation is 
   started for either real or simulated time (SLOW MODE not enabled).
   -If the SLOW MODE is enabled, the new orbit number algorithm is only used 
   when elements are loaded ("/R" command line option or F2 from the Main 
   Menu) to avoid additional processor delays. In SLOW MODE, the initial 
   calculation is done once for real time and some error will be noted in the 
   orbit number if simulated time is set days different from real time.

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 64


   -Corrected a 1 pixel vertical error in plotting which occured under certain 
   circumstances. The TDRS satellites, for example, were sometimes plotted 1 
   pixel above the equator.
   -Improved the map centering logic to avoid an occasional incorrect map 
   center (usually quadrant maps) which was followed by an immediate redraw.
   -Improved ascending and descending node logic to (hopefully) eliminate 
   spurious data which was displayed under certain circumstances.
   -Fixed a minor bug in printer output where five digit orbit numbers were 
   incorrectly displayed as "%11007" instead of "11007".
   -In response to user requests, I have added an additional status message, 
   "Recalculating Map and Position data ...", which appears on what was 
   previously a blank screen before the actual map is drawn. The message 
   doesn't even appear on my 486/33 but is visible for about 15 seconds on a 
   vintage 8MHz 8088 with no coprocessor.
   -Repaired a minor bug that set the default satellite name to the last 
   satellite found in a file when the satellite being searched for was not 
   found. The original satellite default name is now restored correctly.
   -Repaired the demo (F1 on the Main Menu) so the correct mission name and 
   icon are used. The "countdown" may now be terminated with ENTER.
   -The format of the data printed with the LOG function has been changed to 
   avoid numeric overflow of the ORBIT field and the columns changed. The 
   NORAD number has been added to the initial data block.
   -Only minor updates and changes to the main documentation.


   Version 9219 -- April, 1992
   ---------------------------
   -Version 9219 corrects a minor bug in the circles of visibility for the 
   user's location, the alternate location, and the tracking stations. These 
   circles were incorrectly shaped in Version 9218 due to a minor error in the 
   formula that crept in during testing. (The circle of visibility for the 
   spacecraft was correctly shaped and all numerical data was correct.)
   -Versions 9204 through 9218 ignored bad checksums in 2-line elements but 
   did not read the data correctly. This has now been repaired and a bad 
   checksum on either data line is reported but otherwise ignored and the data 
   read correctly.
   -Several minor typos were corrected in this documentation.


   Version 9218 -- April, 1992
   ---------------------------
   -Version 9218 is the initial formal release of program STSORBIT PLUS and 
   now includes complete program documentation. The beta releases included 
   only update notes to the original STSORBIT 9134 documentation. While the 
   STSORBIT PLUS documentation borrows heavily from that original STSORBIT 
   documentation, many sections are new or have been rewritten and updated.
   -I had planned to modify STSPLUS for dual satellite operation but this 
   proved more difficult than expected. After many hours of work, I have put 
   that feature aside, at least for the present. The basic structure of the 
   program does not lend itself to multiple satellites; this is particularly 
   true of the multi-layered graphics features. The processor workload was 
   also increased substantially, making things even more difficult for the 
   many users without a math coprocessor chip. Finally, given the other 
   demands on my time, a complete rewrite from scratch would simply require 
   too long. I'm sorry to disappoint those who asked for that feature ... 

   Program STSORBIT PLUS Satellite Orbit Simulation                   Page 65


   especially the folks working on Mission STS-49.
   -In order to eliminate problems due to changes from one program version to 
   another, STSPLUS now ignores all data from different versions of file 
   STSPLUS.INI and the program must be initialized as if being run for the 
   first time. Only .INI files written by the same program version will be 
   accepted. Trying to maintain backward compatibility with all prior versions 
   of the .INI file has become both difficult and time consuming -- and has 
   not always been successful. Too many problem reports have been due to 
   corrupt or incompatible .INI files, sometimes from versions dating back 
   several years.
   -There have been many changes from Beta Version 9206, too many to describe 
   in detail here. Even "seasoned users" of STSPLUS should check this 
   documentation carefully!


   Beta Versions 9139 thru 9206
   ----------------------------
   -Beta versions released for testing and comment. Version numbers included 
   9139, 9145, 9146, 9148, 9202, 9203, 9204, and 9206. Significant changes and 
   improvements were incorporated in these releases, often the result of user 
   feedback. Many thanks to those who sent in bug reports and suggestions!


   Beta Version 9137 -- September, 1991
   ------------------------------------
   -Initial public beta version.