System Monitor Version 2.1

                      Copyright 1991 all rights reserved
                     Rosenthal Engineering, 3737 Sequoia
                        San Luis Obispo, CA USA 93401


     --------------------------------------------------------------------
             System Monitor - Monitor and report problems early.
     --------------------------------------------------------------------

   What is System Monitor?

   System  Monitor is a program that installs in your IBM PC/XT/AT  386  or 
   486  Compatible  computer to test and extensively monitor  a  number  of 
   performance indicators. Each time you use your computer, System  Monitor 
   re-evaluates  the  system and alerts you to any discrepancies  it  finds 
   with an announcement that is hard to ignore.

   You  install  System  Monitor  as soon as  you're  confident  that  your 
   computer is configured and operational. From then on System Monitor will 
   intervene  immediately  upon detecting problems, usually long  before  a 
   user  even suspects any difficulty. This early monitoring and  detection 
   is  essential  in  avoiding  and correcting  problems  before  they  can 
   compound.

   System Monitor also supports the optional Rosenthal Engineering Hardware 
   circuit  board. This circuit card installs directly within the  computer 
   and affords System Monitor access to a number of additional  monitoring, 
   security and anti-virus functions. 

          -    -    -    -    -    -    -    -    -    -    -    

   What Does System Monitor Do?

   The first time you run System Monitor it will guide you through a simple 
   installation    procedure   and   then   generate   extensive    reports 
   (REPORTSM.EXE)   unique  to  your  computer  a   report   (CONFIGSM.EXE) 
   containing information about your system configuration file (CONFIG.SYS) 
   and AUTOEXEC.BAT file (AUTOSM.EXE). 

   The REPORTSM.EXE, AUTOSM.EXE and CONFIGSM.EXE are referred to by  System 
   Monitor from then on.

   The  information  contained  in  these  files  is  very  valuable   when 
   attempting  to  resolve conflicts especially when you  request  customer 
   support assistance for products supplied by a number different  vendors. 
   Much  of  the information in these files is encrypted  to  protect  them 
   against  corruption (whether accidental or intentional) and  deals  with 
   System  Monitors formidable anti-virus protection, however you can  view 
   much  of  the more public information by simply entering their  name  as 
   these file are also directly executable. 


   If  you have the optional Rosenthal Engineering hardware circuit  board, 
   System Monitor will add direct hardware security control to your system, 
   including  formidable  password protection limiting access  to  your  of 
   computer and sensitive data. 

          -    -    -    -    -    -    -    -    -    -    -    

   How Does System Monitor Work?

   Because  you  install System Monitor prior to developing  problems,  the 
   report  files (REPORTSM.EXE, CONFIGSM.EXE and AUTOSM.EXE)  generated  at 
   that  time  provide  a  detailed  base  line  for  comparison.  Abnormal 
   deviations from the established base line cause System Monitor to  issue 
   a  warning message. In most cases both the current monitored  value  and 
   the original base line information are displayed for comparison. For  an 
   example of some of these warning messages refer to the /D  demonstration 
   mode section.

   Many of the current viruses have mechanisms to help them avoid infection 
   detection  and  prevention  schemes so System  Monitors  anti-virus  and 
   security  methods are encrypted and will not be disclosed.  When  System 
   Monitor discovers a virus contamination or its effect, a warning will be 
   issued. Again refer to the /D demonstration mode for examples.

   Because  the  optional  Rosenthal Engineering  hardware  board  directly 
   accesses  the  computer hardware through the single short card  slot  it 
   occupies  within  your  computer,  System  Monitor  can  provide  direct 
   hardware  monitoring  which is otherwise  inaccessible.  System  Monitor 
   works  with  or without the hardware board. The hardware board  is  only 
   needed  if you require it's additional security and restricted  password 
   protected  access,  or your data is of a sensitive nature, or  you  have 
   reason  to believe your computer to be vulnerable to a hostile  software 
   or operator environment.

          -    -    -    -    -    -    -    -    -    -    -    

   How will System Monitor support other protection schemes?

   There are a number of excellent anti-virus programs that interface  well 
   with  System  Monitor  including (but certainly not  limited  to)  those 
   available  from Microcom (919) 490-1277 or McAfee Associates  (408)-988-
   0411. These programs can be installed ahead of System Monitor. With this 
   configuration a virus that attempts to disable either of these  programs 
   will  have  the very Herculean task of disabling or  circumventing  them 
   both or risk detection by the other. 

   In  addition to the optional Rosenthal Engineering hardware board  which 
   intervenes between the computers ROM bios and DOS, even before the  boot 
   sector is read. There are a number of password security cards  available 
   from  other sources that System Monitor will support. If an  attempt  is 
   been  made to bypass a computers access restriction by removing  one  of 
   these security cards, System Monitor reports its absence.




          -    -    -    -    -    -    -    -    -    -    -    

   Installation

   System  Monitor should be installed after your system is configured  and 
   completely  operational.  System  Monitor is designed  to  be  installed 
   before  you  develop problems. Your CONFIG.SYS  and  AUTOEXEC.BAT  files 
   should already be configured for your system. 

   If your system has a clock (most do) make sure the time and date are set 
   correctly before continuing.  Erratic clock behavior is often a sign  of 
   other problems (such as impending death your configuration ram  battery) 
   and  it's one of the things System Monitor evaluates. It's all right  to 
   use  DOS TIME and DATE functions to check the time and date, but not  to 
   set  them.  Use  your SETUP program to set the correct  time  and  date, 
   otherwise your system may not retain the correct settings when you  turn 
   off the power.

   Copy System Monitor to the ROOT directory of your BOOT drive where  your 
   AUTOEXEC.BAT and CONFIG.SYS files are.

   Enter SysMon at the DOS prompt and System Monitors built in editor  will 
   allow you to install SysMon.EXE into your AUTOEXEC.BAT file. You  should 
   add  SysMon.EXE near the end of your AUTOEXEC.BAT file after  any  TSR's 
   and before applications or Windows. 

   System Monitor will then "WARM BOOT" the system and conduct an extensive 
   series of tests before generating several report files. The report files 
   are  displayed  confirming  installation. These report  files  are  only 
   displayed  automatically when they are first created. From then  on  you 
   can  recall  them by entering REPORTSM, AUTOSM or CONFIGSM  at  the  DOS 
   prompt.
   
   Installation   is   now  complete  and  System  Monitor   will   operate 
   automatically each time the system is turned on or BOOTed.

          -    -    -    -    -    -    -    -    -    -    -    

   Demonstration Mode /D

   System  Monitor will normally operate a few seconds when you first  turn 
   on  the system without finding anything wrong. To demonstrate a  few  of 
   the tests being monitored enter SYSMON /D  at the DOS prompt. 

          -    -    -    -    -    -    -    -    -    -    -    

   Warning Messages 
   
   When  System  Monitor discovers a discrepancy, it will issue  a  Warning 
   announcement  (try the /D demonstration mode for an  example).  Remember 
   these  are only warnings. Often these warnings can easily  be  accounted 
   for. For example, installing a new device driver or version of DOS  etc. 
   When this happens just erase the report file REPORTSM.EXE and reBOOT the 
   system. System Monitor will then re-evaluate the system and create a new 
   REPORTSM.EXE unique to your system and its new configuration.

   Some  warning  messages will not require any attention to  correct.  For 
   example, a warning message caused by setting the clock back for daylight 
   savings  time.  System  Monitor will figure out  that  the  problem  has 
   corrected itself when the clock advances normally again.

   Optional Service Referral Message

   System administrators, service organizations and consultants can include 
   an  optional  text  message. When an ascii  text  file  (SYSMON.TXT)  is 
   included in the root directory, it will be displayed at installation and 
   when ever System Monitor issues a warning message. 

   The  SYSMON.TXT file is optional and allows users to receive a  referral 
   message  when assistance may be required. A SYSMON.TXT file is  included 
   as  an  example.  This  file can be deleted, or  edited  with  a  ("non-
   document") text editor to display your own personalized announcement.  

   Scheduled Preventive maintenance

   The  best  way  to  minimize  computer down  time  is  with  a  periodic 
   preventative   maintenance  schedule.  Inspection   checks,   cleanings, 
   lubrication etc. must be performed regularly to be effective. Every  six 
   months  is generally acceptable for most offices with  some  adjustments 
   made  for hostile environments or where systems are more heavily  relied 
   upon.  System Monitor will issue a reminder warning when maintenance  is 
   scheduled if that option is selected. 

   Monitoring TSR's

   System  Monitor returns all the memory it uses back to the  system  when 
   it's finished. It leaves nothing behind as a TSR program (terminate  and 
   and  stay  resident). Since System Monitor runs at power up  (from  your 
   AUTOEXEC.BAT) after your authorized TSR's where installed it will report 
   any  that  where  unauthorized or installed since then,  whether  by  an 
   application  or a virus. You can re-evaluate the system at any  time  by 
   entering SysMon once again at the DOS prompt. 

          -    -    -    -    -    -    -    -    -    -    -    

   Printing Warning Messages

   To  toggle  the  printer  ON or Off enter <CTRL>  P  .  Check  your  DOS 
   reference for Details. Then enter SysMon at the DOS prompt. 

          -    -    -    -    -    -    -    -    -    -    -    

   Speech or Beep Mode /S

   System  Monitor  evaluates  a  number  of  performance  indicators  that 
   directly  access the computers hardware. Some (a very few)  systems  may 
   have  compatibility  problems  in this area. If you have  one  of  these 
   comparatively  rare  systems  you  may  have  noticed  other   problems, 
   especially  with programs that produce sounds. If at all  possible,  you 
   should  not disable the speech and additional hardware tests unless  the 
   system just won't run any other way. Before disabling the speech, try to 
   run  System Monitor normally first. To disable the  additional  hardware 
   performance tests and replace the speech with a beep, reBOOT the  system 
   and press <CTRL> <BREAK> to abort the AUTOEXEC.BAT routine before SysMon 
   is called. Use your (Non-Document) editor to add  /S to the command line 
   following the SysMon.EXE.

          -    -    -    -    -    -    -    -    -    -    -    

   DOS Version

   System Monitor requires DOS version 2.0 or higher.


          -    -    -    -    -    -    -    -    -    -    -    



                            Shareware Announcement


   Please feel free to use and evaluate this software without charge for 30 
   days.  You are encouraged to copy and distribute it freely  provided  it 
   remains  unmodified,  complete in it's original form and no  fee  (other 
   than  a nominal copy charge) is required. This software is provided  "as 
   is" without warranty either expressed or implied.

   System  Monitor is fully functional and not copy protected  or  crippled 
   (other  than  the  shareware announcement).   If  you  determine  System 
   Monitor to be useful, you must register it before the end of the 30  day 
   evaluation period. 

   Once  the required registration fee are received, the latest  registered 
   version of System Monitor (without shareware announcement) will be  sent 
   by priority first class mail.

                          Software License agreement

   This Software is copyrighted material. It is not sold, but licensed. The 
   registration  fee must be paid before the free 30 day evaluation  period 
   expires or its use discontinued.  

   You  are encouraged to copy and distribute only the unregisterd  version 
   freely  provided it remains unmodified, complete in it's  original  form 
   and no fee (other than a nominal copy charge) is required. This software 
   is provided "as is" without warranty either expressed or implied.

   You  may not make any changes or modifications to the software  and  you 
   may  not  decompile,  disassemble  or in  anyway  reverse  engineer  the 
   software. 

   This  constitutes  the entire agreement and  understanding  between  the 
   parties and supersedes any prior agreement or understanding whether oral 
   or written and may only be modified in writing.

   This  software  is  provided "as is" without  warranties  of  any  kind. 
   Responsibility rests entirely with the user to determine its fitness for 
   a  particular  purpose. ROSENTHAL ENGINEERING SHALL NOT IN ANY  CASE  BE 
   LIABLE FOR SPECIAL, INCIDENTAL, CONSEQUENTIAL, INDIRECT OR OTHER SIMILAR 
   DAMAGES ARISING FROM ANY USE OF THIS SOFTWARE. Some states may not allow 
   these  limits  on warranties, so they may not apply to you. In  no  case 
   shall Rosenthal Engineering's liability exceed the license fees paid  by 
   you to Rosenthal Engineering for the right to use the Licensed Software.

   The single users license is obtained by sending your check for $25  (US) 
   to:

      Rosenthal Engineering, 3737 Sequoia, San Luis Obispo, CA 93401 USA