Electrical and Electronic Formulas version 3
Copyright (C) 1990 - 1992 Miller

Introduction:

      This program contains a collection of basic electrical and electronic
      formulas, which can be found in any electrical engineering handbook.
      The software was developed, in an effort, to alleviate the necessity
      of looking up individual formulas each time they are needed. This
      software includes the most commonly used electrical and electronic
      formulas.

      The software was complied to include the use of a math coprocessor,
      if one is present. The coprocessor will be emulated if one is not
      found in your system.

Differences:

      This release contains all the features of version 1 and 2, plus a
      a choice  of calculators, either algebraic or RPN (Reverse Polish 
      Notation). A color code chart was added to the electronics section, and
      junction box sizing, a motor full load current chart, and a wire
      ampacity chart was added to the electrical section. Also the command
      line options were removed, options are now set in the configure area
      and stored in a data file. Some additional minor maintenance changes
      were also put into effect in this version.
 
File Index:

      EEF    .EXE : 81760 Bytes, Electrical and Electronic Formula program
      EEF    .DOC : 18873 Bytes, file containing general program information
      EEFELEC.DBF : 21280 Bytes, file containing the world wide voltage chart
      EEFHELP.DBF : 12880 Bytes, file containing general help information

System Requirements:

      The software minimum requirements are as follows...
      
      Any XT compatible computer
      DOS version 3.0 or later
      256K memory
      A CGA color monitor
      A floppy or hard disk drive
   
Installation:

      The program, including support files, is compact enough that it will
      run satisfactorily on a floppy disk. If a hard disk is available it
      should be used, this will allow faster access to the data files as
      they are needed. Type each of the following lines into the computer,
      at the DOS prompt, to install on a hard disk system.

      MD FORMULA                  <ENTER>    Make a directory
        
      COPY A:EEF*.* C:\FORMULA /V <ENTER>    Copy files to new directory

      CD\FORMULA                  <ENTER>    Change to new directory

      EEF                         <ENTER>    Execute the program

      A batch file can be created to allow easier loading of the program.
      This file should be located in the root directory of the hard drive.
      Type each of the following lines into the computer, at the DOS
      prompt, to create a batch file.
        
      COPY CON C:\EEF.BAT <ENTER>

      CD\FORMULA          <ENTER>

      EEF.EXE             <ENTER>

      ^Z                  <ENTER>

      To execute the program, change to the root or formula directory, and
      type EEF, followed by the <ENTER> key. If the DOS path is set to
      include the root and formula directories, changing to a particular
      directory will become unnecessary. Refer to your DOS manual for
      instructions on using the path command.

Command Line Options:

      Command line options were removed from this version. See the configure
      section on setting up the program options.

General Information:
                                                           
      Select the proper subject from the main menu. Once the new menu is
      displayed you will have to select an appropriate topic. The program 
      will then display this screen. The first few lines, starting at the
      top of the monitor will give a brief description of the area you have
      accessed. If a prompt will require more than a one character
      response, then a window will be displayed. The window has a wrap
      feature, which works as follows; as the window becomes filled,
      characters on the left will be dropped, as new characters are added
      on the right side of the window. The <BACKSPACE> key can be used to
      eliminate characters, from the right side of the window, one at a
      time. When you are sure that you have entered the data properly,
      press the <ENTER> key, this will allow the program to read and store 
      the data. When all the necessary data has been entered the program
      will solve for the unknown value, or perform a conversion, and
      display the result. The <ESC> key is always enabled, and can
      be used in any area. Pressing the <ESC> once will return you to the
      first data entry point on the current screen, this is useful if you
      made an incorrect entry. Pressing the <ESC> key again will cause the
      most recent menu to be displayed. Use this method to find your way
      back to the main menu, and also to exit the program.
                                          
Configuration Options:

      This section is accessible from the main menu by pressing the <A> key.
      There are four items that can be set up to suit the user, this
      setup data is then stored, for future reference, in a 8 byte file
      named EEF.DAT. The setup options include foreground and background
      colors, calculator type, and sound generation. The options are 
      displayed on the lower area of the screen, one at a time. If a change
      is necessary simply key in the appropriate numeric values and press the
      <ENTER> key. If no change is to be made then simply press the <ENTER>
      key to go to the next choice. The options are listed below.

      Foreground color : Range 0 - 15
      Background color : Range 0 - 7
      Calculator type  : Range 0 - Algebraic / 1- RPN
                                                  (Reverse Polish Notation)
      Sound            : Range 0 - On / 1 - Off

      The foreground and background colors can not be set to the same value,
      an error message will be displayed if this occurs. See the on-screen
      calculator information area for operational considerations, concerning
      the type selection. To save the changes press the <ESC> key, this will
      exit the configure area and write the setup information to the setup
      file.
                                                                              
Electronics Overview:                                                                                                                                           
      This section is accessible from the main menu by pressing the <B> key.
      This section of the program will calculate various electronic related  
      formulas as listed below. Also included is a electronics color code
      chart.                                                                    
             Ohms law (DC)                 Coupled inductance                 
             Ohms law (AC)                 Impedance                          
             Resistance total              Resonance                          
             Capacitance total             Admittance                         
             Inductance total              Susceptance                        
             Mutual inductance             Conductance                        

      Most sections will calculate several different derivatives of a
      formula, for instance, the resonance area has the capability of
      solving not only for resonance, but also capacitance, or inductance
      in a resonant circuit. In the areas where this is possible, you will
      be given several choices then, by user selection, the formula for the
      specified quantity will be performed. The formula used to arrive at
      the result is displayed on the screen at the end of any calculation.
      The standard print screen function can be used to obtain a hard copy,
      the screen is also time and date stamped, as a further aid to the
      user.
                                                                       
Electrical Overview:                                                                   
      This section is accessible from the main menu by pressing the <C> key.
      This section of the program will calculate various electrical related  
      formulas as listed below.
                                                     
             Efficiency                    Fuse and wire size
             Power factor                  Conduit and junction box size
             Amperes from horsepower       Wire resistance and voltage drop
             Amperes from kilowatts        Kvar capacitor sizing
             Amperes from kva              Supply system conversion
             Kilowatts and KVA             Also a FLC and wire ampacity chart
                                                                              
      The left column represents formulas that can be used for calculating   
      both single and three phase circuits. The other formulas are not
      phase dependant and can be used for any circuit configuration.
      Efficiency and Power Factor are calculated and displayed on the    
      screen as a percent. Also, when entering data at an Efficiency or
      Power Factor prompt, the data must be input as a percent. The supply
      system area calculates the current draw, by a load, on any
      conventional power system. This is convenient for 60hz to 50hz
      conversions. The formula used to arrive at the result is displayed on
      the screen at the end of most calculations. The standard print screen
      function can be used to obtain a hard copy, the screen is time
      stamped, as a further aid to the user.
  
Number Systems:
                                                                
      This section is accessible from the main menu by pressing the <D> key.
      This section of the program will evaluate, and change a quantity in
      one number system to an equivalent value in another system. A box is 
      used to indicate the current system type. Use the space bar to toggle
      between the displayed number systems. Once you have entered the data to 
      be converted, simply press the <ENTER> key, and the equivalent values 
      will be displayed for all systems simultaneously.
      
      When entering a binary value you can use the left and right arrow keys
      to assist in locating the cursor to a particular bit position. The
      <BACKSPACE> key can be used to reset the individual bits to zero. 
      Pressing a <1> or <0> key will automatically move the cursor to the 
      next lower bit position.

      The current lower and upper conversion limit is:

        Decimal (base 10) : +/-1048575
        Binary  (base 02) : 1111 1111 1111 1111 1111
        Octal   (base 08) : 3777777
        Hex     (base 16) : FFFFF

      If a value outside these limits is entered, or calculated, an error
      message will be displayed on the monitor screen.
                                                                        
World Wide Voltage:                                                    
    
      This section is accessible from the main menu by pressing the <E> key.
      This section of the program provides a current list of the worlds      
      electric power supplied to consumers. The list covers a wide range of
      countries, and includes frequency, system (wye/delta), single phase
      voltage, and three phase voltage, when available. All voltages listed
      are alternating current (AC). A wye or star system will have a high
      voltage that is 1.732 times the low voltage, for example 120/208. A
      delta system will have a high voltage that is 2 times the low
      voltage. If a single voltage is listed under the single phase
      column, then it can be assumed that the consumer has only the one
      voltage available, and that it is a two wire service, (one phase wire
      and one neutral). Two voltages listed under the same column would
      indicate that the consumer has a three wire service, and both are
      available, (two phase wires and one neutral). A three phase service,
      when available, will normally be furnished with four wires, (three
      phase wires and one neutral). The higher voltage listed can be either
      single or three phase, but the lower voltage will always be single
      phase.

Helpful Information:

      This section is accessible from the main menu by pressing the <F> key.
      Basically this section of the program is a quick reference guide, the
      information contained in this section is essentially the same as
      what is found in this documentation file.   

On-screen Calculator:

      This feature is accessible from anywhere in the program by pressing
      the <F1> key. A short list of special functions will be displayed,
      along with the calculator itself. The capabilities include the normal
      four basic functions, plus squaring, square root, reciprocal, and
      exponential math. The current value in the display can also be
      exported back to the main program.
      There are two types of calculators available, an algebraic, and an RPN
      (Reverse Polish Notation) style. The main difference between the two is
      the way in which the data is entered, algebraic notation places the
      operators between the numeric data, and Reverse Polish Notation places
      the operators after the numeric data. Some sample comparisons are 
      shown below.

      Problem (2 + 5 - 3 = ?):

           Algebraic                     RPN
      Keystroke   Display        Keystroke   Display
          2                          2
          +       2.000...        <ENTER>    2.000...
          5                          5
          -       7.000...           +       7.000...
          3                          3
          =       4.000...           -       4.000...

      Problem (12 * 10 / 5 = ?):

           Algebraic                     RPN
      Keystroke   Display        Keystroke   Display
         12                         12
          *      12.000...        <ENTER>   12.000...
         10                         10
          /     120.000...           *     120.000...
          5                          5
          =      24.000...           /      24.000... 
      
      Problem (20 - 10 + 30 / 5 = ?):

           Algebraic                     RPN
      Keystroke   Display        Keystroke   Display
         20                         20
          -      20.000...        <ENTER>   20.000...
         10                         10
          +      10.000...           -      10.000...
         30                         30
          /      40.000...           +      40.000...
          5                          5
          =       8.000...           /       8.000...

      The function keys provide the calculator with some extended functions
      as noted above these include the following.
      F(1) - Clear the display
             Pressing this key once clears the numeric entry in progress,
             pressing the key again will clear the entire calculator.
      F(2) - Change sign
             Pressing this key toggles the display from positive to negative.
      F(3) - Export result
             Pressing this key will take the value in the display and place 
             it in the data window of the main program. This function will
             export back to the electrical and electronic sections if a
             window is displayed, and also to the number system conversion
             area if the decimal system is the base system.
      F(4) - Pi
             Pressing this key will place the constant Pi in the display.
      F(5) - Square
             Pressing this key will square the number in the display.
      F(6) - Reciprocal
             Pressing this key will give the reciprocal of the number 
             in the display.
      F(7) - Square root
             Pressing this key will give the square root of the number
             in the display.
      F(8) - Exponential math
             Pressing this key will give the exponential result of the last
             numeric values keyed in to the calculator. An example is shown
             below.               
      
           Algebraic                     RPN
      Keystroke   Display        Keystroke   Display
          2                          2
          +       2.000...        <ENTER>    2.000...
          3                          3
        F(8)      8.000...         F(8)      8.000...
    
      When using the algebraic mode any of the basic function keys (+ - * /),
      or the (=) key, can be used to enter the initial value for exponential
      math. Also relating to the algebraic mode, the <ENTER> key can be
      substituted for the <=> key. All functions can be chained together
      except for the exponential math function. Select the calculator you
      are most comfortable with in the configure section, which is accessible
      from the main menu.

Disclaimer:

      The author accepts no responsibility for the application of this
      software, the result obtained, any errors or omissions contained
      herein. This material is subject to change without notice.

Comments:

      The author welcomes all comments, either good or bad, input from users
      is very important to future releases of this software. Please feel
      free to contact me on Compuserve (73407,546), or at the address below.

Registration:
        
      This program is copyrighted, and is offered as shareware software. If
      you find this software useful, and plan to retain and use it, then
      please register the program. By doing so, you will receive a copy of
      the latest version of this software and also be assured of being
      informed of future updates. Please send the form below, along with
      $20.00, to the address shown.
 
      Name:___________________________________________________________

      Address:________________________________________________________

      City, State:____________________________________________________

      Zip Code:_______________________________________________________

      Country:________________________________________________________

      Version You Are Using:________________Media Type________________
                                      (5.25 / 3.50 Diskette)
      Gregory J. Miller
      2303 Bennington Place
      Maryland Heights, Mo. 63043