G8BPQ Host Mode

From Version 4.00, a new application interface to the switch will be provided.
This will replace the existing interfaces (TNC2, PK Host and KISS). New
software should if possible use the new interface - interface routines
supporting the old modes, and WA8DED Host mode, will be provided as TSRs
to support existing application software.

The interface is normally called using INT 7Fh. From version 4.03 the interrupt
number may be changed - The value is specified in BPQCFG.TXT as INTERRUPT=nnn,
where nnn is in decimal. The function required is in AH, and the stream in AL.
The system supports 64 streams, or sessions, numbered from 1 - 64.

Changes in Version 4.05.

1.	Additional option on funtion 6 - allows connects using BBS Call, even
	if APPLMASK is not set (say to prevent connects).

2.	Additional info returned by function 8.

3.	Format of frame returned by function 11 added to documentation.

4.	Function 15 added. Simplifies access to timing info.

5. 	Broadcast option added. If function 2 is called with AL=0, the
	data will be sent as a UI frame to all ports which have an UNPROTO
	address set.

6. 	Function 12 added to update Beacon text. 


COMMANDS SUPPORTED ARE:

Note that in all cases where a string is returned, ES:DI must point to
a buffer supplied by the user, and the switch will copy the data to 
this buffer. The code does NOT return pointers to its own data.


	AH = 1	Set application mask to value in DL.
		Set application flags to value in CL.
		  If top bit of CL is set, monitored frames will be available.
		  Use function 11 to receive them. 

	AH = 2	Send frame in ES:SI (length CX)


	AH = 3	Receive frame into buffer at ES:DI, length of frame returned
		in CX.  BX returns the number of outstanding frames still to
		be received (ie. after this one) or zero if no more frames
		(ie. this is last one).
		Note that CX is NOT an input param - the supplied buffer
		must be big enough to receive a full AX.25 frame, including
		up to 8 digi callsigns. 340 should be enough.


	AH = 4	Get stream status.  Returns:

		CX = 0 if stream disconnected or CX = 1 if stream connected
		DX = 0 if no change of state, or DX = 1 if
		       the connected/disconnected state has changed.

	AH = 5	ACK stream status change. Must be called to allow another
		status change to be reported. 


	AH = 6	Session control.

		CX = 0 Connect to Node. Session uses BBS callsign if bottom
					bit of DL=1, otherwise uses Node Call .

		CX = 1 Connect to Node. Session uses BBS Call if APPLMASK=1,
					otherwise Node Call.

		CX = 2 Disconnect
		CX = 3 Return user to node


	AH = 7	Get buffer counts for stream.  Returns:

		BX = number of frames queued for receive
		CX = number of un-acked frames to be sent
		DX = number of buffers left in node


	AH = 8	Port control/information.  Called with a stream number
		in AL returns:

		ES:DI = CALLSIGN (10 bytes space padded)

		The following are now supported (4.05 onwards)

		AL = Radio port on which channel is connected (if level 2)
		AH = Session Type (If Connected). Session type bits are:

		   L2LINK	EQU	1
		   SESSION	EQU	10B
		   UPLINK	EQU	100B
		   DOWNLINK	EQU	1000B
		   BPQHOST	EQU	100000B
	
		BX = L2 paclen for the session
		CX = Maxframe. Taken from PORT maxframe if L2 session,
		     Switch maxframe if L4.
		DX = L4 window size (if L4 circuit, or zero)


	AH = 10	RAW (KISS) transmit frame.  Data pointed to by ES:SI, of
		length CX, is transmitted as a HDLC frame on the radio
		port (not stream) in AL.


	AH = 11 Get Trace (RAW Data) Frame into ES:DI, Length to CX. Data
		is as received off air (ie with calls in AX.25 format, etc)
		See note on CX under function 3.

		The returned buffer includes a 5 byte header:

		    Bytes 0-1  - Internal control info (ignore)
		    Byte  2    - Port number. Top bit set if transmitted frame.
		    Bytes 3-4  - Frame length (including this header)


	AH = 12 Update Switch Info. This will be used for a number of
		operations. At the moment the only one implemented is to
		update the Beacon Text field.

		DX = Function Number.
		
		   DX = 1  Update Beacon Text.

			ES:SI Data to send in Beacons
			CX    Length of Data

	AH = 15 Get time marker in AX. Value is number of timer interrupts
		since switch was loaded, modulo 65536. Timer interrupts 
		normally occur at approx 18.2 per second.



	The following additions have been proposed. Similar functions may
	be provided, but not necessarily in this format.


	AH = 0	Get node/switch version number and description.  On return
		AH = major version number and AL = minor version number,
		and user's buffer pointed to by ES:SI is set to the text
		string normally output by the USERS command. CX is set to the
		length of the text string.


	AH = 9	Fetch node/application callsign & alias or application names

		AL = application
		BL = 0 to get Callsign, 1 to get Application Name

		number:

		0 = node
		1 = BBS
		2 = HOST
		3 = SYSOP etc. etc.

		Returns string with alias & callsign or application name in
		user's buffer pointed to by ES:SI length CX.  For example:

		"WORCS:G8TIC"  or "TICPMS:G8TIC-10".



PACLEN.

Frames are transmitted as received from the application, so the application
is responsible for the transmitted PACLEN. Function 8 will return the
recommended value for the current session. I think the value is always OK,
but I suggest you treat a value of zero as 'undefined', and use your own
default. The value may change during a session, if for instance, you connect
to the switch, and then out on a port with a different MAXFRAME. Also at
some time in the future I hope to adjust PACLEN to suit conditions on the
channel. So I recommend that the value is re-read from time to time during
a session.



The following sample of code shows how to find the Interrupt Number to use
to call the switch, and check that the switch is loaded.


NOTBPQERROR	DB	'Switch not found$'
VERSERROR	DB	'Version not compatible with Node Software$'
G8BPQ		DB	'G8BPQ'



BADCONFIGMSG	DB	'Configuration file read error',0DH,0AH,'$'
CONFIGFILENAME	DB	'BPQCFG.BIN',0
NOCONFIGMSG	DB	'Configuration file BPQCFG.BIN not found',0DH,0AH,'$'
;
;	BPQCFG FIRST 128 BYTES
;
CONFIGTABLE	LABEL	BYTE
;
;	CONFIGURATION DATA STRUCTURE
;
;	DEFINES LAYOUT OF CONFIG RECORD PRODUCED BY CONFIGURATION PROG
;
;	LAYOUT MUST MATCH THAT IN CONFIG.C SOURCE
;
C_NODECALL	DB	10 DUP (0)	 ; OFFSET = 0 
C_NODEALIAS	DB	10 DUP (0)	 ; OFFSET = 10
C_BBSCALL	DB	10 DUP (0)	 ; OFFSET = 20
C_BBSALIAS	DB	10 DUP (0)	 ; OFFSET = 30
;
C_OBSINIT	DW	0		 ; OFFSET = 40
C_OBSMIN	DW	0		 ; OFFSET = 42
C_NODESINTERVAL	DW	0		 ; OFFSET = 44
C_L3TIMETOLIVE	DW	0		 ; OFFSET = 46
C_L4RETRIES	DW	0		 ; OFFSET = 48
C_L4TIMEOUT	DW	0		 ; OFFSET = 50
C_BUFFERS	DW	0		 ; OFFSET = 52
C_PACLEN	DW	0		 ; OFFSET = 54
C_TRANSDELAY	DW	0		 ; OFFSET = 56
C_T3		DW	0		 ; OFFSET = 58
   		DW	0		 ; OFFSET = 60
		DW	0		 ; OFFSET = 62
C_IDLETIME	DW	0		 ; OFFSET = 64
C_EMSFLAG	DB	0		 ; OFFSET = 66
		DB	0
C_BBS		DB	0		 ; OFFSET = 68
C_NODE		DB	0		 ; OFFSET = 69
C_HOSTINTERRUPT	DB	0		 ; OFFSET = 70
C_DESQVIEW	DB	0		 ; OFFSET = 71
C_MAXLINKS	DW	0		 ; OFFSET = 72
C_MAXDESTS	DW	0
C_MAXNEIGHBOURS	DW	0
C_MAXCIRCUITS	DW	0		; 78
 
C_TNCPORTLISTO	DB	16 DUP (0)	 ; OFFSET = 80

C_IDINTERVAL	DW	0		; 96
C_XXXXXXXX	DW	0		; 98    ; SPARE (WAS DIGIFLAG)
C_MINQUAL	DW	0		; 100
C_HIDENODES	DB	0		; 102
C_L4DELAY	DW	0		; 103
C_L4WINDOW	DW	0		; 105
C_BTINTERVAL	DW	0		; 106
X_UNPROTO	DB	9 DUP (0)	; 108	; NOW SPARE
C_BBSQUAL	DW	0		; 117
		DB	(CONFIGTABLE+128-$) DUP (0)



CONFIGHANDLE	DW	0

NODE:

	INT	7FH
	RET


INIT:
;
;	GET NODE INTERRUPT NUMBER FROM CONFIG FILE
;
	MOV	DX,OFFSET CONFIGFILENAME
	MOV	AH,3DH
	MOV	AL,0			; READ ONLY
	INT	21H			; OPEN IT

	JC	NOCONFIGFILE

	MOV	CONFIGHANDLE,AX

	MOV	BX,AX
	MOV	DX,OFFSET CONFIGTABLE
	MOV	CX,128
	MOV	AH,3FH

	INT	21H			; READ
	CMP	AX,CX
	JNE	SHORTCONFIG

	JMP SHORT PROCESSCONFIG

NOCONFIGFILE:

	MOV	DX,OFFSET NOCONFIGMSG
	JMP SHORT CONFIGERR

SHORTCONFIG:

	MOV	DX,OFFSET BADCONFIGMSG

CONFIGERR:

	MOV	AH,9
	INT	21H

	MOV	AX,4C01H
	INT	21H			; EXIT

PROCESSCONFIG:

	MOV	BX,CONFIGHANDLE
	MOV	AH,3EH
	INT	21H			; CLOSE IT

	MOV	AL,C_HOSTINTERRUPT	; INTERRUPT
	MOV	BYTE PTR NODE+1,AL	; PATCH NODE CALL INSTRUCTION
;
;	GET NODE VERSION
;
	PUSH	DS
	MOV	AH,0
	ADD	AX,AX			; VECTORS ARE 4 BYTES LONG
	ADD	AX,AX
	MOV	SI,AX

	XOR	AX,AX
	MOV	DS,AX

	LDS	SI,DS:[SI]		; GET POINTER TO HOST SUPPORT CODE

	SUB	SI,7
	MOV	DI,OFFSET G8BPQ
	MOV	CX,5
	REP CMPSB			; MAKE SURE SWITCH IS LOADED

	JE	SWITCHOK

	POP	DS

	MOV	DX,OFFSET NOTBPQERROR

	MOV	AH,9
	INT	21H

	JMP SHORT EXIT

SWITCHOK:

	CMP	BYTE PTR DS:[SI],MAJORVERSION
	JNE	BADVERSION

	CMP	BYTE PTR DS:1[SI],MINORVERSION
	JE	VERSIONOK


BADVERSION:

	POP	DS

	MOV	DX,OFFSET VERSERROR
	MOV	AH,9
	INT	21H

EXIT:
	MOV	AX,4C00H
	INT	21H

BADPORTVAL:

	MOV	AH,9
	MOV	DX,OFFSET ERRORMSG
	INT	21H

	RET

VERSIONOK:

	POP	DS
;
	..........



The release disk also contains a demonstration terminal program, TERM4,
written by G8IMB (in PASCAL) to demonstate the use of the new interface from
a high level language. Note, however, that it was written for version 4.02,
and therefore only works with the Host Mode interrupt configred at 7Fh



John Wiseman, G8BPQ @ GB7BAD
20/12/91